PrintGL  1.56

                    (c) Copyright Ravitz Software Inc. 1990,1995

                  PrintGL/D - pen plotter emulator for DOS
                  PrintGL/W - pen plotter emulator for Windows
                  PrintCAD  - printer driver for DOS CAD software


       Ravitz Software Inc.                BBS/fax               606-268-0577
       PO Box 25068
       Lexington, KY  40524-5068           Compuserve  Cary Ravitz [70431,32]
       USA                                 Internet   70431.32@compuserve.com


       ------------------------------ License -------------------------------

       PrintGL (including PrintGL/D, PrintGL/W, and PrintCAD) is provided  as
       is.  There  are no  warranties expressed or  implied.  PrintCAD  is  a
       swapping   resident  program  that  may  have  problems  with  unusual
       environments.

       PrintGL is copyrighted by Ravitz Software Inc.  You  may copy  PrintGL
       only for use under this license agreement.

       PrintGL is distributed  as  shareware.  You  may use  PrintGL  without
       charge on a trial basis to  determine its suitability for you.  If you
       continue  to  use  it after  your  evaluation,  you  MUST  purchase  a
       registered copy for  $50 (US$).  Registration  covers use by a  single
       person  (on  multiple computers) or installation on a  single computer
       (may  be  used by a group of people).  There is no cost to use a later
       1.** version after registering any 1.** version.

       You  may distribute PrintGL as a stand alone product if you  keep  the
       entire  package  together,  unchanged,  clearly  label   the  disk  as
       shareware,  and do not charge more than  $10.  You  may not distribute
       PrintGL as  part  of another  product or  on  the  same disk with  any
       commercial software.

       See Order Form in PRINTGL.TXT for ordering information.               



       ------------------------------ Contents ------------------------------

       PrintGL Initial Information File ......................... PRINTGL.TXT
       PrintGL Supplemental Documentation File                   PRINTGL2.DOC
       Introduction ....................................................... 3
       License and Registration                                             5
       Installation ....................................................... 6
       Operation                                                            7
       How To Get HP-GL Plotfiles From Your Graphics Software ............. 9
       Messages                                                             9
       User Interface .................................................... 10
       Example Setup Instructions For PrintCAD                             11
       Overview of Options ............................................... 12
       /1, /2, /3, /4, /5 - PrintGL/D and PrintGL/W Default Options        12
       /1, /2, /3, /4, /5 - PrintCAD Alternate Configurations ............ 12
       /A - Position Option                                                13
       /B - Tiling Option ................................................ 13
       /C - Pen Color Option                                               13
       /D - Output Destination Option .................................... 15
       /F - Output Format Option                                           15
       /I - Scaling Point Location Option ................................ 18
       /J, /K - Printer Code Prefix, Suffix Options                        18
       /L - Page Layout Option ........................................... 19
       /M - Magnification Option (Scale, Size)                             20
       /N - Page Number Option ........................................... 20
       /O - Origin and Orientation Option                                  20
       /P - PrintGL/D and PrintGL/W Plotfile Option ...................... 21
       /P - PrintCAD Intercept Mask Option                                 21
       /Q - Number of Copies Option ...................................... 21
       /R - Internal Resolution Option                                     21
       /S - Pen Shading Option ........................................... 22
       /T - Temporary File Option                                          22
       /W - Pen Width Option ............................................. 22
       /X - PrintGL/D and PrintGL/W User Interface Option                  23
       /X - PrintCAD Control Option ...................................... 23
       /Y - Plotter Options                                                24
       /Z - Processing Options ........................................... 24
       PrintGL/D and PrintGL/W Menu                                        25
       Menu Specific Functions ........................................... 25
       Menu Input and Output Choices                                       26
       Menu Processing Options ........................................... 26
       Menu Pen Options                                                    26
       Menu Page Layout Options .......................................... 27
       Menu Other Options                                                  27
       Menu Auto Run Mode ................................................ 27
       Large Paper                                                         28
       Tips On AutoCAD ................................................... 29
       Color Processing                                                    29
       Compatibility and Technical Information ........................... 30
       HP-GL, HP-GL/2, and ADI Commands                                    30
       Output Devices (Displays, Printers, Plotters, Bit Maps, Fax) ...... 31
       Useful Prefix and Suffix Codes                                      38
       Answers ........................................................... 39
       PrintCAD Answers                                                    40
       User Support ...................................................... 40


                                                                          p-3
       Introduction ---------------------------------------------------------

         PrintGL is a  shareware  pen plotter  emulator package  for  DOS and
         Windows.  It includes a DOS program that can be run from the command
         line  and BAT  files or via menu  (PrintGL/D), an equivalent Windows
         program (PrintGL/W),  and a  resident DOS  program  that  intercepts
         plotter data as it is being written to file (PrintCAD).

         PrintGL/D  is  a  command line or menu driven program  for  DOS.  It
         prints  or displays HP-GL (Hewlett-Packard Graphics Language,  7475,
         17440 subsets), HP-GL/2 (limited subset), or  ADI  (Autodesk  Device
         Interface 4.0  vector plotter  binary format)  plotfiles  on most PC
         graphics  devices.  HP-GL  is  widely  supported  by  CAD,  drawing,
         plotting,   and   other   graphics   programs   including   AutoCAD,
         Microstation,  FastCAD, Generic CADD, MathCAD,  Schema,  OrCAD,  and
         SAS.  PrintGL will  print on  Epson and IBM 9 pin  printers,  Epson,
         Fujitsu,  IBM, NEC, and Toshiba 24 pin printers, Canon BJ,  BJC, and
         LBP  printers,  Epson  Stylus,  HI  JetPro,  HP  Laserjet,  Deskjet,
         PaintJet, and HP-GL,  HP-GL/2,  and HP-RTL devices,  IBM ExecJet and
         LaserPrinter, PDP ProTracer, Star  SJ-144, PostScript printers,  and
         others.  It will  also display  plots with a CGA, EGA, HGC, VGA,  or
         VESA SVGA, and  output a PCX or DCX bit map file or an  Encapsulated
         PostScript file with preview bit map.

         PrintGL/W is a Windows version of PrintGL/D.

         PrintCAD  is a resident pen plotter  emulator that acts as a printer
         driver for most DOS based CAD packages.  It lets  you print drawings
         directly from CAD programs, via  the CAD program's  HP-GL or HP-GL/2
         driver or AutoCAD's ADI plotter driver. PrintCAD works with AutoCAD,
         AutoSketch,  Microstation,  Cadkey,  FastCAD,  Generic  CADD,  Micro
         CADAM, Draft Choice,  PC-Draft-CAD, and other CAD programs.  It will
         print on the same printers noted above but does not do screen output
         or  generate  PostScript preview bit maps.  PrintCAD  is set  up via
         command line (or BAT file).  PrintCAD is a swapping resident program
         that uses 5K of base memory and 400K  of EMS or XMS  memory.  Either
         400K  of  EMS  or XMS  memory  is required and  a  VCPI  handler  is
         recommended.

         Even if  your  graphics  program  supports  your  printer,  you will
         probably  find  that PrintGL is faster, gives better  print quality,
         and/or  gives more  formatting  flexibility.  PrintGL uses  the best
         graphics modes available for  each printer that it supports and uses
         transfer data  compression to improve print speed  on many printers.
         And it gives options such  as orientation,  magnification, position,
         and pen  width, color, and  shading.  If  you need  printed graphics
         output from personal software, you can output  HP-GL and use PrintGL
         to do the printing.  This gives immediate support to a wide range of
         printers.  And  it lets  you use advanced graphics  functions  while
         supporting low function plotters.
                                                                    continued


                                                                          p-4
         PrintGL  interprets all of the HP 7475 and 7440/17440 (ColorPro with
         GEC)  command  set  that  is  applicable  to  plotfiles  except  for
         character set 8 (Katakana).  None of the digitize, output, or device
         control commands (except plotter  on and off) are supported as these
         are only used with  direct control of a plotter.  And the error mask
         command is not supported.  In addition to the HP 7475 and 7440/17440
         commands, PrintGL handles paper feed, label origin, extra space, and
         enhanced clipping window  commands and  proportional fonts  and line
         types -8..-1, 7, and 8.

         PrintGL's HP-GL/2 subset  includes pen color, shading, transparency,
         and width control, compressed data, a few other useful functions. It
         does not include line attributes, user defined line types and fills,
         three point  arcs,  Bezier  curves,  and  HP-PCL and  HP-RTL related
         functions.

         This program is produced by a member of the Association of Shareware
         Professionals (ASP).  ASP wants to  make  sure  that  the  shareware
         principle  works   for  you.   If  you   are  unable  to  resolve  a
         shareware-related  problem  with  an ASP  member  by  contacting the
         member directly, ASP may be able to help. The ASP Ombudsman can help
         you resolve a  dispute or problem  with an  ASP member, but does not
         provide technical support for members' products. Please write to the
         ASP  Ombudsman at  545  Grover Road,  Muskegon, MI 49442  or send  a
         CompuServe message via CompuServe Mail to ASP Ombudsman 70007,3536. 


                                                                          p-5
       License and Registration ---------------------------------------------

         PrintGL (including PrintGL/D, PrintGL/W, and PrintCAD)  is  provided
         as is.  There are no warranties expressed or implied.  PrintCAD is a
         swapping  resident  program  that  may  have  problems with  unusual
         environments.

         PrintGL is copyrighted by Ravitz Software Inc.  You may copy PrintGL
         only for use under this license agreement.

         PrintGL  is  distributed as shareware.  You may use PrintGL  without
         charge on a trial basis to determine its suitability for you. If you
         continue to  use  it after  your  evaluation,  you  MUST purchase  a
         registered copy for $50 (US$).  Registration covers  use by a single
         person (on  multiple computers) or installation on a single computer
         (may be used by a group of people).  There is no cost to use a later
         1.** version after registering any 1.** version.

         You may distribute PrintGL as a stand alone product if you  keep the
         entire  package  together,  unchanged,  clearly label  the  disk  as
         shareware,  and do not charge more than $10.  You may not distribute
         PrintGL  as  part of another product or  on the same  disk with  any
         commercial software.

         See Order Form in PRINTGL.TXT for ordering information.

         PrintGL  Printer  Driver  is  the  graphics  engine  used  in  these
         programs. It may be licensed for use in commercial programs.  Send a
         note to request more information on this.                           


                                                                          p-6
       Installation ---------------------------------------------------------

         The PrintGL package includes these files:

           FILE_ID.DIZ   standard description of package
           PRINTCAD.EXE  resident DOS program
           PRINTGL.DOC   documentation
           PRINTGL.PLT   sample plotfile
           PRINTGL.TXT   initial information
           PRINTGL2.CHR  HP-GL character set plotfile
           PRINTGL2.DOC  supplemental documentation
           PRINTGLD.EXE  DOS program
           PRINTGLW.EXE  Windows program
           README.BAT    displays the initial information file

         To install PrintGL create a directory  called  PRINTGL, and  copy or
         unpack the distribution  files into this directory.  It is preferred
         that the PRINTGL directory be in your DOS PATH.

         To install PrintGL/W as an  icon in  the  Windows  Program  Manager,
         select  File, then New, then program  item  to bring up the  Program
         Item Properties menu.  Enter the item  name - PrintGL/W, the command
         line - C:\PRINTGL\PRINTGLW, and the working directory - wherever you
         keep your plotfiles.  You can choose  from  three icons designed for
         two, sixteen, and 32K color setups.

         PRINTGL.TXT  is  initial  information.  You can view it from DOS  by
         running README.BAT or from PrintGL by pressing F1. While viewing it,
         you can print pages or the entire file. Press T repeatedly until the
         correct setup is  displayed and  then press  P.  Or from  DOS, "COPY
         PRINTGL.TXT PRN" to print the entire file.

         PRINTGL.DOC  is the documentation.  This is viewed  and printed just
         like PRINTGL.TXT.

         PRINTGL2.DOC  is supplemental  documentation  for  supported  HP-GL,
         HP-GL/2, and ADI commands and the program interface. PRINTGL2.CHR is
         a plotfile that documents the supported HP-GL characters sets.

         PRINTGL.PLT is a sample plotfile that you can  print or display with
         PrintGL.                                                            


                                                                          p-7
       Operation ------------------------------------------------------------

         PrintGL reads a plotfile, does arc,  character, fill, etc.  to  line
         conversion,  stores the data in a  coordinate  list, and  if needed,
         puts the list on disk. It then reorients the data and determines the
         plot size. Next the data is resized and relocated. For vector output
         formats (HP-GL,  HP-GL/2, PostScript) data is output from here.  For
         bit   mapped  devices  (most  printers,  displays,   bit  maps)  the
         coordinate  list is rasterized and output in swaths.  You are likely
         to  see  the  printer  print  a  swath  and  stop  while PrintGL  is
         processing the next swath.

         Esc  stops PrintGL at the next good break point, leaving the printer
         ready for new data. Ctrl-B stops PrintGL as quickly as possible. You
         generally need to do a printer reset after a Ctrl-B.

         When you  display a  plot, press Enter or  Esc  to return to the DOS
         text screen,  or  any  of  the four  cursor movement  keys to scroll
         across the plot.  Press S to cycle between full, half (the default),
         quarter, and eighth page scrolling.

         PrintGL  works within a  printer's current margins and starts at the
         current vertical print position. If you decline the form feed option
         (/L or "form feed") then PrintGL  leaves the printer at the start of
         the line directly below the plot.

         PrintGL will not automatically change a printer's operating mode. On
         multimode printers,  the  right operating  mode must be  set  before
         running  PrintGL or with  the  prefix  code  option (/J  or  "modify
         output" "prefix codes: ").

         Internally PrintGL  uses two byte  coordinates  on  a 1016 dots/inch
         grid. This allows for plots with coordinates of over 30 inches - far
         larger than an HP 7475 can handle. However, if you are using PrintGL
         to emulate a large plotter, you may overflow the internal coordinate
         system.  This condition  is  not checked, and  it will cause garbage
         output.  You can change the internal resolution to 508 dots per inch
         (giving 60 inch maximum plot sizes) with the /R option (/R508). This
         only helps  store the  original plot  internally.  The  next step in
         PrintGL converts  these  coordinates  to the  requested size  in the
         resolution of the output device, and these coordinates must also fit
         in the two byte coordinate list.

         PrintCAD is a resident program that intercepts plot data output from
         CAD software, processes the data, and prints the resulting  picture.
         When PrintCAD is first run it installs itself.  Subsequent runs look
         for the resident copy  and  send control information to it, updating
         the parameters.

         PrintCAD must  be installed before running the CAD software.  Do not
         install it from a DOS shell.  PrintCAD automatically loads high if a
         5K DOS or XMS upper memory block is available.  Do not use LOADHI or
         LOADHIGH.
                                                                    continued


                                                                          p-8
         PrintCAD  can  intercept data from  two sources, DOS file writes and
         AutoCAD/Sketch ADI  4.0  interrupts.  With  the  option  /PADI,  ADI
         interrupts are intercepted.  With /Pmask,  for example  /P*.PLT, DOS
         file writes are intercepted.

         PrintCAD can interpret two kinds of data,  HP-GL and AutoCAD ADI 4.0
         binary plotter data.  HP-GL  data is always interpreted.  If you use
         the /PADI or /YA options then ADI plotter data is  also interpreted.
         PrintCAD  can only interpret plotter  data,  not printer/plotter  or
         rendering data.

         To  use PrintCAD as an HP-GL interpreter, use /Pmask to tell it what
         files to intercept. Use /P*.PLT, /P*.DPF, /P*.HPG, /P*.000, etc.  to
         match the names that the CAD software uses when writing HP-GL files.
         Configure the CAD software  for  HP-GL  (HP 7550 or 7585) output  to
         file.  Then plot (do  NOT print).  PrintCAD  intercepts the data and
         prints it.

         To use  PrintCAD  with AutoCAD/Sketch as  an  ADI  interpreter  that
         intercepts files use /P*.PLT /YA.  Configure AutoCAD  for an ADI 4.0
         plotter,  binary output to file, up to forty  pens, 1016 steps/inch,
         and eight non-solid line types. Then plot.

         To use PrintCAD  with AutoCAD/Sketch as an installed ADI 4.0 plotter
         driver use /PADI. After installing PrintCAD configure AutoCAD for an
         ADI 4.0 plotter,  installed at  interrupt hex 78, up to  forty pens,
         1016 steps/inch, and eight non-solid line types. Then plot.

         After  starting  PrintCAD, you  can  verify  the  installation  with
         "printcad  /xq".  You can  check  its function from DOS  with  "COPY
         PRINTGL.PLT PCAD.PLT".

         PrintCAD  causes a  high/low beep  the  first time that data is sent
         after a file open. If you turn on sound (/XS), it causes a high beep
         after swapping in its code and a low beep before swapping it out, to
         let you monitor its processing.                                     


                                                                          p-9
       How To Get HP-GL Plotfiles From Your Graphics Software ---------------

         To  use PrintGL you must be  able to  output HP-GL plotfiles or  ADI
         binary plotfiles from your graphics application.  Most CAD, drawing,
         and graphing software lets you do this. Just tell the application to
         output  your  picture  to  a  plotter.  In  either the configuration
         process or the output  process, you  will need  to  specify that you
         have  an HP  7475 or  HP 7440/17440 plotter  and  that you want  the
         output to go to a file instead of a COM port (some programs name the
         file automatically and some ask  you for a name).  You might need to
         set up a pen assignment table that specifies what color each pen is.
         Once you have the file, you can print it with PrintGL/D, either from
         a DOS shell or after exiting the application. With PrintGL/W you can
         run  without exiting the  application.  With  PrintCAD  the  file is
         intercepted and printed instead of being written to disk.

       Messages -------------------------------------------------------------

         PrintGL/D and  PrintGL/W display  a number of messages to  keep  you
         informed of what they are doing. The output looks like this.

           Reading PRINTGL.PLT
           Plotfile has 1 page(s)    Processing page 1    2283 data records
           Overall magnification    0.9964
           Print window   Horizontal   0.00   7.54    Vertical   0.00  10.14
           Plot area      Horizontal   0.42   7.13    Vertical   0.61   9.54
           Output format /FT   HxV dpi 180x180 corrected to 180x180  color
           Writing to device LPT3

         The first  line  is the plotfile  that is currently being processed.
         The second line tells how many pages are in the plotfile, which page
         is being processed, and the number of data points in that page.  The
         number of  data points  is roughly  equivalent  to the number of pen
         moves and  is  shown  to  give  you  an  indication  of  the  plot's
         complexity.

         The  overall magnification is  either  the  magnification  that  you
         specified  with the /M option or the  effective  magnification after
         fitting to the print  window with /MF.  The  print window line gives
         the horizontal  and vertical coordinates of the print window, always
         starting  at 0,0 and in inches.  The plot area  gives the horizontal
         and vertical coordinates of a box that just covers the plotted data.
         This uses the same coordinate system as the print window, so you can
         tell where the plot is relative to the print window.

         The output format and  resolution are  given  and  then  the  output
         destination is noted  (except for screen  plots).  If three  or four
         plane color  is being used, the word  "color" is  displayed.  If you
         have a black only printer, but the output format allows color  (this
         is  common  with 9 and  24 pin  printers),  using color will greatly
         increase the PrintGL run time with no improvement in print quality.

         During processing,  PrintGL/D and PrintGL/W inform you when they are
         processing and writing data, and you can watch  the progress from 0%
         to 100%, along with the elapsed time.

         After initial startup PrintCAD runs without screen output.          


                                                                         p-10
       User Interface -------------------------------------------------------

         PrintGL can be run from  the command  line  (DOS or  Windows)  using
         various  options to tell it  what to  do  or run  with no options to
         bring up a menu system.  The menu options have corresponding command
         line  options,  so the  two  forms  of  options  will  be  described
         together.  The menu options  are noted by  the  menu name in quotes,
         sometimes followed by the menu choice in quotes.

         From the command line, the calling syntax is:

           PRINTGLD plotfile /option1 /option2 ...
           PRINTGLW plotfile /option1 /option2 ...
           PRINTCAD /option1 /option2 ...

         Spaces between parameters  are  not required.  The  plotfile  may be
         specified with  the /P option if it  is inconvenient to make it  the
         first parameter.

         Except for the  /X and /P options in PrintCAD,  if a given option is
         entered more than  once, only the  last  entry is  used.  And  if an
         option is  invalid (but not  incorrect), it is ignored.  Only one /X
         and one /P option is allowed in PrintCAD.

         When run  from the  command line,  PrintGL/D  and  PrintGL/W use the
         current menu options as the default, so if  you have the menu set up
         as desired, you can  run PRINTGLD plotfile from the command line and
         avoid going through the menu to select the plotfile.

         The DOS environment variables  PRINTCAD,  PRINTCAD2,  PRINTCAD3, and
         PRINTCAD4 are read by PrintCAD and put  in front of the command line
         parameters.  When you need to exceed the  127 character DOS  command
         line limit, put some of the parameters in the PRINTCAD variable, for
         example

           SET PRINTCAD=/CRGB... /S... /W...
           PRINTCAD /P*.PLT ...
           SET PRINTCAD=

         Below,  [ and ] enclose optional suboptions and | separates mutually
         exclusive suboptions. The options and suboptions may be in any order
         except  that  multiple numeric  suboptions are  ordered  and numeric
         suboptions must follow character suboptions where the characters may
         be digits. "c" refers to a suboption character, "x", "y", and "z" to
         suboption numbers,  "i"  and  "j"  to  suboption integers, "b"  to a
         suboption byte, and "f" to a DOS file or device name.

         For  numbers (x, y, z), a  decimal  point  is  allowed  but  is  not
         required, and scientific notation is not allowed. "-" is allowed but
         not "+".  For  integer input  (i, j), only  base ten  integers  from
         -32768 to 32767 are allowed.  "+" is not allowed. A byte (b) must be
         a base ten integer  from 0 to 255  or a  hexadecimal number prefixed
         with $  from  $00  to $FF.  Further range checking  is done for most
         options to flag  unreasonable  input.  If  an  option  has  multiple
         numeric suboptions, these may be separated with commas or blanks.   


                                                                         p-11
       Example Setup Instructions For PrintCAD ------------------------------

         Below  are instructions for simple setups  to  help  you get started
         with PrintCAD.  After you have  PrintCAD  running,  there  are  many
         additional options that might be useful.

         To use  AutoCAD (or  AutoSketch)  with  an HP  DeskJet 500C or 550C,
         install PrintCAD with "printcad /padi /fa! /L7.9,10,0,.3 /crygcbmk".
         Configure AutoCAD  for  an  ADI  4.0  vector  plotter  installed  on
         interrupt  78h,  7  pens,  1016  steps/inch,  plot area  10x7.9,  no
         calibration.  Set  up the AutoCAD pen assignment  table so that  the
         seven pens are assigned red, yellow, green, cyan, blue, magenta, and
         black. Set skip perforation off on the printer by setting DIP switch
         1-8 up. Then plot.

         To use  a Canon BJC800 or 820 with 11x17 paper with AutoCAD, install
         PrintCAD with "printcad /p*.plt  /ya  /f& /L10.5,16,0,0  /crygcbmk".
         Configure AutoCAD for  an ADI 4.0 vector plotter with  binary output
         to  a  file,  7  pens,   1016  steps/inch,  plot  area  16x10.5,  no
         calibration.  Set up the AutoCAD  pen  assignment table so  that the
         seven pens are assigned red, yellow, green, cyan, blue, magenta, and
         black. Then plot.

         To  use  a Canon BJ330 with cut sheet  paper  with  AutoCAD, install
         PrintCAD with:

           printcad /f7 1,1.01 /L8,10,0,.4 /j27,67,0,11
           printcad /2/f7 1,1.01 /L10.5,16,0,.4 /j27,67,0,17
           printcad /3/f7 1,1.01 /L13.5,21,0,.4 /j27,67,0,22

         Configure AutoCAD for an HP  7585 plotter with output to a file.  To
         print on 8.5x11 paper set the plot area to 10x8 and output  the plot
         to file PCAD1.  For 11x17  paper set  the  plot area to 16x10.5  and
         output to  PCAD2.  For 17x22  paper set the plot area to 21x13.5 and
         output to PCAD3.

         To  use the BJ330 with another CAD  package, replace the ".plt" with
         the  default   plotfile   extension  for  that   package.   AutoCAD,
         AutoSketch,  and  Micro CADAM use  ".plt", Microstation uses ".000",
         GenCADD  uses ".dpf", and EasyCAD and FastCAD use ".hpg".  DesignCAD
         has no default extension - use ".plt" and enter the entire file name
         when plotting (PCAD1.PLT for example).

         To use a LaserJet with Microstation, install PrintCAD with "printcad
         /p*.000  /fL /L7.9,10,0,.1".  Configure Microstation for an  HP 7585
         plotter, set  the  plot  area  to 10x7.9, and plot.  Instead of /fL,
         choose the best LaserJet driver from this list:

           /FL  any LJ
           /FL! any LJ2 and any LJ3 with less than 1.5 Meg
           /FI  any LJ3 with 1.5 Meg or more and the LJ4L
           /FI+ any 600 dpi LJ4

         For   manual  feed  legal  paper  use  "/p*.000  /fL   /L7.9,13,0,.1
         /J27,38,108,50,72,27,38,108,51,65" and set the plot area to 13x7.9. 


                                                                         p-12
       Overview of Options --------------------------------------------------

         PrintGL's options fall into several categories.  The  first is input
         and output choices.  The  input is chosen with /P, the plotfile, and
         /N,  the  page number.  Output options  are  /F,  the output  format
         (printer model), and /D, the destination port, device, or file.

         The second category is the  page  layout.  /L controls the size  and
         location  of the print window (hard clip limits), and the option  to
         box the window, not send a form feed,  and reverse the image  color.
         Tiling is set with /B and copies with /Q.

         The third category  defines  how  the  plot  looks  within the print
         window.  /M,  the  magnification, sets the  size  of  the  plot.  /A
         determines the location of the plot within the print window. /O sets
         the  origin and orientation, and  is  used to  rotate  or mirror the
         plot. /I sets the plotter's initial scaling points.

         The  fourth category defines the pens, /W for the width,  /C for the
         color, and /S for the shade.

         The  fifth category determines how PrintGL processes the plot.  This
         includes the temporary file /T, the default and minimum chord angle,
         enhanced  font,  and color to shade options  /Z, the plotter Y/D and
         S/E  switch positions  and HP-GL/2 and ADI handling /Y, the internal
         resolution /R, user interface  options /X, and /J and /K let you set
         up and reset the printer for special situations.

         PrintCAD  has separate setup options, /P sets the intercept mask, /X
         sets up the  initial configuration, /1,  /2,  /3, /4, and /5  set up
         multiple configurations.

         And PrintGL/D and PrintGL/W use /1, /2, /3, /4, and /5 to choose one
         of the menu setups as the command line default.

       /1, /2, /3, /4, /5 - PrintGL/D and PrintGL/W Default Options ---------

         These  option select a configuration from the menu to be used as the
         default.  This option must match the first character of the title of
         one of the five menu configurations.

       /1, /2, /3, /4, /5 - PrintCAD Alternate Configurations ---------------

         These options select up to 5 alternate configurations, labeled 1..5.
         /1  is the  default.  The configuration used  for printing is chosen
         based on the file name and mask (/P option).                        


                                                                         p-13
       /A - Position Option -------------------------------------------------

         /A[O][x,y] - position - default /A

         "position"

         The A option determines the location of the plot in the print window
         via  a point on  the plot that  is aligned with a point in the print
         window.  You can specify the plot alignment point with x,y in inches
         from the plot's  origin  (before  PrintGL applies magnification), or
         let  it default to the plot  center.  For the print window alignment
         point, you can default to the center or specify the origin with O.

         /A      puts the center of the plot at the center of the print
         /AO0,0  puts the plot 0,0 at the print window origin

       /B - Tiling Option ---------------------------------------------------

         /B[i,j,x] - tiling parameters - default /B1,1,0

         "tiling"

         /B  lets you specify  tiling  options that  break a  large plot into
         tiles. Each tile is defined by the page layout option (/L).  I and j
         specify the number of tiles horizontally and vertically. X specifies
         the overlap  in inches.  Displayed  plots are  sized  based  on  the
         tiling, but only the first tile is displayed. Use the cursor keys to
         scroll the plot.

         /B2,2,.5  breaks the plot into 4 pages with .5 inch overlap
         /B        is the same as /B1,1,0 and produces no tiling

       /C - Pen Color Option ------------------------------------------------

         /C[O|T]c.. - color - default /COK

         "pen color"
         "pen mode"
         "pen all"

         /C specifies  the  color of each of 40  pens.  The colors are  B for
         blue, C for  cyan, G  for green, K  for black, M for magenta,  R for
         red, W for white,  and Y  for yellow.  Unspecified pens use the last
         selected  color (/CRGB is the same  as /CRGBBBBBB).  For black/white
         output  formats,  color  are translated into either  black  or shade
         levels, based on the /Z option.
                                                                    continued


                                                                         p-14
         Additional colors can be created with shade mixing. These colors use
         shading  patterns to mix  the  eight pure colors.  The format for  a
         mixed color is .??  where  each ?  represents any of  the eight pure
         colors.  The first  color is printed  with the pen's shading pattern
         (/S option)  and the  second  is printed  with  the  inverse shading
         pattern.  If  the shade value is 0 (solid) it is replaced by 2 (50%)
         which  produces the most  uniform  mixed colors.  On many  printers,
         using  a shade of 1 (75%) or 3 (25%) gives a better color.  Here are
         some useful mixed colors for inkjet printers.

           color shade   description      color shade   description
           .bc   3 (25%) azure            .ry   3 (25%) orange
           .bm   3 (25%) violet           .rk   1 (75%) brown
           .gc   3 (25%) jade             .ck   1 (75%) teal
           .gy   3 (25%) lime             .rk   3 (25%) black on DeskJet 500C

         Mixed  colors  need line widths  of at least 2 (4 for coarse shading
         patterns) to  look good, and they may have visual artifacts on edges
         near a 45 degree angle.  Multipass dot matrix formats may not handle
         color mixing well.

         The  following  single  letters may be  used  in place of the  color
         mixing notation.

                  equivalent                         equivalent
           color  mixed color  description    color  mixed color  description
           a      .bc          Azure          i      .bk          dark blue
           v      .bm          Violet         e      .ck          tEal
           j      .gc          Jade           f      .gk          Forest
           l      .gy          Lime           p      .mk          Purple
           s      .rm          roSe           d      .rk          dark red
           n      .ry          oraNge         h      .yk          dark yellow

         By default, colors are overwritten into the  print, so  they  appear
         opaque.  You can  switch to translucent colors (ored into the print)
         with  the  T suboption, and then back  to opaque  with O.  Make  the
         switch in  front of the pen that you want to change.  For PostScript
         and  plotters, the color  processing is  done  by  the  device,  not
         PrintGL.  PostScript uses opaque colors and plotters use translucent
         colors.

         " means repeat the previous color.

         /COKR.MB""T.KY  sets pen 1     to opaque black
                              pen 2     to opaque red
                              pen 3..5  to opaque magenta on blue
                              pen 6..40 to translucent black on yellow       


                                                                         p-15
       /D - Output Destination Option ---------------------------------------

         /D[+][*]f - destination - default /D1

         "destination"

         The D option specifies the output printer port, device, or file. The
         + suboption causes files to be appended rather than overwritten.  1,
         2,  and 3 select the  BIOS printer  routines.  P1..P3  select direct
         parallel port drive - add extension 001  to 999 (for example P1.010)
         to slow the  function  of  the  port  for  compatibility  with older
         printers.  X1..X4  select xon/xoff serial port drive.  H1..H4 select
         hardware (RTS/CTS) serial port drive.  W  selects the Windows  print
         manager (PrintGL/W only).  You can also  use the  DOS  devices LPT1,
         COM1, etc. /D is ignored for display output.

         The * suboption causes PrintGL to output a continuous stream of data
         with pauses of less than one second. This is useful for networks and
         multiple  PC printer  buffers, where  print  jobs  are separated  by
         pauses in the data stream.

         PrintGL cannot set up the serial ports.  This is usually done in the
         AUTOEXEC.BAT with MODE (for example MODE COM1:9600,N,8,1,P).

         If you choose  a three  digit number  for  the  file  extension (for
         example .000), and multiple pages are output via the multiple copies
         option, tiling, or multiple HP-GL pages then,  instead  of appending
         the destination file, additional files are  created  with sequential
         extensions.  If you  specify *, then the extension is incremented to
         avoid overwriting existing files. This is useful for PCX output.

         /D2           sends output to the second parallel port via BIOS
         /D+TEMP.PRN   appends output to file TEMP.PRN
         /DOUTPUT.000  sends output to OUTPUT.000, OUTPUT.001, ...

       /F - Output Format Option --------------------------------------------

         /Fc[%][-|+|*|^][!|­][~|`][x,y] - output format - default /FV

         "output format"
         "modify output" "h,v size multiplier: "
         "modify output" "compression mode: "

         The  F  option  specifies the  output format.  -, +, *,  and  ^  are
         resolution modifiers, ! and ­ select compression levels, ~ turns off
         color processing, and ` switches four  plane color processing  on or
         off.  These suboptions are allowed  even if they have  no effect.  %
         selects a different driver.

         For  HP-GL  (/F8),  HP-GL/2  (/F0-, /F0), HP-RTL (/F0+),  PostScript
         (/FS), PCX/DCX (/FZ),  and  PS  preview  (/FY)  you  can append  the
         nominal device resolution.  Matching the  nominal  resolution to the
         printer  is critical  for  HP-RTL and  is  often useful  for  HP-GL,
         HP-GL/2, and  PostScript.  For PCX/DCX and  PS preview  the  nominal
         device resolution may be one or two numbers.
                                                                    continued


                                                                         p-16
         For output  formats other  than bit  maps,  you  can append the true
         horizontal  and  vertical   resolution  of   the  output  device  in
         dots/inch.  This overrides the normal output  device resolution, but
         does not affect the structure of the  output.  These numbers  should
         follow all other suboptions. This lets you compensate for print size
         error. For example, a 360x360 dpi printer consistently under indexes
         so  that a 6  inch high box comes out  5.94 inches.  Using 360,363.6
         (6/5.94*360 =  363.6) removes the error.  For print size correction,
         you also specify a number  from .5 to 2 which  is interpreted as the
         nominal  resolution  times this  number.  For  example on  a 360 dpi
         printer, 1.0,1.01 is the same as 360,363.6.

         Each printer driver has a default level of  data compression, chosen
         to give maximum compatibility among the different  printers that the
         driver supports.  Many  drivers have  an optional enhanced  level of
         compression, chosen with  !.  This  will be incompatible  with  some
         printers.  And  some drivers let you turn all compression off with ­
         (ASCII 173).  This is rarely of any use.  Where these suboptions are
         effective, they are marked in the table below.

         PrintCAD cannot use any  of the  display drivers or the EPS  preview
         bit map driver.

         Where effective, the !, ­, `, and ~ modifiers are listed below.

         /F0-[i]      ~ HP-GL/2 printers ....................... 600x600, ixi
         /F0[i]       ~ HP-GL/2 raster plotters                  600x600, ixi
         /F0+[i]      ~ HP-RTL raster plotters ................. 300x300, ixi
         /F1         `~ IBM 9 pin                                      120x72
         /F1+        `~ IBM 9 pin (2 pass) .......................... 120x144
         /F1*        `~ IBM 9 pin (4 pass)                            240x144
         /F2            IBM Quietwriter 2 ........................... 240x240
         /F3            IBM Quietwriter 3                             240x240
         /F4-        !­ IBM LaserPrinter (PPDS mode) ................ 150x150
         /F4         !­ IBM LaserPrinter (PPDS mode)                  300x300
         /F4+        !­ IBM LaserPrinter (PPDS mode) ................ 600x600
         /F5        !`~ IBM 24 pin alternate 1                        180x180
         /F5+       !`~ IBM 24 pin alternate 1 (2 pass) ............. 360x180
         /F5*       !`~ IBM 24 pin alternate 1 (4 pass)               360x360
         /F6          ! IBM Proprinter X24 .......................... 180x182
         /F6+         ! IBM Proprinter X24 (2 pass)                   360x182
         /F6*         ! IBM Proprinter X24 (4 pass) ................. 360x364
         /F7          ­ Canon BJ IBM mode, IBM ExecJet                360x360
         /F7+         ­ Canon BJ IBM mode, IBM ExecJet (2 pass) ..... 360x360
         /F8[i]         HP-GL                                  1016x1016, ixi
         /F9        !`~ NEC 24 pin .................................. 180x180
         /F9+       !`~ NEC 24 pin (2 pass)                           360x180
         /F9*       !`~ NEC 24 pin (4 pass) ......................... 360x360
         /F#          ­ JRL J bubblejet Epson mode                    360x360
         /F$         `~ Epson Esc/P2 ................................ 360x360
         /F$+        `~ Epson Esc/P2                                  720x720
         /F&         `~ Canon BJ/BJC native mode .................... 360x360
         /F:         `~ Star Micronics SJ-144                         360x360
         /F@          ~ Canon BJC CaPSL mode ........................ 360x360

                                                                    continued


                                                                         p-17
         /FA-       !`~ HP DeskJet 500C, color PCL .................. 150x150
         /FA        !`~ HP DeskJet 500C, color PCL                    300x300
         /FB        ­`~ Canon BJ/BJC Epson mode, Epson Stylus ....... 360x360
         /FB+       ­`~ Canon BJ/BJC Epson mode (line overlap)        360x360
         /FC            CGA display ................................... 62x25
         /FD-        !­ Canon LBP (ISO/CaPSL mode)                    150x150
         /FD         !­ Canon LBP (ISO/CaPSL mode) .................. 300x300
         /FD+        !­ Canon LBP (ISO/CaPSL mode)                    600x600
         /FE         `~ 128K EGA color display ........................ 62x45
         /FF        !`~ Fujitsu 24 pin                                180x180
         /FF+       !`~ Fujitsu 24 pin (2 pass) ..................... 360x180
         /FF*       !`~ Fujitsu 24 pin (4 pass)                       360x360
         /FG          ­ PDP Protracer (IBM mode) .................... 360x360
         /FH            Hercules graphics card display                  70x45
         /FI-           HP LaserJet 3, DeskJet ...................... 150x150
         /FI            HP LaserJet 3, DeskJet                        300x300
         /FI+           HP LaserJet 4 ............................... 600x600
         /FJ            Canon BJ BJ130 mode                           360x360
         /FK          ~ Kodak Diconix Color 4 ....................... 192x192
         /FL-        !­ HP LaserJet                                   150x150
         /FL         !­ HP LaserJet ................................. 300x300
         /FM            128K EGA monochrome display                     62x45
         /FN         `~ Epson 9 pin .................................. 120x72
         /FN+        `~ Epson 9 pin (3 pass)                          120x216
         /FN*        `~ Epson 9 pin (6 pass) ........................ 240x216
         /FO        !`~ Toshiba 24 pin                                180x180
         /FO+       !`~ Toshiba 24 pin (2 pass) ..................... 360x180
         /FO*       !`~ Toshiba 24 pin (4 pass)                       360x360
         /FP         !~ HP PaintJet ................................. 180x180
         /FQ            HP QuietJet (PCL mode)                        192x192
         /FR         `~ Tektronix ColorQuick ........................ 216x216
         /FS[i]       ~ PostScript                               600x600, ixi
         /FT        !`~ Epson 24 pin ................................ 180x180
         /FT+       !`~ Epson 24 pin (2 pass)                         360x180
         /FT*       !`~ Epson 24 pin (4 pass) ....................... 360x360
         /FV         `~ VGA display                                     62x62
         /FV+        `~ VESA 800x600 VGA display ...................... 78x78
         /FV+b       `~ 800x600 VGA display - mode b                    78x78
         /FV*        `~ VESA 1024x768 VGA display ................... 100x100
         /FV^        `~ VESA 1280x1024 VGA display                    125x134
         /FV%        `~ Windows display (PrintGL/W only) ....................
         /FW         `~ Epson 9 pin alternate                          120x72
         /FW+        `~ Epson 9 pin alternate (3 pass) .............. 120x216
         /FW*        `~ Epson 9 pin alternate (6 pass)                240x216
         /FW%        !~ Windows default printer (PrintGL/W only) ............
         /FX        !`~ IBM 24 pin alternate 2                        180x180
         /FX+       !`~ IBM 24 pin alternate 2 (2 pass) ............. 360x180
         /FX*       !`~ IBM 24 pin alternate 2 (4 pass)               360x360
         /FY[i[,j]]     append EPS preview bit map .......... 72x72, ixi, ixj
         /FZ[i[,j]]  `~ ZSoft PCX                           100x100, ixi, ixj
         /FZ![i[,j]] `~ DCX ............................... 100x100, ixi, ixj

         See Output Devices (Displays, Printers, Plotters, Bit  Maps, Fax) to
         match your printer with one of these drivers.                       


                                                                         p-18
       /I - Scaling Point Location Option -----------------------------------

         /IA|R|W[N] - IP point location - default /IA

         "scaling pnts"

         This  option is not useful with AutoCAD or any software that outputs
         HP-GL that  does not use  scaling commands  or that initializes  the
         plotter or sets the scaling points.

         The  I option  sets the initial scaling points (P1, P2 - the scaling
         points  may  be set  in  the HP-GL  file  with  the IP  command).  A
         (absolute) sets the points  to the default  for  the paper size (see
         below).  R fits P1 and P2 to the print window with at least .25 inch
         margins  and an x/y ratio of 10/7.2 (the same ratio as  the HP  7475
         with small paper).  W fits P1 and P2  to the print window with a .25
         inch margin. N makes the margin 0 for R or W and is ignored with A.

         The   default  scaling   points  are  plotter   specific.   If   the
         magnification is  1.0  then  PrintGL looks at  the print window  and
         orientation to decide if they match one of the plotters/papers noted
         below.  If so  the default scaling points match that plotter.  If no
         match  is  found or the magnification is not 1 then the defaults are
         taken from the 7440.

         7440                     7475                     7550
         paper  window            paper  window            paper  window
         A       7.54,10.14       A       7.84,10.20       A       7.72, 9.92
         A4      7.54,10.74       A4      7.60,10.88       A4      7.48,10.70
                                  B      10.20,16.38       B      10.01,16.19
                                  A3     10.88,15.90       A3     10.70,15.72

         /IWN  sets the scaling points to fit the print window

       /J, /K - Printer Code Prefix, Suffix Options -------------------------

         /J[b,b,..] - printer code prefix - default /J
         /K[b,b,..] - printer code suffix - default /K

         "modify output" "prefix codes: "
         "modify output" "suffix codes: "

         /J lets you send codes to the printer before PrintGL's usual data is
         sent and /K  lets you send codes after PrintGL's usual data is sent.
         This lets you set up and reset the  printer for special  situations.
         For  HP-GL  and   PostScript  output,   the  /J  codes   follow  the
         initialization commands.

         The codes  are  specified  with  byte  values  (0..255  or  $0..$FF)
         separated with blanks or commas.

         /J27 69  does a printer reset before printing on HP-PCL printers    


                                                                         p-19
       /L - Page Layout Option ----------------------------------------------

         /L[B][F|N][R][x,y[,x,y]] - page layout - default depends on printer

         "window/margins"
         "form feed"
         "box"
         "reverse image"

         The L option defines the page layout.

         B boxes the plot at the print window edge using pen 40.

         F, the default,  turns  form feeds on and  N  turns  form feeds off.
         These are ignored for bit maps and display output.

         R  reverses the  colors on displays, bit maps, and output formats 4,
         D, I, and L  (Canon,  HP, and IBM  page  printers) and is  otherwise
         ignored. This gives the equivalent of a photographic negative.

         The first optional x and y are the print window width  and height in
         inches.  These define  the hard  clip  limits.  These values are not
         checked against the printer's capabilities.  If you specify  a print
         window  that  exceeds  the  output  device limits, the  results  are
         unknown.  You may need to reset the printer's margins or page length
         for large plots (see Large Paper). The size needed for a given width
         and height exceeds x and y by 8 dots to allow for line widths.

         The  second  optional x and y are the left and top margins, measured
         from the printer's  left margin and current vertical position to the
         print window. The margins for HP-GL and PostScript are measured from
         0,0 (left, bottom).  Margins are ignored for display output  and bit
         maps.

         THE PRINT WINDOW PLUS THE MARGINS MUST FIT WITHIN THE PRINTABLE AREA
         OF  THE PRINTER.  To find the largest printable area turn on the box
         and form feed  options  and set a  window and margins of 7.5,10,0,0.
         Any plotfile will do - the  only  concern  is the box.  Increase the
         window until you have the largest  box that fits on the paper.  This
         is the best that you can do. To improve centering you can reduce the
         print window and increase the corresponding margin.

         The default print window is 7.54x10.14 for printers and bit maps and
         10.14x7.54 for HP-GL and displays, corresponding to HP 7440 A paper.
         The  default  margins are printer  specific to compensate for  paper
         handling.

         /L7.5,3,.5,0   print window 7.5x3, left margin .5, top margin 0
         /L7.54,10.14   sets window equivalent to HP 7440 with A  paper
         /L7.54,10.74   sets window equivalent to HP 7440 with A4 paper
         /L7.84,10.20   sets window equivalent to HP 7475 with A  paper
         /L7.60,10.88   sets window equivalent to HP 7475 with A4 paper
         /L10.20,16.38  sets window equivalent to HP 7475 with B  paper
         /L10.88,15.90  sets window equivalent to HP 7475 with A3 paper      


                                                                         p-20
       /M - Magnification Option (Scale, Size) ------------------------------

         /M[F]x - magnification - default /MF.9

         "magnification"

         The M option  sets the magnification.  F fits  the plot to the print
         window.  The default, /MF.9, prints at  90% of the largest size that
         fits in the print window.

         /MF.9  prints at 90% the largest size that fits in the print window
         /M1    plots at the same size as an HP 7475

       /N - Page Number Option ----------------------------------------------

         /N[i] - page number - default /N

         "plot page"

         /Ni says to print only page i of the plotfile. If you do not specify
         i then all pages in the plot will be printed (this is the default).

         This option is not allowed with PrintCAD.

         /N   prints all pages in the plotfile
         /N3  prints only page 3

       /O - Origin and Orientation Option -----------------------------------

         /O[1|2|3|4[L]] - origin, orientation - default /O

         "origin/rotate"

         The O  option  sets  the print  window origin  and orientation.  The
         origin  is  one of four corners numbered 1..4  for upper left, lower
         left, lower right, and upper right, and implies a plot rotation. The
         L suboption specifies a left handed coordinate system, which mirrors
         the plot.  If no origin is specified then it is chosen so that the x
         axis is the longer dimension.

         Here are  pictures of PrintGL's view of the output media compared to
         an HP 7475's view.

         HP 7475                               PrintGL
                                                             display or
         A size           B size               printer       plotter

           y --------     0,0 -------- y       ul  ----- ur   ul  -------- ur
            |        |       |        |         1 |     |4     1 |        |4
            |        |       |        |           |     |        |        |
         0,0 -------- x      |        |           |     |     ll  -------- lr
                             |        |           |     |      2           3
                             |        |        ll  ----- lr
                             |        |         2        3
                            x --------

         /O2  puts the print window's origin in the lower left corner        


                                                                         p-21
       /P - PrintGL/D and PrintGL/W Plotfile Option -------------------------

         /Pf - plotfile - no default

         "plotfile"

         The plotfile may be specified as the first parameter with no prefix,
         or  it may be specified anywhere in the option list with /P.  If you
         use a  file name  mask with "*"  and/or  "?",  each matching file is
         processed, but the first failure or user break stops all processing.

       /P - PrintCAD Intercept Mask Option ----------------------------------

         /PADI|mask - intercept mask

         /PADI sets up PrintCAD as an AutoCAD ADI plotter driver. /Pmask lets
         you  choose  a DOS file mask as PrintCAD's intercept mask.  The mask
         should not include disk  or directory information - PrintCAD ignores
         this information when looking at  file names.  The mask may  contain
         the character #.  This is the same as ?, but when a file matches the
         mask   the  character  that  matches  the  #  selects  the  PrintCAD
         configuration - 1..5  selects configurations 1..5  and anything else
         selects configuration 1.

         AutoCAD 10 will work with PrintCAD only via /PADI.

         Regardless of the /P option, PrintCAD always responds to PCAD#.PLT.

         /Padi     sets up PrintCAD to take data from AutoCAD interrupt 78
         /P*.plt   intercepts data written to *.plt
         /Px#.plt  intercepts data written to x1.plt, x2.plt, etc.

       /Q - Number of Copies Option -----------------------------------------

         /Q[H]i - number of copies - default /Q1

         "copies"

         /Q sets the number of copies for each printed  page.  The default is
         one. The H suboption specifies to send the codes to have the printer
         produce  multiple  copies, which is much faster than having  PrintGL
         send the data for each page. This only works with page printers.

       /R - Internal Resolution Option --------------------------------------

         /Ri - internal resolution - default /R1016

         "plotter" "internal dpi: "

         /R sets the internal grid resolution  in dots/inch.  It is  normally
         1016 and rarely needs  to be changed.  To fit very large plots  into
         the   -32768..32767  coordinate  limit,  use   /R508.   Setting  the
         resolution to a multiple  of the output device  resolution times the
         magnification may yield a small improvement in print quality.       


                                                                         p-22
       /S - Pen Shading Option ----------------------------------------------

         /Sc.. - pen shading patterns - default /S0

         "pen shade"
         "pen all"

         /S  assigns a shading pattern to each pen.  Unspecified pens use the
         last specified  shade.  The  shade values  are  0..4  and A..M.  The
         percent coverage for each shade is listed below.  Narrow line widths
         may not work well with some shade patterns.

           0 100%     1 75%       A 6.2%      D 87.5%     G 93.7%     K 43.7%
                      2 50%       B 3.1%      E 62.5%     H 81.2%     L 31.2%
                      3 25%       C 1.6%      F 37.5%     I 68.7%     M 18.7%
                      4 12.5%                             J 56.2%

         Some  printers,  especially dot matrix printers in  multipass modes,
         wash out high percentage shade patterns because they have a dot size
         that is large relative to the dot spacing.

         /S024  sets pen 1 to solid, pen 2 to 50%, pen 3..40 to 12.5%

       /T - Temporary File Option -------------------------------------------

         /T[+]f - temporary file - default /TPLOT.TMP

         "temp file"

         PrintGL uses a temporary  file  when there is  not enough memory  to
         handle a plotfile.  You can use /T to put it on a RAM disk for extra
         speed. You can force the use of a temporary file with + (if the plot
         fills the buffer). Using a RAM disk may speed printing.

       /W - Pen Width Option ------------------------------------------------

         /Wc.. - pen widths - default /WA

         "pen width"
         "pen all"

         The W option assigns pen line widths. Each width may be 0..9, .10 ..
         .24 dots, A..I for  2..10 units of 4/1016 inch (.1 mm), M for 4/1016
         inch  (.1  mm), or N to  turn off  the  pen.  A..I and  M widths are
         approximations, based on the device  technology.  Odd widths of 9 or
         above are modified to the next higher (even) width.  Unassigned pens
         use the last assigned width.

         For nonsquare matrix printers, PrintGL uses pen points optimized for
         an h/v ratio of .67, 1, or 1.5.  Widths are figured in the direction
         of higher resolution, and are not accurate in the other direction.

         Line widths  of over eight dots are  distorted at  the print  window
         edge to fit within the four dot border.

         /WA      sets pens 1..40 to .2 mm
         /WB2.16  sets pen 1 to .3 mm, pen 2 to 2 dots, pens 3..40 to 16 dots


                                                                         p-23
       /X - PrintGL/D and PrintGL/W User Interface Option -------------------

         /X[B][C][O][P][S][F][U][M][Z][V] - interface options - default /X

         "other"

         The X option sets various interface options. C causes a break when a
         plot is clipped.  P causes  a pause  before  each  printed  page.  O
         suppresses file overwrite queries.

         S suppresses  location  and  size messages.  F  suppresses location,
         size,  file  name, and page  number messages.  B suppresses progress
         messages.  U  suppresses unsupported  command and  incorrect  number
         messages. V starts PrintGL/W as an icon (command line only).

         M prevents PrintGL from allocating DOS upper memory blocks.

         Z turns off the shareware notice panel (menu only).

         /XS  gives only the most important messages

       /X - PrintCAD Control Option -----------------------------------------

         /XQ - queries PrintCAD installation
         /XR - removes PrintCAD if allowed
         /X[E|N|X][A][M][L][W][P][S][Z][-|+] - controls PrintCAD's setup

         /XQ  checks to see  if  PrintCAD is installed.  /XR removes PrintCAD
         from memory, if allowed. /XQ and /XR disallow all other options.

         The other  suboptions  control setup,  and  are  effective only  for
         initial setup. X specifies XMS for swapping - this is the default. E
         forces the use  of  EMS  for  swapping instead  of  XMS.  N inhibits
         swapping.  This forces the  entire program to load in low memory and
         it will  take a large chunk of  DOS  memory.  In return,  all of the
         compatibility problems of  swapping TSRs  are removed.  This  can be
         very useful with DOS extender based CAD programs.

         A sets  an  alternate  handle  (use  with PC-Draft-CAD,  Drafix, and
         DesignCAD).  M sets an alternate mouse handler. These suboptions may
         improve compatibility.

         L forces PrintCAD to load its resident  part low.  W forces PrintCAD
         to load its swapping work area low.  P causes program prefix segment
         checking.  These  suboptions may  improve compatibility  in  unusual
         situations, but are generally not needed and may make things worse.

         + or  -  increases  or  decreases  the PrintCAD  memory  space,  for
         improved speed or reduced resource usage.

         S adds progress beeps. This is not advised with the N suboption.

         Z turns off the shareware notice panel.

         /XM  sets up PrintCAD with its alternate mouse handler              


                                                                         p-24
       /Y - Plotter Options -------------------------------------------------

         /Y[D|Y][S|E][A][1|2][N][B] - plotter options - default /YDS

         "plotter" "D/Y switch position: "
         "plotter" "S/E switch position: "
         "plotter" "read ADI: "
         "plotter" "read HP-GL/2 (Y|except Pens|N): "
         "plotter" "start on for Y, HP-GL/2: "
         "plotter" "large polygon fill buffer: "

         The  Y option sets the plotter's D/Y switch  to D  or Y  and the S/E
         switch to S or E.  Y  starts with  the plotter off  and responds  to
         esc.(, esc.Y, esc.), and esc.Z commands.  D starts with the  plotter
         on and ignores these commands. S sets the standard interpretation of
         IW (clipping  window) commands.  E sets 7550 enhanced interpretation
         of IW commands, so that they use scaled coordinates.

         The A suboption turns on  PrintGL's ADI handler.

         The 2 suboption turns on PrintGL's HP-GL/2 subset interpretation and
         sets the Y and E suboptions.  The 1 suboption is the same but causes
         PrintGL   to  ignore   HP-GL/2  pen   width,   color,  shading,  and
         transparency control.

         The N  suboption starts  with the  plotter  on  if the  Y  switch or
         HP-GL/2 processing is on.  This is useful  for HP-GL/2  that assumes
         the plotter is already in HP-GL/2 mode rather than HP-RTL mode.

         B increases the polygon fill buffer by 4000 line segments.

       /Z - Processing Options ----------------------------------------------

         /Z[x,y[,z]][E][C] - processing options - default /Z10,5,180

         "plotter" "def, min, max chord angle: "
         "plotter" "enhanced font: "
         "plotter" "color to shade on b/w formats: "

         Except  for the  C suboption, this  option is not  useful with HP-GL
         (including AutoCAD's) or ADI that  draws circles, arcs, and text  as
         line segments rather than using circle, arc, and label commands.

         The Z option  specifies  the  default,  minimum, and  maximum  chord
         angles for circles and arcs.  The HP 7475 defaults to  a chord angle
         of 5 with  no  minimum.  Using chord  angles of less than 10 returns
         little print quality  improvement and adds  to processing time.  The
         default is /Z10,5,180. For better emulation use /Z5,2,180.

         The E suboption says to  use  the enhanced  font, which doubles  the
         number of chords on curves in text,  improving the curve smoothness.
         This is only effective on character heights above .5 cm.

         C says  to  convert colors to  shade  levels  for monochrome  output
         formats. Otherwise all colors except white are converted to black.

         /Z5,2  sets the default chord angle to 5 degrees, the minimum to 2  


                                                                         p-25
       PrintGL/D and PrintGL/W Menu -----------------------------------------

         PrintGL/D  and PrintGL/W include  a menu interface to let you select
         options, choose a  list  of  plotfiles, and print.  Run PRINTGLD  or
         PRINTGLW with no command line parameters to bring up the menu.

         The main menu is displayed at the top of the  screen, and the bottom
         of the screen is used differently for each main menu item.  The main
         menu is divided  by column  into  six  groups, described below.  The
         functions of the menu items are described in detail above.

         When the  cursor is  on a main menu item, the current  state of  the
         submenu is displayed below.  To change the submenu, press Enter. The
         items are  modified with  cursor movement and  typing numbers/names.
         Enter returns you to the main menu with the new values.  Esc returns
         you to the main menu with the values unchanged.

         The PrintGL documentation can be viewed by pressing F1 from any menu
         that displays F1 on its key line.

         If one of the first two letters of  a main menu item is capitalized,
         that item may be accessed immediately by pressing the letter. When a
         cursor bar has a notch, the value in the notch may be edited.

       Menu Specific Functions ----------------------------------------------

         The first column  of  main  menu items is  dedicated to menu related
         functions  These  include   run  PrintGL,  switch  to  an  alternate
         configuration, exit, save the configurations,  set menu options, and
         create a BAT file corresponding to the current configuration.

         The "Alt config" item rotates between five menu configurations.  The
         current  configuration name is in the upper left corner.  Menu items
         that begin with * are the same for every configuration.

         The "save configs" item saves all of the current menu configurations
         by writing them into the EXE file.  Only the first nine lines in the
         plotfile list are saved.  You  can copy the EXE  file to a different
         name and it will have its own configurations.

         The "menu config" item lets you  set the  configuration name, screen
         colors,  and the name of  the BAT  file created by  the "create BAT"
         option.  For PrintGL/W  you  can  choose  the  screen  font  height,
         selected from  current  "fixedsys" fonts,  VGAFIX (15), and  8514FIX
         (20). Screen colors are specified with the mnemonics listed here:

           k black    r red             k+ gray            r+ bright red
           b blue     m magenta         b+ bright blue     m+ bright magenta
           g green    y yellow/brown    g+ bright green    y+ bright yellow
           c cyan     w white           c+ bright cyan     w+ bright white

         For  PrintGL/W you can use  - and * as  color  modifiers.  These are
         effective with 15, 16, or  24 bit color setups.  To use  the default
         Windows colors, blank out the desired line of colors.

         "create BAT" creates a single configuration BAT  file for  PrintCAD.
         You will have to add any /X or /P options as desired.               


                                                                         p-26
       Menu Input and Output Choices ----------------------------------------

         Column two  of the main menu lets  you choose the plotfiles to  plot
         (the /P  command line option), the plot page number (/N), the output
         destination  (/D),  output format  (/F),  and modifications  to  the
         output  -  compression  mode  (/F),  horizontal  and  vertical  size
         multiplier (/F) and prefix and suffix printer codes (/J, /K).

         You  may enter up to 99  plotfiles  in the "plotfile" submenu.  Each
         file may  be preceded  by a repetition count from 2 to 5.  To choose
         from a list of files, enter a mask name and press  Enter (the cursor
         must  be  on  the  mask).  The menu  will  then  display  a list  of
         corresponding  files.  Select any number of the  files by moving the
         cursor  to  the desired file and pressing Space (or the  right mouse
         button).  Consecutive presses increment the repetition count.  If no
         files have been selected, then pressing Enter selects the file under
         the cursor.  The selected files are added to the file list below the
         cursor.  Files that would overflow the 99th position on the plotfile
         list are dropped.

         Directories are shown at the top of file lists and are designated by
         a trailing \.  If you select  a directory (repetition counts are not
         allowed), then you can use that to display a new file list.  This is
         handy for navigating a disk to search for image files.

         The first nine plotfiles are saved when you do a "save configs".

         When you "Run PrintGL", PrintGL is run for each file on the plotfile
         list. Masks are ignored. For any plotfiles that are not successfully
         processed, an arrow is inserted in front of  the plotfile name.  You
         can  view the results from the "plotfile" main menu item.  The arrow
         is  not  considered  part  of the file  name, so you do not need  to
         remove it to retry PrintGL.

         Printers that  support  color  have  a  color  option ("clr:" on the
         menu).  This lets you specify a  black/white printer even though you
         may have set  up colors with the  "pen color"  menu.  Output formats
         that do not support color do not have this option and always convert
         the selected colors to black and white.

       Menu Processing Options ----------------------------------------------

         The  third  column  of  main  menu  items  define  how  the  plot is
         processed.  The  options  include  magnification  (/M), origin (/O),
         position (/A), plotter (/Y,  /Z,  and  /R options  such  as ADI  and
         HP-GL/2   interpretation,   default  chord   angles,   and  internal
         resolution), and initial scaling points (/I).

       Menu Pen Options -----------------------------------------------------

         The fourth column of main menu items covers the pen characteristics:
         width (/W), color and opaque/transparent mode (/C),  and shade (/S).
         Each of these submenus use the up  and  down cursor keys to select a
         pen, and the left and right cursor keys to choose an attribute.  The
         "pen all" submenu combines the four other submenus to let you see or
         choose all of a pen's attributes at once.
                                                                    continued


                                                                         p-27
         For  color  selection,  the  one character  colors (b,c,g,k,m,r,w,y)
         represent  pure  colors,  and  the  two character  colors are  shade
         pattern mixes.  The  shade pattern  mixed  colors  use  the  current
         shading  option  for  that  pen,  unless the  shade  pattern is 100%
         (solid), in which case 50% is used.

       Menu Page Layout Options ---------------------------------------------

         The fifth  column  of  main menu items  covers the page layout.  The
         first three items are suboptions of the /L option - print window and
         margins, form feed, and box. Tiling options (/B) and multiple copies
         (/Q) are also here.

       Menu Other Options ---------------------------------------------------

         Other options are  in column six.  These  include the temporary file
         name (/T),  and  under  "other", the pause  to load  paper, suppress
         unsupported command  messages and other  /X suboptions and one  line
         that lets you enter command line options to override anything on the
         menu.

         At the bottom of column six are the auto run options.

       Menu Auto Run Mode ---------------------------------------------------

         The lower right corner of the menu  includes  "auto  opts" and "auto
         run".  In auto run mode,  the disk is  continually searched  for new
         files that match the mask or file specified in "auto opts". Whenever
         one  is  found, PrintGL is run on  that file.  This  is useful  with
         multitasking systems such  as DESQview and  Windows.  Run  PrintGL's
         auto run mode and switch it to the background.  Then you can  output
         files and they will be printed automatically.

         The auto run mask may  include the # character.  This is the same as
         ?, but when a file matches the mask the character that matches the #
         selects the PrintGL configuration - 1..5 selects configurations 1..5
         and anything  else  selects  the  current configuration.  The  first
         character of the  configuration  title must  be  1..5 to  match  the
         selected configuration.

         Auto run mode uses  one of two ways of choosing new files (specified
         under "auto opts"). The first is by time/date stamp. In this mode it
         will only catch files that have a time/date stamp that is later than
         when  auto  run  mode was started  and  is later than the  last file
         processed  in auto run mode.  The file  with the  earliest time/date
         stamp  is  processed first.  Copying  a  file does  not  change  its
         time/date  stamp, so  copying a  file  to the auto run mask will not
         cause it to be seen as a new file.

         The second way is by archive bit. When auto run mode is started, any
         file  that  matches the  mask and has its archive bit  set  will  be
         processed, regardless  of  when it  was created.  The file  with the
         earliest time/date stamp is processed first. After it is chosen, its
         archive bit is unset so that it will not be chosen again.  This lets
         you copy files to the auto run mask to print them.                  


                                                                         p-28
       Large Paper ----------------------------------------------------------

         PrintGL can handle printing on paper  larger than the  usual 8.5x11,
         but this takes some extra work. First you need to increase PrintGL's
         print window  to cover  the large  paper.  This  is done with the /L
         option  or "window/margins".  The print window plus the margins must
         fit within the printer's printable area.

         And then you must make  sure that your printer recognizes the larger
         paper height.  For  continuous  forms paper  this  is  best  done by
         setting skip perforation to off,  either by  printer switch or  with
         PrintGL prefix codes.  For Canon, Epson, Fujitsu, IBM, and NEC  line
         printers (dot  matrix,  ink jet, thermal) use  /J27  79,  or "modify
         output" "prefix codes: 27 79".

         For  cut  sheet  paper,  on Canon  (except BJ  native  mode), Epson,
         Fujitsu, IBM, and  NEC line printers use /J27 67 0 n, where n is the
         page length in inches.  For the PDP ProTracer use /J27 67 n, where n
         is the page length in lines, at six lines per inch.

         And for some printers you need to increase the right margin. For the
         Canon BJC  in  Epson  mode  use  /J27 81 114.  For the HI V50/100 in
         printer mode use /J27 91 88 2 0 1 255.

         For page  printers, legal size  paper  may  be specified  with these
         printer code prefixes: HP-PCL  printers  /J27 38 108 51 65  (/K27 38
         108 50 65 to  reset to letter), Canon  LBP  /J27 91  51 50 59 59 112
         (/K27 91 51 48  59 59 112 to reset), IBM LaserPrinter /J27 91 70 5 0
         3 1 2 1 (/J27 91 70 5 0 3 1 1 1 to reset).

         To  get  a 10x16  print window on  11x17 paper with  a Canon, Epson,
         Fujitsu,  IBM, or NEC line printer, use these options: /L10 16 0 .25
         /J27 67 0 17.  You  will probably need to adjust the margins (0 .25)
         for best centering.

         The  maximum  width  of  the print  window on  most  narrow carriage
         printers is 8  - 8/(horizontal dpi).  For 300 dpi printers,  this is
         7.97.  At 120 dpi it is 7.93.  The maximum width of the print window
         on most wide carriage printers is 13.6 - 8/(horizontal dpi).  At 180
         dpi this is 13.55.  At 360 dpi it is 13.57.  The  horizontal  margin
         should be set to 0 to get this width.                               


                                                                         p-29
       Tips On AutoCAD ------------------------------------------------------

         There are many ways to use PrintGL with AutoCAD.  Here is a good way
         to start.

         Configure  AutoCAD for an HP 7585 plotter.  Select output to a file.
         Do not do any plotter calibration. Set a specific scale, do not fit.
         Do not rotate.  Set  a plotter  window that is larger than  you will
         ever  need,  30x30  for  example  (this  will  prevent  AutoCAD from
         clipping the  plot).  Set  up your plotter  pen table so  that  each
         screen color is assigned a different pen.

         With  PrintGL  you  can  rotate  (/O  or "origin"), magnify  (/M  or
         "magnification"), assign pens (/C,/S,/W or "pen color", "pen shade",
         "pen  width"),  and  calibrate  (/F or  "modify  output"  "h,v  size
         multiplier").  Use /A or  "position"  "plot  center  at print window
         center" to automatically center your plot in the print window.

         To use  the AutoCAD  12 plot preview  function  set the AutoCAD plot
         area  to match the PrintGL print window with horizontal and vertical
         numbers reversed (for an 8x10 print window set a 10x8 plot area).

       Color Processing -----------------------------------------------------

         Color graphics devices use a variety of color technologies.  PrintGL
         supports these basic types.

         CMY or cyan/magenta/yellow is used by inkjet printers with  no black
         ink. This uses three color planes and gives eight pure colors.

         CMYK or  cyan/magenta/yellow/black  is used by inkjet and dot matrix
         printers.  This uses  four color planes and gives eight pure colors.
         Using black ink instead of  a  cyan/magenta/yellow  mix gives a more
         neutral black color.

         RGB  or red/green/blue is used  by displays and bit maps.  This uses
         three color planes and gives eight pure colors.

         RGBI  or red/green/blue/intensity is used  by displays and bit maps.
         This  uses  four  color planes.  All simple colors except black  are
         intense.  When you specify any  color  mixed with black at 50%, then
         instead  of  mixing the colors  at 50%, the intensity is turned off.
         This gives fifteen pure colors.

         CMYK and RGBI are used by default when they are appropriate. You can
         switch to CMY or RGB with the ` suboption of /F.  For displays  this
         gives a better picture of how a printer will handle the colors.  For
         dot matrix printers it may speed printing by  eliminating the use of
         the black ribbon.

         /FA!  (300  dpi  color HP-PCL)  uses  CMY  color by  default.  /FA!`
         switches to CMYK color to access true black on the DeskJet 550C.    


                                                                         p-30
       Compatibility and Technical Information ------------------------------

         PrintGL/D  will run on any DOS  computer  with MS-DOS  3.0 or above.
         MS-DOS 3.3 or later is recommended.  It requires up to 256K of  free
         memory.  More memory may speed printing.  The PrintGL/D menu can use
         any  text display  mode  with  at  least 80  columns and  25  lines.
         PRINTGLD.EXE should  not  be  compressed  with  EXE file compressors
         because it rewrites the EXE file when saving its configurations.

         PrintGL/W is an MS Windows 3.1 program  and requires a 286 computer.
         It uses its own printer drivers, not Windows printer drivers.

         PrintCAD will  run on any DOS 286 computer with  MS-DOS 3.0 or above
         with 400K  of  EMS or XMS memory and  a base memory region of  512K.
         Because it is a swapping resident program, it  may  have problems in
         some environments. PrintCAD can handle VCPI (Virtual Control Program
         Interface) based  DOS  extenders, but DPMI based  programs and stand
         alone DOS extenders may cause problems.

         When  using a DOS extender  based program  such  as  AutoCAD  386 or
         Microstation   4,  use  an  extended/expanded  memory  manager  that
         provides VCPI, such as MS-DOS 5 EMM386/HIMEM, QEMM 386, or 386MAX.

         PrintGL was written  by Cary Ravitz and compiled with Borland Pascal
         7.0.

       HP-GL, HP-GL/2, and ADI Commands -------------------------------------

         PrintGL supports  the  7475  and 7440/17440 command  sets except for
         character  set 8 (Katakana), digitize commands, output commands, the
         error mask command, and some device control commands.  In  addition,
         PG, AF,  ES,  LO, character set 5, line types -8..-1, 7,  and 8, and
         proportional spaced  fonts  are  supported.  Forty  pens are allowed
         instead of eight.

         With /YA or "plotter" "read ADI: Y", PrintGL supports ADI 4.0 vector
         plotter binary commands created at 1016  steps/inch with up to forty
         pens and up to eight non-solid line types.

         With  /Y2  or "plotter" "read HP-GL/2 (Y|except Pens|N): Y", PrintGL
         adds support for a subset of HP-GL/2, switches to enhanced IW and RO
         interpretation,  and  switches to  plotter  on/off mode  (/YY)  with
         esc%..B switching  the  plotter  on and esc%..A  switching  it  off.
         HP-GL/2 support includes pen color, shading, transparency, and width
         control, compressed data, shaded fills, 256 pens, and  the AC and IR
         commands.  PrintGL  acts  like  an HP-GL/2  plotter, not an  HP-GL/2
         printer, so form feeds are done with  the  PG  command not the  form
         feed character.  If you  are using a  monochrome printer, you should
         turn PrintGL's color off  with ~ or "clr:  N" to prevent color being
         turned  on from the  plotfile.  Many  HP-GL  files  will not  run if
         HP-GL/2 interpretation is on.

         With  /Y1 or "plotter" "read HP-GL/2 (Y|except Pens|N): P",  PrintGL
         interprets HP-GL as  with /Y2 except that the HP-GL/2 pen control is
         ignored and the PrintGL pen attributes are used.

         PRINTGL2.DOC and PRINTGL2.CHR include details on this subject.      


                                                                         p-31
       Output Devices (Displays, Printers, Plotters, Bit Maps, Fax) ---------

         Canon BJ and BJC Printers ------------------------------------------

           PrintGL has five basic drivers for Canon BJ and BJC printers.  /F7
           is  the  IBM  mode  driver.   It   works  with  the  BJ130e,  BJ5,
           BJ10/10e/10ex, BJ20, BJ200/230, BJ300/330, and BJC4000. /F7+ gives
           dark print with line to line overlap.

           /FJ is the BJ130 mode driver.  It works with all Canon BJ printers
           in IBM or native mode. The printer is set to 10 pitch text.

           /FB is the Epson mode driver. It works with the BJ200/230, BJC600,
           BJC800/820,  and BJC4000.  Color is supported.  /FB+  gives sparse
           line to line overlap. For the BJC800/820 the prefix code 27 81 114
           sets the print width to 11.4 inches.

           /F&  is  the native mode  driver.  It  works  with  the BJ200/230,
           BJC600, BJC800/820, and BJC4000 in  any mode.  Color is supported.
           Epson/IBM mode prefix codes are not compatible and are not needed.
           Always  use form feed with the  BJ native  driver unless  you have
           previously set BJ native mode.

           /F@ is the CaPSL mode driver for the BJC880. Color is supported.

           Some  of these printers have  an image density option (DIP  switch
           and/or  front panel switch).  Low density  eliminates every second
           dot. To get the full 360 dpi resolution, use high density.

         Canon LBP Printers -------------------------------------------------

           /FD works with any Canon LBP 4 and 8 printers that do not have the
           SX or 30 suffix.  If the printer is in Diablo mode, it is switched
           to ISO  mode.  At 300 dpi it takes up to one meg of printer memory
           to print a full page of graphics.

           The ! suboption switches to CaPSL 4 data compression. /FD+! is the
           best driver for the LBP 8 Mk4 at 600 dpi.

           You might need to set up the printer with /J27 59 27 91 50 38 122.
           To switch back to Diablo mode on completion, use /K27 58.

           Any Canon  LBP printer with  the SX or  30  suffix  is  an  HP-PCL
           printer and should use the /FI drivers.

         Display ------------------------------------------------------------

           When you display a plot, the cursor keys scroll the plot, S cycles
           between  full,  half  (the  default),  quarter,  and  eighth  page
           scrolling, and Enter or Esc returns to DOS.

           PrintCAD cannot drive displays.

           /FC drives a CGA, but does not give color.
                                                                    continued


                                                                         p-32
           The EGA drivers, /FE and /FM, require a 128K or 256K EGA. /FC will
           work with a 64K EGA.  /FM is for an EGA  card with a digital (TTL)
           monochrome monitor.

           /FH supports the Hercules monochrome graphics card.

           /FV works with any VGA card.

           /FV+ works with VESA 800x600 mode, /FV* works  with VESA  1024x768
           mode, and /FV^ works with VESA 1280x1024 mode.

           For MCGAs, use the VGA driver without color - /FV~.

           The Windows  display  driver (/FV%) does not  use  the  resolution
           modifier,  and instead sets the resolution to the screen  width in
           dots divided by 10.8.

           Display output cannot be redirected to a file.

         Epson, IBM 9 Pin Printers ------------------------------------------

           /FN, /FW, and /F1 cover a wide range of Epson/IBM compatible 9 pin
           dot matrix printers.  You need a  cyan/magenta/yellow/black ribbon
           to get color prints. The * drivers use 1/240 graphics. /FN+, /FN*,
           /FW+,  and  /FW*  use  1/216  indexing  and  do  three  vertically
           interleaved passes.  /F1+  and /F1* use  1/144 indexing and do two
           vertically interleaved passes. /FW sets line feeds to 1/6 inch.

           For  Epson  printers  and  other  printers  with  1/216   indexing
           hardware,  /FN  is  preferred.   For  some  not  quite  compatible
           printers,  /FW works.  For IBM Proprinters and other printers with
           1/144 indexing hardware, /F1 gives better results.

           These drivers use the following escape codes:

             esc 3  set n/216 line feeds for all /FW
             esc J  index n/216 (n=2 for 1/144 index) for all /FN and /F1
             esc L  graphics command for /FN, /FN+, /FW, /FW+, /F1, and /F1+
             esc Z  graphics command for /FN*, /FW*, and /F1*
             esc r  set ribbon color (only if color is specified)

         Epson, Fujitsu, NEC, Toshiba 24 Pin Printers -----------------------

           /FT  covers  all  Epson LQ printers and  many  compatible printers
           (Panasonic in LQ mode and others).  /FF works with  Fujitsu 24 pin
           printers in Fujitsu mode.  /F9 works with NEC 24 pin printers. /FO
           works  with Toshiba 24  pin printers.  /FO  resets the  line  feed
           distance to 1/6 inch on completion.

           For all of these  drivers,  you need  a  cyan/magenta/yellow/black
           ribbon to get color prints. The + and * drivers use 1/360 graphics
           mode, and the *  drivers use 1/360 (1/120  for /FO*)  indexing and
           reset the line feed distance  to  1/6 inch on completion.  A clean
           paper  path  with equal tension on  each side  is  needed for good
           360x360 graphics.
                                                                    continued


                                                                         p-33
           Many 24 pin printers are not capable of 360x360 graphics and a few
           cannot handle 360x180 graphics.

           The compression mode  drivers  (!  suboption  or  "modify  output"
           "compression mode: Y") may or may not be an improvement.

           The /FT drivers use the following printer escape codes:

             esc $    absolute tab
             esc * '  graphics command for /FT
             esc * (  graphics command for /FT+, /FT*
             esc +    set n/360 indexing for /FT*
             esc 2    set 1/6 indexing for /FT*
             esc J    index n/180 for /FT, /FT+
             esc r    set ribbon color (only if color is specified)

         Epson Stylus and Esc/P2 printers -----------------------------------

           /F$  drives  Epson Stylus  and  other  Esc/P2 printers.  Note that
           Esc/P2 requires a different prefix code for paper size  than other
           line  printers.  Always use the form feed option with  this driver
           unless you have previously set compressed graphics mode.

           /F$+, the 720 dpi Esc/P2 driver, is only for the Stylus Color with
           special paper.  The  prints  are  screened  by  50%  to  eliminate
           excessive ink  flow  (which  would  result  in  ink  bleeding  and
           pooling).

           /FB~  drives  Epson  Stylus  and  older  Epson  48  nozzle  inkjet
           printers,  using  compressed  Esc/P  control codes.  It  does  not
           require a form feed or interfere with previous printer settings.

         Fax/Modems ---------------------------------------------------------

           PrintGL will not create data for direct use by  fax/modem devices.
           Most fax software will read PCX or DCX (for multiple images) files
           and PrintGL can generate these files.

           Use /FZ~203,196 or "ZSoft PCX b/w h,v dpi: 203,196" to  generate a
           PCX at 203x196 dpi which is the native fax high resolution.

         HI Jetpro V50/100 --------------------------------------------------

           You can drive the HI V50/100 with  HP-GL/2.  Set the resolution to
           360  (/F0  360)  and  reverse the  width and  height  in the print
           window, for example 10x8  instead of  8x10 for  8.5x11 paper.  The
           maximum window height is 15.25.

           In printer mode the HI V50/100 acts as a Canon BJ IBM mode printer
           (/F7).  The  maximum  print width is 15.25 and you need the prefix
           code 27,91,88,2,0,1,255 to get beyond 13.6 inches.                


                                                                         p-34
         HP DeskJet ---------------------------------------------------------

           /FI works with any black/white DeskJet in portrait mode.

           /FA has three modes for different levels of color HP-PCL. /FA uses
           RGB color and works with the DeskJet 500C. /FA! uses CMY color and
           works with all color DeskJets.  /FA!` uses CMYK color to give give
           better  blacks  only on the  DeskJet 550C and 560C  (the DJ  1200C
           converts from CMY to CMYK color internally).

         HP LaserJet --------------------------------------------------------

           /FL works with any LaserJet compatible printer. /FL! works with LJ
           2 (PCL 4) printers.  /FI works with LJ 3 (PCL 5) printers. /FI+ is
           a 600 dpi driver for the LaserJet 4.

           All  of these drivers work in portrait mode, which may be set with
           /J 27 38 108 48 79 or you can reset the printer with /J 27 69.

           LaserJets with under one meg of memory may not be able to handle a
           full page of graphics. /FL!  uses less printer memory than /FI, so
           it may be preferred on LaserJet 3s with limited memory.

         HP PaintJet --------------------------------------------------------

           /FP drives 180 dpi PaintJet printers. /FP! uses data transfer mode
           2 and works only with a PaintJet XL.

           Use /FA! (the DeskJet CMY driver) with the PaintJet XL300.

         HP QuietJet --------------------------------------------------------

           /FQ works with QuietJets in HP-PCL mode.

         HP-GL, HP-GL/2, and HP-RTL -----------------------------------------

           /F8 drives HP-GL and HP-GL/2 pen plotters. The output is low level
           HP-GL, converting  text, arcs,  fill, and  clips to  vectors.  The
           output is  HP  7220 compatible, containing IN, IP, SC, SP, IW, LT,
           PA, PU, and PD commands. PG is used for form feeds. If you specify
           no form feed then multiple plots may be appended to the same page.

           /F0 drives HP-GL/2 raster plotters (HP-GL/2 / HP-RTL devices).

           /F0- drives HP-GL/2 printers (HP-PCL 5 devices).

           /F0+ drives HP-RTL raster plotters.

           For any of these drivers,  you can append  the  nominal resolution
           (for example /F8 300).  When you  set  the nominal  resolution  of
           HP-GL to other than 1016,  enhanced  IW command interpretation (HP
           7550 enhanced mode) is needed to handle dashed lines correctly.

           For  HP-GL  output  the  width  parameter (/W) is  used  as  a pen
           selector, so for each pen in the original HP-GL, you can specify a
           new  pen  in  the  output.  The  default  /W  option  for  /F8  is
           /W12345678. Shading and color are ignored.                        


                                                                         p-35
         IBM Inkjets - ExecJet 4072, ExecJet II, Color Jetprinter 4079 ------

           These are three completely different printers. The ExecJet 4072 is
           Canon BJ330 compatible. Put the printer in IBM mode and use /F7.

           The ExecJet  II and IIc  are DeskJet and  DeskJet 500C  compatible
           printers and should be used with /FI and /FA!. Use the prefix code
           27,38,108,48,69 to start printing at the top of the paper.

           The  4079 is basically  a PostScript printer and it can be  driven
           with /FS360.  Newer versions of  the printer can be  set  to ASCII
           text mode and driven with /F& (Canon BJ  native mode),  which will
           likely be faster than PostScript.  Older printers can be turned on
           with  the two leftmost buttons held down until startup is complete
           and then put in ASCII dump mode to use  /F&.  Always use form feed
           with the BJ native driver unless you have previously set BJ native
           mode.

         IBM LaserPrinter 4019, 4029, 4037, 4039 ----------------------------

           /F4  drives  any LaserPrinter 4019, 4029, or 4037 in PPDS (native)
           mode.  /FL will work for HP LaserJet mode.  At 300 dpi it takes up
           to one meg of printer memory to print a full page of graphics.

           The !  suboption or "modify output" "compression mode: Y" switches
           to 4029 data compression.  /F4+!  works with the 4029 with 600 dpi
           PPDS upgrade.

           All 4039s are HP-PCL printers and  should  be  driven with /FI  or
           /FI+ (the printer menu must be set to 600 dpi in this case). These
           printers do not support PPDS mode (/F4).

         IBM 24 Pin Printers ------------------------------------------------

           PrintGL has three drivers  for Proprinter X24 compatible printers.
           Use  native  mode, not AGM.  /F6 is for all IBM X24s and  the 24P.
           These  printers  do 1/144 inch indexing and using  them at 180 dpi
           gives horizontal  white streaks  every 2/3 inch.  The  /F6 drivers
           compensate  for this by indexing 19/144  per line, giving 182 dpi.
           To work properly the  printer must start on  a 1/72 boundary so it
           is best to keep line feeds at a multiple of 1/72 (1/6, 1/8, 1/9).

           /F5 is referred to as X24 alternate 1 and is for printers that are
           X24 compatible  except for  1/180 inch indexing.  This is the case
           with  most X24 compatible printers, including the IBM  Quickwriter
           and IBM 2390 and 2391. /F5* works only with printers that do 1/360
           indexing, including the 2390 and 2391 but not the Quickwriter.

           /FX  is referred to  as X24  alternate 2  and is  the same  as /F5
           except for the  vertical units command.  /FX  works with Panasonic
           printers in X24 mode.

           The compression mode  drivers  (!  suboption  or  "modify  output"
           "compression mode: Y") may or may not be an improvement.          


                                                                         p-36
         IBM Quietwriter 2 and 3 --------------------------------------------

           /F2  and /F3 drive the Quietwriter 2 and 3.  Line feeds are set to
           1/6 inch on completion.

         JRL J bubblejet ----------------------------------------------------

           /F# drives the JRL J bubblejet in Epson LQ mode.

         Kodak Diconix Color 4 ----------------------------------------------

           /FK drives the Color 4.

         Mannesmann Tally MT92C ---------------------------------------------

           /FA (the DeskJet 500C RGB driver) drives the MT92C.

         Pacific Data Products ProTracer ------------------------------------

           /FG drives the ProTracer (base model) in IBM Proprinter mode.  The
           maximum print window width is 14.97.

         PostScript ---------------------------------------------------------

           /FS outputs printable Encapsulated PostScript with no  preview bit
           map.  Text, arcs,  fill,  and clips are  converted to vectors,  so
           PrintGL is not a general purpose HP-GL to PostScript converter. If
           no form feed is specified then "showpage"  is not output, and more
           PostScript  may be appended to the page.  PostScript overwrites as
           it draws, so overlapping lines appear opaque.

           You  can  specify  the  nominal  resolution  of the  PostScript by
           appending it to the /F option (for example /FS 300).

           You  can specify  the paper tray with  a prefix code that includes
           the tray number followed by " XP". For example /J 49 32 88 80 uses
           tray 1.

           /FY (not included in PrintCAD) appends  a black/white TIFF preview
           bit map to a PostScript file.  To use it, create a PostScript file
           with PrintGL  and then  run  PrintGL  again, specifying  the  same
           options  except /FY  instead  of  /FS.  The  destination  file  is
           appended by  default.  /FY assumes a PostScript file, generated by
           PrintGL, is  being  appended.  You  may set  the resolution  - the
           default is 72x72 dpi. Here is an example:

             PRINTGLD printgl.plt /Dsample.eps/LB6,6/O2/FS
             PRINTGLD printgl.plt /Dsample.eps/LB6,6/O2/FY

         Star Micronics SJ-144 ----------------------------------------------

           /F: drives  the SJ-144.  Always use the form feed option with this
           driver unless you have previously set CDM mode.

           When  using /F: with PrintCAD and color you might need to use /XM+
           to give PrintCAD enough memory for processing.                    


                                                                         p-37
         Tektronix ColorQuick -----------------------------------------------

           /FR drives the ColorQuick.

         Windows Printer ----------------------------------------------------

           /FW%  drives the default Windows printer.  The data is sent at the
           resolution of the  printer and is always sent to the Print Manager
           regardless of  the PrintGL destination.  !  causes PrintGL to band
           the  output to the driver.  This can  improve print speed or cause
           Windows to abort the print.

         ZSoft PCX, DCX Bit Map ---------------------------------------------

           /FZ and /FZ~ output 1 bit/plane color and monochrome ZSoft PCX bit
           maps.  The horizontal  and vertical dots/inch  may be appended  to
           override the default 100x100, for example /FZ80,90.

           PCX  output should generally  be  directed to  a  file with the /D
           option.  For multiple page plots and tiled plots use a three digit
           number for the output file (/D option) so that a new (sequentially
           numbered) file will be created for each page.

           Since  most fax  software can  take  PCX  files  as input, this is
           useful  for  faxing images.  Use  /FZ~203,196  to  match  the  fax
           resolution.

           DCX is an extension to PCX that allows multiple images  in a file.
           /FZ! and /FZ!~ are analogous to the PCX drivers but you can append
           these images  to other DCX images by setting the destination to an
           appended file.                                                    


                                                                         p-38
       Useful Prefix and Suffix Codes ---------------------------------------

         Below, n represents  an integer,  nA represents an  integer in ASCII
         format (1 becomes 49, 2 becomes 50, 43 becomes 52 51, etc.).

         Canon,      Reset                    27 64
         Epson,      N inch paper             27 67 0 n
         Fujitsu,    17 inch paper            27 67 0 17
         IBM, NEC    Right margin n columns   27 81 n           (not for IBM)
         dot matrix, Skip perforation off     27 79
         inkjet      Unidirectional printing  27 85 1

         Canon BJ    Page length, print width x 10   27 40 103 3 0 n 1 n
         native

         Esc/P2      N/dpi inch paper         27 40 67 2 0 lo(n) hi(n)
                     Unidirectional printing  27 85 1

         HP PCL,     Reset                    27 69
         DeskJet,    Portrait mode            27 38 108 48 79
         LaserJet,   Top margin 0             27 38 108 48 69
         PaintJet    Skip perforation off     27 38 108 48 76
                     11 inch paper            27 38 108 50 65
                     14 inch paper            27 38 108 51 65
                     11x17 inch paper         27 38 108 54 65
                     Manual feed              27 38 108 50 72

         HP DJ500C   High quality, slow       27 42 111 49 81
                     No ink depletion         27 42 111 49 68

         HP PJXL300  Low quality, fast        27 42 111 45 49 81

         HP QJ       HP-PCL mode              27 37 65
                     DIP switch mode          27 37 64

         IBM LP      11 inch paper, tray 1    27 91 70 4 0 3 1 1
                     14 inch paper, tray 1    27 91 70 4 0 3 1 2
                     14 inch paper, manual    27 91 70 4 0 1 1 2

         Canon       Reset                    27 99
         CaPSL,      11 inch paper            27 91 51 48 59 59 112
         LBP,        14 inch paper            27 91 51 50 59 59 112
         BJC880      Manual feed              27 91 49 113
                     Automatic feed           27 91 48 113
                     Full page memory mode    27 59 27 91 50 38 122
                     Cursor to top of page    27 91 48 100
                     Diablo mode              27 58
                     ISO mode                 27 59

         PostScript  Paper tray n             nA 32 88 80

         ProTracer   N line paper             27 67 n

         HI V50/100  Max margins              27 91 88 2 0 1 255             


                                                                         p-39
       Answers --------------------------------------------------------------

         If  your plot is messed up, with wraparound lines covering the page,
         you have probably exceeded PrintGL's internal coordinate limit. This
         happens when the  HP-GL  coordinates exceed  32 inches.  Reduce  the
         internal resolution with "plotter" "internal  dpi: 762" or /R762 for
         coordinates up to 42 inches or /R508 for up to 64 inches.

         If  your  printer ejects the paper before the  plot is finished, you
         probably need to specify a  paper length prefix code.  For most line
         printers use /J27 67 0 n where n is the page length in inches. Canon
         BJ  native  mode uses /J27 40 103 3 0 n 1  114  where  n is the page
         length in inches times 10  (the  default is 17).  Epson Esc/P2  uses
         /J27 40 67 2 0 lo(n) hi(n) where n is  a two byte integer specifying
         the page length in dots.  The PDP ProTracer in IBM mode uses /J27 67
         n where n is the page length in lines (6 lines/inch usually).

         If  an  extra sheet of paper feeds  after a print, your print window
         probably  exceeds the print area of the printer.  Turn form feed and
         box  on and reduce the vertical window  or margin until then  entire
         box prints and just one sheet feeds.

         If  you  are having trouble getting the print size  or  location  as
         desired, check your /L option or "window/margins".  The print window
         plus  the  print  margins  must define  an area  that  fits  in  the
         printable area of  the paper.  Printers cannot print over the entire
         area of the paper. They usually require .25 to .5 inch margins.

         To  get  color output from PrintGL set  up the pens in your graphics
         package so that each pen is assigned  a  color  and assign the  same
         colors to PrintGL's pens with /C or "pen color".

         If  your prints are  coming  out not  quite to  scale, check that no
         calibration is being  done by the  graphics package and then use the
         "modify  output" "h,v size multiplier:" option  or  the /F option to
         adjust the print size. See /F - Output Format Option for information
         on print size correction.

         If  your print is  being clipped unexpectedly, and  PrintGL  is  not
         giving  a "Plot will clipped" message, the clipping may be caused by
         the  program  that   generated   the   plotfile,   the  printer,  or
         misinterpretation of the plotfile. To ensure that the printer is not
         doing  any clipping,  turn box  on and reduce the  window or margins
         until then entire box prints.  If the plotfile is using the enhanced
         clipping  window  command,  you  must   set  "plotter"  "S/E  switch
         position: Y" to interpret it correctly.

         For the Canon BJC-800 in Epson mode, the right margin  defaults to 8
         inches. Use /J27 64 27 81 114 to set it to 11.4 inches.

         For the  Canon BJ-330 and most wide  carriage printers,  the maximum
         print window  width is 13.57  inches.  This is a printer  limitation
         that you cannot get around.                                         


                                                                         p-40
       PrintCAD Answers -----------------------------------------------------

         Do not use PrintCAD with Windows. Use PrintGL/W instead.

         To access PrintCAD from a CAD package you must PLOT. Do NOT print.

         AutoCAD 10 will work with PrintCAD only via /PADI.

         If you are getting system  crashes or nothing from PrintCAD, try the
         options /XAM and /XAEM.

         To get COLOR output from PrintCAD, you must:
         - Define a multipen plotter in your CAD package.
         - Set up the  pens in the CAD package so that each color is assigned
           to a pen.
         - Use the /C option to assign the same colors to PrintCAD's pens.

         Plot spoolers  are not generally compatible with PrintCAD, and would
         be of little value if they were.  Print buffers/caches are generally
         compatible and useful. You must install the buffer first.

         If your prints are coming out not quite to scale:
         - For ADI plotters check that the plotter is set to 1016 steps/inch.
         - Check that no calibration is being done by the CAD package.
         - See /F - Output Format Option for print size correction.

       User Support ---------------------------------------------------------

         Correspondence  about  this  program  may be  sent  via the  support
         bulletin board, fax, Compuserve, Internet, or mail.

         BBS:        606-268-0577  1200..14400,N,8,1  24 hours/day

           To ask a  question prepare an  ASCII  text file with the  details.
           Call  the bulletin  board and choose the  upload question  option.
           XMODEM,  1K  XMODEM, or ZMODEM file transfer protocol is  required
           for this. Your question will be assigned a number (such as 1015) -
           remember  this number.  An answer  file (with the assigned number)
           will be posted, usually  within 24 hours on  weekdays.  To get the
           answer, call  the bulletin board, choose the download option, then
           the answer option, and then enter the answer number.

         Compuserve: Cary Ravitz [70431,32]

         Internet:   70431.32@compuserve.com

         Fax:        606-268-0577

           If  your fax machine does not send the fax calling signal, the BBS
           will  answer and  hang  up (about  30  seconds), then the  call is
           routed to the fax.

         Mail:       Ravitz Software Inc.
                     PO Box 25068
                     Lexington, KY  40524-5068
                     USA