MCS-51 Microcontroller Family Cross Assembler






             AAA     SSSSSS  EEEEEEE  MM   MM        5555555   11
            AA AA   SS       EE       MMM MMM        55       111
           AA   AA  SS       EE       MM M MM        55        11
           AA   AA   SSSSS   EEEEEEE  MM   MM  ====  555555    11
           AAAAAAA       SS  EE       MM   MM             55   11
           AA   AA       SS  EE       MM   MM             55   11
           AA   AA  SSSSSS   EEEEEEE  MM   MM        555555   1111









                         U S E R ' S    M A N U A L

                                Version  1.2




                              January 22, 1996

















                Copyright (c) 1994, 1996  by  W.W. Heinz




                          TABLE OF CONTENTS
                          -----------------


      Foreword to Version 1.0
      Foreword to Version 1.2

I.    Introduction

II.   Getting started

      II.1  Files
      II.2  ASEM-51 Installation
      II.3  Invoking ASEM
            II.3.1  DOS Command Line Operation
            II.3.2  Running ASEM-51 in the Borland-IDE
            II.3.3  Running ASEM-51 from Windows 3.1
            II.3.4  Running ASEM-51 from BRIEF
            II.3.5  Running ASEM-51 in a UNIX Environment
      II.4  The HEXBIN Utility
      II.5  The DEMO Program

III.  The ASEM-51 Assembly Language

      III.1  Statements
      III.2  Symbols
      III.3  Constants
      III.4  Expressions
      III.5  The 8051 Instruction Set
      III.6  Pseudo Instructions
      III.7  Segment Type
      III.8  Assembler Controls
             III.8.1  Primary Controls
             III.8.2  General Controls
      III.9  Predefined Symbols
      III.10 Conditional Assembly

IV.   Compatibility with the Intel Assembler

      IV.1  Restrictions
      IV.2  Extensions
      IV.3  Further Differences

V.    List File Format

VI.   Support of 8051 Derivatives

Appendix A:  ASEM-51 Error Messages
             A.1  Assembly Errors
             A.2  Runtime Errors
Appendix B:  HEXBIN Error Messages
             B.1  Conversion Errors
             B.2  Runtime Errors
Appendix C:  Predefined Symbols
Appendix D:  Reserved Keywords
Appendix E:  Specification of the Intel-HEX Format
Appendix F:  The ASCII Character Set
Appendix G:  Literature
Appendix H:  Trademarks
Appendix I:  8051 Instructions in numerical Order
Appendix J:  8051 Instructions in lexical Order



Foreword to Version 1.0
=======================

Today microcontrollers are used in a wide range of applications from simple
consumer electronic products to complex avionic components. Thus I was not
very surprised to find an 80C31 on the videotext decoder board, I purchased
some time ago. Since it had a poor user interface and many bugs, I thought
I could do it better and so I began to look for an 8051 cross assembler.
But in contrast to the huge number of hardware components sold, the number
of people developing microcontroller software seemed to be remarkable small,
and so was the number of development tools on the market.
There was a very small number of good professional cross assemblers for $250
and up - too expensive for hobby purposes. Aside of useless demos, there were
no restricted starter kits or school versions available.
I found also a few shareware and public domain assemblers. But either they
were poor and not very reliable, or not very 8051-specific, or they used some
kind of fantasy syntax that was 100 % compatible to itself, but far away from
the Intel standard. I didn't like them all!
There seems to be a general lack of useful and affordable microcontroller
development software. This is a pity, because their universality, simple
architectures and low prices make microcontrollers so interesting especially
for hobby and education.
So I decided to write a handy 8051 cross assembler for the PC.

And here it is:             ASEM-51 V1.0

I hope it will help to discover the wonderful world of microcontrollers.

Have fun!


                                        Deisenhofen,  July 19, 1994

                                                         W.W. Heinz



Foreword to Version 1.2
=======================

More than one year has passed, since I had released ASEM-51 V1.1 in
October 1994. Although I didn't spend all the time on ASEM-51, V1.2
comes with several extensions, bug fixes, and numerous functional or
internal improvements!
Highlights of the new version are a nearly perfectly featured list
file with cross-reference and some new printing options, a bootstrap
program for MCS-51 evaluation boards, and plenty of new *.MCU files.
For detailed information see the ASEM-51 V1.2 Release Notes.

What I have learned through the last two years is that freeware is
not free, neither for the author nor for the users.
ASEM-51 could not be made with nothing but numberless free hours,
spent on pure software development. I also had to purchase a PASCAL
development system, lots of microcontroller literature, and an 80C535
evaluation board.
The distribution of freeware seems to be a bigger problem than its
development. First of all, one has to buy a modem. After that, it
costs a lot of time, fees, trouble, and "interesting" discussions
with the particular sysops, until the stuff is posted (or not) on
several BBS and ftp sites.
To publish a program on shareware CD-ROMs, one has only to find out,
which are the most suitable. For this, it is best to buy a dozen or
two (and a CD-ROM drive), and to send the software to the publishers
of those that seem to be the most popular.
The interested users finally have to purchase modems or CD-ROM drives,
and pay the same fees, or buy the same CD-ROMs, to get the "freeware"
again from these public sources.
After all, it may be cheaper, faster, and more convenient, to simply buy
a professional software solution (if any) in the PC shop at the corner.
But it's not half the fun!

ASEM-51 V1.1 had been distributed (and mirrored) to more than 60 ftp
sites all over the world, uploaded to so many BBS, and published on
at least two shareware CD-ROMs.
But I only received mails from 9 users, a local cockroach, and an
international monster. The latter two asked me for permission, to
sell ASEM-51 for (their) profit, and failed miserably.
Most of the user mails started with "I have copied your assembler
from an ftp site, which I don't remember. It is looking fine on the
first glance! By the way, have you got a data sheet of the 80Cxyz?",
or something like that.
During all the time, I have received one single error report only.
Since it had been reported by phone, I couldn't reproduce it.
Nevertheless two serious bugs have been fixed since version 1.1, but
I have found them by myself in November 1995 both.
Sure ASEM-51 is no mainstream software, but to be honest, I am a
little disappointed of the poor user feedback!

Finally, I should thank the persons, who helped me to release ASEM-51:
Andreas Kies has tested all previous beta versions of the assembler. He
has distributed the first releases, and maintained a free ASEM-51 support
account right from the beginning.
Gabriele Novak has checked the orthography of all the documentation files.
Werner Allinger has tested the latest beta version and the bootstrap program.
Last but not least, I want to thank all interested users for their comments
and suggestions.
                                     Deisenhofen,  January 22, 1996

                                                         W.W. Heinz


I. Introduction
===============
ASEM-51 is a generic two-pass cross assembler for the MCS-51 microcontroller
family. It is running on IBM-PC/XT/AT computers and all true compatibles.
It only requires 256K of memory and MS-DOS 2.0 (or higher).
The ASEM-51 assembly language is a subset of the Intel standard that
guarantees maximum compatibility with existing 8051 assembler sources.
ASEM-51 generates an Intel-HEX file output, which is directly accepted by
most EPROM blowers. Thus ASEM-51 is suitable for small and medium 8031/51-
based microcontroller projects in the non-profit area.
However, ASEM-51 has been designed to process also very large programs!
Its most important features are:

    - fast, compact, reliable, easy to use, and well-documented
    - easy installation, no configuration required
    - command line operation, batch and networking capability
    - support for easy integration into the popular Borland IDE
    - support for installation under Windows 3.1
    - Intel-compatible syntax
    - five location counters, one for each of the 8051 address spaces
    - built-in symbols for 8051 special function registers (can be disabled)
    - 8051 register bank support
    - assembly-time evaluation of arithmetic and logical expressions
    - segment type checking for instruction operands
    - automatic code optimization of generic jumps and calls
    - nested include file processing
    - nested conditional assembly
    - detailed assembler listing with symbol table or cross reference
    - further fancy printing facilities  ;-)
    - Intel-HEX file output
    - hex-to-binary conversion utility
    - direct support of more than thirty 8051 derivatives
    - support of user-defined 8051 derivatives
    - special support of the Philips 83C75x family
    - bootstrap program for testing on the MCS-51 target board
    - limited update service by the author

    - also running under OS/2 2.x and Warp     (in the DOS window)
    - also running under Windows 3.1 and 95    (in the DOS box)
    - also running under LINUX 1.1.12 and up   (with dosemu 0.52 and up)
    - YES, it runs with Novell DOS 7.

All executable programs of the ASEM-51 package have been developed with:

      Turbo-Pascal 7.01 for DOS (c) Borland International 1992



II. Getting started
===================


II.1 Files
----------
Your ASEM-51 distribution disk or archive should contain the following
groups of files:

1.)  ASEM_51.DOC          ASEM-51 User's Manual  (this file)
        ASEM.EXE          cross assembler
        ASEM.PIF          program information file for Windows 3.1
        ASEM.ICO          icon file for Windows 3.1
    ASEM2MSG.EXE          ASEM-51 message filter for Borland-IDE
    ASEM2MSG.PAS          Turbo-Pascal source of ASEM2MSG.EXE
      HEXBIN.EXE          hex-to-binary conversion utility
        DEMO.A51          a sample 8051 assembler program
           *.MCU          processor definition files of 8051 derivatives
                          (for a detailed list of MCU files see chapter
                           "VI. Support of 8051 Derivatives")

2.)   BOOT51.DOC          BOOT-51 user's manual
      BOOT51.A51          BOOT-51 assembler source (requires ASEM-51 V1.2)
    CUSTOMIZ.EXE          BOOT-51 customization utility
        BOOT.BAT          batch file for application program upload
        LOAD.BAT          called by BOOT.BAT only
       RESET.EXE          program to reset target system via PC printer port
       BLINK.A51          sample test program for BOOT-51

3.)  LICENSE.DOC          ASEM-51 License Agreement
     RELEASE.120          ASEM-51 V1.2 Release Notes
     UPDATES.DOC          ASEM-51 Updating Guide
    KILLASEM.BAT          deletes all files of the ASEM-51 package
     FILE_ID.DIZ          a brief description of the ASEM-51 archive

The first group contains all files directly associated with the assembler.
The second group contains all files directly associated with the bootstrap
program. The third group contains general support and documentation files
that apply to the whole package.


II.2 ASEM-51 Installation
-------------------------
In principle ASEM-51 doesn't require a fuzzy software installation or
configuration. In the simplest case you can copy all files of the package
to your working directory, and enjoy the benefits of true plug-and-play
compatibility!
On the other hand, an installation of ASEM-51 under MS-DOS is very simple:

  - Create a new directory on your harddisk, e.g. C:\ASEM51.

  - Copy all files of the ASEM-51 package into this directory.

  - Append it to your PATH statement in file AUTOEXEC.BAT, e.g.

        PATH C:\DOS;C:\UTIL;C:\ASEM51

  - Reboot your PC.



II.3 Invoking ASEM
------------------
ASEM-51 provides full support of DOS command line operation and batch
capability as the best commercial development tools.   :-)
Nevertheless, it can be integrated into foreign development environments,
if desired.


II.3.1 DOS Command Line Operation
---------------------------------
ASEM-51 is invoked by typing:

ASEM <source> [<hex> [<list>]] [/INCLUDES:p] [/DEFINE:s:v:t] [/COLUMNS]

where <source> is the 8051 assembler source, <hex> is the output file in
Intel-HEX format, and <list> is the assembler list file.
The parameters <hex> and <list> are optional. When omitted, the file names
are derived from the <source> name, but with extensions HEX and LST.
All file names may be specified without extensions. In these cases, the
assembler adds default extensions as shown below:

        file             extension
        --------------------------
        <source>         .A51
        <hex>            .HEX
        <list>           .LST

If you want a file name to have no extension, terminate it with a '.'!
Instead of file names you may also specify device names to redirect the
output to character I/O ports. Device names may be terminated with a ':'!
It is not checked, whether the device is existing or suitable for the task.
Although it is possible to read the source file from a character device
(e.g. CON:) instead of a file, this cannot be recommended: Since ASEM-51
is a two-pass assembler, it always reads the source file twice!

When the /INCLUDES option is used, the assembler searches the specified
path p for include files that cannot be found in the working directory.
p may be any number of directories separated by ';' characters.
The directories will be searched from left to right.

The /DEFINE option is useful for selecting particular program variants
from the command line that have been implemented with conditional assembly.
It allows to define a symbol s with value v and segment type t in the
command line. v and t are optional. The segment type of the symbol defaults
to NUMBER, if t is omitted. The symbol value will be 0, if v is omitted.
v may be any numeric constant. t must be one of the following characters:

             C   =   CODE
             D   =   DATA
             I   =   IDATA
             X   =   XDATA
             B   =   BIT
             N   =   NUMBER    (default)

Options may be abbreviated as long as they remain unique!

Examples:

  1.)      ASEM PROGRAM

     will assemble the 8051 assembly language program PROGRAM.A51 and
     produce an Intel-HEX file PROGRAM.HEX and a listing PROGRAM.LST.

  2.)      ASEM TARZAN.ASM JANE JUNGLE.PRN

     will assemble the 8051 assembly language program TARZAN.ASM and
     produce an Intel-HEX file JANE.HEX and a listing JUNGLE.PRN.

  3.)      ASEM PROJECT EPROM.

     will assemble the 8051 assembly language program PROJECT.A51 and
     produce an Intel-HEX file EPROM and a listing PROJECT.LST.

  4.)      ASEM sample COM2: NUL

     will assemble the 8051 assembly language program SAMPLE.A51, send
     the HEX file output to the serial interface COM2 and suppress the
     list file output by sending it to the NUL device.

  5.)      ASEM APPLICAT /INC:C:\ASEM51;D:\MICROS\8051\HEADERS

     will assemble the program APPLICAT.A51, while all required include
     files will be searched first in the default directory, then in
     C:\ASEM51, and finally in D:\MICROS\8051\HEADERS.

  6.)      ASEM UNIVERSL /D:Eva_Board:8000H:C

     will assemble the program UNIVERSL.A51, while the CODE symbol
     EVA_BOARD will be predefined with value 8000H during assembly.

When program errors are detected, they are flagged on the console. This
may look as follows:


        MCS-51 Family Cross Assembler ASEM-51 V1.2

        APPLICAT.A51(14): must be known on first pass
        USERBITS.INC(6): attempt to divide by zero
        DEFINES.INC(37): symbol not defined
        APPLICAT.A51(20): symbol not defined
        APPLICAT.A51(27): no END statement found

             5 errors detected


Every error is flagged with the name of the source or include file, the
local line number where it was found, and the error message itself.
This output format makes it easy to integrate ASEM-51 into existing foreign
development environments or workbenches.
A perfect fit for the Turbo C++ IDE (and perhaps others) can be reached
with the /COLUMNS option. When specified, the column numbers of program
errors are output additionally after the line numbers:


        MCS-51 Family Cross Assembler ASEM-51 V1.2

        APPLICAT.A51(14,12): must be known on first pass
        USERBITS.INC(6,27): attempt to divide by zero
        DEFINES.INC(37,18): symbol not defined
        APPLICAT.A51(20,18): symbol not defined
        APPLICAT.A51(27,1): no END statement found

             5 errors detected


When terminating ASEM-51 returns an exit code to the operating system:

     situation                           ERRORLEVEL
     ----------------------------------------------
     no errors                               0
     program errors detected                 1
     fatal runtime error                     2


II.3.2 Running ASEM-51 in the Borland-IDE
-----------------------------------------
Turbo C++ (1.0 thru 3.0) users will appreciate the possibility to invoke
ASEM-51 as a transfer program from the Borland IDE.
For this, the filter program ASEM2MSG for the ASEM-51 error messages
has been provided. To integrate ASEM-51 into the Borland IDE, perform
the following steps:

  - Be sure that ASEM-51 has been installed properly as described before,
    or that ASEM.EXE and ASEM2MSG.EXE are somewhere in your PATH.

  - Start the Turbo C++ (or Borland C++) IDE for DOS.

  - For Turbo C++ 1.0, first click:  Options | Full menus | ON

  - Click from the menu bar:         Options | Transfer

  - When the "Transfer" dialog box is active, press the Edit button.

  - Now the "Modify/New Transfer Item" dialog box should be active.
    Fill in the following items:

         Program Title:   ASEM-~51
         Program Path:    ASEM
         Command Line:    $NOSWAP $SAVE CUR $CAP MSG(ASEM2MSG) $EDNAME /C
         Translator:      [X]
         Hot key:         Shift F8

    Then press the New button.

  - When returned to the "Transfer" dialog box, press the OK button.

  - Click from the menu bar:         Options | Save | OK

Now it should be possible, to assemble the file in the active edit
window with ASEM-51, when pressing Shift-F8. The error messages (if any)
should appear in the "Message" window. You can browse through the errors,
and jump into the source text by simply pressing <Enter>. This even works,
if the error is not in the program itself, but in an include file!

Turbo-Pascal 7.0 users can also employ their Borland IDE for assembly.
To integrate ASEM-51 into the Turbo-Pascal IDE, perform the following
steps:

  - Be sure that ASEM-51 has been installed properly as described before,
    or that ASEM.EXE and ASEM2MSG.EXE are somewhere in your PATH.

  - Start the Turbo-Pascal 7.0 (or Borland-Pascal 7.0) IDE for DOS.

  - Click from the menu bar:         Options | Tools

  - When the "Tools" dialog box is active, press the New button.

  - Now the "Modify/New Tool" dialog box should be active.
    Fill in the following items:

         Title:           ASEM-~5~1
         Program path:    ASEM
         Command line:    $NOSWAP $SAVE CUR $CAP MSG(ASEM2MSG) $EDNAME
         Hot keys:        Shift+F8

    Then press the OK button.

  - When returned to the "Tools" dialog box, press the OK button.

  - Click from the menu bar:         Options | Environment | Preferences

  - When the "Preferences" dialog box is active, disable the "Close on
    go to source" item in the "Options" checkbox. Then press the OK button.

  - Finally click from the menu bar: Options | Save

Now ASEM-51 can be invoked with Shift F8, to assemble the program in the
active edit window, while error messages (if any) appear in the "Messages"
window.

Users of both Turbo C++ and Turbo-Pascal should prefer the Turbo C++ IDE.
In the Turbo-Pascal 7.0 IDE, the /COLUMNS (or /C) option has no effect!


II.3.3 Running ASEM-51 from Windows 3.1
---------------------------------------
For integration into the Windows 3.1 desktop, the files ASEM.PIF and
ASEM.ICO have been provided. To insert ASEM-51 into a group of the
Program Manager, perform the following steps:

  - Be sure that ASEM-51 has been installed properly for MS-DOS
    as described before.

  - Start Windows 3.1 and expand the Program Manager window to its
    full screen size representation, if necessary.

  - Focus the program group in which ASEM-51 is to be inserted,
    e.g. "Applications".

  - Click from the Program Manager menu bar:   File | New

  - When the "New Program Object" dialog box is active, choose
    the option "program", and click the OK button.

  - Now the "Program Properties" dialog box should be active.
    Fill in the following items:

         Description:          ASEM-51
         Command line:         ASEM.PIF
         Working Directory:                  (whatever you want)
         Hot key:                            (whatever you want)
         as a Symbol:          [ ]

    Then press the [Change Icon] button.

  - Now a message box appears with the error message
    "no icon available for the specified file".
    Simply press the OK button.

  - The "Select Icon" dialog box should be displayed now. Fill in

         File Name:      ASEM.ICO

    and press the OK button. Now the ASEM-51 icon should be displayed
    in the icon field. Press the OK button again.

  - When returned to the "Program Properties" dialog box, press the
    OK button.

(Since I had no English Windows version to try this, things may look
 slightly different in real life.)

Now ASEM-51 can be invoked by simply clicking the ASEM-51 icon twice.
After entering the program parameters in a corresponding dialog box,
ASEM-51 is running in a DOS window, which remains open after program
termination, to let you have a look on the error messages.


II.3.4  Running ASEM-51 from BRIEF
----------------------------------
BRIEF 3.x users can integrate ASEM-51 into their editor by simply
defining another DOS environment variable in their AUTOEXEC.BAT with

         SET BCA51="ASEM %%s"

This specifies the command for compiling files with extension *.A51.
After that, ASEM-51 can be invoked from BRIEF with Alt-F10.


II.3.5  Running ASEM-51 in a UNIX Environment
---------------------------------------------
If you are running ASEM-51 on a Linux or another PC-based UNIX system
with an MS-DOS emulator, note that all executable programs of the ASEM-51
package can only read ASCII files in DOS format with CR/LF at the end of
line. Native UNIX text files with only a LF at the end of line cannot be
processed!
Consequently, all ASCII files, generated by programs of the ASEM-51
package, are written in MS-DOS format.



II.4 The HEXBIN Utility
-----------------------
Most EPROM blowers accept the Intel-HEX object file format that is output
by ASEM-51. However, for dumb EPROM blowers and special purposes it might be
useful to convert the HEX file to a pure binary image file.
For this the conversion utility HEXBIN is provided.
It is invoked as follows:

        HEXBIN <hex> [<bin>] [/OFFSET:o] [/LENGTH:l] [/FILL:f]

where <hex> is the input file in Intel-HEX format, and <bin> is the
binary output file. The parameter <bin> is optional. When omitted, the
file name is derived from the <hex> file name, but with the extension BIN.
All file names may be specified without extensions. In these cases, the
program adds default extensions as shown below:

        file             extension
        ------------------------------
        <hex>            .HEX
        <bin>            .BIN

If you want a file name to have no extension, terminate it with a '.'!
Instead of file names you may also specify device names to redirect the
output to character I/O ports. Device names may be terminated with a ':'!
It is not checked, whether the device is existing or suitable for the task.

The binary file output can also be controlled with the options /OFFSET,
/FILL and /LENGTH.
Normally the first byte in the binary file is the first byte of the HEX
record with the lowest load address. If a number of dummy bytes is to be
inserted on top of the file (e.g. for alignment in an EPROM image), this
can be performed with the /OFFSET option:

        /OFFSET:1000

would insert 4096 dummy bytes before the first byte of the first HEX record
loaded. The offset must always be specified as a hex number. The default
offset is 0.
Since there may be peepholes between the HEX records, a fill byte value can
be defined with the /FILL option:

        /FILL:0

would fill all peepholes between the HEX records with zero bytes as well as
all the dummy bytes that might have been inserted with the /OFFSET or /LENGTH
option. The fill byte value must always be specified as a hex number.
The default fill byte is the EPROM-friendly FFH.
By default the last byte in the binary file is the last byte of the HEX
record with the highest load address. If the binary file should have a
well defined length, then a number of dummy bytes can be appended to the
file (e.g. for exactly matching an EPROM length), this can be performed
with the /LENGTH option:

        /LENGTH:8000

would append as many dummy bytes behind the last byte of the file, that the
total file length becomes exactly 32768 bytes. The file length must always
be specified as a hex number.
Options may be abbreviated as long as they remain unique!

Examples:

  1.)      HEXBIN PROGRAM

     will convert the Intel-HEX file PROGRAM.HEX to a pure binary image file
     PROGRAM.BIN.

  2.)      HEXBIN TARZAN.OBJ JUNGLE/FILL:E5

     will convert the Intel-HEX file TARZAN.OBJ to a binary image file
     JUNGLE.BIN and fill all peepholes between the HEX file records with
     the binary value E5H.

  3.)      HEXBIN PROJECT EPROM. /off:8000 /length:10000 /f:0

     will convert the Intel-HEX file PROJECT.HEX to a binary image file
     EPROM, insert 32K dummy bytes on top of file, fill all peepholes
     and the dummy bytes with nulls, and extend the file to exactly 64K.

When terminating HEXBIN returns an exit code to the operating system:

     situation                           ERRORLEVEL
     ----------------------------------------------
     no errors                               0
     conversion errors detected              1
     fatal runtime error                     2


II.5 The DEMO Program
---------------------
For getting started with a new assembler, it is always good to have a
program, that can be assembled with it. For this purpose, the 8051
assembler program DEMO.A51 is provided, that can be used for a first
test of ASEM-51. Be sure to have all files of the ASEM-51 package on your
disk! Then simply type

        ASEM DEMO
        HEXBIN DEMO

at the DOS prompt. ASEM and HEXBIN should finish without errors and you
should have the following new files on your disk:

        DEMO.HEX          Intel-HEX file
        DEMO.LST          assembler list file of DEMO.A51
        DEMO.BIN          binary image file of DEMO.HEX

When something goes wrong, there may be files missing in your distribution!
DEMO.A51 may also serve as a sample assembler program that includes
examples for all machine instructions, pseudo instructions and assembler
controls, that have been implemented in ASEM-51. Whenever in doubt how to
use a particular command, DEMO.A51 may be a valuable help.



III.  The ASEM-51 Assembly Language
===================================
The user should be familiar with 8051 microcontrollers and assembly
language programming. This manual will not explain the architecture of
the MCS-51 microcontroller family nor will it discuss the basic concepts
of assembly language programming. It only describes the general syntax
of assembler statements and the assembler instructions that have been
implemented in ASEM-51.


III.1 Statements
----------------
Source files consist of a sequence of statements of one of the forms:

          [symbol:]  [instruction [arguments]]     [;comment]

           symbol     instruction  argument        [;comment]

          $control   [argument]                    [;comment]

Everything that is written in brackets is optional.
The maximum length of source code lines is 255 characters.
Everything from the ';' character to the end of line is assumed to be
commentary. Blank lines are considered to be commentary, too.
The lexical elements of a statement may be separated by blanks and tabs.
Aside of character string constants, upper and lower case letters are
equivalent.

Examples:     HERE:   MOV A,#0FFH     ;define label HERE and load A with FFH

                      YEAR EQU 1996   ;define symbol for current year

              $INCLUDE (80C517.MCU)   ;include SAB80C517 register definitions


III.2 Symbols
-------------
Symbols are user-defined names for addresses or numbers.
Their maximum significant length is 31 characters. They can be even
longer, but everything behind the first 31 characters is ignored.
Symbols may consist of letters, digits, '_' and '?' characters.
A symbol name must not start with a digit!
Upper and lower case letters are considered to be equivalent.
Note: Assembly language keywords must not be redefined as user symbols!

Example:     Is_this_really_a_SYMBOL_?       is a legal symbol name!



III.3 Constants
---------------
Numeric constants consist of a sequence of digits, followed by a radix
specifier. The first character must always be a decimal digit.
The legal digits and radix specifiers are:

          constant     digits        radix
          ------------------------------------
          binary       0 ... 1       B
          octal        0 ... 7       Q or O
          decimal      0 ... 9       D or none
          hex          0 ... F       H

Thus, for example, the following constants are equivalent:

          1111111B      binary
              177Q      octal
              177o      octal
               127      decimal
              127d      decimal
              07FH      hex

Character constants may be used wherever a numeric value is allowed.
A character constant consists of one or two printing characters enclosed
in single or double quotes. The quote character itself can be represented
by two subsequent quotes. For example:

               'X'       8 bit constant:       58H
              "a@"      16 bit constant:     6140H
              ''''       8 bit constant:       27H

In DB statements, character constants may have any length.
In this case, we call it a character string. For example:

              "It's only text!"



III.4 Expressions
-----------------
Arithmetic expressions are composed of operands, operators and parentheses.
Operands may be user-defined symbols, constants or special assembler symbols.
All operands are treated as unsigned 16-bit numbers.
Special assembler symbols, that can be used as operands are:

    AR0, ... , AR7     direct addresses of registers R0 thru R7

    $                  the location counter of the currently active segment
                       (start address of the current assembler statement)

The following operators are implemented:

Unary operators:   +          identity:             +x = x
                   -          two's complement:     -x = 0-x
                   NOT        one's complement:  NOT x = FFFFH-x
                   HIGH       high order byte
                   LOW        low order byte

Binary operators:  +          unsigned addition
                   -          unsigned subtraction
                   *          unsigned multiplication
                   /          unsigned division
                   MOD        unsigned remainder
                   SHL        logical shift left
                   SHR        logical shift right
                   AND        logical and
                   OR         logical or
                   XOR        exclusive or
                   .          bit operator used for bit-adressable locations
                   EQ  or =   equal to                ----.
                   NE  or <>  not equal to                |  results are:
                   LT  or <   less than                   |
                   LE  or <=  less or equal than          |     0 if FALSE
                   GT  or >   greater than                |  FFFF if TRUE
                   GE  or >=  greater or equal than   ____|

Operators that are no special characters but keywords as SHR or AND must
be separated from their operands by at least one blank or tab.
In general expressions are evaluated from left to right according to
operator precedence, which may be overridden by parentheses.
Parentheses may be nested to any level.
Expressions always evaluate to unsigned 16-bit numbers, while overflows
are ignored. When an expression result is to be assigned to an 8-bit
quantity, the high byte must be either 00 or FF.

      Operator precedence:
      -----------------------------------------------------------------
      ( )                                                   ^   highest
      + - NOT HIGH LOW                       (unary)        |
      .                                                     |
      * / MOD                                               |
      SHL SHR                                               |
      + -                                    (binary)       |
      EQ = NE <> LT < LE <= GT > GE >=                      |
      AND                                                   |
      OR XOR                                                v   lowest
      -----------------------------------------------------------------

Example:  The expression  P1.((87+3)/10 AND -1 SHR 0DH)  will evaluate to 91H.



III.5 The 8051 Instruction Set
------------------------------
ASEM-51 implements all 8051 machine instructions including generic jumps
and calls. The assembler implements two instructions

        JMP  <address>
        CALL <address>

that do not represent a specific opcode: generic jump and call.
These instructions will always evaluate to a jump or call, not necessarily
the shortest, that will reach the specified address.
JMP may assemble to SJMP, AJMP or LJMP, while CALL can only evaluate to
ACALL or LCALL. Note that the assembler decision may not be optimal. For
code addresses that are forward references, the assembler always generates
LJMP or LCALL respectively. However, for backward references this is a
powerful tool to reduce code size without extra trouble.

With the $PHILIPS control, ASEM-51 can be switched to the reduced instruction
set of the Philips 83C75x family of microcontrollers. This disables the LJMP,
LCALL, and MOVX instructions as well as the XDATA and XSEG pseudo instructions,
and generic jumps and calls will always assemble to absolute addressing.

The rest of the 8051 instruction mnemonics is listed in Appendix D.
Appendices I and J are containing tables of all 8051 instructions with
their opcodes, mnemonics, arguments, lengths, affected flags and durations.
The comprehensive example program DEMO.A51 provided shows all the 8051
instructions in a syntactical context.
All 8051 instruction mnemonics are copyright (c) by Intel corporation!



III.6 Pseudo Instructions
-------------------------
In the subsequent paragraphs, all ASEM-51 pseudo instructions are described.
Lexical symbols are written in lower case letters, while assembler keywords
are written in upper case.
Instruction arguments are represented by <arg>, <arg1> or something like
that. Expressions are represented by <expr>, <expr1> and so on.
Syntax elements enclosed in brackets are optional.
The ellipsis "..." means always "a list with any number of elements".


DB <arg1> [,<arg2> [,<arg3> ... ]]              define bytes

        The DB instruction reserves and initializes a number of bytes with
        the values defined by the arguments. The arguments may either be
        expressions (which must evaluate to 8-bit values) or character
        strings of any length. DB is only allowed in the CODE segment!

        Example:   DB 11,'January',96,(3*7+12)/11


DW <expr1> [,<expr2> [,<expr3> ... ]]           define words

        The DW instruction reserves and initializes a number of words with
        the values defined by the arguments. Every argument may be an
        arbitrary expression and requires two bytes of space.
        DW is only allowed in the CODE segment!

        Example:   DW 0,0C800H,1996,4711


DS <expr>                                       define space

        Reserves a number of uninitialized bytes in the current segment.
        The value of <expr> must be known on pass 1!
        DS is allowed in every segment!

        Example:   DS 200H


DBIT <expr>                                     define bits

        Reserves a number of uninitialized bits.
        The value of <expr> must be known on pass 1!
        DBIT is only allowed in the BIT segment!

        Example:   DBIT 16


NAME <symbol>                                   define module name

        Defines a name for the program module. The module name must be a
        legal symbol. Only one NAME instruction is allowed in the program.
        Since the NAME instruction has been introduced for compatibility
        purposes only, the symbol is not currently used. It may be redefined
        in the subsequent program.


ORG <expr>                                      origin of segment

        Sets the location counter of the current segment to the value <expr>.
        Additional ORG statements may be used to generate program segments
        which will load at different locations.
        The value of <expr> must be known on pass 1!
        The default value of all location counters at program start is 0.

        Example:   ORG 08000H


USING <expr>                                    using register bank

        Sets the register bank used to <expr>, which must be in the range
        of 0...3. The USING instruction only affects the values of the
        special assembler symbols AR0, ... , AR7 representing the direct
        addresses of registers R0, ... , R7 in the current register bank.
        The value of <expr> must be known on pass 1!
        The default value for the register bank is 0.

        Example:   USING 1


END                                             end of program

        This must be the last statement in the source file. After the END
        statement only commentary and blank lines are allowed!

        Example:   END       ;end of program


<symbol> EQU <expr>                             define constant
<symbol> SET <expr>                             define variable

        The EQU instruction defines a symbolic constant of the type NUMBER.
        A symbol defined with EQU can never be changed!
        The SET instruction defines a symbolic value of the type NUMBER,
        that may be changed with subsequent SET statements.
        The value of <expr> must be known on pass 1!
        A symbol that has been SET, cannot be redefined with EQU!
        A symbol that has been EQU'd cannot be reSET!
        On pass 2, forward references to a SET symbol always evaluate
        to the last value, the symbol has been SET to on pass 1.

        Examples:   MAXMONTH  EQU 12
                    OCTOBER   EQU MAXMONTH-2

                    CHAPTER   SET  1
                    CHAPTER   SET  CHAPTER+1


<symbol> CODE  <expr>                           define ROM address
<symbol> DATA  <expr>                           define direct RAM address
<symbol> IDATA <expr>                           define indirect RAM address
<symbol> BIT   <expr>                           define bit address
<symbol> XDATA <expr>                           define external RAM address

        These instructions define symbolic addresses for the five 8051
        memory segments (address spaces). For DATA, IDATA and BIT type
        symbols, the value of <expr> must not exceed 0FFH!
        The value of <expr> must be known on pass 1!
        Once defined with one of the above instructions, the symbols cannot
        be redefined.

        Examples:   EPROM    CODE  08000H
                    STACK    DATA       7
                    V24BUF   IDATA   080H
                    REDLED   BIT     P1.5
                    SAMPLER  XDATA  0100H


CSEG [AT <expr>]                           switch to CODE  space [at address]
DSEG [AT <expr>]                           switch to DATA  space [at address]
ISEG [AT <expr>]                           switch to IDATA space [at address]
BSEG [AT <expr>]                           switch to BIT   space [at address]
XSEG [AT <expr>]                           switch to XDATA space [at address]

        These instructions switch to one of the five 8051 memory segments
        (address spaces) and optionally set the location counter of that
        segment to a particular address <expr>.
        When the construction "AT <expr>" is omitted, the location counter
        keeps its previous value.
        The value of <expr> must be known on pass 1!
        At program start the default segment is CODE and all the location
        counters are set to zero.

        Examples:   DSEG            ;switch to DATA segment

                    CSEG AT 8000h   ;switch to CODE segment at address 8000H

                    XSEG at 0       ;switch to XDATA segment at address 0



III.7 Segment Type
------------------
Every assembly time expression is assigned a segment type, depending on
its operands and operators. The segment type indicates the address space,
the expression result might belong to, if it were used as an address.
There are six possible segment types:

        CODE
        DATA
        IDATA
        XDATA
        BIT
        NUMBER    (typeless)

Most expression results have the segment type NUMBER. That means they are
assumed to be typeless. However, in some cases it may be useful to assign
a particular segment type!
The following six rules apply when the segment type is evaluated:

    1. Numerical constants are always typeless.
       Consequently their segment type is NUMBER.

    2. Symbols are assigned a segment type during definition. Symbols
       that are defined with EQU or SET have no segment type.
       Labels get the segment type of the currently active segment.

    3. The result of a unary operation (+, -, NOT, HIGH, LOW) will have
       the segment type of its operand.

    4. The results of all binary operations (except "+", "-" and ".") will
       have no segment type.

    5. If only one operand in a binary "+" or "-" operation has a segment
       type, then the result will have that segment type, too. In all other
       cases, the result will have no segment type.

    6. The result of the bit operation "." will always have the segment
       type BIT.

Examples:
---------       The following symbols have been defined in a program:

                OFFSET  EQU   16
                START   CODE  30H
                DOIT    CODE  0100H
                REDLED  BIT   P1.3
                VARIAB4 DATA  20H
                PORT    DATA  0C8H
                RELAY   EQU   5

    1.)  The expression  START+OFFSET+3  will have the segment type CODE.
    2.)  The expression  START+DOIT  will be typeless.
    3.)  The expression  DOIT-REDLED  will be typeless.
    4.)  The expression  2*VARIAB4  will be typeless.
    5.)  The expression  PORT.RELAY  will have the segment type BIT.

The segment type is checked, when expressions appear as addresses. When the
expression result is not typeless and does not have the segment type of the
corresponding segment, the instruction is flagged with an error message.
The only exceptions are the segment types DATA and IDATA, which are assumed
to be compatible in the address range of 0 to 7FH. Since ASEM-51 does only
support absolute segments, those addresses are really always pointing to the
same physical location in the internal memory.

Example:
--------

 Line  I  Addr  Code            Source

    1:          N        30             DSEG AT 030H     ;internal RAM
    2:      30  N        01     COUNT:  DS 1             ;counter variable
    3:
    4:                                  CSEG             ;ROM
    5:    0000  C2 30           START:  CLR COUNT
                                                 ^
                          @@@@@ segment type mismatch @@@@@

The CLR instruction is flagged with the error message "segment type mismatch"
in the assembler list file, because only a BIT type address is allowed here.
However, COUNT is a label with the segment type DATA!



III.8 Assembler Controls
------------------------
ASEM-51 implements a number of assembler controls that influence the
assembly process and list file generation. There are two groups of
controls: primary and general controls.
Primary controls can only be used at the beginning of the program and
remain in effect throughout the assembly. They may be preceded only
by control statements, blank and commentary lines. If the same primary
control is used multiple times with different parameters, the last one
counts.
General controls may be used everywhere in the program. They perform a
single action, or remain in effect until they are cancelled or changed by
a subsequent control statement.
Assembler controls may have a number or string type operand.
Number type operands are arithmetic expressions that must be known on pass 1.
String type operands are character strings which are enclosed in parentheses
instead of quotes. In analogy to quoted strings, no control characters
(including tabs) are allowed within these strings! The string delimiter ')'
can be represented by two subsequent ')' characters.
The subsequent paragraphs contain detailed explanations of the implemented
controls and their abbreviations:


Control        Type  Default    Abbreviation            Meaning
------------------------------------------------------------------------------
$DATE(string)    P      ''      $DA      inserts date string into page header
------------------------------------------------------------------------------
$DEBUG           P   $NODEBUG   $DB      (currently dummy)
$NODEBUG         P              $NODB    (   "        "  )
------------------------------------------------------------------------------
$EJECT           G              $EJ      start a new page in list file
------------------------------------------------------------------------------
$INCLUDE(file)   G              $IC      include a source file
------------------------------------------------------------------------------
$LIST            G   $LIST      $LI      list subsequent source lines
$NOLIST          G              $NOLI    don't list subsequent source lines
------------------------------------------------------------------------------
$MOD51           P   $MOD51     $MO      enable predefined SFR symbols
$NOMOD51         P              $NOMO    disable predefined SFR symbols
------------------------------------------------------------------------------
$PAGING          P   $PAGING    $PI      enable listing page formatting
$NOPAGING        P              $NOPI    disable listing page formatting
------------------------------------------------------------------------------
$PAGELENGTH(n)   P   n=64       $PL      set lines per page for listing
------------------------------------------------------------------------------
$PAGEWIDTH(n)    P   n=132      $PW      set columns per line for listing
------------------------------------------------------------------------------
$PHILIPS         P   MCS-51     ---      switch on 83C75x family support
------------------------------------------------------------------------------
$SYMBOLS         P   $SYMBOLS   $SB      create symbol table
$NOSYMBOLS       P              $NOSB    don't create symbol table
------------------------------------------------------------------------------
$NOTABS          P   use tabs   ---      don't use tabs in list file
------------------------------------------------------------------------------
$TITLE(string)   G   copyright  $TT      inserts title string into page header
------------------------------------------------------------------------------
$XREF            P   $NOXREF    $XR      create cross reference
$NOXREF          P              $NOXR    don't create cross reference



III.8.1 Primary Controls
------------------------

$DATE (string)    Inserts a date string into the list file page header.
                  If $DATE() is specified, the actual date is inserted.
                  Date strings will be truncated to a maximum length of
                  11 characters.
                  Default is: no date string.
                  The control has no effect, when the $NOPAGING control has
                  been specified.

$DEBUG            Dummy. (For compatibility purposes only!)

$NODEBUG          Dummy. (For compatibility purposes only!)

$MOD51            Switches on the built-in 8051 special function register
                  and interrupt symbol definitions. (Default!)

$NOMOD51          Switches off the built-in 8051 special function register
                  and interrupt symbol definitions.

$PAGING           Switches on the page formatting in the list file.
                  (Default!)

$NOPAGING         Switches off the page formatting in the list file.

$PAGELENGTH (n)   Sets the list file page length to n lines.
                  (12 <= n <= 65535)
                  Default is n=64.
                  The control has no effect, when the $NOPAGING control has
                  been specified.

$PAGEWIDTH (n)    Sets the list file page width to n columns.
                  (72 <= n <= 255)
                  Default is n=132.

$PHILIPS          Switches on the Philips 83C75x family support option.
                  This disables the LJMP, LCALL, and MOVX instructions as
                  well as the XDATA and XSEG pseudo instructions. Generic
                  jumps and calls will always assemble to absolute addressing.

$SYMBOLS          Generates the symbol table at the end of the list file.
                  (Default!)
                  When the $XREF control is active, $SYMBOLS has no effect!

$NOSYMBOLS        Suppresses the symbol table at the end of the list file.
                  When the $XREF control is active, $NOSYMBOLS has no effect!

$NOTABS           Expands all tab characters in the list file output to
                  blanks.

$XREF             Generates a cross-reference listing instead of a symbol
                  table. Note that this slightly slows down assembly, and
                  consumes about 67 % more memory space!

$NOXREF           Generates a symbol table instead of a cross-reference
                  listing. (Default!)


Examples:   $NOMOD51              ;switch off 8051 SFR symbol definitions
            $PAGELENGTH(60)       ;set page length to 60 lines per page
            $PW(80)               ;set page width to 80 characters per line
            $NOSYMBOLS            ;no symbol table required
            $NOTABS               ;printer doesn't support tab characters
            $DATE(2. 8. 95)       ;date of latest version
            $XREF                 ;generate a cross-reference listing


III.8.2 General Controls
------------------------

$EJECT            Starts a new page in the list file.
                  The control has no effect, when the $NOPAGING control has
                  been specified.

$INCLUDE (file)   Includes an external source file into the assembler program
                  just behind the $INCLUDE statement. If the include file
                  cannot be found in the default directory, the include file
                  path, specified with the /INCLUDES command line option, is
                  searched. Include files may also be nested.

$NOLIST           After this control statement source code lines are no longer
                  listed, provided they do not contain errors, until the next
$LIST             statement occurs.

$TITLE (string)   Inserts a title string into the list file page header.
                  Titles may be truncated according to the specified (or
                  default) page width.
                  Default: ASEM-51 copyright information.
                  The control has no effect, when the $NOPAGING control has
                  been specified.


Examples:   $NOLIST               ;switch off listing
            $INCLUDE (8052.MCU)   ;include 8052 SFR symbol definition file
            $LIST                 ;switch on listing
            $TITLE (Computer-Controlled Combustion Unit for Motorcycles)
            $EJ                   ;new page with new title


III.9 Predefined Symbols
------------------------
For easy access to the 8051 special function register and interrupt
addresses, ASEM-51 has a number of predefined (built-in) DATA, BIT and
CODE symbols.
These predefined symbols can be switched off with the $NOMOD51 control.
For detailed information on symbols and addresses refer to Appendix C.



III.10 Conditional Assembly
---------------------------
To support easy configuration control and maintenance of 8051 application
programs, the following fife meta instructions have been implemented for
conditional assembly:

       IF     <expr>
       IFDEF  <symbol>
       IFNDEF <symbol>
       ELSE
       ENDIF

For the IF statement, conditional assembly works as follows:
When the expression <expr> in the IF statement is not equal to 0 (TRUE),
then the statements 1 to n are assembled and the statements n+1 to n+m
are ignored.

      IF <expr>
        <statement 1>
        <statement 2>       ;assembled when <expr> is TRUE
            .
            .
        <statement n>
      ELSE
        <statement n+1>
        <statement n+2>     ;assembled when <expr> is FALSE
            .
            .
        <statement n+m>
      ENDIF

Should <expr> be equal to 0 (FALSE), it is exactly vice versa! That means
the statements 1 to n are ignored and the statements n+1 to n+m are
assembled.
This works also, when the IF or ELSE branches contain no statements at all.
When the ELSE branch doesn't enclose any statements, the whole construction
can be simplified to a special case:

      IF <expr>
        <statement 1>
        <statement 2>       ;assembled when <expr> is TRUE
            .
            .
        <statement n>
      ENDIF

Then the statements 1 to n are assembled, if <expr> is not equal to 0,
otherwise they are ignored.
The value of <expr> must be known on pass 1!

Example:     TARGET EQU 0    ;configuration:  1 for application board
                             ;--------------  0 for evaluation board
             IF TARGET
               ORG 0         ;program start address of application board
             ELSE
               ORG 08000H    ;program start address of evaluation board
             ENDIF

The IFDEF and IFNDEF statements are working quite similar:

             IFDEF <symbol>
               .
             ELSE
               .
             ENDIF

When the <symbol> is defined in the program, the statements in the IFDEF
branch are assembled, and those in the ELSE branch (if any) are ignored.
When the <symbol> is not defined in the program, it is exactly vice versa!

             IFNDEF <symbol>
               .
             ELSE
               .
             ENDIF

When the <symbol> is defined in the program, the statements in the IFNDEF
branch are ignored, and those in the ELSE branch (if any) are assembled.
When the <symbol> is not defined in the program, it is vice versa!

Example:    ;EVA_537 EQU 0      ;symbol undefined: 80C537 application board
                                ;symbol defined:   80C537 evaluation board
             IFNDEF EVA_537
               CLOCK EQU 16     ;clock frequency of application board
               CSEG  AT  0      ;program start address of application board
             ELSE
               CLOCK EQU 12     ;clock frequency of evaluation board
               CSEG  AT  08000H ;program start address of evaluation board
             ENDIF

        Currently the program is configured for the application board version.

The <symbol> operands of the IFDEF and IFNDEF instructions must be either
undefined or defined on pass 1!

IF/IFDEF/IFNDEF...ELSE...ENDIF constructions may be nested to any depth!



IV. Compatibility with the Intel Assembler
==========================================
The ASEM-51 assembly language is a subset of the Intel standard, that
guarantees maximum compatibility with existing 8051 assembler sources.
It implements all 8051 instruction mnemonics as well as a useful subset
of the Intel pseudo instructions and assembler controls.


IV.1 Restrictions
-----------------
Since ASEM-51 generates an Intel-HEX file output instead of relocatable
object modules, the whole source code of an 8051 application program has to
reside in one single file. Consequently all pseudo instructions, that deal
with relocatable segments or external symbols, have not been implemented:

        PUBLIC
        EXTRN
        SEGMENT
        RSEG

The SET command cannot redefine special assembler symbols (e.g. registers)!
Macros are not supported!
Up to now only the following assembler controls and their abbreviations have
been implemented:

         |  primary controls         abbrev. |  general controls    abbrev.
---------+-----------------------------------+-----------------------------
         |  $DATE (<string>)          $DA    |  $EJECT               $EJ
         |  $DEBUG                    $DB    |  $INCLUDE (<file>)    $IC
         |  $NODEBUG                  $NODB  |  $LIST                $LI
         |  $MOD51                    $MO    |  $NOLIST              $NOLI
Intel-   |  $NOMOD51                  $NOMO  |  $TITLE (<string>)    $TT
         |  $PAGING                   $PI    |
controls |  $NOPAGING                 $NOPI  |
         |  $SYMBOLS                  $SB    |
         |  $NOSYMBOLS                $NOSB  |
         |  $PAGELENGTH (<lines>)     $PL    |
         |  $PAGEWIDTH (<columns>)    $PW    |
---------+-----------------------------------+-----------------------------
ASEM-51  |  $NOTABS                   -----  |
controls |  $PHILIPS                  -----  |


IV.2 Extensions
---------------
Assembler controls need not start in column 1, but may be preceded by any
number of blanks and tabs. Primary controls may also be preceded by
$INCLUDE statements, provided the corresponding include files are only
containing other control statements.
Character strings may also be enclosed in double quotes.
The DATA symbol for the special function register PCON is predefined.
The bit operator '.' is allowed in all expressions, not only in those that
have to match the segment type BIT.
To support easy conditional assembly, the following fife meta instructions
have been implemented:

        IF     <expression>
        IFDEF  <symbol>
        IFNDEF <symbol>
        ELSE
        ENDIF


IV.3 Further Differences
------------------------
To make semantics unique, especially the precedence of unary operators in
expressions is slightly different. Furthermore, expressions with a bit
operation "." evaluate to a BIT type result, not to NUMBER. This is described
in detail in chapters "III.4 Expressions" and "III.7 Segment Type".
Except in DB instructions, the zero length string constant '' is illegal.
The $NOMOD51 control disables also the predefined CODE addresses.
The special assembler symbols AR0...AR7 are predefined for bank 0 before
the first USING statement occurs.



V. List File Format
===================
The ASEM-51 list file format has been designed to give the user as much
information about the generated code as possible.
Besides the source code listed, there are five basic layout structures
in the listing:

  - the page header
  - the file header
  - the line headings
  - the error diagnosis
  - the symbol table or cross-reference listing

Normally every page of the listing starts with a page header as shown below:


ASEM-51 V1.2              Copyright (c) 1996 by W.W. Heinz               PAGE 1


It identifies the assembler, contains the copyright information and shows the
actual page number at the right margin. After the page header, source lines
are output in the list file format. When the maximum number of lines per page
is reached, another page header is output after a form feed character. When
the printer used doesn't work with form feeds, the page header can be
suppressed with the $NOPAGING control. The number of lines per page can be
adjusted to the paper format with the $PAGELENGTH control. The width of the
page header (and all other lines) can be set with the $PAGEWIDTH control.

The file header appears only on the first page. It identifies the assembler,
lists all input and output files and marks the columns for the line headings.
A typical file header is looking as shown below:


       MCS-51 Family Cross Assembler   A S E M - 5 1   V 1.2
       =====================================================



        Source File:    DEMO.A51
        Object File:    DEMO.HEX
        List File:      DEMO.LST



 Line  I  Addr  Code            Source


Directly after the file header starts the listing of the source code lines.
Every source code line is preceded by a line heading. The line heading
consists of four columns: line number, include file level, line address,
and generated code.

The column "Line" contains the source file line number. It is not necessarily
the local line number within the particular source file, but a global line
number, that is counted over the main source and all include files.

The column "I" flags the level of include file nesting. In the main source,
this column is empty. The first include file gets level 1. If this include
file includes another include file, this one gets level 2, and so on.

The column "Addr" shows the start address of the listed line in the currently
active segment (8051 address space). All addresses are represented as hex
numbers. The addresses in the CODE and XDATA segments are four-digit numbers.
Addresses in all other segments are two-digit numbers. For lines that cannot
be assigned to a particular segment, the "Addr" field is left blank.

The "Code" column may contain up to four bytes of generated code, which is
sufficient for all 8051 instructions. The code is listed in hex byte
quantities starting from the left margin of the "Code" column.
However, the code generated for DB and DW instructions may be longer than
four bytes. In these cases, the source code line is followed by additional
line headings until the whole code of the line is listed.
The "Code" column does not always contain code, that consumes space in the
8051 CODE segment. In contrast to many other assemblers, ASEM-51 lists the
evaluation results of all expressions that may appear in pseudo instructions
or assembler controls. These values are listed in hex representation at the
right margin of the "Code" column. The segment type of those expressions is
flagged with one single character at the left margin of the "Code" column:

                        C         CODE
                        D         DATA
                        I         IDATA
                        X         XDATA
                        B         BIT
                        N         number

The "Source" column finally contains the original source code line.
A typical source code listing is looking as follows:


 Line  I  Addr  Code            Source

    1:                                  ;A sample List File Demo Program
    2:                                  ;-------------------------------
    3:                          $NOMOD51                 ;no 8051 SFR
    4:          N      004F     $PAGEWIDTH (79)          ;79 columns per line
    5:                          $NOTABS                  ;expand tabs
    6:          N        90             P1    DATA 090H  ;port 1 address
    7:          B        93             INPUT BIT  P1.3  ;pulse input
    8:
    9:          N      8000             ORG  08000H      ;set location counter
   10:    8000  80 20                   SJMP START       ;jump to start address
   11:
   12:    8002  01 07                   DB  1,7          ;define bytes
   13:    8004  00 02 00 0C             DW  2,12,9       ;define words
          8008  00 09
   14:    800A  63 6F 66 66             DB  'coffeeright (c) 1996',0    ;string
          800E  65 65 72 69
          8012  67 68 74 20
          8016  28 63 29 20
          801A  31 39 39 36
          801E  00
   15:    801F  N      0003             DS  3            ;define space
   16:
   17:    8022  75 30 00        START:  MOV COUNT,#0     ;reset counter
   18:    8025  30 93 FD        LLEVEL: JNB INPUT,LLEVEL ;wait for high
   19:    8028  20 93 FD        HLEVEL: JB  INPUT,HLEVEL ;wait for low
   20:    802B  05 30                   INC COUNT        ;count pulse
   21:    802D  80 F6                   JMP LLEVEL       ;next pulse
   22:
   23:          N        30             DSEG AT 030H     ;internal RAM
   24:      30  N        01     COUNT:  DS 1             ;counter variable
   25:
   26:                                  END


If an error is detected in a source line, its position is flagged with a ^
character as good as possible, and a comprehensive error message is inserted.
This is looking as shown below:


   17:    8022  75 30 00        START:  MOV COUNT,#0     ;reset counter
   18:    8025  30 93 FD        LLEVEL: JNB INPUT,LLEVEL ;wait for high
   19:    8028  20 93 00        HLEVEL: JB  INPUT,HLEUEL ;wait for low
                                                  ^
                          @@@@@ symbol not defined @@@@@

   20:    802B  05 30                   INC COUNT        ;count pulse
   21:    802D  80 F6                   JMP LLEVEL       ;next pulse


The error diagnosis at the end of program lists the register banks used,
and the total number of errors detected throughout the assembly:


                     register banks used:  0, 1, 3

                     187 errors detected


A register bank counts as "used", if the program had switched to that
bank with a USING instruction, or one of the special assembler symbols
AR0 ... AR7 has been used, while the bank was active. The message

                     register banks used:  ---

means, that no bank has been used explicitly, and that the program
code may, but need not, be register bank independent.

After the source code listing and error diagnosis, the symbol table or
cross-reference listing starts. By default, a symbol table is generated.
The symbol table lists all the symbols of a program in alphabetical order
with their symbol name, segment type, hex value and first definition line.
Predefined symbols are listed without a definition line number.
The symbol table listing can be suppressed with the $NOSYMBOLS control.
A typical symbol table listing is looking as shown below:


               L I S T   O F   S Y M B O L S
               =============================


SYMBOL                            TYPE     VALUE        LINE
------------------------------------------------------------
COUNT                             DATA        30          46
HLEVEL                            CODE      802E          35
INPUT                             BIT         93          12
LLEVEL                            CODE      802B          34
MY_PROGRAM                        MODULE                  14
P1                                DATA        90
QUANT                             NUMBER    0013          22
SP                                DATA        81
STACK                             IDATA       80          17
START                             CODE      8022          31
VOLTDC                            XDATA     D785          49


If the $XREF control is specified, a cross-reference listing is generated
instead of a symbol table. The corresponding cross-reference listing for
the above symbol table is looking as follows:


               C R O S S - R E F E R E N C E - L I S T I N G
               =============================================


SYMBOL                           TYPE     VALUE     DEFINED  REFERENCED
-------------------------------------------------------------------------------
COUNT                            DATA        30          46          32      39
                                                                     42      43
HLEVEL                           CODE      802E          35          35
INPUT                            BIT         93          12          34      35
LLEVEL                           CODE      802B          34          34      40
MY_PROGRAM                       MODULE                  14
P1                               DATA        90                      12
QUANT                            NUMBER    0007          22          43
                                 NUMBER    0013          37
SP                               DATA        81                      31
STACK                            IDATA       80          17          31
START                            CODE      8022          31          24
TRASH                            undef.    ----                      41
VOLTDC                           XDATA     D785          49          33


It lists all the symbols of the program in alphabetical order, with their
symbol name, all definitions including definition lines, segment types, and
numerical values. Furthermore, all symbol references are listed as well.
The SYMBOL column contains the symbol name, while the columns TYPE, VALUE,
and DEFINED may contain the segment types, numerical values, and definition
lines of one, more, or no symbol defintions.
Module names have the symbol type "MODULE", and symbols that have been
referenced but not defined, are flagged with "undef." in the TYPE column.
Starting from column REFERENCED up to the right margin, there is a number of
columns (depending on the page width), containing all line numbers of symbol
references (if any).
The cross-reference listing does not distinguish, whether multiple definitions
of, or references to a particular symbol are legal or not. For this, refer to
the error messages in the source listing.



VI. Support of 8051 Derivatives
===============================
Today a large number of 8051 derivatives is available that grows almost
monthly! They all use the same instruction set of the 8051 processor kernel,
but are different in peripheral components, to cover a wide range of
applications. The difference for the assembly language programmer is mainly
the varying set of special function registers and interrupt addresses.
It is always good practice to use the same SFR names in a microcontroller
application program that the manufacturer of the derivative used has defined.
For this the processor definition files *.MCU are provided. They all are
include files with the special function register definitions of a particular
8051 derivative. However, the predefined symbols of ASEM-51 must be switched
off prior to including the SFR definitions of another derivative as shown
below:
              $NOMOD51
              $INCLUDE (80C515.MCU)

This would switch off the predefined symbols of the 8051 and include the
register definitions of the 80C515 or 80C535 respectively.
Hence it is easy for the user to adapt ASEM-51 to a brandnew 8051 derivative!
All what he has to do is to write a corresponding include file with the SFR
definitions derived from the manufacturer's data sheet.
The name of every processor definition file is corresponding to the ROM
version of a particular derivative. Of course it also applies to the EPROM,
EEPROM, and ROM-less versions (if any) of that derivative.
By the way, the file 8051.MCU provided contains exactly the predefined
symbols of ASEM-51, because its internal symbol table has been generated
from it!
To switch ASEM-51 to the reduced instruction set of the Philips 83C75x
family of microcontrollers, the $PHILIPS control can be used.



Currently the following processor definition files are provided with ASEM-51:


      Name        Manufacturer    Versions
    ---------------------------------------------------------------------
      8051.MCU    Intel           8051, 8031, 8751BH
                  (and others)    8051AH, 8031AH, 8751H, 8051AHP, 8751H-8
                                  80C51BH, 80C31BH, 87C51, 80C51BHP
      8052.MCU    Intel           8052AH, 8032AH, 8752BH
                  SIEMENS         80513, 8352-5
     80C52.MCU    Intel           80C52, 80C32
    83C51F.MCU    Intel           83C51FA, 80C51FA, 87C51FA
                                  83C51FB, 87C51FB, 87C51FC
    83C152.MCU    Intel           80C152JA, 83C152JA, 80C152JB
                                  80C152JC, 83C152JC, 80C152JD
    83C452.MCU    Intel           83C452, 80C452
      8044.MCU    Intel           8044AH, 8344AH, 8744AH
     80512.MCU    SIEMENS         80512, 80532
     80515.MCU    SIEMENS         80515, 80535, 80515K, 83515-4
    80C515.MCU    SIEMENS         80C515, 80C535, 83C515H
   83C515A.MCU    SIEMENS         83C515A-5, 80C515A
    80C517.MCU    SIEMENS         80C517, 80C537
   83C517A.MCU    SIEMENS         83C517A-5, 80C517A
      C501.MCU    SIEMENS         C501-1R, C501-L
      C502.MCU    SIEMENS         C502-2R, C502-L
      C503.MCU    SIEMENS         C503-1R, C503-L
      C511.MCU    SIEMENS         C511, C511A
      C513.MCU    SIEMENS         C513, C513A, C513A-H
    83C451.MCU    Philips         83C451, 80C451, 87C451
    83C528.MCU    Philips         83C528, 80C528, 87C528, 83C524, 87C524
                                  83CE528, 80CE528, 89CE528
    83C550.MCU    Philips         83C550, 80C550, 87C550
    83C552.MCU    Philips         83C552, 80C552, 87C552
    83C562.MCU    Philips         83C562, 80C562
    83C652.MCU    Philips         83C652, 80C652, 87C652
                                  83C654, 87C654, 83CE654, 80CE654
    83C750.MCU    Philips         83C750, 87C750
    83C751.MCU    Philips         83C751, 87C751
    83C752.MCU    Philips         83C752, 87C752
    83C851.MCU    Philips         83C851, 80C851
    83C852.MCU    Philips         83C852
    80C521.MCU    AMD             80C521, 80C541, 87C521, 87C541, 80C321
    80C324.MCU    AMD             80C324
    83C154.MCU    OKI             83C154, 80C154, 85C154VS
    80C320.MCU    DALLAS          80C320, 87C320, 80C323, 87C323
  COM20051.MCU    SMC             COM20051
   89C1051.MCU    Atmel           89C1051, 89C2051



Appendix A
==========


ASEM-51 Error Messages
----------------------

A.1 Assembly Errors:
--------------------
Assembly errors apply to the consistency of the assembly language
program in syntax and semantics. If one of these errors is detected,
it is flagged in the list file, and program execution continues.
When assembly is finished, ASEM terminates with ERRORLEVEL 1:

address out of range                    The address of a jump or call
                                        instruction cannot be reached with
                                        the selected addressing mode.

attempt to divide by zero               During evaluation of an assembly time
                                        expression, the assembler has to
                                        divide by zero.

binary operator expected                In this position of an expression,
                                        only binary operators are allowed.

comma expected                          There should be a ',' character in
                                        the marked position.

commands after END statement            The END statement is followed by
                                        further assembler statements.

constant out of range                   A numerical constant is greater
                                        than 65535.

ENDIF statement expected                There are IF, IFDEF, or IFNDEF meta
                                        instructions, which are not terminated
                                        with an ENDIF instruction.

expression out of range                 The result of an expression is too
                                        big or too small for that purpose.

file name expected                      There should be a valid file name
                                        in this position.

illegal character                       A statement contains characters, which
                                        are not allowed in MCS-51 assembly
                                        language.

illegal constant                        There are syntax errors in a
                                        numeric constant.

illegal control statement               A statement is starting with an
                                        unknown keyword beginning with a $.

illegal operand                         In this position of an expression,
                                        a valid operand had been expected.

illegal operator                        An expression contains a special
                                        character or keyword instead of an
                                        arithmetical or logical operator,
                                        which is not allowed in that place.

illegal statement syntax                A statement contains a syntax element,
                                        which is not allowed in this context.

invalid base address                    A DATA address that is not bit-
                                        addressable has been used on the
                                        left side of a '.' operator.

invalid bit number                      A number greater than 7 has been
                                        used on the right side of a '.'
                                        operator.

invalid instruction                     The instruction has previously been
                                        disabled with the $PHILIPS control.

module name already defined             There are more than one NAME
                                        statements in the program.

must be known on first pass             The result of an expression must
                                        fully evaluate on pass 1 of assembly.

must be preceded by IF                  An ELSE or ENDIF meta instruction
                                        occurs without a preceding IF,
                                        IFDEF, or IFNDEF instruction.

no END statement found                  The program ends without an END
                                        statement.

not allowed in BIT segment              Instruction is not allowed in a
                                        BIT segment.

only allowed in BIT segment             Instruction is only allowed in a
                                        BIT segment.

only allowed in CODE segment            Instruction is only allowed in a
                                        CODE segment.

operand expected                        An instruction ends, before it is
                                        syntactically complete.

phase error                             On pass 2, a symbol value has evaluated
                                        to another value than on pass 1.
                                        This is a serious, internal assembler
                                        error, and should be reported to the
                                        author immediately!

preceded by non-control lines           A primary control occurs after
                                        statements that are no assembler
                                        controls.

segment limit exceeded                  The location counter exceeds the
                                        boundaries of the current segment.

segment type mismatch                   The segment type of an operand does
                                        not match the type of the instruction.

string exceeds end of line              A character string is not properly
                                        terminated with a quote.

symbol already defined                  Attempt to redefine a symbol, which
                                        is already defined.

symbol name expected                    There should be a valid symbol name
                                        in this position.

symbol not defined                      A symbol is referenced, which has
                                        never been defined.

too many closing parentheses            An expression contains more closing
                                        than opening parentheses.

too many opening parentheses            An expression contains more opening
                                        than closing parentheses.

too many operands                       An instruction contains more operands
                                        than expected.

unary operator expected                 In this position of an expression,
                                        only unary operators are allowed.


A.2 Runtime Errors:
-------------------
Runtime errors are operational errors, or I/O errors.
If one of these errors is detected, it is flagged on the console,
and ASEM is aborting with ERRORLEVEL 2:

access denied                 No priviledge for attempted operation.
disk full                     No more free disk space.
disk write protected          Attempt to write to a write-protected disk.
drive not ready               Disk drive is off, or no media mounted.
duplicate file name           Attempt to overwrite an input or output file.
fatal I/O error               General (unknown) disk or device I/O error.
file not found                Source or include file not found.
invalid argument              Option has an illegal argument value.
no input file                 There is no file name in the command line.
no parameters                 ASEM has been invoked without any parameters.
out of memory                 Heap overflow!
path not found                Disk or directory not found.
too many open files           No more free file handles.
too many parameters           More than three file names have been specified.
unknown option                Option is not implemented.



Appendix B
==========


HEXBIN Error Messages
---------------------

B.1 Conversion Errors:
----------------------
Conversion errors apply to the consistency of Intel-HEX file and
program options. If one of these errors is detected, it is flagged
on the console, and HEXBIN is aborting with ERRORLEVEL 1:

checksum error                        Checksum is not correct.
data after EOF record                 Type 0 records after type 1 record.
file length out of range              /LENGTH option makes file too large.
fill-byte out of range                /FILL option defines byte value > 255.
hex file format error                 Certainly no Intel-HEX file.
illegal hex digit                     Character is no valid hex digit.
illegal record type                   Record type is none of 0 or 1.
invalid record length                 Record length doesn't match the record.
multiple EOF records                  More than one type 1 record.
no data records found                 File doesn't contain any type 0 records.
no EOF record found                   File ends without a type 1 record.
offset out of range                   /OFFSET option makes file too large.
record exceeds FFFFH                  Address space wrap around in record.
record exceeds file length            /LENGTH option made file too short.


B.2 Runtime Errors:
-------------------
Runtime errors are operational errors, or I/O errors.
If one of these errors is detected, it is flagged on the console,
and HEXBIN is aborting with ERRORLEVEL 2:

access denied                 No priviledge for attempted operation.
disk full                     No more free disk space.
disk write protected          Attempt to write to a write-protected disk.
drive not ready               Disk drive is off, or no media mounted.
duplicate file name           Attempt to overwrite an input or output file.
fatal I/O error               General (unknown) disk or device I/O error.
file not found                Intel-HEX file not found.
invalid argument              Option has an illegal argument value.
no input file                 There is no file name in the command line.
no parameters                 HEXBIN has been invoked without any parameters.
path not found                Disk or directory not found.
too many open files           No more free file handles.
too many parameters           More than two file names have been specified.
unknown option                Option is not implemented.



Appendix C
==========


Predefined Symbols
------------------

                             DATA Addresses:
                             ---------------
        P0          080H                        P1          090H
        SP          081H                        SCON        098H
        DPL         082H                        SBUF        099H
        DPH         083H                        P2          0A0H
        PCON        087H                        IE          0A8H
        TCON        088H                        P3          0B0H
        TMOD        089H                        IP          0B8H
        TL0         08AH                        PSW         0D0H
        TL1         08BH                        ACC         0E0H
        TH0         08CH                        B           0F0H
        TH1         08DH


                             BIT Addresses:
                             --------------
        IT0         088H                        EA          0AFH
        IE0         089H                        RXD         0B0H
        IT1         08AH                        TXD         0B1H
        IE1         08BH                        INT0        0B2H
        TR0         08CH                        INT1        0B3H
        TF0         08DH                        T0          0B4H
        TR1         08EH                        T1          0B5H
        TF1         08FH                        WR          0B6H
        RI          098H                        RD          0B7H
        TI          099H                        PX0         0B8H
        RB8         09AH                        PT0         0B9H
        TB8         09BH                        PX1         0BAH
        REN         09CH                        PT1         0BBH
        SM2         09DH                        PS          0BCH
        SM1         09EH                        P           0D0H
        SM0         09FH                        OV          0D2H
        EX0         0A8H                        RS0         0D3H
        ET0         0A9H                        RS1         0D4H
        EX1         0AAH                        F0          0D5H
        ET1         0ABH                        AC          0D6H
        ES          0ACH                        CY          0D7H


                             CODE Addresses:
                             ---------------
        RESET      0000H                        EXTI1      0013H
        EXTI0      0003H                        TIMER1     001BH
        TIMER0     000BH                        SINT       0023H



Appendix D
==========


Reserved Keywords
-----------------

                      Special Assembler Symbols:
                      --------------------------
        $                                   location counter
        A                                   accumulator
        AB                                  A/B register pair
        AR0,AR1,AR2,AR3,AR4,AR5,AR6,AR7     direct register addresses
        C                                   carry flag
        DPTR                                data pointer
        PC                                  program counter
        R0, R1, R2, R3, R4, R5, R6, R7      registers


                      Instruction Mnemonics
                      ---------------------
        ACALL       DA          JNB         MUL         RR
        ADD         DEC         JNC         NOP         RRC
        ADDC        DIV         JNZ         ORL         SETB
        AJMP        DJNZ        JZ          POP         SJMP
        ANL         INC         LCALL       PUSH        SUBB
        CALL        JB          LJMP        RET         SWAP
        CJNE        JBC         MOV         RETI        XCH
        CLR         JC          MOVC        RL          XCHD
        CPL         JMP         MOVX        RLC         XRL


                      Pseudo Instructions
                      -------------------
        AT          DATA        DSEG        IDATA       SET
        BIT         DB          DW          ISEG        USING
        BSEG        DBIT        END         NAME        XDATA
        CODE        DS          EQU         ORG         XSEG
        CSEG

                      Operators
                      ---------
        AND         GT          LOW         NE          SHL
        EQ          HIGH        LT          NOT         SHR
        GE          LE          MOD         OR          XOR


                      Assembler Controls
                      ------------------
        $DA         $LI         $NOMO       $NOXREF     $SB
        $DATE       $LIST       $NOMOD51    $PAGING     $SYMBOLS
        $DEBUG      $MO         $NOPAGING   $PAGELENGTH $TITLE
        $DB         $MOD51      $NOPI       $PAGEWIDTH  $TT
        $EJ         $NODB       $NOSB       $PHILIPS    $XR
        $EJECT      $NODEBUG    $NOSYMBOLS  $PI         $XREF
        $IC         $NOLI       $NOTABS     $PL
        $INCLUDE    $NOLIST     $NOXR       $PW


                      Meta Instructions
                      -----------------
        ELSE        ENDIF       IF          IFDEF       IFNDEF


Appendix E
==========


Specification of the Intel-HEX Format
-------------------------------------
This object file format is supported by many cross assemblers, utilities,
and most EPROM blowers.
An Intel-HEX file is a 7-bit ASCII text file, that contains a sequence of
data records and an end record. Every record is a line of text that starts
with a colon and ends with CR and LF.
Data records contain up to 16 data bytes, a 16-bit load address, a record
type byte and an 8-bit checksum. All numbers are represented by upper case
ASCII-hex characters.

       DATA RECORD:

       Byte 1               colon (:)
            2 and 3         number of binary data bytes for this record
            4 and 5         load address for this record, high byte
            6 and 7         load address  "    "     "     low byte
            8 and 9         record type: 00  (data record)
           10 to  x         data bytes, two characters each
          x+1 to  x+2       checksum (two characters)
          x+3 to  x+4       CR and LF

       A typical data record looks like

                         :10E0000002E003E4F588758910F58DF58BD28E302A

The end record is the last line of the file.
In principle it is structured like a data record, but the number of data
bytes is 00, the record type is 01 and the load-address field is 0000.

       END RECORD:

       Byte 1               colon (:)
            2 and 3         00   (number of data bytes)
            4 and 5         00   (load address, high byte)
            6 and 7         00   (load address, low byte)
            8 and 9         record type: 01  (end record)
           10 and 11        checksum (two characters)
           12 and 13        CR and LF


       The typical END record looks like

                         :00000001FF

The checksum is the two's complement of the 8-bit sum, without carry, of
the byte count, the two load address bytes, the record type byte and all
data bytes.



Appendix F:
===========


The ASCII Character Set
-----------------------



         hex |   00   10   20   30   40   50   60   70
        -----+------------------------------------------
          0  |  NUL  DLE         0    @    P    `    p
          1  |  SOH  DC1    !    1    A    Q    a    q
          2  |  STX  DC2    "    2    B    R    b    r
          3  |  ETX  DC3    #    3    C    S    c    s
          4  |  EOT  DC4    $    4    D    T    d    t
          5  |  ENQ  NAK    %    5    E    U    e    u
          6  |  ACK  SYN    &    6    F    V    f    v
          7  |  BEL  ETB    '    7    G    W    g    w
          8  |   BS  CAN    (    8    H    X    h    x
          9  |   HT   EM    )    9    I    Y    i    y
          A  |   LF  SUB    *    :    J    Z    j    z
          B  |   VT  ESC    +    ;    K    [    k    {
          C  |   FF   FS    ,    <    L    \    l    |
          D  |   CR   GS    -    =    M    ]    m    }
          E  |   SO   RS    .    >    N    ^    n    ~
          F  |   SI   US    /    ?    O    _    o  DEL



Appendix G:
===========


Literature
----------
                                                             Ordering Number

Intel:        MCS-51 Macro Assembler User's Guide
              8-Bit Embedded Controllers 1990

SIEMENS:      SAB 80512/80532 User's Manual                B2-B3808-X-X-7600
              SAB 80515/80535 User's Manual                B2-B3976-X-X-7600
              SAB 80C515/80C535 Data Sheet
              SAB 80C515A/83C515A-5 Addendum             B158-H6613-X-X-7600
              SAB 80C515A/83C515A-5 Data Sheet           B158-H6605-X-X-7600
              SAB 80C517/80C537 User's Manual            B258-B6075-X-X-7600
              SAB 80C517A/83C517A-5 Addendum             B158-H6612-X-X-7600
              SAB 80C517A/83C517A-5 Data Sheet           B158-H6581-X-X-7600
              SIEMENS Microcontrollers Data Catalog      B158-H6569-X-X-7600
              SAB 80513/8352-5 Data Sheet                B158-B6245-X-X-7600
              SAB-C501 User's Manual                     B158-H6723-G1-X-7600
              SAB-C502 User's Manual                     B158-H6722-G1-X-7600
              SAB-C503 User's Manual                     B158-H6650-G1-X-7600
              Application Notes and User Manuals, CD     B193-H6900-X-X-7400

Philips:      PCB83C552 User's Manual
              PCB83C552, PCB80C552 Development Data
              8051-Based 8-Bit Microcontrollers - Data Handbook 1994

AMD:          Eight-Bit 80C51 Embedded Processors - Data Book 1990

OKI:          MSM80C154, MSM83C154 User's Manual
              Microcontroller Data Book, 5th Edition 1990

DALLAS:       High-Speed Micro User's Guide, V1.3 January 1994        011994
              DS80C320 High-Speed Micro, PRELIMINARY                  081793

Andreas Roth: Das MICROCONTROLLER Kochbuch, 1992, iWT     ISBN 3-88322-225-9



Appendix H:
===========


Trademarks
----------

ASEM-51 is a trademark of W.W. Heinz.
MCS-51 is a trademark of Intel Corporation.
Turbo-Pascal and Borland-Pascal are trademarks of Borland International, Inc.
Turbo C++ and Borland C++ are trademarks of Borland International, Inc.
IBM-PC, IBM-XT, IBM-AT and OS/2 are trademarks of IBM Corporation.
MS-DOS and Windows are trademarks of Microsoft Corporation.
Novell DOS is a trademark of Novell, Inc.
BRIEF is a trademark of SDC Partners II L.P.
All device codes of 8051 derivatives are trademarks of the manufacturers.
Other brand and product names are trademarks of their respective holders.



Appendix I:
===========


8051 Instructions in numerical Order
------------------------------------

Abbreviations:      direct   =   8-bit DATA address in internal memory
                    const8   =   8-bit constant in CODE memory
                    const16  =  16-bit constant in CODE memory
                    addr16   =  16-bit long CODE address
                    addr11   =  11-bit absolute CODE address
                    rel      =  signed 8-bit relative CODE address
                    bit      =   8-bit BIT address in internal memory


Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  00      NOP                           1                    1
  01      AJMP    addr11                2                    2
  02      LJMP    addr16                3                    2
  03      RR      A                     1                    1
  04      INC     A                     1              P     1
  05      INC     direct                2                    1
  06      INC     @R0                   1                    1
  07      INC     @R1                   1                    1
  08      INC     R0                    1                    1
  09      INC     R1                    1                    1
  0A      INC     R2                    1                    1
  0B      INC     R3                    1                    1
  0C      INC     R4                    1                    1
  0D      INC     R5                    1                    1
  0E      INC     R6                    1                    1
  0F      INC     R7                    1                    1
  10      JBC     bit, rel              3                    2
  11      ACALL   addr11                2                    2
  12      LCALL   addr16                3                    2
  13      RRC     A                     1     CY       P     1
  14      DEC     A                     1              P     1
  15      DEC     direct                2                    1
  16      DEC     @R0                   1                    1
  17      DEC     @R1                   1                    1
  18      DEC     R0                    1                    1
  19      DEC     R1                    1                    1
  1A      DEC     R2                    1                    1
  1B      DEC     R3                    1                    1
  1C      DEC     R4                    1                    1
  1D      DEC     R5                    1                    1
  1E      DEC     R6                    1                    1
  1F      DEC     R7                    1                    1
  20      JB      bit, rel              3                    2
  21      AJMP    addr11                2                    2
  22      RET                           1                    2
  23      RL      A                     1                    1
  24      ADD     A, #const8            2     CY AC OV P     1
  25      ADD     A, direct             2     CY AC OV P     1
  26      ADD     A, @R0                1     CY AC OV P     1
  27      ADD     A, @R1                1     CY AC OV P     1



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  28      ADD     A, R0                 1     CY AC OV P     1
  29      ADD     A, R1                 1     CY AC OV P     1
  2A      ADD     A, R2                 1     CY AC OV P     1
  2B      ADD     A, R3                 1     CY AC OV P     1
  2C      ADD     A, R4                 1     CY AC OV P     1
  2D      ADD     A, R5                 1     CY AC OV P     1
  2E      ADD     A, R6                 1     CY AC OV P     1
  2F      ADD     A, R7                 1     CY AC OV P     1
  30      JNB     bit, rel              3                    2
  31      ACALL   addr11                2                    2
  32      RETI                          1                    2
  33      RLC     A                     1     CY       P     1
  34      ADDC    A, #const8            2     CY AC OV P     1
  35      ADDC    A, direct             2     CY AC OV P     1
  36      ADDC    A, @R0                1     CY AC OV P     1
  37      ADDC    A, @R1                1     CY AC OV P     1
  38      ADDC    A, R0                 1     CY AC OV P     1
  39      ADDC    A, R1                 1     CY AC OV P     1
  3A      ADDC    A, R2                 1     CY AC OV P     1
  3B      ADDC    A, R3                 1     CY AC OV P     1
  3C      ADDC    A, R4                 1     CY AC OV P     1
  3D      ADDC    A, R5                 1     CY AC OV P     1
  3E      ADDC    A, R6                 1     CY AC OV P     1
  3F      ADDC    A, R7                 1     CY AC OV P     1
  40      JC      rel                   2                    2
  41      AJMP    addr11                2                    2
  42      ORL     direct, A             2                    1
  43      ORL     direct, #const8       3                    2
  44      ORL     A, #const8            2              P     1
  45      ORL     A, direct             2              P     1
  46      ORL     A, @R0                1              P     1
  47      ORL     A, @R1                1              P     1
  48      ORL     A, R0                 1              P     1
  49      ORL     A, R1                 1              P     1
  4A      ORL     A, R2                 1              P     1
  4B      ORL     A, R3                 1              P     1
  4C      ORL     A, R4                 1              P     1
  4D      ORL     A, R5                 1              P     1
  4E      ORL     A, R6                 1              P     1
  4F      ORL     A, R7                 1              P     1
  50      JNC     rel                   2                    2
  51      ACALL   addr11                2                    2
  52      ANL     direct, A             2                    1
  53      ANL     direct, #const8       3                    2
  54      ANL     A, #const8            2              P     1
  55      ANL     A, direct             2              P     1
  56      ANL     A, @R0                1              P     1
  57      ANL     A, @R1                1              P     1
  58      ANL     A, R0                 1              P     1
  59      ANL     A, R1                 1              P     1
  5A      ANL     A, R2                 1              P     1
  5B      ANL     A, R3                 1              P     1
  5C      ANL     A, R4                 1              P     1
  5D      ANL     A, R5                 1              P     1
  5E      ANL     A, R6                 1              P     1
  5F      ANL     A, R7                 1              P     1



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  60      JZ      rel                   2                    2
  61      AJMP    addr11                2                    2
  62      XRL     direct, A             2                    1
  63      XRL     direct, #const8       3                    2
  64      XRL     A, #const8            2              P     1
  65      XRL     A, direct             2              P     1
  66      XRL     A, @R0                1              P     1
  67      XRL     A, @R1                1              P     1
  68      XRL     A, R0                 1              P     1
  69      XRL     A, R1                 1              P     1
  6A      XRL     A, R2                 1              P     1
  6B      XRL     A, R3                 1              P     1
  6C      XRL     A, R4                 1              P     1
  6D      XRL     A, R5                 1              P     1
  6E      XRL     A, R6                 1              P     1
  6F      XRL     A, R7                 1              P     1
  70      JNZ     rel                   2                    2
  71      ACALL   addr11                2                    2
  72      ORL     C, bit                2     CY             2
  73      JMP     @A+DPTR               1                    2
  74      MOV     A, #const8            2              P     1
  75      MOV     direct, #const8       3                    2
  76      MOV     @R0, #const8          2                    1
  77      MOV     @R1, #const8          2                    1
  78      MOV     R0, #const8           2                    1
  79      MOV     R1, #const8           2                    1
  7A      MOV     R2, #const8           2                    1
  7B      MOV     R3, #const8           2                    1
  7C      MOV     R4, #const8           2                    1
  7D      MOV     R5, #const8           2                    1
  7E      MOV     R6, #const8           2                    1
  7F      MOV     R7, #const8           2                    1
  80      SJMP    rel                   2                    2
  81      AJMP    addr11                2                    2
  82      ANL     C, bit                2     CY             2
  83      MOVC    A, @A+PC              1              P     2
  84      DIV     AB                    1     CY    OV P     4
  85      MOV     direct, direct        3                    2
  86      MOV     direct, @R0           2                    2
  87      MOV     direct, @R1           2                    2
  88      MOV     direct, R0            2                    2
  89      MOV     direct, R1            2                    2
  8A      MOV     direct, R2            2                    2
  8B      MOV     direct, R3            2                    2
  8C      MOV     direct, R4            2                    2
  8D      MOV     direct, R5            2                    2
  8E      MOV     direct, R6            2                    2
  8F      MOV     direct, R7            2                    2
  90      MOV     DPTR, #const16        3                    2
  91      ACALL   addr11                2                    2
  92      MOV     bit, C                2                    2
  93      MOVC    A, @A+DPTR            1              P     2
  94      SUBB    A, #const8            2     CY AC OV P     1
  95      SUBB    A, direct             2     CY AC OV P     1
  96      SUBB    A, @R0                1     CY AC OV P     1
  97      SUBB    A, @R1                1     CY AC OV P     1



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  98      SUBB    A, R0                 1     CY AC OV P     1
  99      SUBB    A, R1                 1     CY AC OV P     1
  9A      SUBB    A, R2                 1     CY AC OV P     1
  9B      SUBB    A, R3                 1     CY AC OV P     1
  9C      SUBB    A, R4                 1     CY AC OV P     1
  9D      SUBB    A, R5                 1     CY AC OV P     1
  9E      SUBB    A, R6                 1     CY AC OV P     1
  9F      SUBB    A, R7                 1     CY AC OV P     1
  A0      ORL     C, /bit               2     CY             2
  A1      AJMP    addr11                2                    2
  A2      MOV     C, bit                2     CY             1
  A3      INC     DPTR                  1                    2
  A4      MUL     AB                    1     CY    OV P     4
  A5      illegal opcode
  A6      MOV     @R0, direct           2                    2
  A7      MOV     @R1, direct           2                    2
  A8      MOV     R0, direct            2                    2
  A9      MOV     R1, direct            2                    2
  AA      MOV     R2, direct            2                    2
  AB      MOV     R3, direct            2                    2
  AC      MOV     R4, direct            2                    2
  AD      MOV     R5, direct            2                    2
  AE      MOV     R6, direct            2                    2
  AF      MOV     R7, direct            2                    2
  B0      ANL     C, /bit               2     CY             2
  B1      ACALL   addr11                2                    2
  B2      CPL     bit                   2                    1
  B3      CPL     C                     1     CY             1
  B4      CJNE    A, #const8, rel       3     CY             2
  B5      CJNE    A, direct, rel        3     CY             2
  B6      CJNE    @R0, #const8, rel     3     CY             2
  B7      CJNE    @R1, #const8, rel     3     CY             2
  B8      CJNE    R0, #const8, rel      3     CY             2
  B9      CJNE    R1, #const8, rel      3     CY             2
  BA      CJNE    R2, #const8, rel      3     CY             2
  BB      CJNE    R3, #const8, rel      3     CY             2
  BC      CJNE    R4, #const8, rel      3     CY             2
  BD      CJNE    R5, #const8, rel      3     CY             2
  BE      CJNE    R6, #const8, rel      3     CY             2
  BF      CJNE    R7, #const8, rel      3     CY             2
  C0      PUSH    direct                2                    2
  C1      AJMP    addr11                2                    2
  C2      CLR     bit                   2                    1
  C3      CLR     C                     1     CY             1
  C4      SWAP    A                     1                    1
  C5      XCH     A, direct             2              P     1
  C6      XCH     A, @R0                1              P     1
  C7      XCH     A, @R1                1              P     1
  C8      XCH     A, R0                 1              P     1
  C9      XCH     A, R1                 1              P     1
  CA      XCH     A, R2                 1              P     1
  CB      XCH     A, R3                 1              P     1
  CC      XCH     A, R4                 1              P     1
  CD      XCH     A, R5                 1              P     1
  CE      XCH     A, R6                 1              P     1
  CF      XCH     A, R7                 1              P     1



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  D0      POP     direct                2                    2
  D1      ACALL   addr11                2                    2
  D2      SETB    bit                   2                    1
  D3      SETB    C                     1     CY             1
  D4      DA      A                     1     CY       P     1
  D5      DJNZ    direct, rel           3                    2
  D6      XCHD    A, @R0                1              P     1
  D7      XCHD    A, @R1                1              P     1
  D8      DJNZ    R0, rel               2                    2
  D9      DJNZ    R1, rel               2                    2
  DA      DJNZ    R2, rel               2                    2
  DB      DJNZ    R3, rel               2                    2
  DC      DJNZ    R4, rel               2                    2
  DD      DJNZ    R5, rel               2                    2
  DE      DJNZ    R6, rel               2                    2
  DF      DJNZ    R7, rel               2                    2
  E0      MOVX    A, @DPTR              1              P     2
  E1      AJMP    addr11                2                    2
  E2      MOVX    A, @R0                1              P     2
  E3      MOVX    A, @R1                1              P     2
  E4      CLR     A                     1              P     1
  E5      MOV     A, direct             2              P     1
  E6      MOV     A, @R0                1              P     1
  E7      MOV     A, @R1                1              P     1
  E8      MOV     A, R0                 1              P     1
  E9      MOV     A, R1                 1              P     1
  EA      MOV     A, R2                 1              P     1
  EB      MOV     A, R3                 1              P     1
  EC      MOV     A, R4                 1              P     1
  ED      MOV     A, R5                 1              P     1
  EE      MOV     A, R6                 1              P     1
  EF      MOV     A, R7                 1              P     1
  F0      MOVX    @DPTR, A              1                    2
  F1      ACALL   addr11                2                    2
  F2      MOVX    @R0, A                1                    2
  F3      MOVX    @R1, A                1                    2
  F4      CPL     A                     1              P     1
  F5      MOV     direct, A             2                    1
  F6      MOV     @R0, A                1                    1
  F7      MOV     @R1, A                1                    1
  F8      MOV     R0, A                 1                    1
  F9      MOV     R1, A                 1                    1
  FA      MOV     R2, A                 1                    1
  FB      MOV     R3, A                 1                    1
  FC      MOV     R4, A                 1                    1
  FD      MOV     R5, A                 1                    1
  FE      MOV     R6, A                 1                    1
  FF      MOV     R7, A                 1                    1



Appendix J:
===========


8051 Instructions in lexical Order
----------------------------------

Abbreviations:      direct   =   8-bit DATA address in internal memory
                    const8   =   8-bit constant in CODE memory
                    const16  =  16-bit constant in CODE memory
                    addr16   =  16-bit long CODE address
                    addr11   =  11-bit absolute CODE address
                    rel      =  signed 8-bit relative CODE address
                    bit      =   8-bit BIT address in internal memory

                    i  =  register numbers 0 or 1
                    n  =  register numbers 0 thru 7
                    a  =  32 * m
                    m  =  the 3 most significant bits of an absolute address


Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  11+a    ACALL   addr11                2                    2
  24      ADD     A, #const8            2     CY AC OV P     1
  26+i    ADD     A, @Ri                1     CY AC OV P     1
  25      ADD     A, direct             2     CY AC OV P     1
  28+n    ADD     A, Rn                 1     CY AC OV P     1
  34      ADDC    A, #const8            2     CY AC OV P     1
  36+i    ADDC    A, @Ri                1     CY AC OV P     1
  35      ADDC    A, direct             2     CY AC OV P     1
  38+n    ADDC    A, Rn                 1     CY AC OV P     1
  01+a    AJMP    addr11                2                    2
  54      ANL     A, #const8            2              P     1
  56+i    ANL     A, @Ri                1              P     1
  55      ANL     A, direct             2              P     1
  58+n    ANL     A, Rn                 1              P     1
  B0      ANL     C, /bit               2     CY             2
  82      ANL     C, bit                2     CY             2
  53      ANL     direct, #const8       3                    2
  52      ANL     direct, A             2                    1
  B6+i    CJNE    @Ri, #const8, rel     3     CY             2
  B4      CJNE    A, #const8, rel       3     CY             2
  B5      CJNE    A, direct, rel        3     CY             2
  B8+n    CJNE    Rn, #const8, rel      3     CY             2
  E4      CLR     A                     1              P     1
  C2      CLR     bit                   2                    1
  C3      CLR     C                     1     CY             1
  F4      CPL     A                     1              P     1
  B2      CPL     bit                   2                    1
  B3      CPL     C                     1     CY             1
  D4      DA      A                     1     CY       P     1
  16+i    DEC     @Ri                   1                    1
  14      DEC     A                     1              P     1
  15      DEC     direct                2                    1
  18+n    DEC     Rn                    1                    1
  84      DIV     AB                    1     CY    OV P     4
  D5      DJNZ    direct, rel           3                    2



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  D8+n    DJNZ    Rn, rel               2                    2
  06+i    INC     @Ri                   1                    1
  04      INC     A                     1              P     1
  05      INC     direct                2                    1
  A3      INC     DPTR                  1                    2
  08+n    INC     Rn                    1                    1
  20      JB      bit, rel              3                    2
  10      JBC     bit, rel              3                    2
  40      JC      rel                   2                    2
  73      JMP     @A+DPTR               1                    2
  30      JNB     bit, rel              3                    2
  50      JNC     rel                   2                    2
  70      JNZ     rel                   2                    2
  60      JZ      rel                   2                    2
  12      LCALL   addr16                3                    2
  02      LJMP    addr16                3                    2
  76+i    MOV     @Ri, #const8          2                    1
  F6+i    MOV     @Ri, A                1                    1
  A6+i    MOV     @Ri, direct           2                    2
  74      MOV     A, #const8            2              P     1
  E6+i    MOV     A, @Ri                1              P     1
  E5      MOV     A, direct             2              P     1
  E8+n    MOV     A, Rn                 1              P     1
  92      MOV     bit, C                2                    2
  A2      MOV     C, bit                2     CY             1
  75      MOV     direct, #const8       3                    2
  86+i    MOV     direct, @Ri           2                    2
  F5      MOV     direct, A             2                    1
  85      MOV     direct, direct        3                    2
  88+n    MOV     direct, Rn            2                    2
  90      MOV     DPTR, #const16        3                    2
  78+n    MOV     Rn, #const8           2                    1
  F8+n    MOV     Rn, A                 1                    1
  A8+n    MOV     Rn, direct            2                    2
  93      MOVC    A, @A+DPTR            1              P     2
  83      MOVC    A, @A+PC              1              P     2
  F0      MOVX    @DPTR, A              1                    2
  F2+i    MOVX    @Ri, A                1                    2
  E0      MOVX    A, @DPTR              1              P     2
  E2+i    MOVX    A, @Ri                1              P     2
  A4      MUL     AB                    1     CY    OV P     4
  00      NOP                           1                    1
  44      ORL     A, #const8            2              P     1
  46+i    ORL     A, @Ri                1              P     1
  45      ORL     A, direct             2              P     1
  48+n    ORL     A, Rn                 1              P     1
  A0      ORL     C, /bit               2     CY             2
  72      ORL     C, bit                2     CY             2
  43      ORL     direct, #const8       3                    2
  42      ORL     direct, A             2                    1
  D0      POP     direct                2                    2
  C0      PUSH    direct                2                    2
  22      RET                           1                    2
  32      RETI                          1                    2
  23      RL      A                     1                    1
  33      RLC     A                     1     CY       P     1



Opcode  Mnemonic  Operands            Bytes     Flags     Cycles
----------------------------------------------------------------
  03      RR      A                     1                    1
  13      RRC     A                     1     CY       P     1
  D2      SETB    bit                   2                    1
  D3      SETB    C                     1     CY             1
  80      SJMP    rel                   2                    2
  94      SUBB    A, #const8            2     CY AC OV P     1
  96+i    SUBB    A, @Ri                1     CY AC OV P     1
  95      SUBB    A, direct             2     CY AC OV P     1
  98+n    SUBB    A, Rn                 1     CY AC OV P     1
  C4      SWAP    A                     1                    1
  C6+i    XCH     A, @Ri                1              P     1
  C5      XCH     A, direct             2              P     1
  C8+n    XCH     A, Rn                 1              P     1
  D6+i    XCHD    A, @Ri                1              P     1
  64      XRL     A, #const8            2              P     1
  66+i    XRL     A, @Ri                1              P     1
  65      XRL     A, direct             2              P     1
  68+n    XRL     A, Rn                 1              P     1
  63      XRL     direct, #const8       3                    2
  62      XRL     direct, A             2                    1