MCS-51 Microcontroller Family Bootstrap Program






           BBBBBB    OOOOO    OOOOO  TTTTTTTT       5555555   11
           BB   BB  OO   OO  OO   OO    TT          55       111
           BB   BB  OO   OO  OO   OO    TT          55        11
           BBBBBB   OO   OO  OO   OO    TT    ====  555555    11
           BB   BB  OO   OO  OO   OO    TT               55   11
           BB   BB  OO   OO  OO   OO    TT               55   11
           BBBBBB    OOOOO    OOOOO     TT          555555   1111









                         U S E R ' S    M A N U A L

                                Version  1.0




                              January 20, 1996

















                   copyright (c) 1996  by  W.W. Heinz




                          TABLE OF CONTENTS
                          -----------------



I.    Introduction

II.   BOOT-51 Installation

      II.1   Files
      II.2   Customizing BOOT-51
      II.3   Tayloring the Cables

III.  BOOT-51 Operation

      III.1  Interactive Operation
      III.2  Batch File Operation
      III.3  The BLINK Program

IV.   Troubleshooting


Appendix A:     CUSTOMIZ Error Messages

                A.1 Parameter Errors
                A.2 Baudrate Errors
                A.3 Runtime Errors

Appendix B:     RESET Error Messages

Appendix C:     BOOT-51 Error Messages

Appendix D:     Trademarks

Appendix E:     Tables of Baudrates



I. Introduction
---------------
Usually an 8051 application program is not running correctly at once, and
it is not quite easy to debug it without suitable test equipment.
It is very unconvenient, to blow the program into an EPROM after every
change. Instead it would be nice to load the program into the external
RAM of the target board and then start it. This would dramatically speed
up the turn-around cycles. However, three problems must be solved first:

  1. There must be a suitable interface to transmit the application
     program from the host (PC) to the target (8051) system.

  2. The target board needs a suitable firmware that can receive a
     program from the host computer, store it in the external RAM,
     and finally execute it.

  3. Once loaded, the application program must be executable, although
     it is stored in the external RAM, which is usually mapped into the
     XDATA address space.
     (Programs can only be executed in the CODE address space!)

The corresponding three solutions are:

  1. an RS-232 interface between the PC and the 8051 board
  2. a bootstrap program
  3. external RAM that is mapped into both the CODE and XDATA address space

Nearly all evaluation boards for 8051 derivatives are meeting requirements
1 and 3. In most cases it is easy to establish a memory map according to
requirement 3, even on target boards that do not originally support it:
The -OE input of the (usually static) RAM must be driven by a logic AND of
the -RD and -PSEN signals of the MCU, rather than by -RD alone. That's all!

Requirement 2 can be met by blowing a customized version of BOOT-51 into
the EPROM of the target board. After system reset, it can receive an
Intel-HEX file over the serial interface, store it in the external RAM,
and finally jump to the program start address.
BOOT-51 itself doesn't need any external RAM, and it is by no means
restricted to a PC-based host system. BOOT-51 requires only 1 kB of EPROM.
Sure, a bootstrap program cannot replace a target debugger, but it's a start.



II. BOOT-51 Installation
------------------------
Before blowing BOOT-51 into an EPROM, it must be customized for the target
board, and one or two cables must be taylored for local requirements.



II.1 Files
----------
The BOOT-51 package consists of the following files:

  BOOT51.DOC            BOOT-51 user's manual    (this file)
  BOOT51.A51            BOOT-51 assembler source (requires ASEM-51 V1.2)
  CUSTOMIZ.EXE          BOOT-51 customization utility
  BOOT.BAT              batch file for application program upload
  LOAD.BAT              called by BOOT.BAT only
  RESET.EXE             program to reset target system via PC printer port
  BLINK.A51             sample test program for BOOT-51



II.2 Customizing BOOT-51
------------------------
BOOT-51 must be customized for the target board, before it is ready for
assembly. This is performed with an include file BOOT51.INC, containing
the required configuration data. BOOT51.INC is generated with the utility
program CUSTOMIZ.EXE provided.
There are two major groups of configuration parameters:

  -  baudrate generation
  -  memory addresses

CUSTOMIZ is invoked as shown below:


  CUSTOMIZ <baudrate> [<timer> [<accuracy> [<clock> [<start> [<user>]]]]]


The first four parameters are for baudrate generation, and the last two
parameters are memory addresses. Parameters in brackets are optional.

<baudrate> is the desired nominal baudrate (in Baud), BOOT-51 should use
           for communication with the host system.

<timer>    is the on-chip timer or baudrate generator that is used for
           baudrate generation. Legal values are:

           T1 = timer 1, available on nearly all 8051 derivatives (default)
           T2 = timer 2, available on 8052/32 and all true compatibles
           BG = internal baudrate generator on 80C515/35 and 80C517/37
           BA = internal baudrate generator on 80C515A and 80C517A
           D1 = timer 1 with clock/12 or clock/4 prescaler on 80C320

<accuracy> is the required relative precision of the baudrate in %.
           The default precision is 1.0 %.

<clock>    is the system clock frequency in MHz. (11.0592 MHz default)

<start>    is the start address of BOOT-51 on the target system in hex
           representation. (default is 0000H)

<user>     is the usual hex start address of the application programs
           in the external memory. (default is 8000H)

Baudrate:
---------
For the serial interface, the standard UART is used that is available on
almost every 8051 derivative. BOOT-51 is always running the UART in mode
1, that is asynchronuous mode, 8 data bits, 1 stop bit, no parity.
However, depending on the derivative, there may be various timers or
prescalers that can be used for baudrate generation.
If the desired baudrate cannot be generated or the precision is too bad,
CUSTOMIZ will display a corresponding error message. In this case, try
another baudrate generator that is also available on your derivative.
When this fails, too, try another baudrate that may also do, or think of
using another oscillator crystal that suits better for the task.
You should play around with CUSTOMIZ, to explore how to get best results.
The tables in Appendix E show the precisions of the most frequently used
baudrates that can be generated with the supported timers and baudrate
generators, for some standard clock frequencies.
In most cases baudrate deviations of 2 to 3 % are no problem for the
communication with a PC. Whenever in doubt, try it!
BOOT-51 can receive data at very high baudrates without the need for a
handshake protocol. Output is done more slowly with short pauses between
the characters, to avoid a data overrun of the PC UART. The maximum
effective output speed of BOOT-51 is corresponding to 9600 Baud.
In general, speed is rather a problem for the PC than for the micro.

Example 1:   CUSTOMIZ 9600 BG 0.1 12
----------
             will generate an include file for BOOT-51 that configures it
             for 9600 Baud, generated with the internal baudrate generator
             of a SAB80C535 or SAB80C537 that is clocked with 12.0 MHz.
             The required precision is 0.1 %.
             The bootstrap and application program start addresses are
             set to their default values.

Addresses:
----------

<start>:
An 8051 starts program execution at CODE address 0000H after reset.
Thus there must always be ROM at CODE address 0000H to execute the first
instructions. On most 8051 boards there is EPROM in the range 0000H-7FFFH,
and RAM in the range 8000H-FFFFH. However, the final application programs
will usually start at address 0000H, and the 8051 interrupt addresses start
at address 0003H. When application programs can be loaded into RAM at 8000H,
this is normally not quite realistic for testing.
Hence it would be nice to have CODE/XDATA-RAM at address 0000H to load
and test application programs. That is why some evaluation boards remap the
EPROM from address 0000H to 8000H, and the RAM from 8000H to 0000H, when the
first memory access to a CODE address > 7FFFH is made.
To support this, BOOT-51 starts with a long jump to its entry point, to
eventually remap the memory. If you own a corresponding evaluation board,
specify the <start> address of BOOT-51 to the location, where it resides
after memory remapping!

<user>:
In principle, BOOT-51 can load an application program at any location in
the external RAM and start it there. However, the interrupt addresses
should be redirected to the location, where application programs usually
start, e.g. the start address of the external RAM.
Hence the <user> address should point to the location, where the CODE/XDATA-
RAM starts. If it starts at 8000H, interrupt 0003H is redirected to 8003H,
interrupt 000BH to 800BH, and so on.
If the CODE/XDATA-RAM starts at 0000H (after remapping), the <user> address
has no practical meaning and can be left default.

Example 2:   CUSTOMIZ 19200 T2 1 11.0592 0 C000
----------
             will generate an include file for BOOT-51 that configures it
             for 19200 Baud, generated with timer 2 of an 80C52 or 80C32
             that is clocked with 11.0592 MHz. The required precision is 1 %.
             BOOT-51 is located at address 0000H in the EPROM, and the
             interrupt addresses are redirected to location 0C000H.

If CUSTOMIZ aborts with an error message, it returns ERRORLEVEL 1 on para-
meter- and baudrate-errors, and ERRORLEVEL 2 on fatal runtime errors.
When CUSTOMIZ terminates without error message, it returns ERRORLEVEL 0, and
a customization header file BOOT51.INC should be present in the default
directory. With this file, BOOT-51 can be assembled as usual with

              ASEM BOOT51

Remember that BOOT-51 requires ASEM-51 V1.2 or later!
Now there should be an Intel-Hex file BOOT51.HEX, which may serve directly
as input for the EPROM blower. We may also convert it to a binary image file
with the HEXBIN utility:

             HEXBIN BOOT51/LENGTH:4000

would generate a binary image file BOOT51.BIN for a 16 kB EPROM (27C128).
(Note: Only 1 kB of EPROM is required for the BOOT-51 program code.)
Once in an EPROM, BOOT-51 should be ready to run on the target system.



II.3 Tayloring the Cables
-------------------------
Application programs are uploaded to the target system over a serial
interface. The serial ports of the PC may have 9-pin or 25-pin male
D-Shell connectors. Suitable RS-232 cables for the MCS-51 board can
be taylored as follows:


   RS-232 cable with 25-pin female D-Shell connector:
   --------------------------------------------------

   PC serial port:                                  MCS-51 target system:

        pin

    Tx   2  o----------------------------------------->  RXD

    Rx   3  o----------------------------------------->  TXD

   RTS   4  o-----+
                  |
   CTS   5  o-----+

   DSR   6  o-----+
                  |
   DCD   8  o-----+
                  |
   DTR  20  o-----+

ground   7  o----------------------------------------->  ground


Shortening the modem control signals is absolutely required for batch
operation! If the CTS-, DSR-, or DCD-input is not set to logic low (+12V),
the PC will hang during character output to the serial port.
For operation with most terminal emulation programs, only the Tx-, Rx-,
and ground lines are required, and the handshake lines may be left open.
For further information refer to the documentation of your terminal
emulation program.


   RS-232 cable with 9-pin female D-Shell connector:
   -------------------------------------------------

   PC serial port:                                  MCS-51 target system:

        pin

    Rx   2  o----------------------------------------->  TXD

    Tx   3  o----------------------------------------->  RXD

   RTS   7  o-----+
                  |
   CTS   8  o-----+

   DCD   1  o-----+
                  |
   DTR   4  o-----+
                  |
   DSR   6  o-----+

ground   5  o----------------------------------------->  ground


If you own a 9/25-pin mouse adaptor with all pins connected, the 9-pin
version of the cable should be preferred!
If your MCS-51 board has a reset input (or you can establish one), the
target system can be reset in batch files over a printer port of the PC.
For this, a suitable reset cable must be taylored as shown below:


   Reset cable with 25-pin male D-Shell connector:
   -----------------------------------------------

   PC printer port:                                 MCS-51 target system:

            pin

        D0   2  o----------------------------------------->  Reset
                                                             _____
        D1   3  o----------------------------------------->  Reset

    ground  25  o----------------------------------------->  ground


In practice, only one of the two reset lines will be required.
When the program RESET.EXE is invoked, a positive reset pulse appears
at D0 (8031, 8032), and a negative pulse at D1 (80C535, 80C537).
For detailed information on the RESET program, refer to chapter III.2,
"Batch File Operation".



III. BOOT-51 Operation
----------------------
When BOOT-51 is customized correctly, and the target board is connected to
the host PC with the cable(s) described above, we can start to upload and
run application programs. There are two possible modes of operation:

  - interactive operation
  - batch file operation



III.1 Interactive Operation
---------------------------
BOOT-51 implements a simple ASCII user interface for serial communication.
The bootstrap program can be operated interactively with a terminal emulation
program running on the PC (e.g. TELIX).
To perform this, start your terminal emulation program, and configure it for
the correct baudrate, 8 data bits, 1 stop bit, no parity, and no handshake.
Then reset the MCS-51 target system.
Now the BOOT-51 sign-on message should appear on your screen:

        BOOT-51  V1.0           Copyright (c) 1996 by W.W. Heinz

        >

The '>' character indicates that the BOOT-51 command line interpreter is
ready for input. It implements exactly two commands:

1. The UPLOAD command:
   First press the 'U', and then the return key.
   Now the upload prompt ':' should be displayed. BOOT-51 is now ready to
   receive an application program in Intel-Hex format. Send an Intel-Hex
   file with the ASCII upload function of your terminal emulation program.
   Now the received Intel-Hex records are loaded to their start addresses
   specified in the record headers. If an EOF record is received, upload
   is terminated and the command prompt '>' is displayed again, and the
   command line interpreter is ready for the next command.
   When a format error is detected in the Intel-Hex file, BOOT-51 waits
   until no more characters are received for about two seconds, and then
   aborts with a corresponding error message.  (see Appendix C)

2. The GO TO command:
   To start an application program at address 8000H, enter "G 8000" and
   press return. BOOT-51 sets now all MCU registers to reset conditions
   (as far as possible), and jumps to the start address specified.
   Now the previously loaded application program should be running!

Any desired number of Intel-Hex files may be loaded, before entering the
'G' command. The commands may be entered in upper or lower case letters.
Interactive operation should be preferred, when the application program
performs serial I/O. This can easily be supervised with the terminal
emulation program. In interactive mode, a reset cable is of little use!



III.2 Batch File Operation
--------------------------
If serial I/O is only used for program upload, batch file operation may be
the most convenient way of testing with the shortest turn-around cycles.
The sample batch job below, shows the principles of operating BOOT-51 from
a PC with MS-DOS batch commands:

        MODE COM2:9600,N,8,1,P
        RESET LPT1
        ASEM %1
        ECHO U >COM2
        COPY %1.HEX COM2
        ECHO G 8000 >COM2

In this example, serial I/O is done over serial port COM2, and the target
system can be reset over printer port LPT1.
First of all, the serial port COM2 is initialized to the desired baudrate
of 9600 bps, 8 data bits, 1 stop bit, and no parity with the MODE utility.
Then the RESET program provided is executed to reset the target system via
printer port LPT1.
To give the MCS-51 board some time to recover from reset (and to send its
sign-on message), ASEM-51 is now invoked to assemble the application program.
When finished, the BOOT-51 upload command 'U' is ECHOed to COM2, and the
Intel-Hex file is also simply copied to the serial port.
Finally the application program is started at address 8000H with the
command "ECHO G 8000 >COM2".
To test an application program MYPROG.A51 with the above batch job (stored
in a file TEST.BAT), simply type

        TEST MYPROG

at the DOS prompt, and see what you get.
Of course this was only a minimized example! In general you will not only
have to modify serial port, baudrate, printer port, and start address for
your local requirements, but also to do something for plausibility checking
and error handling.
For this, the more sophisticated batch file BOOT.BAT has been provided.
It allows an easy change of all configuration parameters with any ASCII
editor. For further information see the commentary inside BOOT.BAT.
In principle, BOOT.BAT contains only that configuration data!
(The actual work is done by another batch file LOAD.BAT provided,
 which is invoked by BOOT.BAT.)
A program MYPROG.A51 can now be assembled, uploaded and started with

        BOOT MYPROG

Finally, the RESET program provided, may be worth a detailed explanation:
When invoked, RESET forms a reset pulse of the duration <pulsewidth> at
the D0 and D1 outputs of the PC printer port <port>:

              RESET <port> [<pulsewidth>]

Legal <port> values are:  PRN, LPT1, LPT2, and LPT3.
PRN and LPT1 are equivalent.
The optional parameter <pulsewidth> is the duration of the reset pulse in ms.
Legal values are:  1 <= <pulsewidth> <= 65535.  (default is 50)
When invoked without parameters, a help screen is displayed.
In case of error, RESET returns the ERRORLEVEL 1, 0 otherwise.
When executed, RESET forms a positive pulse at D0 (pin 2), and a negative
pulse at D1 (pin 3) of the PC printer port. The default pulse width is 50 ms.
If it is too short to reset the MCS-51 board, specify a greater pulse width.

For batch file operation, a reset cable is highly recommended! If you don't
have it, you will always have to press the reset button of the target system,
before invoking BOOT.BAT. Since this may easily be forgotten, it is better
to automate this step.


III.3 The BLINK Program
-----------------------
When BOOT-51 is customized and blown into an EPROM, and the target board
is connected to the host PC, it would be nice to verify, whether the whole
configuration is working together correctly. This can be done with a short
test program that performs a well-defined action when started.
For this purpose the tiny assembly program BLINK.A51 has been provided.
It simply toggles the logic level of a port pin (roughly) once a second
(great when connected to a LED) to verify, whether all the components in
the chain

    assembly -> serial interface -> target system <-> bootstrap program

are working together correctly.
It can be adapted to your requirements with little efforts:

1. If your target system carries a LED that can be switched with a
   (bit-addressable) port pin, please change the BIT symbol LEDPIN
   accordingly. Then the program will make the LED blink.

2. Change the program start address START to the location, where
   user programs are usually loaded on your target system.
   The program code itself is position-independent!

If there is no LED on your target system, connect the port pin LEDPIN to
a volt-meter. This may also do. Aside of P0 and P2 you may use every
bit-addressable port with LEDs or spare outputs. Now the DOS command

        BOOT BLINK

should reset the MCS-51 board, assemble the test program, upload it to the
target system, and finally start it. If the LED is blinking, everything is
now perfectly installed and ready for daily work.
If not, you should read the next chapter!



IV. Troubleshooting
--------------------
1. When initializing the serial port, the DOS MODE utility aborts with an
   error message like:  "function not supported on this computer", or
   "illegal parameter", or something like that.
   On most PCs, the BIOS doesn't support baudrates greater than 9600 Baud.
   However, most terminal emulation programs can operate at baudrates of up
   to 115200 Baud.

2. The RESET program aborts with "printer port not found".
   The PC-BIOS didn't recognize the printer port specified.
   Try another printer port or check your PC hardware.

3. The RESET program aborts with "hardware failure".
   The PC-BIOS has recognized the printer port, but the data latch doesn't
   work. Try another printer port, or check the defective port.

4. RESET terminates without any error, but the target system is not reset.
   The reset cable may be plugged into the wrong printer port.
   First of all try the other ports.
   There may also be something wrong with the cable itself.
   Employ the BOOT-51 manual and the circuit diagram of the target board,
   and check the cable.
   Furthermore, the reset pulse may be too short.
   Specify a greater pulse width. You may also decrease the reset capacitor
   of the MCS-51 system.

5. The target system is reset all the time.                            _____
   When tayloring the reset cable, you may have mixed up the RESET and RESET
   lines. Simply interchange them.

6. The PC hangs when data are sent over the serial interface in batch mode.
   The RS-232 cable may be plugged into the wrong COM-port.
   First of all, try the other ports.
   There may also something be wrong with the modem control signals.
   Employ the BOOT-51 manual and check the RS-232 cable on the PC side.

7. It works in interactive mode, but the PC hangs, if data are sent in batch
   mode. There is something wrong with the modem control lines!  (see 6.)
               ==
8. In batch mode everything seems to work fine on the PC, but on the target
   system you get absolutely nothing.
   Try the interactive mode and reset the target system. If nothing happens,
   you may have mixed up the receive and transmit lines of the target board.
   If you get some garbage, the baudrates and/or serial data formats of the
   target system and the PC are probably different.
   Configure your terminal emulation program correctly, and change BOOT.BAT
   accordingly. (correct data format: 8 data bits, 1 stop bit, no parity)

9. When invoked, the MS-DOS MODE command hangs, or fails to change the
   previous baudrate, although it terminates without error.
   Remove all networking and communication drivers and TSR programs from
   your CONFIG.SYS and AUTOEXEC.BAT files, reboot, and try it again.
   There is plenty of quick'n dirty software, doing something strange
   with the BIOS interrupts!



Appendix A:     CUSTOMIZ Error Messages
===========


A.1 Parameter Errors:
---------------------
Parameter errors apply to the correctness and consistency of the command
line parameters. If one of these errors is detected, it is flagged on the
console, and CUSTOMIZ is aborting with ERRORLEVEL 1:

accuracy out of range                 Baudrate accuracy < 0, or > 5 %.
address out of range                  Address is no unsigned 16-bit number.
baudrate out of range                 Specified baudrate is < 0.
clock frequency out of range          Specified clock frequency is < 0.
illegal real number                   Parameter is no valid real number.
invalid hex number                    Parameter is no valid hex number.
too many parameters                   More than 6 parameters specified.
unknown baudrate generator            Baudrate generator not implemented.


A.2 Baudrate Errors:
--------------------
Baudrate errors apply to the results that CUSTOMIZ has derived from the
given program parameters. If one of these errors is detected, it is flagged
on the console, and CUSTOMIZ is aborting with ERRORLEVEL 1:

baudrate cannot be generated          Baudrate error is greater than 10 %.
insufficient accuracy                 Baudrate error is greater than the
                                      required accuracy.

A.3 Runtime Errors:
-------------------
In general, runtime errors are file I/O errors.
If one of these errors is detected, it is flagged on the console,
and CUSTOMIZ is aborting with ERRORLEVEL 2:

access denied                 No priviledge for attempted operation.
disk full                     No more free disk space.
disk write protected          Attempt to write to a write-protected disk.
drive not ready               Disk drive is off, or no media mounted.
fatal I/O error               General (unknown) disk or device I/O error.



Appendix B:     RESET Error Messages
===========

too many parameters           More than two parameters specified.
illegal device name           No printer port.
invalid pulse-width           Pulse width is 0, or no unsigned 16-bit number.
printer port not found        The BIOS did not recognize the printer port.
hardware failure              The printer port data latch cannot be read back.








Appendix C:     BOOT-51 Error Messages
===========

checksum error                Intel-HEX record checksum is not correct.
illegal command               A command other than U or G has been entered.
illegal hex digit             Hex digit expected. Another character received.
illegal record ID             Intel-HEX record type is greater than 1.
unexpected character          The received Intel-HEX record doesn't start
                              with ':', or doesn't end with CR/LF.








Appendix D:     Trademarks
===========


ASEM-51 is a trademark of W.W. Heinz.
MCS-51 is a trademark of Intel Corporation.
TELIX is a trademark of deltaComm Development.
IBM-PC, IBM-XT, and IBM-AT are trademarks of IBM Corporation.
MS-DOS is a trademark of Microsoft Corporation.
All device codes of 8051 derivatives are trademarks of the manufacturers.
Other brand and product names are trademarks of their respective holders.



Appendix E:     Tables of Baudrates
===========


The following tables show the most frequently used baudrates that can
be generated with a particular timer or baudrate generator, for some
standard clock frequencies.
Baudrates which can be generated with a relative accuracy of better
than 4.0 %, are marked with that accuracy (in %) or with a '+' character,
if they can be generated exactly (= better than 0.01 %).




Baudrates that can be generated with Timer 1:
---------------------------------------------


bps\MHz |  11.0592  12.0000  14.7456  16.0000  18.0000  20.0000  24.0000
--------+---------------------------------------------------------------
 115200 |
  76800 |                       +
  64000 |             2.34                                         2.34
  57600 |     +
  38400 |                       +
  31250 |              +                          +                 +
  19200 |     +                 +                2.34
   9600 |     +                 +       3.55     2.34     1.36     0.16
   7200 |     +       3.55     3.03     3.55     0.16     3.34     2.12
   4800 |     +       0.16      +       2.12     2.34     1.36     0.16
   3600 |     +       2.12     1.59     0.64     0.16     0.22     0.79
   2400 |     +       0.16      +       0.79     0.16     0.94     0.16
   1800 |     +       0.79     0.78     0.64     0.16     0.22     0.64
   1200 |     +       0.16      +       0.64     0.16     0.22     0.16
    600 |     +       0.16      +       0.08     0.16     0.22     0.16
    300 |     +       0.16      +       0.08     0.16     0.22     0.16
    200 |     +       0.16      +       0.16     0.16     1.73
    150 |     +       0.16      +
    134 |    0.03     0.09
    110 |    2.27
     75 |
     50 |







Baudrates that can be generated with Timer 2 of the 8052:
---------------------------------------------------------


bps\MHz |  11.0592  12.0000  14.7456  16.0000  18.0000  20.0000  24.0000
--------+---------------------------------------------------------------
 115200 |     +                 +                2.34
  76800 |             2.34      +                         1.73     2.34
  64000 |             2.34     2.86     2.34     2.34     2.34     2.34
  57600 |     +                 +       3.55     2.34     1.36     0.16
  38400 |     +       2.34      +       0.16     2.34     1.73     2.34
  31250 |    0.54      +       1.70      +        +        +        +
  19200 |     +       2.34      +       0.16     1.02     1.36     0.16
   9600 |     +       0.16      +       0.16     0.69     0.16     0.16
   7200 |     +       0.16      +       0.64     0.16     0.22     0.16
   4800 |     +       0.16      +       0.16     0.16     0.16     0.16
   3600 |     +       0.16      +       0.08     0.16     0.22     0.16
   2400 |     +       0.16      +       0.16     0.16     0.16     0.16
   1800 |     +       0.16      +       0.08     0.16     0.06     0.08
   1200 |     +       0.16      +       0.08     0.05     0.03      +
    600 |     +        +        +       0.04     0.05     0.03      +
    300 |     +        +        +       0.02      +       0.02      +
    200 |     +        +        +        +       0.02      +        +
    150 |     +        +        +       0.01      +        +        +
    134 |     +       0.02      +        +        +        +        +
    110 |     +        +        +       0.01      +        +        +
     75 |     +        +        +        +        +        +        +
     50 |     +        +        +        +        +        +        +







Baudrates that can be generated with the 80535 Internal Baudrate Generator:
---------------------------------------------------------------------------


bps\MHz |  11.0592  12.0000  14.7456  16.0000  18.0000  20.0000  24.0000
--------+---------------------------------------------------------------
 115200 |
  76800 |
  64000 |
  57600 |
  38400 |
  31250 |
  19200 |                                                           +
   9600 |              +                                            +
   7200 |                                         +
   4800 |              +
   3600 |
   2400 |
   1800 |
   1200 |
    600 |
    300 |
    200 |
    150 |
    134 |
    110 |
     75 |
     50 |







Baudrates that can be generated with the 80C515A Internal Baudrate Generator:
-----------------------------------------------------------------------------


bps\MHz |  11.0592  12.0000  14.7456  16.0000  18.0000  20.0000  24.0000
--------+---------------------------------------------------------------
 115200 |     +                 +                2.34
  76800 |             2.34      +                         1.73     2.34
  64000 |             2.34     2.86     2.34     2.34     2.34     2.34
  57600 |     +                 +       3.55     2.34     1.36     0.16
  38400 |     +       2.34      +       0.16     2.34     1.73     2.34
  31250 |    0.54      +       1.70      +        +        +        +
  19200 |     +       2.34      +       0.16     1.02     1.36     0.16
   9600 |     +       0.16      +       0.16     0.69     0.16     0.16
   7200 |     +       0.16      +       0.64     0.16     0.22     0.16
   4800 |     +       0.16      +       0.16     0.16     0.16     0.16
   3600 |     +       0.16      +       0.08     0.16     0.22     0.16
   2400 |     +       0.16      +       0.16     0.16     0.16     0.16
   1800 |     +       0.16      +       0.08     0.16     0.06     0.08
   1200 |     +       0.16      +       0.08     0.05     0.03      +
    600 |     +        +        +       0.04     0.05     0.03      +
    300 |     +        +        +       0.04     0.05     1.73
    200 |     +       0.05
    150 |
    134 |
    110 |
     75 |
     50 |







Baudrates that can be generated with Timer 1 of the DALLAS 80C320:
------------------------------------------------------------------


bps\MHz |  11.0592  12.0000  14.7456  16.0000  18.0000  20.0000  24.0000
--------+---------------------------------------------------------------
 115200 |                       +
  76800 |                       +                         1.73     2.34
  64000 |             2.34              2.34              2.34     2.34
  57600 |     +                 +                2.34
  38400 |             2.34      +                         1.73     2.34
  31250 |              +                 +        +        +        +
  19200 |     +       2.34      +       0.16     2.34     1.73     2.34
   9600 |     +       2.34      +       0.16     1.02     1.36     0.16
   7200 |     +       0.16      +       0.79     0.16     0.94     0.16
   4800 |     +       0.16      +       0.16     0.69     0.16     0.16
   3600 |     +       0.16      +       0.64     0.16     0.22     0.16
   2400 |     +       0.16      +       0.16     0.16     0.16     0.16
   1800 |     +       0.16      +       0.08     0.16     0.22     0.16
   1200 |     +       0.16      +       0.16     0.16     0.16     0.16
    600 |     +       0.16      +       0.08     0.16     0.22     0.16
    300 |     +       0.16      +       0.08     0.16     0.22     0.16
    200 |     +       0.16      +       0.16     0.16     1.73
    150 |     +       0.16      +
    134 |    0.03     0.09
    110 |    2.27
     75 |
     50 |