PIONEER Electronic Corporation
DRD608.SYS (8 Drives)
CD-ROM Device Driver Instruction Manual

As you requested some time ago, a prototype MS-DOS 8 DRIVE
CD-ROM device driver has been finished. The following is an
explanation of that driver.

Included files

1.DRD608.SYS
The driver for Future Domain SCSI interface board.

2.DRD608PS.SYS
The driver for IBM SCSI Adapter/A interface board.

3.DISC.EXE
The utility program allows the designation of the CD-ROM drive
order.

4.XDISC.EXE
The utility program to select a disc on each CD-ROM drives.

5.MSCDEX.EXE
Microsoft CD-ROM Extensions

6.SETUP.EXE
Setup program

This device driver assigns a DRD-600 drive to a drive letter. To
select a disc to be an active disc, you can use XDISC.EXE utility
program. This program produces the same result as if you changed
the disc by hand. Attention please, only one disc can be seen by the
system at any one time.

Usage.
1.DRD608.SYS
This is the device driver for Future Doman SCSI interface board.
This driver allows 8 DRM-600 CD-ROM drives. When the PC is
booting up, the driver checks if a DRM-600 is connected and
allocates a drive letter to each drive automatically. The max.
number of drives is 8.

Usage as follows.

Add 2 lines in your CONFIG.SYS file.

        LASTDRIVE=Z
        DEVICE=(path)\DRD608.SYS /D:MSCD000 ........

The syntax for the driver's switches (underlined part) is as
follows.

/D:device name             ex. /D:MSCD000
When the device driver is installed, this name is what will be used
by the device driver to name and MSCDEX use this name to find the
device driver.

/N:number of drives               ex. /N:6
Choose a number from 1 to 8 for the number of drives that you
wish to use as CD-ROM drives. The driver allocates drives from
that which has the lowest SCSI ID up to the specified number.
The default is 8.

/C:CD device name             ex. /C:CDP\
CD device name is the CD Player character type device name.
Default is no CD Player device driver, when you omit this switch.

This driver doesn't allow the allocating of the SCSI ID using the
"/S" option

2.DRD608PS.SYS
This is the device driver for IBM SCSI Adapter/A interface
board. The usage is the same as DRD608.SYS. Because of the
limits of the interface board, the max. drive number is 3.

3.DISC.EXE
The DRD608 series driver can handle a max. of 8 drives.
This utility program allows the designation of the CD-ROM drive
letters order in conjunction with the driver.
The usage as follows.

To see the current order of the drive.

    >DISC CD-ROM_device_name
    >DISC CD-ROM_drive_letter:
        The colon is required.

To change the current order of the drives.

  >DISC CD-ROM_device_name [-r] no1 no2 ...

Where [-r] is a reset option and "no1 no2 ..." is your desired
order of the discs in the magazine.

To exchange two drive letters.
CD-ROM_drive_letter:
Changes the drive letter of the first drive to that of the second and
vice versa.

4.XDISC.EXE
This utility program allows to select an active disc for the given
CD-ROM drive letter of an DRM-600.

     To see the selected disc number in the drive D:.
       >XDISC d:

To select third disc in magazine in the drive D:.
      >XDISC d: 3


5.MSCDEX.EXE
MSCDEX.EXE is an extension to the MS-DOS operating system
which permits reading of CD-ROM discs which conform to
the High Sierra or ISO-9660 format.

To install the extensions.
     >MSCDEX /D:MSCD000

The device name (under line) is the same as the name specified in
CONFIG.SYS file.

6.SETUP.EXE
This setup program install the device driver and MSCDEX.EXE
automatically.