Local Area Network Option

                                        for

                          Master File Manager version 2.10



                             Installation and Reference





                                    version 1.00

                                    March, 1993





        MFM Local Area Network option version 1.00 requires MS-DOS or PC-DOS
            version 3.10 or above and at least 460k of available memory.

         MFM/LAN operates on a Personal Computer (PC) attached to the TBBS
                         computer via a Local Area Network.




       Overview



       The Master File Manager Local Area Network option (MFM/LAN)
       compliments and expands Master File Manager version 2.10 operation.

       MFM/LAN adds new features to MFM and extends existing ones. The
       interface is open and expandable, offering capabilities required today
       and needed tomorrow.

       MFM/LAN is an application designed to provide support services to a
       TBBS system attached via a Local Area Network (LAN). Its operation is
       controlled by an application program interface involving combinations
       of requests and responses. The interface provides necessary
       communication and synchronization among applications so a multi-
       computer TBBS system presents a seamless view to callers.

       MFM/LAN operates as a dedicated application on a PC. Its basic off-
       line storage file copy operations require approximately 160,000 bytes
       of memory. Its advanced DOS-based operations (File contents
       examination, DOS shell operations, etc) require at least an additional
       300,000.

       MFM/LAN functions include:

         -  COPY
            This operation copies files from LAN-attached CD-Rom or other
            mass storage devices to a common download area, avoiding the
            multiple long delays and BBS performance degradation commonly
            associated with CD and other mass storage device access.

         -  EXAMINE
            This operation executes SysOp-provided external programs to
            examine the contents of files based on the file extension. The
            contents examine operation allows callers to view the table of
            contents of LAN-resident compressed archives before downloading
            them without impacting BBS performance.

         -  DOS
            The DOS operation is a "shell to DOS" facility with limitless
            possibilities for real-time BBS support services.

         -  EXIT
            This operation exits the MFM/LAN program with a specified DOS
            ErrorLevel so the controlling BATch file can branch to perform
            predefined off-line operations. Mail handling, File Echo
            processing, upload screening, and system maintenance are but a
            few applications.

         -  STATISTICS
            The MFM/LAN program maintains cumulative COPY performance
            statistics by drive letter. This operation can be used to
            retrieve or reset the statistical data.




       Files Included



            MFMLAN.Doc     This documentation file.

            MFMLAN.Exe     The control program.

            MFMLAN.Cfg     The configuration control file.

            Mfm.Key        A new key file must be issued to activate MFM/LAN.




       MFMLAN.EXE



       MFMLAN.Exe must be executed with at least one parameter. That
       parameter must be a wildcard filename that matches the location of
       MFM/LAN operation request files. The request filenames will always
       begin with NFS and will always have the extension .REQ.

       The path to the request filenames is configured via Mfm.Tpg SysOp
       Control Panel selection 5. The filename must always be NFS*.REQ for
       use with MFM.

       An example command line is:

         MFMLAN D:\MFM   [D:\PATH\MFMLAN.LOG] [/T#] [/V]

         D:\MFM  is the drive and path identified in SysOp Control Panel
            screen 5 [Path to write request file]. This drive and path MUST
            be visible to both the BBS computer and the MFM/LAN computer.
            This is the common communication directory that MFM.TPG and
            MFMLAN.EXE use to pass request and status data back and forth.
            Formats like C: or C:\ or C:\MFM or C:\MFM\ are all accepted.
            This path can be on a RAM drive.

         D:\PATH\MFMLAN.LOG  is the location for the program to write an
            optional activity log. If the parameter is omitted the log will
            not be written. If used, the log file must be written to a drive
            on the MFM/LAN computer.

         /T#  The internal timer will look for requests every # seconds. /T5
            instructs MFMLAN to look for requests every 5 seconds. The timer
            value can be set to a value between 1 and 60 seconds. The default
            is once a second.

         /V  Turns off fullscreen operation. Fullscreen operation splits the
            screen into two segments -- history and current operation. If the
            screen can be set to 43 or 50 or even 60 lines high the display
            will change to fill the screen. Some video modes might not allow
            fullscreen operation. /V changes MFM/LAN output to a TTY-style
            scrolling display.




       MFMLAN.CFG



       The ASCII text MFM/LAN configuration control file consists of
       parameter lines to direct and customize MFM/LAN operation.
       Configuration file changes can be made with any text editor in non-
       document mode.

       MFMLAN.Cfg is optional. If used, it must be in the current logged
       directory when MFMLAN.Exe is executed.




            EXAM



       EXAM definition lines define file contents examination operations
       based on file extensions.

       Default definitions are used if none are found in MFMLAN.Cfg. If any
       definitions are found in MFMLAN.Cfg they replace ALL default
       definitions.

       Programs indicated on EXAM definitions must be available either
       explicitly via full drive:\path\program or via the directories defined
       in the MFM/LAN computer PATH environment variable. Up to 64 Exam
       extension/program selections can be defined.

       The EXAM parameter has three parts:

       EXAM <3 character file extension> <inspect/list command>

       EXAM indicates the parameter type.

       The 3 character file extension represents the three characters
       following the period in filenames. Common extensions are ZIP, ARC,
       ARJ, and LZH.

       The inspect/list command is the actual DOS command issued by MFM/LAN
       to perform the file contents examine. The selected filename is placed
       after the command and the string is passed to DOS for execution.

       All data on the line is used. Do not add comments after the command.

       Exam definitions are processed sequentially.
       A special case "catch all" extension is an asterisk (*). An Exam
       selection with an asterisk as the file extension is treated as a
       "match" no matter what the actual file extension is. This allows
       general purpose archive contents listers (eg Vern Buerg's FV) to be
       used without having to list all possible file extensions.

       The inspect/list command can be a program or a BATch file. Standard
       DOS output is redirected, captured, and returned to the calling
       program on the TBBS computer. Direct screen writes will not be
       captured.

       These default EXAM parameter definitions are in effect if none are
       defined in MFMLAN.Cfg:

         EXAM ZIP PKZIP -V
         EXAM LZH LHA L
         EXAM ARJ ARJ L
         EXAM ARC ARC V
         EXAM AR7 ARC V
         EXAM PAK PAK L

       An expanded list in MFMLAN.Cfg might include these entries to define
       additional file extensions inluding the special case "catch-all"
       asterisk extension. In this example if a file extension match is not
       found by searching the list sequentially (ARC, ARJ, ..., PAK, ZIP) the
       search will fall through to the asterisk parameter and execute a
       program called FV.

         Exam ARC arc7 l
         Exam ARJ arj l
         Exam AR7 arc7 l
         Exam LZH lha l
         Exam SDN pak l
         Exam PAK pak l
         Exam ZIP pkzip -v
         Exam *   FV




       Basic Installation



       This installation procedure assumes that you have already installed
       and tested a Local Area Network and already have Master File Manager
       version 2.10 installed and operating on your TBBS computer.

       A principal operation of MFM/LAN is to copy files from CD-Rom or other
       mass storage device to RAM or high speed disk for staged downloads. As
       a result the recommended configuration is to set up a "file server"
       computer on the Local Area Network and attach all mass storage devices
       to that computer. MFM/LAN is then run as a dedicated application on
       the "file server" computer to accept and process requests issued from
       applications running on the main TBBS computer. This completely
       offloads slow device operation from the TBBS computer.

       Perhaps the most difficult part of the installation process is the
       selection and setup of drive letter "mappings" so both the main TBBS
       computer and the server computer have access to everything they need
       when they need them.

       Essentially, there are two drive letter overlaps required between the
       TBBS computer and the file server computer. These two drive letter
       definitions (mappings) MUST be the same on the TBBS computer and the
       MMF/LAN computer:
         -  The drive MFM.TPG writes requests to [Path to write request file]
            and MFM/LAN will look on for operation request files. This might
            be a drive on the TBBS computer or one on the server computer
            itself. All other drive letters and access to them are relative
            to the computer needing access to them.

         -  The download staging drive MFM/LAN will copy the files to for
            actual download. This drive is configured via MFM's SysOp Control
            Panel screen 1.

       In other words, a person sitting at the keyboard of either computer
       must be able to reference both the request file path and the download
       staging path using exactly the same drive letter.

       Certainly, the easiest and most conveniently maintained setup is one
       in which both the TBBS computer and the server computer are installed
       as both LAN Client and LAN Server and where all drive letters on both
       machines are "mapped" the same.

       This mirrored mapping approach is the recommended "starter setup". In
       this way you can install the server computer and drive hardware, test
       everything, and actually run the BBS on-line before you even try to
       install the MFM/LAN software. If you have troubles you can fall back
       without reconfiguring your system.

       One "gotcha" is trying to map drive letter C. Some LAN software does
       not allow drive letter C on a server to be mapped.

       Let's say drives U through Z are six CD-Rom drives on the MFM/LAN file
       server computer. All your TBBS .DIR files will point to those drive
       letters and the MFM.EXE program will build the MFM databases
       referencing those drives. Drive letter mappings make the drive letters
       accessible from the TBBS computer just as if they are local drives. At
       run-time, TBBS, MFM.TPG, and MFMLAN.EXE can look at the U-Z drives and
       not be concerned where they exist on the LAN.

       Assuming the drive mappings and access tests are successful we're
       ready to get started with MFM/LAN. MFM/LAN is simply an access layer
       you install between the TBBS computer and the CD-Rom drives so
       performance of the TBBS computer -- and your callers -- will not be
       impacted by the slow access of those drives.

       Step one is to install the MFMLAN.EXE and optional MFMLAN.CFG files.
       Select a subdirectory for request / response exchanges [Path to write
       request file] and execute MFMLAN.EXE using parameters explained
       previously...

            MFMLAN D:\MFM

       MFM/LAN will offer onscreen feedback indicating that it is ready to
       accept requests.

       Step two is to activate the MFM/LAN configuration options in the
       MFM.TPG SysOp Control Panel.

       If selection 5 [<5> Local Area Network (MFM/LAN) config] is not
       available please make sure you are using the new MFM.KEY file provided
       with the MFM/LAN option. Selections 5 and 6 are only available when a
       new key file is installed.

       The selection 5 options are repeated twice. Either one or two MFM/LAN
       machines can be configured so more drive letters, devices, or
       operations can be configured than might comfortably be serviced by one
       machine. The server machines are referred to as MFM/LAN 1 and MFM/LAN
       2:

            Drive letters via MFM/LAN #.

            Path to write request file

            DOS command line ...........

            Wait for files .............

       Drive letters are the MS-DOS drive letters (A-Z) referenced in the MFM
       database that should be accessed via the MFM/LAN interface. This is
       the on/off switch for MFM/LAN operations. These drive letters must be
       accessible from the server computer since MFM/LAN copy operations are
       executed on that computer. All files on these drives will be accessed
       via the MFM/LAN request interface. The MFM/LAN drive list is checked
       before the Control Panel screen 1 list of drives to cache so you can
       leave that list as is was before you installed MFM/LAN.

       The Path to write request file is the location MFM.TPG will write
       MFM/LAN request files and must be accessible to both MFM.TPG and the
       MFMLAN.Exe program using the same drive letter. Enter only the path
       (trailing back-slash optional). MFM will build and add filenames as
       needed for each request operation.

       The DOS command line is an optional MS-Dos command to execute after a
       requested file has been copied and before control is passed back to
       the caller. This might be used to add or remove archive comments, to
       check for virus infection, or even to generate custom logging. If the
       DOS command line contains the 2 characters %s (percent and lower case
       s) the filename being copied will be substituted at that point in the
       command line at request time. Otherwise the filename will be added to
       the end of the DOS command line.

       The wait for files setting controls whether MFM.TPG will wait for each
       requested file to arrive or return control to the caller without
       waiting. Setting this to Y allows the caller to select additional
       files for download while the server machine processes requests
       independently. When the caller finally decides to download the
       selected file(s) MFM.TPG will wait until at least 300,000 bytes or 300
       seconds of requested files are available and then will allow the
       download to begin.

       Well, that's it. Your MFM/LAN system is running. You and your callers
       will see the difference -- immediately!




       Technical Information



       MFM/LAN operates under control of "request" files. It generates
       "acknowledge" files to let the requesting application know a request
       has been received and queued. And finally, it generates "response"
       files to return operation results to the requesting application.

       All three file types share a common multi-part filename structure:

            Prefix
            Request source
            Sequence number
            Extension

       The filename prefix is always LAN.


       The request source is a two character numeric value ranging from 00 to
       99. Values of 00 through 64 are TBBS line numbers. Other values are
       reserved for custom applications.

       The sequence number is a one to three character numeric value ranging
       from 1 to 999. The sequence is relative to the request source. It is
       reset to 1 at the start of each application and wraps from 999 to 1.

       The extension is REQ or ACK or RSP to indicate the state of the
       requested operation. A REQ file is built by the requesting application
       (eg MFM.TPG) and initiates MFM/LAN operation. When MFM/LAN recognizes
       the file it extracts request control data from the file and renames
       the file to an ACK extension to inform the requestor that the request
       has been queued. When MFM/LAN completes the requested operation it
       writes the data or a response message to a filename with a RSP
       extension.

       The three files -- REQ, ACK, and RSP -- are a request set. All three
       share a common unique eight character identity throughout a request
       operation so all phases of the operation are linked.

       REQ files are built with one to three lines of data:

            Operation <parameters...>
            Auxiliary parameters
            Requestor information

       The operation is COPY, DOS, EXIT, EXAM, RESET, or STATS.

       Auxiliary parameters are optional depending on the operation. COPY
       operations use this line to trigger execution of a program or BATch
       file on the copied file. The COPY auxiliary operation is configured
       via MFM.TPG SysOp Control Panel screen 5 selections.

       Requestor information is optional for display and log purposes only.
       It is typically the caller or requestor name.

       All MFM/LAN operations are performed using LAN-aware file I/O and
       directory operations in order to eliminate file name conflicts and
       share violations.




       Warranty



       Master File Manager Local Area Network option, a product of ProtoSoft,
       is distributed "as is" without warranty. ProtoSoft, M.O. Enterprises,
       and their dealers and distributors shall have no liability to any
       person or entity for loss or damage related to use of this product.




       Support



       ProtoSoft will work with MFM/LAN Customers to diagnose and correct
       program flaws as they are discovered. Contact the author via BBS at
       717-657-8699 or via E-Mail at Pete White's Cul de Sac Bar and Grill
       BBS.

       ProtoSoft is a division of M.O. Enterprises of Harrisburg Pa, USA
       TBBS and TDBS are manufactured by eSoft, Inc. of Aurora Co, USA