C O M M H E X
                                 Version 3.1
             Copyright (C) 1986, 1987 by Michael Burton Software

    COMMHEX is a diagnostic program that displays information received by 
    a serial port in two windows. The one window shows data received by 
    the serial port in ASCII, and the other window shows the same data in 
    hexadecimal.  Characters that are entered via the keyboard (except 
    F1, CTL-C and CTL-K) are sent to the serial port and are optionally 
    displayed.  
    
    The only keys that have special functions within COMMHEX are the 
    function keys F1 through F10, and CTL-C and CTL-K.  
    
    Function key F1 is used to create, store or load macro character 
    strings.  Up to nine macros may be created, stored or loaded.  When 
    created or loaded, the macros are activated by pressing F2 through 
    F10.  A delay between transmission of each character of a macro may 
    be set in the initialization window. 
    
    A macro consists of up to 80 characters.  It is created one byte at a 
    time by entering its decimal (0-255) or hexadecimal ($0-$FF) 
    equivalent.  When a macro definition is complete, an ENTER with 
    nothing preceding it is entered to close the string. The macros may 
    then be stored to a file for later loading, or they may be used 
    immediately.
    
    CTL-K is used to clear the ASCII and Hexadecimal windows, as well as 
    the incoming and outgoing byte counters.  CTL-C is used to exit the 
    program and return to DOS.

    Each byte received on the serial port is filtered through three 
    masks; an AND mask, an OR mask and an exclusive OR mask, in that 
    order.  If the default masks in the initialization window are used, 
    the incoming byte will remain unchanged.  
    
    COMMHEX is a Shareware program, which is an attempt to provide good 
    software at a low cost.  You are free to copy the program for all 
    your friends, but if you find yourself using it on a regular basis, 
    we ask that you make an $8 contribution to: 

                            Michael Burton Software
                            15540 Boot Hill Rd.
                            Hayden Lake, ID  83835

    You will receive the latest update of COMMHEX and will be placed on 
    our mailing list.  If you have any questions about COMMHEX, call 
    (208)772-9347 after 6 p.m. Pacific time.