SANDWICH PANEL LOAD-SPAN TABLES

     As a COPAN/II user, you have access to the use of a program that 
     generates look-up tables for sandwich panel applications.   If 
     you are interested in this service, fill out the attached request 
     form and up to 20 pages of output will be run for you at no
     charge.    

     Load-Span produces look-up tables that provide approximate load 
     carrying ability of specific core/face combinations over varying 
     core thicknesses and spans.   The output can be in KG/M^2, PSF or 
     PSI.  

     Here is a portion of a page taken from a Load-Span run:

              Deflection Limit: L/ 100
             
            SPAN    D       0.50IN    0.75IN    1.00IN    1.25IN
             
              30  0.30        0.58      1.39      2.39      3.52     
              34  0.34        0.41      1.02      1.79      2.68      
              38  0.38        0.30      0.76      1.37      2.08      
              42  0.42        0.22      0.58      1.06      1.63      
              46  0.46        0.17      0.45      0.84      1.30      
              50  0.50        0.13      0.36      0.67      1.05      
              54  0.54        0.10      0.29      0.54      0.86      
              58  0.58        0.08      0.23      0.45      0.71      
              62  0.62        0.06      0.19      0.37      0.59      
              66  0.66        0.05      0.16      0.31      0.50      
             
              LBS/FT^2        1.98      2.08      2.17      2.27
              I  (in^4)   .0228498  .0448021  .0741391  .1108609
              Z  (in^3)   .0620655  .0908475  .1199358  .1491757

     Loads are based on a predefined deflection criteria expressed as 
     SPAN over any integer between 10 and 1000.    In essence, the 
     report is saying that a core having a some thickness over a span 
     will be able to carry this load while bending that amount.

     The above table would be read as follows:

      A 1.00" core, when loaded over a 50" span will deflect .500"
      while carrying .67 PSI.

     The core type, in this case, was a 5 pound PVC with .118" facings 
     of MAT/ROVING at 35% resin.  The end fixity was Simple-Fixed.

     A single page of output shows the same table three times each one 
     with a different deflection limit.   The following page shows a 
     complete page of output from which the above was taken.
     



     This page is blank


     


              
      Which Span/Core Combinations Are Acceptable?

     Another way that the report can be run is when you are looking 
     for a specific load performance.  Let's say that a structure 
     needs to take a 1psi load.   By locating all of the loads that 
     are within a certain range, say 1.00 to 1.25, the corresponding 
     core thickness and span is found.

     The report will flag the loads that are within this range with a 
     < mark to the immediate right of the applicable value.
     

     Ordering Information
     
     If you are interested in obtaining some tables for your own use, 
     fill out the request form and mail it to us.  You are entitled to 
     20 pages of output at no charge.   The only catch is that a 
     maximum of only two face materials will be accepted.  For 
     instance, you could not run 20 different face materials on the 
     same core.  You could run 10 thickness of two different materials 
     or 20 thicknesses of the same.  If you have any questions, just 
     give us a call. 

     All output will be sent to you on an MS/DOS formatted 5-1/4" 
     floppy disk.  The file(s) will be in ASCII so printing should be 
     very uncomplicated.  Any word processor/text editor will work 
     just fine.   

     If you would like us to print them on presentation quality paper, 
     the charge is $.50 per page.  

     Additional pages of output can be obtained from us for $1.00 per 
     page for orders up to 50 pages.   50 - 100 pages are $.75/pg 
     while over 100 are $.60.    Complete look-up manuals based on 
     your materials are available.  Call for pricing.
     



                        LOAD-SPAN REQUEST FORM

     This form is used to generate load/span tables for sandwich 
     panels.   Each page of output contains 360 beam equation results.

     Name    _________________________________________
     Company _________________________________________
     Address _________________________________________
     City    ___________________________State______Zip_________
     Phone# 
     ================================================================
      MATERIALS           (Only one core and one face per sheet)

     Core Description>
     Shear Modulus   >         psi      Strength>         psi
     Density         >         PCF
      
     The mechanical properties are not necessary if the manufacturers 
     advertised properties are to be used but make sure that the 
     description is complete.   
                                    
     Face Description>
     Bending Modulus >          psi     Strength>         psi
     Density         >          PCF     Poisson >

     All mechanicals must be given for face material.  Sandwich will 
     be considered symmetrical.   (Same properties/thicknesses for 
     each face)
     ================================================================
      CALCULATION PARAMETERS                      Output Units  PSI[ ]  PSF[ ]

     Parameter             Start    Increment   End        Default

     Length of span                             XXXXX   24 to 144 by 12
     ------------------------------------------------------------------
     Core thickness                             XXXXX .5 to 3.25 by .25
     ------------------------------------------------------------------
     Deflection Limits    L/____  L/____  L/____        100, 150, 200
     ------------------------------------------------------------------
     Facing thickness                                        None
     ------------------------------------------------------------------
     End Fixity    Simple[ ]  Fixed[ ]  Simple-Fixed[ ]     Simple

     Each page produces output for a single face thickness.  Because 
     no default exists for facing thickness, all 3 values must be 
     given.   If the default values are to be used for the others, 
     enter nothing. 
     
                   Parados Technical Services   912 N. Main Street   Ann Arbor, MI  48104  (313) 668-8111