NOTE:  The user interface of PCAT was redesigned.  (Program is PC2.EXE)
       Therefore, much of the screen references to this and PCAT2.DOC
       will be inaccurate.  However, much of the concept remained the
       same so there should be something that you can learn from this.


                        Introduction to PCAT (PC2.EXE)

     PCAT is the module in the COPAN system which serves as a material 
     property editor and database.   PCAT is  actually an abbreviation 
     for Property CATalog.

     The primary function of PCAT is to create and edit data files 
     containing material properties for cores and plies.   PCAT also 
     maintains a unit base file which is used by the other modules in 
     the work that they perform. 

     Of all the COPAN/II programs,  PCAT was the least exciting to  
     write because it does such non-creative work:  it writes data 
     files.   But do not misunderstand, PCAT itself is not boring.  
     Quite to the contrary, PCAT is one of the  finest composite 
     material database programs that can be found on the market.   
     Billions of work hours went into its creation and it does very 
     well what it does.   It's operation is effortless and efficient.   
     This module, as well as the others, was designed to allow 
     virtually anyone to analyze composite panels.   Actually,  we 
     believe that all these pages of explaining how to use it is 
     contrary to its simplicity.  Unfortunately, todays software 
     customer expects something with a binding to be included with the 
     disks...if they didn't copy the program. 

                        ------------------------------
                        |                 |          | 
                        |                 |          |
                        |        2        |          |
                        |                 |          |
                        |                 |     3    |
                        |                 |          |
                        |-----------------|          |
                        |        1        |          |
                        ------------------------------
                      The PCAT windows shown in Hi-Res
     
     PCAT uses multiple windows to communicate with you.   There are 
     four primary windows that you will become familiar with.   Each 
     of them has a slightly different function. 

     Window 1

     It is here that the diamond cursor Main> prompt will appear 
     when PCAT is first booted.   The cursor will not blink so don't 
     expect it to.

     Window 1 is where all of the keyword commands will  be  entered.   
     Most of the commands will be available via the function keys F1-
     F10.   To  make it as simple as possible, the 25th row will show 
     which commands are assigned to which function keys.   By pressing 
     the appropriate function key,  the command will be automatically 
     entered.  A carriage return <CR> is added to each so that 
     immediately after the command is displayed, it is entered.   This 
     way, all it takes is a single key to kick-in most routines. 




     Window 2

     The second window is located in the upper left hand area and is 
     used as a display area for larger text groups such as material 
     entry for plies and cores and showing the disk directories. 


     Window 3

     The third window is a help oriented partition that is used to 
     display narrative prompts to assist users with the entry of 
     correct keystrokes.  This window is about 25 columns wide and 
     runs along the right side of the screen. 


     Window 4

     The very bottom row of the screen is used to display all of the 
     available keywords.  Each keyword is assigned to a corresponding 
     function key.   The function keys may be reassigned by using the 
     SWITCH command. 



     PCAT Operational Instructions

     Screen Saver

     Should you be called away from the monitor during a PCAT session,
     you may return and find that PCAT has vanished.  However, don't 
     panic--everything is fine. 

     If no activity occurs for a duration of about a minute, PCAT will 
     assume that  you got bored and went home.   At that time, the 
     screen will be cleared to keep your monitor in showroom 
     condition. 

     PCAT will then "roll some dots" to let everyone know that nothing 
     has frozen-up. 

     To  signal that work is ready to commence,  stab any key and the 
     Main> will  be returned.   The timer will then be reset in the 
     event you're called away again.  This screen saver is active only 
     in the Main> level. 
     



     WARNING: No UNITS Read

     When running PCAT for the first time, this message may appear in 
     the upper right hand corner of the screen.   This indicates that 
     a certain PCUNITS.001 file was not read from disk.  This possibly 
     is because the PCAT that you possess has been supplied without a 
     predefined set of units. 

     In most instances, we have preset these units based  on your  
     requirements.   However, with  the growing  popularity  of 
     COPAN/II, it is possible that you have received a version that 
     does not contain the unit file.  In this instance, you will have 
     to define these units on your own. 

     The other reason that this might occur is if you booted PCAT from 
     one drive/path while the PCUNITS.001 file exists in another.   If 
     this is this case, it will be necessary to use the keyword GET so 
     that the units may be established. 


     Why define the Unit Base?

     To begin the process of constructing the material  datafiles,  it 
     is necessary to establish in which unit base you will be working. 
     By defining the unit base,  you will be lowering the potential of 
     entering property data which has not been properly converted. 
     PCAT does not require the user to enter data in a factory 
     predefined set of units but rather in a user predefined  set. 
     Once the units have been defined using the keyword UNITS, all 
     subsequent data records should be entered in a fashion consistent 
     with this definition.  This means that after you have created the 
     first data record,  the unit base should not be changed.   ALL 
     records must have a consistent unit base. 

     For example, if you create a ply record with the mechanical units 
     in PSI, all records must be in PSI.   If you wish to input a ply 
     which is in Pascals,  it must first be converted to PSI.   PCAT 
     does not make conversions.  A separate program called CONVERT is 
     included on the system disks to assist with this type of 
     application. 


     How to Establish the UNIT Base    [UNITS]

     To establish the unit base, enter the keyword UNITS after the 
     Main> prompt.  This keyword may be abbreviated with the first two 
     letters or it may be invoked using the function keys. 

     If done properly, the UNITS command should produce a small 
     narration  and a list of the current units in the  data  window. 
     When no units have been defined, no units will appear.  Simple. 
     



     Where to begin...

     To set the units, it is logical to begin with number one and work 
     down the list.   By pressing key [1], a short menu of available 
     mechanical units will appear.   Choose the unit base which 
     corresponds to the units in which you will be entering your 
     material properties.   Because all menu choices can be  signaled 
     with a single keystroke, PCAT will respond without the <CR>. 

     After all units have been defined, it will be necessary to record 
     your choices on disk.  The drive and path which will be used in 
     the save will be those which existed prior to loading  PCAT.   It 
     should be included that this is true only if you have not changed 
     them using the PCAT keyword DRIVE. 

     Saving the new unit base

     To save the units which appear in the Status Menu,  simply press 
     the [Esc] key.   The filename as well as the drive and path used 
     will be displayed immediately after the [Esc] entry.  When the 
     save is complete, a message will indicate such and PCAT will 
     pause until any key is depressed. 

     This is done so that you will know what has been saved and where.  
     Remember  to save the unit file on the same disk which contains 
     PCAT because one of the first statements in the program  is a 
     call to the procedure which reads the file. 
     



     Manual Read of the UNIT File   [GET]

     In the event you disobey this last suggestion it is possible to 
     "force a read" of the unit file.   Let's consider the example 
     given here: 

          You have created your unit file on a floppy disk,
          which is in the A drive,  but you carelessly booted
          PCAT from a C>  drive default. ie. C>PC  This means
          that PCAT will not find the unit  file  on its first
          attempt because  it  will  be looking in the C> drive.

          Rather than have to exit and restart,  it is  possible
          to read  the  unit  file  with little  effort.  All
          that  is required,  is  to  issue  a DRIVER command  to
          change  the default  to A:\,  or the appropriate
          subdirectory in  which the UNIT file resides,  and then
          enter the  keyword GET.  This  will call the same
          procedure that PCAT used when  the program was started.
          This time however, the read should be successful  given
          that the file actually exists on the  new default.

          Remember that these are two separate keywords.  Enter
          DRIVER <CR> (or use the function key) and set the
          new default.   Then,  after the Main> has been
          returned, the GET should be entered.  Entering Main>
          DRIVER GET will be construed as a DRIVER Command.
     

     CREATING RECORDS - SETTING OUTPUT FILE NAMES

     At this point you are now ready to begin creating core and ply 
     records. 


     Default File Names

     Core and ply records are stored in separate data files each 
     designated with its own unique name.  When PCAT is initialized at 
     start-up the filenames are set automatically.  These filenames 
     are displayed in the opening screen and are referenced as  FILE1 
     and FILE2.   FILE1 is given the name PLYDATA.MAT while FILE2 is 
     called COREDATA.MAT  Which file holds which data should be rather 
     obvious. 

     Before you begin to create any records, you need to decide  if 
     these names are appropriate.  PCAT was designed to hold all plies 
     in one file and all cores in  another.  However, the file size is 
     limited to 50 plies.  This limit was established due not to a 
     PCAT design problem, but more one of disk access time.   Because 
     these are sequential ASCII files, the entire file must be read if 
     you are editing the last record. 
     



     Why use such slow files?

     While this is an obvious disadvantage,  we felt that ASCII files 
     would provide the vital necessity of allowing users to easily 
     manipulate the data with an editor such as PC-WRITE or to allow 
     extension modules to be developed by independent programers. 


     Building Individual Material Files

     Another concept using filenames might be to catalog materials 
     according to manufacturer.  All cores from Hexcel in a HEXCEL.MAT 
     file, all PVC foam cores in a PVCFOAM.MAT file and so on.   Your 
     ply datafiles could be organized in  the same manner;  
     KNYTEX.MAT,  COFAB.MAT,  ORCON.MAT or whatever...   By using this 
     method, you would minimize the number of records in each, thereby 
     reducing your disk access time during edit sessions. 

     This multi-file concept is supported by LAMCON, the laminate 
     stacking program, as the catalog name is kept variable.  In other 
     words, before each create or edit session in LAMCON, a catalog 
     filename is requested. 

     If you decide to use filenames other than the default, you have 
     the option of changing them. 


     Using the Keyword FILE

     This is done by entering  the  keyword FILE or NAME.  This must 
     be done BEFORE a core or ply record is created. 

     A small routine will then help you to install two filenames.  Any 
     valid DOS filename is acceptable.  When this is complete, the new 
     filenames will be posted in the upper right hand corner where the 
     original defaults appeared.   NOTE:  When entering these names,
     you must use a .MAT extension as LAMCON will not read any other 
     type.  PCAT will not automatically add the .MAT extension.

     After the filenames have been set,  it is then possible to begin 
     to create records. 
     



     CREATING RECORDS

     Creating Core Records

     To create a core record, the keyword CORE is entered  at the 
     Main>.   Upon doing so, a prompt will appear to determine whether 
     you wish to create or edit a core record. 

     The first letters of Create and Edit will be highlighted in
     bright white.  This means that in order to choose one or the 
     other, all that is necessary is the stroke of a  single key.  
     Should you stroke any key other than the [C] or the [E],  PCAT 
     will construe this as a request to terminate.   Control will then 
     be returned to the Main> prompt. 

     The Create option...

     After the [C] has been pressed, the command window will then 
     display a new prompt allowing you to begin or escape.  A <CR> 
     is necessary to begin the data entry sequence.   When, on those 
     rare occasions, you make a mistake and wish to escape, this is no 
     sweat as the [Esc] key will magically transport you back to the 
     Main. 

     A <CR> response produces a screen of text items which 
     describes the variables which must be input.   The screen will 
     appear as follows:

     ----------------------------------------------< Active Filenames >
        Core Description:>>                        Ply File> PLYDATA.MAT
        Secondary Text  :                          CoreFile> COREDATA.MAT
                                                   Path> C:\COPAN
        Density:                                         
                                                         
                     Strength        Modulus             
                     --------        -------             
        Comp. >                                          
        Shear >                                          
        Tens. >                                          
                                                         
        Poisson's Ratio:                                 
                                                         
        Cost File:                                       
        Text 1:                                          
        Text 2:                                          
                                                         
     ----------------------------------------------------
     ----------------------------------------------------
                        Core Creation                    
        1>>                                              
     ----------------------------------------------------




     A small blue bracket (for those of you with color) will appear in 
     two places in the create screen.   The bracket in the command 
     window  (with the header CORE CREATE) will be positioned to the 
     left most column and will have a small blinking cursor to its 
     immediate right. 

     Using the entry cursors...

     This of course, means that any characters typed will be returned 
     at this cursor location.   But for which information is PCAT 
     waiting?   The answer can be found by locating the other matching 
     blue bracket in the data window.   This bracket  (called the 
     pointer) will be easy to find as it will be blinking at about the 
     same speed as the cursor.   The text which is on the same line as 
     the pointer is the information for which PCAT is awaiting.   The 
     first item will be the core description, the second will be a 
     secondary description, and third will be core density and so on 
     down the record. 

     To signal to PCAT that you have completed an input line, the 
     <CR> is used to advance to the next data item. 


     Correcting Mistakes

     If an incorrect character is input, the backspace [<--] key is 
     used to remove it.  Each press of the [<--] key will subtract the 
     last character in the string buffer.   After it is subtracted, 
     the cursor is then moved one place to the left.   If the [<--] 
     key is pressed as many times as there are characters in the 
     buffer,  the cursor will continue to move left, and remove old 
     characters from the screen and buffer until it is back at the 
     original starting location.  Additional [<--] entries will do 
     nothing. 


     Backspacing up the record

     Pressing the [Esc] key twice will move the input sequence  back 
     two items and so on.   When the blinker is at the first item (the 
     Primary description), an [Esc] entry will produce the original 
     entry prompt which will allow exit from the record without save.  
     The option to go back into the record will also be available  by 
     pressing the <CR>. 
     



     Previous data preserved by PCAT

     All of the data items that had been entered up to the point 
     where the [Esc] key was first pressed will be preserved.   The 
     blinker can be moved back down the record with multiple  
     <CR>'s.  This  way  data values need not be re-entered just 
     because the blinker is passing by. You should think of the [Esc] 
     key as the [ ] and the <CR> as the [v].   This concept 
     required a few extra lines of code, but we thought it was worth 
     all those saved keystrokes.   (Think how much longer your 
     keyboard will last because of our forethought...what a deal). 


     A SINGLE CORE RECORD

     The following is a brief description of the data items that  make 
     up a single core record. 


     Primary Description

     The first item in a core record is the primary description of the 
     core.   This is any 32 characters that you feel will do the job.   
     This description will be used by LAMCON when prompting you for 
     core selections. 

     If  you  want to include a density designation,  it is suggested 
     that you define this first (ie., 75 ACMEcell rather than ACMEcell 
     75)   The reason for this is that LAMCON will use only a leading 
     portion of the description  in order to maximize the screen 
     display.   

     If more than 32 characters are input,  only the first 32 will  be 
     used.  No error or warning will be issued by PCAT that the string 
     was truncated. 


     Secondary Description

     This is another text line of 32 characters which was originally 
     intended for the name of the manufacturer but what it is actually 
     used for is up to you.   Consider it an extra line to hold 
     whatever data you consider worth holding.   An example of what 
     might go here is the type of core material.  eg. PVC, PU, 
     BALSA... 
     


          
     Density

     This value is to represent the density of the core  material in 
     units as specified with the keyword UNITS. The required units 
     will be displayed in the right hand window of PCAT. 

     
     Compression Values

     The first of the mechanical units in the record is  compression.   
     Strength is entered first, then modulus.  The entries are 
     converted to a scientific format so that they fit evenly on the 
     screen.  These values are usually very easy to obtain from core 
     manufacturers because testing is quick and easy. 
     


     Shear Values

     The second of the mechanical units in the record is shear. 

     Strength is entered first, then modulus.   These values are  also 
     very easy to obtain  from  core manufacturers but the problem 
     then becomes accuracy.  Because the value of a  core is sometimes 
     based on it's shear data, the advertised values may be on the 
     high side.  To be on the safe side, get a few opinions and 
     develop an average. 


     Tension Values

     The last of the mechanical units in the record is tension.  These 
     values are not vitally important because the core material is 
     usually not put into direct tension. 

     Poisson Ratio

     Not much can be said here except that this is a real value.
     
     
     C2BASE Costfile

     This is one of the interesting features of the COPAN/II system.   
     When this package was designed, it was realized by the authors 
     that cost analysis is equally important as strength and stiffness 
     calculations. 
     



     Due to this realization, it is possible to catalog all core costs 
     using the module C2BASE.   This program sets up another text file 
     which holds all costs for a specific file or manufacturer.   Using 
     C2BASE, you build a type of spreadsheet for all densities and 
     thicknesses.   Then, when it's time to analyze costs, it is not 
     necessary to have a current price sheet available.   This is a 
     really nice option for those persons using COPAN/II on the 
     portable/lap machines. 

     If you do not wish to use this feature, there is no need for 
     alarm.  Simply press the <CR> and PCAT will place a flag in 
     the file which means you elected to not use this option. 

     If you do wish to use it,  enter a filename that you will use 
     later to hold cost data.  For example, for a Klegecell core, you 
     might use the name KCELL.  For Divinycell- DCELL and so on. 
     


     Additional Text 1

     Whatever additional information you wish to store with the record 
     is held in the last two data items.   The limitation is 32 
     characters.  If you use more than 32, PCAT will ignore them. 


     Additional Text 2

     Same applies here as above.  Rather than duplicate the  text, 
     please rotate your eyeballs a few degrees up and read  again.  
     Thanks. 

     


     SAVING CORE RECORDS

     When the last data item has been entered into the  record, a 
     message will be displayed in window 2 which indicates the current 
     options.  Here it  is possible to do one of three things: 

                   Options       Key
                   ----------    -----------
                   Save it       [S]
                   Change it     [Esc]
                   Abandon it    [SPACE BAR]
     



     Save [S]

     When a record is saved while in the create mode,  it is  merely 
     appended to the existing datafile.   If one does not exist, then 
     one is created and the record then becomes the first in the file. 

     To record the information, a single press of the [S] key  will 
     write the data to disk.   The name of the file written and where 
     it was written will be displayed.  When the save sequence is 
     complete, the entry prompt will be displayed in the command 
     window.   In addition, all of the information which was on the 
     screen is removed, which gives the appearance of a fresh record 
     waiting for new data.   At this point a <CR> will begin the 
     data entry  sequence again while the [Esc] key terminates CREATE 
     and returns control to the Main> prompt. 


     Change   [Esc]

     If a bad character or value is detected before the [S]  key is 
     pressed, it can be changed by backspacing up the record using the 
     [Esc] key.  Each press of this key causes the blinker to move one 
     field up the record. 

     When the blinker points to the data item which requires  change, 
     key in the new value or string and enter it with a <CR>.   
     The corrected value or character string will be displayed over 
     the old  one.   Make all changes this way using the [Esc] key to 
     move up  the record and the <CR> to move down.   When the 
     changes are complete, keep pressing the <CR> until the 
     blinker moves beyond the last data item.   Don't worry about 
     entering too many <CR>'s, when  you reach the bottom of the 
     record, as additional  <CR>'s have no effect. 

     When the end of the record is reached, these three options  are 
     again presented. 
     

     Abandon      [SPACE BAR]

     If for some reason you do not wish to save the record on disk, it 
     is possible to bypass the disk writing procedure by pressing the 
     [SPACE BAR] once.   Usually if the time is spent to enter the 
     record, it would make sense to save it.  However, it is possible 
     that you may have just finished entering a Klegecell core with a 
     DIAB.MAT  filename waiting in the wings.   Rather than write a 
     record to the wrong file, the [SPACE BAR] can come to the rescue. 
     



     EDITING CORE RECORDS

     To edit a core record, the keyword CORE is entered at the Main>.   
     Upon doing so, a prompt will appear to determine whether you wish 
     to create or edit a core record. 

     As before, the first letters of Create and Edit will be
     highlighted in bright white.   This time, the [E] key is used.

     After [E] has been pressed, the command window will produce a 
     prompt for the record that should be retrieved  from disk.   A 
     small message will also be displayed in the data window reminding 
     you that you must know which record number you wish to edit. 


     Scanning For Records

     Should you forget which record is which, a scan function is 
     available from the Record #>   By entering the letter [S] a scan 
     of all records will be produced on the screen. 


     What is a scan?

     A scan consists of the record # and its primary description.   
     The record data will be output to the screen without pause so if 
     the file contains more than a screenful, it will be  necessary to 
     execute a keyboard interrupt using the [Ctrl]  [S].   By 
     pressing [Ctrl] and then [S] you will cause output to stop.   
     To resume the action, press the [S] key again.   If you need to 
     stop it again, repeat this keyboard sequence.

     If you are not fast enough,  just do another scan by entering the 
     [S] again when the Record #> prompt returns. 

     When the record # is determined, enter it at the Record #> prompt 
     and don't forget the <CR>.  After a slight delay for disk 
     access, the data screen will be replaced with what looks like a 
     new record without data.  Actually, that's not the case.  All of 
     the data  has been read into the memory but they haven't yet been 
     put on the screen. 




     Looking at the existing values...

     To view them, press the <CR>.   Each <CR> will produce 
     one value.   The blinker will show where the next value or string 
     will be placed.   If it is known exactly which data item requires 
     edit, the <CR> should be pressed until the blinker is 
     pointing to it. 

     By typing in the new value and ending with a <CR>,  the new 
     value is placed on the screen.   If too many <CR>'s are 
     entered,  the blinker can be moved backward using the [Esc] key.   
     If this sounds familiar, it's because this is the same routine 
     that was used for CREATE.   Except with CREATE,  the sequence 
     begins with all strings set to null and all values = 0.   Here,  
     the variables are first filled with the record data which was 
     read from  disk.   At the completion of the edit, press the 
     <CR> until the blinker moves beyond the last data item. 

     This will bring back those same three options which allow you to: 

                       Save - Change - Abandon

     For the Change and Abandon,  the same explanations apply as did 
     for the CREATE.   If you're unsure about these you might want to 
     flip back a few pages and refresh your memory. 

     The Save is the same in terms of use.  That is,  all you do  is 
     extend one finger and apply a few ounces of pressure on the [S] 
     key.  PCAT does the rest. 

     What you will then see on the screen is what filename was used 
     and where it was written.   This information is just to keep you 
     informed of where your data was moved to and to confirm that it 
     is where you intended. 


     PCAT does some housecleaning...

     After the primary save is complete, PCAT takes care of a few 
     other details which, for the most part, remain fairly transparent 
     to the user.  The only exception to this transparency is that 
     your edited record now exists at the end of the file even if it 
     was the first one when you began. 

     Because of the nature of sequential files, it is necessary to 
     write the entire file even if only a single record is being 
     changed.   Rather than read the entire file into RAM,  PCAT reads 
     only one record at a time and stops after it has read the 
     requested record #. 
     



     If for example, record #5 in a file of 15, requires edit, the 
     first five files must be read before the edit may begin.   When 
     the edit is complete, the correct data must now be inserted back 
     into the file.  However, because the entire file was not read it 
     is not possible to write this corrected record back into its 
     original location. 

     One too many records...

     So what PCAT does is write the edited record at the end of the 
     file.  But now a problem arises, because two records with the 
     same general information exist with the exception that one is 
     correct and one is not. 

     PCAT must now restack the file to remove the old record so  that 
     the total number of records is equal to the pre-edit level. 


     The .UNM file

     The first action is to rename the appended file as filename.UNM.  
     The .UNM is the file extension which indicates UNModified.   The 
     UNM file will continue to grow with every edit.   This  way a 
     historical  file is maintained which can be used if an old value 
     needs to be reinstated.   PCAT does not use .unm files so if you 
     wish, you may delete it. 

     After the appended file has been renamed with the .UNM extension 
     a new file is written which uses the current  core filename.  
     Before the rewrite begins, a flag is set to the number of the 
     most recently edited record.  The new file is then created using 
     data from the .UNM file.   When the record number in the new file 
     equals the flag,  the write operation pauses while input from the 
     .UNM file  continues.   This effectively skips over the edited 
     record in the .UNM file and continues for the remainder.   The 
     result is that the edited record moves from its original position 
     to the end of the file. 

                       
          COREDATA.MAT      COREDATA.UNM      COREDATA.MAT
               A                 A                  A
               B                 B    Restacked     C
               C      Becomes    C      to ---->    D
               D  ----->         D                  B'
               B'                B'


     This process should not present a problem unless you had  your 
     heart set on memorizing where each record was in the file.  Even 
     this is not a problem as long as you don't edit your materials. 
     



     What happens then?

     When the edited SAVE is complete,  the Record #> prompt will be 
     redisplayed in the command window assuming that another record 
     will be modified.   By entering a valid record #,  the entire 
     process begins again.   If the assumption is not correct,  the 
     Main> can be accessed by entering a null string.   This  complex 
     task involves pressing the <CR> once.   PCAT will respond  
     with "Edit  session  terminated" and will wait for another key to 
     be pressed.   At that time, the screens will clear and PCAT will 
     be ready for the next Main> Keyword. 




     CREATING PLY RECORDS

     Creating a ply record is just as easy as it was with the core.  
     The functions and operation of the two procedures  are nearly 
     identical because the only difference between the two was the 
     actual data being collected and written to disk.   Basically, if 
     you've already created a CORE record, you shouldn't have to read 
     this section. 

     The keyword PLY

     To create a ply record, the keyword PLY is entered  at the Main>.    
     Upon doing so, a prompt will appear to determine whether you wish 
     to create or edit a ply record. 

     Turn back a few pages now if you need additional guidance.  The 
     core create/edit sequence is identical. 

     ----------------------------------------------------
        Ply Description:>>                               
        Secondary Text :                                 
        Resin % by Wgt :                                 
                     STRENGTH              MODULUS       
                    0        90          0        90     
        Tens.                                            
        Comp.                                            
        Shear                                              Data Type : STRING
        Poissons Ratio:       Therm.Exp:                   Max.Length: 32
                                                         
        Laminated Ply Thickness:                         
        Dry Fabric Cost:                                 
        Dry Fabric Weight:                               
                                                         
        Text 1:                                          
        Text 2:                                          
                                                         
     ----------------------------------------------------
                         Ply Creation                    
      (  1) >>                                           
     ----------------------------------------------------
                            The PLY Create Screen
     



     Primary Description

     The first item in a PLYDATA record is the primary description of 
     the ply.   This is any 32 characters that you feel will do the 
     job.   Please do not include any commas in the description as  it 
     will be construed as a delimiter,  which will really screw things 
     up.   This description will be used by the laminate construction 
     program when prompting you for ply selections. 

     If you want to include a weight or style designation,  it is 
     suggested that you define this first (ie., 24 Woven Roving rather 
     than Woven Roving 24)   This is because the laminate construction 
     program will use only a leading portion of the description in 
     order to maximize the screen display.  Not to worry, however 
     because the full description can be invoked but this will require 
     a few additional keystrokes. 

     If  more than 32 characters are input, only the first 32 will be 
     used.  No error or warning will be issued by PCAT that the string 
     was truncated. 

     Secondary Description

     This is another text line of 32 characters which was  originally 
     intended for the name of the manufacturer, but  what it is 
     actually used for is up to you.   An example here would be a note 
     regarding resin matrix used. 

     Resin Content (percentage)

     This represents the percent of resin by weight that the  laminate 
     contains.   This is used by the cost and weight analysis program 
     COSAN for calculations.    This entry  does not affect the 
     mechanical properties of the laminate.  The variable is declared 
     as real so a 45.1 would be acceptable. 


     Tensile Values

     Four real values are required to be input here.  Should you not 
     have all the properties a null string will produce zero.   It is 
     suggested that if you are unable to obtain these values from the 
     material distributor,  contact the manufacturer.   If this is not 
     possible, then estimate a value.  Note: These are laid-up values!

     When the value is entered, it is converted to scientific notation 
     so that it fits on the screen.   The original precision is saved 
     on disk.