POWERPAK
                                 Version  1.0

                       Power Distribution Design Software
                                      for
                   Electric Utility Engineers and Consultants


                                       by
                               George Kwascha, PE
                              copyright 1984, 1985
        












        POWERPAK software has been placed in the public domain for free 
        distribution.  The  programs  are provided on as "as is"  basis 
        without warranty of any kind,  expressed or implied,  including 
        but  not limited to implied warranties of  merchantability  and 
        application  for  a particular purpose.  The user  assumes  all 
        responsibility  for  damages of any sort arising from  the  use 
        and/or application,  direct or indirect,  of PowerPak software. 
        This  software  is  not  a  replacement  for  good  engineering 
        practices.























                               TABLE OF CONTENTS


                                                                  page
        
        Introduction .............................................  3
        System Files .............................................  4

        Preparing Your PowerPak System Disk ......................  5
        Running PowerPak .........................................  5

        General Instructions .....................................  6

        OPTION 1- Conductor Tables ...............................  7

        OPTION 2- Voltage Drop Calculations ......................  9

        OPTION 3- Secondary Fault Current Calculations ........... 11

        OPTION 4- Transformer Tables ............................. 12

        Future Enhancements and Updates .......................... 14

        Software Registration .................................... 15

        Invoice and Feedback Form ................................ 16































                                       2








        
        ------------
        INTRODUCTION
        ------------
        
        PowerPak  has  been designed for use by  the  Electric  Utility 
        Distribution Engineer or Consultanting Engineer with the intent 
        of simplifying basic design calculations necessary in providing 
        electric  utility  service.  This preliminary version  provides 
        tools for secondary voltages calculations. Future versions will 
        support primary voltage circuit calculation tools.

        PowerPak  allows the user to create a set of  parameter  tables 
        for  secondary conductors and transformers.  This set of tables 
        is  utilized  by PowerPak to make calculations easier  for  the 
        user   by   eliminating  the  need  to   constantly   look   up 
        specifications for voltage drop and fault current calculations. 
        PowerPak  allows the user to perform individual voltage drop or 
        fault current calculations or create tabular outputs.  This  is 
        further   discussed   in  the   documentation.   Voltage   drop 
        calculations  can  be  done  with  or  without  motor  starting 
        criteria.  Secondary  fault current calculations can be done at 
        the  point  of  delivery,  whether it  be  at  the  transformer 
        connections or at the end of the service conductor.

        PowerPak  is  menu-driven  for ease of use  with  user  prompts 
        highlighted  at the bottom of each screen.  All data is entered 
        on  formated  screens.  PowerPak is designed to be run  from  a 
        single  floppy  system with a minimum of 64K of memory  with  a 
        color/graphics adaptor.



























                                       3








        
        ------------
        SYSTEM FILES
        ------------
        
        PowerPak  is configured to run self-contained on a floppy disk. 
        The floppy disk can reside in either drive and the program will 
        function properly as long as the resident drive is the  default 
        drive.  PowerPak  can also be operated from a hard disk as long 
        as  all  files  are  in the same  sub-directory  and  the  sub-
        directory is the default directory.

        The following files come with the PowerPak 1.0 disk:

        README       - initial instruction & help file
        POWERPAK.DOC - program documentation in ASCII format
        POWERPAK.TXT - program documentation in WordStar format

        POWERPAK.COM - main control and loading module
        MAINMENU.CHN - main menu

        CABLSPEC.CHN - secondary conductor data table access program
        TXSPECS.CHN  - transformer data table access program

        SECVDROP.CHN - secondary voltage drop loading program
        CABLDROP.CHN - secondary conductor voltage drop calculator
        TXDROP.CHN   - transformer voltage drop calculator
        CABLMOTR.CHN - secondary conductor voltage drop with motor
                       starting calculation
        TXMOTR.CHN   - transformer voltage drop with motor starting
                       calculation
        STLTDROP.CHN - street light design voltage drop calculator
        STLIGHT.PIC  - street light calculator input screen

        CABLE.DAT    - secondary conductor data file
        TRANSF.DAT   - transformer data file


        It  is  recommended  that  the user  format  a  new  disk  with 
        operating  system and then transfer all the above files to this 
        new disk before using the program. Store your original PowerPak 
        disk in a safe place.















                                       4








        
        -----------------------------------
        PREPARING YOUR POWERPAK SYSTEM DISK
        -----------------------------------
        
        The  first  step  in preparing your  PowerPak  system  disk  is 
        formatting  a new disk.  Please follow instructions in your DOS 
        manual, if you are not already familiar with this procedure. Be 
        sure to format this new disk with the   /S  option.  This  will 
        also  transfer the DOS system onto your new disk.  With the DOS 
        system  on  your disk,  you will be able to  boot  your  system 
        directly from the PowerPak disk.

        The  next step in this process is to tranfer all PowerPak files 
        to your newly formatted disk.  Again,  refer to your DOS manual 
        if you are not familiar with this procedure. Using the COPY *.* 
        command is recommended.

        For your information,  the original PowerPak disk comes on an 8 
        sector formatted disk to allow compatibility with all  versions 
        of DOS. The disk is double-sided.


        
        ----------------
        RUNNING POWERPAK
        ----------------
        
        To  start  PowerPak,  simply type POWERPAK from the A>  prompt. 
        Note that your PowerPak disk must be in drive A: throughout the 
        duration of your session.

        You  may wish to create a Batch file or and AUTOEXEC.BAT  file. 
        Refer  to  your DOS manual if you are not familiar  with  batch 
        files.  When creating a batch file,  simply include POWERPAK as 
        your last command.





















                                       5








        
        --------------------
        GENERAL INSTRUCTIONS
        --------------------
        
        1.  All  menus require single keystroke entry when choosing  an 
        option. Options are numbered anywhere from 0 to 9.

        2.  Except for the Main Menu,  all single keystroke options are 
        bracketed with {  } on menu screens.

        3.  There  are several standard prompts that will appear at the 
        bottom of the screen:

        Field  {#} - hit the appropriate number that  corresponds  with 
        the field that you wish to correct.

               {+} - hitting  the  plus sign will increment the  record 
        forward by one.

               {-} - hitting  the minus sign will increment the  record 
        backwards by one.

               {M} - hitting  the  "M"  key  will  return  you  to  the 
        previous menu.

               {E} - hitting  the "E"  key will allow you  to  view  or 
        print the entire file.

               {P} - hitting  the "P" key will specify that any  output 
        be redirected to the printer.

               {S} - hitting  the "S" key will specify that any  output 
        be directed to the screen.

           {space} - hitting the space bar will scroll window data.

          {RETURN} - hitting  the Return or Enter key will perform  the 
        action specified in the prompt.  These will vary from screen to 
        screen.

        4.  Hitting the {ESC} key from most prompts in the program will 
        return you to the previous menu.

        5.  The  only other type of data entry prompt is found  in  the 
        conductor  and transformer data files,  where the  --->  prompt 
        asks you to enter a code.  Since this code can be more than one 
        character in length,  it will be necessary for you to terminate 
        your entry by hitting the RETURN or ENTER key.

        6. Use {SHIFT} + {PrtSc} to dump screen results to your printer.






                                       6








        
        -------------------------------------
        MAIN MENU OPTION 1 - CONDUCTOR TABLES
        -------------------------------------
        
        The  Conductor  Data file can be accessed by choosing option  1 
        from  the  Main Menu.  You will be presented with a  menu  that 
        allows you to Add,  Edit,  Delete and Print/View your conductor 
        records.

        A sample data file is provided on the disk.  If your conductors 
        do  not match the ones specified in this sample file,  you  may 
        change the appropriate conductors one by one or you may  delete 
        the  CABLE.DAT  file and start your own file.  The Edit  option 
        allows you to change data in each record. The Add option allows 
        you to add records to the file. If the file does not exist, the 
        Add option will create the file automatically.  Option 4 is not 
        functional at this time.

        
        {1} ADD CONDUCTOR DATA
        
        When  this  option is chosen you will be presented with a  data 
        input  screen that allows you to enter the following  conductor 
        parameters:

        Conductor Code- a unique code assigned by the user.  This  code 
        can  be up to 3 characters in length,  comprised of numbers  or 
        letters.  It  is used to retrieve conductor data records.  This 
        value is treated as a string variable.

        Cable Type- 20 spaces are provided for the user to describe the 
        type of conductor.

        Phase Conductor Size-   9 spaces are provided for the  user  to 
        record the size of the phase conductor.

        Rated Amps-  3 spaces are provided to denote the rated  current 
        carrying capacity of your cable.

        Phase Cond Resistance-  specify the phase conductor  resistance 
        value in ohms/1000 feet. 6 spaces are provided.

        Phase Cond Reactance-   specify the phase  conductor  reactance 
        value in ohms/1000 feet. 6 spaces are provided.

        Neutral Conductor Size-  9 spaces are provided for the user  to 
        record  the size of the neutral conductor.  If the size is  the 
        same as the phase conductor, just hit the RETURN key.

        Neutral Cond Resistance-   specify neutral conductor resistance
        value in ohms/1000 feet.  6 spaces are provided.  If this value 
        is the same as the phase conductor, just hit the RETURN key.





                                       7








        Neutral  Cond Reactance-  specify neutral  conductor  reactance 
        value in ohms/1000 feet. If this value is the same as the phase 
        conductor, just hit the RETURN key.

        
        {2} EDIT CONDUCTOR DATA
        
        When  this  option  is  chosen you will  be  prompted  for  the 
        conductor code that you wish to edit or you can scroll the file 
        forward   or  backward  by  hitting  the  plus  and  minus  key 
        respectively.  When  you wish to edit a field on the  displayed 
        screen,  type  the number of the field and then  re-enter  your 
        data.

        
        {3} DELETE CONDUCTOR DATA
        
        When  this  option  is  chosen you will  be  prompted  for  the 
        conductor code that you wish to delete.

        The  Delete  option does not actually delete  the  record.  Any 
        record that is deleted by the user is only marked for deletion. 
        The next record that is added is written into the record  space 
        of your deleted record.

        
        {5} PRINT/VIEW CONDUCTOR RECORDS
        
        When this option is chosen you will be prompted for a conductor 
        code.  If you type a plus sign, the records will be scrolled on 
        the  screen.  Typing the letter "E" specifies the entire  file. 
        When specifying the entire file,  you will also be prompted for 
        screen or printer output.
        
        {6} RETURN TO MAIN MENU
        
        This option returns you to the Main Menu.




















                                       8








        
        --------------------------------
        MAIN MENU OPTION 2- VOLTAGE DROP
        --------------------------------
        
        The  Voltage  Drop  calculation  option is  comprised  of  five 
        different types of calculations.

        {1} Service Cable Voltage Drop- calculates the voltage drop  on 
        secondary  conductors  under  normal  loading  conditions.  The 
        conductors must be in the conductor data file.
           
        {2} Transformer Voltage Drop-  calculates  the voltage drop  in 
        the  transformer  core under normal  loading  conditions.  This 
        value should be added to the service cable voltage drop to  get 
        the  total drop seen by the associated load.  The  transformers 
        must be in the data file.


        The two sections above have the same basic screen input design. 
        A sub-menu will allow you to choose whether you wish to perform 
        one calculation for a particular situation or whether you  wish 
        to  create a set of voltage drop tables for various parameters. 
        The  table  creation feature is a very  valuable  feature  that 
        allows you set up a complete set of tables for each transformer 
        and conductor with different ranges of footage and load.

        The  single calculation option will prompt you for a  conductor 
        or transformer code by displaying a window of the data file and 
        allowing  you  to  scroll through the file searching  for  your 
        conductor or transformer. You will be prompted for power factor 
        and  load values.  The conductor calculation will also  require 
        the  entry  of the number of  phases,  voltage,  and  conductor 
        length  in  feet.  It will also ask you to  specify  single  or 
        parallel conductors.

        The cable option will calculate the line-to-neutral and line-to 
        line voltage drop in volts and percent.  The transformer option 
        will  calculate the voltage drop in percent for the given  load 
        and  for full load.  The full load value can be used as a worst 
        case   value  if  there  are  other  loads  connected  to   the 
        transformer.

        The   respective  table  calculation  option  will  need   some 
        additional  values.  The cable option will requires a  starting 
        load value with an increment. For example, if you wish to start 
        your table at 10 KW and increment it by 5 KW, you would specify 
        the starting load at 10 KW and load increment at 5  KW.  Values 
        for  starting  length and length of increment in feet are  also 
        needed.  The transformer option only requires the starting load 
        and load increment values.


        {3} Cable Voltage Drop for  Motor Starting-   calculates  the 
        voltage  drop associated with motor starting only.



                                       9









        {4} Transformer Voltage Drop for Motor Starting- calculates the 
        voltage  drop associated with motor starting only.  This  value 
        may be added to the Cable Motor Starting value to get the total 
        drop due to starting motors.


        The two sections above have the same basic screen input design 
        as  the voltage drop calculations without motor  starting.  The 
        only  additional  parameter needed is a value for the  starting 
        amps of the motor or motors.  This value is usually a nameplate 
        value  called locked-rotor amps.  An approximate value  of  six 
        times the normal current can also be used.


        {5}  Street Light Voltage Drop- a specialized section  designed 
        to calculate voltage drops for street light design.

        This  option  presents you with a graphic representation  of  a 
        street  light circuit,  showing cable impedance  and  luminaire 
        locations.  A  table allowing input of footage,  conductor code 
        and number of luminaires at each point is displayed.  Enter the 
        secondary voltage at the prompt.  Enter the load per  luminaire 
        next.  This  program assumes that all luminaires in use are the 
        same.  Enter the luminaire load value in VA, not KVA! Next, the 
        program will allow you to scroll through the conductor file  to 
        pick  out  your  cable size.  Enter the conductor code  of  the 
        segment  in  column  one.   Enter the number of  feet  in  each 
        segment  in the second column.  The third column  requests  the 
        number  of  luminaires  that are connected at  that  point  and 
        beyond. For example, if one luminaire is connected at points 1, 
        2,  and  3,  then you specify 3 luminaires at point 0 to 1.  At 
        point 1 to 2 you specify 2 luminaires and 1 luminaire at  point 
        2 to 3.

        After  the  entry  of  each  line  segment,  the  program  will 
        calculate  and display the voltage drop,  the actual voltage at 
        that end point, and the total percent drop at the end point.

        A suggestion ...  if you have more than 10 luminaires,  you can 
        combine  cable segments and luminaires into one point near  the 
        voltage  source.  In this manner you will still be able to  get 
        the voltage drop values toward the end of the circuit.














                                      10








        
        ----------------------------------
        MAIN MENU OPTION 3 - FAULT CURRENT
        ----------------------------------
        
        Option 3 will allow you to perform secondary fault caluclations 
        with ease. You can make single calculations or create tables of 
        fault  currents  for each type of conductor in the  data  file. 
        This  is  done  in  much the same manner as  described  in  the 
        Voltage Drop sections.

        You  will  need to specify a transformer code and  an  optional 
        conductor code and conductor length.  This is done in the  same 
        manner  as  described  in the previous  sections  by  scrolling 
        through the data files in the window displays. If a fault value 
        is needed at the transformer spades only, then a conductor code 
        should not be entered. If a conductor code is entered, then you 
        must  specify  a conductor length of zero feet,  otherwise  the 
        calculation will include the secondary conductor and the  fault 
        current value given, will be at the end of the conductor.

        A  table  of  fault currents is  generated  for  conductors  of 
        various  lengths only,  with a particular transformer  type.  A 
        table  of  various transformers cannot be  generated.  Use  the 
        single calculation option to do this.
































                                      11








        
        ---------------------------------------
        MAIN MENU OPTION 4 - TRANSFORMER TABLES
        ---------------------------------------
        
        The Transformer Data file can be accessed by choosing option  4 
        from  the  Main Menu.  You will be presented with a  menu  that 
        allows you to Add,  Edit,  Delete and Print/View your conductor 
        records.

        A sample data file is provided on the disk.  If your conductors 
        do  not match the ones specified in this sample file,  you  may 
        change the appropriate conductors one by one or you may  delete 
        the TRANSF.DAT  file and start your own file.  The Edit  option 
        allows you to change data in each record. The Add option allows 
        you to add records to the file. If the file does not exist, the 
        Add option will create the file automatically.  Option 4 is not 
        functional at this time.

        
        {1} ADD TRAMSFORMER DATA
        
        When  this  option is chosen you will be presented with a  data 
        input screen that allows you to enter the following transformer 
        parameters:

        Transformer Code- a unique code assigned by the user. This code 
        can  be up to 3 characters in length,  comprised of numbers  or 
        letters.  It is used to retrieve transformer data records. This 
        value is treated as a string variable.

        Transformer  #- 5 spaces are provided for a transformer  number 
        if necessary.

        Transformer  Type- 20  spaces  are provided  for  the  user  to 
        describe the type of transformer, ie. aerial or pad-mounted.

        #  phases- specify "1" for single phase or "3" for three  phase 
        transformers.

        TX  Size (KVA)- 4 spaces are provided to record the transformer 
        KVA.

        TX  Impedance  (%)- 5 spaces are provided for  the  transformer 
        impedance value in percent.

        Nameplate Voltage Rating- 32 spaces are provided to record  the 
        nameplate voltage information.

        Secondary  Volts  (line-line)- record the secondary voltage  in 
        volts.  5 spaces are provided.  Line-to-line or  phase-to-phase 
        voltage must be used. This value is used in the calculations.

        Total  Losses  (Watts)- 5  spaces  are provided  to  enter  the 
        transformer  total full load losses expressed  in  watts.  This 



                                      12








        value includes no load core loss and full load copper loss.

        No  Load  Loasses (Watts)- 5 spaces are provided to  enter  the 
        transformer no load core loss in Watts.

        
        {2} EDIT TRAMSFORMER DATA
        
        When  this  option  is  chosen you will  be  prompted  for  the 
        transformer  code  that you wish to edit or you can scroll  the 
        file  forward  or backward by hitting the plus  and  minus  key 
        respectively.  When  you wish to edit a field on the  displayed 
        screen,  type  the  number of the field and then re-enter  your 
        data.

        
        {3} DELETE TRANSFORMER DATA
        
        When  this  option  is  chosen you will  be  prompted  for  the 
        transformer code that you wish to delete.

        The  Delete  option does not actually delete  the  record.  Any 
        record that is deleted by the user is only marked for deletion. 
        The next record that is added is written into the record  space 
        of your deleted record.

        
        {5} PRINT/VIEW TRANSFORMER RECORDS
        
        When  this  option  is  chosen  you  will  be  prompted  for  a 
        transformer code.  If you type a plus sign, the records will be 
        scrolled  on the screen.  Typing the letter "E"  specifies  the 
        entire file.  When specifying the entire file, you will also be 
        prompted for screen or printer output.
        
        {6} RETURN TO MAIN MENU
        
        This option returns you to the Main Menu.



















                                      13








        
        -------------------------------
        FUTURE ENHANCEMENTS AND UPDATES
        -------------------------------
        
        PowerPak   is  distributed  under  a  modified   user-supported 
        shareware  concept.  Please read the following statement  under 
        software registration for a complete explanation. The author is 
        relying  on  the  users  of PowerPak to  make  suggestions  for 
        improvements and enhancements that they would like to see.

        The author will notify all registered users any time  revisions 
        are  made to PowerPak.  Registered users may then obtain a copy 
        of the updated disk for a $5.00 fee (subject to  change).  This 
        fee  is to cover the cost of disk media,  postage and handling. 
        The  user  may  also choose to send a blank  disk  with  proper 
        enclosed  return  postage  for a free updated  copy.  The  disk 
        mailer must be re-usable.

        The author has spent a great deal of his own time writing  this 
        program,  with hopes of benefiting from user contributions. The 
        software  availability  of  good inexpensive  programs  in  the 
        electric  utility  area is limited.  PowerPak is an attempt  to 
        change  this.  With  your  help  and  support,  maybe,  we  can 
        encourage  other engineers to write and release their  programs 
        to  the  realm  of User-Supported  Shareware.  Help  make  this 
        experiemnt a success and send a donation.

        If  you  have written useful engineering software and  wish  to 
        participate in this experiment please let us know.  Wordstar is 
        a registered trademark of MicroPro International.


























                                      14








        
        ---------------------
        SOFTWARE REGISTRATION
        ---------------------
        
        PowerPak  is  distributed  under  a  modified  version  of  the 
        shareware  concept.  PowerPak  has been released to the  public 
        domain for free distribution.  Users are encouraged to copy the 
        program for use by others. This includes use by individuals and 
        companies.  This  program  may  not  be  sold  without  written 
        permission  of  the  author,  with  one  exception.  Non-profit 
        organizations,   such  as  computer  clubs,   user-groups   and 
        electronic bulletin boards may sell this software as long as it 
        is for no more than $6.00. Source code is not available.

        The  author  will  support  PowerPak  users  for  a  one   time 
        contribution of $10.00. Support includes notification of future 
        updates,  corrections  of any "bugs" in the software,  and  any 
        relevant  written correspondence that requires a written reply. 
        All users,  however,  are encouraged to supply the author  with 
        any  suggestions  for future improvements to this software  and 
        any  other comments that do not require a written reply by  the 
        author. The author will not supply copies of PowerPak without a 
        contribution of $10.00 for user-support and an additional $5.00 
        for  postage,  handling  and disk media.  Free copies  of  this 
        software can be obtained from your colleagues,  computer clubs, 
        user groups or electronic bulletin boards. If you have obtained 
        a  free  copy of this software and wish to  register  with  the 
        author please send your contribution of $10.00 only. Please use 
        the attached invoice form for all correspondence.



























                                      15








        
        ------------------------------
        INVOICE AND USER FEEDBACK FORM
        ------------------------------
        


        Name: __________________________________________

        Company: _______________________________________

        Address: _______________________________________

        City: ________________ State: ____ Zip: ________



        ===============================================================
        Item Description                          | Price Ea |   Price
        ===============================================================
                                                  |          |
        PowerPak 1.0 Registration fee             |  $10.00  |  $     
                                                  |          |
        PowerPak 1.0 software on 5" disk          |  $ 5.00  |  $     
         postage included                         |          |
        -----------------------------------------------------|---------
                                         Total               |      
        ===============================================================

        Make checks payable to: Information Management Solutions, Inc

                       Send To: Information Management Solutions, Inc
                                P.O. Box 13263    Durham, N.C.  27709

         
        List  any  comments or suggestions for future  improvements  to 
        PowerPak below. Use reverse side if necessary. Your interest is 
        appreciated.



















                                      16







rest i