1


                       VAPOR-LIQUID ACTIVITY COEFFICIENTS
                                        
               ESTIMATED BY THE  UNIFAC GROUP CONTRIBUTION METHOD
                                        
                          Pete Goffinet -- January 1987
                                        
                                        
        INTRODUCTION

                 These MSDOS programs provide an estimation of vapor-
        liquid activity coefficients by the UNIFAC group contribution
        method for a system of up to ten components, each formed from a
        maximum of ten different subgroups.  Recently published group
        interaction parameters and subgroup constants (1985) are supplied
        and are automatically loaded and accessed by the program.

                 The following files are included on the distribution
        disk:
             
             UNIFAC.EXE   Compiled UNIFAC Program with Printer Output
             UNIFACS.EXE  Compiled UNIFAC Program with Screen Output
             UFR2.DTA     Sub Group Rk Constants
             UFQ2.DTA     Sub Group Qk Constants
             UFA2.DTA     Main Group Interaction Parameters
             UFN2$3.DTA   Sub Group Names
             UFN1$3.DTA   Main Group Names
             UFC92.DTA    Main Group Numbering File
             UFCC92.DTA   Sub Group Numbering File
             UNIFAC.DOC   Documentation (TYPE to screen or printer)
             README.1ST   Brief Instructions for UNIFAC.DOC

                 Documentation is not meant to be tutorial in scope, and
        familiarity with the procedure for using the UNIFAC method is
        assumed.  Articles by Gmehling, Rasmussen, and Fredenslund and
        the text by Reid, Prausnitz, and Sherwood (1) are particularly
        recommended for detailed information.  Since various tables of
        constants have been published, it is important to check group and
        subgroup structures with the identification table provided by
        these programs to insure that consistent structure identification
        numbers are assigned.

                 Program operation is controlled by the function keys F1
        through F6.  Each input is prompted, and provisions for error
        checking have been included.  Improper entries are signaled and
        re-entry is prompted.  Each group of entries is displayed or
        printed depending on the program selected and may be checked and
        re-entered if mistakes are detected.

                 Because of the number of iteration loops involved,
        calculation of activity coefficients may routinely require from
        several seconds to more than one minute depending on the number
        of components and the number of different groups composing each
        component.










                                        2


                 Since one of the principal uses of this program is to
        estimate infinite dilution activity coefficients for binary pairs
        to be used in determining constants in less complex equilibrium
        correlations, entering concentrations of "0" and "1.0" for the
        first component of a binary pair sets minimal concentrations for
        such an estimation.

        OPERATING INSTRUCTIONS

                 A disc containing the selected program version and all
        the data files should be inserted in the default drive or made
        the default directory of a hard disk drive. The program is
        initiated by entering UNIFAC or UNIFACS at the operating system
        prompt.  The data files will be loaded automatically, and the
        introductory screen which labels the function keys F1 through F6
        will be displayed.  If the program directing output to the screen
        is selected, intermediate screens may be difficult to read
        because the pause key is not recognized during program execution.

                 F1 - The group and subgroup identification list can be
        displayed or printed depending on the selected program by keying
        F1 whenever the function keys are active.

                 F2 - Input of component information is begun by keying
        F2.  For initial data entry, keys F2 through F4 should be
        employed in sequence.  After data have been entered, changes can
        be input by keying the appropriate function key.  The requested
        component names are arbitrary and limited to a maximum of twelve
        characters.  They are used for identification purposes only.  For
        each component, entry of the subgroup numbers making up its
        structure and their frequency of occurrence is next prompted.
        Entry of subgroups for each component is terminated by entering
        "0,0".  Entry of components is in turn concluded by keying ENTER
        without a component name.  Logically incorrect entries result in
        an error message and a re-entry prompt.

                 After all component data are entered, a summary of the
        input together with the appropriate subgroup constants and main
        group interaction parameters to be used in estimating
        coefficients is listed, and verification is requested.  "Y"
        should be entered if corrections are needed or "N" if input is
        correct.  Any entry other than "Y" is interpreted as a no.  If
        this information is displayed, it may be examined using the CTRL
        Num Lock keys if necessary as described above.



















                                        3


                    *************** NOTE WELL ***************

                 Since interaction parameters have not been determined
        for all pairs of main structural groups, an interaction parameter
        of zero for an unlike pair may mean that the value is unavailable
        and that "ideal" interaction will be assumed.  In such cases,
        Table I should be checked to determine whether the value is in
        fact zero or unavailable and assumed ideal.  The worth of the
        calculated activity coefficients should be judged accordingly.

                    *************** NOTE WELL ***************

                 F3 - Entry of concentration data for each component is
        initiated by keying F3.  Concentrations are entered in mole
        fraction units.  Entry of "0" for the first component of a binary
        pair sets its concentration to 10E-6 mole fraction for
        calculation of its "infinite dilution" activity coefficient.
        Entry of "1.0" sets the concentration of the second component to
        10E-6 for the same calculation.  An entry greater than unity
        results in an error message and a re-entry prompt.  After data
        for all but the last component are entered, its concentration is
        calculated by difference, and the input composition is displayed
        or printed for verification. The last component should be checked
        for a negative value indicative of an input error.

                 F4 - Temperature in degrees Celsius is input by keying
        F4.

                 F5 - Calculation of activity coefficients is begun by
        keying F5, and the result is displayed or printed together with
        temperature and composition.  Coefficients at other temperatures
        and concentrations can be determined by entering new data with
        keys F3 and F4.  Components can be changed by keying F3.

                 F6 - Keying F6 returns control to the operating system.


        

























                                        4


                                     TABLE I
                                        
                        MAIN GROUP INTERACTION PARAMETERS
                                        
                                   x Available
                                 o Not Available

        No.
         2   x
         3   x  x
         4   x  x  x
         5   x  x  x  x
         6   x  x  x  x  x
         7   x  x  x  x  x  x
         8   x  x  x  x  x  x  x
         9   x  x  x  x  x  x  x  x
        10   x  x  x  x  x  x  x  o  x
        11   x  x  x  x  x  x  x  x  x  x
        12   x  x  x  x  x  x  o  o  x  x  x
        13   x  x  x  x  x  x  x  o  x  x  x  o
        14   x  x  x  o  x  x  x  o  o  o  o  o  o
        15   x  x  x  x  x  x  x  o  o  o  x  o  x  x
        16   x  x  x  x  x  x  x  o  x  o  o  o  o  x  x
        17   x  x  x  x  x  x  x  x  x  o  x  o  o  x  o  o
        18   x  o  x  x  x  x  x  x  x  o  o  o  o  o  o  o  o
        19   x  x  x  x  x  x  x  o  x  o  x  o  x  o  o  o  x  x
        20   x  x  x  x  x  x  x  o  x  o  x  x  x  o  o  o  o  x  o
        21   x  x  x  x  x  x  x  o  x  x  x  o  x  o  o  o  x  o  x  x
        22   x  x  x  x  x  x  x  o  x  o  x  o  x  o  o  x  o  x  x  x
        23   x  x  x  x  x  x  x  o  x  x  x  x  x  o  o  x  o  x  x  x
        24   x  x  x  x  x  x  x  x  x  o  x  x  x  x  x  x  x  x  x  x
        25   x  x  x  x  x  x  x  o  x  o  x  o  x  x  x  x  x  o  x  o
        26   x  x  x  x  x  x  x  o  x  o  x  o  x  o  o  o  o  o  x  o
        27   x  o  x  x  x  o  x  o  o  o  o  o  o  o  o  o  x  o  o  o
        28   x  x  x  x  x  x  x  o  x  o  x  o  x  o  o  o  o  o  x  o
        29   x  o  x  o  x  x  o  o  x  o  o  x  x  x  o  o  o  o  x  o
        30   x  o  x  x  x  o  x  o  x  o  x  o  o  o  o  o  o  o  o  o
        31   x  o  x  x  x  o  x  x  o  o  x  o  x  o  o  o  x  o  o  o
        32   x  o  x  o  x  o  o  o  x  o  x  o  x  o  o  o  o  o  o  o
        33   x  o  x  x  x  x  o  o  x  o  x  o  x  o  o  o  o  o  o  x
        34   x  x  o  o  o  o  o  o  x  o  o  o  o  o  o  o  o  o  x  o
        35   x  x  x  x  x  x  x  o  x  o  x  o  x  o  o  o  o  o  o  o
        36   x  o  o  o  o  o  x  o  o  o  x  o  o  o  o  o  o  o  x  o
        37   x  x  x  o  x  x  o  o  x  o  x  o  x  o  o  o  o  o  x  x
        38   x  o  x  x  x  x  o  o  o  o  o  o  x  o  o  x  o  o  o  o
        39   x  x  x  x  x  x  x  o  x  o  o  o  x  o  o  o  x  o  o  o
        40   x  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o
        41   x  x  x  x  x  x  x  x  x  o  x  x  x  o  x  o  x  o  x  x
        42   x  o  x  o  x  o  o  o  x  o  o  o  o  o  o  o  o  o  o  o
        43   x  o  x  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o
        44   x  o  x  x  x  o  x  o  o  o  o  o  o  o  o  o  o  o  o  o
        
        No.  1  2  3  4  5  6  7  8  9 10 11 12 13 14 15 16 17 18 19 20
        









                                        5



        No.
        22   x
        23   x  x
        24   x  x  x
        25   x  o  o  x
        26   x  o  o  x  x
        27   o  o  o  x  o  x
        28   x  o  x  x  o  o  o
        29   x  o  o  o  o  o  o  o
        30   o  o  x  x  o  o  o  o  o
        31   o  o  o  o  o  x  o  o  o  o
        32   o  x  x  x  o  x  o  o  o  o  o
        33   x  o  o  x  x  x  o  o  o  o  o  o
        34   o  o  o  o  o  x  o  o  o  o  o  o  o
        35   o  x  x  x  o  o  o  o  x  o  x  o  o  o
        36   o  o  o  x  o  o  o  o  o  o  o  o  o  o  o
        37   x  o  x  x  o  x  o  x  o  o  o  o  o  o  o  o
        38   o  o  o  x  o  o  o  o  o  o  o  o  o  o  o  o  o
        39   o  o  o  x  o  o  o  o  x  o  x  o  o  x  x  o  o  o
        40   o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  x  o
        41   x  x  x  x  x  x  o  x  o  o  o  x  o  o  x  x  x  o  o  o
        42   o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o
        43   o  o  o  x  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o
        44   o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o  o

        No. 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40


        No.
        42   o
        43   o  x
        44   o  o  o

        No. 41 42 43

        Program and documentation copyright 1984, 1986, 1987
        Edward P. Goffinet, Jr., Wilmington, Delaware

        REFERENCE

        (1) Robert C. Reid, John M. Prausnitz, and Thomas K. Sherwood
        "The Properties of Gases and Liquids", 3rd Edition, McGraw-Hill,
        New York, 1977.


















         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,000+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                      (713) 721-6104 or (713) 721-5205