FFT-256 Documentation
   
                  Copyright 1991 by Harry Garland, Ph.D.


   1) Introduction
   
   FFT-256 is a software package that makes it easy for you to find the
   spectral content (i.e. the sine wave or "Fourier" components) of a
   waveform or set of data.  The program achieves this by taking 
   the 256-point Fast Fourier Transform (FFT) of your waveform or data.
   This determines the amplitude and phase of 128 sinusoidal waves
   that, when added together, exactly match your original data or waveform.

   Both the amplitude and phase of these 128 Fourier components can be 
   displayed at your console.  You can also list the amplitude
   and phase of these components to your printer or to a disk file.

   To illustrate graphically that the 128 Fourier waves do indeed sum to
   your original waveform, you can invoke the "Synthesize" option
   to watch your waveform materialize as the 128 Fourier components 
   are added together.
   
   There are seven files in this package:

                   FFT256.exe      The main program
                   FFT256.doc      This documentation file
                   Wave1.wve       Example waveform #1
                   Wave2.wve       Example waveform #2
                   Wave3.wve       Example waveform #3
                   Wave4.wve       Example waveform #4
                   Wave5.wve       Example waveform #5

   
   2) Example waveforms

   To view the example waveforms, press 1 from the Main Menu to "Begin
   program."  From the Program Menu press 3 to select "Disk file."  To
   select Wave1.wve simply type Wave1 followed by a carriage return.  
   The waveform will then be displayed on the screen.
   
   Each of the five example waveforms is described below:

   
   2.1) Wave1

   Wave1 is a waveform described by the formula y = sin (2*pi*16*t/256).
   After selecting this waveform you can view its spectral content by 
   pressing "F" to perform the FFT.  From the spectral plot you can see 
   that there is a single sine wave component, representing the 16th
   harmonic of the fundamental.  The fundamental frequency is defined
   here as the frequency corresponding to one cycle over 256 samples.
   The 16th harmonic then has 16 cycles over the 256 samples.  In 
   general the formula for harmonic number "h" is given by
   sin (2*pi*h*t/256).

   While viewing the amplitude spectrum you can press P to view the
   phase or "shift" of each of the spectral components relative to
   a cosine wave.  Notice that the 16th harmonic is shifted by 90
   degrees.  This is because there is a 90 degree phase difference
   between a sine wave and a cosine wave.

   
   2.2) Wave2

   Wave2 is designed to illustrate the superposition or addition of
   sinusoidal waveforms.  Wave2 is defined by the formula:

       (1/2) * sin(2*pi*16*t/256) + (-1/2) * cos(2*pi*32*t/256)

   After loading this waveform, press F to take the FFT and view the
   spectrum.  Notice that both the 16th harmonic and the 32nd harmonic
   appear in the Fourier amplitude spectrum.  Press P to view the 
   phase angles of the Fourier components.  The 16th harmonic is a
   pure sine wave with a 90 degree phase shift.  The 32nd harmonic has 
   a 180 degree phase shift because the cosine component of the waveform
   is multiplied by a negative number.
   
   Wave2 is a composite waveform formed by the superposition of two 
   component waveforms that interact to produce a more complicated 
   waveform.  The FFT, however, effectively resolves this complexity 
   and successfully extracts the two component waveforms from the 
   composite waveform.


   2.3) Wave3

   Wave3 illustrates the effect of multiplying two sinusoidal waveforms.
   This waveform is defined by the formula:

              y = cos(2*pi*64*t/256) * sin(2*pi*60*t/256)

   In taking the FFT of this waveform there is a surprise!  Even though
   we are multiplying the 64th harmonic by the 60th harmonic, NEITHER
   of these harmonics appear in the resultant spectrum!  Instead we have
   the sum and the difference frequencies (sometimes called the sidebands.)
   The amplitude of each of these is just half that of the original waves.

   Notice also the phase of these two components (by pressing P while
   viewing the amplitude spectrum.)  The 4th harmonic is shifted -90 degrees
   from a cosine wave (i.e. it is the negative of a sine wave) and the
   124th harmonic is shifted 90 degrees from a cosine wave (i.e. it is
   a sine wave.)  In other words the mathematical expression for our
   original wave, namely:

               y = cos(2*pi*64*t/256) * sin(2*pi*60*t/256) 

   is mathematically the same as:

              = .5 * sin(2*pi*124*t/256) - .5 * sin(2*pi*4*t/256)

   and in fact this identity can be proven true from trigonometry.
   It is always amazing to me that the Fourier transform somehow
   "knows" the trig identities!
   

   2.4) Wave4

   Wave4 is a pulse waveform.  Because of the symmetry of this pulse, it 
   is composed of only cosine wave components (i.e. the phase of each
   component is either 0 degrees or 180 degrees.)  Notice the undulating 
   pattern of harmonics so typical of the pulse waveform (the mathematical
   formula for these harmonic amplitudes is described in my tutorial
   program "Fourier-7" described in section 4.0 below.) 

   It is interesting to see the rectangular pulse as it is synthesized
   from its harmonic components.  While viewing the spectrum amplitude
   display, select the Synthesize option by pressing S.

  
   2.5) Wave5

   Wave5 is an example of a waveform made up of a strong sinusoid component
   and a large amount of superimposed noise.  The formula for this waveform
   is given by:

               y = .5 * sin(2*pi*16*t/256) + .5 * cos (t^3)

   where cos(t^3) is our contrived way to generate a bounded uncorrrelated
   noise source.  This waveform can be used to illustrate one practical
   application of the FFT, namely recovering a signal that has been
   corrupted by noise.  The amplitude spectrum of this signal shows very
   clearly the dominant sinusoidal component, even though this would be
   very difficult to discern accurately by looking at the time domain
   waveform alone.  This technique has many applications, such as the 
   accurate determination of the frequency of the doppler shift in an
   ultrasonic blood flow meter. 
   
   
   3) Your own waveforms

   Having seen how these example waveforms work, you can experiment with
   your own waveforms or data.  I have tried to make it as easy as possible
   to enter your own data or wave information.  You have three options,
   selectable from the Program Menu.  

   
   3.1) Cursor entry

   Press 1 from the Program Menu to enter one cycle (256 data points) of
   your waveform using the cursor keys on your keyboard.  These 256 data
   points correspond to time samples from t=0 to t=255.  Once you enter 
   the last data point (t=255) you may choose to save your waveform to
   a file on your disk (press S to save), take the FFT of your waveform
   (by pressing F), abandon the waveform and enter a new one (Press N), or
   return to the Program Menu (Press X).

   
   3.2) Math formula

   Press 2 from the Program Menu to enter a mathematical expression to
   define your waveform. You will be prompted with "y = " after which
   you can enter a mathematical expression of the variable t.  The 
   program will then compute and plot the value of your expression for
   256 values of t ranging from 0 to 255.
   
   The following functions and operators are supported:    

        ABS      Absolute Value          AND       Logical AND            
        ARCCOS   Arc Cosine              ARCCOSH   Arc Hyperbolic Cosine   
        ARCCOT   Arc Cotangent           ARCCOTH   Arc Hyperbolic Cotangent
        ARCCSC   Arc Cosecant            ARCCSCH   Arc Hyperbolic Cosecant 
        ARCTANH  Arc Hyperbolic Tangent  ARCSEC    Arc Secant              
        ARCSECH  Arc Hyperbolic Secant   ARCSIN    Arc Sine                
        ARCSINH  Arc Hyperbolic Sine     ATN       Arc Tangent             
        CLG      Common Log (base 10)    COS       Cosine                 
        COT      Cotangent               COTH      Hyperbolic Cotangent   
        CSC      Cosecant                CSCH      Hyperbolic Cosecant    
        EXP      Exp                     LOG       Natural Log (base e)   
        NOT      Logical NOT             OR        Logical OR             
        SINH     Hyperbolic Sine         SECH      Hyperbolic Secant      
        SEC      Secant                  SIN       Sine                   
        SQR      Square Root             TAN       Tangent                
        TANH     Hyperbolic Tangent      !         Factorial              
        ^        Exponentiation          *         Multiplication         
        /        Division                +         Addition               
        -        Subtraction             >         Greater than           
        <        Less than               =         Equal                  

   The mathematical constants pi and e are also recognized.                       
                                                                
   Logical operations take the value of -1 when true, and 0 when   
   false.  For example, the following formula would take the value  
   of 0 for t greater than or equal to 64 and the value of -t/64 for 
   t less than 64:                                                   
                         y = (t<64) * t/64                           
                                                                  
   Sine waves corresponding to the harmonics of the Fourier series 
   are represented by:                                               
                         y = SIN(2*pi*h*t/256)

   where h is the harmonic number (you must substitute a number for  
   the letter h in the above expression.)                            
                                                                  
   Once you have entered your formula, you can save your formula   
   and the resultant waveform to a disk file by selecting the Save      
   option (press S).  Press F to take the FFT of your waveform. Press                                           
   N to enter a new formula.  Press X to return to the program menu.
   
   
   3.3) Disk file
           
   Press 1 from the Program Menu to read data that is stored in a disk
   file.  A disk file can be created by invoking the Save option, 
   described above, after entering data using the cursor keys or after 
   producing a waveform from a mathematical formula.

   This disk file can also be created by another program (such as a data 
   acquisition program) or you can create the disk file yourself using a 
   text editor, such as EDIT in DOS 5.0.  The format of the disk file is 
   simply an ASCII list of 256 numbers, each separated by a carriage 
   return.  If you wish to add a one-line title or description of your 
   file you can do so by adding this to the end of your list of numbers.  
   Each of the 256 numbers is called a record.  If you add a title it is 
   the 257th record.  A carriage return must separate the 256th number from 
   the title.  There should be no carriage return after the title.  The 
   title is optional.

   When you Save a waveform that you created as a mathematical formula,
   the formula itself is recorded as the title in the 257th record of the 
   disk file.  If you want to change this title, you can use a text editor 
   to do so.  When doing this, be careful to not insert a carriage return
   at the end of the title.



   4.0) License information

   FFT-256 is a shareware program that may be distributed freely for
   evaluation purposes.  The program may be registered for use by sending
   $10 to the author at the address below.  I also have an extended
   version of this program available for sale.  This program, FFT-1024,
   gives you the option of working with 128, 256, 512, or 1024 sample
   points.  

   If you would like to purchase FFT-1024 the price is $19.95 (which
   includes postage.)  To order the 3.5 inch disk version order
   FFT1024-S.  To order the 5.25 inch disk version, order FFT1024-L.

   I also have an interactive tutorial program available that teaches
   the priciples of Fourier analysis and synthesis through interactive 
   examples and on-line tutorial text.  The price for this package is
   $24.95.  To order this tutorial software package on 3.5 inch disk
   order Fourier7-S.  To order on a 5.25 inch disk order Fourier7-L.
   The price of $24.95 for Fourier7 includes postage.

   Please send your order to:

                             Harry Garland
                             27555 Purissima Rd.
                             Los Altos Hills, California
                             94022

   Thank you.



         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 3,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.