ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³      *** One, Two, and Three Stage TRINOMIAL Sampling ***       ³
    ³                                                                 ³
    ³               A Quality Assurance Training Tool:                ³
    ³        Statistics Committee of the QA Section of the PMA.       ³
    ³                                                                 ³
    ³        by Bob Obenchain, Manager, Nonclinical Statistics        ³
    ³               Glaxo, MIS Statistical Services.                  ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

   TABLE-OF-CONTENTS
   =================
           NOMAJORS.EXE.................................Executable Module
           NOMAJORS.OUT.................................ASCII Output File
           <NOMAJORS.IN...............ASCII Batch Input (DOS Redirection)
           PROMPTS and DEFAULTS..................Minimum & Maximum Values
           NOMAJRUN.BAT...........................Input & Output Examples
           NOMAJORS.C..............................C-language Source Code

   *********************************************************************

   NOMAJORS.EXE

       NOMAJORS calculates the expected percentage of acceptable lots
       in single, double, or triple stage TRINOMIAL sampling in which
       acceptance implies that NO MAJOR Nonconformances were observed.

       Testing of each unit sampled is assumed to yield one of three
       possible results...

           Observance of a Conformance to Specification
                   (say, within 25% of a target value), or

           Observance of a Minor Nonconformance
                   (say, deviation from target by 25% to 35%), or

           Observance of a Major Nonconformance
                   (say, deviation from target by more than 35%).

       Furthermore, NOMAJORS assumes that...

          the observance of a single MAJOR Nonconformance implies
          rejection of the lot, and

          a one, two, or three stage acceptance sampling plan for MINOR
          Nonconformances will be specified.


       NOMAJORS.EXE is an executable module for IBM-compatible personal
       computers.  It was compiled using Microsoft C, version 5.0.
       NOMAJORS.EXE thus provides automatic detection (and use or
       emulation) of an 8087/80287/80387 numeric math coprocessor.  If
       your PC has a math chip, NOMAJORS should run much faster.  If
       your PC does NOT have a math chip, NOMAJORS will still run and
       should yield identical numerical results.



   NOMAJORS.OUT

       This is the default filename for the ASCII summary file of inputs
       and outputs from NOMAJORS.EXE.  You may specify an alternative
       name and/or extension for this file as the first argument to the
       NOMAJORS invocation on the DOS command line...

                        Prompt> nomajors myname.ext

       You can read/print this file after the program terminates, so you do
       not need to make hand-written notes during execution.


   <NOMAJORS.IN

       NOMAJORS accepts ACSII batch input via "redirection" (from a file
       to the keyboard console) specified on the DOS command line.  You
       simply specify the batch filename preceded by the < (less than)
       symbol as the last argument to the NOMAJORS invocation...

                        Prompt> nomajors myname.ext <batch.in
       or
                        Prompt> nomajors <batch.in

       The format for a batch INPUT file is similar to that of a NOMAJORS
       OUTPUT file, except that

           * lines that do not start with a number should not be present,

       and

           * only the first number on each line of the file is utilized as
             input.  This number may be either an integer or a floating
             point number - but must be separated from other information
             on the same line by at least one white space (blank or tab.)

       The example input file distributed with NOMAJORS is USP_CAP.IN,
       for analysis of the USP (two-stage) Capsule Acceptance Plan.

       One way to create an input file would be to use the invocation

                        Prompt> nomajors trial.out

       to run NOMAJORS in prompt mode, saving calculations for, say, 50
       different pairings of Major and Minor % NonConforming incoming
       for inspection in a file named TRIAL.OUT.

       Now suppose you edited TRIAL.OUT, changing sample sizes or
       accept and/or reject numbers for Minor Nonconformances, deleting
       lines that do not start with a number, and separating the % Major
       NonConf and % Minor NonConf values - placing them on successive
       lines of the file.  Name the new file, say, TRIAL.IN.  Then
       an invocation of the form

                        Prompt> nomajors trial.new <trial.in

       could evaluate a new trinomial sampling plan at, say, the same
       50 Major-Minor % NonConf pairings that you used in your first
       run.


   PROMPTS and DEFAULTS

           ...Type responses to prompts using the number keys along the
              top row of the keyboard, and then press the ENTER key.

           ...If you press the ENTER key without typing a value, your
              response will be assigned to the DEFAULT value.

           ...The prompts are listed below with minimum, default, and
              maximum allowed values.

                 Enter your First Stage Sample Size: n1
                 Minimum Sample Size =     2
                 Default Sample Size =    50
                 Maximum Sample Size = 5,000

                 Enter your First Stage MINOR Nonconformance Accept Number: a1
                 Minimum Acceptance Number =     -1
                     (i.e. lot acceptance impossible at stage 1
                      even if zero nonconformances are observed.)
                 Default Acceptance Number =      0
                 Maximum Acceptance Number =      min(n1,999)

                 Enter your First Stage MINOR Nonconformance Reject Number: r1
                 Minimum Reject Number =      max(a1+1,1)
                                        (i.e. single stage sampling)
                 Default Reject Number =      max(a1+1,1)
                 Maximum Reject Number =      n1

                 Enter your Second Stage Sample Size: n2
                 Minimum Sample Size =     1
                 Default Sample Size =    50
                 Maximum Sample Size = 5,000

                 Enter your Second Stage MINOR Nonconformance Accept Number: a2
                 Minimum Acceptance Number =      a1
                 Default Acceptance Number =      a1
                 Maximum Acceptance Number =      min(n1+n2,999)

                 Enter your Second Stage MINOR Nonconformance Reject Number: r2
                 Minimum Reject Number =      a2+1
                     (i.e. two stage sampling)
                 Default Reject Number =      a2+1
                 Maximum Reject Number =      n1+n2

                 Enter your Third Stage Sample Size: n3
                 Minimum Sample Size =     1
                 Default Sample Size =    50
                 Maximum Sample Size = 5,000

                 Enter your Final MINOR Nonconformance Accept Number:  a3
                 Minimum Acceptance Number =      r2 - 1
                 Default Acceptance Number =      r2 - 1
                 Maximum Acceptance Number =      min(n1+n2+n3,999)

                 Specify Testing Efficiency (Percentage):
                 Minimum Testing Efficiency =    10%
                 Default Testing Efficiency =   100%
                 Maximum Testing Efficiency =   100%


   YIELD Calculations...

           ...The user is repeatedly prompted to specify pairs of
              major-minor nonconformance percentages of units within lots.
              These are the values of quality (% NonConf) "incoming" to
              the acceptance sampling inspection.

           ...Enter values between 0.0% and 100.0%.

           ...Enter any negative value (say, -1) for % MAJOR
              Nonconforming to halt execution of NOMAJORS.EXE.

           ...NOMAJORS.EXE will calculate the "Yield Percentage"
              corresponding to each specified incoming % NonConf pairing.
              This Yield % is 100 times the Probability of Lot Acceptance,
              which defines the Operating Characteristic Curve for the
              trinomial sampling plan.


   NOMAJRUN.BAT...

           ...This DOS batch command file contains "nomajors %1.out <%1.in"
              and is invoked by entering a command line of the form...

                           Prompt> nomajrun xyz

              where XYZ is a DOS filename (8 characters maximum) with
              neither a period (.) nor a 3 character filename extension.

              NOMAJORS then creates (or overwrites) file XYZ.OUT using a
              file named XYZ.IN, which must already exist, as input.  If
              file XYZ.IN cannot be found, XYZ.OUT is not created and no
              calculations are performed.


   NOMAJORS.C

       This is an ASCII file of C-language source code for NOMAJORS.  The
       only external functions called by NOMAJORS are the logarithm and
       exponential functions, so the code should be highly portable.  For
       example, to compile and run the program on a VAX under VMS, upload
       NOMAJORS.C to the VAX in ASCII mode and enter the commands...

                           VAX Prompt> cc nomajors
                           VAX Prompt> link nomajors
                           VAX Prompt> run nomajors


   *********************** End of NOMAJORS.DOC *************************


         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,800+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                               (713) 665-7017