ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º                                                     º
               º         Quality Trend Monitoring ...by Month        º
               º                                                     º
               º                  QTM User's Manual                  º
               º                    Version 9403                     º
               º                                                     º
               ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
               º         "A Quality Assurance Training Tool"         º
               º    Statistics Committee, Quality Control Section,   º
               º    Pharmaceutical Manufacturing Association (PMA)   º
               ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
               º      Bob Obenchain, CompuServe User [72007,467]     º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


       Section 1 - Introduction..............................................2

       Section 2 - Requirements for IBM-compatible PC Systems................4

       Section 3 - dBASE3+ Components of QTM.................................7

       Section 4 - QTM Walk-Through.........................................10

               4.1  Work on an Existing Component Processes.................11
                    4.1.1 Enter New Data....................................13
                    4.1.2 Accumulate Results Over Lots......................15
                    4.1.3 List Accumulated Equivalent Defects/Expectancy....17
                    4.1.4 DISPLAY Trend Chart (VGA Graphics Mode)...........18

               4.2  Adding a New Component Process..........................21

               4.3  Archive/Delete an Existing Component Process............23

               4.4  Create / Update / Delete a Composite Process............24

               4.5  Exit QTM & Return to DOS................................26

       Section 5 - Guidelines for Specifying the Statistical
                   Distribution of Loss at Standard Quality.................27

       REFERENCES & Software Update History.................................29

       Appendix 1.  Equivalent Nonconformances and Expectancy...............31

       Appendix 2.  The Ten QTM Regret Function Families....................32

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 2 of 37



                           ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                           ³  Section 1 - Introduction  ³
                           ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       QTM and CapQuant are a pair of software systems designed to complement
       each other.  Both systems use state-of-the-art methods for converting
       observed deviations from an intended target value (in almost any form
       of quantitative variable) into surrogate measures of cost-of-poor-
       quality.

         CapQuant is designed to perform process capability studies on
         historical data to set "quality standards" for expected performance.

         QTM then uses these standards for Quality Trend Monitoring as new
         data accumulate on a month-by-month basis.

       Note that QTM looks primarily for "long-term" effects associated with
       customer and/or regulatory dissatisfaction.  This is the process
       control strategy commonly known as "off-line" or "open-loop, advisory"
       control.

       Commonly used methods for Statistical Process Control (SPC) [such as
       Shewhart, EWMA and CuSum charts] tend to be applied "on-line" or in
       "real-time" to achieve short-term control.  Similarly, Engineering
       Process Control (EPC) focusses almost exclusively on "closed-loop,
       automatic" methods for truly short-term control of process parameters.

           Simple Shewhart X-bar and S (or R) charts can be used to monitor
           results on a monthly basis because the "spread" between upper and
           lower Shewhart control limits can be increased/decreased monthly to
           adjust for "unequal subgroup sizes"; i.e. different numbers of
           observations in different months.  Unfortunately, this Shewhart
           approach is notoriously low in POWER to detect process changes.

           Powerful SPC methodologies such as EWMA and CuSum charts require
           consecutive observations to have constant variance; this is the
           "identically distributed" and/or "homoscedastic observations"
           assumption.  In other words, smoothing of monthly results for
           "in-control" processes using either EWMAs or CuSums technically
           requires EQUAL numbers of observations each (monthly) reporting
           period.  [Modest departures from equal sub-group sizes might not
           totally invalidate results from month-by-month EWMA or CuSum
           analyses, but who knows how to gage the extents of such
           departures?]

       QTM implements a closely related pair of POWERFUL Moving Average (MA)
       statistical methodologies:

             QMP ...the Quality Measurement Plan of Hoadley[1,5,6] and

           WAMOC ...the Windowed-At-Most-One-Change approach of Obenchain
                    and Kenett(1993).

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 3 of 37



       The QMP and WAMOC approaches are both superior to the Shewhart, EWMA
       and CuSum approaches in the sense that they ...

           (1) treat both equal and unequal monthly sub-groub sizes,

           (2) use a finite moving "window" of fixed width in months (such
               as, say, six months) to "smooth" results and yield powerful
               statistical inferences,
       and
           (3) use parametric "regret" (loss) functions to convert observed
               deviations in almost any form of variables data from from their
               intended target value into surrogate measures of the long-term
               economic impact implied by those deviations.

       The QTM system allows the user to choose his/her regret function from
       any one of ten general families...

           One form of data commonly used in quality monitoring are called
           attributes (or defects or go/nogo) data; a certain sample size is
           inspected/tested, and the number of nonconforming units found is
           recorded.  QTM handles this simple situation by use of a "Goal-
           Posts" form of regret function: regret = zero within a pair of
           specification limits, and regret = 1 outside of those limits.

           Taguchi's (quadratic) "Loss-to-Society" is another possible choice
           for the functional form of regret.  And QTM also offers regret
           function choices (such as "Logistic" and "Inverted-Normal") that
           are bounded (i.e. "flat" in the tails corresponding to very large
           deviations from target) and thus are much more "robust" to outlying
           observations than are unbounded choices (such as "Quadratic" or
           "Absolute Value" regret.)

       In short, QTM can be quite effectively used with almost any form of
       single, observed numerical values.  Furthermore, QTM also handles
       "matched pairs" data, such as the minimum and maximum observed
       measurements in samples of fixed size from each lot produced within in
       a month.  And, because QMP and WAMOC both "combine" quality estimates
       from the current monthly reporting period with historical data over a
       window of recent/previous months, the END RESULT is an accurate,
       overall picture of the long-term trends in true quality levels of
       processes under QTM study.

       The primary outputs of QTM are graphical quality trend charts which
       are displayed on your personal computer monitor screen in high-
       resolution (VGA) mode.  A key-press will then generate a hard copy of
       the screen on a dot-matrix graphics printer or a Hewlett-Packard
       LaserJet/DeskJet connected to you personal computer's LPT1 parallel
       port.  Or a key-press will store the screen in a .PCX graphics file
       for import into your work processing system.  In addition to being
       plotted, all numerical values (plus other detailed summary statistics)
       are also automatically saved in an ASCII output file.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 4 of 37



                              *** getting started ***

       You do not really need to read this documentation file before trying
       QTM out...assuming that you have kept a copy of the original QTM94.EXE
       electronic distribution archive and/or make backup copies of all QTM
       files.  For example, executing QTM94.EXE not only unpacks the QTM
       files but also retains copies of all the QTM files inside the archive.

       The QTM system is distributed with three example files for (i) two
       "currently defined/specified" component processes plus (ii) their
       composite.  Feel free to use QTM menu options to view, modify, or
       augment these examples in any way you wish.  But, once you start to
       define your own processes and enter data to characterize them, you
       will probably wish to delete the example files distributed with the
       QTM94.EXE archive.  You should then use the "Delete Process" and/or
       "Delete Composite" menu items to get rid of the databases and the
       parameter definitions for these "sample" processes.  PLEASE don't
       delete these currently existing processes right now (before new
       processes have been defined); QTM needs to have at least two component
       processes plus at least 1 composite process "currently active."


                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                      ³  Section 2 - PC System Requirements  ³
                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       QTM is a dBASE/Clipper 5.01 application for IBM-compatible personal
       computers that has been RTLinked using "virtual memory overlays"...
       _______________________________________________________________________
       Version 7.00        Demo Versions, .RTLs, Profiling, & Environment Var. Burn-in
       DOS 386-Mode    (C) Copyright Pocket Soft Inc., 1988-1993. All Rights Reserved.

        MEMORY LAYOUT SUMMARY for: QTM.EXE

         Load Size of Resident Portion:            175.K    +26H Para

         VIRTUAL MEMORY ARENA SIZES:
           CONVENTIONAL
             Minimum Conventional VM Arena required to run:    18.K    +2EH Para
             when Expanded memory is present
               (VCACHE CONVENTIONAL or REGULAR):        10.K    +0H Para
               (but leave at least:  150.K    +0H Para )
             when Expanded NOT present but Extended IS present
               (VCACHE NOEXPANDED or NOLIM):            20.K    +0H Para
               (but leave at least:  150.K    +0H Para )
             when neither Expanded nor Extended is present
               (VCACHE ONLYCONVENTIONAL):             15.%
               (but leave at least:  150.K    +0H Para )
             If present, additional memory blocks will be used,
                 in blocks of at least:  0.K    +3DH Para
               (UMB's, then Conventional memory if necessary).
           EXPANDED (LIM, EMS) when available

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 5 of 37



             (VCACHE EXPANDED or LIM):                75.%
           EXTENDED (XMS) when available (VCACHE EXTENDED):    100.%

       ____________________________________________________________________________

       To display VGA graphics trend charts, QTM needs to "spawns" calls to
       the QMPCHART.EXE or WAMOC.EXE systems.  To provide memory for these
       graphics programs to execute, QTM "shells out" by writing a majority
       of its current memory usage to a temporary (.TMP) file in either...

        (i) the current working directory on your hard or floppy disk or else

       (ii) the location specified in a "TMP=<path\directory>" environmental
            variable.

         WARNING: QTM may "hang" if sufficient space is not available on disk
                  to write these temporary files.  Assure that at least 200
                  kBytes of disk space is free in the current working
                  directory or in the TMP= location before launching QTM.EXE.


       IN SUMMARY, the minimum requirements for a personal computer system to
       use QTM are as follows:

            ...First of all, your PC must be IBM-compatible with at least the
               above listed minimum of FREE conventional (lower 640 kBytes),
               extended or expanded RAM memory.

               NOTE: Use of an 80486 or 80386 machine with a hard disk is
                     highly recommended.

            ...Secondly, your monitor must be capable of displaying VGA (high
               resolution) screen graphics.

            ...Thirdly, only laser or dot-matrix printers connected to LPT1
               can be used to produce screen prints by pressing a single,
               "special" key:

                   L or F10   ...dumps the screen to an HP Laserjet or DeskJet
                   I or F9    ...dumps to an IBM Graphics or ProPrinter
                                        as well as to Epson LX and MX printers
                   E or F8    ...dumps to Epson FX, JX-80, or LQ-1500 printers

               Alternately...

                   P or F11   ...saves screen in PCX format (black, blue & red
                                 on white) in a file with the same filename as
                                 the "infile" but with the extension ".PCX".

            ...OPTIONAL software systems can also be useful in maintaining
               QTM databases.  These optional components can be copies of the
               Clipper BROW.EXE and DOT.EXE utilities or else any dBASE3+
               compatible interpreter (including either Foxbase+ or dBXL.)

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 6 of 37



                   WARNING: BROW.EXE, DOT.EXE or dBASE3+ interpreters can be
                   used to make changes and/or to introduce "errors" that would
                   be detected and/or prevented by the QTM.EXE Clipper menu-
                   access system.


       CONFIG.SYS requirements:
       ========================

       To make efficient use of QTM software, DOS should be informed of QTM's
       special needs for management of files, buffers and/or environmental
       variables.  This is accomplished by having a CONFIG.SYS file in your
       C:\ root directory that is read by your system when it boots.  For
       example, you could add the following sorts of lines to your CONFIG.SYS
       file:
                        BUFFERS=8
                        FILES=20
                        SHELL=C:\COMMAND.COM C:\ /E:480 /P

       You must edit your C:\CONFIG.SYS file (using your favorite ASCII
       editor) to assure that, at the very minimum, at least "FILES=20" and
       "BUFFERS=8" are specified.  The above suggestion for the "SHELL="
       directive increases the amount of space your system sets aside for
       environmental variables (e.g. SET RTxxxxxx = ) that modify QTM's usage
       of conventional, expanded and extended memory.  The DOS default
       environment size is only 160 bytes; the example above increases that
       size by a factor of 3.  You should reboot your system after revising
       your C:\CONFIG.SYS file and before you try to use QTM.  This rebooting
       is accomplished by holding down the Ctrl and Alt keys and then
       pressing the Del key.

       Forms for QTM RTlink environmental variable strings are...

         Save Swap File:   SET TMP = <PATH\DIRECTORY>

         Overlay Cache:    SET RTOVCONV=<MAXSIZE>[,<MINLEAVE>]
                           SET RTOVEXP =<MAXSIZE>[,<MINLEAVE>]
                           SET RTOVEXT =<MAXSIZE>[,<MINLEAVE>]

         Virtual Memory:   SET RTVMCONV=<MAXSIZE>[,<MINLEAVE>]
                           SET RTVMEXP =<MAXSIZE>[,<MINLEAVE>]
                           SET RTVMEXT =<MAXSIZE>[,<MINLEAVE>]
       where
           MAXSIZE  =  30% (or some other percent) of memory for VML Caching
       and
           MINLEAVE =  100K (or some other no. of kBytes) of memory for QTM.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 7 of 37



       QTM dBASE and Memory Files:
       ===========================

       Every disk directory from which you intend to invoke QTM.EXE must
       contain the main QTM data bases and memory files (REGPARMS.DBF,
       COMPARMS.DBF, DATASETS.DBF, APPEND.DBF, PERIODS.DBF, COMPOSIT.DBF and
       QTM_MAIN.MEM) as well as the individual data bases and memory files
       for the currently existing "process" that are being monitored from
       that directory.

       QTM Executable Modules:
       =======================

       Even if you will be using MORE THAN ONE directory for QTM, you will
       NOT really need multiple copies of the .EXE files.  Instead, you may
       locate single copies of QTM.EXE, QMPCHART.EXE and WAMOC.EXE in any
       directory listed in your DOS "PATH=" environmental variable.



                    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                    ³  Section 3 - dBASE3+ Components of QTM  ³
                    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       The data for each product/process to be monitored using QTM are stored
       in dBASE3+ compatible files.  For example, REGPARMS.DBF contains a
       record with 18 fields for each existing (component) "Process Spec."...

                     Structure for database: REGPARMS.DBF

                     Field  Field Name  Type       Width    Dec

                         1  REGRETPARM  Character      8
                         2  DATANAME    Character      8
                         3  PROCNAME    Character      8
                         4  SPECDATE    Date           8
                         5  TYPELOSS    Character      8
                         6  FIRSTNAME   Character     20
                         7  FIRSTVAR    Character      4
                         8  SECONDNAME  Character     20
                         9  SECONDVAR   Character      4
                        10  TARGET      Numeric       15      7
                        11  PARM1       Numeric       15      7
                        12  PARM2       Numeric       15      7
                        13  EXPLOSS     Numeric       15      7
                        14  VARLOSS     Numeric       15      7
                        15  HEAD1       Character     40
                        16  HEAD2       Character     40
                        17  FOOT1       Character     40
                        18  FOOT2       Character     40
                     ** Total **                     324

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 8 of 37



       QTM manages data entry/browsing/editing of data series by insisting
       that raw data reside in a dBASE file with the same structure as the
       empty APPEND.DBF file.  For example, note that every such dBASE file
       must have exactly 6 fields (named VAR1 to VAR6) that may contain raw
       data.  The DATANAME field of REGPARMS.DBF specifies the filename of
       the raw data dBASE file; the FIRSTNAME and FIRSTVAR (plus possibly the
       SECONDNAME and SECONDVAR) fields of REGPARMS.DBF specify either one or
       two raw data variable names and positions (again within VAR1 to VAR6):

                     Structure for database: APPEND.DBF
                     Number of data records:       0

                     Field  Field Name  Type       Width    Dec

                         1  YEAR        Numeric        4
                         2  MONTH       Numeric        2
                         3  LOTID       Character      8
                         4  VAR1        Numeric       15      7
                         5  VAR2        Numeric       15      7
                         6  VAR3        Numeric       15      7
                         7  VAR4        Numeric       15      7
                         8  VAR5        Numeric       15      7
                         9  VAR6        Numeric       15      7
                        10  COMMENT     Character     40
                        11  REGRETPARM  Character      8
                        12  REGRET      Numeric       15      7
                        13  EQVEXP      Numeric       15      7
                        14  EQVNCF      Numeric       15      7
                     ** Total **                     198

       QTM also uses a separate dBASE file, DATASETS.DBF, to keep track of
       the number (1 to 6) and 20-character names of variables in each raw
       data file having the above APPEND.DBF structure.  This additional
       dBASE file has the structure...

                     Structure for database: DATASETS.DBF

                     Field  Field Name  Type       Width    Dec

                         1  DATANAME    Character      8
                         2  NUMBERVAR   Numeric        1
                         3  VAR1NAME    Character     20
                         4  VAR2NAME    Character     20
                         5  VAR3NAME    Character     20
                         6  VAR4NAME    Character     20
                         7  VAR5NAME    Character     20
                         8  VAR6NAME    Character     20
                     ** Total **                     130

       When QTM accumulates equivalent nonconformances and equivalent
       expectancies over all lots within each monthly reporting period, QTM
       copies the structure of the empty PERIODS.DBF file into the dBASE with
       the name specified in the PROCNAME field of REGPARMS.DBF...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 9 of 37



                     Structure for database: PERIODS.DBF
                     Number of data records:       0

                     Field  Field Name  Type       Width    Dec
                         1  PERIOD      Numeric        6
                         2  CMONTH      Character      1
                         3  REGRETPARM  Character      8
                         4  LOTS        Numeric        4
                         5  EQVEXP      Numeric       15      7
                         6  EQVNCF      Numeric       15      7
                         7  REGTMEAN    Numeric       19      7
                         8  REGTVAR     Numeric       19      7
                     ** Total **                      88

       Each QTM "composite" process is described in a record in the
       COMPARMS.DBF database...

                     Structure for database: COMPARMS.DBF
                     Number of data records:       0
                     Field  Field Name  Type       Width    Dec
                         1  COMPNAME    Character      8
                         2  NUMBER      Numeric        1
                         3  HEAD1       Character     40
                         4  HEAD2       Character     40
                         5  FOOT1       Character     40
                         6  FOOT2       Character     40
                         7  PROC1       Character      8
                         8  ACCF1       Character      8
                         9  WGHT1       Numeric        4      2
                        10  PROC2       Character      8
                        11  ACCF2       Character      8
                        12  WGHT2       Numeric        4      2
                        13  PROC3       Character      8
                        14  ACCF3       Character      8
                        15  WGHT3       Numeric        4      2
                        16  PROC4       Character      8
                        17  ACCF4       Character      8
                        18  WGHT4       Numeric        4      2
                        19  PROC5       Character      8
                        20  ACCF5       Character      8
                        21  WGHT5       Numeric        4      2
                        22  PROC6       Character      8
                        23  ACCF6       Character      8
                        24  WGHT6       Numeric        4      2
                     ** Total **                     290

           The COMPNAME field (8 characters maximum) contains the name of the
           composite process and the NUMBER of fields indicates the number of
           its "component" processes (always between 2 and 6.)

           Pairs of PROCx and ACCFx fields identify the component process
           specification and accumulation dBASE filenames, respectively.  Each
           WGHTx field contains a number between 0.01 and 1.00.  A WGHTx value

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 10 of 37



           less than 1.00 represents a (subjective) relative DOWN-WEIGHTING of
           the information content from that component process.

       When QTM accumulates equivalent nonconformances and equivalent
       expectancies over all component processes within a given composite for
       each monthly reporting period, QTM copies the structure of the empty
       COMPOSIT.DBF file into the dBASE with the name specified in the
       COMPNAME field of COMPARMS.DBF...

                     Structure for database: COMPOSIT.DBF
                     Number of data records:       0

                     Field  Field Name  Type       Width    Dec
                         1  PERIOD      Numeric        6
                         2  CMONTH      Character      1
                         3  EQVEXP      Numeric       15      7
                         4  EQVNCF      Numeric       15      7
                     ** Total **                      38


                          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                          ³ Section 4 - QTM Walk-Through ³
                          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       The four MAJOR PHASES of QTM operation, plus a termination option,
       are the five items on QTM's MainMenu:

           [1] work with any currently existing (component) process,
           [2] add a new component process specification,
           [3] delete one or more existing process specifications,
           [4] create, update or delete a composite of between 2 and 6
               of the currently existing [phase 1,2,3] component processes,
       and
           [5] exit from QTM and return to the operating system.

       Let us now take a brisk "walk-through" the QTM software menus and
       screens to give the first time user a feel for how the various phases
       of QTM operations work.

           NOTE: Routine use of QTM usually consists of a fixed sequence of
                 steps that are followed in one prescribed, default order.
                 Only advanced users should depart from the sequential steps
                 described in this walk-through.

       To start-up the QTM software system, you should "cd" (change
       directories) to the appropriate hard-disk drive and directory (say,
       C:\qtm) and invoke QTM.EXE.  You could accomplish this by typing the
       following three commands at your DOS prompt, pressing the ENTER or
       Return key at the end of each of the three commands...

                                     c:
                                     cd\qtm
                                     qtm

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 11 of 37



       The opening screen of QTM.EXE tells you how to obtain a source code
       license for the QTM software system.  Although a copyrighted work, QTM
       is distributed as "freeware" and, thus, is UNSUPPORTED.  If (due, say,
       to federal regulations) you will need to "validate" the QTM software
       system before you can officially use it in you business, your
       validation team will need to acquire a copy of the QTM source code...
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°
       °°°°º                                                           º°°°°°
       °°°°º           QTM: Quality Trend Monitoring by Month          º°°°°°
       °°°°º             Copyright (c) 1993 - Bob Obenchain            º°°°°°
       °°°°º                                                           º°°°°°
       °°°°º  To obtain a dBASE/Clipper/C-language source code license º°°°°°
       °°°°º  for this QTM software system, send $50.00 US to          º°°°°°
       °°°°º                                                           º°°°°°
       °°°°º               QA Training Tools                           º°°°°°
       °°°°º               c/o Bob Obenchain, Ph.D.                    º°°°°°
       °°°°º               5261 Woodfield Drive North                  º°°°°°
       °°°°º               Carmel, IN 46033 USA                        º°°°°°
       °°°°º                                                           º°°°°°
       °°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

       The above QTM copyright notice will disappear when you press-any-key,
       and you are then given the opportunity to read a series of "overview
       screens" that describe the QTM system.  [This introductory/background
       information is distinct from the information provided here in the QTM
       documentation file.]  The "default" response here is "N" (to NOT read
       overview screens).  You may exercise this default by simply pressing
       the ENTER/Return key.
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°
       °°°°º       Read QTM Overview Information Now ? [N|y] :         º°°°°°
       °°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

       The QTM MainMenu items for the major phases of QTM operations then
       appear along the horizontal white BAR near the top of your screen,
       with one of the five MainMenu options highlighted in reverse-video...
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 12 of 37



       4.1 WORKING WITH THE "EXISTING PROCESS" OPTION
       ==============================================

       Because two sample data files for component processes are
       distributed with the QTM system, let us start our walk-through by
       demonstrating how to work with an "Existing Process."  Thus, either
       press the "E" key or else use the arrow keys to highlight the
       left-most MainMenu item and then press the ENTER/Return key...
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Left/Right Arrows - Move Pointer ² ENTER-Select ² ESC-Exit ²°°°°°°°°

       The main QTM screen then displays not only which existing process
       specification is "currently active" but also displays the 5-item
       SubMenu for working with existing processes.  For example, in the
       following screen dump, the "1SIDISSO" process defined on the "TABLETS"
       raw data dBASE is the "currently active" process.  If "1SIDISSO" is
       the existing process that you wish to work on now, you would pick one
       of the first 4 items on this sub-menu.  But, if you wish to work on
       some other existing process specification or you wish to simply
       refresh your memory about what the "1SIDISSO" process specification
       consists of, you would pick the last (5th) item on this sub-menu to
       browse process specifications and/or "select" a different process as
       the "currently active" process...
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°º  Current Process Spec ID = 1SIDISSO º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°º  Current Raw Data dBASE  = TABLETS  º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°°°°°°°°°°°°°°°°°°
       °°º  View Trend Chart for Current Process      º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Browse/Edit/Add Raw Data to dBASE File    º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Re-Accumulate Results by Month            º°°°°Move the HighLight
       °°º  List Equivalent Nonconforms & Expectancy  º°°°°Bar here and press
       °°º ÛSelect/Browse/Edit Existing ProcessesÛÛÛÛ º°<--ENTER or press the
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°"s" key to change
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°"currently active"
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°process...°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

       The following screen dump shows what the first record in REGPARMS.DBF
       looks like...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 13 of 37



       Active Specification = 1SIDISSO                      Record No:    1
                  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ÚÄÄÄÄÄÄÄÄÄÄº   QTM Process Specification ID : QADASSAY    ÇÄÄÄÄÄÄÄÄÄ¿
       ³          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼         ³
       ³ TABLETS  = Raw Data dBASE File     ³                              ³
       ³                                    ³ QUADRATC = Regret TYPE       ³
       ³ QADASSAY = Process  dBASE File     ³ 06/12/93 = Date Last Updated ³
       ³           (accumulate over lots)   ³                              ³
       ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ SECOND Variable in Use ? N   ³
       ³                                                                   ³
       ³ NAME of FIRST Variable: (REQUIRED)     NAME of SECOND Variable:   ³
       ³ Potency Assay                          NONE                       ³
       ³ VAR1 (VAR1...VAR6 = dBASE Position)         (VAR1...VAR6)         ³
       ³                                                                   ³
       ³     150.0000000 = TARGET Value           5.0000000 Expected Value ³
       ³       0.0000000 = Regret Parameter One  75.0000000 and Variance   ³
       ³       0.0000000 = Regret Parameter Two             of Regret.     ³
       ³                                                                   ³
       ³ Pharmaceutical Tablet AssayÛÛÛÛÛÛÛÛÛÛÛÛ  <-- First and Second     ³
       ³ Taguchi Quadratic LossÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ      HEADER Strings       ³
       ³        First and Second -->  Label Claim = 150mgÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ   ³
       ³        FOOTER Strings        Exp.Loss = 5; Var.Loss = 75ÛÛÛÛÛÛÛ   ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
       N:Next P:Previous F:First  L:Last  G:Goto  E:Edit  S:Select  R:Return

       4.1.1  Browse/Edit/Add Raw Data to dBASE File
       =============================================

       But let us suppose that "1SIDISSO" (monitoring of tablet dissolution
       results using one-sided quadratic regret) is indeed the existing
       process that we wish to work on.  Furthermore, suppose that we have
       some new data on 3 batches manufactured in March 1993 to add to the
       TABLETS.DBF that already contains data on 242 batches made in the 27
       months between January 1993 and March 1993.  Of course, we could use
       the 1st item on the "existing process sub-menu" to review how the trend
       chart looks BEFORE entering data on the 3 new lots.  But let us start
       here by simply using the 2nd item to ADD new data to the dBASE...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 14 of 37



       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°º  Current Process Spec ID = 1SIDISSO º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°º  Current Raw Data dBASE  = TABLETS  º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°Move the HighLight
       °°º  View Trend Chart for Current Process      º°°°°Bar here and press
       °°º ÛBrowse/Edit/Add Raw Data to dBASE FileÛÛÛ º°<--ENTER or press the
       °°º  Re-Accumulate Results by Month            º°°°°"b" key to ADD new
       °°º  List Equivalent Nonconforms & Expectancy  º°°°°data to the dBASE.
       °°º  Select/Browse/Edit Existing Processes     º°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

       The screen below displays the contents of the first out of 242 batches
       already contained in TABLETS.DBF.  Note that only 2 of the possible 6
       variables data fields are named: VAR1 = ASSAY (with a target value of
       150mg) and VAR2 = DISSOLUTION (with a target value of 100% of label
       claim.)  And note on the BOTTOM LINE of the screen that there are 8
       possible commands for moving around, revising, or exiting TABLETS.DBF:
                                                            Record No:    1
       ÉÍÍÍÍÍÍÍÍÍÍ» Current Raw Data dBASE File = TABLETS  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º          ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼              º
       º  1991 = YEAR (1990 to 2089)                                      º
       º   1   = MONTH (1 to 12)                        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÐÄ¿
       º                                                ³                   ³
       º  T011     = Lot Identification                 ³  DERIVED VALUES   ³
       º             (Maximum of 8 Characters)          ³  FOR THIS RECORD: ³
       º                                                ³                   ³
       º      149.3000000 = Value of ASSAYÛÛÛÛÛÛÛÛÛÛÛ   ³  Process Spec.    ³
       º                                                ³  1SIDISSO         ³
       º      100.0000000 = Value of DISSOLUTIONÛÛÛÛÛ   ³  Regret/Loss      ³
       º                                                ³        0.0000000  ³
       º        0.0000000 = Value of ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ   ³  Equiv.Expectancy ³
       º                                                ³        1.6666667  ³
       º        0.0000000 = Value of ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ   ³  Equiv.Nonconform ³
       º                                                ³        0.0000000  ³
       º        0.0000000 = Value of ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ   ³  Number of Fields ³
       º                                                ³  in Use : 2 of 6. ³
       º        0.0000000 = Value of ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ   ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÒÄÙ
       º                                                                  º
       º   ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ = COMMENT (40 Characters)   º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       N:Next P:Previous F:First  L:Last  G:Goto  E:Edit  A:Append  R:Return

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 15 of 37



       The first 5 commands (N:Next P:Previous F:First L:Last and G:Goto) are
       used simply for moving from record to record within the current raw
       data dBASE.

       The E:Edit command is used to revise/update previously entered data
       whenever an input error is discovered.  Simply locate the batch that
       contains the error and then E:Edit that record.

       The A:Append command is the one used to ADD new data at the end of the
       current raw data dBASE.  Rather than being blank, the default value
       for each field in the new record being added is simply the value from
       the last record either added or viewed.  On the other hand, the append
       of a new record will FAIL if you accept ALL of these default values by
       simply pressing the ENTER/Return key for each field.  After all, at
       least the "Lot Identification" of the new record should be different
       from that of the previous record!  (In fact, this new "Lot Id" should
       be different from that of ALL other batches made in the same year, but
       QTM does not check on that.)

       [NOTE ON EDITING or APPENDING RECORDS: Until you have pressed the
       ENTER key with the cursor in the bottom box of a screen, you can
       usually return to earlier boxes with the left or up arrow keys.  After
       you press the ENTER key with the cursor in the last box, its too
       late to use arrow keys to move between fields.]

       For practice, you could ADD the following 3 records at the end of
       TABLETS.DBF:
                       YEAR   MONTH   LOT    ASSAY   DISSOLUTION

                       1993     3     T279   148.7   93
                       1993     3     T288   150.9   91
                       1993     3     T291   147.9   95

       4.1.2 Accumulate Results Over Lots
       ==================================

       Next, use the R:Return command to return to the "existing process sub-
       menu" and then select the third menu item...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 16 of 37



       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°º  Current Process Spec ID = 1SIDISSO º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°º  Current Raw Data dBASE  = TABLETS  º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°°°°°°°°°°°°°°°°°°
       °°º  View Trend Chart for Current Process      º°°°°Move the HighLight
       °°º  Browse/Edit/Add Raw Data to dBASE File    º°°°°Bar here and press
       °°º ÛRe-Accumulate Results by MonthÛÛÛÛÛÛÛÛÛÛÛ º°<--ENTER or press "r"
       °°º  List Equivalent Nonconforms & Expectancy  º°°°°key to ACCUMULATE
       °°º  Select/Browse/Edit Existing Processes     º°°°°results by month.
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

       Depending upon the speed of your PC, re-accumulation of results over
       more than 200 lots spanning 27 months could require a couple of
       minutes of processing time.  Therefore, you would normally perform
       this step only after errors have been corrected and/or new data have
       been added to the raw data dBASE...
          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³         LOT-BY-LOT CALCULATIONS and ACCUMULATIONS PROCEDURE       ³
          ³                  Current Process Spec. ID...1SIDISSO              ³
          ³                                                                   ³
          ³                    Current Raw Data dBASE...TABLETS               ³
          ³                                                                   ³
          ³                Process Accumulation dBASE...1SIDISSO              ³
          ³                                                                   ³
          ³                       Current Regret Type...ONESIDED              ³
          ³                                                                   ³
          ³   Regrets, Equivalent Nonconformances, and Equivalent             ³
          ³   Expectancies will be re-calculated for all OLD or NEW           ³
          ³   observations.                                                   ³
          ³                                                                   ³
          ³   Perform these calculations now ?  :  Y  <-- Accept this default.³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       This data processing step involves not only

             - converting each individual measurement into a regret, an
               equivalent nonconformances value and an equivalent
               expectancy number

       but also

             - accumulating these statistics into their corresponding
               monthly reporting period totals.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 17 of 37



       In other words, observed regrets are converted into information-rich
       measures of nonconformance and literally summed over all lots/batches
       produced in the same month.  This conversion process is called
       "Poissonization."  More information about Poissonization is given in
       Appendix 1 and reference [5].


       4.1.3 List Accumulated Equivalent Defects/Expectancy
       ====================================================
                    
       At this point, you may use the fourth item on the "existing process
       sub-menu" to review the results of the most recent reaccumulation in
       numerical form:
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°º  Current Process Spec ID = 1SIDISSO º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°º  Current Raw Data dBASE  = TABLETS  º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°°°°°°°°°°°°°°°°°°
       °°º  View Trend Chart for Current Process      º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Browse/Edit/Add Raw Data to dBASE File    º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Re-Accumulate Results by Month            º°°°°°°°°°°°°°°°°°°°°°°
       °°º ÛList Equivalent Nonconforms & ExpectancyÛ º°<--HighLightBar°°°°°°
       °°º  Select/Browse/Edit Existing Processes     º°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

       The following screen dump shows what the first record in 1SIDISSO.DBF
       looks like...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 18 of 37



                                                            Record No:    1
              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³  Listing of Accumulated Data in the  1SIDISSO dBASE  ³
         ÉÍÍÍÍµ                                                      ÆÍÍÍÍ»
         º    ³       QTM Process Specification ID = 1SIDISSO        ³    º
         º    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    º
         º                                                                º
         º             9101 = Four Character Year/Month Identifier        º
         º                J = Single Character Symbol (e.g. D=>December)  º
         º                                                                º
         º                5 = Number of Lots Accumulated into this Period º
         º                                                                º
         º        8.3333335 = Accumulated Equivalent Expectancy           º
         º                                                                º
         º        6.1666666 = Accumulated Equivalent Nonconformances      º
         º                                                                º
         º       37.0000000 = Mean of Accumulated Regrets this Period     º
         º       50.0000000 = Current Regret Mean Standard                º
         º     1713.0000000 = Variance of Accumulated Regrets this Period º
         º     1500.0000000 = Current Regret Variance Standard            º
         º                                                                º
         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
         N:Next    P:Previous    F:First     L:Last     G:Goto     R:Return

       Each screen (i.e. each record in the dBASE3+ file) gives nine items of
       information about the lots accumulated into one monthly reporting
       period...

           Item 1 is the YYYYMM code for the Year/Month reporting period.
           Item 2 is the single letter code for that month.
           Row 3 counts the total number of lots accumulated within that month.

           The next two columns are the critical ones...
                  4 gives monthly equivalent defect expectancy, and
                  5 gives monthly observed equivalent defects.

           The final two columns help the user check basic assumptions...
                  6 gives the loss mean value within that month.
                  7 gives the loss variance within that month.

       [The statistics in Columns 6 and 7 are displayed so that the user
       can see the extent to which the within-lot mean loss and loss
       variance agree with what was specified as the mean loss and loss
       variance when quality is at the standard level.]


       4.1.4 DISPLAY Trend Chart (VGA Graphics Mode)
       =============================================

       After re-accumulating, it is more common to immediately use the first
       item on the "existing process sub-menu"  to view the VGA graphics
       trend chart...

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 19 of 37



       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºÛExistingProcessÛ AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°º  Current Process Spec ID = 1SIDISSO º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°º  Current Raw Data dBASE  = TABLETS  º°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°°°°°°°°°°°°°°°°°°
       °°º ÛView Trend Chart for Current ProcessÛÛÛÛÛ º°<--HighLightBar°°°°°°
       °°º  Browse/Edit/Add Raw Data to dBASE File    º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Re-Accumulate Results by Month            º°°°°°°°°°°°°°°°°°°°°°°
       °°º  List Equivalent Nonconforms & Expectancy  º°°°°°°°°°°°°°°°°°°°°°°
       °°º  Select/Browse/Edit Existing Processes     º°°°°°°°°°°°°°°°°°°°°°°
       °°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

          ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
          ³                    TREND CHART PROCEDURE                        ³
          ³                                                                 ³
          ³                                                                 ³
          ³ Enter filename for ascii QMP/WAMOC input file:   1SIDISSO       ³
          ³ (Enter blank name to return to main menu...)                    ³
          ³                                                                 ³
          ³ Maximum Months Displayed per Chart :  24                        ³
          ³ ...allowable range = 10 to 24.                                  ³
          ³                                                                 ³
          ³ History Window Width   :   6                                    ³
          ³ ...1 to 24 consecutive months.                                  ³
          ³                                                                 ³
          ³                                                                 ³
          ³ Enter filename for ascii QMP/WAMOC input file:   1SIDISSO       ³
          ³                                                                 ³
          ³ Use DEFAULT Values for Chart Parameters ?  Y                    ³
          ³                                                                 ³
          ³ Display a WAMOC rather than a QMP Trend Chart ?  Y              ³
          ³                                                                 ³
          ³ Display Forecasts, I-Plots, or Both [F|i,b] ?  F                ³
          ³                                                                 ³
          ³ Standby for Data File Creation...                               ³
          ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 20 of 37



       Note that QTM requests the user to choose between the WAMOC and QMP
       smoothing algorithms and between three modes of graphical display:

                  "F" ...Forecast confidence intervals for the true quality
                         level of the next monthly reporting period (using
                         only data from the current and previous periods),

                  "I" ...I-plot confidence intervals for the true quality
                         level of the current reporting period (using
                         only data from the current and previous periods),
       and
                  "B" ...Both I-plot and Forecast confidence intervals, i.e.
                         a pair of back-to-back intervals with present-period
                         intervals on the left and next-period-ahead forecast
                         intervals on the right.
               ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
               ³   Both types of Confidence Intervals on WAMOC/QMP charts are ³
               ³   designed to cover the unknown true Quality Index (present- ³
               ³   period or next-period-ahead) with probability 0.9...       ³
               ³                                                              ³
               ³             ÚÄÄ <ÄÄÄ 5% Forecast Ahead Percentile            ³
               ³             ³                                                ³
               ³             ³                                                ³
               ³          ÄÄ¿³ <ÄÄÄ 5% I-Plot Percentile                      ³
               ³            ³³                                                ³
               ³           \³³                                                ³
               ³            \³ <ÄÄÄ  Next Period Forecast (Process Average)   ³
               ³ Best       ³\                                                ³
               ³ Present-> Ä´³\                                               ³
               ³ Measure    ³³                             Observed           ³
               ³            X³ <ÄÄÄ Present Period Index = ÄÄÄÄÄÄÄÄ Ratio     ³
               ³            ³³                             Expected           ³
               ³            ³ÀÄÄ <ÄÄÄ 95% Forecast Ahead Percentile           ³
               ³          ÄÄÙ  <ÄÄÄ 95% I-Plot Percentile                     ³
               ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       On the other hand, if you wish to plot a different range of months
       than that given by the default, simply press the SPACE BAR to erase
       the graphics screen and start a second iteration.  The next prompt
       will be "Quit Trend Chart Screen Display?"  If you press the "N" key,
       you will recycle back through all of the Trend Chart prompts.  The
       values used in the previous cycle will now be the defaults, and you
       can accept default values simply by pressing the ENTER/Return key.

       A hard copy of the trend chart being displayed on your monitor screen
       can now be made on a dot-matrix printer or to a Hewlett-Packard
       LaserJet or DeskJet connected to LPT1 by pressing a single key:

            L or F10   ...dumps the screen to an HP Laserjet or DeskJet
            I or F9    ...dumps to an IBM Graphics or ProPrinter
                                 as well as to Epson LX and MX printers
            E or F8    ...dumps to Epson FX, JX-80, or LQ-1500 printers

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 21 of 37



       Depending upon the speed of your printer, these screen dumps can take
       as much as two minutes to complete.  And you will not be able to do
       any other sort of processing while this printing takes place.  So you
       usually only make a hard copy of trend charts that show "interesting"
       changes (for the better or for the worse) ...something you will want
       to show to your management, colleagues and/or clients.

       QTM has written a pair of ASCII files.  If the accumulation data base
       is 1SIDISSO.DBF, the default names of these two files will be
       1SIDISSO.WIN and either 1SIDISSO.WAM or 1SIDISSO.QMP.

           The file with the .WIN extension is the data input file for
           either the WAMOC or the QMPT number crunching and screen display
           modules.
           
           The files with .WAM and/or .QMP extension document the "details" of
           WAMOC or QMP calculations.  They list defect and expectancy values
           input for analysis, all internal parameter settings used in these
           algorithms, and all statistical results that were plotted in the
           resulting quality monitoring trend charts.


       4.2 HOW TO USE THE "ADD PROCESS" OPTION
       =======================================

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess ÛAddProcessÛ DeleteProcess  CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Left/Right Arrows - Move Pointer ² ENTER-Select ² ESC-Exit ²°°°°°°°°

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess ÛAddProcessÛ DeleteProcess  CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°º  Like an Existing Process  º°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°º  All Default Values BLANK  º°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Add a New Process to QTM dBASE   ² ENTER-Select ² ESC-MainMenu ²°°°°

       Creating a new process specification involves:

                 - naming the dBASE where raw data on individual observations
                   will be stored and identified by the year (1990 to 2089)
                   and month (01 to 12) they correspond to,
                 - naming the variable (or pair of variables) to be monitored,
                 - naming the Regret (LOSS) Function family and specifying
                   its corresponding parameters, such as the target value,
                 - specifying the "current capability" quality standards for

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 22 of 37



                   process performance in terms of the Mean (expected value)
                   and Variance of Regret,
                 - entering header and footer "titles" for QMP and WAMOC trend
                   chart displays.

       Specifying a NEW process is complicated, but QTM allows you to
       generate reasonable "default" values for most parameters by creating a
       new process "like" an existing one.

       The regret functions which can be defined in QTM belong to one of
       ten general families.

               1) attributes loss, which is zero inside an interval and one
                  outside that same interval,

               2) quadratic loss, where the loss is the square of the deviation
                  of the measurement from its target value,

               3) linear loss, in which the economic impact of a measurement is
                  directly proportional to the measurement's value,

               4) one-sided loss, which is quadratic on one side of a target
                  and zero on the other side of that target value,

               5) opportunity loss, in which the economic impact of a demand
                  for a perishable product is measured relative to the
                  inventory on hand,

               6) end-point quadratic loss, in which the minimum and maximum
                  observed values in samples of fixed size are monitored, and
                  loss is the sum of the quadratic loss at the two end-points,

               7) range loss, in which the difference between the minimum and
                  maximum values in samples of fixed size are monitored,

               8) logistic (bounded max) loss, in which loss follows a double-
                  logit pattern that is V-shaped in its center (at the target)
                  but flat like attribute loss in its tails,

               9) inverted-normal loss, which looks like an upside-down
                  normal distribution, is smoothly quadratic around the target,
                  and flat like attribute loss in its tails, and

              10) an unspecified loss pattern called "defect-expectancy," in
                  which case QTM simply accumulates nonconformance
                  results over individual lots.

       Appendix 2 gives complete details on the above ten QTM loss function
       families.

       Two additional types of information are entered at the same time that
       the loss functions family and parameters are specified.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 23 of 37



               ...First of all, statistical information on expected loss
                  (EXPLOSS) and loss variance (VARLOSS) when quality is at its
                  standard level must be specified.  This statistical
                  information, which is used in the "Poissonization" process
                  that converts loss into equivalent defects and expectancy,
                  is discussed in Section 4 and described, technically, in
                  Appendix 1.

               ...The second type of information entered at the time of loss
                  function specification consists of tentative titles (2 headers
                  and 2 footers) for quality trend charts.  These default titles
                  are redisplayed by the "Select/Browse/Edit Existing Processes"
                  item on the "Existing Process", so the QTM user always has the
                  option of customizing each header and footer later.


       4.3 HOW TO USE THE "DELETE PROCESS" OPTION
       ==========================================

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess  AddProcess ÛDeleteProcessÛ CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Left/Right Arrows - Move Pointer ² ENTER-Select ² ESC-Exit ²°°°°°°°°


       Active Specification = 1SIDISSO                        Record No:    1
                                                                                       
        ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿ 
        ³               QTM: Deletion of Process Specifications            ³ 
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
                                                                                       
          Process/Regret Specification = QADASSAY                                      
                                                                                       
                   Raw Data dBASE name = TABLETS                                       
                                                                                       
             Type Regret/Loss Function = QUADRATC                                      
                                                                                       
                    Process dBASE name = QADASSAY
                                                                                       
                     Date Last Updated = 06/12/93                                      
                                                                                       
       N:Next   P:Previous   F:First   L:Last   G:Goto   D:Delete   R:Return

       Use the N, P, F, L and G keys to locate the process specification that
       you want to delete and archive, then press the D key.  You will be
       asked to confirm your delete decisions.  The press the R key to return
       to the QTM main menu.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 24 of 37



       4.4 WORKING WITH THE "COMPOSITE PROCESS" OPTION
       ===============================================

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess  AddProcess  DeleteProcess ÛCompositeProcessÛ Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Left/Right Arrows - Move Pointer ² ENTER-Select ² ESC-Exit ²°°°°°°°°

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º            QTM: Quality Trend Monitoring ...by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess  AddProcess  DeleteProcess ÛCompositeProcessÛ Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»ÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°º Current Composite ID = TABLTCOM     º°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°°°°°°°°°°°°°°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°°°
       °°°°°°°°°°°°°°°°°º  View Trend Chart for Current Composite    º°°°°°°°
       °°°°°°°°°°°°°°°°°º  Re-Composite Results by Month             º°°°°°°°
       °°°°°°°°°°°°°°°°°º  List Equivalent Nonconforms & Expectancy  º°°°°°°°
       °°°°°°°°°°°°°°°°°º  Select/Browse/Edit Existing Composites    º°°°°°°°
       °°°°°°°°°°°°°°°°°º  Create a New Composite Process            º°°°°°°°
       °°°°°°°°°°°°°°°°°º  Delete an Existing Composite Process      º°°°°°°°
       °°°°°°°°°°°°°°°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Up/Down Arrows - Move Pointer    ² ENTER-Select ² ESC-MainMenu ²°°°°

       The six menu items on the "composite process" menu are really quite
       similar to the corresponding "Existing Process", "Add Process", and
       "Delete Process" items for currently existing (component) process.
       The primary distinction is simply that a "composite" process is being
       defined by literally "adding-up" the equivalent defects and equivalent
       nonconformances observed on each of its individual, component
       processes over each monthly reporting period...

          4.4.1. View Trend Chart for the Current Composite

                This operation is essentially the SAME as that explained in
                Section 4.1.4 for viewing a VGA Trend Chart for an individual,
                "component" process.

          4.4.2. Re-Composite Results by Month

                While similar to the operation described in Section 4.1.2, here
                one simply sums up the Equivalent Nonconformances and
                Expectancies for each component processes within the stated
                composite ...possibly subjectively down-weighting the
                information content from relatively unimportant components on
                which data are readily available and possibly over-abundant.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 25 of 37



                ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                ³        COMPOSITE INDEX ACCUMULATIONS PROCEDURE              ³
                ³           Composite Process dBASE = TABLTCOM                ³
                ³           Number of Component Processes = 2                 ³
                ³                                                             ³
                ³                                                             ³
                ³  Equivalent Nonconformances and Equivalent Expectancies     ³
                ³  will be accumulated over all component processes within    ³
                ³  each monthly period starting with a specified Year/Month.  ³
                ³                                                             ³
                ³  Perform these calculations now ?  :  Û                     ³
                ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

          4.4.3. List Equivalent Nonconforms & Expectancy

                This operation is essentially the SAME as that explained in
                Section 4.1.3 for Listing Accumulated Equivalent Defects
                and Expectancy, but here results are accumulated over the
                individual component processes that make up the composite.

          4.4.4. Select/Browse/Edit Existing Composites

                This operation is essentially the SAME as that explained at
                the very start of Section 4.1.  But here we are specifying
                which Composite process is to be currently active rather than
                which Component process is to be active.

        Active Composite = TABLTCOM                           Record No:    1
                 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ÚÄÄÄÄÄÄÄÄÄº   QTM Composite Process ID :     TABLTCOM    ÇÄÄÄÄÄÄÄÄÄÄ¿
       ³         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼          ³
       ³                Number of Component Processes= 2                   ³
       ³                                                                   ³
       ³  Component 1 = QADASSAY  dBASE 1 = QADASSAY Weight 1 = 1.00       ³
       ³  Component 2 = 1SIDISSO  dBASE 2 = 1SIDISSO Weight 2 = 1.00       ³
       ³  Component 3 = ÛÛÛÛÛÛÛÛ  dBASE 3 = ÛÛÛÛÛÛÛÛ Weight 3 = ÛÛÛÛ       ³
       ³  Component 4 = ÛÛÛÛÛÛÛÛ  dBASE 4 = ÛÛÛÛÛÛÛÛ Weight 4 = ÛÛÛÛ       ³
       ³  Component 5 = ÛÛÛÛÛÛÛÛ  dBASE 5 = ÛÛÛÛÛÛÛÛ Weight 5 = ÛÛÛÛ       ³
       ³  Component 6 = ÛÛÛÛÛÛÛÛ  dBASE 6 = ÛÛÛÛÛÛÛÛ Weight 6 = ÛÛÛÛ       ³
       ³                                                                   ³
       ³ ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ <-- First and Second          ³
       ³ Tablet Potency and BioavailabilityÛ     HEADER Strings            ³
       ³        First and Second --> Composite of Assay and DissolutionÛÛÛ ³
       ³        FOOTER Strings       ÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛÛ ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
          N:Next P:Previous F:First L:Last G:Goto E:Edit S:Select R:Return

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 26 of 37



          4.4.5. Create a New Composite Process

                This operation is similar to that explained in Section 4.2 on
                defining a new Component process.  But here we are faced with
                the somewhat more simple task of defining a new Composite in
                terms of its previously defined individual Components.

                But here we must assign a WEIGHT (between 1.00 and 0.01) for
                each component of the composite.

                - Assign the full [default] weight of 1.00 whenever data from
                  a component is to carry its full "information content."

                - On the other hand, data can accumulate on some components
                  simply because those components are "easy to measure."  These
                  sorts of data need to be (subjectively) down-weighted simply
                  because they tend to be over-abundantly sampled.

                - Finally, some components are either known (or at least
                  suspected) of having much lower cost-of-poor-quality impact
                  than others.  The observed/expected ratios used by CapQuant
                  and QTM measure only relative "information content" and not
                  relative importance to the "bottom line."  The user of QTM
                  should subjectively down-weight any components that he/she
                  views as having relatively small overall economic impact.

          4.4.6. Delete an Existing Composite Process

                This operation is essentially the SAME as that explained in
                Section 4.3, except that here we are deleting Composite
                processes rather than their individual Component processes.



       4.5 HOW TO USE THE "QUIT" OPTION
       ================================

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess  AddProcess  DeleteProcess  CompositeProcess ÛQuitÛº
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ² Left/Right Arrows - Move Pointer ² ENTER-Select ² ESC-Exit ²°°°°°°°°

       To exit from the QTM system, you may highlight the "Exit" item on the
       main menu and press the ENTER/Return key. Otherwise, press the Escape
       key until the following dialog-box pops up and then press the Y key or
       the ENTER/Return key.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 27 of 37



       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º               QTM: Quality Trend Monitoring by Month               º
       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º ExistingProcess  AddProcess  DeleteProcess  CompositeProcess  Quit º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       °°°°ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»°°°°°
       °°°°º          Exit QTM and Return to DOS [Y|n] : Y             º°°°°°
       °°°°ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°°°°
       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
       ²  Exit QTM Now ?  ² ENTER or Y => Exit ² ESC or N => Remain ²°°°°°°°°


             ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
             ³  Section 5 - Guidelines for Specifying the Statistical ³
             ³              Distribution of Loss at Standard Quality  ³
             ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

       The two key parameters needed to setup an application of QTM are the
       expected value (EXPLOSS) and the variance of the loss (VARLOSS) at
       standard quality.  Basically, many different shapes for loss functions
       might be appropriate for a particular variable in a particular
       situation.  The exact form of the loss function chosen is sometimes
       not terribly important.  As a result, even after the loss function and
       all of its describing parameters (TARGET, PARM1, and PARM2) have been
       specified, the critical final phase of customizing a QTM application
       still remains... namely, choice of numerical values for the EXPLOSS
       and VARLOSS parameters.

       While it might be possible to specify the distribution of loss at
       standard quality using only technical assumptions and theoretical
       calculations, the more common approach is an empirical one in which
       actual data on the operation of the process are converted to losses,
       and the statistical distribution of those sample losses is then
       studied (say, using the CapQuant.EXE software system.)  If one has
       data on only a small number (dozen or so) of lots, it could be
       misleading to blindly use the observed sample values of the mean and
       variance of loss as EXPLOSS and VARLOSS, respectively.  After all,
       small sample estimates are notoriously imprecise.

       On the other hand, even if one had data for hundreds of lots, it could
       still be misleading to use the observed sample mean and variance of loss
       to establish QTM parameter values because even large sample results
       can be biased.  There could be several different causes of bias.  The
       data at hand may not represent the results of the process operating at
       (or even near) an industry-wide "standard" quality level.  The history
       being used might, in fact, reflect an operation in which the quality is
       either well above or well below standard.  Modern, new manufacturing
       equipment (using, say, robotics) or a change in ingredient formulations
       may have been introduced without changing the quality standard that was
       barely within the capability of the old technology.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 28 of 37



       If you aren't an expert on the operation of the manufacturing process
       in question, consult with an expert.  Develop opinions about the
       quality level of the process as reflected in its history.  Ask
       yourself, "How did I react to these quality monitoring results when I
       first saw them?" (Or, "How would I have reacted if I had been the
       manager in charge at that time?")  Were you ever concerned that the
       process might be out of "statistical control?"  Did you ever become
       alarmed because rejection rates jumped at final inspection or because
       in-process yields dropped?  Might you have reacted quite differently
       if the data had been only slightly different?  Or, would your
       reactions have been basically the same even if the data had shifted
       even more than it did in level and/or were even more highly variable
       from lot-to-lot?

       A common situation is that all the observed history reflects data taken
       from the process when it was operating well within its current process
       capability.  In other words, the variable could have deviated much more
       from its target without management having been alarmed at all!  This
       means that the values for EXPLOSS and VARLOSS that should be specified
       to QTM will indeed differ from what is observed in the history.
       General rules-of-thumb for this well-within-capability situation are...

          ...the EXPLOSS parameter should usually be chosen to be rather close
             to the observed value of the sample mean loss if the history that
             is available consists of 50 lots or more.

          ...the VARLOSS parameter, on the other hand, might be selected to be
             10 or even 100 times larger than the observed loss variance of the
             available data.

       There are two primary reasons for using a rather large VARLOSS value.
       Again, the history data may be very well behaved, and management would
       not have been alarmed even if the deviations of measurements from the
       target had been much larger than observed.  The second reason for using
       a large variance is that variables data are very rich in information.
       (Variables data are usually much more informative than nonconformance
       data.)  Specifically, as data from lots/days/weeks are accumulated to
       form monthly reports, so much information can be accumulated that the
       resulting I-plot confidence intervals will be extremely short.

       Charts with very narrow I-plots are not only difficult to read but also
       hard for management to "believe."  Such charts can defy management
       perception of the potential for accuracy in the measurements.  After
       all, in the pharmaceutical industry, testing tends to be destructive; an
       extremely small fraction of the product is actually tested.  For
       example, as little as 1/10,000 of the tablets in a lot are typically
       subjected to potency assay.  On the other hand, many many lots may be
       made during a given month, perhaps a hundred.  As a result, if the
       defect expectancy for a single measurement is more than about .25, one
       can end up with a total defect expectancy for the entire month of more
       than 25.  (Total defect expectancy for a month of attributes data
       collection is only rarely larger than 2 or 3.)  A convenient and
       reasonable approach to avoiding very high equivalent expectancies is to

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 29 of 37



       specify a VARLOSS parameter that is 1 or 2 orders of magnitude larger
       than what is observed in losses from well-behaved data.

       The summary report tables produced by QTM (and displayed on your
       screen or printed at your printer under item <4>) provide valuable
       information about the the EXPLOSS and VARLOSS values presently in use.
       Specifically, the last two columns of these tables (columns 6 and 7)
       display the mean loss and the variance of loss for all lots/days/weeks
       within each monthly reporting period.  If these within-month mean values
       and variances are quite different than what has been assumed, this is an
       indication that the application should be reevaluated.  In particular,
       if data appear to be well-behaved and yet the loss variance is larger
       than what has been hypothesized, this is indeed cause for concern.

       Charts with very narrow I-plots can also be replaced by next-period-ahead
       forecast confidence interval plots.  Forecast intervals will be much
       more wide (and more realistic) than present-period intervals when the
       quality process is more highly variable between periods than within
       periods.

       It would be possible to fine-tune the EXPLOSS and VARLOSS parameters of
       QTM by making repeated "iterations" as follows.  Parameters are
       first set and the within-month mean and variance of loss are observed.
       EXPLOSS and VARLOSS are then reset and the corresponding within-month
       estimates are again produced by QTM.  One continues until...

          ...within-month estimates stabilize near the operative EXPLOSS and
             VARLOSS values, and

          ...the resulting QMP Trend Charts indicate that process average
             quality is neither well above nor well below standard.

       On the other hand, because the reports of QTM are are written to disk,
       an easier and quicker procedure can be to read those reports from the
       first iteration into either the CapQuant software system or a
       statistical analysis package (such as SAS) and to do the fine-tuning
       there.

       *********************************************************************
                                    REFERENCES
       *********************************************************************

       [1]  "The Quality Measurement Plan (QMP)," Bell Communications Research
            Technical Reference TR-TSY-000438, Issue 1, April 1987.

       [2]  Gipe, Jan, and Guyton, Debbie, "Monitoring Quality Improvement on
            a PC," Proceedings of the ACM 1986 Conference on Personal and
            Small Computers, December 1986.

       [3]  Gipe, Jan, "QMP/Trend Users Manual," Bell Communications
            Research Technical Memorandum, February 1987

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 30 of 37



       [4]  Guyton, Debbie A. and Tang, Jen, "Introduction to Quality Trend
            Charts," Bell Communications Research Publication, Copyright 1986.

       [5]  Hoadley, Bruce, "The Quality Measurement Plan," Bell System
            Technical Journal, Volume 60, Number 2, February 1981, 215-271.

       [6]  Hoadley, Bruce, "Quality Measurement Plan (QMP)," Encyclopedia of
            Statistical Sciences (Kotz and Johnson, Eds.) Volume 7, 393-398,
            John Wiley, New York, 1986.

       [7]  Link, P. A., and Ripacki, B. R., "Quality Assurance Approach to
            Fiber Optic Cable," International Wire and Cable Symposium
            Proceedings, 1985.

       [8]  Obenchain, Bob, "QMP-On-Line User's Manual",  PMA/QC Statistics
            Committee, May 1990.

       [9]  Obenchain, Bob, "Introduction to Quality Trend Monitoring using
            QMP - The Quality Measurement Plan,"  PMA/QC Statistics Committee,
            January 1988.

       [10] Obenchain, Bob, and Kenett, Ron. "Windowed-At-Most-One-Change
            (WAMOC) Methodology for Quality Trend Monitoring."  Unpublished
            manuscript.  June 1993.

       [11] "Bellcore-Std-100 and Bellcore-Std-200 Inspection Resource
            Allocation Plans,"  Especially...Appendix A: Formulas used in the
            Quality Measurement Plan Algorithm, Bell Communications Research
            Technical Reference TR-TSY-000016, Issue 1, November 1985.

       *********************************************************************
                            QTM Software Update History
       *********************************************************************

       9311  ...Original Version; Link QTM.EXE with RTLink ver.6.10
       9403  ...Update WAMOC.EXE algorithm; Link QTM.EXE with RTLink ver.7.0

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 31 of 37



       ======================================================================
               Appendix 1.  Equivalent Nonconformances and Expectancy
       ======================================================================

       Knowledge of the statistical distribution of Loss when Quality is at a
       STANDARD LEVEL (that is within the Present Capability of the
       Manufacturing Process) is needed for Poissonization.  All that is
       involved here is a simple CHANGE-OF-SCALE that assures that the
       statistical distribution of the rescaled regret (when quality is at a
       "standard" level) has its expected (mean) value equal to its variance.

       The two statistical parameters which must be specified are:

                   EXPLOSS = Expected Regret at Standard Quality,
                   VARLOSS = Regret Variance at Standard Quality.

       Poissonization is accomplished by multiplying Regret by EXPLOSS and
       then dividing by VARLOSS...

                EQUIVALENT NONCONFORMS = REGRET * EXPLOSS / VARLOSS.

       Equivalent nonconformances have a statistical distribution that is
       like a Poisson or standardized gamma distribution in the sense that
       the mean and the variance of this distribution are EQUAL.  This common
       value is...

                    EQUIVALENT EXPECTANCY = EXPLOSS^2 / VARLOSS.

       A separate "QA Training Tool" software system, CapQuant.EXE, is ideal
       for analyzing historical process results to determine appropriate
       values for the EXPLOSS and VARLOSS parameters.

       By ignoring the time-series order of observations, these sorts of
       "Process Capability" calculations study the entire MARGINAL
       distribution of observed regret values in addition to estimating its
       mean and variance.

       In fact, CapQuant.EXE can also display the resulting EQUIVALENT
       NONCONFORMANCE values in Q-Q and/or P-P probability plots to verify
       that their statistical distributions are, in fact, well approximated
       by either a Poisson or a standardized gamma (chi-squared like)
       distribution.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 32 of 37



       ======================================================================
                 Appendix 2.  The Ten QTM Regret Function Families
       ======================================================================

       VARIABLES data measurements can be used in Quality Trend Monitoring
       by:
                  ...converting them into measures of economic
                     REGRET (loss or cost-of-poor-quality), and

                  ...Poissonizing that regret to determine
                     EQUIVALENT NONCONFORMANCES & EXPECTANCY.

       QTM allows the user to select a Regret Function from any of ten
       general families:

                      ATTRIBUT        QUADRATC        LINELOSS

              ONESIDED        LOGISTIC        INVMORML        RANGLOSS

                      OPPORTUN        DEFTEXPT        ENDPOINT

       ======================================================================

       Six of the Regret Function families quantify the economic impact of a
       SINGLE variables data measurement:

           ATTRIBUT, LOGISTIC, INVNORML, LINELOSS, ONESIDED and QUADRATC.

       Four of the Loss Function families quantify the economic impact of a
       PAIR of variables data measurements:

          OPPORTUN requires input of both Demand and Inventory.

          ENDPOINT and RANGLOSS require input of Minimum and Maximum values
              from a fixed sample size.

          DEFTEXPT requires direct input of Equivalent Defects & Expectancy.

       A Loss Function can also have as many as three PARAMETERS:

          TARGET = Value of Variable corresponding to ZERO LOSS.

          PARM1  = Lower Bound, Left-Right Indicator, etc.

          PARM2  = Upper Bound, Shortage Slope, Maximum Loss, etc.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 33 of 37



       ======================================================================

       Loss Type:      ATTRIBUT

       Description:    Economic Loss is either 0 (negligible) or 1
                       (complete).  A variable measurement outside of an
                       acceptable range indicates a nonconforming unit.

                                 Variables Measurement -->

                                   |                   |
             Loss = 1  ************|                   |************
                                   |                   |
                                   |                   |
                                   |                   |
              Loss = 0 ------------*********************------------
                                   |                   |
                                 Lower               Upper
                                 Bound               Bound

       Parameters:     No TARGET value need be specified.
                       PARM1 = Lower Bound; PARM2 = Upper Bound.

       Restrictions:   Lower Bound cannot exceed Upper Bound.

       ======================================================================

       Loss Type:      QUADRATC

       Description:    Economic Loss is assumed to be proportional
                       to the SQUARE of the deviation of the measured
                       value from its (zero defect) TARGET value.

                                  Variables Measurement -->

                         *                  |                  *
                          *                 |                 *
                           **               |               **
                             **             |             **
                               **           |          ***
                                  ***       |       ***
                                     ****   |   ****
             Loss = 0  ------------------*******---------------------
                                            |
                                         TARGET

                            LOSS = ( Value - TARGET )^2

       Parameters:     TARGET = Value corresponding to ZERO LOSS.
                       No PARM1 or PARM2 values need be specified.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 34 of 37



       ======================================================================

       Loss Type:      LINELOSS

       Description:    Economic Loss is assumed to be directly
                       proportional to the measured value.

                                |    Variables Measurement -->
                                |                               ****
                                |                           ****
                                |                       ****
                                |                   ****
                                |               ****
                                |           ****
                                |       ****
                                |   ****
             Loss = 0  ---------****-----------------------------
                                |
                       TARGET = 0

       Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

       Restrictions:   Variable measurements must be non-negative.
                       TARGET is implicitly ZERO.

       ======================================================================

       Loss Type:      ONESIDED

       Description:    Economic Loss is ZERO on one side of the TARGET
                       and proportional to the SQUARE of the deviation
                       from TARGET on the other side.

                       *          Variables Measurement -->
                        *
                         *                  |
                          *                 |       PARM1 = +1
                           **               |
                             **             |       Zero Loss on
                               **           |       Right Side.
                                  ***       |
                                     ****   |
             Loss = 0  ------------------****************************
                                            |
                                         TARGET

       Parameters:     PARM1 is a LEFT(-1) or RIGHT(+1) indicator.
                       PARM1 = -1 indicates zero loss left of TARGET.
                       No PARM2 value need be specified.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 35 of 37



       ======================================================================

       Loss Type:      OPPORTUN

       Description:    Two variables measurements are required, a DEMAND
                       level & an INVENTORY level for a perishable product.
                       Economic Loss is proportional to production cost per
                       unit when inventory > demand, but there is a Profit
                       (Opportunity) Loss per unit when demand > inventory.

                           ****        DEMAND -->          **
                               ****               |      **
                                   ****           |    **
                                       ****       |  **
                                           ****   |**
             LOSS = 0  ------------------------****-----------------------
                                                  |
                                           DEMAND = INVENTORY

       Parameters:     PARM1 = Loss per Unit of Excess Inventory.
                       PARM2 = Loss per Unit of Inventory Shortage.
                       No TARGET value need be specified.

       Restrictions:   DEMAND, INVENTORY, PARM1, and PARM2 non-negative.

       ======================================================================

       Loss Type:      ENDPOINT (quadratic)

       Description:    Two variables measurements are required, the
                       MINIMUM and MAXIMUM observed values in a random
                       sample of fixed size (say, 10 measurements.)
                       Economic Loss is assumed to be the SUM of the
                       QUADRATC losses at the min. and max. values.

                          *                 |                 *
                           **---------------|               **
                            |**             |             **
                            |  **           |          ***
                            |     ***       |-------***
                            |        ****   |   ****|
             Loss = 0  -----+------------*******----+----------------
                           MIN              |      MAX
                            |            TARGET     |

                  LOSS = ( MIN - TARGET )^2 + ( MAX - TARGET )^2

       Parameters:     TARGET = Value corresponding to ZERO LOSS.
                       No PARM1 or PARM2 values need be specified.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 36 of 37



       ======================================================================

       Loss Type:      RANGLOSS

       Description:    Two variables measurements are required, the
                       MINIMUM and MAXIMUM observed values in a random
                       sample of fixed size.  Economic Loss is assumed
                       to be proportional to the RANGE between the
                       Maximum and Minimum values.

                                |                           ****
                                |                       ****
                                |                   ****
                                |               ****
                                |           ****
                                |       ****
                                |   ****
             Loss = 0  ---------****-----------------------------
                                |         RANGE -->

                       TARGET = 0

       Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

       Restrictions:   TARGET is implicitly ZERO.

       ======================================================================

       Loss Type:      LOGISTIC

       Description:    Economic loss follows a double-logit pattern that
                       is V-shaped in the center but flat like ATTRIBUT
                       in its tails.  This limits the impact of large
                       absolute DEVIATIONS of values from the TARGET.

         PARM2 = 1  *****          |  Measurement-->   |          ******
        (max loss)       ******    |                   |    ******
                               *****                   *****
                                   |****           ****|
                                   |    ***     ***    |
                                   |       ** **       |
             Loss = 0  ----------------------*----------------------
                                   |         |         |
                           minus PARM1    TARGET     plus PARM1

                         LOSS = DEVIATION / ( PARM1 + DEVIATION )

       Parameters:     TARGET = Value corresponding to ZERO LOSS.
                       PARM1  = Half-Width to Half-Height (Loss = 0.50.)
                       PARM2  = MAXIMUM possible Loss = 1.00.

           QTM.EXE, ver.9403 . . . . . . . . . . . . . . . . Page 37 of 37



       ======================================================================

       Loss Type:      INVNORML

       Description:    Economic loss looks like an up-side-down normal
                       distribution.  Thus loss is flat like ATTRIBUT
                       in its tails, but loss is smoothly quadratic when
                       DEVIATIONS from the TARGET are small.

             PARM2 = 1   ******    |  Measurement-->   |     ******
             (max loss)        ****|                   |*****
                                   ***               ***
                                   |  **           **  |
                                   |    *         *    |
                                   |     **     **     |
             Loss = 0  --------------------*****--------------------
                                   |         |         |
                           minus PARM1    TARGET     plus PARM1

                   LOSS = 1.0 - (0.5) to the power [(DEVIATION/PARM1)^2]

       Parameters:     TARGET = Value corresponding to ZERO LOSS.
                       PARM1  = Half-Width to Half-Height (Loss = 0.50.)
                       PARM2  = MAXIMUM possible Loss = 1.00.

       ======================================================================

       Loss Type:      DEFTEXPT

       Description:    Two variables measurements are required, the
                       EQUIVALENT DEFECTS and EQUIVALENT EXPECTANCY for an
                       individual production lot.

                       This option is made available so that QTM can be
                       used to ACCUMULATE equivalent nonconformances &
                       expectancies over production lots within monthly
                       reporting periods.

                       With input data of this type, no Loss Function is
                       actually specified.  Similarly, no LOSSMEAN and
                       LOSSVAR are needed to Poissonize the loss.

       Parameters:     No TARGET, PARM1 or PARM2 values need be specified.

       Restrictions:   At most one loss function of the DEFTEXPT type is
                       usually need for a dataset.

       ======================================================================