ELOGANAL

                Copyright (c) 1990 H L Hendrick, all rights reserved.


                ELOGANAL is a shareware microcomputer program  which  allows
           the  user  to  perform  the  calculations  involved  in analyzing
           electric logs run on prospective oil and gas wells.   The program
           was written in the "C" language for reduced code size,  speed and
           mathematical  accuracy.

                If this program  is  useful  to  you,  please  register  the
           program  with  the  author  by sending a check for $100.00 to H L
           Hendrick P.O. Box 79530 Houston TX 77279. Program support and up-
           date information will be furnished to registered users.

                This package contains computer software and printed material
           copyrighted by H L Hendrick.  You should carefully read the  fol-
           lowing  terms  and conditions before using the software.   Use of
           the software indicates your acceptance of the  software  and  all
           terms and conditions.

                This software product is licensed to one user for use on one
           machine only.

                Under  international  copyright laws there are penalties for
           making unauthorized copies.   You may make and distribute  copies
           of the program to others for their consideration.   Any copy that
           you make must include reproduction of the  copyright  notice  and
           warranty disclaimer.  You may not sell any copy that you make.

                H  L  Hendrick  makes no express or implied warranty for the
           software which is provided solely on an  "as  is"  basis.    H  L
           Hendrick disclaims all conditions and warranties, whether express
           or  implied  with  regard to the software,  including all implied
           conditions or warranties of fitness for a particular purpose.   H
           L  Hendrick shall not have any liability or responsibility of any
           kind including special, indirect or consequential damages,  aris-
           ing  out  of  or  resulting  from  such  software  or  the use or
           modification thereof.

                H L Hendrick is a member of  the  Association  of  Shareware
           Professionals  (ASP).  ASP  wants to make sure that the shareware
           principle  works  for  you.  If  you  are  unable  to  resolve  a
           shareware-related  problem  with  an ASP member by contacting the
           member directly,  ASP may be able to help.  The ASP Ombudsman can
           help,  but  does  not  provide  technical  support  for  members'
           products.   Please write to the ASP Ombudsman at  P.O.  Box  5786
           Bellevue,  WA  98006 or send a CompuServe message via easyplex to
           ASP Ombudsman 70007,3536



                                           1












                The design goals of the program were  to  create  a  program
           which would be of use to the log analyst in working old type logs
           as well as the new more modern type logs.  Empirical routines are
           included  to  estimate the oil or gas content of the flushed zone
           with an option to change it.  Porosity estimates  using  the  old
           short normal technique are included with an option to re-enter if
           the value is not deemed in an acceptable range.  Rw can be calcu-
           lated from the SP curve or from an API water analysis as well  as
           the  Rwa  method  or  by direct input of ppm of Cl or NaCl.   The
           program uses standard oil field analysis methods, formula and al-
           gorithms.   The statistical  and  empirical  routines  used  were
           recommended  in  publications  by  Douglas Hilchie and Jim Brock.
           These publications are available from the  Society  of  Petroleum
           Engineers.    Chart books from Schlumberger,  Dresser and GO were
           also used in designing and testing the program.

                Estimates of critical water can be made from a list of  for-
           mation  options or by entering core permeability.   Relative per-
           meability is calculated for all reservoir  fluids  regardless  of
           their presence.  Water cut is estimated using Reservoir Engineer-
           ing  techniques  utilizing  relative permeability.   The critical
           water is estimated from statistical data for the type  of  forma-
           tion  selected  and  may  not  be correlative with the calculated
           water cut.

                The author of the program assumes the user is aware  of  the
           uses  and  limitations  of electric logs run on drilled wells and
           does not intend to present a tutorial in log analysis.  Petroleum
           oriented literature should be reviewed for instructions regarding
           the correct application of logging techniques.  Standard  logging
           symbols are used in the screen presentation and printout.

                                 HARDWARE REQUIREMENTS

                Minimum requirements are a 128K,  one disk drive, 8086/8088,
           MS or PC DOS 2.xx or greater microcomputer or compatible.

                If a co-processor is present it will be  used.    If  a  co-
           processor  is  not  present,  the  program  will  emulate the co-
           processor using an internal 7K emulator.


                In order to use the program,  format a new disk and  install
           your operating system. Copy ELOGANAL.EXE to the new disk. Use the
           new program disk you created and boot up.  Enter ELOGANAL and run
           the program. If you prefer, Copy the program to your hard disk.

                Follow the menu prompts.  Screen displays will be  presented
           and remain on screen until you enter a requested key.




                                           2












                The program can create and maintain a data file for each log
           analysis.  Provisions  to display to screen or print the file are
           included.   The file name selected should relate to the  name  of
           the  well or operator.  These files are stored in an ASCll format
           and can be incorporated in a report prepared with a word  proces-
           sor.

                After the initial run through the program,  the UP ARROW and
           DOWN ARROW keys will toggle the Main (underlined heading)  menus.
           A new depth can be input by entering a RIGHT ARROW or LEFT ARROW.
           When  a  Main  (underlined  heading)  menu  is  displayed,  a re-
           calculation can be made by entering <RETURN>. If the shale volume
           or the type of shale changes,  a new porosity will be  calculated
           and  corrections  made  based  on the shale changes.  To exit the
           program from a Main menu (underlined heading) enter END key.

                Data entry begins  with  input  from  the  log  heading  and
           proceeds  in  a logical manner to set flags and constants used in
           the calculations for the specific log being analyzed.

                Entered log heading data will be displayed to screen with an
           option to change a value.   Most pre-1958 logs did not record the
           Rmf and Rmc.   If this is the case, you will be prompted to enter
           a zero.   The program will estimate both from Rm and the tempera-
           ture will be set to the temperature of the mud.

                                      TYPE OF MUD

                     1-Light weight fresh water muds sets density
                       of fluid to 1.0 and travel time to 189.

                     2-Heavy weight fresh water muds sets density
                       of fluid to 1.01 and travel time to 189.

                     3-Salt water base mud sets density of fluid to
                       1.1 and travel time to 185.

                The  log matrix lithology flag must be set for all log types
           requested even though a Density,  Neutron  or Sonic  log  is  not
           available.  If one or all of these logs is not available, setting
           these flags  will not affect the program.

                                 LOG MATRIX LITHOLOGY
                                 ~~~~~~~~~~~~~~~~~~~~
                     1-Sand, sets matrix flags for density log to
                       2.65, Sonic log to 55.5 and neutron response
                       to a correction algorithm.

                     2-Lime, sets matrix flags for density log to
                       2.71, Sonic log to 47.5

                     3-Dolomite, sets matrix flags for density log to

                                           3












                       2.87, Sonic log to 43.5 and neutron response
                       to a correction algorithm.

                     4-User input allows the user to input the desired
                       factor.



                                   FORMATION OPTIONS
                                   ~~~~~~~~~~~~~~~~~
                     1- Soft Formations, sets MXP to 2.15,COER
                        to .62 and SXP to 2. (Humble).

                     2-Hard formations, sets MXP to 2, COER to 1
                       and SXP to 2. (Archie).

                     3-Low porosity carbonates, uses the Shell
                       developed method and sets SXP to 2, COER
                       to 1 with MXP being set based on porosity.

                     4-User input allows the user to input the
                       desired factors.

                                      Rw OPTIONS
                                      ~~~~~~~~~~
                     1- Input Rw, allows direct input of known
                        water resistivity and temperature.

                     2-Compute from salinity, allows computation
                       of water resistivity from known ppm of NACL or CL.

                     3-Compute from Rwa, uses the method recommended
                       by the major logging companies for computation
                       of Rw from log data.

                     4-Compute from SSP, uses the method recommended
                       by the major logging companies for computation
                       of Rw from the SP curve.

                     5-Compute from analysis, allows computation
                       of Rw from a known API water analysis.
                       Factors used in the computation are set
                       for a water with a total solids content of
                       70000 ppm NACL.  The user has the option
                       to change the factors to the correct values
                       for the water being used.  These factors are
                       available in all logging company chart books.

                                 SHALE CONTENT OPTIONS
                                 ~~~~~~~~~~~~~~~~~~~~~



                                           4












                Seven options are available for calculating VOLSH. Selection
           of  any option other than no correction,  requires a selection of
           the type of shale.

                                   1-No corrections

                                  Sets VOLSH to zero.

                                   2-Direct input

                          VOLSH must be entered in a decimal fraction.

                                   3-Gamma or SP index

                          Calculates VOLSH from the gamma or SP.

                                   4-Tertiary age rocks

                          Calculates VOLSH using gamma index as proposed
                          by Larinov.

                                   5-Older age rocks

                          Calculates VOLSH using gamma index as proposed
                          by Larinov.

                                   6-Density-Neutron
                                   7-Density-Sonic
                                   8-Sonic-Neutron
                          Calculates VOLSH using a ratio of porosity
                          technique.

                Five options are  available  for  calculating  porosity.  If
           x-plot  is selected,  four combinations of x-plots are available.
           If direct input is selected,  the porosity input will not be cor-
           rected for fluid or shale content;  however,  the correction flag
           must be set in order to output the water cut in  the  final  dis-
           play.

                                   POROSITY OPTIONS
                                   ~~~~~~~~~~~~~~~~
                                    1-Direct input
                                    2-Sonic
                                    3-Density
                                    4-X-plots
                                    5-Short Normal

                If the x-plots option is selected,  the x-plot menu will ap-
           pear as follows:

                                      1-CDL & CNL
                                      2-Sonic & CNL

                                           5












                                      3-CDL & SNP
                                      4-Sonic & SNP

                The Short Normal option should be used only  when  no  other
           option  is  available.   It is an empirical estimate and only ap-
           plies where specific conditions of invasion exist.

                              ENTER SOURCE OF RESISTIVITY
                              ~~~~~~~~~~~~~~~~~~~~~~~~~~~
                     1-Direct input, must be entered in decimal
                       fraction.

                     2-Induction Electrical Log, This option requires
                       input of the Induction and 16 inch normal. An
                       empirical correction is made as suggested by
                       Hilchie in his book "Old Electrical Log
                       Interpretation".

                     3-Dual Induction logs with SFL, this option requires
                       input of deep, medium and shallow resistivity.
                       A "Tornado Chart" correction is made mathematically.

                     4-Dual Induction logs with laterolog, this option
                       requires input of deep, medium and shallow
                       resistivity.  A "Tornado Chart" correction is made
                       mathematically.

                     5-Dual Laterolog (20' Sequential), correction made
                       on tool type.

                     6-Dual Laterolog (28' Simultaneous), correction made
                       on tool type.

                       A 16 inch normal will corrected for hole size.  If a
                       caliper survey is not available, the correction will
                       be made assuming a gauge hole.

                             SELECTION FOR CRITICAL WATER
                             ~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                Option selection for several formations on  which  empirical
           data is available can be made.  If the logged formation is not on
           the  list  of  options  or  the  formation is not known or if one
           prefers to enter a known core permeability,  option o  should  be
           selected.   If the logged formation is not on the list of options
           and a core permeability is not known,  options o must be selected
           and  when the prompt ask for entry,  a zero must be entered.   If
           this is the case,  the critical water cannot be estimated and the
           permeabilities and water cut cannot be estimated.

                After  all  data  is  entered,  the program calculations are
           made.  All calculations are corrected for  depth,  shale  volume,
           fluid content and temperature. Resistivity is corrected as stated

                                           6












           above.  An empirical estimate is made of critical water, absolute
           permeability,  relative permeability,  effective permeability and
           water cut.  Water cut for oil is reported in a fraction. Water to
           gas ratio is reported as bbls. per mcf.

                Printer output is optional.

                After entering log data and calculating factors for a  zone,
           recalculation  of other zones of interest can be made without en-
           tering all new data.   The log heading data and type of mud  does
           not change.  Use the arrow and entry key for rapid calculation of
           additional zones of interest.

                                   PLAYING "WHAT IF"

                In order to play "what if",  after the initial  run  through
           the  program,  use the arrow keys to toggle the main menus.  When
           changes are made in the log matrix option or shale volume or type
           of shale,  porosity calculations made from  Density,  Neutron  or
           Sonic logs or x-plots are recalculated.

                Each time the depth is changed,  the temperature of the for-
           mation and the Rw is automatically  recalculated.  Any  parameter
           that changes with depth i.e.,resistivity,  shale volume, porosity
           must be recalculated.

                                    To exit the program:

                                    1-Enter the END key or
                                    2-Enter control C or
                                    3-Enter control break.

                                  MISCELLANEOUS HINTS

                Names of logs used in the program are based on Schlumberger
           trade marks.  Logs from other companies which are compatible  may
           be used in the program.

                Neutron  logs  from each logging company are not compatible.
           The program requires the log matrix for these logs to be  set  to
           lime  and the charts from the logging company used to correct the
           log reading to lime before using the cross-plot option.  The  CNL
           is corrected for mud weight and temperature. The SNP is corrected
           for hole size.  If a caliper survey is not available, the correc-
           tion will be made assuming a gauge hole.

                The gamma ray log entry will be corrected for mud weight and
           hole size.   If a caliper survey is not available, the correction
           will be made assuming a gauge hole.

                When entering data from the log heading, operator name, well
           name, location, county and state will accept 60 characters each.

                                           7













                Direct entry of porosity and  shale  content must    be  en-
           tered  in  decimal  fractions  NOT  per-cent.  In  other  words a
           porosity of 30% must be entered as .30 not 30.

                When entering data from a density log, the entry may be made
           in either a decimal fraction or the entry may be made  in  gm/cc.
           The    mathematics    involved  requires  that  the   entries  be
           consistent.   In other words,  if a shale correction is made  and
           the    formation  density is entered in gm/cc,  the shale density
           must also be entered in gm/cc.  If the formation density porosity
           is entered in decimal fraction,  the shale density porosity  must
           also  be  entered in decimal fraction.   Neutron porosity must be
           entered in decimal fraction.

                Porosity crossplots for density and neutron logs are made by
           a crossplot  algorithm ,  after correcting for  fluid  and  shale
           content.  Porosity    crossplots   using a  sonic log are made by
           converting  all  data to  lime  matrix and    averaging,    after
           correcting for fluid and shale content.

                Factors  used  to  correct   porosity  for fluid content are
           calculated assuming a normal pressure gradient and a natural  gas
           gravity of 0.65.  The residual oil saturation in the flushed zone
           is estimated based on empirical data and API gravity.    The  low
           gravity cut off is 10 degrees API and the high gravity cut off is
           50 degrees API.   In other words, if one enters an API gravity of
           less than 10,  the value for 10 will be used.   If one  enters  a
           gravity greater than 50, The value for 50 will be used.

                If  the Induction Electric log option is selected and the 16
           inch normal is greater than 10 times the mud resistivity,  an in-
           termediate  evaluation is made for Sw,  Porosity and Ro using the
           Rocky Mountain method.  If a shale option is selected,  the Sw is
           reduced  by  10  per-cent and the porosity is adjusted to reflect
           the decrease in Sw.   This information will be displayed  to  the
           screen but will not be printed on the final print out.

                In  order  to maintain maximum versatility and range of data
           input methods and allow the user to play "what if" ,  error trap-
           ping  is  kept at a minimum.   It is possible to enter data which
           will cause math errors (divide by zero ,  etc).   Care should  be
           used  when entering data and the menu prompts should be followed.
           If one enters data which causes a math error,  the  program  will
           notify the user and abort to the operating system.

                Support  for  registered  users  is  provided by mail to H L
           Hendrick at P.O. Box 79530, Houston,  TX 77279 or by telephone at
           713-932-9408 or through CompuServe at address 76217,1171.




                                           8