XCLONE - Copy Utility for XPORT.EXE

                                   Version 1.3

                    Copyright (C) 1992 by Digital Innovations
                              All rights reserved.

            If you would like to use XPORT, the D. I. File Transporter,
       but you don't already have a way to transfer files between two
       systems with different disk sizes, or incompatible disk formats
       (or the program you do have just WON'T WORK), this utility will
       allow you to get XPORT.EXE to the system that doesn't have it.
       All you need on the inaccessible system is your DOS disk, with the
       files MODE.COM and DEBUG.COM (or SID.EXE if you are using DR-DOS).
       Just run XCLONE on the system that has XPORT.EXE on it, and follow
       the simple directions.

            Basically, you will be following these steps:

       1)  Connect a null modem cable to both systems.

       2)  Run XCLONE on the source system (be sure XPORT.EXE is in the
           same directory as XCLONE).

       3)  Boot the other system - should be at the DOS prompt.

       4)  Type "MODE COMx:96,N,8,2", followed by ENTER, then type "CTTY
           COMx", followed by ENTER on the other system - its console
           will now be redirected to the specified serial port.
           (The 'x' in COMx is the port number that the cable is
           connected to, COM1 or COM2).

       5)  Hit any key on the source system.  XCLONE will ask you to
           verify the destination drive and directory.  If you approve
           the destination, it will create a copy of XPORT.EXE on the
           other system's disk.

            XCLONE takes control of the target system, runs DEBUG (or
       SID if you are using DR-DOS), sends a short loader program to it,
       starts it up and transfers the contents of XPORT.EXE into the
       target system's memory (the transfer and verification process
       takes less than a minute).  It then commands DEBUG to write the
       data to the disk, and names the resulting file XPORT.EXE.  If you
       are using SID under DR-DOS, you will also be prompted to enter the
       number of the COM port to which you have the cable connected, since
       there is no way for XCLONE to automatically determine this under
       SID.

            The cable that you use must include a connection between the
       DTR output on the source system and the DSR input on the target,
       and the RTS output on the source and the CTS input on the target;
       this is required by the DOS CTTY function.  Or, you can just connect
       DTR to DSR and RTS to CTS on the target system end of the cable -
       that makes CTTY happy, too.  On some systems, either MODE or CTTY
       doesn't appear to enable DTR, however; in this case, try doing a
       copy of a short file, such as CONFIG.SYS, to the port using COPY
       FILENAME.EXT COMx, before issuing the CTTY COMx command.  DTR should
       then be enabled, allowing CTTY to work.  Recommended cable connections
       are as shown below:

                     SOURCE                TARGET
                     (25 pin)              (25 pin)

                 DTR (pin 20) ------------ (pin 6) DSR
                 RTS (pin 4)  ------------ (pin 5) CTS
                  TD (pin 2)  ------------ (pin 3) RD
                  RD (pin 3)  ------------ (pin 2) TD
              GROUND (pin 7)  ------------ (pin 7) GROUND


                     SOURCE                TARGET
                     (9 pin)               (9 pin)

                 DTR (pin 4)  ------------ (pin 6) DSR
                 RTS (pin 7)  ------------ (pin 8) CTS
                  TD (pin 3)  ------------ (pin 2) RD
                  RD (pin 2)  ------------ (pin 3) TD
              GROUND (pin 5)  ------------ (pin 5) GROUND


                     SOURCE                TARGET
                     (25 pin)              (9 pin)

                 DTR (pin 20) ------------ (pin 6) DSR
                 RTS (pin 4)  ------------ (pin 8) CTS
                  TD (pin 2)  ------------ (pin 2) RD
                  RD (pin 3)  ------------ (pin 3) TD
              GROUND (pin 7)  ------------ (pin 5) GROUND


                     SOURCE                TARGET
                     (9 pin)               (25 pin)

                 DTR (pin 4)  ------------ (pin 6) DSR
                 RTS (pin 7)  ------------ (pin 5) CTS
                  TD (pin 3)  ------------ (pin 3) RD
                  RD (pin 2)  ------------ (pin 2) TD
              GROUND (pin 5)  ------------ (pin 7) GROUND


            Universal null modem cables, including all the above
       connections with both types of female connectors on both ends are
       available from various distributors.  One such distributor is
       DALCO Electronics in Franklin, OH, 1-800-445-5342.  Their null
       modem cable part number is 42965.


            Helpful tip:  If for some reason you have XPORT on one
       system, and XCLONE on the other, and you need to get XCLONE itself
       to the other system, you can transfer XCLONE disguised as XPORT.
       Just copy XCLONE.COM to XPORT.EXE, run XCLONE, and let it transfer
       its disguised copy.  Once transferred, you can then rename it to
       XCLONE.COM on the other system.

                                   Ken Logsdon
                               Digital Innovations