****************************  VIDEO MODES  ***********************************

ASM32 video mode subroutines (C) Copyright 1993 Douglas Herr
All rights reserved

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

HGRAPH:      establishes Hercules graphics mode, pages 0 & 1
HGRAPH0:     establishes Hercules graphics mode, clear page 0 only
Source:      hgraph.asm ($herc.asm, $hmode.asm)

Hercules or compatible required
(including Hercules InColor)

Call with:   no parameters
Returns:     if CF = 1, no Hercules installed
             if CF = 0, AX = code for Hercules model
             128 = HGC
             144 = HGC+
             208 = InC
Uses:        AX, ECX, CF
Supports:    Hercules graphics cards and compatibles: graphics mode
             see also Use64k in SYSTEM.DOC
Example:     call    hgraph      ; establish graphics mode
             jc      no_hercules ; drat!



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

HRAM8029:    establish an 80-column, 29-row RamFont mode, loading a
             standard 8x12 character font in RAM
Source:      hram8029.asm ($herc.asm, $hmode.asm, $h8x12.asm, f8x12rle.asm,
                           $rld.asm)

HRAM8043:    establish an 80-column, 43-row RamFont mode, loading a
             standard 8x8 character font in RAM
Source:      hram8043.asm ($herc.asm, $hmode.asm, $h8x8.asm, f8x8.asm)

HRAM9025:    establish a 90-column, 25-row RamFont mode using
             standard ROM characters
Source:      hram9025.asm ($herc.asm, $hmode.asm)

HRAM9029:    establish a 90-column, 29-row RamFont mode, loading a
             standard 8x12 character font in RAM
Source:      hram9029.asm ($herc.asm, $hmode.asm, $h8x12.asm, f8x12lre.asm,
                           $rld.asm)

HRAM9043:    establish a 90-column, 43-row RamFont mode, loading a
             standard 8x8 character font in RAM
Source:      hram9043.asm ($herc.asm, $hmode.asm, $h8x8.asm, f8x8.asm)

Hercules RamFont card required
(including Hercules InColor)

Note:        use htext to restore normal 80 x 25 text mode

Call with:   no parameters
Returns:     if CF = 1, no RamFont card installed
             if CF = 0, AX = code for Hercules model
             144 = HGC+
             208 = InC
Uses:        AX, CF; all other flags and registers are saved
Supports:    HGC+ and InC cards: 4k RamFont mode
Example:     call  hram8043      ; RamFont mode: 80x43
             jc    no_ramfont    ; drat!


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

HTEXT:       establish (or restore) Hercules text mode
Source:      htext.asm ($herc, $hmode)

Call with:   no parameters
Returns:     if CF = 1, no Hercules installed
             if CF = 0, AX = code for Hercules model
             128 = HGC
             144 = HGC+
             208 = InC
Uses:        AX, CF
Supports:    Hercules graphics cards and compatibles: text mode
             (including Hercules InColor)
Example:     call  htext         ; Hercules text mode
             jc    no_herc       ; drat!



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MODE13243:   switches supported systems to 132 column, 43 row text mode
MODE13225:   switches supported systems to 132 column, 25 row text mode
Source:      mode132.asm (isevga.asm)

Call with:   AX = SuperEGA/VGA code returned by IsSEVGA
Returns:     CF = 1 if mode not supported
             if CF = 0, AX = mode number
Uses:        AX, CF; all other registers and flags are saved
Supports:    Equipment detected by IsSEVGA (see IsSEVGA in SYSTEM.DOC).
             Most VGA boards require a multi-frequency monitor to
             use 132-column modes; consult your board's documentation.
             The Paradise EGA 480 requires an EGA monitor; the Everex
             EGA works with Monochrome and EGA monitors, and the 25-row
             mode also works with a CGA monitor.
Example:

include code32.inc

extrn   issevga:near, mode13243:near

; code
        .
        .
        .
        call  issevga        ; test for Super EGA or Super VGA
        jc    no132          ; no good - skip
        call  mode13243      ; set mode
        jc    no132          ; no good
        .
        .
        .




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TOCOLOR:     switches system to color text mode; may be used to switch
             monitors on a 2-monitor system, or to switch to the standard
             80-column, 25-rows color mode from other color modes
Source:      tocolor.asm ($6845.asm)

Call with:   no parameters
Returns:     CF = 1 if no color monitor
             CF = 0 if successful
Uses:        CF; all registers and all other flags are saved
Example:

include code32.inc

extrn   tocolor:near

; code
        .
        .
        .
        call  tocolor
        jc    no_color
        .
        .
        .


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TOMONO:      switches system to monochrome text mode; may be used either
             to switch active monitors on a 2-monitor sysem or to switch
             to monchrome text mode (80x25) from graphics mode (EGA or
             Hercules).
Source:      tocolor.asm ($6845.asm)

Call with:   no parameters
Returns:     CF = 1 if no monochrome or InColor monitor
             CF = 0 if successful
Uses:        CF; all registers and all other flags are saved
Example:

include code32.inc

extrn   tomono:near

; code
        .
        .
        .
        call  modemono
        jc    no_mono
        .
        .
        .


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MODE43:      switch EGA to 80x43 text mode or VGA to 80x50 text mode
             Mode43 switches an EGA to the 80-column, 43-row text mode from
             any color mode or any EGA monochrome mode, or switches a color
             VGA to 80x50 text mode from any other color mode.
Source:      mode43.asm

Call with:   no parameters
Returns:     if CF = 1, AX = 0 if no EGA or VGA in system
                        AX = -1 if EGA connected to CGA monitor
             if CF = 0, AX = 3 if EGA or VGA connected to color monitor
                        AX = 7 if EGA or VGA connected to monochrome monitor
Uses:        AX, CF; all other registers and flags are saved
Example:     call  mode43
             jc    noega



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SVGA16:      set Super VGA mode
Source:      svga16.asm (banks.asm, $graph.asm)

Call with:   AX = 16-color mode desired
             AX = 0 for 800x600
             AX = 1 for 1024x768

             ASM32's SVGA subroutines are derived from John Bridges'
             public domain VGAKIT board identification and bank switching code.
             Boards supported are:

             Ahead Technologies
             ATI
             Chips & Technologies
             Everex
             Genoa GVGA
             NCR
             Oak Technologies
             Paradise (Western Digital)
             Trident
             Trident 8900
             Tseng (Genoa, Orchid, Willow)
             Tseng 4000
             VESA standard
             Video 7

             I have not been able to test SVGA16 on all boards; please
             let me know if you encounter difficulties.

Returns:     if CF = 0, AX = extended BIOS mode number
             if CF = 1, requested mode is not available
             SVGA16 cannot determine if the monitor you are using will
             work with the requested mode.  Monitor damage may result
             from improper use of SVGA16.

Example:

include code32.inc

public mygraph
extrn  whichvga:near, extrn  svga16:near

; code
mygraph proc   near
; I want to use a 16-color 1024x768 mode if available
; start by calling WhichVGA to determine if the equipment is capable
        call   whichvga
        or     ax,ax            ; SuperVGA installed?
        jz     no_svga          ; nope, use some other mode
        mov    ax,1             ; specify 1024x768 mode
        call   svga16


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SVGA256:     set Super VGA 256-color mode
Source:      svga256.asm (banks.asm)

Call with:   AX = 256-color mode desired
             AX = 0 for  640x400
             AX = 1 for  640x480
             AX = 2 for  800x600
             AX = 3 for 1024x768

             ASM32's SVGA256 subroutines are derived from John Bridges'
             public domain VGAKIT board identification and bank switching code.

             Equipment supported is listed under SVGA16, plus:

             Compaq (640x480 only)


Returns:     if CF = 0, AX = extended BIOS mode number
             if CF = 1, requested mode is not available
             SVGA256 cannot determine if the monitor you are using will
             work with the requested mode.  Monitor damage may result
             from improper use of SVGA256.

Example:     see SVGA16



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VGA13X:      changes standard VGA systems to undocumented 256-color graphics
             modes.  ASM32 graphics subroutines support 4 VGA13X modes
             with up to 4 pages.  See also XModeClear.
             VGA13X is derived from public domain code from John Bridges
             and Themie Gouthas.
Source:      vga13x.asm (crtc.13x, $graph.asm)

Call with:   AX = VGA13X mode number
              0 = 320 x 200, 4 pages
              1 = 320 x 240, 3 pages
              2 = 320 x 400, 2 pages
              3 = 360 x 480, 1 page
Returns:     nothing
Uses:        nothing
Supports:    VGA or SVGA only: graphics mode
Example:

include code32.inc

extrn   vga13x:proc

; code
        .
        .
        .
        call   getcrt
        cmp    al,3
        jne    short oops            ; do something else if no VGA
        mov    ax,2                  ; 320 x 400, 2 pages
        call   vga13x




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

XMODE16:     establish SuperEGA/SuperVGA graphics mode and configure
             ASM32 graphics subroutines to work with the mode.
XMODECLEAR:  restore ASM32's default graphics configuration
Source:      xmode16.asm ($graph.asm)

Parameters:  maximum x, maximum y, registers as required to set mode.
             XMode16 assumes that the mode is set with AH = 0.
Returns:     nothing
Uses:        All registers and flags saved.
Supports:    16-color EGA/VGA-style graphics modes, up to 800 x 600 pixels.
             Various equipment.  You must have the required equipment and
             use the correct mode number;  hardware damage may result from
             improper use of XMode16.  I cannot be held responsible for
             damage resulting from use or misuse of XMode16.  Use XMode16
             if your equipment is not supported by SVGA16.

             If 800 horizontal pixels are available, maxX% should be 799.
             Similarly, if 600 vertical pixels are possible, maxY% should
             be 599.

             Your graphics card manual lists mode numbers, monitor
             requirements, and the number of horizontal and vertical
             pixels corresponding to the mode.  Mode numbers are usually
             in hex format.  Some modes and corresponding mode numbers
             are listed on the next pages.




    Equipment            mode     mode number   Example

    Orchid ProDesigner   800x600        29h     mov   ax,799
    STB EM/16                                   push  ax
    Genoa                                       mov   ax,599
    Sigma X16                                   push  ax
    (Tseng chip set)                            mov   al,29h
                                                call  xmode16


    Everex MED EGA       640X480   AL = 70h, BL = 00h
    (Micro Enhancer Deluxe)
                         752x410   AL = 70h, BL = 01h
                                                mov   ax,751
                                                push  ax
                                                mov   ax,409
                                                push  ax
                                                mov   al,70h
                                                mov   bl,01h
                                                call  xmode16


    ATI VGA Wonder       800x600        54h     mov   ax,799
                                                push  ax
                                                mov   ax,599
                                                push  ax
                                                mov   al,54h
                                                call  xmode16


    ATI VIP              800x560        53h     mov   ax,799
                                                push  ax
                                                mov   ax,559
                                                push  ax
                                                mov   al,53h
                                                call  xmode16

(continued)


    Paradise Plus-16     800x600        58h     mov   ax,799
    Paradise Professional                       push  ax
                                                mov   ax,599
                                                push  ax
                                                mov   al,58h
                                                call  xmode16
    

    Video 7 Fastwrite    800x600        62h     mov   ax,799
    Video 7 VRAM                                push  ax
                                                mov   ax,599
                                                push  ax
                                                mov   al,62h
                                                call  xmode16


    Western Digital      800x600   6Ah (color)  mov   ax,799
                                   6Bh (mono)   push  ax
    (VESA modes)                                mov   ax,599
                                                push  ax
                                                mov   al,6Ah   ; color
                                                call  xmode16
    

    If any of this information conflicts with the specifications in your
    video card's instruction manual, the manual's recommendation is a safer
    bet.  Note that all the above modes require a multi-frequency monitor.

    When you're all done with Graphics mode, CALL ModeColor to return to
    80x25 text mode, and CALL XModeClear to reset ASM32's graphics mode
    flags.