CDXF v1.0 


                                DXF Viewer

                   Copyright (c) 1993 Joseph V. Gagliano
                            All Rights Reserved


                            Joseph V. Gagliano
                              P.O. Box 202275
                          Austin, TX  78720-2275

                       Internet: jvgagliano@aol.com

                            September 30, 1993








                             Table of Contents



          Introduction . . . . . . . . . . . . . . . . . . . . . . . . .  1

          Equipment. . . . . . . . . . . . . . . . . . . . . . . . . . .  1

          Disclaimer . . . . . . . . . . . . . . . . . . . . . . . . . .  2

          Registration Information . . . . . . . . . . . . . . . . . . .  2

          CDXF v1.0 REGISTRATION FORM  . . . . . . . . . . . . . . . . .  3

          Distribution . . . . . . . . . . . . . . . . . . . . . . . . .  4

          Packing List . . . . . . . . . . . . . . . . . . . . . . . . .  4

          Setup. . . . . . . . . . . . . . . . . . . . . . . . . . . . .  5

          Running CDXF . . . . . . . . . . . . . . . . . . . . . . . . .  6

          CDXF Limitations . . . . . . . . . . . . . . . . . . . . . . .  8

          CDXF Screen Layout . . . . . . . . . . . . . . . . . . . . . .  9

          Mouse and Keyboard . . . . . . . . . . . . . . . . . . . . . .  9

          Colors . . . . . . . . . . . . . . . . . . . . . . . . . . . .  9

          CDXF Functions . . . . . . . . . . . . . . . . . . . . . . . . 10

          Function Descriptions. . . . . . . . . . . . . . . . . . . . . 10

          Miscellaneous. . . . . . . . . . . . . . . . . . . . . . . . . 13

          Glossary . . . . . . . . . . . . . . . . . . . . . . . . . . . 14



                                                                          1



          ============
          Introduction
          ===================================================================

          CDXF is a 2-Dimensional DXF (Drawing Interchange File) viewer. 
          DXFs are usually associated with Autodesk's AutoCAD, although many
          other programs can also read and write them.  Basically, a DXF is
          an ASCII text file which contains information to reproduce a .DWG
          file in other formats/programs.  DXFs are easily created using
          AutoCAD's DXFOUT function.

          CDXF is intended for users who frequently need to look at CAD
          drawings but aren't necessarily CAD experts.  It can also be used
          to view DXFs without the hassle of running AutoCAD.

          CDXF's minimal memory and disk space requirements make it more
          "portable."  Most full-blown CAD packages aren't.  If you need to
          inspect DXFs and don't want the expense of a full CAD system, CDXF
          is the way to go.

          =========
          Equipment
          ===================================================================

          You will need the following to run CDFX:

               MS-DOS 3.3 or better
               640x480x16 VGA display
               Mouse 
               150K free RAM
               80x87 Math-coprocessor supported but not necessary
               ** Hard disk drive optional (but strongly recommended!)

          If you can run AutoCAD, you probably won't have any trouble running
          CDXF. 

          A mouse is not necessary to view a file when CDXF is run with the 
          -v option, but none of the CDXF functions are accessible.  See
          "Running CDXF" below.

          **   CDXF creates a temporary disk file that is about one-half the
               size of the DXF being viewed.  This isn't a problem for small
               DXFs.  However, for a 500K DXF, for example, you will need
               approximately 250-300K free space in the disk/directory of
               CDXF.


                                                                          2



          ==========
          Disclaimer
          ===================================================================

          The author, Joseph V. Gagliano, claims no responsibility for any
          damages caused by the use or misuse of this product.  This product
          is distributed "as is" with no warranty expressed or implied.  The
          author will not be responsible for any losses incurred, either
          directly or indirectly, by the use of this product.  Use this
          product entirely at your own risk.  The author reserves the right
          to make modifications at any time.  Prices are subject to change
          without notice.

          AutoCAD is a registered trademark of Autodesk, Inc.


          ========================
          Registration Information
          ===================================================================

          CDXF is distributed as User-Supported software.  It is NOT
          "Freeware" or Public Domain.  You are encouraged to copy and
          distribute this software freely as long as the files in the Packing
          List are not removed or altered in any way.  If you find it useful,
          you are encouraged to register your copy.

          Registering your copy of the software helps the author continue to
          provide quality software at very reasonable prices.

          Registration is $25.00 and includes unlimited technical support, a
          printed and bound manual, and a free upgrade to the next released
          version of CDXF.

          Additional copies of CDXF may be obtained for $5.00 each.

          Orders from outside the U.S. need to include an additional shipping
          charge of $5.00.  Checks and money orders must be drawn on a U.S.
          bank and must be in U.S. Dollars.

          Print the registration form (REGISTER.DOC) or include on a piece of
          paper your name, address, and phone number, and send it along with
          your payment to:

               Joseph V. Gagliano
               P.O. Box 202275
               Austin, TX  78720-2275

          If you don't have the REGISTER.DOC file, a copy of it is provided
          on the next page.


                                                                          3



                         CDXF v1.0 REGISTRATION FORM 

         Remit to:                       From:


         Joseph V. Gagliano              _________________________

         P.O. Box 202275                 _________________________

         Austin, TX  78720-2275          _________________________

         (512) 335-3215                  _________________________

         Internet: jvgagliano@aol.com    _________________________


         Qty                                Unit Price      Total

         ___  CDXF v1.0                      $25.00         ______


         ___  Additional Copies of           $ 5.00         ______
              CDXF v1.0                 


                                             Subtotal:      ______


              Shipping outside U.S. @ $5.00                 ______
                 (U.S. Dollars/U.S. Bank)


                                            Total:          ______


              I use 5.25"____   3.5"____ disks.


          Where did you receive CDXF? ___________________________

          _______________________________________________________

          COMMENTS:  ____________________________________________ 

          _______________________________________________________



                                                                          4



          ============
          Distribution
          ===================================================================

          Feel free to make as many copies of the program as you like and
          distribute them as you see fit (friends, co-workers, Bulletin
          Boards...)  The only restriction is that _all_ files on the
          distribution disk (or ZIP file) must be copied faithfully (i.e.:
          not omitted nor altered.)  If any files in the Packing List are
          missing, please contact the author.


          ============
          Packing List
          ===================================================================

               13x8.FON       font file
               20x12.FON      font file
               5x3.FON        font file
               8x5.FON        font file
               CDXF.DOC       CDXF reference manual (this doc)
               CDXF.EXE       CDXF executable program
               CDXF.PCX       bitmap
               CENTER.DAT     bitmap
               DIST.DAT       bitmap
               INFO.DAT       bitmap
               QUIT.DAT       bitmap
               README         up-to-date info about CDXF
               REGISTER.DOC   registration form
               SNAPSHOT.DAT   bitmap
               TEST.DXF       DXF for testing
               ZOOMO.DAT      bitmap
               ZOOMW.DAT      bitmap


                                                                          5



          =====
          Setup
          ===================================================================

          First, make a backup disk.  Copy all the files from the
          distribution disk to a blank formatted disk.

          For example:

               COPY a:\*.* b:\*.*
          or   DISKCOPY a: a:

          If you're going to run CDXF from a floppy, use one of the disks as
          a work disk.  If you want to run CDXF from a hard disk, make a
          directory for it.

          For example:

               MD c:\cdxf

          Now copy all the files from the distribution disk to the CDXF
          directory.  This will be the working directory.

          For example:

               COPY a:\*.* c:\cdxf\*.*


                                                                          6



          ============
          Running CDXF
          ===================================================================

          CDXF accepts a .dxf file as a command line parameter in addition to
          several switches.  If a file name is not found, you will be
          prompted for one.

          * IMPORTANT: DO NOT include the ".dxf" extension!

          A command line switch is identified by the "-" that precedes it.

          Switch         Description
          ------         --------------------------------------------------

            v            bypasses CDXF's user interface and simply displays
                         the DXF in a full-screen view.  If you choose this
                         option, you will not be allowed to access CDXF's
                         functions.  Press any key to end the display.

            f            causes CDXF to display the DXF in "fast mode".  No
                         texts, fills, or fit polylines are displayed.  Once
                         inside CDXF, this option can be toggled-off by the
                         "Fast" button.

            q            suppresses the copyright notice and
                         "Extracting...." This can be useful if you use CDXF
                         in a batch file.

          Note that the command line switches can be capital letters also.

          If you don't have a mouse and just want to view a DXF, use the -v
          option.

          For example:

               CDXF test      loads test.dxf into CDXF

               CDXF test -v   display test.dxf in a full screen view w/o
                              interface

               CDXF -v test   same as above

            CDXF test -Q -f   loads test.dxf into CDXF in "fast mode".  Also
                              disables copyright notice.

               CDXF           prompts you to enter a DXF name




                                                                          7



          ============
          Running CDXF (continued)
          ===================================================================


          If everything has been entered correctly, you will see the
          following message (unless you've used the "-q" switch):

               "Extracting information..."



          CDXF uses the DXF LIMITS (usually set in AutoCAD by LIMITS
          function) as its drawing limits.  Therefore, anything outside of
          the limits will not be displayed initially.

          After a few seconds (depending on the size of the DXF) CDXF will
          display the DXF and allow you to perform several functions.

          If you would like to see entities that lie outside the DXF LIMITS,
          you can use the CENTER function to "pan" around the display.


                                                                          8



          ================
          CDXF Limitations
          ===================================================================

          The current version of CDXF works only with full DXFs.  That is, a
          DXF containing an ENTITIES section but not a HEADER section, is not
          allowed.  This type of DXF is usually produced using the AutoCAD
          DXFOUT-ENTITIES function.  Future versions may support this.

          Only "non-anonymous" BLOCKs contained in the BLOCKS section of the
          DXF will be extracted.  "Anonymous" BLOCKs include DIMENSIONs and
          HATCHes.
          * IMPORTANT:   Any drawing entities contained solely in an
                         "anonymous" BLOCK will not be displayed!  If you
                         wish to view these entities with CDXF, you must
                         first EXPLODE them, then DXFOUT.

          CDXF will faithfully reproduce the following entities:

               LINE
               CIRCLE
               ARC
               POINT
               TRACE
               SOLID
          
          CDXF approximates the following entities:

               PLINE (limited to 100 VERTICES)
               TEXT
               INSERT

          CDXF does not process:

               SHAPE
               ATTDEF
               ATTRIB
               3DFACE
               VIEWPORT
               DIMENSION

          PLINEs (polylines) are very powerful drawing tools.  With this
          power comes complexity.  PLINEs can have any number of vertices. 
          Each vertex can have a width greater than zero.  The PLINE can be
          curve-fit or spline-fit, etc....

          Currently, CDXF does not reproduce curve-fit PLINEs as they should
          be.  Future versions of CDXF will correct this.  Also, PLINEs with
          widths greater than zero may appear segmented.

          The problem with reproducing TEXTs is representing a scalable
          vector font with a bit-mapped font.  For most purposes, there
          shouldn't be a problem, but once again, future versions will
          correct this.


                                                                          9



          ==================
          CDXF Screen Layout
          ===================================================================

          After the DXF is processed, the CDXF view screen appears.  On the
          right is a tool bar with several "buttons".  At the bottom is a
          status bar that contains current information about the cursor
          position, zoom factor, etc.  

          The rest of the screen is the actual display of the DXF.  You can
          now use the mouse to navigate around the display or use the tools.


          ==================
          Mouse and Keyboard
          ===================================================================

          Although most of CDXF's functions are accessible through the tool
          bar, it is necessary to perform some functions with the keyboard. 
          CDXF was designed to allow the user to select a function with the
          keyboard, then complete the function with the mouse.  After a few
          minutes with CDXF, you will probably find this method the easiest.

          While we're on the subject of the mouse, let's talk about some
          terms.  When you see the word "click", that means to quickly press
          and release the (left) button.  "Drag" means to click the (left)
          button and move the mouse pointer/cursor to a different position,
          then click it again.

          The right mouse button is generally used to "back-up" or escape
          from a function.  Currently, the right mouse button is active only
          while using the "SNAPSHOT" and "PHOTO" functions.

          ======
          Colors
          ===================================================================

          All entity colors are determined BYLAYER.  Manual color settings
          are ignored.




                                                                         10



          ==============
          CDXF Functions
          ===================================================================
          Button         Key(s)    Description
          ------------------------------------------------------------
          ZOOM OUT       O,o       Zooms display out to LIMITS.

          ZOOM WINDOW    W,w       Zooms display to a user defined window.

          CENTER         C,c       Centers the display at user defined
                                   point.

          INFO           I,i       Displays information about the .dxf file.

          DISTANCE       D,d       Calculates a distance between two points.

          SNAPSHOT       F9        Takes a "snapshot".

          (PHOTO)        F10       Takes a "photo".

          QUIT           Q,q       Quits CDXF.

          Fill           F,f       Toggles the FILLMODE (on/off).

          Fast                     Toggles the FASTMODE (on/off).

          Grid           G,g       Toggles the GRIDMODE (on/off).

          (Background)   B,b       Toggles the background color
                                   (light/dark).


          =====================
          Function Descriptions
          ===================================================================

          ZOOM OUT       Use this function to redisplay the DXF at 1x zoom
                         factor.  Remember, CDXF only displays the drawing
                         LIMITS as set in the DXF (not EXTENTS).  Any part
                         outside of the LIMITS will not be displayed.


                                                                         11



          ZOOM WINDOW    This function will zoom in on a window similar to
                         AutoCAD's zoom-window function.  After selection,
                         the pointer will change to an arrow with a "W" by
                         it.  Move the pointer to one corner of the window. 
                         Now click the LEFT mouse button and size the window
                         to the desired limits, then click the LEFT button
                         again.

                         CDXF will redisplay the DXF given the new window.

                         * SEE NOTE at the end of this section.       


          CENTER         Choose this function to define a new center of the
                         display.  After selection, the pointer will change
                         to a cross-hair.  Move to position you wish to have
                         as the center of the display and press the LEFT
                         mouse button.  CDXF will redisplay the DXF with the
                         new center.  This is similar to AutoCAD's PAN
                         command.

                         CENTER does not affect the zoom factor.

                         * SEE NOTE at the end of this section.


          INFO           This function pops-up a window that displays
                         information about the current DXF.  It will show:

                                    Example INFO window
                         +-------------------------------------+
                         |           test.dxf                  |
                         | Origin : AutoCAD R10                |
                         | Created: 13:10:03  09-23-93         |
                         | Edited : 15:45:32  10-04-93         |
                         | Edit time:  01:34:65         +----+ |
                         |                              | OK | |
                         |  Press any key to continue.  +----+ |
                         +-------------------------------------+

                         Press a key or click on the "OK" button to return.



                                                                         12



          DIST           The DIST or distance function allows you to
                         determine a distance between two points on the
                         display.  After selecting DIST, the pointer will
                         change to an arrow with a "D" by it.  Move the
                         pointer to the start point then click the LEFT
                         mouse button.  You can now drag the pointer to any
                         point on the display.  Click the LEFT mouse button
                         again to choose an endpoint.

                         The status bar on the bottom shows the start point,
                         the current end point, the delta-x and delta-y
                         distances and the actual distance between the two
                         points.

                         * SEE NOTE at the end of this section.


          SNAPSHOT       This is function allows you to take a "snapshot" of
                         the DXF being displayed.  The "snapshot" is
                         actually 100 x 100 pixel, 16 color .PCX file that
                         is created by CDXF.  Simply click on the SNAPSHOT
                         button, then move the mouse cursor (it will change
                         to a camera with a 100 pixel square box around it)
                         to the area you want to capture.

                         You are allowed to take up to 999 per session. 
                         That is if you have registered.  Unregistered users
                         are only allowed 12.

                         CDXF will attempt to create a subdirectory called
                         "album" (under the current working directory).  The
                         .PCX files will be saved as "\album\sshot___.pcx" ,
                         where "___" is replaced by the number of the
                         snapshot.  For example, the first snapshot would be
                         "sshot000.pcx", then "sshot001.pcx", etc.  If CDXF
                         can't create "album", it will save the file in the
                         current working directory.

                         * SEE NOTE at the end of this section.



                                                                         13



          (PHOTO)        This function is only accessible through the F10
                         key.  It's similar to SNAPSHOT in that it
                         "captures" a .PCX file.  This function allows you
                         to "photo" an area that you specify.

                         The area is limited to available memory.  If a
                         photo fails (not enough memory), you will hear a
                         beep.  Try again with a smaller area.

                         The captured "photo" will be saved similarly to
                         SNAPSHOTS as "photo___.pcx".  See SNAPSHOT above
                         for details.

                         Unregistered users are limited to one PHOTO per
                         session.

          QUIT           simply ends the program.

          Fill           This function toggles the FILLMODE.  Some drawing
                         entities, such as SOLIDs and TRACEs, can be filled. 
                         By "filled," it is meant that the entity is
                         "colored-in" or painted with that entity's color.
                         Default is "off" unless set in the DXF.

          Fast           This function toggles the FASTMODE.  If on, no
                         texts, fills, or fit polylines will be displayed. 
                         Subsequent redraws thus should be faster.

          Grid           This function toggles the GRIDMODE.  When "on," a
                         grid of dots is displayed starting at LIMMIN and
                         ending at LIMMAX.  Grid spacing is set by GRIDUNIT. 
                         Default GRIDMODE is "off" and default GRIDUNIT
                         spacing is 1.0 x-direction, 1.0 y-direction.


          (Background)   There is no tool bar button to change the
                         background color.  To toggle the background color
                         between light (gray) and dark (black), press the
                         "b" or "B" key.

          * NOTE:   If you select this function from the tool bar, the
                    pointer will jump to the center of the display.  This
                    gets you back to the display quickly.



          =============
          Miscellaneous
          ===================================================================

          CDXF uses FONTLIB v1.1 to display TEXT entities.


                                                                         14



          =========
          Glossary
          ===================================================================

          

          "Anonymous"    means, when dealing with BLOCKS, that the BLOCK was
                         created by ACAD (or another third-party
                         application).  DIMENSIONs are "anonymous", until
                         they are EXPLODEd.

          AutoCAD        is a computer-aided drafting program developed and
                         sold by Autodesk, Inc., which is also known as
                         ACAD.  There are several versions of ACAD, the
                         latest being release 12.

          BLOCKS         contain lines, circles, etc. grouped together. 
                         Blocks are displayed with the AutoCAD INSERT
                         function.  Only "non-anonymous," INSERTed BLOCKS
                         are displayed by CDXF.

          Buttons        control most of CDXF's functions.  To "press a
                         button," move the mouse cursor to it and press the
                         left mouse button.

          BYLAYER        is a term used in ACAD to determine what color to
                         use for an ENTITY or BLOCK.  In ACAD, you can also
                         set color BYBLOCK or set an ENTITY's color manually
                         to any entity.  CDXF displays all ENTITIES and
                         BLOCKS BYLAYER.

          DIMENSIONS     are "anonymous" BLOCKS.  They are not displayed by
                         CDXF unless they are EXPLODEd.

          DWG            is a proprietary file format that AutoCAD uses to
                         store its drawing files.  Information about this
                         file format is not revealed freely as is
                         information about the DXF format.  Although it
                         would be more convenient to simply view a DWG file,
                         it is impractical in the scope of CDXF since it
                         changes for each ACAD version.

          DXF            is the file name extension used for Drawing
                         Interchange Files.  The DXF format was created by
                         Autodesk for AutoCAD.  DXF are usually in an ASCII
                         text format, although there is now a binary format
                         available (no relation to a DXB file).  CDXF must
                         receive an ASCII text DXF.


                                                                         15



          =========
          Glossary (continued)
          ===================================================================


          DXFOUT         is the AutoCAD command to create a DXF from the
                         current drawing (.DWG).  For CDXF, use the entire
                         drawing when creating a DXF, i.e., don't choose the
                         "ENTITIES" option from the DXF command.  Choose an
                         accuracy of six (6) decimal places for best
                         results.

          ENTITIES       are drawing images or references to images.  The
                         most common are:  LINE, PLINE, CIRCLE, ARC, POINT,
                         SOLID, TRACE, TEXT, and INSERT.

          EXPLODE        is an ACAD command that breaks a BLOCK, PLINE or
                         DIMENSION into its individual ENTITIES.

          EXTENTS        are the maximum display limits that are needed to
                         display a drawing.  CDXF uses the drawing LIMITS.  

          FILLMODE       determines if fill-capable entities are actually
                         filled.  This can be toggled on or off in ACAD or
                         CDXF.

          GRIDMODE       determines if a grid is displayed.  This can be
                         toggled on or off in ACAD or CDXF.

          GRIDUNIT       determines the x and y spacing of the grid.

          HEADERS        contain the setup information in a DXF.

          LIMITS         are the drawing limits usually set in ACAD.  CDXF
                         uses these as its own drawing limits.

          LIMMAX         is the upper-right (x,y) coordinate set by LIMITS.

          LIMMIN         is the lower-left (x,y) coordinate set by LIMITS.

          PCX            is a bitmap file format.  This format is easily
                         imported into many popular word processors and
                         desktop publishers. 

          Status Bar     displays current CDXF information.

          TABLES         contain layer and linetype information in a DXF.

          Tool Bar       contains the buttons that control most of CDXF's
                         functions.