|
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |        ELECTRC9
                        |
                        |        Copyright 1992, by Robert J. La Capra
                        |        All Rights Reserved
                        |
                        |        Shareware Version 9.2
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |        USER'S MANUAL
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |        Robert J. La Capra
                        |        50 Hillside Terrace
                        |        Andover, NJ 07821
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |
                        |





                               TABLE OF CONTENTS

         Introduction .............................................. I
         Shareware ................................................ II
         
         Benefits Of Registration ................................. II
         How To Register .......................................... II
         
         Functions Supported By Registered User Version .......... III
         Product Support Policy ................................... VI
         ELECTRC9 Registration Form .............................. VII
         
         Disclaimer ............................................. VIII
         Files Included On ELECTRC9 Disk ........................ VIII

         SETTING UP ELECTRC9
              Making A Backup Copy Of The ELECTRC9 Disk ........... IX
              Setting Up ELECTRC9 On A Floppy Disk ................ IX
              Setting Up ELECTRC9 On A Hard Drive ................. IX

         RUNNING ELECTRC9
              From A Floppy Disk ................................... 1
              From A Hard Drive .................................... 1
              Menu Selection ....................................... 1
              Data Input ........................................... 1
              Selecting Conductors ................................. 2
              Setup Color Defaults ................................. 2

         BOX FILL & SIZING CALCULATIONS
              Device Box Fill & Sizing ............................. 2
              Junction, Pull Box Sizing - Straight Pull ............ 4
              Junction, Pull Box Sizing - Angle or U Pull .......... 4

         CONDUIT SELECTOR .......................................... 5

         GENERAL CALCS:
              Cost To Operate ...................................... 6
              Motor Amps When Hp, Pf, And Efficiency Are Known ..... 6
              Motor Hp When Volts, Amps, Pf And Efficiency Are Known 7
              Amps When Va And Pf Are Known ........................ 7
              Va When Volts, Amps, And Pf Are Known ................ 7

         LIGHTING CALCULATIONS (Zonal Cavity Method) ............... 8

         MOTOR CALCULATIONS
              Branch Conductor Sizing ............................. 11
              Fuse or Breaker Sizing .............................. 11
              Overload Protection Sizing .......................... 12

         PIPE & WIRE SELECTOR ..................................... 13

         POWER FACTOR CORRECTION .................................. 14

         PRINTING REPORTS ......................................... 16





         QUICK REFERENCE TABLES
              Equipment Grounding Conductors ...................... 16
              Grounding Electrode Conductors ...................... 16
              Killowatt - Ampere Tables ........................... 17
              Underground Cover Requirements ...................... 17
              Metal Device Boxes .................................. 17
              Standard Pull & Junction Boxes ...................... 17
              Standard Fuses & Breakers ........................... 17
              Transformer Kva - Amperes ........................... 17
              Terminal/Conductor Temperature Limitations .......... 17
              Conductor Ampacity .................................. 18

         SHORT CIRCUIT CALCS ...................................... 18

         TERMINAL/CONDUCTOR TEMPERATURE LIMITATIONS ............... 22

         VOLTAGE DROP CALCULATOR .................................. 23

         OTHER ELECTRICAL SOFTWARE AVAILABLE
              LOADCALC Service/Feeder Calcs Version 1.1 ........... 24






         NOTE !!

         Pages 1 thru 23 of this file includes all documentation text 
         from the Registered User Version of ELECTRC9. However, not 
         all referenced features are available in this Shareware 
         Version of the program. The full text is included here to 
         give you a better idea of what the Registered User Version 
         supports. 




         __________________________  Page I  _________________________


         INTRODUCTION


         This Shareware evaluation Version Of ELECTRC9 is designed to
         perform most common electrical contracting and engineering
         calculations :

         * Device, junction and pull box calcs.

         * Conduit fill calculations.

         * Cost to operate various loads at different kwh charges.

         * Lighting calculations based on the Zonal Cavity Method.

         * Motor conductor, overcurrent and overload calculations.

         * Wire and conduit sizing based on allowable voltage drop.

         * General Calculations:
            Amps when hp, pf, and efficiency are known
            Amps when va and pf are known
            Va when volts, amps, and pf are known
            Hp when volts, amps, pf and efficiency are known

         * Quick Reference Tables for:
            Grounding electrode & equipment ground conductor sizes
            Underground cover requirements
            KW to ampere tables
            Transformer Kva to ampere tables
            Device, pull & junction box size and capacity
            Standard fuse & breaker ratings
            Wire ampacity table
            New terminal temp rating requirements - NEC 110-14(c)

         * Voltage drop calcs.

         * Power factor correction.

         * All functions operate with 'what-if' capability. You can
           quickly and easily change only the data you wish to,
           without having to start a new calculation and re-enter all
           the required data. Results are calculated and displayed as
           you make each change.


         ** All functions conform to the 1993 National Electrical Code.

         The National Electrical Code is a copyrighted document of the
         National Fire Protection Association, Batterymarch Park,
         Quincy, MA. 02269.




         __________________________  Page II  ________________________


         SHAREWARE

         ELECTRC9 is copyrighted (c) 1992, By Robert J. La Capra.
         ELECTRC9 is not free software. This shareware version is made
         publicly available only to allow users to preview ELECTRC9 on
         a trial basis. Any use of this shareware version beyond this
         limited evaluation period requires registration with the
         author, as described below. Use of unregistered copies past
         the evaluation period is prohibited.



         BENEFITS OF REGISTRATION

         Registration of ELECTRC9 brings you the following benefits:

         You receive the latest, expanded 'Registered User' version of
         ELECTRC9, which supports functions and capabilities in
         addition to those supported in this shareware version. The
         Registered User Version will not have the opening or closing
         shareware screens.

         You support the 'Shareware' concept of marketing which allows
         you to try the software before making a purchase.

         You receive unlimited priority support by US Mail, CompuServe
         Mail, and optional fax support.

         You receive automatic notification of future upgrades and new
         programs as soon as they become available. These are also
         offered to you at substantial discounts.

         Read the 'Product Support Policy' in this file for the major
         benefits of becoming a Registered User, and the 'Functions
         Supported By Registered User Version', in this file.



         HOW TO REGISTER

         A single registration of ELECTRC9 may be used by only one
         user at a time - it may not be installed on a server,
         network, etc..., nor may it be copied for use on multiple
         machines at one time, or be potentially available for use by
         more than one person at a time. A Single User Licensing
         Agreement will be supplied for each user that you register.

         To encourage ethical use of ELECTRC9, discounts are available
         for multiple registrations. Available licensing agreements
         range from six or more users to unlimited site licenses, in
         several increments. Write for current availability & fees.

         To register, fill out completely and mail the ELECTRC9
         Registration Form included in this file, or the one supplied
         in the disk file "ELECTRC9.REG", with the appropriate fee.




         _________________________  Page III  ________________________


         FUNCTIONS SUPPORTED BY THE REGISTERED USER VERSION


         Conduit Fill & Sizing

         Selects raceway size for any combination of insulated
         conductors. Calculates individual & total conductor areas,
         total area of raceway selected, and percent conduit fill. #18
         thru 2000 kcmil copper & aluminum conductors. Types tw, thw,
         thwn, thhn, rhw, rhh, use, xhhw.

         Power Factor

         Determines existing PF based on measured line volts, line
         amperes and true power you supply. Calculates Kvars needed to
         raise existing PF to any new PF. Specifies phase angle, Kva &
         Kvar of existing and proposed PF. Specifies recovered
         distribution system losses at the proposed PF. Single phase
         and balanced three phase.

         Box Fill & Sizing

         Calculates minimum cubic inch capacity of device boxes based
         on intended conductor/device/fitting fill. Selects minimum
         box dimensions for straight and angle pull and junction boxes
         Pop-up quick reference tables for standard dimensions and
         cubic capacities of device, junction & pull boxes are
         viewable with a single keypress.

         Lighting Design

         Performs interior lighting design based on the Illuminating
         Engineering Society's Zonal Cavity Method. Calculates
         required fixture quantity for any desired footcandle level.
         Supports cavity ratios, surface reflectances, and maintenance
         factors. Built-in support for generic recessed incandescent,
         fluorescent and hid fixtures as well as many lamp types. Also
         allows you to specify any fixture/lamp combination with data
         you can obtain from the manufacturer of the fixture/lamp that
         you choose to specify.


         Pipe & Wire Sizing
         
         Selects conductor size for any load amperage and picks 
         correct raceway size for those conductors. Supports 6 circuit 
         types, including harmonic. 21 supported conductor 
         material/insulation/temperature rating combinations. Derating 
         for ambient temperature & for the number of current carrying 
         conductors contained in the raceway. Terminal temperature 
         limitations. You can also choose to specify a maximum voltage 
         drop percentage which cannot be exceeded, and supply the 
         circuit run length, and the correct conductor will be 
         selected Supports single & three phase. 


 
         
         _________________________  Page IV  ________________________


         Motor Calcs
         
         Selects motor branch circuit conductors. Selects overcurrent 
         protective device ratings. Selects motor overload protection 
         ratings. Supports squirrel cage & wound rotor motors. 
         Supports full voltage, resistor, reactor & autotransformer 
         starting methods. Supports 21 conductor 
         material/insulation/temperature rating combinations. Supports 
         all code letters. Ambient temperature derating. Terminal 
         temperature limitations. Time delay & non time-delay fuses. 
         Instantaneous trip & inverse time circuit breakers. 110-240 
         volt, .17-10 HP Single Phase. 208-480 volt, .5-200 HP Three 
         Phase. 

         Voltage Drop
         
         Calculates voltage drop on existing or proposed resistive 
         circuits (100% PF) at any voltage, amperage and run length. 
         Supports circuit conductors from #18 awg thru 2000 kcmil, 
         aluminum & copper. Displays volts dropped, volts at load 
         terminals and the percentage of voltage dropped. Single & 
         three phase. 
         

         Short Circuit
         
         Calculates available fault currents from the source to a 
         maximum of 10 downstream points on the distribution system. 
         Calculations include the effect of voltage drop, impedance 
         and the inductive effects of the conductor/raceway system. 
         Supports single & parallel conductor runs, #12 awg thru 1000 
         kcmil, copper & aluminum. Supports magnetic & non-magnetic 
         raceways. Single & three phase. 
         

         General Calcs
         
         Calculates the cost to operate any load for any number of 
         hours per day for any number of days at any utility Kwh rate. 
         Calculate motor amps when hp, pf, & efficiency are known. 
         Calculates motor hp when volts, amps, pf & efficiency are 
         known. Calculates amps when va, volts & pf are known. 
         Calculates va when volts, amps & pf are known. 


 
         
         _________________________  Page V  _________________________
         
         
         Quick Reference
         
         Built in reference table screens that can be accessed from 
         the main menu, and from within certain functions for which 
         they are in context. They can be viewed on screen and can be 
         printed to printer or disk file. Conductor ampacities, 
         temperature ratings & ambient correction factors as per NEC 
         Table 310-16. Terminal temperature limitations as per NEC 
         110-14(c). Kw to amperes. Transformer Kva to amperes. 
         Underground cover requirements as per NEC 300-5. Standard 
         pull & junction box dimensions and cubic capacities. Standard 
         metal device box dimensions and cubic capacities as per NEC 
         370-16(a). Grounding electrode sizing as per NEC 250-94. 
         Equipment grounding conductor sizing as per NEC 250-95. 
         Standard fuse & circuit breaker ratings. Three phase tables, 
         where appropriate.
         

         Printed Reports
         
         Professional, detailed reports for all program functions. 
         Send reports out to a printer, or to an ASCII disk file where 
         you can then import the report into your word processor and 
         fine tune the appearance before printing. You can input up to 
         four lines of data which will print at the top of your 
         report. Printer output is generic, will work on any printer 
         connected to parallel port LPT1. 
         

         What-If Data Input
         
         Quickly and easily see what effect a change of one data item 
         will have on the result of the design you are working on. 
         Once you have entered all required data within a function and 
         the function has calculated the result, you can then change 
         one data item at a time and the function will automatically 
         recalculate the results instantly. Great for quick 
         comparisons of alternate design specs. 
         

         NEC Compliance
         
         ELECTRC9 has been written to produce design specifications 
         that comply with the 1993 National Electrical Code. 
         

         System Requirements

         To run ELECTRC9, you will need to have the following minimum 
         hardware configuration: An IBM or compatible computer. Any 
         brand or version of DOS 2.11 or greater. 390 K of free memory 
         available. One floppy disk drive. Monochrome or color 
         monitor. 





         _________________________  Page VI  _________________________


         PRODUCT SUPPORT POLICY

         Your registration of ELECTRC9 software will entitle you to
         extended product support services and other features which
         are intended to provide you with continuous satisfaction.

         The Registered User version of ELECTRC9 that you receive upon
         registration will support many enhancements and capabilities
         that are not available in this Shareware version.

         If any program bugs are discovered which affect the intended
         functionality or accuracy of the program, a revised program
         will be sent to you, as a Registered User, free of charge.

         As a Registered User, you will automatically be notified of
         any upgrades and new programs as they become available.
         Upgrades will be made available to you at reduced fees.

         You, as a Registered User, will have unlimited free support
         via US Mail. No phone support is presently available.

         If you have access to the CompuServe Information Service,
         you, as a Registered User, will also have unlimited priority
         support via CompuServe Mail, by leaving me a Mail Message.
         Your message will generally be answered within 24 hours or
         less. No messages will be accepted or returned through any
         gateways of other electronic mail services, or in any case
         where postage is due.

         If you select the optional fax support subscription for
         ELECTRC9 when you register, you will have one year of
         unlimited fax support for ELECTRC9. The fax number will be
         included with your disk shipment.

         Your feedback is the most important planning and development
         tool available to me. I look forward to hearing your thoughts
         about the present capabilities of the software, your wish
         list for additions and modifications of future versions, and
         any additional ideas for making the software more useful to
         yourself and other users.





         _________________________  Page VII _________________________


                      ELECTRC9 Ver. 9.2 REGISTRATION FORM
                                     S1234

         Registration fee for 1 to 5 users is $59.00 for each user or 
         machine. Site License & Multiple discounts available for 6 or 
         more users. Write for info. Purchase orders without payment 
         attached cannot be accepted. US funds drawn from a US bank. 


         INCLUDED WITH YOUR REGISTRATION
         Latest program version and documentation file.
         Documentation is supplied on disk file. No printed manuals.
         One License To Use Software for each user registered.
         Unlimited support by US Mail and by CompuServe Mail. 
         No phone support available.
         Shipping via US Postal Service.
         Orders shipped same day registration received.

         OPTIONAL ITEMS
         * UPS Ground Delivery - $10.00 additional per order. Multiple
               registrations or registration of ELECTRC9 and LOADCALC
               together qualify as 1 order, and shipping is $10.00 total. 
               Supply street address. NO P.O. BOXES.
         * 1 Year Of Fax Support for ELECTRC9 - $10.00 additional per year.
               For multiple registrations of ELECTRC9, fee is still $10.00
               total. Fax # supplied with shipment.

         Return This Form And Registration Fee PAYABLE TO:

                          ROBERT J. LA CAPRA
                          50 Hillside Terrace
                          Andover, NJ 07821
                          S.S.# 137-44-7561
         SHIP TO:

         Name: _______________________________________________________
         
         Company: ____________________________________________________

         Address: ____________________________________________________  
         
         City,State,Zip: _____________________________________________

         Phone : ______-______-________    Fax : ______-______-_______


         Number Of Users: ______ x $59.00 Each = Reg. Fee . : $_______

         UPS Ground Shipping - $10.00 Per Order [Optional]  : $_______

         1 Year Of ELECTRC9 Fax Support - $10.00 [Optional] : $_______
         _____________________________________________________________

                                    TOTAL FEE ENCLOSED .... : $_______


         DISK SIZE PREFERRED:   [   ] 5 1/4"     [   ] 3 1/2"




         _________________________  Page VIII  ______________________


         DISCLAIMER OF WARRANTY

         THIS SOFTWARE AND DOCUMENT ARE OFFERED "AS IS" AND WITHOUT
         WARRANTIES AS TO PERFORMANCE OF MERCHANTABILITY OR ANY OTHER
         WARRANTIES WHETHER EXPRESSED OR IMPLIED. BECAUSE OF THE
         VARIOUS HARDWARE AND SOFTWARE ENVIRONMENTS INTO WHICH THIS
         PROGRAM MAY BE PUT, NO WARRANTY OF FITNESS FOR A PARTICULAR
         PURPOSE IS OFFERED.

         GOOD DATA PROCESSING PROCEDURE DICTATES THAT ANY PROGRAM BE
         THOROUGHLY TESTED BEFORE RELYING ON IT. THE USER MUST ASSUME
         THE ENTIRE RISK OF USING THIS PROGRAM. THE AUTHOR OF THIS
         PROGRAM ASSUMES NO LIABILITY FOR YOUR USE OF THIS PROGRAM.

         DUE TO THE NATURE OF THIS PROGRAM, THE USER MUST BE FAMILIAR
         WITH THE SAFETY CONSIDERATIONS OF DESIGNING AND SAFELY
         INSTALLING ELECTRICAL WIRING SYSTEMS, IN ACCORDANCE WITH THE
         NATIONAL ELECTRICAL CODE. THIS PROGRAM IS NOT INTENDED TO
         REPLACE THE NEED FOR A QUALIFIED PERSON WHO IS EXPERIENCED IN
         THE ELECTRICAL DESIGN, CONSTRUCTION AND MAINTENANCE OF SAID
         ELECTRICAL SYSTEMS IN THEIR ENTIRETY.



         FILES INCLUDED ON ELECTRC9 DISK

         Electrc9.Doc ... This documentation file
         Electrc9.Exe ... Electrc9 program file
         Electrc9.Reg ... ELECTRC9 Registration Form
         Descrip.Doc .... Shareware Version Description





         _________________________  Page IX  ________________________


         SETTING UP ELECTRC9


         Making A Backup Copy Of The Electrc9 Disk

         The importance of making a backup copy of this program disk
         cannot be too strongly stressed ! Please STOP NOW and copy all
         the files included on the ELECTRC9 disk to a blank formatted
         disk, and place the original in a secure place.


         Setting Up ELECTRC9 On A Floppy Disk

         You can use the backup disk created above to run ELECTRC9.


         Setting Up ELECTRC9 On A Hard Drive

         1. Create a subdirectory on the hard drive to hold all the
            ELECTRC9 files as follows:
            A. Log onto the root directory of the hard drive - If drive
               is C:, type "C:" then press ENTER. Then type "CD\" and
               press ENTER. (do not type the quotes).
            B. Type "MD ELECTRC9" then press ENTER (you can substitute
               any name for ELECTRC9 - do not type quotes).
         2. Install the backup ELECTRC9 disk in floppy drive A: or B:
         3. Log onto the floppy drive containing the backup disk -
            (type "A:" or "B:" then press ENTER (do not type quotes).
         4. Type "COPY *.* C:\ELECTRC9" then press ENTER (don't type
            the quotes).

         The installation is complete. To verify the setup went OK,
         type "DIR C:\ELECTRC9\*.*" then press ENTER (no quotes). you
         should see a directory listing showing the names of all the
         files included on the ELECTRC9 disk.



        _________________________  Page 1  __________________________


        RUNNING ELECTRC9


        From Floppy Disk

        Insert the backup program disk into the disk drive and at the
        DOS prompt type "ELECTRC9" then press ENTER.


        From Hard Drive

        Enter the directory where the ELECTRC9 files are located, and
        at the DOS prompt type "ELECTRC9" then press ENTER.

        SHAREWARE VERSION ONLY - In the shareware version of ELECTRC9,
        you will first be asked to input a random number before you
        are given control of the main menu.

        Menu Selection

        The main menu is a pull down type, structured as a horizontal
        bar at the top of the screen with main titles displayed. Each
        of these main titles represents a sub menu with one or more
        related program functions.

        To select specific program functions :

        1. Press the hilighted letter of the menu item (main or sub).
        OR,
        2. Press the DOWN ARROW key to open the first sub menu, then
           use LEFT or RIGHT ARROW keys to move between sub menus.
        OR,
        3. Position the hilighted block over a menu selection (main or
           sub), then press ENTER.



        Data Input

        All functions operate with 'What-If' data entry routines. This
        allows you to instantly see the results of changing one data
        item at a time.

        Data input routines are similar in all functions. Use the UP,
        DOWN, or ENTER keys to move between input fields, entering
        data as you go. Some fields limit your input to certain
        values, and if you input data that is unacceptable, you will
        hear a beep and will not be able to move from that field until
        the correct data has been entered (or leave the field empty).

        Some functions require that you select one data item from a
        list. This is done by pressing a function key which pops up a
        menu where you will select one item from a list of choices.
        Use the UP or DOWN ARROW keys to position the hilighted bar
        over your choice and press ENTER.



        _________________________  Page 2  __________________________


        After you have entered all required data, the calculation will
        be performed and displayed. You can then change individual
        data items and instantly see the results.

        CAUTION:
        When entering the last data item, or changing one data item
        which was previously entered: Be sure to record that change by
        moving from that field to another field, or by pressing ENTER
        while still on that field.



        Selecting Conductors

        ELECTRC9 supports the new NEC 110-14(c) temperature limitation
        requirements. Now when you press the function key which pops
        up a list of available conductor types, there is also a
        temperature rating associated with each conductor and a
        location reference to help you choose. When you select a
        conductor from the list, you are also choosing which
        temperature rating that conductor will be 'USED AT' (which
        column of 310-16 will be searched for ampacity). When
        selecting a conductor, remember that the temperature rating of
        the terminal or equipment must not be exceeded. If the
        equipment is listed for use at 75 degrees C maximum, then you
        must choose a conductor from the list with a rating that
        doesn't exceed 75 degrees.



        Setup Color Defaults

        Initially the program starts up in black and white. Select
        'Setup' from the main menu. Then select either Color Display
        or Mono Display. Your choice will be saved to a disk file,
        which will automatically be used for future program use.



        BOX FILL & SIZING


        Device Box Fill & Sizing

        Determines cubic inch volume required for boxes, as per 1993
        NEC section 370-16. Conductor size range is from #18 thru #6.

        Free space (cu.in.) required for each conductor:
        ------------------------------------------------
        # 18 .. 1.5     |    # 12 .. 2.25    |    #  6 .. 5
        # 16 .. 1.75    |    # 10 .. 2.5     |
        # 14 .. 2       |    #  8 .. 3       |



        _________________________  Page 3  __________________________


        Deductions are as follows:

        * 1 or more fixture studs, cable clamps, or hickeys:
            1 deduction for each type of fitting, based on the
            largest conductor contained in the box.
        * Each Strap containing 1 or more devices:
            2 deductions, based on the largest conductor connected to
            each device strap.
        * Grounding conductors:
            1 deduction, based on largest grounding conductor in box.
        * Isolated Ground conductors:
            1 deduction based on largest isolated ground conductor
            in box.

        Enter The Quantity Of Each Size Conductor Within The Box:

        A conductor running thru the box with no splices or
        connections within the box should be counted as 1 conductor.

        A conductor originating outside the box and terminating within
        the box should be counted as 1 conductor.

        Conductors, no part of which leaves the box (example ... a
        jumper or pigtail from a splice within the box to a switch,
        outlet or fixture mounted on the box), should not be counted.

        Answer the prompts for devices, clamps, fittings, ground
        conductors, add'l ground conductors:

        Count each mounting yoke or strap containing one or more
        devices as 1. Example... one duplex outlet - count as 1. two
        duplex outlets - count as 2.

        The remaining prompts are self explanatory. Answer Y for yes.
        There is no need to answer N for any prompts which would be
        answered as 'no'. A blank field is interpreted as 'no'.

        A quick reference table of standard metal boxes and their
        cubic inch capacity is available for viewing at any time, by
        pressing F2. The current screen will be saved, and the table
        will be shown. When you wish to return to the previous screen,
        press any key. A printout is available by pressing F10. See
        the documentation for printing for details.




        _________________________  Page 4  __________________________


        Junction & Pull Box Sizing - Straight Pull

        Calculates the minimum length, in inches, of pull and junction
        boxes where raceways enter and leave the box at opposite ends.
        If the wiring method is cable assemblies instead of raceways,
        first determine the trade size conduit which would be
        appropriate for the size and quantity of conductors in the
        cable assembly, then use that conduit size.

        If more than one raceway or cable enters and/or leaves either
        end of the box, always use the largest size.

        The method used to determine minimum box length for straight
        pull: Eight times the trade diameter of the largest raceway.

        The operation of this function is straightforward. Position
        the hilighted bar over the largest raceway size for this
        calculation, then press ENTER. The results will be displayed.
        A printout is available by pressing F10. See the documentation
        for printing for details.



        Junction & Pull Box Sizing - Angle or U Pull

        Calculates the minimum distance, in inches, between each
        raceway entry inside a junction or pull box and the opposite
        wall of the box, where raceways enter and leave the box at
        angles. If the wiring method is cable assemblies, see the
        explanation above, under 'Straight Pull'.

        The method used to determine minimum distance for angle or U
        Pull: Six times the trade diameter of the largest raceway,
        PLUS, the sum of the diameters of all other raceway entries in
        any one row on the same wall of the box. Use the row with the
        largest total diameter of raceways.

        A quick reference table of standard boxes and their cubic inch
        capacity is available for viewing at any time, by pressing F2.
        When you wish to return to the previous screen, press any key.
        A printout is available by pressing F10.



        _________________________  Page 5  __________________________


        CONDUIT SELECTOR

        The Conduit Selector allows you to quickly and accurately
        determine the conduit size required for 1 or more conductors.
        Calculations are based on the Dimensions and Percent Area of
        Conduit and Tubing from table 4, and from Conductor Dimensions
        as per Table 5 of the NEC. Maximum allowable percent conduit
        fill is 53% for 1 conductor, 31% for 2 conductors and 40% for
        more than 2 conductors, as per table 4.

        Use the UP, DOWN, TAB or SHIFT+TAB keys to move the cursor to
        the desired wire size/type position, then enter the quantity
        of that size/type conductor to include in the conduit. If you
        want to include other size/types of conductors into the same
        conduit, then repeat the above procedure. You can enter any
        combination of conductors in the same conduit.

        NOTE: Several fields will show an asterisk ( * ). This
        represents the unavailability of those sizes/types of
        conductors. Do not alter those fields.

        Pressing F2 at any time will show the results of the
        calculation. The program will list all the sizes and types of
        conductors you chose for the calculation, their individual
        areas, the total area extensions, the grand total area for all
        conductors, the minimum trade size conduit required, the total
        area for the calculated conduit, and the percent conduit fill
        for the calculation. If more data is available than will fit
        on the screen, you will be able to use the UP and DOWN ARROW
        keys to scroll through the data. Pressing any key will return
        you to the conduit selector input screen with all previous
        data intact. A printout is available by pressing F10. See the
        documentation for printing for details.



        _________________________  Page 6  __________________________


        GENERAL CALCULATIONS


        Cost To Operate

        Calculates the cost to operate a certain load a number of
        hours daily for some number of days at a certain KWH utility
        charge.

        POWER OF LOAD is the number of watts the load draws.
        DAILY USE is the number of HOURS the load is operated per day.
        NUMBER OF DAYS is the number of days the load is operated.
        PRICE / KWH is the utility charge per killowatt hour.
                     (Example..  10 cents/kwh, enter .10)

        NOTE: A value of ten cents/Kwk initially appears in the
              'Price/Kwh' field, as an example only. You should change
              this value to reflect your own price/Kwh charge.

        After entering the above information, the program calculates
        and displays the cost to operate the load for the number of
        hours daily for the number of days at the chosen utility
        charge. A printout is available by pressing F10. See the
        documentation for printing for details.


        Motor Amperes

        A generic procedure to calculate motor amperage when hp, pf
        and efficiency are known.

        The calculation formula is:
        1 phase:
          (hp x 746) / (volts x pf x efficiency)
        3 phase:
          (hp x 746) / (1.73 x volts x pf x efficiency)

        Simply enter appropriate values at the prompts for hp, pf and
        eff. If pf and/or eff. is 100% or unity, enter 100 at those
        prompts. Note that this procedure is not to be used in
        determining motor full load amperage for the purpose of
        calculating conductor, overcurrent or overload sizes. Use the
        'Motor Calcs' function.



        _________________________  Page 7  __________________________


        Motor HP

        A generic procedure to calculate motor horsepower when
        voltage, amperage, pf and efficiency are known.

        The calculation formula is:
        1 phase:
          (volts x amps x pf x efficiency) / 746
        3 phase:
          (1.73 x volts x amps x pf x efficiency) / 746

        Simply enter appropriate values at the prompts for volts,
        amps, pf and eff. If pf and/or eff. is 100% or unity, enter
        100 at those prompts.



        Amperes

        Used to calculate amperes when va and volts, and pf are known.

        The formula is:
        1 phase:
          va / (volts x pf)
        3 phase:
          va / (1.73 x volts x pf)

        Simply enter appropriate values at the prompts for va, volts
        and  pf. If pf is 100% or unity, enter 100 at that prompt.



        Va

        Used to calculate va when volts, amps and pf are known.

        The formula is:
        1 phase:
          volts x amps x pf
        3 phase:
          1.73 x volts x pf

        Simply enter appropriate values at the prompts for volts, amps and
        pf. If pf is 100% or unity, enter 100 at that prompt.



        _________________________  Page 8  __________________________


        LIGHTING CALCULATION ( Zonal Cavity Method )

        Calculates the quantity of lighting fixtures required to light
        any room or area to any desired footcandle level.

        The Illuminating Engineering Society (IES) has devised a
        flexible and accurate method for calculating lighting
        requirements, called the ZONAL CAVITY METHOD. This method
        assumes that any room or area to be lighted is made up of
        three cavities, the CEILING CAVITY, the ROOM CAVITY, and the
        FLOOR CAVITY.

        The CEILING CAVITY extends from the ceiling surface down to
        the lighting fixture mounting level. If the lighting fixtures
        are recessed or surface mounted then the value of the Ceiling
        Cavity will be zero. If they are suspended some distance below
        the ceiling then the value of the Ceiling Cavity is the volume
        of space between the ceiling surface and the fixture mounting
        level.

        The ROOM CAVITY extends from the fixture mounting level down
        to the work height level. The work height level is the
        distance above the floor where the required quantity of
        footcandles is to be maintained (usually desktop or work bench
        level).

        The FLOOR CAVITY extends from the work height level down to
        the floor. If the required footcandles is to be maintained all
        the way to the floor, then the Floor Cavity value will be
        zero.

        Every surface exibits a certain ability to reflect light.
        Light colored surfaces reflect more light than dark surfaces,
        so more light will need to be provided in a dark environment.
        The degree of a surface's reflectivity is referred to as it's
        Percent Reflection value. Percent Reflection can be accurately
        measured with a reflectometer, or standard reflectance tables
        can be referred to, such as the following:


                    TABLE FOR INTERIOR ILLUMINATION DESIGN
                   ----------------------------------------
                      COLOR                % REFLECTION
                   ----------------------------------------
                       Flat white               75 - 85
                       Ivory                    70 - 75
                       Buff                     60 - 70
                       Yellow                   55 - 65
                       Light tan                45 - 55
                       Light green              40 - 50
                       Gray                     30 - 50
                       Blue                     25 - 35
                       Red                      15 - 20
                       Dark brown               10 - 15
                  ------------------------------------------



        _________________________  Page 9  __________________________


        The MAINTENANCE FACTOR is a value determined from the
        anticipated maintenance of the fixtures and reflective
        surfaces in the room or area. The intensity of illumination
        produced by a lighting installation will depreciate after some
        time due to lamp aging, and dust and dirt buildup. The
        MAINTENANCE FACTOR is designed to adjust for this. Typical
        values are from .5 to .8. (.5 for a poorly maintained
        environment, .8 for well maintained).

        Each lighting equipment manufacturer publishes data for the
        COEFFICIENT OF UTILIZATION (CU) for each fixture type and size
        in it's line. The CU of a fixture is a measure of it's
        efficiency under specific conditions of room cavity values and
        effective reflectance values.


        The formulas used in the ZONAL CAVITY METHOD :

        CEILING CAVITY RATIO = (5 * Hc (L + W)) / (L * W)

        ROOM CAVITY RATIO =  (5 * Hr (L + W)) / (L * W)

        FLOOR CAVITY RATIO = (5 * Hf (L + W) / (L *  W)

        WHERE:
        Hc = distance from ceiling to fixture level (in feet).
        Hr = distance from fixture level to work height (in feet).
        Hf = distance from work height to floor (in feet).
        L = length of room in feet.
        W = width of room in feet.

        ROOM LENGTH and ROOM WIDTH values must be entered in FEET.
        Decimal points are accepted (Ex. 125, 50.5, etc...).

        CEILING HEIGHT and FIXTURE HEIGHT must also be entered in
        FEET. Decimal points are acceptable.

        WORK HEIGHT must also be entered in FEET. Decimal points are
        acceptable. If you want the WORK HEIGHT to be equal to the
        floor, simply enter zero.

        FOOTCANDLE LEVEL is a measure of the intensity of light
        falling upon a specific surface.

        Values for Percent CEILING, WALL, and FLOOR Reflectances must
        be entered as whole numbers (50, 80, etc...) Exact values can
        be obtained by use of a reflectometer, or a standard table for
        interior illumination design can be referred to, such as the
        table for interior illumination design on the previous page.



        _________________________  Page 10  _________________________


        The value entered for MAINTENANCE FACTOR must be less than or
        equal to 1. The value of between .5 and .8 will be accurate
        for nearly all calculations. A value of 1 will exclude the
        MAINTENANCE FACTOR from the lighting calculation.

        NOTE:
        A value of .8 initially appears in the 'Maintenance Factor'
        field, as an example only. You can change this value to
        reflect your own conditions.

        To select fixture type, press F2. The menu will ask you to
        select either 'built-in fixture type' or 'specify fixture
        type'.


        Built-In:

        Fixture types stored internally include Recessed Incandescent,
        Fluorescent, and High Intensity Discharge. COEFFICIENT of
        UTILIZATION (CU) values which have been compiled by IES are
        stored internally for these fixtures. The internally stored
        fixtures are representitive of their types, as are the
        internally stored lamp types. You will get accurate results
        using them, but if you wish to use a type of fixture not
        available internally, you can choose to specify your own type.


        Specify:

        If you choose to specify your own fixture type, you will be
        prompted for the number of lamps per fixture, the quantity of
        lumens per lamp, and, the coefficient of utilization (CU) of
        the fixture. You will need to have the fixture manufacturer's
        CU specs. LUMEN specs are available from various sources. Lamp
        manufacturers will have lamp catalogs which will list LUMEN
        values for their line of lamps.

        After all data has been entered, the number of fixtures
        required will be calculated and displayed. A printout is
        available by pressing F10. See the documentation for printing
        for details.



        _________________________  Page 11  _________________________


        MOTOR CALCULATIONS


        Branch Conductor Sizing

        Calculates motor branch circuit conductor size as per NEC
        Article 430, Part B, and 430-6.

        Conductor ampacity is based on 125 percent of motor full load
        amperage (as determined from table 430-148 or 430-150),
        multiplied by appropriate power factor multiplying factor,
        multilpied by appropriate ambient temperature multiplier. This
        product yields the 'Wire Ampacity Required' of the conductor
        to be used to supply the motor. The program then selects the
        conductor size of the type/temperature rating that you
        specified that meets the required ampacity. This selected wire
        size is verified by listing the ampacity (NEC Table 310-16) of
        the calculated wire, and multiplies it by the ambient
        temperature derating factor. This product yields the maximum
        allowable ampacity of the selected wire. This value must equal
        or exceed the 'Wire Ampacity Required' value calculated
        previously.

        21 conductor types/temperature ratings are supported. See the
        section 'Temperature Limitations' in this file for more info.
        Ambient temperature derating of conductors is also supported.


        Fuse or Breaker Sizing

        Calculates rating or setting of motor branch circuit
        overcurrent protective device (Nontime-delay fuse, Time delay
        fuse, Instantaneous trip circuit breaker & Inverse time
        circuit breaker). NEC Article 430-Part D, and, 430-52.

        Rating or setting is based on Full load amperage (from table
        430-148 & 430-150) of motor, multiplied by appropriate power
        factor multiplying factor, multiplied by appropriate
        percentage factor from table 430-152 for the selected device
        type. Article 430-52(a).

        If this results in a value other than a standard size or
        rating of overcurrent protection device, the next higher
        standard rating is selected. Article 430-52(a), Exception 1.



        _________________________  Page 12  _________________________


        Overload Protection Sizing

        Calculates motor overload protective device rating. Article
        430, Part C.

        Rating is based on motor full load amperage (from motor
        nameplate) multiplied by:

        125% if nameplate service factor is not less than 1.15,
        or
        125% if nameplate temperature rise is not over 40 degrees C.,
        or
        115 % for all others.


        Access Keys Used To Select Motor Parameters:

        Press:    To Select:              Press:    To Select:
        --------------------              --------------------
        F1        Help                    F6       Code Letter
        F2        Motor Type              F7       Wire Type
        F3        Start Method            F8       Ambient Temperature
        F4        Phase/Volts             F9       Overcurrent Type
        F5        Horsepower              F10      Print Report


        NOTE:
        The 'Percent Motor Power Factor', parameter is not an accurate
        representation of true power factor. It is a VERY ROUGH item
        that should be used with caution. At the 'Percent Motor Power
        Factor' field, entering 100 will exclude the motor's Power
        Factor from the calculation.



        _________________________  Page 13  _________________________


        PIPE & WIRE SELECTOR

        Calculates the conductor size required to carry a certain load
        for some distance while not exceeding a specific voltage drop
        percentage, and the trade size conduit required to contain
        those conductors.

        21 conductor types/temperature ratings are supported. See the
        section 'Temperature Limitations' in this file for more info.
        Ambient temperature derating of conductors is also supported.

        Conductor ampacity derating due to the number of current
        carrying conductors in the raceway is supported as per NEC
        310-Note 8(a).

        Six circuit types are supported:
        --------------------------------
        1 Phase 2 Wire(Phase & neutral, or 2 Phase conductors)
        1 Phase 3 Wire(2 Phase conductors & neutral)
        1 Phase 3 Wire(Above circuit from a 4 wire wye system)
        3 Phase 3 Wire(3 phase conductors)
        3 Phase 4 Wire Wye(3 phase conductors & neutral)
        3 Phase 4 Wire Wye circuit with the majority of load harmonic

        In the third circuit type above, the neutral will carry
        substantial current, and will be considered as a current
        carrying conductor in the pipe size selection. NEC 310-Note
        10(b).

        In the last circuit type above, the neutral will carry
        harmonic currents, and will be considered as a current
        carrying conductor in the pipe size selection. NEC 310-Note
        10(c).


        Data Input

        The 'Maximum Percent Of Voltage Drop' field will only accept
        whole numbers in the range of 0 to 9. This will be the maximum
        percentage of the supply voltage which can be dropped by the
        circuit conductors. If you enter 0 in this field, voltage drop
        will not be considered in the selection of the wire size.

        'Full Load Amperage Of Load' is the rated or maximum amperage.
        'Source Voltage' is the supply voltage for the circuit.
        'Length of Run In Feet' is one way length from supply to load.

        Access Keys Used To Select Circuit/Conductor Parameters:
        Press:    To Select:         Press:    To Select:
        -----------------------      -----------------------------
        F1        Help               F4        Ambient Temperature
        F2        Circuit Type.      F10       Print Report
        F3        Wire Type.



        _________________________  Page 14  _________________________


        POWER FACTOR CORRECTION

        Calculates the existing power factor and the capacitance
        required to achieve a new power factor. The calculations are
        accurate for single phase and balanced three phase conditions.

        Do not rely on these calculations for situations where several
        loads operate independently on the same feeder or branch
        circuit, because the total power factor on the feeder or
        shared branch circuit will vary, depending on which loads are
        operating. Instead, run a calculation for each load
        independently. Then, the calculated Kvars of capacitance
        required should be installed as close as possible to the
        individual load for which the calculation is performed. Also
        note that if you improve the power factor of an existing
        motor, the overload heaters should be changed to protect the
        motor at the reduced amperage which will result.

        Before considering the use of capacitance to improve power
        factor, determine if the low power factor condition is caused
        by the use of a motor that is oversized for the driven load.
        Replacing the motor with a more efficient, properly sized unit
        may be more practical and cost effective.

        Power factor is the ratio of the true power (in watts) to the
        apparent power (in voltamps). True power is measured with a
        wattmeter. Apparent power is the product of volts and amps.
        The result is the power factor of the load. For example, a
        load is measured with a wattmeter and indicates 1880 watts.
        The measured voltage is 240 volts. The measured current is 10
        amps:

                        True Power          1800       1800
        Power Factor = --------------- = ---------- = ------ = .75
                        Apparent Power    240 x 10     2400

        The power factor of this load is calculated to be .75 (75%).
        The apparent power (delivered power) of this load is 2400 VA
        but the true power (useful power) is only 1800 watts. The
        remaining 600 va are wasted in the form of heat losses.
        Increasing the power factor would reduce the heat loss and
        reduce the current requirements of the circuit supplying this
        load.

        To increase the power factor of an inductive load, capacitance
        can be connected to the load. The required amount of
        capacitance (in Kvars) must be calculated.



        _________________________  Page 15  _________________________


        The formula for determining existing PF and capacitance
        required:

        Single Phase - Existing:

        Kva = (volts x amps) / 1000
        PF  = Kw / Kva
        Phase Angle = The angle that has a cosine equal to the PF
        Kvars = Kva x SIN of the phase angle


        Single Phase - Proposed:

        Kva = Kw / Proposed PF
        Line Amps = (Watts x 1000) / (Proposed PF x Volts)
        Phase Angle = Angle with a COSINE equal to the proposed PF
        Kvars = Proposed Kva x SIN of the proposed phase angle


        Three Phase - Existing:

        Kva = (volts x 1.73 x amps) / 1000
        PF  = Kw / Kva
        Phase Angle = Angle with a COSINE equal to the PF
        Kvars = Kva x SIN of the phase angle


        Three Phase - Proposed:

        Kva = Kw / proposed PF
        Line Amps = (Kw x 1000) / (Proposed PF x volts x 1.73)
        Phase Angle = Angle with a COSINE equal to the proposed PF
        Kvars = Proposed kva x SIN of the phase angle


        Single and Three Phase:

        Capacitive Kvars Required = Existing Kvars - Proposed Kvars
        Recovered Distribution Losses = Existing Kva - Proposed Kva


        NOTE:
        Depending on computer processor speed, there will be some
        delay in calculating the phase angles and the kvars. On a
        486/33, it will be unnoticeable, while on an 8087 at 4.77 Mhz
        it can take 15 seconds or so.



        _________________________  Page 16  _________________________


        PRINTING REPORTS

        You can print reports either to a printer or to a disk file
        for all functions except for the general calcs, and for all
        Quick Reference Tables.

        Printer support is generic (Printer Port LPT1 only), offering
        no special print types, although you can set the desired print
        type, size, etc, on your printer before printing the report.
        Also supported is the printing of reports to an ASCII disk
        file, for importing into your word processing program. For the
        general calcs, you con do a 'Print Screen' to send output to
        the printer. This can be done on most computers by pressing
        the SHIFT key and the PRINT key simultaneously.

        To print a report, press the F10 function key. You will be
        prompted for a Job Name, Address, City & State, and
        Description. These are optional and they may contain any data.
        The data entered at these prompts will be printed at the top
        of the report*. Next, enter P to print to a printer, or, D to
        print to disk. When you are ready to print the report, press
        F10.

        NOTE:
        To print any of the Quick Reference Tables, press F10 while
        viewing the table. The 'Print' input screen allows input of
        job name, address and description, however, this information
        will not be printed to any of the Quick Reference reports.
        Simply leave those fields blank.

        NOTE:
        When printing reports or Quick Reference Tables that are
        longer than one page to printer, the program does NOT check
        for page breaks. If you prefer, you can set your printer to
        'Skip Perforation'. This will leave a margin at the bottom of
        each page, and continue at the top of the next page.



        QUICK REFERENCE TABLES


        Equipment Ground Conductors

        To determine the required size equipment ground conductor, as
        per NEC Table 250-95.



        Grounding Electrode Conductors

        To determine the proper grounding electrode conductor size, as
        per NEC Table 250-94.



        _________________________  Page 17  _________________________


        Kw To Amperes

        To quickly convert single and three phase KW values to ampere
        values and vice versa. Pressing PG UP & PG DN scrolls between
        the single phase and three phase tables.



        Underground Cover Requirements

        To determine the minimum cover requirements of conduit,
        underground cable, and other raceways, as per NEC Table 300-5.



        Metal Device Boxes

        Table of metal device boxes and their cubic inch capacities.



        Standard Pull & Junction Boxes

        Table of standard pull & junction boxes and their cubic inch
        capacities.



        Standard Fuses & Breakers

        Table of standard ratings of overcurrent devices.



        Transformer Kva To Amperes

        To quickly convert single and three phase transformer Kva
        values to ampere values and vice versa. Pressing PG UP & PG DN
        scrolls between the single phase and three phase tables.

        NOTE:
        The data for this table is located in the ELECTRC9.DAT file,
        and is read in by the program. This file must be located in
        the same drive\directory as the main program file,
        ELECTRC9.EXE.



        Terminal/Conductor Temperature Limitations

        The new requrements of the 1993 NEC Section 110-14(c).



        _________________________  Page 18  _________________________


        Conductor Ampacity

        Allowable ampacities and ambient temperature derating factors
        of NEC Table 310-16. Pressing PG UP & PG DN scrolls the table.
        NOTE: The data for this table is located in the ELECTRC9.DAT
        file, and is read in by the program. This file must be located
        in the same drive\directory as the main program file,
        ELECTRC9.EXE.



        SHORT CIRCUIT CALCULATIONS - Point To Point Method

        The point to point method is a method of calculating available
        fault currents.

        To calculate the available fault current at various points
        throughout an electrical distribution system. You can start
        with the available short circuit current at a source point
        (secondary of a utility transformer for example), and
        determine the fault current available at any point beyond that
        based on the voltage drop due to wire impedance and the
        inductive effect of the circuit. Capacative reactance is
        negligible at 600 volts or less, and is ignored. Note that the
        values of effective impedance calculated by the program are
        valid at 75 degrees C, and at 85 percent power factor of the
        circuit.

        A maximum of ten points can be calculated, single and three
        phase. Motor contribution is not presently supportrd in this
        version of the software.



        _________________________  Page 19  _________________________


        Method used to determine available short circuit current at
        any point:

        1. Obtain the available short circuit current at your
           starting point:
             If your starting point is the secondary of a utility
             transformer, the utility company should be consulted
             for this information. If your starting point is a
             transformer and fault current is not known, determine
             the fault current available at the secondary terminals
             as follows:

            A. Calculate the Multiplier:
                 Multiplier = 100 / Percent Transformer Impedance
                 Example:
                   277/480v, 3 phase 500 Kva transformer Percent
                   nameplate impedance = 2 percent
                      Multiplier = 100 / 2
                      Multiplier = 50

            B. Calculate short cct current at the secondary terminals:
                 Isca = Short circuit current at secondary terminals.
                 Isca = Transformer Full Load Amps x Multiplier
                   Example:
                     Isca = 500 amps x 50 'Multiplier from above'
                     Isca = 25000 amps

        2. Calculate the C Factor:
             C Factor = 1 / Wire Impedance Per Foot
               Example:
                 500 kcmil copper conductor in steel conduit
                 From NEC Chapter 9, Table 9:
                   Impedance per 1000 feet = 0.050
                   Impedance per foot = 0.050 / 1000 = .00005
                   C Factor = 1 / .00005 = 20000

        3. Calculate the F Factor:
           L = One way conductor length from source point to the fault
           I = available short circuit current at your starting point
           C = C Factor
           E = Line to line voltage at your starting point
           NPC = Number of parallel conductors per phase

           For 3 Phase Faults:
             F Factor = (1.73 x L x I) / (NPC x C x E)

           For 1 Phase Line to line faults:
             F Factor = (2 x L x I) / (NPC x C x E)

             Example:
               277/480v, 3 phase source, I = 25000 amps,
               150 feet #500 kcmil copper conductors, 1 per phase,
               steel conduit, C = 20000

               F Factor = (1.73 x 150 x 25000) / (1 x 20000 x 480)
               F Factor = 6487500 / 9600000 = .6757813



        _________________________  Page 20  _________________________


        4. Calculate the M Factor:
             M Factor = 1 / (1 + F Factor)

               Example:
                 M Factor = 1 / 1.6757813 = .5967366

        5. Calculate available short circuit current at the fault:
             Short Circuit Current At The Fault = Isca x M Factor

           Isca = available short cct current at your starting point
           Ifsca = Short circuit current at the fault

              Example:
                Ifsca = Isca x M Factor
                Ifsca = 25000 x .5967366 = 14918 Amps


        Data Input And Calculation

        The data input areas are where you will enter parameters for
        the calculations. Use the UP ARROW and DOWN ARROW keys to move
        from prompt to prompt. Using the ENTER key moves you down
        through the prompts. Pressing the ESCAPE key aborts the
        calculation and returns you to the main menu. An exception is
        when you are selecting a choice from a group of options by
        pressing one of the function keys. Pressing ESCAPE here only
        backs you out of that selection area, and you do not lose any
        data from the data input areas.

        The first step in using the function is to input data at an
        initialization area. Enter the number of points that you wish
        to calculate fault currents for (maximum of 10).


        Then press the PG DN key to access the data entry area for
        point number 1 and proceed to enter data as follows:

        Available Fault Current At Source - This will be the short
        circuit amps available at the secondary of your utility or
        distribution transformer, load side of main service
        disconnect, etc, or wherever you choose to start the fault
        calcs from. Note that if you are entering data for point
        number 2, etc., The source would be the place where that point
        is fed from.

        One Way Conductor Length In Feet - The end to end length of
        the wire run from the source to the location where the
        available fault current will be calculated. Could be the mains
        of the service equipment, line terminals of a panelboard, etc.
        Use the one way length of one wire.

        Number Of Parallel Conductors Per Phase - the number of
        multiple conductors in parallel for each phase.



        _________________________  Page 21  _________________________


        Conductor Size - The Awg or Kcmil size of the wire. If the
        wire size is # 4/0, input 4/0 at the prompt. For 750 Kcmil,
        input 750. Acceptable wire range is from #12 to 1000 Kcmil.

        Line To Line Volts Of This Point -  The voltage available at
        the location where the fault current will be calculated. 600
        maximum. Do not include any voltage drop in this value.

        Single Or Three Phase -  Phase of this point.

        Description - Optional field for whatever you wish to enter.

        F2 - Press the F2 function key to select the wire material
        (copper or aluminum) and raceway type (steel, aluminum, pvc)
        used to supply this point. Note that raceway type also applies
        to cable armor. Also, the calculations are based on three
        circuit conductors in the raceway. If the circuit conductors
        for the point being calculated are contained within a raceway
        where other circuit conductors are present, the accuracy of
        the calculation could not be assured.

        Once all the above data has been entered, the results are
        automatically calculated and the fault current amps is
        displayed.

        Pressing the F3 function key will show the details of the
        calculation. The source current, the C Factor, F Factor, M
        Factor, and the calculated fault current are displayed.
        Pressing any key from the detail screen will return you to the
        data entry area with all previously entered data intact. Note
        that if you have not completely entered all required data for
        at least one point, the F3 key will not work. Note that the
        Description field need not be used, and leaving it blank will
        not have any effect.

        You can press PG UP or PG DN to scroll through the data entry
        areas for each of the number of points that you inputted into
        the initialization area. You can also PG UP until you are back
        in the initialization area, change the number of points to
        calculate, and PG DN through the areas without losing data.
        However, if you change to a lesser number of points, you will
        lose the data for the number of points greater than the newly
        selected number of points.

        A printout is available by pressing F10. See the documentation
        for printing for details.



        _________________________  Page 22  _________________________


        TERMINAL/CONDUCTOR TEMPERATURE LIMITATIONS

        NEC Section 110-14(c):

        This new requirement of the 1993 NEC specifies the temperature
        rules for termination of conductors. This requirement affects
        every termination of conductors to electrical equipment. It
        also includes separately installed pressure connectors such as
        lugs. The intent is to protect connected equipment from
        overheating due to the heat transfer that could result from
        the connection of, for example, a 90 degree C conductor to a
        terminal or device that has been tested and approved for use
        at 75 degrees C. If the conductor were loaded so as to operate
        at 80 degrees C, as long as it's ampacity was not exceeded, it
        would not be damaged. However, if that same conductor was
        connected to the terminal of equipment that was approved at 75
        degrees C, the 80 degree heat transfer  could damage the
        equipment or not allow the equipment to function as designed
        and listed.

        The basic rule is to provide two termination provisions for
        conductors and connected equipment, and a third provision for
        separately installed pressure connectors:

        110-14(c)(1) - This first provision groups equipment for
        circuits rated 100 amps or less, or equipment intended for
        conductors from #14 to #1. This rule requires the use of the
        60 degree C ampacity column of Table 310-16 for selecting the
        conductors used to connect to this equipment.

        Exception #1 permits the use of conductors with higher
        temperature ratings only if they are sized in accordance with
        their 60 degree C ampacity.*

        Exception #2 permits the use of higher temperature rated
        conductors at the ampacities of the higher rated conductors
        only if the connected equipment is listed for use with the
        higher rated conductors (such as a 100 amp breaker that is
        listed for use at 60 or 75 degrees C, AND, the panel or
        enclosure that the breaker is installed in is also listed for
        use at the higher temperature).

        110-14(c)(2) - This second provision groups equipment for
        circuits rated over 100 amps, or equipment intended for
        conductors larger than #1. This rule requires the use of the
        75 degree C ampacity column of Table 310-16 for selecting the
        conductors used to connect to this equipment.

        Exception #1 permits the use of conductors with higher
        temperature ratings only if they are sized in accordance with
        their 75 degree C ampacity.*



        _________________________  Page 23  _________________________


        Exception #2 permits the use of higher temperature rated
        conductors at the ampacities of the higher rated conductors
        only if the connected equipment is listed for use with the
        higher rated conductors.

        110-14(c)(3) - Separately installed pressure connectors shall
        be used with conductors at the ampacities not exceeding the
        ampacity at the listed temperature rating of the connector.

        Example:

        Select feeder conductors for the following sub-panel, where:
        The net computed feeder load is 60 amperes, the panel is
        listed for connection at 60 degrees C. maximum, Type THHN
        conductors are to be used, the ambient temp.is 30 degrees C.,
        no derating required.

        NEC 310-16, 60 degree C col. - #4 has an ampacity of 70 amps.



        VOLTAGE DROP CALCULATOR

        Calculates the voltage drop on existing or proposed single or
        three phase resistive AC circuits (100% power factor). Copper
        and aluminum conductors from #14 to 2000 Kcmil are supported.

        The 'Single or Three Phase' is obvious.

        The 'Length Of Run' is the length in feet of one conductor
        from the source of power to the load terminals.

        The 'Source Voltage' is the voltage measured at the source.

        The 'Amperage Of Load' is the current required by the load.
        For example, if the load is a resistance heater requiring 10
        amps to operate as designed, then the AMPERAGE would be
        entered as 10.

        The WIRE SIZE is in the range of #18 Awg to 2000 Kcmil. Do not
        include the # sign or the letters Awg or Kcmil. Enter the
        numeric size of the wire (ex. 14, 1/0, 250, 750).

        The COPPER or ALUMINUM prompt is self explanatory.

        After entering the above values, the program will calculate
        and display:

        1. The VOLTAGE DROP of the circuit (the number of volts
           dropped).

        2. The VOLTS AT LOAD (the voltage delivered to the load
           terminals)

        3. The % DROP (the percentage of the source voltage dropped)



        _________________________  Page 24  _________________________


                     OTHER ELECTRICAL SOFTWARE AVAILABLE
                     -----------------------------------

                LOADCALC Copyright 1991 By Robert J. La Capra
                                 Version 1.1

        LOADCALC is designed to perform service/feeder load calcs for
        single dwelling units. Full implementation of both the
        Standard and Optional Calculation Methods of the 1990 NEC.

        LOADCALC performs demand factoring, computes net computed load
        in volt-amps and amperes, determines minimum service entrance
        and feeder size.

        Complete, professional printed reports. Send report data to
        screen, printer, or to an ASCII disk file for import into your
        word processor. Also prints up to 4 header lines of your
        choice. Printer ports LPT1 and LPT2 supported.

        LOADCALC operates with 'what-if' capability. You can quickly
        and easily change only the data you wish to, without having to
        start a new calculation and re-enter all the required data.
        Results are calculated and displayed instantly.

        Context sensitive help, describing the expected input, any
        special definitions or requirements, and references to NEC
        Article/Section, where applicable.

        Quick reference tables for:
          Grounding Electrode Conductor Sizes (NEC Table 250-94)
          Service/Feeder Conductor Sizes      (NEC 310, Note 3)

        * Standard Calculation Method:
          Demand Factoring For:
            General Lighting, Small Appliance and Laundry Loads.
            Cooktop, Range, Wall Oven.
            Fixed Appliances.
            Largest Motor Load.

          Additional User-Definable Loads:
            2 add'l appliance loads, motor/nonmotor, fixed/nonfixed.
            1 add'l lighting load, continuous/noncontinuous.

          Automatic selection of larger of heating or cooling loads.

        * Optional Calculation Method:
        Demand factoring of 'other loads' as per NEC 220-30.

        Allows input of heating system type per NEC Table 220-30, and
        automatically determines larger of heating or cooling loads.

        Additional User-Definable Loads:
         2 additional appliance loads, 1 additional lighting load.



        _________________________  Page 25  _________________________


               Actual Printed Report From LOADCALC Version 1.1


          STANDARD SERVICE/FEEDER LOAD CALCULATION - One Family Dwelling

 Ralph Colbert
 23 Maple Tree Lane
 Byram Twsp., NJ 18539
 Block 55, Lot 10
 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 General Lighting ... : 3200 Sq. Feet x    3 VA =  9600 VA
 Small Appliance .... :    2 Circuits x 1500 VA =  3000 VA
 Laundry ............ :    1 Circuits x 1500 VA =  1500 VA
 ---------------------------------------------------------
 Total General Light & Small Appliance ........ : 14100 VA
 The First   3000 VA @ 100%  =   3000 VA
 Remaining  11100 VA @  35%  =   3885 VA
 ---------------------------------------
 GENERAL LIGHTING, SMALL APPLIANCE & LAUNDRY DEMAND LOAD ..... :  6885 VA

 Heating Demand ..... : 20000 VA @ 100% = 20000 VA
 Cooling Demand ..... :  9000 VA @ 100% =  9000 VA
 LARGER OF HEATING OR COOLING DEMAND LOADS (Heating) ......... : 20000 VA

 Cooktop ................. :  4000 VA
 Range ................... : 12000 VA
 Wall Oven ............... :  5000 VA
 COOKING EQUIPMENT DEMAND LOAD ............................... : 13850 VA

 Dryer ................... :  5000 VA
 DRYER DEMAND LOAD ........................................... :  5000 VA

 Water Heater ............ :  6000 VA
 Attic Fan ............... :  1000 VA
 Compactor ............... :   800 VA
 Dishwasher .............. :  1200 VA
 Disposal ................ :   650 VA
 Well Pump ............... :  1100 VA
 ------------------------------------
 Fixed Appliance Total ... : 10750 VA
     10750 VA @  75% Demand:  8063 VA
 FIXED APPLIANCE DEMAND LOAD ................................. :  8063 VA

 Largest Motor: Well Pump ............... : @ 1100 VA
 25% OF LARGEST MOTOR LOAD ................................... :   275 VA

 _______________________________________________________________________________

 NET COMPUTED LOAD ........................................... : 54073 VA

 120/240 VOLT SERVICE/FEEDER LOAD ............................ : 225 AMPERES



        _________________________  Page 26  _________________________


               Actual Printed Report From LOADCALC Version 1.1


          OPTIONAL SERVICE/FEEDER LOAD CALCULATION - One Family Dwelling

 Ralph Colbert
 23 Maple Tree Lane
 Byram Twsp., NJ 18539
 Block 55, Lot 10

 ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

 General Lighting ... : 3200 Sq. Feet x    3 VA =  9600 VA
 Small Appliance .... :    2 Circuits x 1500 VA =  3000 VA
 Laundry ............ :    1 Circuits x 1500 VA =  1500 VA
 Cooktop ...................................... :  4000 VA
 Range ........................................ : 12000 VA
 Wall Oven .................................... :  5000 VA
 Dryer ........................................ :  5000 VA
 Water Heater ................................. :  6000 VA
 Attic Fan .................................... :  1000 VA
 Compactor .................................... :   800 VA
 Dishwasher ................................... :  1200 VA
 Disposal ..................................... :   650 VA
 Well Pump .................................... :  1100 VA
 ----------------------------------------------------------
 Total Other Load ............................. : 50850 VA
 The First  10000 VA OF Other Load @ 100% = 10000 VA
 Remaining  40850 VA Of Other Load @  40% = 16340 VA
 ---------------------------------------------------
 OTHER LOAD DEMAND LOAD ...................................... : 26340 VA


 Heating Type:
 One Central Space Heating Unit And/Or Supplimentary Unit In Heat Pump
 Heating Demand Load ... :20000 VA @  65% = 13000 VA
 Cooling Demand Load ... : 9000 VA @ 100% =  9000 VA
 ---------------------------------------------------
 LARGER OF HEAT OR COOLING DEMAND LOADS [ Heating ] .......... : 13000 VA

 _______________________________________________________________________________

 NET COMPUTED LOAD ........................................... : 39340 VA

 120/240 VOLT SERVICE/FEEDER LOAD ............................ : 164 AMPERES



                          LOADCALC REGISTRATION FORM
                                     S1234

  NOTE: THIS FORM TO BE USED TO REGISTER FOR "LOADCALC" SOFTWARE ONLY. Do Not 
        use to register for "ELECTRC9" software.

Registration fee for 1 to 5 users is $45.00 for each user or machine.
Site License & Multiple discounts available for 6 or more users. Write for info.
Purchase orders without payment attached cannot be accepted.
US funds drawn from a US bank only.


INCLUDED WITH YOUR REGISTRATION
Disk containing latest program version and documentation file.
Documentation is supplied on disk file. No printed manuals available.
One License To Use Software for each user registered.
Unlimited support by US Mail and by CompuServe Mail. No phone support available.
Shipping via US Postal Service. Orders shipped same day registration received.

OPTIONAL ITEMS
* UPS Ground Delivery - $10.00 additional per order. Multiple registrations or
      registration of LOADCALC and ELECTRC9 together qualify as 1 order, and
      shipping charge is $10.00 total. Supply street address. NO P.O. BOXES.
* 1 Year Of Fax Support for LOADCALC - $10.00 additional per year. For multiple
      registrations of LOADCALC, fee is still $10.00 total.
      Fax # supplied with shipment.


Return This Form And Registration Fee PAYABLE TO:

                          ROBERT J. LA CAPRA
                          50 Hillside Terrace
                          Andover, NJ 07821
                          S.S.# 137-44-7561
SHIP TO:

Name: ____________________________________________________________________

Company: _________________________________________________________________

Address: _________________________________________________________________

City,State,Zip: __________________________________________________________

Phone Number: ______-______-________    Fax Number: ______-______-________


Number Of Users: ______ x $45.00 Each = Registration Fee .. : $___________

UPS Ground Shipping Charge - $10.00 Per Order [Optional] .. : $___________

One Year Of LOADCALC Fax Support - $10.00 [Optional] ...... : $___________
__________________________________________________________________________

                                    TOTAL FEE ENCLOSED .... : $___________


DISK SIZE PREFERRED:   [   ] 5 1/4"     [   ] 3 1/2"