The manual for the small version of HYDRONET 4.0 follows this order form...



ORDER FORM

Name: __________________________________________  Title: __________________

Firm: ___________________________________________  Phone: _________________

Address: __________________________________________________________________

City, State, Zip: _________________________________________________________


     Both 5 1/4" and 3 1/2" diskettes are included in all packages.


Quantity  Product                                   Price each    Total
____________________________________________________________________________
          HYDRONET 4.0 (single purchase)             $695.00 US
          Additional HYDRONET 4.0 packages (no limit) 495.00
          Upgrades from HYDRONET 3.0 to 4.0           150.00
              please list serial numbers_______________________
          HYDROFLO 1.2                                195.00
          H-CALC 1.1                                   95.00
          Combo - All 3 above products (save $140)    845.00

                          Calif. residents add 7.25% sales tax =
If desired, add $15 Express (2nd Day) within the U.S. per item =
   Outside the US, Canada and Mexico, add $30 airmail per item =

                                                Total Enclosed =

PAYMENT METHOD:
Check  or  M.O.  enclosed _____      or    COD  delivery _____

VISA ______  or MC ______  #_____________________________   Exp. _____/_____

Exact name on card _________________________  Bank issuing card ____________

Cardholder  signature ________________________________________


Foreign orders MUST be pre-paid in US Dollars drawn on a US bank.  Larger
Corporate and Gov't P. O.s accepted.   Please call for exact postage on
larger orders.   Quantity discounts and site licenses available.
 
Mail or FAX to:  ENGINEERING SOFTWARE
                 P. O.  Box 8128
                 Truckee, California  96162
                 (916)  582 - 1525    FAX (916)  582 - 8579




ENGINEERING  SOFTWARE'S

HYDRONET - Small version
Hydraulic Network Analysis Design Tool

Version 4.0

FOR THE PC/MS-DOS OPERATING SYSTEM

Software and manual written by
Brian Haulman
for

ENGINEERING  SOFTWARE
P.O.Box 8128
Truckee, California 96162
(916) 582-1525
FAX (916) 582-8579
Copyright (c) 1992, Brian Haulman

INTRODUCTION


HYDRONET is a hydraulic network analysis tool based on the popular
Hardy-Cross method.  A hydraulic network is a closed pressurized
fluid distribution system made up of pipes, fittings, valves, pumps
and reservoirs.  Examples of networks are industrial fluid conveyance,
municipal water supply, fire protection sprinkler, petroleum transport
and recirculating HVAC systems.  In a network, many interconnected
conveyance lines deliver liquids to numerous destinations simultaneously.
The change in flow through any single pipe influences the flow in all
other regions of the network.  The engineer must know the operational
steady-state flows and pressures throughout the system so that pipe and
pump sizes and system strengths can be specified to meet cost and safety
criteria.  These steady-state flows and pressures can only be determined
through an iterative flow adjustment process.  The Hardy-Cross method
lends itself to this task and, with the help of computers, the analysis
of hydraulic networks becomes a straight forward process.  Once a system
is defined by describing the components in detail, various operational
strategies can be investigated.



The full featured version of HYDRONET provides the ability to model large
systems of up to three thousand nodes and three thousand pipes, valves,
fittings and pumps.  Saving of datafiles, report output to file or printer
and digitizer support is also available.  This small version is limited to
systems of 26 nodes, 22 pipes, 16 valves and fittings and 2 pumps.  With
this limitation it is able to retrieve all the sample HYDROFLO datafiles.
It will only allow you to create 10 loops and 5 branches.  By using the Hazen-
Williams and Darcy-Wiesbach equations to determine pipe head losses, any
type of incompressible fluid can be modeled in an analysis when the proper
fluid properties and pipe conditions are known.  HYDRONET also provides
plots of the 2-dimensional system plan view, 3-dimensional view of the
overall system, hydraulic grade lines and pump performance curves.  A
complete menu of fittings and valves are available for incorporation into
hydraulic systems.  Various control valves can be modeled and will
accurately simulate their physical operating characteristics.  If you have
a Summagraphics or compatible graphics tablet (digitizer), x-y coordinates
for nodes can easily be entered and 2D and 3D system graphics can rapidly be
created.



INSTALLATION


INSTALL is the installation program and must be run before using the small
version of HYDRONET.  You must have 700K of space available on your hard
disk to install HYDRONET.  After starting your computer (booting-up), place
the HYDRONET diskette in a floppy drive and type... 

   drive:INSTALL   where "drive" is the floppy drive holding the diskette.
 
You will be prompted for the source drive and destination path to install
HYDRONET in.  The system files will be uncompressed and installed.


NOTE:  HYDRONET uses overlay technology so execution speed will be enhanced
when you use disk cache software.  Ideally, you want to use caching software
that makes use of Extended or Expanded memory and does not use up any of your
conventional main memory.  DOS's SMARTDRV.SYS is a good disk cache program.


To start the small version of HYDRONET, place yourself in the directory
where it was installed and at the DOS prompt type SMHN.  You wil then
specify the type of display adapter you have.  HYDRONET will take a few
seconds to load.


START-UP

While loading, HYDRONET does a quick check of your graphics tablet
(digitizer) if available, and will warn you of any possible problems.  If
you get a warning, be sure the cursor is in proximity and that you have
properly used the DOS MODE command (see above) to setup your serial port.

The top line of the main HYDRONET screen displays the HYDRONET copyright
notice and version number on the left and the current data filename on the
right with the word "Balanced" if the system has been solved.  Below that is
a space for the current system's title (description) if entered.  The bottom
line of the screen has the computer time and date on the left and the right
has a space reserved for error messages when they occur during system
operation.  The various keystrokes available as responses for any HYDRONET
prompt are displayed on the line just above the bottom of the screen.



         HYDRONET uses the following menu and keystroke syntax...

To select an option from a displayed menu:

        - Use the space bar or cursor arrows to highlight the option and
                 press RETURN (Enter), or
        - press the first character of the menu option name.

To exit from a menu or operation:

        - Press escape (Esc key).
            (Note:  pressing escape repeatedly eventually brings
            you back to the main menu but won't allow you exit to
            DOS.  To fully exit HYDRONET, you must press "Y" at QUIT.)

An on-line help facility is available by pressing the F1 (function) key
anywhere during program execution except in graphic modes.  To obtain help
for a specific menu option, simply highlight the option (using the space
bar) without selecting it and press the F1 key.

When entering characters or numbers in data fields, a toggle between insert
mode and overtype mode is available by pressing the insert (Ins) key.  After
a desired numeric value has been input in a field, press the space bar once
and any remaining characters to the right will be disregarded.





UNDERLYING  THEORIES


THE HARDY CROSS METHOD


The Hardy-Cross method is based on two principles...


      1. The sum of the head losses around a single loop always equals zero
                  (conservation of energy).

      2. The sum of flows into and out of a node always equals zero
                  (conservation of mass).

HYDRONET automatically makes an initial estimation of flows in the system
then adjusts the flows in each loop to meet both the above conditions.  The
flows then approach the steady-state flow levels with each successive
iteration.  You provide the flow tolerance level at which HYDRONET will
exit the flow adjustment process.

The Hardy-Cross method is one of the most stable solution methods in
solving for steady-state pressures and flows throughout complex hydraulic
networks.  Certain instabilities can occur when the loops in a system are
not of near equal length in terms of nodes and elements or when impossible
conditions are set and cannot be met.  In general, the parameters displayed
on the screen when balancing will indicate the stability of the current
design.  If you start inputing smaller sections of a design and balance
the system as you go, you should have no problems.

The original work on the Hardy-Cross method is published in "Hardy Cross,
Analysis of Flow in Networks of Conduits or Conductors", Univ Ill. Bull.
286, Nov. 1936.  Also locate the books "Developments in Water Science" by
David Stephenson,  "Analysis of Flow in Pipe Networks", by Roland W.
Jeppson, Ann Arbor Science,  or "Analysis of Water Distribution Systems"
by Walski for additional information.



NODES

Nodes are the discrete physical points at either the junction of two
elements (pipes, valves, fittings or pumps), at the end delivery point
of a fixed flow line (branch) or at the location of the inlet or exit
of a reservoir (an unknown source or discharge of fluid).  The data
required for complete description of a node are: an optional description,
elevation, demand, head (pressure), and x-y coordinates.

There are two types of nodes used by HYDRONET...

       1.) "fixed flow" nodes where the flow (demand) is set and the
                  pressure head is to be determined,
       2.) "fixed head" nodes where the pressure head is set and the
                  flow is to be determined.

You are not allowed to set both the demand and head at a node.


FIXED FLOW NODES

HYDRONET determines the needed pressure head at "fixed flow" nodes that
will provide the specified demand flow.  In practice, the head at these
nodes is lowered until the demand is met.  Nodes between elements
where the demand is left at zero and the pressure is to be found, are
also of the "fixed flow" type.  The demand will always be out of the
system at these nodes.  If you desire to supply fluid into a system
at a node, it must be modeled as a "fixed head" node and start or end
a pseudo-loop (see pseudo-loops above).


FIXED HEAD NODES

Nodes at an inlet or exit of a supply of unknown flow but known head
are termed "fixed head" nodes (type 2 above).  Nodes that exist between
elements that are not in a branch line can be either "fixed head" or
"fixed flow" type.  Examples of "fixed head" nodes are...

 - discharge or supply point from a pressurized or open tank.
 - discharge or supply point from a lake or reservoir.
 - discharge or supply point from a hydrant, sprinkler head or force main.



LOOPS

Loops consist of an alternating node - element - node - element - node
sequence.  HYDRONET uses two types of loops, pseudo-loops and closed loops.


PSEUDO-LOOPS

If a network is to be modeled as having flows into (and therefore out
of) the system, there must be at least one pseudo-loop in the
model.  These loops allow HYDRONET to determine the flow in or out based
on the user specified pressure head.  Pseudo-loops start and end with
"fixed head" nodes.  The head difference between the starting and ending
"fixed head" nodes maintain a constant head loss or gain in the
calculation of total head losses around a loop.  A sequence of nodes and
elements connecting two pressure mains or reservoirs (tanks) would be a
pseudo-loop.  All "fixed head" nodes must be at the beginning or end of at
least one pseudo-loop.  For example, if there are three "fixed head" nodes
(points of unknown inflow or outflow) in a system, there would be at least
two pseudo-loops connecting these nodes.  It will not hinder the balancing
process to use three pseudo-loops to connect all three "fixed head" nodes
to each other and in some cases will actually speed the convergence to a
solution.


CLOSED LOOPS

Single closed loops start and end at the same node.  They
trace a complete path around a loop of elements and nodes, ending at the
node where the loop started.  There may be many single closed
loops in both open (external inflows/outflows) and closed (recirculating)
loop systems.  This single "closed loop" is different from what is
commonly termed a "closed loop system".

A network modeled by HYDRONET need not have flow into and out of the
system.  There are many recirculating systems that can be modeled where
the fluid is moved around a system by an internal pump.  These "closed
loop systems" may have many internal single closed loops but have no
inflows into or discharges from a system.  They may have a recharge
source to replenish lost fluid but this is not part of a steady-state
analysis.  A "closed loop system" therefore has no pseudo-loops because
there are no "fixed head" nodes.  All demands at "fixed flow" nodes will
be zero.  An example of a "closed loop system" is a chilled or heated
water system in HVAC (Heating/Ventilation/Air Conditioning) systems.



BRANCH  LINES

Branches are fixed flow lines that remove flow from a system.  During the
iterative head loss balancing procedure, all network loops (pseudo-loops
and closed loops) are balanced.  After that, HYDRONET uses the head at the
node that starts the branch to perform simple head loss calculations for
all elements out to the ending branch node.

All the nodes in branches are of the "fixed flow" type so they will each
have fixed demands (fixed at a zero or non-zero flow) and HYDRONET will
determine the branch node pressure heads.  The last node will have the
fixed flow out of the line entered as it's demand.


PIPES

Both the Hazen-Williams and Darcy-Wiesbach equations are available for
the determination of major friction losses in pipes.  The question of
which equation to use depends on fluid conditions.  When Darcy-Wiesbach
meets Hazen-Williams conditions (see below) either equation may be used.
Comparing the results of both equations on 60 degree F water systems can
confirm proper modeling.

The empirical Hazen-Williams equation is available for water systems under
turbulent flow conditions at 60 degrees F. (15.6 degrees C. or turbulent
conditions for fluids with kinematic viscosity around
1.2x10-5 ft2/s).  To use this equation, Hazen-Williams coefficients are
needed for all pipes.  These coefficients have been determined by empirical
methods.  See Cameron page 3-8.  Using the Hazen-Williams equation allows
a system model to converge to a steady-state solution quicker than using
the Darcy-Wiesbach equation.

The fundamentally based Darcy-Wiesbach equation can be used for fluids of
different viscosities.  The kinematic viscosity of the fluid must be known
as well as the piping materials specific roughness (sometimes called
absolute roughness).  Fittings and valves must have custom K values or be
modeled as equivalent lengths of pipe.  HYDRONET uses the Newton-Raphson
method to solve the Colebrook-White equation which then determines the
Moody friction factor, f.  There is no need to manually look-up
friction factor values from the Moody diagram.



FITTINGS

The head loss (conversion of flow energy into heat) due to a gradual
bend in a pipeline is primarily caused by a secondary double spiral flow
which is superimposed on the main flow.  In moving around the bend, the
larger centrifugal force acting on the faster moving center core fluid
forces it toward the outside of the bend.  This added head loss occurs
for as much as 50 to 100 pipe diameters down the next pipe and does not
occur at the bend itself.  These head losses may be minor in systems that
have large lengths of pipe but may be a large component of the losses in
intricate systems with many bends and valves.


HYDRONET has a large selection of fitting resistance (K) coefficients
available for use in WATER systems.  Minor friction losses through
fittings (which includes inlets and exits) in water systems are modeled
by multiplying the velocity head by the appropriate resistance coefficient,
K (see Cameron Pg. 3-110 to 3-116).  HYDRONET automatically uses the proper
friction coefficient upon menu selection of the type and diameter.  Custom
fitting and valve coefficients can also be easily input by the
user.  Reducers, enlargements, orifices and nozzles are also able to be
modeled by HYDRONET.


Friction loss data for fittings and valves in systems modeling fluids
other than water are not readily available and those that are available
vary widely.  The best approach is to assume turbulent flow conditions
and specify that HYDRONET use the equivalent length method for fitting and
valves head losses.  This method models fitting and valve friction in terms
of the friction of turbulent flow through lengths of standard schedule 40
steel pipe.  The calculation of equivalent pipe length is based on the "K"
coefficient for water flow through the fitting or valve, the diameter of
the valve and the friction factor for complete turbulent flow in steel pipe
for this diameter.  Details of these calculations are in Cameron Hydraulic
Databook (pages 3-110, 3-119 to 3-122) and in the section entitled "USING
THE EQUIVALENT LENGTH METHOD" in this manual.


VALVES

A large selection of valves are available for use in water system design.
As with fittings, custom K values can also be input for valves not listed.
Control valves without fixed K values (ie, pressure and flow control
valves) can be used directly for non-water systems because their head
losses are set as needed and are not dependent on fluid conditions.  These
control valves slow down the balancing procedure substantially when used.


CHECK VALVES (CV)

Check valves allow flow in only one direction.  It is important to check
the operating flow velocity to ensure the complete opening of check valves
and therefore the correct friction factor.


PRESSURE REDUCING VALVES (PRV)

PRV's will not let the specified pressure be exceeded downstream.  If the
pressure is already below the specified level, the PRV will have no effect.


PRESSURE SUSTAINING VALVES (PSV)

The specified pressure will be maintained upstream if possible, with nearly
a complete shutoff if the pressure cannot be met.  Head losses are introduced
until the upstream pressure is above the specified level if possible.


FLOW CONTROL VALVES (FCV)

FCV's are modeled like PRV's by introducing enough head loss to decrease the
flow to the specified level.  If the flow is below the specified level, then
the FCV has no effect.


FIXED HEAD LOSS DEVICE (FHL)

The specified head loss will be introduced no matter what the flow is in the
line.  If convergence problems result in a system with a FHL device, try
removing it.  If the system then converges, try lowering the amount of head
loss.  The loop must provide enough added head (by pump or static head
difference in a pseudo-loop) to overcome the fixed head loss.



PUMPS & FLOW VS. HEAD DEVICES (FVH)

If you specify a pump from the element menu, you can select either a
pump or flow vs. head (FVH) device.  HYDRONET allows pumps to be modeled
by adding their head additions to loop head calculations.  FVHs are modeled
by incorporating their their head losses.  Pump curves are described by four
equidistant points and are fit to a cubic equation.  FVHs are described by
three equidistant points on a curve and are fit to a polynomial equation.  A
continuous function for head versus flow is then available for both
devices.  Pump manufacturers provide plots of their pump performance curves
and the four points can be easily taken from them.  The third point input
for a pump curve should be close to it's optimal operating point (second
point for a FVH).  Pump and FVH operation results for balanced HYDRONET
systems include flow rates and operating heads.


The REPORT - DETAIL PUMPS option lists a pump's suction head if the system is
balanced.  These values are critical in the operation of a pump to prevent
cavitation.  The Net Positive Suction Head (NPSH) must always have a positive
value.  The Net Positive Suction Head Available (NPSHA) depends on the system
design and, for an existing centrifugal pump, it is the total suction head in
feet (or meters) of liquid (absolute at the pump centerline or impeller eye)
less the absolute vapor pressure in feet (or meters) of the liquid being
pumped.  A pump's Net Positive Suction Head Required (NPSHR) can be obtained
from the pump's manufacturer.  The NPSHA should be above the pump NPSHR.  If
it is not, the situation must be remedied by using larger diameter suction
pipes by placing the pump closer to higher pressure sources (reducing
dynamic suction lift) or by placing the pump at a lower elevation (reducing
the static suction lift).


The suction head value presented by HYDRONET for a pump must have the
atmospheric pressure (when dealing with gage pressures) along with the
velocity head added to it minus the fluid's vapor pressure to approximate
the NPSHA (Net Positive Suction Head Available).  See Cameron Hydraulic
Data page 1-10 to 1-17 for more information.  Vapor pressures of hot
liquids may be very critical to the calculation as can the velocity head
of low head pumps.




MENU OPTIONS

FILE


The FILE option allows the retrieval from and the saving to disk of
HYDRONET datafiles.  Engineering Software's HYDROFLO datafiles can also
be read (see below).  HYDRONET datafiles store system information in a
compact proprietary binary format.  HYDRONET data filenames are appended
with the extension of " .NET " automatically.  You need not type in the
extension and you cannot override it.  You should not name any report
files or any other files with a .NET extension.

The RETRIEVE sub-option displays screens of HYDRONET data filenames.  Use
the space bar or arrow keys to highlight the desired filename and then
press RETURN to select the desired datafile.  You will then be asked whether
you want to load the file.  Any current system data information and changes
will be erased from memory and the new file will be loaded when you answer
"YES".  You should save any current system data, if it might be needed
later, before retrieving any datafile.

You may also press function key F2 and key in a custom path and
filename.  When you first press F2, the current path will be shown ready
for a new filename.  This is handy for the retrieval of HYDROFLO datafiles
in the current directory (see below).  Press escape (Esc) and an entire
path can be entered with a filename.  Datafiles retrieved will be read by
HYDRONET and the main menu screen will return with the filename displayed
in the upper right corner.  The new data is now available for use and any
previous system data is gone.

HYDROFLO files are NOT displayed along with HYDRONET filenames.  Press F2
(input a custom path and filename) at the RETRIEVE option and enter the
exact path and filename (including the .FLO extension).  If the HYDROFLO
system specified that the pump curve is to be prescribed, you must enter a
pump curve for the system prior to balancing.  HYDROFLO systems will
consist of one pseudo-loop when brought into HYDRONET.  Once in HYDRONET,
datafiles cannot be output in the HYDROFLO datafile format.

If there are more than 55 datafiles in the current directory, more
datafiles can be displayed by pressing the Page-down (Pg-Dn) key.  Each
successive screen will display the next available 55 datafiles.  To go
back to the first screen of filenames, press the Page-Up (Pg-up) key.
You may also press the F3 key to delete the highlighted file from disk.
If you answer "YES" to the delete prompt, the file will be erased from
disk completely.  Pressing the F4 key when a filename is highlighted,
displays the file's title (short description) if entered from the
UTILITIES - TITLE menu option.

When SAVE is selected, the current path and filename will be displayed.
If the current hydraulic design has not been saved or retrieved previously
(a new system), you must specify a filename.  If the file has a name it
will be displayed.  Pressing the escape (Esc) key will present the current
path ready for you to enter a new filename.  Pressing the escape key again
allows both a new path and filename to be entered.  When saving a datafile,
if a file with the same name exists, the following message will be
displayed:

                 file exists!   Cancel  Replace

Press "R" (replace) to overwrite the data file or "C" (cancel) or the
escape (Esc) key to quit the overwrite and cancel the operation.  Once you
have saved a datafile, it will appear in the main list available for use
later.



SETUP

The SETUP option is used to set the default data file directory (where
*.NET datafiles reside), pipe head loss equation, flow tolerance, units
system, units for node and pump heads and flows, fluid properties, bell
on-off, automatic pipe length calculation, use of the equivalent length
method and default friction coefficients.  The bottom of the screen
displays the current hardware configuration for your system.



The up or down arrow keys are used to move between the various input fields
(RETURN acts like the down arrow).  Pressing the escape (Esc) key (or moving
off the end of the fields) will lead to the prompt:


         Reset current system to new values?     NO     YES


If the new parameter values aren't correct or desired, press the escape
(Esc) key or " N " to return to the main menu.  If they are correct,
press RETURN and the system will use the new parameter values and the
next prompt will appear:


         Update default parameter file?     NO     YES


This prompt will only appear if the previous prompt is answered with a
"Y" .  A  "Y" (yes) response to this question will update the HYDRONET
default parameter file that automatically sets initial values upon
start-up.  This is a time saver in establishing new designs and provides
custom setups in multi-user environments.  For example, if an engineer
will always be using the Darcy-Wiesbach equation to analyze oil conveyance
systems, HYDRONET can start with these parameters automatically.  On hard
disk systems, each person can have their own user directory and HYDRONET
will be configured with their desired parameters and view only their data
files while using a central directory for the HYDRONET system files.



SETUP - PARAMETER DESCRIPTIONS

The DATA FILE DIRECTORY is the path where HYDRONET will look for data files
(shown in the FILE - RETRIEVE option).  This DATA FILE DIRECTORY should be
set to the users own sub-directory.  A user may make numerous sub-directories
each for a specific project so that just those datafiles will be displayed
when using FILE - RETRIEVE.  The named directory must exist and HYDRONET
will verify that it exists.  If you press the space bar (erase all characters)
in the DATA FILE DIRECTORY field, the current directory you reside in will be
inserted.  If running HYDRONET from another directory, be sure the HYDRONET
system directory is listed in your path.  (Type path at DOS prompt. See your
DOS manual.)

Pressing RETURN (or down arrow) highlights the HEAD CALCULATION EQUATION
field.  You may choose either the Hazen-Williams or the Darcy-Wiesbach
equation to calculate pipe head losses by pressing the left or right arrow
keys and then pressing RETURN or the arrow down key to select it.  The
differences in these equations is described in the preceding
"UNDERLYING THEORIES - PIPES" section.

The UNIT SYSTEM field is now highlighted.  English or Metric units may be
chosen as above, by pressing arrow right or left then pressing RETURN or
arrow down to select.  HYDRONET does not allow an automatic conversion of
hydraulic systems to or from English and metric unit systems.  Conversions
can be partially made by selecting the desired unit system, then using the
routines available in the UTILITIES option.

The SYS (System) FLOW UNITS are the flow units that element (all but pump
flows) and node flows will be displayed in.  Metric units of liters/second
and cubic meters/second and English units of cfs, gpm, Imperial gpm and
MGD (million gals/day) are available.

The FLOW TOLERANCE is the flow level at which HYDRONET will exit the
iterative flow adjustment balancing process.  The iterative process can
always be exited by pressing escape or the F2 key.



MENU OPTIONS - SETUP

SYS (System) HEAD UNITS are selected like flow units before.  If using
units of psi (English) or Kpascals (Metric), be sure to set the needed
specific gravity.

The DEFAULT SPEC ROUGH (SPECIFIC ROUGHNESS) or DEFAULT H-W (HAZEN-WILLIAMS)
COEFFICIENT can be set so that you have only to press RETURN when performing
pipe data input.  This does not change any currently defined pipe friction
coefficients.  To change ALL EXISTING pipe roughnesses to a new value, use
the UTILITIES - FRICTION option.  To change a specific existing pipes
roughness coefficient, enter the DEFINE option and press F2 when positioned
at the pipe.

The SPECIFIC GRAVITY value is needed for the conversion of head units to psi
or Kpascals.

The KINEMATIC VISCOSITY is required when using the Darcy-Wiesbach equation.
(See Cameron page 3-4.)

BELL ON-OFF selects whether the beep will be sounded for errors and data
input.  Pressing arrow-right or arrow-left will toggle the choices.

The PUMP HEAD & FLOW UNITS are the units in which head and flow values will
be displayed for all pumps and FVH devices.

The AUTO PIPE LENGTHS parameter specifies whether you want pipe lengths to
be automatically recalculated when ANALYZE or BALANCE is chosen.  This will
only be done if node coordinates are defined (non-zero).  If you leave a
pipe's length at zero, it's length is automatically calculated even if
the AUTO PIPE LENGTHS field is "NO".  When a pipe's length is not zero and
you change an adjacent node's coordinates, the length would not be
recalculated unless this field is set to "YES".

The USE EQUIV LENGTH METHOD field tells HYDRONET whether to model fittings
and valves as equivalent lengths of standard steel pipe.  This is needed for
modeling systems that convey fluids other than water.  The K coefficients
from the fitting and valve menus are for water systems only.

The bottom of the SETUP screen displays your current hardware configuration.
Re-run the HNINSTAL program to change this configuration if not correct or
if you change any of your hardware devices.



DEFINE

Use the DEFINE main menu option to enter element and node data.  The
sub-menu of " LOOPS  BRANCHES " allows either loop (pseudo-loop and closed
loops) or branch information to be entered.  Select LOOPS by highlighting
the word and pressing RETURN or simply pressing the letter "L".


GRAPHICS TABLET ALIGNMENT AND USE

If you are using a graphics tablet, when you enter the DEFINE option and
either edit or enter node data, you will be asked to align the tablet
with the diagram of your system.  This procedure may be postponed by
pressing the escape (Esc) key and using the Tablet Align (F6) function
later.  To align the tablet, the drawing of your system should be placed on
the pad so that the x direction runs parallel to the bottom line boundary
of the pad (x values increasing to the right) and the y direction is
parallel the right and left sides of the pad (y values increasing toward
the top).  You will enter two diagonal random points (x1,y1 and x2,y2)
from your drawing (ie., diagonal so that x1 does not equal x2 and y1 does
not equal y2).  Enter the x and y coordinates of the first point from the
keyboard.  Place the cursor (stylus) cross-hairs at that point and press
any button.  You will then be prompted to input the second point's
coordinates and click the any cursor button on the second point.  If no
response comes from the graphics tablet, press escape and make sure that
the DOS MODE command has been used to correctly setup the proper serial
port (see the INSTALLATION and START-UP sections).  To re-align the tablet,
while in the DEFINE option, simply press the F6 key when not editing element
or node data.  Repeat the procedure when inputing data from drawings larger
than your graphics tablet.  Press the escape (Esc) key to exit from the
tablet alignment procedure.

When positioned at a node's x coordinate field the statement to place the
cross-hairs at the node is displayed.  The proper coordinates will be
automatically inserted into the field when any button on the tablet cursor
is pressed.  If you do not wish to take advantage of the 2D and 3D graphics,
simply leave all node coordinates at 0 (zero).  They will be displayed as
" N/A " for not available.


LOOPS

Upon entering the LOOP sub-option of DEFINE, you will be prompted for a
loop number if a new design is being entered.  The loop number offered for
use will be the lowest loop number not yet used.  Use this number or enter
any other number you desire.  If you have retrieved a datafile, the first
screen of the lowest numbered loop in the system will be displayed.  Loops
can be entered in any order.

You will enter data for nodes and elements in the same order that they
occur in the loops of your design (ie, node - element - node - element -
node, etc.).  It doesn't matter if you enter the element and node data in
clockwise or counter-clockwise order.  The default value in the element
or node number field will be the lowest number that has not been used
in the current design.  You can overtype this value with any number
desired.  Upon pressing RETURN, the node data fields appear.  Once the
first node's data is input, an element menu will appear and allow the
next element's type in the sequence to be specified.  Once the element
type is selected by highlighting it and pressing RETURN, the input field
for the element will appear.  To input the second and remaining loops,
press the F9 key.  Select "LOOP" by pressing Return or " L " and enter
the loop number.  If the loop exists, it will be displayed.  If the loop
has not yet been created, you will be asked whether you wish to create it.
The current loop or branch number out of the total number in the design 
and the current screen (page) out of the total number of screens in the
current loop or branch will be displayed on the bottom of the screen.


BRANCH LINES

HYDRONET allows fixed flow discharge lines to be included in a network
design.  These lines are not part of the actual "network".  Simple head
loss calculations are performed to find the heads at branch nodes.

The flow direction in a branch is always away from the node that starts
the branch (the node connected to the network).  On the screen this flow
appears left to right.  The direction is described on the bottom of the
branch input screen.  Branch input ends at the last discharge point
in the line.  This last node will have the flow through the branch entered
in it's demand field.  Other nodes in a branch may have a demand value
entered also.  The first node in a branch is the only node that may occur
elsewhere in the system since branches are outlets and do not flow
into other parts of the system.  Nodes with "fixed heads" are not allowed
in branch lines because the flows are fixed.  You are not allowed to have
a branch off of another branch because this would actually be a network
problem in deciding the flows in each line.




These sections detail the types of nodes and elements that may be used...

NODES

Node data includes optional description, elevation, demand (flow), head
(pressure) and optional x-y coordinates.  There are two types of nodes.
Nodes with a "fixed head" and those with a "fixed flow".  Do not enter
the optional description if you wish to save memory.  It will use up
memory much faster than just the essential node and element data needed
for network analysis.

If you are inputing node data and have just entered a fitting, valve or
pump, the elevation and X-Y coordinates will default to the values used
for the node on the other side of the element.

A node with a fixed pressure and an unknown inflow or outflow is a termed
a "fixed head" node.  Examples are any supply or outlet fluid level
(reservoir, tank, etc.) or an unrestricted supply or drain of fluid at
a specific elevation and pressure.  For a fluid reservoir at a specific
surface height, the surface elevation would be input in the elevation field,
a " ? " (question mark) would be input in the demand field (specifying
that flow is to be solved for), and zero would be entered in the head field
(if at atmospheric pressure using gage pressures).  If describing a node
for a pressurized tank or a system with absolute pressures, enter the non-
zero pressure in the head field.  As an example, a supply point (hydrant)
would have it's inlet elevation entered, then a " ? " in the demand field
and the actual or desired supply pressure entered for head.

A node with a head to be determined, is a "fixed flow" node, even if the
flow (demand) at the node is zero (zero is a fixed value).  These nodes will
generally be the internal points in a design (ie, points between pipes,
pumps, valves etc).  The elevation would be the physical elevation of the
node and the demand would be input as zero or a negative amount signifying
flow out of the node.  The head field therefore requires a " ? " to be
entered so that HYDRONET will solve for the resulting pressure.

When a system is balanced, "fixed flow" nodes will have the node's
pressure head highlighted in screen reports.  "Fixed head" nodes will have
the node's demand flow highlighted.  In file and printer reports, "fixed
head" nodes will have "fh" listed on the same line.


With the X-coordinate field highlighted, the coordinates of a node can
be specified.  This is optional and if you do not wish to use the 2-D or
3-D view of your system, then simply press RETURN to leave coordinates
at 0,0 and bypass this data.  You should not specify coordinates of 0
(zero) for x or y, unless you wish the coordinates to remain undefined
and not be plotted.  An undefined coordinate will be displayed as
"N/A".  HYDRONET will not plot nodes that have
coordinates of zero when displaying 2-D and 3-D graphics.  To enter the
coordinates of a node using a graphics tablet (see USING GRAPHICS TABLETS
previously), simply place the stylus (tablet cursor) cross-hairs at the node
when a node's X-coordinate field is highlighted and press any button on
the tablet's cursor.  The coordinates will appear in the fields and you
can press any cursor button again to re-do the values or press the RETURN
or ENTER key twice to accept the values.


PIPES

The data entered for pipes include optional description, diameter, length
and friction factor.  A non-zero diameter is needed to set up the default
system diameter.  The friction factor that appears will be the default
coefficient specified in the SETUP menu option and can be edited or another
friction value can be input.

If setting node coordinates, either manually or with a tablet, you
can set pipe lengths to zero and HYDRONET will calculate the distance
between the nodes and set the pipe length accordingly.  The lengths will
be calculated once ANALYZE or BALANCE is selected.  Once the pipe lengths
have been calculated and are non-zero, they will not be re-calculated unless
the AUTO PIPE LENGTHS field in SETUP is set to "YES" or you have set the
diameter to zero again.  Setting the AUTO PIPE LENGTHS field to "YES" makes
the calculation of pipe lengths automatic when node coordinates are changed.


FITTINGS

The fitting and valve coefficients automatically used by HYDRONET when
selected from the menus are for water systems only!  You must specify the
use of the equivalent length method in the SETUP option to model fittings
and valves in non-water transport systems if you do not have custom "K"
values. See the section on "USING THE EQUIVALENT LENGTH METHOD" for more
information.

The fitting menu lists numerous types including inlet and exit openings. 
Use the cursor arrow keys to highlight the desired fitting and press
RETURN to select it.  You will then be prompted for the fitting's
additional description (optional) and actual inside diameter and
HYDRONET will use the appropriate K value for the fitting in it's head
loss calculations when you are modeling a water transport system.  You
have the option of pressing F2 on the fitting menu to input custom K
values.  NOTE:  The diameters you enter for fittings and valves should
be the actual inside diameter.  These inside diameters are converted
to nominal schedule 40 steel diameters (Cameron pg 3-120) to obtain the
proper coefficient from the tables in Cameron (pages 3-111 to 3-116).

Enlargements and contractions (reducers) are also available.  You are
required to have pipes on both sides of these fittings.  You need
to enter the full angle of change between pipe diameters.  HYDRONET will
perform a calculation for head loss using the inside diameters of the
elements on each side of the fitting.  (See the formulas on page 3-117 and
3-118 of Cameron).  Sudden enlargements/contractions
(reducers) can be specified by entering an angle of 180 degrees.

Nozzle and orifices can be modeled by HYDRONET.  Calculations are performed
as on page 2-8 of Cameron.  You are required to have a pipe
on at least one side of the orifice.  You will enter a C value that describes
the shape of the opening along with the inside diameter.  When using the
equivalent length method, nozzles and orifices will not be converted to
a length of pipe because a "K" fitting value is not used for these fittings.

If the fitting was previously defined and is to be edited, press F2 when
positioned at the fitting and it's data will appear for alteration.  You can
press the escape (Esc) key twice and retain the fitting's data at any
time.  You must press RETURN or the arrow down key at the last data field to
have any new data
changes take effect.  Pressing the escape (Esc) key only once presents the
fitting menu again to select a different type.  You can select a new fitting,
press F3 to enter a custom fitting or press F4 to display and select from the
valve menu.  When you simply enter a new inside diameter for a fitting type
from the menu, HYDRONET will use the appropriate K value (see pages 3-111
to 3-115 of Cameron).


VALVES

The valve menu lists numerous
types (gate valves, butterfly valves, various control valves etc.).  Use
the cursor arrow keys to highlight the desired valve type and press RETURN
to select it.  You will then be prompted for optional description and the
valve's inside diameter.  HYDRONET will use the appropriate K value
for it's head loss calculations in water systems.  Custom K values can
be entered by pressing F2 at the valve menu.  Editing previously defined
valves follows the same procedure as editing fittings described at the
bottom of the previous page.


CONTROL VALVES

Use of control valves substantially slows down the balancing procedure.
This is because the system must be balanced completely first, then solved
for head levels and valves checked for proper operation.  The system is
then balanced, heads solved for and the valve checked again.  This is
repeated until the system operates correctly.  If you know that you are
going to be doing a lot of design changes, you may want to set the
balancing tolerance higher to allow a faster, though less accurate, solution
until the design is near it's final form.  Then lower the tolerance to the
desired level.

Using valves that impart a head loss to the system (ie, PRVs, PSVs and
FCVs) to obtain a desired effect, takes energy from a system.  Most of the
time it is more desirable to design a system that doesn't need to burn up
head.  Head that is not wasted results in use of smaller pumps and overall
lower costs for a system.  Smaller diameter pipes burn up more head and,
therefore, provide more back pressure on the system.


- CHECK VALVES (CHV)

Check valves allow flow only in a specified direction.  The direction is
specified the same way pump flow directions are.  Use the right or left
arrow keys to change the direction that the displayed arrow points and
then press RETURN (or down arrow) to select it.

For stable balancing, loops should not have opposing directional devices
within them.  For example, while tracing around a loop, a check valve
allows flow in the forward direction while a pump in the same line allows
flow in the reverse direction.  Due to the flow adjustment procedure in
HYDRONET, this will severely handicap convergence during the balancing of
the system.  HYDRONET will print a warning but still attempt to solve the
problem. If the two devices flow in the same direction around the loop,
there should be no problem and the system will balance faster.   Most often
the problem will show up as a large head check error.  Each directional
device should be alone in it's own loop if possible.

If problems arise with check valve modeling, note those check valves in which
the flow is zero and remove that part of the loop that has no flow.  This is,
in essence, a dead end line.  If a check valve is observed to allow flow in
the proper direction, try replacing it with a custom valve with the same
friction coefficient.  The system will balance faster and be more stable.  It
is also important to check the operating flow velocity to ensure the complete
opening of check valves, and therefore, the correct friction factor.


- PRESSURE REDUCING VALVES (PRV)

When modeling PRV's, HYDRONET will not let the specified pressure be
exceeded downstream.  PRVs are modeled by introducing enough head loss
to drive the pressure down to the desired level.  These valves can be
used effectively in branch lines where there are no "fixed head" nodes
to complicate operation.  The data input for PRVs is an optional description,
inside diameter, allowed direction and desired downstream pressure.  The
elevation of the nodes on each side of the PRV should be the same and no
"fixed head" node is allowed on the downstream side since the valve already
attempts to do that.


- PRESSURE SUSTAINING VALVES (PSV)

When a PSV is used, the specified pressure will be maintained if
possible, with a nearly complete shutoff if the pressure cannot be met.  Head
losses are introduced until the upstream pressure is above the specified
level.  This type of valve is sometimes called a back-pressure valve.


- FLOW CONTROL VALVES (FCV)

FCV's are modeled like PRV's by introducing enough head loss to decrease
the flow to the specified level.


- FIXED HEAD LOSS DEVICE (FHL)

The specified head loss for a FHL device will be introduced no matter what
the flow is in the line.  If convergence problems result in a system with
a fixed head loss device, remove it and if the system converges,
try lowering the amount of fixed loss.  The loop must provide enough added
head through pumps or static head to overcome the fixed loss.


PUMPS & FLOW VS. HEAD DEVICE (FVH)

The data needed for the modeling of pumps and FVHs in a hydraulic design
include the flow direction and curve description.  The device description
is optional.  The pump and FVH flow direction is set by pressing the right
or left arrow keys to change the arrow direction displayed in the input
field.  Be sure that the arrow points to the correct downstream node.  Flow
opposite this direction will not be allowed.

To describe the flow vs. head curves for these devices, you will input
three (FVH) or four (pump) equidistant points from the device's curve.
The flow increment sets the distance between each point.  Pump curves are
fit to a cubic equation and FVH curves are fit to a polynomial equation.

For pumps, the four points of head begin with the shutoff head (the head
at which no flow can be push through the pump).  The remaining three
points on the curve are the head values at one, two and three times the
flow increment.  The desired operating point for the pump should be close
to the third point input for the curve.  It is very important that the pump
curve described is always decreasing - that is, the curve declines toward
the x-axis.  If the pump head does not decrease with increased flow, the
design may be unstable and may not converge.  The curve between the pump
shutoff head and the first point will be modeled as a straight line.  This
prevents problems where the curve has a hump or peak in it and the
balancing routine oscillates.

A FVH device creates a head loss, not a gain.  The first point of flow
vs. head will be at zero head and zero flow.  The rest of the points can
vary in increasing head but must be at equal increments of flow.  The
desired operating point for the pump should be close to the
second (middle) point on the curve.  The DEFINE option will display "FVH"
for the element at the top of the screen.  Once a pump or FVH is defined,
you can position the pointer at the device and press F5 to obtain a graphical
plot of the curve.  Pump and FVH results for balanced HYDRONET systems
include operating flow rates and heads.


EDITING...

This is a list of the keystrokes available for use in editing and moving
through the loop and branch data within the DEFINE option.

        Right and Left Arrow keys
        (F2) Edit existing node or element data
        (F3) Delete an element and node
        (Ctrl-F3) Delete sequence (loop or branch)
        (F4) Insert element and node
        (F5) Plot pump (& FVH) curves (when positioned at pump or FVH)
        (F6) Align tablet
        (F6) Print pump or HGL screens when viewing
        (F7) Go to previous sequence (loop or branch)
        (F8) Go to next sequence (loop or branch)
        (F9) Go to (create) specific loop/branch
        (Ctrl-F9) Copy loop/branch
        (F10) Go to element/node
        (Pg-Up) Go to previous screen (page)
        (Pg-Dn) Go to next screen (page)
        (1..9) Enter a previously defined element/node number

Their use and descriptions follow...

      Right and Left Arrow keys

Use these keys to move the position pointer to the previous or next node
or element in the sequence.


      (F2)  Edit

Use the cursor arrow keys (right or left) to move the pointer to an
existing element or node and press the F2 key to edit it's data.  The
input screen will be displayed with the current data.  You are allowed to
edit or re-enter any element or node data by inserting or overtyping the
numeric or text characters.  Pressing RETURN or the arrow down key at the
last data field accepts all changes to the data.  Pressing the escape
(Esc) key while editing retains the data without any changes made.  The
RETURN (Enter) key or arrow down must be pressed at the last data field
for all data entries or changes to be accepted.


      (F3)  Delete node and element

When positioned at an element or node, pressing the F3 key prompts
for deletion of an element/node pair.  If the element and node are not
the ones to be deleted, press the escape (Esc) key.  You confirm the request
by highlighting the word "Yes", then pressing RETURN or pressing the "Y" key,
and the element and node will be removed.  Pressing "N" or escape will
retain the element and node.  If the pair occurs elsewhere in the system,
you will be prompted "Delete this node and element elsewhere in the
system?".  If you answer "Y", all other occurrences of this element/node
pair in system will be deleted.  You must specifically press the "Y" key
to acknowledge this prompt.  A lot of work will have to be undone if you
are wrong.


      (Ctrl-F3) Delete loop or branch

Pressing Ctrl-F3 (while holding down the Ctrl key, pressing the F3 key)
prompts for the deletion of the entire loop or branch.  If you
did not intend to delete the current loop or branch, press the escape (Esc)
key or "N" and move to the correct sequence using the F7, F8 or F9
keys.  If the sequence is to be deleted, confirm the request by
highlighting the word "Yes", then pressing RETURN or "Y" and the loop (or
branch) will be removed.


      (F4)  Insert node and element

When positioned at an element or node, pressing the F4 key allows
you to insert an element/node pair just before the current position.  You
must confirm the request and select the type of element to insert along
with a node.  You will then be asked as to if you want the same
element/node pair to be inserted elsewhere in the system between the same
node and element.  You must specifically press the "Y" key to acknowledge
this prompt.


      (F5)  Plot pump (& FVH) curves

When positioned at a pump or Flow vs. Head (FVH) device, pressing the F5
key plots the curve on the screen.  If the system is balanced, the operating
point position and values are displayed.  Pressing F6 when any graphic
screen is displayed, sends the plot to the graphics printer type specified
when installing HYDRONET.


      (F6)  Align tablet

If you are using a graphics tablet, you can reset the coordinate system
that your graphics tablet uses by pressing F6.  This is useful when using
drawings that are larger than your graphics tablet.  To enter node positions
from parts of a drawing not within the bounds of the tablet, simply move the
desired portion of the drawing within bounds and press F6.  You then enter
and click on two diagonal points from the new part of the drawing.  All the
points within bounds of the tablet will now be available for entry.


      (F7)  Go to previous sequence (loop or branch)
      (F8)  Go to next sequence

Pressing F7 places the position pointer to the first node of the previous
(lower numbered) sequence.  Pressing F8 will place the position pointer at
the first node of the next (higher numbered) loop or branch.


      (F9)  Go to (or create) loop/branch

Press F9 and you will be prompted for either "Loop" or "Branch".  Once you
select the type of sequence, you will be prompted for it's number.  If you
enter the number of a loop or branch that exists, the pointer will be placed
at the first node of that sequence.  If you enter a number that is not
currently used for a loop or branch, you will be prompted for the creation
of that loop or branch.


      (Ctrl-F9)  Copy loop/branch

When positioned at the last (or only) node in a sequence and press Ctrl-F9,
you can copy any other loop or branch to the current sequence starting at
the last node.  The last node that the pointer was positioned on will be
overwritten.  The copy function is useful when having to input a new loop that
has already been partially input in another loop.  You can use the F3 key to
delete nodes and elements that are not needed.


      (F10)  Go to element/node

Pressing F10 prompts...         Go to...
                                            Node   Element

Press RETURN if you wish to go to a node or press "E", space bar
or right arrow and then RETURN to go to an element.  You will then be
prompted for a node or element number.  When the number is entered, the
position pointer is placed at the occurrence of that element or node.  When
the position pointer is not moved, the F10 key is pressed again and the
same element or node number is entered, the position pointer will be placed
at the next occurrence of that element or node in the system.  This way you
can locate all occurrences of a particular element or node.


      (Pg-Up)  Go to prev page (screen)
      (Pg-Dn)  Go to next page (screen)

These keys allow fast movement within the screens (pages) of each loop or
branch.  The current loop or branch number out of the total number of loops
or branches and the current screen number out of the total available for
the current sequence is displayed on the lower left of the DEFINE screens.


      (1..9)  Enter a previously defined element/node number

When entering loop data that has been entered previously, you can simply
enter node or element numbers at the element menu instead of having to
enter the type and then number of the element.  You have less data input and
you don't have to remember if an element is a fitting or valve etc.


REPORT

The REPORT option offers reports of element and node data, loop and
branch information, summaries of flows, head losses, pressures,
material lists, text printer configurations, hydraulic grade line plots,
pump curve graphics and 2-D and 3-D system graphics.  You will be prompted
as to whether text reports are to be sent to the SCREEN, a FILE or your
PRINTER.  Reports sent to a file can later be edited using standard word
processors.  Text reports sent to your printer will be sent through the text
printer port specified in the HNINSTAL program.  Printer reports first
request you to set the TOP-OF-FORM.  For a continuous form type printer
(dot-matrix), this can be done by setting the first line of the printer
paper at the printhead and turning the printer off and then on again.

PCX OUTPUT OF GRAPHICS SCREENS

PCX files are graphics files in a format created by Z-SOFT (Phone:
(404)428-0008).  Their PC Paintbrush program and other paint programs
can edit these .PCX graphics files.  You can add additional text,
change colors and basically perform any alteration desired.  In addition,
these programs support many more printers than HYDRONET does.  HYDRONET
supports PCX file output of graphics screen when using standard EGA,
VGA, Hercules and HYDRONET supported SuperVGA displays.  You will be ask
for a filename to send the screen to.  A .PCX extension will be added to
the 8 character filename automatically.

SUMMARY REPORT

The first screen of the REPORT - SUMMARY option lists the pipe head loss
equation used along with the flow tolerance and fluid properties on the top
of the first screen.  The bottom of the screen displays a summary of node,
element, loop and branch totals.  The following screens list pipe, fitting,
valve, pump and node data by group and are sorted by element or node number.


The basic data that was input in the DEFINE option is listed if the
current system is not balanced.  The letter "B" is placed behind the pipe,
fitting or valve numbers if the element is in a branch line.  The node
demands and heads that had a "?" entered in their fields will display
"tbs" meaning "to be solved".  If the system is balanced, then the element
data will display the flows, velocities and head losses.  Node data that
was "tbs" will now be highlighted to differentiate results from initially
fixed data.  For printed reports, "fixed head" nodes will be identified
with "fh" on the same report line.  If the flow for a directional device
(pump, check valve, PRV, PSV or FCV) is zero because of attempted back-flow,
the "Head Loss" column will display the head difference across the element
that is preventing flow.


DETAIL

The REPORT - DETAIL option provides integrated element data listed by
element and node number.  The "ALL" sub-option displays all pipe, valve,
fitting and pump data together with their optional descriptions if
desired.  The node data portion of this report is the same as in the end of
the REPORT - SUMMARY option.  If the current system is balanced, the
velocities, flows and head losses will be displayed.  You may also
obtain reports for fittings and valves, pipes, nodes, pumps and optional
descriptions separately.

The REPORT - DETAIL - PUMPS option will list pump data along with suction
node numbers and their head levels if the system is balanced.  For a quick
estimate of the Net Positive Suction Head Available (NPSHA), add the
atmospheric head (approx 33 feet or 10 meters) if using gage pressures and
subtract the vapor pressure of the liquid. (See Cameron Pages 1-10 to 1-17.)


CRITICAL

The REPORT - CRITICAL option provides a list of the 5 highest and 5
lowest pressure nodes in the current balanced system.


LOOPS

The REPORT - LOOPS option lists all loops and branches in the current system
using a  node - element - node - element - node - element - node  format.



MATERIAL

This report provides a list of the total numbers of fittings and valves
of like type and the total lengths of pipe of same diameters.


CONFIG

You may want to customize your text printer to provide more than standard
output.  Setting these parameters is optional.  You can set the
number of lines per printed text report page (the default is 60).  HYDRONET
will send TOP-OF-FORM codes when the number of lines is reached.  This
provides a skip over perforations for continuous forms or a bottom margin
for sheets.

You may also specify whether the optional element and node descriptions
are to be printed along with the standard data in the SUMMARY and DETAIL
reports.  A report of all descriptions that have been entered is available
by the  REPORT - DETAIL - DESCRIPTIONS  option.

A command string can be entered to setup your printer for any text
mode report with the INITIALIZE option.  For instance, if you want to use
the smaller internal line printer font at 8 lines per inch for the HP
Laserjet, you can enter Esc ( s 16.66 H Esc & l 8 D  and then press return
to terminate input (Esc will be displayed as "   ").  Check your printer's
user manual for control codes that may suit your needs.

You also have the option of sending your printer a command string to leave
it in a specific state at the end of reports with the RESET option.  The
standard reset command is Esc E  displayed as "    E ".

If you wish to use these parameters to set-up your text printer and
reports every time you start HYDRONET, select SAVE and the parameters
will be placed in the same default parameter start-up file as the values
set in SETUP.


GRAPHICS

Under the GRAPHICS option, you can display 2 and 3 dimensional,
hydraulic grade line and pump curve graphics.  These sub-options are
described in the following sections.


-  HGL

The REPORT - HGL option provides graphics of hydraulic grade and
elevation lines for each sequence.  Use the UP-ARROW or DOWN-ARROW keys
to display the available loops or branches or just enter the desired
sequence number.  The Y-axis is the head and elevation in feet (or
meters).  The X-axis is the distance along the loop or branch.  Thus
non-length elements such as fittings, valves and pumps are displayed as a
vertical line that represents their head losses or gains.  Major pipe
and node numbers are displayed just above the X-axis.  Potential
problems occur if the HGL drops below the elevation line (negative gage
pressures) or is far above the elevation line (high pressures).  Pressing
F6 when the HGL plot is displayed, sends the graphics plot to the graphics
printer type specified when HNINSTAL was run.


-  PUMPS

You can enter a pump or flow vs. head device (FVH) number and obtain a
display of it's curve using this option.  These are the same graphs that
are displayed in the DEFINE option using the F5 key when positioned at a
pump (or FVH).  Use the UP-ARROW and DOWN-ARROW keys to display available
pump (or FVH) numbers.


-  2-D PLAN VIEW

If you have provided x-y coordinates for the nodes in a system, you can
view it's overhead 2-D system plot.  When you first enter this option,
HYDRONET plots the system in it's entirety.  All node numbers, element
numbers and the grid system are displayed.

The various options for 2-D views are described below...

   F2 - Element #s

Element (pipe, pump, fitting and valve) numbers are toggled on and off with
this option.  For very large systems, the amount of information on screen
can be very confusing and removing element numbers from view can help.


   F3 - Node #'s & flows

Node number displays are toggled on and off with this option.


   F4 - Loop #'s

Loop numbers are toggled on and off with this option.  Only closed regular
loop numbers are plotted and the number will be plotted in the center of
the loop.


   F5 - Grids

The X-Y grid system is toggled off and on with this option.


   F6 - Print

The displayed screen will be sent to the graphics printer port you specified
when you ran the HNINSTAL program.  The graphics dump to your printer takes
some time.  To interrupt the graphics screen dump, press the escape (Esc) key.


   F7 - PCX output

The displayed screen will be output to a .PCX file with this option.  This
feature is only available for standard EGA, VGA, Hercules and supported
SuperVGA displays.  You must enter a name for the file and it will
automatically be appended with the .PCX extension.  You can then use any
PCX capable paint program to view, modify and print the graphics screen.


   F8 - Zoom

Use this option to take a closer look at a smaller piece of a system.  You
are asked to position the top left corner of the ZOOM box (using arrow keys
on keyboard) and then press RETURN to anchor it.  You then move the lower
right corner of the ZOOM box and anchor it by pressing RETURN.  If you wish
to move the top left corner again, press the escape (Esc) key.  Once both
corners are anchored, the part of the system you have selected is
displayed.  You can use ZOOM on this new section to look at an even smaller
part of the system.  To display the system in full again, use the reset (F9)
key.  To view this smaller section in 3 dimensions, use the "Go To 3-D"
(Ctrl-F8) key.



   Ctrl-F8 - Go To 3-D

Use this key to view what is currently displayed in a 3-D
format.  The options for 3-D usage are detailed in the 3-D section that
follows.  When you exit 3-D viewing by pressing the Esc (escape) key,
you return to the 2-D option.


   F9 - Reset

If you have used ZOOM to view a smaller portion of the current system, you
can reset the view to the original full system display with this option.


   F10 - 1:1 ASPECT

When HYDRONET displays a system or portion of a system, it plots the
view using the fully available dimensions.  A problem then occurs where,
for example, 1 inch (or 1 cm.) of the x-axis does not equal the same
distance as 1 inch (or 1 cm.) of the y-axis.  Pressing F10 brings the
display into a 1 to 1 aspect ratio without removing any of the desired
plot.  Pressing the F9 (reset) key displays the plot within the full
dimensions of your monitor again.


   Esc - Exit

To return to the REPORT main menu press the escape (Esc) key.




-  3-D VIEW

Viewing a system in 3-D gives the hydraulic system designer a better
understanding of system operation, elevations and pressures.  You can
immediately observe regions of high or low pressures and other possible
problems.  You can obtain a straight-on view of the entire system for a
hydraulic grade line graphic representation.

When entering this option directly from the REPORT option, the
current system is displayed in it's entirety.  All nodes and elements are
displayed.  Use the 2-D option to ZOOM in on a specific section and then
use the Ctrl-F8 (Go to 3-D) option to view the section in 3-D.

The F2, F3, F6, F7 and Esc keys operate the same as with the 2-D option
described previously.  The following keystrokes have different functions...

   F4 - Plot Hydraulic Grade Lines

If the current system is balanced, this option toggles the hydraulic
grade line graphics off and on.


   F5 - Pressure heads

If the current system is balanced, this option toggles on and off the
pressure head lines (vertical lines between elevation and HGLs).


   ARROW KEYS

You can change the aspect (angle) from which you view the 3-D system by
pressing the up, down, right and left arrow keys.  To make large viewing
angle changes, enter a number from the keyboard, then press the arrow key
to move that number of pixels in a particular direction (ie. to move up
50 dots of resolution, enter "50" then press the up arrow key).


   PLUS (+) and MINUS (-) KEYS

The plus and minus keys expand and shrink the z axis (elevation, pressure
head and HGL scales).  This option provides a less cluttered view.



UTILITIES

DIAMETER

The DIAMETER option allows the alteration of ALL pipe, fitting and valve
inside diameters to a specified value.  If the fitting and valves were
chosen from the HYDRONET menus (not custom coefficients) then the appropriate
friction coefficients will be determined using the new inside diameter.


TITLE

You can enter a description of the current system.  This title is displayed
on the upper right of the working text screen and is saved in the system's
datafile.


NODES

The FRICTION option allows you to multiply all non-zero node demands by a
specified factor.  This allows you to investigate different operational
strategies such as what happens when peak demands double. 


FRICTION

This option allows the alteration of ALL of the current system's
Hazen-William pipe roughness coefficients or Darcy-Wiesbach specific
roughnesses.


ERASE

The ERASE option clears HYDRONET memory of the current system's
data.  Datafiles on disk are untouched.  This option allows you to completely
start a new design without exiting HYDRONET.  Be sure to save any desired
changes to disk (using FILE - SAVE) before using the ERASE option.  Any
default values established in SETUP and REPORT - CONFIG will be reset.


FIXED HEAD

The FIXED HEAD option allows the setting of one "fixed flow" node's
pressure head for recirculating (no external inflows/outflows) systems.  There
cannot be any "fixed head" nodes used in the layout of a "closed loop system"
(recirculating) and the demands at all "fixed flow" nodes should be zero.  To
remove the single fixed head node, and it's pressure head, set the node number
to zero.


ANALYZE


The ANALYZE option provides a way to find potential problems in a
hydraulic design and also provides the steady-state solution to a
design using the BALANCE sub-option.

The ANALYZE sub-option analyzes the current system for data
inconsistencies.  If HYDRONET is unable to plot a graph, balance a system
or outputs strange results, ANALYZE will attempt to find the problem.  The
warnings that this option provides are strictly informational.  ANALYZE
should be run prior to balancing a system so that processing time is not
wasted.  Both a balanced and unbalanced system can be analyzed.  Use ANALYZE
after balancing a system that appears to have had a problem to obtain more
information.

The BALANCE sub-option solves the system for steady-state flows and
pressures.  The system data is first initialized, then briefly interrogated
for completeness, initial system flows are estimated and the iterative
process of adjusting system flows begins.  Press escape to interrupt the
process if the total adjustments to flows does not tend to converge toward
zero or if the set flow tolerance might be too small to allow a solution
within a reasonable amount of time.

If the iterations are taking a long time and you do not want to wait for
the tolerance to be reached, you can press F2 to end the iterations and
solve for final head values.  There may be some large errors in the final
head check though, because the flow adjustments weren't performed all
the way to the set tolerance.  NOTE: Be sure to note any error or warning
messages that are displayed on the screen after the system is balanced. 
There may be some important warnings about your results.

Various statistics are displayed in the balance box.  The first line
shows the iteration number and control valve iteration number.  Because
some control valves induce head losses (ie., PRVs), the whole system
must be balanced and then head losses adjusted for proper valve operation
and the system balanced again.  The control valve iteration number
displays how many times valves were adjusted.


The second line displays the total of flow adjustments for each iteration.
This is the total flow adjustment to all elements.  This number should get
smaller on each iteration.

The third line displays the percent of convergence.  This number is the
percentage of the time the flow adjustments converge (get smaller).  This
number gets close to 100% for a solidly converging system.  If the percent
convergence is in the 80 to 100% range but flow adjustments still reach the
set flow tolerance, everything is probably fine.

The fourth line shows the maximum head error detected when the system heads
were calculated.  This number is obtained by calculating each element's
head loss (using the flow that was determined for it during the balancing
routine) and comparing that to the head value at the downstream node.  This
number should be very small for a properly balanced system.  The value of
maximum head error will flash if the error is greater than 1% of the largest
element's head loss.  If more accuracy is desired and the system seems to
converge well, you can lower the flow tolerance in the SETUP option.  It is
up to you, the engineer, to decide what is an acceptable head error.  If you
have pipes in a system with 100 foot head losses, a maximum head error of
.5 foot may be acceptable.  However, if you have a maximum pipe head loss
of 3.0 feet, an error of only .01 foot may be acceptable.

At the end of the fourth line of the balance box, is the total elapsed time
for the balance.  This is available so that differing system configurations
can be compared for speed of convergence.

If AUTO PIPE LENGTHS data field is set to " YES " in SETUP, then when
ANALYZE or BALANCE is selected, all pipe lengths will be recalculated if
node coordinates are being used.


QUIT

This option is used to exit HYDRONET and return to DOS.  Be sure to save
any desired changes since the last file update using the FILE - SAVE
option.  Pressing "N" or the escape (Esc) key returns you to HYDRONET's main
menu.  You must press "Y" to leave HYDRONET.



USING THE EQUIVALENT LENGTH METHOD


When modeling fluid transport systems that convey fluids other than
water, you can have HYDRONET use the equivalent length method for fitting
and valve head losses.  This method essentially models fitting and valve
friction in terms of the equivalent friction of turbulent flow through
lengths of standard steel schedule 40 pipe having a specific roughness
of .00015 feet (.0457 mm).


To use this technique, enter the SETUP option and specify the
Darcy-Wiesbach equation for use.  A field will appear to specify that
HYDRONET use the equivalent length method (USE EQUIV LENGTHS?) on the
current system.  Set this parameter to "YES" by pressing the right or left
arrow keys.  Now when you specify a certain fitting or valve type and input
an inside diameter, HYDRONET will calculate a length of steel pipe that
will approximate the same resistance.  The calculation is based on the "K"
coefficient for water flow for the valve, the diameter of the valve and
the friction factor for complete turbulent flow in steel pipe for this
diameter.  The K value is multiplied by the diameter and divided by the
friction factor to obtain the equivalent length. (See Cameron page 3-119.)


All "K" values that appear in HYDRONET when the equivalent length
method is specified must be for use with water.  These "K" values
are used in the calculation of equivalent lengths.  If you have "K"
values for fittings and valves for use with fluids other than water,
do not specify the use of the equivalent length method.  Do a manual
equivalent length modeling of fittings and valves that you do not have
non-water "K" values for.  These non-water fittings and valves should be
modeled as steel pipes with the specific roughnesses listed above.  To
compute the equivalent length of pipe, see Cameron pages 3-119 to 3-122.



DESIGN METHODS

1.  Using a plot plan of your system, label all nodes with numbers
and note those with "fixed heads" (sources and discharges with known or
desired pressure heads).  Nodes are placed before, after and between
elements (pipe, fittings, valves, fittings & pumps).

2.  Label all elements with numbers.  Use a numbering scheme that will make
it easy to determine where certain elements and nodes are in the system.  For
example, all nodes and elements that start with 100 (ie, 101,102,etc.) will
be in the first main line. (See example problem 6.)  Obtain pump curve data,
pipe roughnesses, valve types and other needed information.

3.  Create loops making sure all "fixed head" nodes are connected
to at least one other "fixed head" node (w/dashed lines) forming
pseudo-loops.  Try to have loops adjacent to the next and previous numbered
loops (ie, loop 2 adjacent to loop 1 and 3).  Number all loops.  Identify
fixed outflow branch lines that are not to be a part of the loop system.

4.  Start HYDRONET and enter the SETUP option and set the head loss
equation, units, fluid parameters and flow tolerance.  If these conditions
are going to be used for most designs, you may wish to place them in the
default parameter file for automatic start-up.

5.  Use the DEFINE option to start entering system data.  If a portion of
the system can be designed to operate on it's own, starting small will give
you a better feel for HYDRONET's operation.  Start off by entering the system
data without any control valves.  Only after having solved the system without
control valves, use the valves to control pressures and/or flows.  Enter any
branches using the DEFINE - BRANCHES option.

6.  Run the ANALYZE option to identify any incomplete or inaccurate
data that might cause problems.

7.  When data has been newly entered and after running the
BALANCE routine regularly, use the  FILE - SAVE option to save your work.

8.  Run BALANCE to obtain a solution for the system.  Be sure the percent
convergence is high and that the maximum head error is acceptably low.

9.  Use the REPORT - CRITICAL option to obtain a summary of highest
and lowest pressure nodes and possible pump problems and observe the
hydraulic grade line, 2-D and 3-D graphs.  Use the REPORT - DETAIL option to 
observe velocities in pipes and excessive head losses.  Go back to step 5
and using F9 and F10, edit node and element data accordingly.



DESIGN TIPS - TROUBLESHOOTING


- When a pump is restricted to a specific location and the
suction head is low, the diameters of the suction side lines can be increased
to minimize intake losses or a booster pump may be needed somewhere up-stream.

- When a pump is not restricted to a specific location, the insert element
function (F4) and the delete element function (F3) can be used to move the
pump to various positions in the line and provide an adequate NPSHA.  Use the
F9 key to locate pumps by element number.

- When inserting elements and nodes that will be present in two adjacent
loops in an existing design, use the F9 and F10 keys to locate all occurrences
of adjacent elements and nodes.

- Use more pseudo-loops in small systems that contain many pumps and check
valves if convergence is a problem.

- If two or more pumps are in the same loop (especially if adjacent) they
should also appear in other loops in the system (use pseudo-loops if possible)
for stability of convergence.

- If a design is not converging, and there are pumps in the system,
enter the DEFINE option and use the F9 key to locate all the pumps.  Press
F5 when positioned at a pump to make sure curves are always decreasing
(ie, drops toward the x-axis).

- If a design is not converging and has a fixed head loss (FHL) device,
try removing the device and then if it converges, reduce the original amount
of fixed head loss.  The loop must provide enough head (through pumps or
static heads) to overcome the fixed head loss.

- Try not to have to directional devices oppose each other in the same
loop.  For example, while tracing a loop, a check valve allows flow in the
forward direction and two elements away a pump allows flow only in the
backward direction.  This will not allow for the flow in the loop to be
adjusted easily.



EXAMPLE PROBLEMS

The datafiles for these example problems are included on the HYDRONET
diskettes and were loaded into the main HYDRONET directory
created by HNINSTAL.  To review them, use the  FILE - RETRIEVE  option
to retrieve the data, then the  DEFINE  and  REPORT option to edit and
display their data.


PROBLEM  1

This simple example introduces the use of pseudo-loops with "fixed head"
nodes in a gravity flow (no pump) problem, using the Hazen-Williams equation
in English units.

The gravity flow system depicted in the following 2-D plot is to be solved
for steady-state flows and pressures.  We identify the needed loops for the
system by first finding all points of unknown inflow and outflow.  The
system contains three of these which are "fixed head" nodes 1, 11 and 15 at
reservoir inlets and exits.  All other nodes are of the "fixed flow" type
(flow is fixed at zero, head is to be determined).  This system requires at
least two pseudo-loops to include the three "fixed head" nodes and all
elements in the analysis.  Every "fixed head" node must be connected to at
least one pseudo-loop and it does not matter whether the loop goes from
node 1 to 15 and 1 to 11 or if they connect 1 to 15 and 11 to 15.  Three
pseudo-loops could have been used but that many are not required.  If
convergence problems were to occur, a third pseudo-loop could be tried for
added stability.  There are no elements left out of these two loops so there
is no need for any internal closed loops.  The elements (pipes, fittings and
valves) are numbered sequentially starting at 1 and ending at 14.  Nodes are
also numbered sequentially starting at 1 and ending at 15.

This system contains no branches.  Any one (but only one) of the three
lines could be modeled as a branch with one pseudo-loop.  The two "fixed
head" nodes would drive the flow in the system and the branch would have
simple head loss calculations made on it.  The flow in the branch would be
fixed and you would have to ensure that the head at the end of the line
would be met.

After starting up HYDRONET, enter the SETUP option and select the
Hazen-Williams equation for use in calculating pipe head losses.  Specify
English units of gpm for flow and psi for pressure for use in this
design.  Set the flow tolerance to .01 gpm.  We will be using cast-iron
pipe so we'll set the default Hazen-Williams Friction Factor C to 100.  When
inputing numbers, you can simply press the space bar once after entering
the number on the left of the field and the text to the right will be
ignored.  If we were going to be using these conditions for most all of our
designs, we could update the default parameter file with these
settings.  HYDRONET will then be automatically setup to use these values
and settings at start-up.

To enter element and node data, enter the DEFINE option and select
"LOOPS".  A prompt for a loop number appears and we'll keep things simple
and enter "1".  A prompt appears and the number of "1" is displayed as
the next available node number.  We'll start at the top of this design and
type "15" over the default and press RETURN.  If we had input a unintended
node number, we could simply press the escape (Esc) key and input the node
number again.

The node data fields appear in a window for input.  We have the option of
entering a description for the node.  The use of the optional
description for nodes and elements quickly uses up memory available for
other data items.  Next, we enter the elevation of the reservoir and
press RETURN.  Since this is a "fixed head" node where the outflow or
inflow of the reservoir is to be determined we enter "?" (question mark)
for the demand and press RETURN.  This tells HYDRONET to solve for the
flow.  There is no pressure component at this node (open surface reservoir)
so we enter zero for the head and press RETURN again.  We also have the option
of entering X-Y coordinates for the node.  These coordinates are not needed to
obtain a balanced solution.  They make automatic pipe length calculations and
the viewing the system in 2-D and 3-D available.

The element menu appears and we press the down arrow key once so "Fitt"
is highlighted and press RETURN.  We are prompted for an element number
and type "14" over the default value and press RETURN.  The fitting
menu appears and we use the arrow keys to highlight "Inlet" and press
RETURN.  A sub menu appears and again we use the arrow keys to highlight
"flush - sharp-edged" and press RETURN.  Again, a field for optional
description appears and we press RETURN to skip over it.  We enter "4.03" for
the inside diameter of our 4 inch pipe.  This establishes the default
diameter for the system and from now on "4.03" will appear in all
diameter fields until a different diameter is entered.

The node number field appears again and we enter "14" and press RETURN. 
We skip the description field and the elevation field has the value that was
used on the other side of the fitting.  This is not correct in this instance
because that value is the elevation of the water surface, so we enter the
actual elevation of the discharge side of the fitting.  This is a "fixed
flow" node where we want the head to be determined.  There is no demand flow
out of this node so we enter 0.0 or press space bar repeatedly and press
RETURN.  The head at this node is "to be solved"  so we enter "?" in the
head field and press RETURN.

The element menu then appears and we press the arrow down key until
 "Valve" is highlighted and press RETURN.  The prompt for element number
appears and we type "13" over the default value presented.  "Gate Valve" is
highlighted and we simply press RETURN to specify that type.  The valve
data fields appear and we press RETURN twice to skip the description and
accept the default diameter.

At the node number field we enter "13", enter it's ground elevation and,
since there is no demand flow, enter 0.0 then a "?" in it's head field.

The element menu reappears and we press the arrow down key until "Pipe" is
highlighted and press RETURN.  Enter "12" over the default pipe number.  We
press RETURN twice to skip the description and accept the default
diameter.  The length will be left at zero since we are inputing node
coordinates and want HYDRONET to determine the length of pipe.

We continue to enter element and node data in sequence.  Element #5 and #6
are the friction components of a Tee fitting.  Both represent the
branch component of a Tee fittings friction loss.  The current pseudo-loop
data input ends with node 1 where the elevation is entered, a "?"
for demand and zero is entered for it's pressure head.

Press F9 to start the input of the next pseudo-loop #2.  Since this
loop has some common elements and nodes with loop #1, we can enter a single
node for loop #2 of any number and press RETURN to accept all defaults.  We
reposition the pointer back to that node and press "Copy Loop" (Ctrl-F9)
key.  We can now specify loop #1 and HYDRONET will copy it to this
loop.  The single node that we entered will be overwritten.  We can now
delete element and node pairs that are not common between the two loops.  The
remaining needed elements and nodes can now be inserted by using the F4
(insert) function at the beginning of the loop.

Occasionally and especially when all your data is entered,  you should save
your work by entering the FILE option, selecting the SAVE sub-option, specify
a filename and then press RETURN.  The ANALYZE option should be used to
examine the data for completeness and if no errors are found, the system
can be solved by using the BALANCE sub-option under the ANALYZE main option.

The REPORT - SUMMARY report displays the flows through each pipe, fitting and
valve along with the direction, velocity and head loss.  Node data displays
the demand (if negative out of the system, if positive into the system). 
Pressures and hydraulic grade lines in feet are displayed with the
fixed heads identified.  The REPORT - DETAIL option report
lists all elements by type and presents the same data fields as the SUMMARY
report.




PROBLEM  2

This example problem demonstrates the use of the Darcy-Wiesbach equation to
calculate pipe head losses, the use of branch lines, a supply from a "fixed
head" force main and discharge to the atmosphere.

Node 1 is a force main supplying 60 degree F. water at a pressure of 100
psi.  A requirement of at least 1000 gpm at 40 psi is needed at node 14.  The
branch line is to deliver 300 gpm to node 16 and 200 gpm to node 19.  Two
booster pumps are to be used to deliver this flow.  At least one pseudo-loop
is required for this open (external sources and discharges) system. We can
then model the other line as a branch of fixed flow.

Using the SETUP option, we specify the Darcy-Wiesbach equation for
calculating pipe head losses.  We then setup the desired units system and
units of flow and pressure.  The value of .00015 feet is entered for the
default specific roughness.  The kinematic viscosity is set to .00001216
ft2/sec.  Since the fluid is water at 60 degrees F, we can use the standard
fitting and valve coefficients that are automatically input from the
menus.  If this were a fluid with a different viscosity, we would use the
equivalent length method for the modeling of fitting and valve losses.

The force main at node 1 provides water at an elevation of 210.55 feet
and a pressure of 100 psi.  A "?" is entered in the demand field and the
pressure is entered for the node's head.  At node 14, an elevation of 561.83
is entered, a "?" is entered in the demand field and a pressure of 40 psi
is entered for the head.  All other nodes in the system will have
a "?" entered in the head field and of those, only nodes 16 and 19 will
have non-zero flow demands.  The system's pipe, fitting and valve diameters
will be adjusted along with booster pump curves to provide the desired
flows and pressures.

The design arrived at in the following pages is just one possible solution
to this problem.  Trade offs of pipe and pump sizes and operating energy costs
exist and in general a least cost approach would be used.  Pumps should be
placed so that possible cavitation situations are avoided.  The 3-D graph of
the system shows that all line gage pressures are positive.



PROBLEM  3

This problem demonstrates connecting two small sub-networks with a single
line, using the Hazen-Williams equation and branch lines.  The minor friction
losses from fittings and valves will be neglected in this preliminary design.

A single reservoir supplies water to two small networks.  The first network
(outlined by pipes #2, 3, 4, 13, 12, 11, 10 and 9) is on a plateau of
approximate elevation 240'.  Pump 16 provides additional pressure to the
second pressure zone (pipes #18, 19, 20 and 21) on a plateau of approximately
350'.  The design objective will be to provide flow at all
points of demand of .5 cfs at a head above 40 psi.  A pseudo-loop is used so
that each network is not considered isolated.  Nodes #17 and #1 will have
undetermined flows and the system will have to be adjusted (pipe diameters
and pump curve) so that the flow at node 1 will be close to .5 cfs.  The two
networks are connected by a single pipe and pump line.

The information for the "fixed head" node at the supply reservoir
(node #17) will be a water surface elevation of 524.33', a "?" for demand
and zero for the pressure head.  The information for node 1 will be the
ground elevation, a "?" for demand and a value of 50 psi for head.  The
demands at the various other nodes will be entered as negative values (out
of nodes) so that the node reports will display flow into (+) and out (-)
of nodes properly.

Minor losses from fittings and valves can be inserted into the system at a
later time once all the system is adjusted to provide close to the pressures
and flows needed.




APPENDIX  A


ERROR MESSAGES


TABLET USE

" Possible tablet or port problem! "

Problem:    HYDRONET tried to poll the graphics tablet through the port
            specified when you ran HNINSTAL but did not receive a response.

Remedy:     Be sure the port is setup with DOS's MODE command (See Operation
            section earlier).  Also enter the SETUP option and verify that
            the graphics tablet is setup as desired.



" Points must be diagonal! "

Problem:    HYDRONET must perform a mathematical translation from the tablet
            coordinates to your drawing coordinates.

Remedy:     The two alignment points from your drawing must be on opposite
            corners of the pad (ie, x1 cannot equal x2, and y1 cannot equal
            y2).  Use the F6 key while in DEFINE to realign your drawing.



PUMP OPERATION

" Pump # flow is larger than last point of curve! "
" Pump # flow = # (off of curve)! "

Problem:    During the balancing routine, the pump in question has a flow
            that is more than 3 times the flow increment for the pump.

Remedy:     This can signify a potential problem if the system is not
            converging.  If the message disappears when the system is finally
            balanced most likely no problem exists.  If it doesn't, make sure
            your pump curves decrease in head for increasing flow (drop
            toward the flow axis).  Use the F10 key in the DEFINE option to
            find the pump and press F5 to plot.  Final pump flow should be
            between the 2nd and 4th point on the curve.


" Warning: Valve # direction opposes a pump or valve in same loop! "
" Warning: Pump # direction opposes a pump or valve in same loop! "

Problem:    HYDRONET detects two directional devices (pumps and/or valves)
            whose specified flow directions oppose each other.

Remedy:     This is just a warning.  Having two directional devices in the
            same loop that allow flow only in opposite directions penalizes
            the balancing routine.  If the system fails to converge, enter
            the DEFINE - LOOPS option and use the F9 key to locate the pump
            and/or valves in question.  Attempt to place these directional
            devices in separate loops.



" Cannot plot pump curve! "
" Cannot obtain curve for pump #! "
" Error fitting pump curve! "

Problem:    The data for the pump cannot be fit to a cubic equation so that
            HYDRONET can have a continuous function of head vs. flow to work
            with.

Remedy:     Enter the DEFINE - LOOPS option and use the F9 key to find the
            specified pump.  Edit the data so that if F5 is pressed when
            positioned at the pump, it can be plotted.  Pump curves can be
            plotted from the REPORT - GRAPHICS - PUMPS option.




" No flows, be sure total pump shutoff head is at least #"
" No flows... no head difference driving system! "
" No flows, check pumps, valves or lower tolerance...  "

Problem:    This error can occur because...
          - the flow direction of pumps and/or directional valves oppose
            each other.
          - weak pumps in a system are not able to overcome the static head.
          - there is no static head driving the flow in a non-pump system.

Remedy:     Check pump and valve directions.  Check pump shutoff heads to be
            sure they are large enough to push flow against the static head
            opposing them and be sure that a static head is present in
            non-pump systems.



" Pump # curve is not always decreasing. "
" 2nd pt should be less than shutoff! "

Problem:    Pump curves should always decrease. The shutoff head should be the
            highest head value, the next point on the curve should be the next
            highest and so on.


" Pump # flow is less than 2nd pt on curve, straight line approx used."

Problem:    The flow determined for the pump was less than the flow increment
            for the curve.
                    
Remedy:     If the flow is lower than the 2nd point on a pump's curve, the
            head addition is calculated using a straight line approximation
            between the shutoff head and the 2nd point.  For HYDRONET
            to properly model pumps, the optimal operating point for the
            curve should be placed around the 3rd point of the curve.



FILE INPUT/OUTPUT ERRORS

" Error opening file HN.CNF!  Rerun HNINSTAL... "
" Cannot find HN.CNF!   Run HNINSTAL or enter
       directory path where HYDRONET system files are (Q=quit): "

Problem:    HYDRONET can not find the file that contains information on your
            hardware configuration (HN.CNF).

Remedy:     If you are running HYDRONET from another directory, be sure the
            HYDRONET directory is listed in your path (see your DOS manual).
            If you reside in your HYDRONET system directory, run HNINSTAL,
            and make sure the HN.CNF file is present in the directory.



" HN.HLP not found! (gone or bad path) "

Problem:    HYDRONET can not find the file that contains help information that
            is available when F1 is pressed.

Remedy:     There should be a file named HN.HLP in the HYDRONET hard disk
            directory.  Re-run HNINSTAL if there is not!



" Error - not a HYDRONET data file! "

Problem:    You have attempted to retrieve a file that is not a HYDROFLO
            (*.FLO) or HYDRONET (*.NET) datafile.  The file requested
            must have been created by HYDRONET.


" Not HYDROFLO 1.2 or 1.1 data file! "

Problem:    You have attempted to retrieve a file that is not a
            HYDROFLO datafile with a " .FLO " extension.  The
            file requested must have been created by HYDROFLO.



" Coefficient file not found! "
" File  HN.VAL  not found..."

Problem:    HYDRONET cannot find the files (HN.VAL and HN.FIT) that contains
            the preset fitting or valve coefficient data for water systems.

Remedy:     Be sure that all files on the distribution diskette (other than
            ".NET" datafiles) are in the same directory as the HN.EXE file.
            You can execute HYDRONET from any directory but all system files
            must be together.  Re-run HNINSTAL if using a hard disk system.



" No files in data directory! "

Problem:    If you have gotten this message and you know there are data files
            out there somewhere, the default data directory is not specified
            properly or there are no datafiles in your directory.

Remedy:     Enter the SETUP option in HYDRONET and specify the correct default
            data file directory.  If you will be using this same directory
            often, consider updating the default parameter file so that this
            directory is always looked at upon start-up.




BALANCING ERRORS


" Cannot set initial flows. Node # demand cannot be routed to fixed head! "

Problem:    This error message occurs because part of the network is isolated
            (ie, check valve or pump flow directions do not allow flow into
            a portion of the network).

Remedy:     Locate the stated node (use F10 in define) and attempt to trace
            it's flow through the system to a "fixed head" node.  Note pump
            and control valve directions to see if the flow is blocked.



" System not converging! Check data! "

Problem:    Some instability is present not allowing the system to converge.
          
Remedy:     Run ANALYZE.  Check pump curves to see if a pump is too small
            or the pump curves are not decreasing.  Try adding extra
            pseudo-loops to the system if possible.



" Loop # must start/end w/ fixed heads (psloop) or w/ same node (closed)! "

Problem:    A pseudo-loop in the system does not begin and end with "fixed
            head" nodes or a closed loop does not begin and end with the
            same node.

Remedy:     Enter the DEFINE - LOOPS option and use the F7 and F8 keys to move
            to the loop in question.  Check beginning and ending nodes to be
            sure they are "fixed head" nodes if using pseudo-loops.  Be sure
            that closed loops begin and end with the same node.



" ERROR:  Flows from fixed head nodes don't total zero! "
" Sum of flows at node # not equal zero! Check results! "
" In and out demands at nodes do not total zero! "

Remedy:     These errors should not occur in straight forward piping designs.
            These are HYDRONET internal errors.  If you get one of these
            errors, prepare to send us a disk with the datafile on it.



GENERAL ERRORS


" Out of memory for this file! " or
" Out of memory for description! " or
" Out of memory for this file! " or
" Out of memory for pipes, valves, pump or node! "

Problem:    Available RAM memory is used up.

Remedy:     Uninstall any memory resident programs, add memory chips to
            bring total memory up to 640K or clear any unnecessary
            description fields.  HYDRONET limits are 3000 elements
            and 3000 nodes.



" Must get node data! "

Problem:    HYDRONET requires that a node be placed here.

Remedy:     If the node is not needed and to be deleted later, simply
            press RETURN repeatedly to get past this node.

          

" Must have at least one loop! "

Problem:    You cannot delete a loop if it is the only loop in the system.

Remedy:     If you want to clear HYDRONET memory of all current data,
            use the UTILITIES - ERASE option.



" Number used for different element! "

Problem:    You have specified an element number that has been used before
            for another type of element.  HYDRONET makes sure that numbers
            are not duplicated in differing types of elements.  You must
            use different element numbers for each element.



" Must enter a loop first! "

Problem:    You have tried to enter data for branch pipe section when the
            system does not have a loop that the branch can flow from.  Enter
            a loop first.
                    


" Warning, Loop # doesn't have an element in another loop! "

Problem:    HYDRONET has found an isolated loop that does not have any
            elements in common with any other loop.  This may lead to
            unwieldy results.

Remedy:     A pseudo-loop should be created if a closed loop cannot be added
            to link the isolated loop to the rest of the network.



" Element # has different start and end nodes! "

Problem:    While HYDRONET was initializing the system data, it found that a
            certain element had different specified starting and ending nodes.

Remedy:     Enter the DEFINE - LOOPS option and use F9 to locate the
            specified element.  Press F9 and specify the element number again
            to locate all the occurrences of the element and find where the
            mistake lies.  An element can only have one unique beginning
            and ending node.



" Cannot have fixed head after PRV #! "
" Cannot have fixed head before PSV #! "

Remedy:     You cannot have a fixed head node just downstream from a pressure
            reducing valve (PRV).  HYDRONET knows to supply enough head loss
            to drive the pressure down to the specified level.  HYDRONET also
            notes the pressure upstream of a pressure sustaining valve (PSV)
            to try and maintain the desired pressure level.



" No X - Y coordinates defined for system! "

Remedy:     You cannot look at 2-D or 3-D graphics if you haven't input X,Y
            coordinates for nodes.



" Unable to estimate initial flows! "

Problem:    HYDRONET was unable to set up a initial flow grid for the system.

Remedy:     Most likely check valves and/or pumps are isolating a portion of
            the network and HYDRONET cannot trace a set demand to a supply or
            outflow "fixed head" node.  Use the REPORT - SUMMARY option to
            check demands at nodes and locate all check valves and pumps to
            be sure their flow directions are correct.



" System must be balanced! "

Problem:    You cannot observe data on the REPORT - CRITICAL option or look
            at Hydraulic Grade Line plots if the system is not balanced.



" Must use a defined valve or fitting! "
" Must use a previously defined pump! "
" Must use a previously defined pipe! "
" Must use a previously defined node! "

Problem:    You have run out of memory or reached the limits for the number
            of the type of elements or nodes.

Remedy:     HYDRONET has a limitation of 3000 elements (consisting of 3000
            pipes, 1000 fittings and valves and 300 pumps.  If you
            have run out of memory, you can add more memory to reach
            640K or remove some memory resident programs from main
            memory or you can combine some pipes into longer sections
            or delete unnecessary optional descriptions.



" Must enter defined element number! "

Problem:    If inputing element numbers when the element menu is displayed,
            you can only input previously defined elements.  Press escape
            to get back to the element menu and select the type of a new
            element.  Then input it's number if not previously defined.



" Can't have both unknown flow and head! "
" Cannot set both demand and head! "

Problem:    You can only set one parameter, either the pressure head or the
            demand flow at a node.  HYDRONET will solve for the unknown
            parameter. 



" Cannot have fixed heads in branches! "

Problem:    You cannot have "fixed head" nodes in a branch.  Simple head
            loss calculations are performed in branches as the flow is
            fixed.  If you wish to set the head and have the flow
            determined, convert the branch to a pseudo-loop.



" Demand must be out of node (negative)! "

Problem:    All fixed demands at nodes are outflows and are represented by
            negative values.  If you want to fix the head level and determine
            the possible inflow, make that node the beginning or end of a
            pseudo-loop.



" Error in sequence! "

Problem:    When deleting a node/element pair, you are prompted whether you
            want the pair deleted everywhere else in the system where they
            exist.  This message occurs when HYDRONET finds the node/element
            pair elsewhere but the sequence (the adjacent nodes and elements)
            are not consistent.  HYDRONET will not delete the pair where
            that occurs.  Use F10 to locate the remaining occurrences of the
            pair.



" Warning, Branch #, starting node #d isn't in main network! "

Problem:    The starting node in a branch must exist in the main network.
            This is how HYDRONET knows the total head for the simple head
            loss calculations performed on branches.



" Error!  Node # doesn't start or end a pseudo-loop! "

Problem:    All "fixed head" nodes must start or end at least one
            pseudo-loop.



" No fixed head in system, use UTILITIES-FIXED HEAD to set head...  "

Problem:    HYDRONET has balanced the system but has found no fixed head
            to use as a starting point for head.  No HGL's or nodal pressures
            can be calculated.

Remedy:     This is not a problem unless you want hydraulic grade lines
            computed.  Use the UTILITIES-FIXED HEAD option to set one
            node's head and allow nodal pressures to be computed for
            recirculating (no external inflows or outflows) systems.  There
            should be no pressure heads set when inputing node data for
            recirculating systems.



" Pipe # length is zero and one or more coordinates are zero! "

Problem:    If you are inputing coordinates for nodes, do not set any at
            zero.  Use zero to have HYDRONET ignore the coordinate and not
            plot it.  If you've left pipe lengths at zero so that they will
            be calculated, you cannot leave adjacent node's coordinates at
            zero.



" Pipes are not on both sides of enlargement/contraction # ! "

Problem:    Pipes are needed on both sides of an enlargement/contraction
            (reducer) to determine the head loss for the fitting.  Put
            pipes on both sides of this type fitting even though they may
            be short.



" No pipe on either side of nozzle/orifice # ! "

Problem:    At least a short section of pipe is needed on one side of the
            nozzle/orifice to calculate the head loss.





APPENDIX  B


Metric D-W Specific Roughnesses


Darcy-Wiesbach specific roughnesses in mm.
(Source - Pipeflow analysis by Stephenson, 1984)

Finish                              Smooth     Average     Rough     
______________________________________________________________

Glass, drawn metals                   0          0.003      0.006
Steel, PVC or AC                      0.015      0.03       0.06
Coated steel                          0.03       0.06       0.15
Galvanized, vitrified clay            0.06       0.15       0.3
Cast iron or cement lined             0.15       0.3        0.6
Spun concrete or wood stave           0.3        0.6        1.5
Riveted steel                         1.5        3          6
Foul sewers, tuberculated
       water mains                    6         15         30
Unlined rock, earth                  60        150        300




APPENDIX   C


COMMON UNIT CONVERSIONS


MULTIPLY                           BY                      TO GET
________________________________________________

centistokes                      1x10-6              square meters / sec.
cubic ft/sec (cfs)               448.8               gpm (US)
cubic ft/sec (cfs)               .028317             cubic meters/sec.
cubic meters/sec                 1000.               liters per second
feet (length)                    .30480              meters
feet of liquid                   SG/2.31             psi
gpm (US)                         .06309              liters per second
gpm (Imperial)                   1.20094             gpm (US)
inches                           25.4                mm. (millimeters)
liters/sec.                      15.85               gpm (US)
Kpascals                         .1450               psi
Kpascals                         .102/SG             meters of liquid
meters (length)                  3.2808              feet
meters of liquid                 SG/.102             Kpascals
Million gal/day (MGD)            .0438               cubic mtr/sec 
Million gal/day (MGD)            694                 gpm (US)
mm (millimeters)                 .0394               inches
pounds/sq.inch (psi)             6.8948               Kpa
pounds/sq.inch (psi)             2.31/SG              feet of liquid


SG is specific gravity (See Cameron pages 4-37 to 4-45)
(for kinematic viscosity conversions, see 4-25 in Cameron)




APPENDIX  D

ATMOSPHERIC PRESSURES AT VARIOUS ALTITUDES


        ALTITUDE                          PRESSURE
  FEET            METERS              Psia           Kpa
 -1000            -304.8              15.2          104.8
  -500            -152.4              15.0          103.4
     0                 0              14.7          101.4
   500             152.4              14.4           99.3
  1000             304.8              14.2           97.9

  1500             457.2              13.9           95.8
  2000             609.6              13.7           94.5
  2500             762.0              13.4           92.4
  3000             914.4              13.2           91.0
  3500            1066.8              12.9           88.9

  4000            1219.2              12.7           87.6
  4500            1371.6              12.4           85.5
  5000            1524.0              12.2           84.1
  5500            1676.4              12.0           82.7
  6000            1828.8              11.8           81.4

  6500            1981.2              11.5           79.3
  7000            2133.6              11.3           77.9
  7500            2286.0              11.1           76.5
  8000            2438.4              10.9           75.2
  8500            2590.8              10.7           73.8

  9000            2743.2              10.5           72.4
  9500            2895.6              10.3           71.0
 10000            3048.0              10.1           69.6
 15000            4572.0               8.3           57.2
 20000            6096.0               6.7           46.2

 30000            9144.0               4.4           30.3
 40000           12192.0               2.7           18.6
 50000           15240.0               1.7           11.7