ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

                ÛÛÛÛÛÛÛÛÛ
                Û       Û             Û              Û    Ü
                Û       Û                            Û  ÜÛß
                Û       Û   Û    Û    Û    ÛÛÛÛÛÛ    ÛÛÛß
                Û     Ü Û   Û    Û    Û    Û         Û ßÛÜ
                ÛÛÛÛÛÛÛÛÛ   ÛÛÛÛÛÛ    Û    ÛÛÛÛÛÛ    Û   ßÛ
                      ß
                ÛÛÛÛÛÛÛÛÛ
                Û                               Û       Û
                Û                             ÛÛÛÛÛ   ÛÛÛÛÛ
                Û      ÜÜ   ÛÛÛÛÜÛ   ÛÛÛÛÜÛ     Û       Û
                Û       Û   Û    Û   Û    Û     Û       Û
                ÛÛÛÛÛÛÛÛÛ   ÛÛÛÛßÛ   Û    Û     Û       Û

                ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ













                        A  Project  Scheduling  Tool
                               By  L. Varga

                           Copyright(c) 1987,88
                               Release  2.0








                            Release 2.0



                          Table of Contents

                                                       Section
               Introduction .  .  .  .  .  .  .  .  .  .  1

               System Requirements   .  .  .  .  .  .  .  2

               Overview of Quick Gantt  .  .  .  .  .  .  3

               Screen Fields   .  .  .  .  .  .  .  .  .  4

               Menu Commands.  .  .  .  .  .  .  .  .  .  5

               Key Commands .  .  .  .  .  .  .  .  .  .  6

               Messages  .  .  .  .  .  .  .  .  .  .  .  7

               Quick Gantt Tips.  .  .  .  .  .  .  .  .  8



                                                                page 1-1

                           Introduction
                           ------------

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º                                                         º
       º Quick Gantt is a project scheduling tool that makes it  º
       º easy to create and maintain Gantt charts. It is         º
       º available in two sizes and two prices. The small versionº
       º which handles up to 50 tasks is available for FREE whereº
       º you find it ( BBS, a friend and Shareware outlets have  º
       º it). The large version which handles up to 500 tasks is º
       º available for $20 from me along with support.           º
       º                                                         º
       º L. J. Varga                                             º
       º 18725 S. E. 43rd St.                                    º
       º Issaquah, WA. 98027                                     º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

                     Just a Quick Note from the Author

     The reason I created QG was probably for the reason you are looking at
     it.  I didn't need a $400 project manager. All I wanted to do was
     determine the end date of a project allowing for weekends, holidays,
     etc. I also wanted to add, delete and change tasks and get a quick
     answer.  I am working to improve Quick Gantt and the copy you purchase
     will no doubt be improved. I am trying to include your suggestions as
     they come.

     I have discovered that I can improve the appearance of the printed
     chart by simply altering a few character fonts on the printer. The
     result is a is solid black bar for completed tasks and a white bar for
     the incomplete portions.  I intend to proved my font set for the HP
     Laser Jet Series II and plan to have a set for the Epson (or
     compatable) too.

                      OK now to Quick Gantt ............


     The Gantt chart is a popular way of displaying schedules.  It is
     constructed with a calendar on the horizontal axis and a list of
     events or tasks on the vertical axis. The duration of the task is
     shown as the horizontal line.  The Gantt chart tends to have a
     stepped or 'waterfall' appearance as the tasks go down the side and
     the duration line moves further to the right.



                             Calendar(time) ---->
           Tasks
             1         ----------
             2                   ---------
             3                            ----
             4                                -----



                                                                page 1-2


     Another tendency is for many of the tasks to be dependent upon one
     another.  The second task often must wait for the first task to be
     completed before it can start.  This dependency can be useful in
     constructing the chart.  For example, if one knows when Task 1 is to
     begin and its flow time (duration) and that Task 2 begins with the
     end of Task One and that Task 3 begins with the end of Task 2, etc.,
     all that is required to build dependencies in the chart is to know
     when Task One starts, the flow time of each task and the order of
     task execution.  If Task One is delayed then the second is also
     delayed. As a result the chart can be thought of as a series of
     dependencies.

     Gantt charts are popular for project control because they are easy to
     construct and graphically show the tasks, their dependencies and
     their durations.  As a task is worked or completed it is often
     'colored' in to more easily display project status at any point in
     time.

     Some scheduling programs account for resources, cost and other
     items.  But in most projects the schedule is the overriding concern.
     The need then is for a simple tool that can depict tasks, their flow
     time and their relationships, thereby providing an overall view of
     when each task of a project is predicted to occur.

     The objective of Quick Gantt is to rapidly create, maintain and print
     a project schedule in the form of a Gantt chart.



                                                                page 2-1




                     System Requirements for Quick Gantt
                     -----------------------------------

              -  IBM (tm) PC or compatible

              -  DOS 2.0+

              -  Minimum of 140k of memory for the Small Version
                 and 300k for the large version. You can open
                 a shell to DOS but more memory will be necessary
                 to run programs or execute DOS commands.

              -  Monochrome or color monitor

              -  Printer with IBM (tm) extended character set
                  (for better visual appeal only)
                 This program has been designed to use the font
                 found on standard printers and requires no
                 graphics capabilities.

              -  One disk drive but a fixed hard drive is better.





                                                                page 3-1

                         An Overview of Quick Gantt
                         --------------------------

     Quick Gantt treats tasks in a schedule very much as a spreadsheet
     treats cells.  Tasks can be set up as dependent on one another such
     that if one changes, all dependent tasks are changed to agree.

     Up to 500 tasks can be scheduled over any time span.  Weekends can be
     included or excluded along with specific user defined holidays.  The
     minimum increment of scale is one (1) day.  Tasks of less then one day
     will appear as a one day flow on the Gantt chart.  The printed copy
     can be up to 255 characters wide. Most of the Fields on the report are
     optional, so only necessary data need be presented.

     Quick Gantt creates and maintains a Gantt chart on the PC screen.
     Each task requires only three pieces of data to create a useful
     chart:

                   1.  A task number or name.
                   2.  The task duration or flow time in days.
                   3.  The identity of an absolute start date or the
                       preceding task upon which the task is dependent.

     As a task is created or changed, the task duration will be displayed
     as a bar in the chart portion of the screen along with other tasks and
     their durations. In this way you can see the position of the task with
     respect to both calendar dates and the other tasks.

     Once the data has been entered the chart can be printed or sent to a
     file where it can be edited for a report.

     Once a report has been created the report titles and specifications
     are saved with the file.


                                                               page 3-2

                            Input  Screen

     The input screen is used to edit one task at a time. The top two rows
     contain all the data about the task which has been selected for
     editing.  The rest of the screen is a condensed Gantt chart which
     displays this task and eleven adjacent tasks.  As you scroll or page
     through the chart, the tasks and related information will appear for
     editing in the top two rows of the screen.




ÉTASKÍÍÍÍÍÍÍÍÍÍËTITLEÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËRESPONSIBILITYÍËWËH»
º3             ºSelect a contractor                       ºME             º1º1º
ÌESDÍÍÍÍÍÍÍËFLOWËECDÍÍÍÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
º10/17/1988º30  º11/25/1988º33 ºBegin with End of     2                 º-6   º
ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹
º           YR º  1988                     1989                               º
º           MO º  Aug Sep  Oct   Nov  Dec  Jan  Feb  Mar  Apr  May  Jun  Jul  º
º           DA º  08 26 13 01 19 06 24 12 30 17 04 22 12 30 17 05 23 10 28 16 º
ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍ¹
º1             º  ====           .                                            º
º2             º      ======     .                                            º
º3             º             ==----                                           º
º4             º             =======------                                    º
º5             º                 .         ---------------------------        º
º5.1           º                 .         --                                 º
º5.1.1         º                 .         -                                  º
º5.1.2         º                 .          -                                 º
º5.1.3         º                 .          -                                 º
º5.1.4         º                 .           -                                º
º              º                                                              º
º              º                                                              º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

Line #  1 of   1
File: WORK.QG



                                                               page 3-3

                                 Printed Report


     The report is initiated from the menu.  The width of all the columns
     is variable and optional. The report can be up to 255 columns wide and
     can be formatted to fit all common sizes of printer paper.


As of 10/10/1988
ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
º                                                      My Project
º
ÌÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÑÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
º      ³                     ³       ³    ³     1988                        198
ºTASK  ³TITLE                ³RESPONS³FLOW³     Aug Sep   Oct   Nov   Dec   Jan
ÌÍÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍÍÍÍØÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
º1     ³Select the site      ³ME     ³20  ³08/08     09/02 .
º      ³                     ³       ³    ³     =====      .
º      ³                     ³       ³    ³                .
º2     ³Prepare plans        ³Archati³30  ³     09/05      . 10/14
º      ³                     ³       ³    ³          ======+-
º      ³                     ³       ³    ³                .
º3     ³Select a contractor  ³ME     ³30  ³              10/17        11/25
º      ³                     ³       ³    ³                .  --------
º      ³                     ³       ³    ³                .
º4     ³Get financing        ³ME     ³60  ³              10/17               01
º      ³                     ³       ³    ³                .  ---------------
º      ³                     ³       ³    ³                .
º      ³                     ³       ³    ³                .
º5     ³Construction         ³A&B Con³120 ³                .             01/09
º      ³                     ³       ³    ³                .                  -
º      ³                     ³       ³    ³                .
º5.1   ³Prepare the site     ³       ³12  ³                .             01/09
º      ³                     ³       ³    ³                .                  -
º      ³                     ³       ³    ³                .
º5.1.1 ³Notify the Utilities ³A&B Con³2   ³                .             01/09
º      ³                     ³       ³    ³                .                  -
º      ³                     ³       ³    ³                .
º5.1.2 ³Clear the site       ³A&B Con³3   ³                .              01/11
º      ³                     ³       ³    ³                .                  -
º      ³                     ³       ³    ³                .
ÈÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÏÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

 This example is wider than shown and has been truncated on the right side.



                                                                page 3-4

                     Preparing for Quick Gantt


     When planning a project, forethought must be given to the structure
     and organization of tasks so that the project will become more
     manageable.

     The Gantt chart should be constructed to reflect the project and how
     it will develop remembering that most projects are made up of many
     small projects.

     People generally find it natural to think in a structured "top down"
     order.  They visualize the completed project in total then disassemble
     it into its major components. Each major component is subdivided into
     its components until the work is broken down into meaningful and
     manageable tasks.  Quick Gantt is designed to utilize this work
     breakdown structure (WBS).

     It is not necessary to retain the higher level tasks to use Quick
     Gantt but the intermediate tasks will provide more reporting
     possibilities.

     The Natural order is to start with the first task assign it a number
     or identifier then get the next task(s) which immediately follows and
     number it. In this way the Gantt chart will have a full left to right
     and descending appearance. This is clean, neat and orderly and clearly
     shows the dependencies of the tasks.  It is fine for small projects.


     The Tiered WBS order is to assign each major task a number (or letter)
     such as 2, 4A or B, then take each task and decompose it numbering
     each as a subset of the parent.

      Ex:  2.2 and 2.3 are under task 2.

     Repeat this process until each task has a clearly defined action and
     deliverable product.  Retain the intermediate tasks.

     The WBS allows assignment of responsibility at a detailed level and
     "rolling" the tasks up to be managed at a higher level.  The use of
     this structure is not necessary when using Quick Gantt but doing so
     allows reporting at various levels of detail depending upon the
     management level to be addressed.  This structure creates extra tasks
     but they can be self maintained by Quick Gantt (refer to "Formulas" in
     the Screen Fields section). This structure also permits large charts
     to be broken down into small ones for more effective tracking.  The
     WBS method permits flexibility in the level of reporting detail.

     Quick Gantt reports can be printed in either Natural or Work
     Breakdown order.



                                                                page 3-5


     Below is a graphical example of a task, 3, being sub defined like a
     product structure. The lower level or 'Tier' is identified by a
     decimal system  where the task takes the numerical name of its parent,
     then identifies itself by adding a decimal (.) and a character.

  Example
     If 3 is a task then 3.1 and 3.2 are a subset of 3.  3.1.1 and
     3.1.2 are a third level tier of 3. In this way a schedule and
     responsibility can be assigned with a separate schedule, yet the
     schedule supports the total project.

     Quick Gantt identifies tiers in the schedule by a decimal point.

     The Natural Gantt chart can become too large with too many tasks
     to efficiently track progress and can become cluttered with
     irrelevant tasks when there are many responsible participants.







      Natural Order
      ÉÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º       ³3/3   4/6                         º
      º 1     ³   ---                            º
      º       ³  4/7        6/16                 º
      º 2     ³      -------                     º
      º       ³         6/17       8/10          º
      º 3     ³             -------              º <--
      º       ³         6/17   7/1               º
      º 3.1   ³             ---                  º <--
      º       ³         6/17 6/20                º
      º 3.1.1 ³             -                    º
      º       ³          6/21  7/1               º
      º 3.1.2 ³              --                  º
      º       ³             7/2    8/10          º
      º 3.2   ³                ----              º
      º       ³                                  º
      ÈÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

     Tasks 3 and 3.1 are not necessary since they are simply higher levels
     of task 3.2, 3.1.1 and 3.1.2.



                                                               page 3-6


      Tiered - Work Breakdown Structure
      ÉÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º       ³3/3   4/6                         º
      º 1     ³   ---                            º
      º       ³  4/7        6/16                 º
      º 2     ³      -------                     º
      º       ³         6/17       8/10          º
      º 3     ³             -------              º
      ÈÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍ   /           \ ÍÍÍÍÍÍÍÍÍÍ¼
                      /                  \
                   /                         \
                /                                \
             /                                       \
            ÉÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º       ³         6/17       8/10          ºÍ»
            º 3                   -------           <-------- 3 is a summary
            º       ³         6/17   7/1               º º º  rollup of any
            º 3.1              /  ---                  º º º  3.**** task.
            º       ³       /         \                º º º
            º 3.2   ³    /              \              º º º
            ÈÍÍÍÍÍ    /                   \ÍÍÍÍÍÍÍÍÍÍÍÍ¼ º º
              ÈÍÍ  /                        \ÍÍÍÍÍÍÍÍÍÍÍÍ¼ º
                /                              \ÍÍÍÍÍÍÍÍÍÍÍ¼
             /                                    \
            ÉÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
            º       ³         6/17   7/1               ºÍ»
            º 3.1   ³             ---         <------------- 3.1 is a summary
            º       ³         6/17 6/20                º º   rollup of any
            º 3.1.1 ³             -                    º º   3.1.**** task
            º       ³          6/21  7/1               º º
            º 3.1.2 ³              --                  º º
            ÈÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ º
              ÈÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




 

                                                               page 4-1

                         SCREEN  FIELDS
                        ----------------

      This section will describe the use and purpose of the fields on the
      screen. To move between screen fields, use the tab key to advance
      right or (shift + tab) to move left.



     Field Name:    TASK

     Purpose:       To provide a unique alphanumeric identity for an
                    event.

     Restrictions:  This is a required field. Any character is valid. One
                    to 14 characters may be used. Although there is no
                    restrictions to task identifiers Quick Gantt has
                    features that use a decimal work breakdown structure.
                    This means the major task is identified by a character
                    (Ex: 32 ) and as the task is broken down is components
                    take the parents Id. (Ex: 32.5)
     How to use:
                                                  2       Major Task
                     ÉTASKÍÍÍÍÍÍÍÍÍÍËTITLEÍÍÍÍÍ     2.1     Sub Task of 2
                     º2.1           º                 2.1.1    Sub Task of 2.1
                     ÌESDÍÍÍÍÍÍÍËFLOWÍÍÍËECDÍÍÍ       2.2.2    Sub Task of 2.1
                                                    2.2      Sub Task of 2


                    Enter any character or number. The task can be a number or
                    name.

                      Ex :  1
                            Start
                            1-st

                    Tasks must always be referenced using exactly the format
                    that was initially used.  Task dependencies are based on
                    correct labeling.

                      Ex:
                       'First-Task'is not the same as 'first-task'.


                    Although there are no restrictions on the task name, it is
                    worth giving thought to the level of detail that will
                    ultimately be incorporated into the schedule.  For example
                    if you plan to build a new house you might set tasks such
                    as:

                          1   select site
                          2   have plans drawn
                          3   select contractor
                          4   get bank loan
                          5   start construction

 

                                                               page 4-2



                    These tasks are quite broad and their duration may be too
                    lengthy for good control.  It is then necessary to break
                    down these tasks to a lower level:

                          5 Construction
                             5.1   prepare the site
                             5.2   frame
                             5.3   finish exterior
                             5.4   finish interior

                   Even at this level many important tasks are not identified
                   so further breakdown may be necessary:

                          5.1   prepare the site
                            5.1.A   notify the utility companies
                            5.1.B   clear the site
                            5.1.C   dig to foundation level
                            5.1.D   provide utility access





     Field Name:   TITLE

     Purpose:      To provide a description of the event.

     Restrictions: This field is not required.  Any alphanumeric character
                   is valid.  1 to 42 characters may be entered.

     How to use:
                       ÍÍÍÍÍÍËTITLEÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËRESP
                             ºGrade building site  to foundation level   º
                       ÍÍËFLOWÍÍÍËECDÍÍÍÍÍÍÍËFORMULAÍÍÍÍÑÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÊÍÍÍÍ


                    Enter the title of the task, splitting the title at the
                    hash mark, if desired.  When the TITLE column of the
                    chart is printed, up to 21 characters of the title will
                    appear on the first line with up to the remaining 21
                    characters appearing on the second line.  The hash mark
                    indicates the start of the second line.


 

                                                               page 4-3



     Field Name:   RESPONSIBILITY

     Purpose:      To identify the person or group responsible for
                   completing the task.

     Restrictions: This field is not required.  Any alphanumeric character
                   is valid.  1 to 18 characters may be entered.

     How to use:   Enter the name, title or description that is to assume
                   responsibility for the task. This might also be used to
                   identify resources.

                     ÍÍÍÍÍÍÍÍÍËRESPONSIBILITYÍËWËH»
                              ºA&B Constructioº1º1º
                     ÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹





                        ESD, FLOW and ECD

      Many factors influence the timing of tasks but there are two basic
      approaches. The first is to establish a starting date for the first
      task, specify the sequence in which all tasks will occur and provide
      the flow time or duration of each.  Then it is a simple process to
      'draw' the chart.  When the flow time of any task changes all
      dependent tasks are changed to agree.

      The second approach is to establish absolute fixed start and
      completion dates. The flow time is calculated to be the number of work
      days between these two dates.

      Both approaches can be accommodated when using the next three fields:
      ESD,FLOW and ECD.  The user must choose to establish the flow time and
      let the estimated start and completion dates 'float' or to input
      firmly 'fixed' the start and completion dates. Depending upon this
      choice either the FLOW time field or the ESD/ECD fields will be used
      but not both.

 

                                                               page 4-4


     Field Name:   W (Workday Schedule)

     Purpose:      To define which of five (5) possible workday schedules.
                   is used to calculate the beginning or end dates of a task.
                   The default is schedule 1.

     Restrictions: Must be a number between 1 and 5.

                     ÍÍÍÍÍÍÍÍÍËRESPONSIBILITYÍËWËH»
                              º               º1º º
                     ÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹





     Field Name:   H (Holiday Schedule)

     Purpose:      To define which of three (3) possible holiday schedules.
                   is used to calculate the end dated of a task.

     Restrictions: Must be a number between 1 and 3.

                          ÍÍÍÍÍÍÍÍÍËRESPONSIBILITYÍËWËH»
                                   º               º º1º
                          ÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹





     Field Name:   ESD (Expected Start Date)

     Purpose:      To define the date a specific task is expected to begin.

     Restrictions: Must be a valid date.

                    ÌESDÍÍÍÍÍÍÍËFLOWËECDÍÍÍÍÍÍÍË%CMËFORMULAÍÍ
                    º09/16/1986º    º          º   º
                    ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍ

                    This field can  only be reached if 'Fixed Esc/Ecd'
                    appears in row 24 of the screen.  It is used when
                    flow is not as important as firm ESD's and ECD's.
                    See page 26 on key F6.

                    In all other instances in which it is dependent upon
                    another task's schedule before this task's schedule can
                    be established this date is calculated by formula.  It
                    is calculated from the beginning or end of a parent or
                    driving task.

                    As with all fields in which a date is entered, if the
                    year is excluded then it is assumed to be the current
                    year.


                                                                page 4-5


     Field Name:   FLOW

     Purpose:      To define the duration of a task.

     Restrictions: This field is required unless using the fixed ESD/ECD
                   option.  6 numeric characters may be entered.

     How to use:

                    ÌESDÍÍÍÍÍÍÍËFLOWËECDÍÍÍÍÍÍÍË%CMËFORMULAÍÍ
                    º          º23  º          º   º
                    ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍ

                    FLOW is the expected duration of the task in days.  Only
                    whole days can be entered, not fractions.  It is not
                    necessary and in fact not desirable to include weekends
                    and holidays in the flow time. These non-workdays will be
                    dealt with in the CALENDAR section . The
                    flow time should be thought of as net work days to
                    perform the task.





     Field Name:   ECD (Expected Completion Date)

     Purpose:      To define the date a task is expected to complete.

     Restrictions: Valid date

     How to use:

                    ÌESDÍÍÍÍÍÍÍËFLOWËECDÍÍÍÍÍÍÍË%CMËFORMULAÍÍ
                    º          º    º10/04/1986º   º
                    ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍ

                   This field is the date the task will end and is calculated
                   from the start date plus flow.  Normally this field is not
                   used  and the cursor will jump over it.  However, when the
                   fixed ESD/ECD mode is used this field must be completed.



                                                               page 4-6


     Field Name:   %CM (Percent Complete )

     Purpose:      To define the amount of the task that has been
                   completed.

     Restrictions: A numerical value between 0 and 100.

     How to use:   Determine the actual portion of the task that has
                   been completed. This should be a percentage of the
                   effort required.  Zero (0) if the task has not been
                   started and 100 if the task is complete. An internal
                   progress date is calculated.



                  ÌESDÍÍÍÍÍÍÍËFLOWËECDÍÍÍÍÍÍÍË%CMËFORMULAÍÍÍÍ
                  º          º    º          º22 º
                  ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍ



                                                               page 4-7


     Field Name:   FORMULA

     Purpose:      To establish the start or end dates of a task. To
                   create dependencies between tasks. To enter an
                   informational note.

     Restrictions: Required. See complete instructions below.

     How to use:

                   The formula performs one of four functions for any given
                   task:

                    1.  To set an absolute start or end date to a task.
                    2.  To set up the dependencies between tasks
                    3.  To summarize or 'rolls up' a group of tasks.
                    4.  To create a note or information line.

                    In addition the formula field is made up of four
                    sub-fields.  It is necessary to enter data into one or more
                    of these sub-fields to perform each of the functions.



           1.  Set an absolute start or end date to a task.

               If the task is to begin or end on a specific date, then in
               the first position  of the formula field enter a 'B' when
               meaning the task beginning or a 'E' when meaning a task
               ending.  The first sub-field will be filled with 'Begin
               with' or 'End with' then the cursor will move to the second
               sub-field.  In this field enter the date that the task is to
               begin or end.  The date is entered as month / day /year.  A
               slash (/) or dash (-) is required between numbers.

                ÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                    º   ºBegin with 7/14/86                       º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹

               Press the return key and if no errors appear, the task,
               title and its' associated scale line will be displayed in
               the chart section of the screen.

               The formula will read :
                   (This task will)   END WITH   (the date)   7/4/86

                or (This task will)   BEGIN WITH   (the date)  7/4/86

 

                                                               page 4-8

        2.  Set up the dependencies between tasks

               As with setting an absolute date (above), in the first
               sub-field enter a 'B' meaning 'begin with' or an 'E' meaning
               'end with'.  When the cursor moves to the second sub-field
               again choose "B" if the task is dependent upon the beginning
               of another task or "E" if it is dependent upon the end of a
               task. The sub-field will be filled with "Begin of" or "End
               of". The cursor will move to the third sub-field where the
               parent task is entered.

                          end of the
                          independent task >|
                A.1             ------------
                B.1                          ----------
                                            | > beginning of the
                                                dependent task

               Formula for task B.1
                ÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                    º   ºBegin with End of     A.1                º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹


               The cursor can then be tabbed to the fourth field where an
               adjustment in days can be entered. The purpose of the
               adjustment is to shift the beginning or ending of the
               dependent task.  For example this task may begin 5 days
               before its parent task ends.

                          end of the
                          independent task >|
                A.1             ------------
                                      |     |
                       adjustment of  |     |
                            5 days    |     |
                B.1                   |----------
                                      | < beginning of the
                                                dependent task

               Formula for task B.1
                ÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                    º   ºBegin with End of     A.1           -5   º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹


 

                                                               page 4-9


               With these choices a number of task relationships can be
               created so that a formula now reads something like:

          (This task will)   BEGIN WITH  (the)   END OF  (task)  1.a
                            start when the first ends

       or (This task will)   BEGIN WITH  (the)  BEGIN(ning) OF  (task)  1.a
                            start when the first starts

       or (This task will)   END WITH  (the)   END OF  (task)  1.a
                            end when the first ends


       or (This task will)   END WITH  (the)  BEGIN(ning) OF  (task)  1.a
                            end when the first starts

              Using the adjustment field :

  (This task will) BEGIN WITH (the) END OF  (task)  1.a  (plus) 5 (days)
                           start 5 days after the first task ends


         3.  Summarize or 'roll up' a group of tasks.

               The formula field can also be used to display a 'summary'
               bar. Often it is useful to include in a Gantt chart a higher
               level summary bar which represents the total time required
               to complete a group of related lower level tasks.

               Since the summary task is made up of all the detailed tasks,
               when one of the detail tasks changes, the summary task
               changes accordingly.  Quick Gantt allows the creation of tasks
               which are not individually scheduled but picks up the
               schedule for a group of tasks.  In this way the summary
               level schedule is maintained.

               Entering 'S' in the first position of the first sub-field
               will fill the sub-fields one and two with 'Summary   Level
               of  ' and then move the cursor to sub-field 3 for a task
               mask.  The mask must end with '.*'.   The character string
               before the .* is used as a constant so that any task with
               this string is included in the 'roll up'.

                ÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                    º   ºSummary    Level   of 1.a.*              º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹

 

                                                               page 4-10


               In the above example any task with '1.a.' in the first 4
               positions will be "rolled up" into this task so the flow
               days for the summary task will be calculated for the range
               of all these detail tasks.

                 ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍßÍ
                 º1.a           º -----------------
                 º1.a.1         º ------
                 º1.a.b         º               ---
                 º1.a.2         º       ---------
                 º1.b.1         º                ---------
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

               Note that 1.b.1 was not included in the roll up.  As the
               duration of any task with a '1.a.' in the first 4 positions
               is changed, the roll up bar '1.a' will change. A
               recalculation is usually necessary.

          4.  Create a note.

               Occasionally a task is known to be required but the flow,
               time start date or dependency is not known at the time the
               Gantt chart is created. In this case it may be desirable to
               enter a note of explanation or status on the chart so the
               task is not forgotten and can be completed when all the
               information is available.  The formula field permits this by
               starting the formula with a double quotation mark (") then
               using the next 43 characters in the formula field to enter
               an explanatory note into the chart.

               This field can also be used without a task label to provide
               descriptive breaks in the chart.


                ÍÍÍÍË%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                    º   º"Awaiting estimate from engineering      º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹

             ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍ
             º1.a           º -----------------
             º2.            º Awaiting estimate from engineering
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ



 

                                                               page 4-11


             Summary of Formula constructs:



                          field 1   | field 2  |  field 3    | field 4
                                    |          |             |
                ÍÍÍÍË%CMËFORMULAÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÍÍÊÍÍÍÍÍÍÑÍÍÍÍÍËÍÍÍÍÍ¹
                    º   ºBegin with End of     4.3.1         5     º     º
                ÍÍÍÍÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÊÍÍÍÍÍ¹

                         Begin with Begin of  task #         +- adjustment
                                                                 days
                         End with   End of

                                    MM/DD/YY

                         Summary    Level  of task #.*

                         " text ----------------------------------->


     Field Name:   DEV (Deviation from schedule)

     Purpose:      To define the number of work days the task is
                   ahead (+) or behind (-) schedule.

     Restrictions: This field is calculated no entry is permitted.


     How to use: This field is calculated from the percentage complete
                 (%CM) field. The current date is then subtracted from
                 the progress date.


                  Ë%CMËFORMULAÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍËDEVÊÍ¹
                  º   º                                         º-7   º
                  ÊÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÊÍÍÍÍÍ¹




                                                             page 4-12




     Field Name:   Scale

     Purpose:      To display the dates of the tasks.

     Restrictions: The Quick Gantt chart is always shown in a 60 character
                   field on the screen with the minimum increment being one
                   day.

     How to use:

               ÌÍÍÍÍÍÍÍÍÍÍÊÍÍÍËÍÍÍÊÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍÏÍÍÍÍÍÍÍÍÍ
               º           YR º  1987                    1988
               º           MO º  Nov     Dec             Jan            Feb
               º           DA º  15 21 27 03 09 15 21 27 02 08 14 20 26 01 07
               ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍ

                   The scale is made up of three lines. The first shows the
                   year, the second the month (abbreviated) and the last
                   displays the day. The scale is calculated with the first
                   date entry.  As tasks are added the scale will change to
                   show the duration of all tasks currently entered into the
                   Gantt chart. If a task is deleted or shortened the scale
                   line will not change until the entire chart is
                   recalculated.  The scale will never be less the one day per
                   scale column but it can be can compressed so a column can
                   represent several days. As seen in the above example each
                   column represents 2 days.



                                                               page 4-13


     Field Name:   Chart

     Purpose:      To provide a visual display of task durations

     Restrictions:  The chart cannot be directly accessed but is
                    the graphic result of the formulas and input in the
                    first two lines of the screen.

     How to use:

                 ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍÍßÍ
          1      º1.2           º -----------------
          2      º1.2.A         º --------
          3      º1.2.B         º         ---------
          4      º              º
          5      º1.3           º ERROR in parent
          6      º1.3.A         º ERROR in task
          7      º1.4           º  To Be Determined
                 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

                   There are twelve Gantt lines displayed on the screen. On
                   each line, the left side displays the task identity; the
                   right side displays the graphical duration of a task. The
                   length of a line is the task duration from the expected
                   start date (ESD) to the expected completion date (ECD) when
                   measured on the scale line.  As the formula for the task is
                   changed, the length and position of this line will change.
                   If this task is dependent upon another task then it may
                   change due to that task.

                   Seven samples of line display are shown above:

                1)  Could be a summary level (the rollup of lines 2 & 3)
              2&3)  These are tasks with dates and dependencies established
                    by their formula field.
                4)  A blank line in which the task was left blank.
                5)  This message 'ERROR in task' indicating
                    that a task cannot be calculated because at least one
                    of the three required data items is wrong or missing
                    data is missing in the task.
                6)  This a message 'ERROR in parent' indicates
                    that a task cannot be calculated because some required
                    data is missing in the parent task. This task cannot
                    be calculated until the parent is correct.
                7)  Example of a note where no start or finish time has
                    been determined.


                                                              page 5-1

                         Menu Commands
                        ---------------

          The menu can be reached by pressing the F1 key. A list of
          commands will appear below the chart. By pressing the first
          letter of each command that command will be executed. Some
          commands will lead to additional commands.  The menu
          structure is represented as follows:


            keys            description
          ---------     ------------------------------
          Esc           MENU
          Esc,F             Files
          Esc,F,L              Load
          Esc,F,S              Save
          Esc,F,A              Append
          Esc,F,C              Clear
          Esc,T             Tasks
          Esc,T,I              Insert
          Esc,T,C              Copy
          Esc,T,I              Move
          Esc,T,F              Formulas
          Esc,T,F,R               Recalculate
          Esc,T,F,E               Errors
          Esc,T,F,F               Fixed Esd/Ecd
          Esc,T,F,L               Link
          Esc,T,D              Delete
          Esc,T,S              Sort
          Esc,T,L              Locate
          Esc,T,N              Next
          Esc,C             Calendar
          Esc,C,W              Weekends
          Esc,C,H              Holidays
          Esc,R             Report
          Esc,H                Header
          Esc,C                Columns
          Esc,D                Data
          Esc,P                Print
          Esc,A             Appearance
          Esc,A,R              Refresh
          Esc,A,C              Color
          Esc,A,G              Gantt Line
          Esc,A,Q              Quick Keys
          Esc,D             DOS
          Esc,Q             Quit


                                                               page 5-2



     Menu Name:    Esc  (Escape Key)

     Purpose:      To present the menu and terminate screen changes.

     Restrictions: None.


     How to use:   Press Escape (Esc) key and the F-key menu will be
                   replaced by a command line menu. The escape (Esc) can
                   be used to exit this menu. No chart updates can occur
                   while in this menu.





     Menu Name:    Files,Load

     Purpose:      To load a previously saved Gantt chart.

     Restrictions: File must have been created by QUICK GANTT.

     How to use:   Press Esc,F,L keys. Type the name of a valid file and
                   press enter.  Include the full path if not in the
                   current directory.





     Menu Name:    Files,Save

     Purpose:      To save a Gantt chart

     Restrictions: File must have been created by QUICK GANTT.

     How to use:   Press Esc,F,S keys. Type the name of a valid file
                   and press enter. If no file is entered the current
                   file is saved.  The startup file id "WORK.QG".






     Menu Name:    Tasks,Insert

     Purpose:      To insert one or more blank lines.

     Restrictions: Lines are inserted ahead or the current position.

     How to use:   Press Esc,T,I keys. Enter the number of lines to be
                   inserted then press the ENTER key.


                                                                page 5-3

     Menu Name:    Tasks,Delete

     Purpose:      To delete lines no longer required or to remove
                   blank lines.

     Restrictions: One or more lines may be removed at a time.

     How to use:   Press Esc,T,D. On the last line of the screen there will
                   appear a counter of the lines be be deleted. This wilo the
                   start with the current line.

                   Example:
                      If the cursor is at task line 5 then on the last
                      line of the screen will appear

                                                Delete Lines 5..5

                       As the cursor is scrolled up or down the range will
                       change. When the ENTER key is pressed all lines
                       within this range will be deleted.




     Menu Name:    Tasks,Copy

     Purpose:      To copy lines to another area of the chart.

     Restrictions: One or more lines may be copied. The new location
                   must be outside of the range.

     How to use:   Press Esc,T,C. On the last line of the screen there will
                   appear a counter of the lines be be copied. This will the
                   start with the current line. The end of the range wil
                   change as the cursor is moved up and down. At the
                   end of the range press the ENTER key. This will
                   cause the "to" line to appear. Scroll up or down
                   to the desired location then press the ENTER key.
                   The Group of lines will be inserted ahead of this line.

                   Example:
                      If the cursor is at task line 5 then on the last
                      line of the screen will appear

                                                  Copy Lines 5..5

                       As the cursor is scrolled up or down the range will
                       change. When the ENTER key is pressed the copy
                       range will be defined and the "to" location will
                       appear.
                                                   Copy Lines 5..8 to 8

                       Scroll up or down to the desired input line then
                       press the ENTER key. The destination MUST be
                       out side the copy block. It will then be inserted
                       ahead of this line.


                                                              page 5-4

     Menu Name:    Tasks,Move

     Purpose:      To copy lines to another area of the chart.

     Restrictions: One or more lines may be moved. The new location
                   must be outside of the range.

     How to use:   Press Esc,T,M. On the last line of the screen there will
                   appear a counter of the lines be be moved. This will the
                   start with the current line. The end of the range wil
                   change as the cursor is moved up and down. At the
                   end of the range press the ENTER key. This will
                   cause the "to" line to appear. Scroll up or down
                   to the desired location then press the ENTER key.
                   The Group of lines will be inserted ahead of this line.
                   and deleted from their current location. Move is
                   identical to the Copy action except that the original
                   lines are deleted.




     Menu Name:    Tasks,Sort

     Purpose:      To re-arrange the order of the tasks in Gantt chart.

     Restrictions: All tasks lines including blank lines can be sorted in
                   ascending or descending order for following fields:
                     1    Task
                     2    Responsibility
                     3    ESD (Expected Start Date)
                     4    ECD (Expected Completion Date)

     How to use:   Press Esc,T,S. A numerical selection is made for one of the
                   four fields. If the selection is a positive number then
                   the sort is ascending, if the selection is a negative
                   number then the sort is descending
                       Ex:   1  sorts tasks in ascending order.
                            -1  sorts tasks in descending order.




     Menu Name:    Tasks,Locate

     Purpose:      To locate a literal string of characters in the Gantt
                   chart.

     Restrictions: The search is in the Task, Description, Responsible
                   ESD, ECD and Formula fields.

     How to use:   Press Esc,T,R. The enter the string to be searched for.
                   and press the ENTER key. The search will start from
                   first task. When a match is found the task will appear
                   as the first task in the screen.



                                                             page 5-5


     Menu Name:    Tasks,Next

     Purpose:      To locate the next occurrence of literal string
                   of characters in the Gantt chart.

     Restrictions: The search is in the Task, Description, Responsible
                   ESD, ECD and Formula fields. It must follow the
                   Locate action.

     How to use:   Press Esc,T,N.  The search will start from
                   last occurrence. When a match is found
                   the task will appear as the first task
                   in the screen.




     Menu Name:    Tasks,Formulas,Recalc

     Purpose:      To recalculate the date for all tasks on the Gantt
                   chart.

     Restrictions: All tasks that have an entry in Task field are
                   recalculated.

     How to use:   Press Esc,T,R. A recalculating message will appear at the
                   bottom of the screen along with the line number being
                   recalculated. There are no provisions to test for circular
                   dependencies and summary tasks proceeding the tasks being
                   summarized may require more then one recalculation.





     Menu Name:    Tasks,Formulas,Errors

     Purpose:      To locate tasks which have an error in the required
                   fields which will prevent calculation of task
                   schedules.

     Restrictions: The search will begin with the first task.

     How to use:   Press Esc,T,E.





                                                               page 5-6


     Menu Name:    Tasks,Formulas,Fixed Dts

     Purpose:      To establish absolute beginning and end dates for a task.

     Restrictions: Both ESD and ECD dates must be entered.

     How to use:   Press Esc,T,F. "Fixed ESD ECD" message will appear on
                   the bottom of the screen. Access to ESD and ECD fields
                   now occurs. When these dates are enterd the flow time
                   and a formula will be created. You may modify of change
                   or change the task dependencies at any time.




     Menu Name:    Tasks,Formulas,Link

     Purpose:      To simplify the effort when creating tasks of linking
                   tasks in the formula.

     Restrictions: This will change or create the task dependency

     How to use:   Enter the formula up to the parent or preceding task.
                   The task preceding this one may be several pages back
                   and you don't remember it's number. Press Esc,T, F, and
                   L. Then scroll to the dependent task. You will notice
                   a stationary cursor bar marking the original task. When
                   you get to the parent task press the enter key. This will
                   copy the parent task number into the formula and return
                   you to the original position on the chart.




                                                               page 5-7


     Menu Name:    Calendar,Weekends

     Purpose:      To include or exclude weekends (Saturday & Sunday)
                   from the available time period.

     Restrictions: Weekends are either on or off for the entire Gantt chart.

     How to use:   Press Esc,C,W. Schedule #1 will the appear with the
                   cursor on Sunday. Press 'N' if it is a non-workday or
                   'Y' if it is. The cursor will then move to the next
                   day. There must be at least one work day in the week.
                   When complete press the escape key (Esc) and schedule
                   #2, 3, 4, and 5 will appear. When complete with
                   schedule #5 you will return to the main screen.


                             ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                             º    Schedule  #1    º
                             º     Work  Days     º
                             ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
                             º   Sunday    :No    º
                             º   Monday    :Yes   º
                             º   Tuesday   :Yes   º
                             º   Wednesday :Yes   º
                             º   Thursday  :Yes   º
                             º   Friday    :Yes   º
                             º   Saturday  :No    º
                             º                    º
                             º Total Workdays  5  º
                             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                        Total workdays must be greater then 0
                                  Esc  to end





                                                               page 5-8

     Menu Name:    Calendar,Holidays

     Purpose:      To load dates that are to be excluded from the available
                   workdays for the entire Gantt chart.

     Restrictions: A maximum of 120 dates can be loaded.

     How to use:   Press Esc,C,H. The first of three holiday schedules
                   will appear.  A new screen will appear with the cursor
                   in a block in the upper left-hand corner. In this box
                   enter a date which will be a Non-work date in the
                   format of MM/DD/YYYY. Years between 00 and 99 are
                   assumed to be in the 1900's. Then press one of the
                   cursor movement keys (8,2,4 or 6) on the number pad.
                   Do not use the enter keys. The cursor and box will move
                   to the next position for another entry.  When all
                   entries have been made, press the escape key.  There
                   will be a pause as the dates are sorted and checked for
                   duplicates.  When complete press the escape (Esc) key
                   and the second and third holiday schedules will appear.
                   After the third one you will return to the main
                   screen.


           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º              Holiday schedule #1                                º
           º  Enter Specific Non-Work Dates [mo/da/yr] --  Esc. to end    º
           ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¶
           º 12/25/87  12/24/87  1/1/87                                      º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           º                                                                 º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




                                                               page 5-8

     Menu Name:    Report,Header

     Purpose:      To identify the print character which will be used to
                   draw the chart and to create the report title.

     Restrictions: Printer with IBM (tm) graphic fonts is preferred,
                   not necessary. Up to 4 title lines may be used.

     How to use:   Press keys Esc,H. The screen shown below will
                   be presented.






       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º                                 Report  Header                      º
       º                                                                     º
       º   Use graphic characters ..........(Y/N): Y                         º
       º   Boxed or Open header ............(B/O): B                         º
       º   Lines per page................(Min 15): 60                        º
       º                                                                     º
       º                                                                     º
       º                                                                     º
       º                                                                     º
       º   Number of Title Lines ..........(0..4): 2                         º
       º   Enter Title Line      2                                           º
       ºThis is the second Title line                                        º
       º   Corrections ...(Y/N):                                             º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
   º                                Title line 1
   º                        This is the second Title line
   ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ


   The above title block will be created on the Header screen as it is
   defined. It is an example of a boxed graphics  header with two
   title lines. The one below is an open header in non-graphics with
   three title line.


                                    Title line 1
                            This is the second Title line
                               This is a 3rd Title Line
   +--------------------------------------------------------------------------



                                                             page 5-9


     Menu Name:    Report,Columns

     Purpose:      To define the columns and their size that will appear
                   on the report.

     Restrictions: All columns except the Gantt chart are optional. Most
                   permit variable sizes.

     How to use:   Press keys Esc,R,H. The screen shown below will
                   be presented.



     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º                            Report  Columns                            º
     º                                                                       º
     º   Enter Task width . . . . . (0..14): 4                               º
     º   Enter Title width. . . . . (0..21): 21                              º
     º   Enter Responsible width. . (0..15): 0                               º
     º   Enter Flow width . . . . . . (0,4): 4                               º
     º   Enter % Complete width.  . . (0,3): 3                               º
     º   Enter Deviation width. .   . (0,5): 5                               º
     º   Enter Print width  . . .(min..255): 80                              º
     º   Gantt width ......................: 36                              º
     º   Corrections....(Y/N):                                               º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     º                                Title line 1
     º                        This is the second Title line
     ÌÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÑÍÍÍÍÑÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     º    ³                     ³    ³   ³     ³
     ºTask³Title                ³Flow³%Cm³d Sch³
     ÌÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍØÍÍÍÍØÍÍÍØÍÍÍÍÍØÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ


     The full header including column titles will be created on this
     screen as they are defined.




                                                              page 5-11

     Menu Name:    Report,Data

     Purpose:      To define which tasks are to be printed on the report
                   by data content.

     Restrictions:


     How to use:   Press keys Esc,R,D. The screen shown below will
                   be presented.





     ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
     º                            REPORT  DATA                               º
     º                                                                       º
     º                 From                          To                      º
     º   Task . . . .:                 Task . . . :                          º
     º   ESD  . . .  :                 ESD. . . . :                          º
     º   ECD  . . . .:                 ECD. . . . :                          º
     º   %Complete. .:   0             %Complete. : 100                      º
     º   Deviation. .: -9999           Deviation. :  9999                    º
     º   Flow . . . .:    0            Flow . . . : 9999                     º
     º   Responsible :                                                       º
     º   Sort by :                                                           º
     º      1-Task 2-Responsible 3-ESD 4-ECD 5-Flow 6-%Cmpl 7-Dev            º
     º   Corrections ......(Y/N):                                            º
     º                                                                       º
     ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼





                                                              page 5-12


     Menu Name:    Report,Print

     Purpose:      To initiate the actual printing of the report
                   and to determine the report output destination.

     Restrictions: Output is to the printer unless a file is stated.


     How to use:   Press keys Esc,R,P. The screen shown below will
                   be presented.






              ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
              º Report by Tier or Natural order..(T/N): T       º
              º   From Tier: 1    To Tier: 1                    º
              º Output to Printer or Disk........(P/D): d       º
              º   File Name: c:\qg\myfile.qg                    º
              º                                                 º
              º Quit, Change, Print:                            º
              ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼




                                                              page 5-13






     Menu Name:    Appearance,Refresh

     Purpose:      To restore the screen if shifted or altered by system
                   error messages.

     Restrictions: None.

     How to use:   Press Esc,A,R.  The entire screen will be cleared and
                   replaced with a new copy of the chart.



     Menu Name:    Appearance,Colors

     Purpose:      To change the colors of the screen.

     Restrictions: This feature should only be used on color monitors but
                   can be used on monochrome to reverse the white on black
                   standard.

     How to use:   Press Esc,A,C. The first request will be for a foreground
                   color or the character color. Select a number between 0
                   and 15. Then a request will be made for a background
                   color or the field behind the character.  Select a number
                   between 0 and 7. Do not use the same color for both or
                   there will be no visible characters on the screen.

                      Number   Color            Number  Color
                         0     Black               8    Gray
                         1     Blue                9    Light Blue
                         2     Green              10    Light Green
                         3     Cyan               11    Light Cyan
                         4     Red                12    Light Red
                         5     Magenta            13    light Magenta
                         6     Brown              14    Yellow
                         7     white              15    Hi Intensity White





                                                              page 5-14


     Menu Name:    Appearance,Gantt line

     Purpose:      To change the image of the Gantt line on both the screen
                   and the printed chart.

     Restrictions: Any character.

     How to use:   Press Esc,A,G. There are 3 characters displayed on the
                   screen and the report, they are for the task line
                   character for the portion of the task completed, the
                   character for the portion of the task in work or not
                   yet complete and a character to mark the current date.
                   Each will be requested.  if no character change is
                   wanted press the ENTER key.  after the final character
                   request the the chart will be redrawn. These characters
                   are save in the definition file and loaded with the
                   program.



                                                               page 5-15


     Menu Name:    Appearance,Quick keys

     Purpose:      To replace multiple menu key strokes with a single
                   key by use of the 40 (F) function keys.

     Restrictions: The first character of each menu item is used just
                   as if the keys were pressed.

     How to use:   Press Esc,A,Q. There are 40 function keys which can
                   be defined to replicate menu key strokes. Each of
                   the 10 function keys can be used in normal condition,
                   in the shifted position by holding the 'Shift' key then
                   pressing the 'F' key, with the 'Ctrl' key and
                   with the 'Alt' key.

                   Key strokes and data are put in the action field just
                   as it would be typed using the menu; with two
                   exceptions, the 'Enter' key is replaced with '<'
                   and do not start with the 'Esc' key as you would on
                   the menu.

                   Once defined they are saved in the QG.DEF file which
                   is loaded with the program.


               ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
               º         Norm      Quick Key Definitions          º
               ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄ¶
               º       Action                           ³  Menu   º
               ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄ¶
               º F1 = AQ                                ³1-QKeys  º
               º F2 = FS<                               ³2-Save   º
               º F3 =                                   ³         º
               º F4 =                                   ³         º
               º F5 =                                   ³         º
               º F6 =                                   ³         º
               º F7 =                                   ³         º
               º F8 =                                   ³         º
               º F9 = RHCD{Esc}                         ³9-Rpt    º
               º F0 = RP{Esc}                           ³10-Prnt  º
               ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄ¶
               º Select-Keys, Key Group, [Ecs]:                   º
               º Keys 1..0,                                       º
               º Key Group N Normal, S Shifted, A Alt, C Cntl     º
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼



                                                               page 5-16

               Select the group you want to define and press the key for that
               group. 'N' for the normal group, S for shifted, 'A' for the
               alt group and 'C' for the control gorup. When this is done
               the top line in window will identify the group.

               Then press a number for the F-key; Ex. 2 is F2. The cursor
               will then go to this line in the window. Type the key strokes
               then press enter. The cursor will then move to the Menu column.
               Enter the prompt you want to appear on the main screen menu.
               Up to 8 characters can be used for each key. Four menu lines
               will be created. One each for Norm, Shift, Ctrl and Alt.
               When the Shift, Alt or Ctrl key is pressed, the function key
               menu will appear under the chart.

               Example above
                   Normal F1 is Appearance,Quickkeys
                                   this will go to the Quick Key window.
                          F2 is Files,Save and ENTER
                                   this will cause immediate saving of the
                                   current file.


                  The F-key menu will appear as:

               º5.1.4         º        ==========----
               ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
               1-QKeys 2-Save 9-Rpt 10-Prnt
               Line #  1 of   1
               File: WORK.QG

               NOTE: If running from a floppy be sure to put your program
               diskette back in the drive before Quiting. The key
               definitions are save at this time and are reloaded when
               the program is started.




                                                               page 5-16


     Menu Name:    DOS

     Purpose:      To execute DOS commands.

     Restrictions: If you run this program from a hard disk then Command.com
                   should be in the root directory. If run from a floppy then
                   copy command.com to the floppy disk.

     How to use:   Press F1,D.  You can then enter the DOS command. If doing a
                   directory listing be sure to include asterisks (*).
                   Ex; dir a:*.dat






     Menu Name:    Quit

     Purpose:      To terminate this program.

     Restrictions: None.

     How to use:   Press Esc,Q. If no changes have been made to the chart
                   since the last save (see F2 key), the program will halt. If
                   a change has occurred, Quick Gantt prompts "File not saved-
                   Quit without saving [Y/N]".  A "Y" response will halt the
                   program.  Any other character will cause Quick Gantt to
                   continue.



                                                               page 6-1



                                Key  Commands
                               ---------------
     Esc  - accesses the menu or exits the menu.

     Home - moves the window to the first task.
     End  - moves the window to the last task.

     PgUp - moves the Gantt Chart window up 12 lines.
     PgDn - moves the Gantt Chart window down 12 lines.

     Cursor Up - moves up one task
     Cursor Down - moves down one task

     Tab Right - moves the cursor to the next screen field.
     (Shift) Tab Right - moves the cursor to the previous screen field.

     Shift, Ctrl, Alt - will also cause the Function key menus to appear
            if they have been defined.


     See the Menu section on Quick Keys for defining and use of the
     Function (F) keys.




                                                              page 8-1

                              Messages
                              --------
          Two types of messages exist - those that inform you about
          current processing and those that identify an error or warning.
          All of these appear at the bottom of the screen.

          Informational messages:

          "Line # xxx of xxx " is always present on line 24 and identifies
               the current line being edited along with the total number of
               lines in the chart.

          "Fixed ESD ECD" appears in line 24 and is toggled on/off through
                use of the menu or defined Quick keys.  When this appears
                the ESD and ECD fields are accessible but the flow field is
                not.

          "Recalculating xxx" appears in line 24 when the chart is being
               recalculated. The xxx is the current line being
               recalculated.

          "INSERT" appears in line 24 and is toggled on/off by the insert
               key on the number pad.

          "File :xxxxxxxx.xxx" appears on line 25 and is the name of the
               current Gantt file being edited.




                                                              page 8-2


          Error messages:

          "ERROR in task" appears in the chart instead of a flow line when
               one or more of the three required items is missing.

          "ERROR in parent" appears in the chart instead of a flow line
               when the task on which the current task depends upon has an
               error.

          "Invalid file name" appears in line 25 when the entered file
               cannot be found.

          "Value must be 0 to 9" appears when the key pressed is not within
               the range.

          "Exceeds maximum number of tasks" appears when attempting to add
               another task and that task would exceed the total number
               of tasks permitted in the Quick Gantt program.

          "Invalid date  Re-enter" appears when attempting to begin or end a
               task on a specific invalid date.

          "Task does not exist" appears when making a task dependent upon
               another which does not exist.

          "ECD must equal or be greater then ESD" appears when in the fixed
               ESD/ECD mode, the dates are in the wrong order.

          "Input file is not for this program" appears when attempting to
               load a file not created by Quick Gantt.

          "Must be 'B','E' or 'S'" appears when entering the first field of
               the formula.

          "Must be 'B' or 'E' or valid date" appears when pressing the
               wrong key in the second field of the formula.



                                                               page 9-1


                         Quick Gantt Tips
                         ----------------

     1.  Save your file regularly and ALWAYS save before printing,
         sorting or working with blocks of tasks. No software or
         system is without its bugs.

     2.  For Floppy Use Only: Before quitting Quick Gantt return the
         program disk to the active drive so that the current QG.DEF
         file can be saved.  This file contains any changes made to
         F-Key assignment, etc.


     3.  If you want to preview your report before printing, you can
         print it to a file. Using the DOS shell of the menu, you can
         view the file of your report. If it is not what you want, simply
         make the corrections and reprint.

     4   The use of a text editor will allow additions, footnotes,
         etc, that Quick Gantt may not provide.

     5.  Printing can be a lengthy process, depending upon the size of
         the chart.  You can print to a file, then QUIT Quick Gantt,
         exiting to DOS. You can print the report in background,
         using the DOS PRINT program thereby enabling the use of you
         computer for other tasks.

     6.  A report up to 255 characters can be built. This is often too
         wide for many printers. By first printing to a file, then
         using a simple program, "slices" can be printed and "glued"
         side by side to create a full width Gantt chart. This works
         well when using double wide font. You can create a wall size
         chart that allows several people to view at one time. Be sure
         you do not use a proportional print font.

     7.  Some companies have standards for the symbols that appear on
         a Gantt chart and most printers permit "user defined
         characters" (see your user guide). You can define the
         characters used for the Gantt line or others you may have
         "edited" into the file so that when printed the chart meets
         your standards. There are utilities for designing these fonts.
         They look very good when done on a laser jet.



         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,000+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                               (713) 665-7017