HPLOT USER INSTRUCTIONS

      The program HPLOT (HP Plot) will plot two and three dimensional data
      on a HPGL compatible plotter connected to a serial port (COM1 or COM2).

      If the user types "HPLOT filename COMn" at the DOS prompt the
      program HPLOT will read plot commands from the text file "filename"
      and output HPGL plotter instructions to a plotter connected to serial
      port "COMn".  If the parameter "COMn" is omitted it defaults to
      "COM1".  The port "COMn" must have been configured with the DOS
      command "MODE COMn:baudrate,parity,databits,stopbits,P".  The plot
      commands are a subset of the plot commands recognized by the SPLOT
      (Screen Plot) program; HPLOT does not have an interactive mode and
      does not recognize the commands intended for interactive use.  Type
      just "HPLOT" at the DOS prompt to display a summary of the plot
      commands recognized by HPLOT.  You can use the SPLOT program to display
      a plot on the screen then use the SAVE command to create a plot
      command file that the HPLOT program can use to produce a hardcopy plot.

      The command "HPLOT filename hpfile" will send the HPGL plotter
      instructions to file "hpfile"; this file could then be transfered to
      another computer to be output to a HPGL compatible plotter. The file
      could also be included in a WordPerfect word processing document.
      However, there is a bug in the way WordPerfect handles certain HP
      character sets that causes letters and numbers produced by HPLOT to
      be misplaced and too small when output to a printer by WordPerfect.
      HPLOT will correct for this bug in WordPerfect if the following DOS
      command is used to set a DOS environment variable:

      SET HPLOT=WP

      Note that with the above DOS environment varible set, HPLOT letters
      and numbers will be misplaced and too LARGE when output to an HP
      plotter.

      The HPLOT program has been tested on a HP 7550 plotter and on a HP
      ColorPro plotter.

      The HPLOT program is protected by copyright law; it is not public
      domain. It is provided with the SPLOT software and its use, other
      than for evaluation purposes, without payment for the SPLOT software
      is a copyright violation. The HPLOT program is provided "AS IS"
      without warranty of any kind.