GASCALC.EXE


                 Copyright (c),1990, H L Hendrick, all rights reserved


           GASCALC is a microcomputer gas meter flow volume  calculator  for
           volumes measured with standard flange tap static and differential
           reading recorders.

           The  program utilizes factors and methods recommended in AGA Bul-
           letin No. 3 and applies to 2,3,4,6 and 8 inch flange tap standard
           meter tubes.

           Minimum requirements are a one disk drive microcomputer with 128K
           memory and an 8086/8088 processor using MSDOS or  PCDOS  or  com-
           patible computer.  A printer is optional.

           In order to use the program,  format a new blank disk and install
           your  operating system on it.   Insert the program disk furnished
           by H L Hendrick in drive a: and copy the GASCALC.EXE  program  to
           the  new formatted disk in drive b:.  Store the program disk fur-
           nished by H L Hendrick and use the disk you have created as  your
           program  disk.  Insert your program disk in drive a: and boot up.
           Enter GASCALC and follow the menu prompts, or copy the program to
           your hard disk.

           Input to the program is as follows:

           Enter tube size:
                Enter 2,3,4,6 or 8

           Enter orifice size:
                Enter the orifice size in a decimal fraction

           Enter base pressure:
                This entry is the sales contract base pressure and should be
                entered as 14.65 or 14.73 or 15.025, etc.

           Enter specific gravity:
                This entry must be entered in a decimal fraction.

           Enter flowing temperature:
                Enter the flowing temperature in degrees F

           Enter Static pressure:
                Enter the Static pressure in psia

           Enter differential:
                Enter the differential reading in inches



                                           1







           After the input is completed,  the flow volume is calculated  and
           all factors used in the calculation are displayed on the screen.

            An  option is provided to allow changing any of the input values
           for a new calculation.  If a print out is desired,  use the print
           option.

           A data file my be created and the results of each calculation may
           be stored in sequential order. Give each lease or meter data file
           a separate name. The files are stored on disk in the ASCll format
           and  can  be  incorporated  into a word processor file for report
           presentation.

                H L Hendrick is a member of  the  Association  of  Shareware
           Professionals  (ASP).  ASP  wants to make sure that the shareware
           principle  works  for  you.  If  you  are  unable  to  resolve  a
           shareware-related  problem  with  an ASP member by contacting the
           member directly,  ASP may be able to help.  The ASP Ombudsman can
           help,  but  does  not  provide  technical  support  for  members'
           products.   Please write to the ASP Ombudsman at  P.O.  Box  5786
           Bellevue,  WA  98006 or send a CompuServe message via easyplex to
           ASP Ombudsman 70007,3536

                Support for this program is provided to registered users  by
           mail to H L Hendrick at P.O.  Box 79530,  Houston TX 77279 and by
           phone at 713-932-9408 or through CompuServe 76217,1171



























                                           2