************************ ASILIB SYSTEM SUBROUTINES *************************

 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ALLOCDOS:     Allocate DOS memory block.  This permits dynamic memory
              allocation for your ASIC programs.

Parameters:   bytes&, block segment

              Bytes& is the number of bytes you want to allocate.  Bytes&
              may be greater than 64k.

              Block Segment is the segment address of the allocated memory
              block.  The starting offset of the memory block is always 0.
              If the segment address returned by AllocDOS = 0, then
              insufficient memory is available for the requested memory
              block.

Restrictions: Requires ASIC's extended math option and DOS version 3.0 or
              greater; if you are linking your ASIC object modules with
              another library besides ASILIB, ASILIB must be specified
              LAST in your list of libraries or on the command line.

Example:

REM  allocate 128k bytes of DOS memory

        bytes& = &hex20000&
        call sub "allocdos", bytes&, memseg

REM  check memory segment for errors

        if memseg = 0 then
           REM  uh oh, not enough memory
        endif



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ASICDS:       Get ASIC's default data segment.

Parameters:   defaultseg

              ASICDS returns the data segment in use as ASIC's default.
              This segment is nessesary for several ASILIB subroutines
              which require both segment and offset portions of data
              addresses.

Example:

REM  I want to swap the first 150 elements of arrays a() and b()
        dim a(1000)
        dim b(2000)

REM  program fills in the arrays
        .
        .
        .
REM  get ASIC's default data segment
        call sub "ASICDS", defaultseg
        aptr=VARPTR(a(1))
        bptr=VARPTR(b(1))

REM  remember that each integer is 2 bytes
        bytes=300
        call sub "swapb", defaultseg, aptr, defaultseg, bptr, bytes




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DAYNAME:      Returns the name of a specified day

Parameters:   DayNumber, day$

              DayNumber is a number from 1 through 7, inclusive,
              representing the days Sunday through Saturday.
              The name of the day is returned to the calling program in
              day$.  Since ASIC uses 80 bytes for each string, an ASIC
              string array would consume 80*7 = 560 bytes of data space.
              Since ASILIB can store the day names more compactly, only
              138 bytes are required for the entire DayName subroutine,
              including the names of the days!

Restrictions: Assumes that DayNumber is an integer from 1 to 7.

Example:

REM  I want to print "Monday" on the screen

        call sub "dayname",(2,day$)
        print day$


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EXENAME:      Get the name of the program.

Parameters:   ProgramName$

              The full program name including drive and path is returned
              in ProgramName$.  This is handy for finding data files
              in the program's directory, among other things.

Restrictions: Requires DOS 3.0 or greater.

Example:

REM  I need to get the drive and directory where this program is stored

        call sub "exename", ProgramName$



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

EXESIZE:      determine size of any .EXE program

Parameters:   ProgramName$, ProgramSize&

              ProgramName$ is a valid name of a .EXE-format disk file,
              such as the ProgramName$ returned by ASILIB's EXENAME
              subroutine.

              ProgramSize& returned to your program is the number of bytes
              in the file loaded by the DOS program loader.  Additional data
              may be copied to the end of a DOS .EXE file with the DOS
              COPY /B command.  This is handy for help screens or other such
              data that you want to keep with the .EXE file, but that you
              don't want to be loaded in memory with the program.  If you do
              copy additional data to the .EXE file, EXESize will report only
              the portion of the file loaded in RAM by the DOS program loader,
              while ASILIB's FSize reports the entire file size.

Restrictions: Requires ASIC's extended math option.  If EXESize is called
              with an invalid ProgramName$ or if other errors occur,
              ProgramSize& is returned = -1.  More specific information
              about the nature of the error can be determined with FExist.
              Errors may include file not found, access denied or
              not .EXE format.

Example:

REM  I've stored some data at the end of the .EXE file and now I
REM  want to retrieve it.

        call sub "exename", ProgramName$
        call sub "exesize", ProgramName$, ProgramSize&

REM  Now I can open the file & use FSEEK to position the file pointer.
        .
        .
        .



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOPPIES:     determine the number of floppy disk drives intalled

Parameters:   No input parameters; returns n=number of floppy drives

Example:

REM  determine how many floppy drives are installed
        call sub "floppies", n



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FLOPPYTYPE:   determine the type of floppy disk drives intalled

Paramerters:  drive$, drivetype

              FLOPPYTYPE determines what kind of floppy disk drive is
              installed as drive A: or drive B:.  Drivetype codes returned
              are:

               0 = invalid drive number
               1 = 360k
               2 = 1.2M
               3 = 720k
               4 = 1.44M

Restrictions: Supports physical drives A: and B: only

Example:

        call sub "floppytype", "A:", drivetype




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FREEDOS:      Release DOS memory allocated by AllocDOS and other ASILIB
              subroutines.

Parameters:   segment address, errcode

              The segment address passed to FREEDOS must have been
              allocated by ASILIB's AllocDOS subroutine or other ASILIB
              subroutines which recommend using FREEDOS.  Errcode = 0
              normally; if an invalid segment address is used with
              FREEDOS, errcode = &hex09.

Example:

REM  Allocate a block of 1000 bytes, then release the block later.

        call sub "allocdos", 1000&, memseg
        .
        .
        .
        call sub "freedos", memseg, errcode


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETDOSVER:    get DOS version

Parameters:   no input parameters; returns major and minor DOS versions

              The Major DOS version number is 3 for version 3.x, 4 for
              version 4.0, etc.; the minor version, for example, is
              21 for DOS version 3.21.  Some ASILIB subroutines require
              DOS version 3.0 or better; if the major version is 3 or
              greater, these subroutines will work OK.

Example:

        call sub "getdosver", maj, min




 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

INSERT:       Control Insert keyboard toggle.

Parameters:   Insertmode

              If insertmode = 0, the Insert keyboard toggle is turned off.
              If insertmode = 1, the Insert keyboard toggle is turned on.

Example:

REM  turn insert toggle on

        insertmode=1
        call sub "insert", insertmode


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISATT:        determines if an ATT 6300-type display card is installed
              this equipment is like a CGA except that it has an additional
              640 x 400 2-color graphics mode (mode &hex40)

Parameters:   No input parameters; returns &hexFFFF if installed, 0 if not.

              ISATT determines if an ATT 6300-type display card is installed.
              This equipment is like a CGA except that it has an additional
              640 x 400 2-color graphics mode (mode &hex40).

Example:

        call sub "isatt", attflag



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISEVGA:       Determines if an EGA or VGA is installed.

Parameters:   No input parameters; returns monitor type, EGAVGAflag
              and minimum memory.

              Memory is the amount of memory as determined by standard
              BIOS functions; does not attempt to detect SVGA memory
              greater than 256k.  EGA equipment may have memory < 256k.
              If memory = 0, no EGA or VGA is installed.
              EGAVGAflag = 1 if EGA, 3 if VGA.
              EGA boards may be connected to either a Monochrome, CGA or
              EGA monitor.  If monitor = -1, CGA is used.  If monitor = 0,
              the EGA is driving a monochrome monitor.  If monitor = 1, the
              EGA is connected to an EGA or better monitor.

Example:

        call sub "isevga", mon,egavga,mem



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISHERC:       Determines if a Hercules or compatible display card
              is installed and whether it is the active video system.

Parameters:   Returns HercCode.

              HercCode = 0 if no hercules is installed.  If a Hercules
              is detected, HercCode is:

              128 = Hercules Graphics Card or compatible, active
              144 = Hercules Graphics Card Plus, active
              208 = Hercules InColor Card, active
             -128 = Hercules Graphics Card or compatible, inactive
             -144 = Hercules Graphics Card Plus, inactive
             -208 = Hercules InColor Card, inactive

Example:

REM  I want to use Hercules graphics, but first I need to determine
REM  if a Hercules card is installed

        call sub "IsHerc", herccode
        if herccode = 0 then
           REM  no Hercules
        else
           REM  use Hercules graphics
           .
           .
           .
        endif


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISMOUSE:      determines if a mouse is installed

Parameters:   No input parameters; returns mousebuttons

              ISMOUSE determines if a mouse and its software driver are
              installed.  Mousebuttons = 0 if no mouse or no mouse driver
              is installed; otherwise mousebuttons = number of buttons the
              mouse has.

Example:

REM  turn mouse cursor on if the mouse is installed

        call sub "ismouse", mousebuttons
        if mousebuttons > 0 then
            call sub "showmouse"
        endif




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ISSEVGA:      determines if a Super EGA or Super VGA is installed

Parameters:   No input parameters; returns SVGA ID code

              SVGA ID code returned by ISSEVGA is in two parts:
               1) the high byte of the code tells you whether it's an EGA
               or VGA
               2) the low byte tells you the manufacturer

             If high byte = 01, it's an EGA
             If high byte = 03, it's a VGA

             Low byte codes are:

              1 = Paradise
              2 = Everex
              3 = Tseng VGA chipset
              4 = Oak Technologies
              5 = Western Digital (Paradise) OEM
              6 = ATI
              7 = Compaq
              8 = NCR
              9 = Trident
             10 = Video7
             11 = Genoa
             12 = Cirrus
             13 = Chips & Technologies
             14 = Tseng 4000
             15 = Ahead A
             16 = Ahead B
             17 = Trident 8900

             If svgacode = 0, no SuperEGA or SuperVGA is installed.
             See also IsEVGA

Example:

        call sub "issevga", svgacode

        if svgacode < &hex0300 then
        REM  either SuperEGA or no SVGA
            .
            .
        else
        REM  time to decode low byte..
            .
            .
        endif



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETCMD:       isolates command line parameters
              GetCMD assumes that parameters are separated by one or more
              spaces

Parameters:   commandnumber, commandtext$

              GETCMD isolates one or more command-line parameters,
              returning each one as commandtext$.  commandnumber
              determines which parameter is returned; the first command
              line parameter in number 0.  If the length of commandtext$
              = 0, the commandnumber is greater than the actual number of
              command line parameters.

Restrictions: Requires DOS version 3.0 or later.

Example:

REM  I want to see if an input filename was specified when the program
REM  was started

        commandnumber = 0
        call sub "getcmd", commandnumber, inputfile$
        cmdlen=LEN(inputfile$)
        if cmdlen > 0 then
        REM got an input filename
          .
          .
          .

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETCPU:       detects cpu type

Parameters:   no input parameters; returns cputype code

              GETCPU determines the kind of CPU in the computer.  CPUType
              codes are:

               0 if 8086/8088
               1 if 80186/80188
               2 if 80286
               3 if 386 (SX or DX)
               4 if 486 (SX or DX)

Example:

        call sub "getcpu",cputype



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETCRT:       determines active monitor type

Parameters:   No input parameters; reyurns crttype code

              CPUType codes returned are:

              -1       = CGA
               0       = MDA
              &hex0100 = EGA mono
              &hex0300 = VGA mono
               1       = EGA color
               2       = MCGA
               3       = VGA color
             128       = Hercules Graphics Card
             144       = Hercules Graphics Card Plus
             208       = Hercules InColor
             Note: GetCRT may be re-assembled with the /DNOHERC switch
             to eliminate code which detects Hercules equipment

Example:

        call sub "getcrt", crttype



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MATHCHIP:     determines if 80x87 math coprocessor is installed

Parameters:   No input parameters; returns mathchipcode

              Mathchipcodes returned by MATHCHIP are:

               0 = not installed
               1 = 8087
               2 = 287
               3 = 387 (DX or SX)
               4 = 487 (486DX or 487SX)

              If the coprocessor is present, it is initilaized by MathChip.

Example:

        call sub "mathchip", mathchipcode




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MONTHNAME:    Returns the name of a specified month

Parameters:   MonthNumber, month$

              MonthNumber is a number from 1 through 12, inclusive,
              representing the months January through December.
              The name of the month is returned to the calling program in
              month$.  Since ASIC uses 80 bytes for each string, an ASIC
              string array would consume 80*12 = 960 bytes of data space.
              Since ASILIB can store the month names more compactly, only
              170 bytes are required for the entire MonthName subroutine,
              including the names of the months!

Restrictions: Assumes that MonthNumber is an integer from 1 to 12.

Example:

REM  I want to print "February" on the screen

        call sub "monthname",(2,month$)
        print month$



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

PATH:         Isolates PATHs in program enviornment

Parameters:   path number, pathstring

              Much like GETCMD and MONTHNAME, PATH is a pseudo string array
              which returns a path from the program's enviornment block.
              If the length of the string returned by PATH is zero, there
              are no more paths in the enviornment block.

Restrictions: DOS 3.xx or greater

Example:

REM  the PATH statement in my AUTOEXEC.BAT file looks like this:
REM  PATH=C:\;C:\MASM;C:\DOS;..\

        for n=0 to 100
          call sub "path", n, a$
          i=LEN(a$)
          if i=0 then nomorepaths:
          print a$
        next n

REM  this prints:

REM  C:\
REM  C:\MASM
REM  C:\DOS
REM  ..\



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

RAMSIZE:      determine total base RAM intalled

Parameters:   No input parameters; returns bytes& installed.
              Note that bytes& is a long integer; requires ASIC's
              extended math option.

Example:
        call sub "ramsize", bytes&



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SYSTEM:      execute a second copy of COMMAND.COM;  optionally runs another
             program.

Parameters:  command$

             If command$ = "" control is transfered to another copy
             of COMAMND.COM and you get the DOS prompt.  Control is passed
             back to the calling program when EXIT is entered at the
             DOS prompt.
             If command$ is the name of a program either in the current
             directory or in a PATH directory, the program will be executed,
             and control will pass back to the calling program at the
             termination of the second program.  Command$ may include
             command line parameters.

Restrictions:Requires DOS 3.0 or greater

Example:

REM  I want to go to DOS temporarily to format a 720k disk

        command$="format a: /u /f:720"
        call sub "system",command$