******************************  TEXT MODE  *******************************

ASILIB Text mode video subroutines (C) Copyright 1994 Douglas Herr
All rights reserved

Screen writing in TEXT mode

ASILIB subroutines write directly to the video memory buffer, except
where noted.  ASILIB detects the default display type and screen
dimensions.  ASILIB assumes that CGA equipment requires "snow" control
and behaves accordingly.  In text modes, ASILIB does not distinguish
between CGA and MCGA equipment.

Multiple pages of video memory are available except with MDA video adapters.

Pages supported by ASILIB are shown below:

video system      screen size    ASILIB support
-------------     -----------    --------------
MDA               80 x 25        page  0       
CGA, MCGA         80 x 25        pages 0 - 3   
CGA, EGA, VGA     40 x 25        pages 0 - 7   
EGA, VGA          80 x 25        pages 0 - 7   
EGA               80 x 43        pages 0 - 3   
VGA               80 x 50        pages 0 - 3   
SVGA             132 x 25        pages 0 - 3   
SVGA             132 x 44        pages 0 & 1   
SVGA             132 x 50        pages 0 & 1
HGC, HGC+, InC    80 x 25        pages 0 - 15  
HGC+, InC         90 x 25        pages 0 - 13  
HGC+, InC         80 x 43        page  0       
HGC+, InC         90 x 43        page  0       

   ASILIB subroutines assume that rows are the vertical dimension and
   columns are the horizontal dimension of a text-mode screen.  The upper
   left corner of the screen is at row=1 and col=1



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

ANSICOLOR:    determines color attribute used by ANSI device driver.
              See also IsANSI.

Parameters:   No input parameters; returns color attribute

Example:

        call sub "ansicolor", colorattribute


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BLINKOFF:     disable blinking attributes; enable bright background attributes
BLINKON:      enable blinking attributes; disable bright background attributes

Parameters:   None.

              Color attributes which specify a background color greater
              than 7 will cause either blinking foreground characters or
              a bright-color background, depending on whether "Blink" is
              ON or OFF.  BlinkON enables the blinking characters and
              disables the bright background; BlinkOFF disables blinking
              characters and enables bright-color backgrounds.  This is
              unlike ASIC, which does not permit bright backgrounds.

Restrictions: Cannot be used on selected portions of the screen.  Works
              with all monitors in Text mode; may also affect 16-color
              graphics modes.  Affects entire screen, all pages.

Example:

REM  turn blinking attributes into bright background attributes
        call sub "blinkoff"

REM  turn bright background attributes into blinking attributes
        call sub "blinkon"


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

BORDER:       Change border color on CGA, EGA and VGA systems.

Parameters:   colorattribute

              EGA borders are quite thin.  Valid color attributes are 0 - 15.
              See COLORATTR for default colors.

Example:

REM  blue border
REM  assumes color palette was not changed
        attr = 1
        call sub "border", attr


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CLEAREOL:     clear from cursor position to end of line

Parameters:   colorattribute

              CLEAREOL clears from the cursor's current position to the
              right edge of the screen using colorattribute.

Restrictions: On Hercules equipment, works only in text mode on page 0;
              will not work with VGA13X graphics modes.

Example:

REM  I want to clear from (5,10) to the right edge of the screen
REM  with a BLACK color

        cursorrow=5
        cursorcolumn=10
        colorattribute=0
        call sub "cursoron", cursorrow, cursorcolumn
        call sub "cleareol", colorattribute


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSORCOLOR:  set cursor color and enable color palette (InColor only)

Parameters:   colorattribute

              Colorattribute may range from 0 to 15; requires Hercules
              InColor equipment.  If colorattribute = 0, the cursor color
              defaults to 7 (white).  If Hercules InColor is not installed,
              CURSORCOLOR does nothing.

Restrictions: works on Hercules InColor equipment only

Example:

REM  Change cursor color to bright red
        call sub "cursorcolor",12





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSOROFF:    make hardware cursor invisible at present location

Parameters:   None.

Restrictions: Text mode only; supports CGA, MCGA, MDA, HGC, HGC+, InC,
              EGA, VGA, SVGA

Example:

        call sub "cursoroff"


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

CURSORON:     move cursor to (row, col) and update cursor shape

Parameters:   Row, Column

              Row is the vertical dimension of the screen, starting at
              the top of the screen = 1, and column is the horizontal
              dimension of the screen, starting at the left edge = 1.

              Cursor shape is underscore if INSERT is off, larger block
              if INSERT is on.

Restrictions: Text mode only. Supports CGA, MCGA, MDA, HGC, HGC+, InC, EGA
              VGA, SVGA

Example:

REM  move cursor to left bottom of 80-column, 50-row screen

        CursorRow=50
        CursorColumn=1
        call sub "cursoron", CursorRow, CursorColumn





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

COLORATTR:    Calculate color attribute from foreground & background colors

Parameters:   Fore, Back, Colorattribute

              Calculates color attribute used by many ASILIB subroutines
              from foreground and background attributes.  Default
              foreground colors are shown below:

     foreground color   Value

         black            0         Note: Background colors 0-7 are
         blue             1         identical to foreground colors 0-7.
         green            2         Background colors 8-15 are identical
         cyan             3         foreground color 8-15 if Blink has
         red              4         been turned off.  If blink is on,
         magenta          5         background colors 8-15 will look like
         brown            6         colors 0-7, and will make the foreground
         "white"          7         blink.
         gray             8
         bright blue      9
         bright green    10
         bright cyan     11
         bright red      12
         bright magenta  13
         yellow          14
         bright white    15

Example:

REM  determine color attribute for bright red foreground with
REM  white background, no blinking
        fore=12
        back=7
        call sub "colorattr", fore, back, colorattribute



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FILLEOL:      fill row from cursor position to edge of screen

Parameters:   fill character, colorattribute

              FILLEOL fills from the cursor's current position to the
              right edge of the screen using colorattribute and specified
              fill character

Restrictions: On Hercules equipment, works only in text mode on page 0;
              will not work with VGA13X graphics modes.

Example:

REM  I want to fill from (5,10) to the right edge of the screen
REM  with a blue "*".

        cursorrow=5
        cursorcolumn=10
        colorattribute=1
        fillcharacter=ASC("*")
        call sub "cursoron", cursorrow, cursorcolumn
        call sub "filleol", fillcharacter, colorattribute


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETBORDER:    determine border color on CGA, EGA and VGA systens

Parameters:   no input parameters; returns color of screen border.

              Color attributes returned by GETBORDER range from 0 to 15.

Example:

        call sub "getborder", bordercolor



 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETPOS:       Get cursor position

Parameters:   No input parameters; returns cursorrow, cursorcolumn

              Uses BIOS functions to determine the current cursor position.
              Similar to ASIC's col% = POS(x) and row% = CSRLIN commands,
              but works with all text-mode screens sizes.

Example:

        call sub "getpos", cursorrow, cursorcolumn


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETSCREEN:    save a screen page to a memory buffer
PUTSCREEN:    copy a saved screen page to the video buffer

Parameters:   buffersegment, bufferoffset

              Buffersegment is the segment part of the memory buffer's
              address; bufferoffset is the offset part of the buffer's
              address.  You may use either an ASIC array or an ASILIB
              memory block allocated by AllocDOS.

Restrictions: Text mode only.

Example:

REM  allocate 4000 bytes for 80-column, 25-row screen

        dim screenbuffer(2000)

REM  save the screen
        bufferoffset = VARPTR(screenbuffer(1))
        call sub "asicds", buffersegment
        call sub "getscreen", buffersegment, bufferoffset
               .
               .
               .
REM  some time later...
        call sub "putscreen", buffersegment, bufferoffset

REM  see also ScreenMem example


 °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

GETSCREENSIZE:determine screen dimensions

Parameters:   No input parameters; returns screenrows, screencolumns

              GETSCREENSIZE allows you to determine the screen's dimensions.
              Rows are the vertical dimension and columns are the horizontal
              dimension.

Example:

        call sub "getscreensize", screenrows, screencolumns

REM with a standard 80 x 25 screen, getscreenrows returns screenrows = 25
REM and screencolumns = 80



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

HSCROLL:      scroll a portion of the screen left or right.

Parameters:   row0, col0, row1, col1, color, columns

              (Row0, col0) are the coordinates of the upper left part of
              the screen you want to scroll; (row1, col1) is the lower
              right corner.  Color = color attribute for cleared columns.
              Columns is the number of columns scrolled left or right.
              Scrolls left if columns > 0, scrolls right if columns < 0,
              clears area if columns = 0.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to scroll the entire screen area left 3 columns
REM  assume 80-column, 25-row screen

REM  use white-on-blue color attribute

        colorattribute = &hex0107
        call sub "hscroll", 1, 1, 25, 80, colorattribute, 3
        


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MODE43:       switch EGA to 80x43 text mode or VGA to 80x50 text mode
              Mode43 switches an EGA to the 80-column, 43-row text mode from
              any color mode or any EGA monochrome mode, or switches a color
              VGA to 80x50 text mode from any other color mode.

Parameters:   None

Example:

        call sub "mode43"



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MODECOLOR:    switches system to color text mode; may be used to switch
              monitors on a 2-monitor system, or to switch to the standard
              80-column, 25-rows color mode from other color modes

Parameters:   None

Example:

        call sub "modecolor"


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MODEMONO:     switches system to monochrome text mode; may be used either
              to switch active monitors on a 2-monitor sysem or to switch
              to monchrome text mode (80x25) from graphics mode (EGA or
              Hercules).

Parameters:   None

Example:

        call sub "modemono"



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MOVEPOS:      Move cursor position

Parameters:   rowoffset, columnoffset

              Moves the cursor from its present position by rowoffset rows
              and columnoffset columns.  Rowoffset and columnoffset may be
              positive or negative.

Example:

        rowoffset = -2            REM move the cursor up two rows
        columnoffset = 0          REM same column
        call sub "movepos", rowoffset, columnoffset




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SETPOS:       Set cursor location to row, column

Parameters:   row, column

              Positions the cursor at row, column.  Similar to ASIC's

              LOCATE row, column

              command, but works with non-standard text screens.  ASIC's
              PRINT command will not work well beyond 25 rows.

    Example:

        call sub "hram9043"     REM Hercules RAMFont 90-column mode, 43 rows
        row = 40
        column = 85
        call sub "setpos", row, column


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

SCREENMEM:    calculate bytes required to save screen page
              Used with GetScreen and PutScreen.

Parameters:   No input parameters; returns bytes& required to save screen.

              Note that SCREENMEM returns a LONG integer (bytes&) so that
              you can allocate the required space with AllocDOS.  Requires
              ASIC's extended math option.

Example:

        call sub "screenmem", screenbytes&
        call sub "allocdos", screenbytes&, blockseg
        call sub "getscreen", blockseg, 0
               .
               .
               .
REM  some time later...
        call sub "putscreen", blockseg, 0



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCENTER:      Print string directly to video buffer, centered horizontally

Parameters:   TextToPrint$, screenrow, colorattribute

              TextToPrint$ is a normal ASIC text string; Screenrow is
              the row on the screen where you want the text to appear,
              and Colorattribute is the color you want the text to be.
              TCENTER calculates the correct column to center te string
              on the screen.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  Center a warning message at the bottom of the screen.  I already
REM  know that the screen has been set in a 43-row Hercules RAMFont mode.

        call sub "tcenter", warning$, 43,12



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCLEAR:       Clear entire screen

Parameters:   colorattribute

              Clears the entire screen using " " character and color as
              specified by colorattribute.

Restrictions: Text mode only.  Supports all ASILIB screen dimensions.

Example:

        colorattribute = &hex0107
        call sub "tclear", colorattribute



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TCOPY:        copies one page of text-mode video memory to another page

Supports:     all ASILIB text modes, pages 0 - 15; includes CGA snow control

Parameters:   frompage, topage, errcode

              Copies from frompage to topage.
               returns errcode=0 if no problem
                       errcode=&hexFF00 if frompage out-of-bounds
                       errcode=&hex00FF if topage out-of-bounds

Example:

REM  copy from page 0 to page 1
        frompage=0
        topage=1
        call sub "tcopy", frompage, topage, errcode


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TFILL:        Fill entire screen with specified character

Parameters:   ASCIIcode, colorattribute

              Fills the entire screen using the character specified by the
              ASCII code and color as specified by colorattribute.

Restrictions: Text mode only.  Supports all ASILIB screen dimensions.

Example:

        colorattribute = &hex0107
        ASCIIchar=ASC("$")
        call sub "tfill", ASCIIchar, colorattribute



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TGETCHR:      Get character and color attribute at specified screen
              position.

Parameters:   row, column, character, color attribute.

              Determines what character and color attribute are at
              (row, column).  The character returned is the ASCII
              character code, not a string.

Restrictions: Text mode only.

Example:

        row = 14
        column = 28
        call sub "tputchr", row, column, character, colorattribute
        



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPRINT:       Print string directly to video buffer.

Parameters:   TextToPrint$, screenrow, screencolumn, colorattribute

              TextToPrint$ is a normal ASIC text string; Screenrow is
              the row on the screen where you want the text to appear;
              Screencolumn is the column on the screen where you want
              the text, and Colorattribute is the color you want the
              text to be.  TPrint may be used to print on any part of
              any text-mode screen; it is not limited to ASIC's 25-row,
              80-column screen area.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  Print a warning message at the bottom of the screen.  I already
REM  know that the screen has been set in a 43-row Hercules RAMFont mode.

        call sub "tprint", warning$, 43,1, 12



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPRINTCE:     Print string directly to video buffer, clearing to right edge.

Parameters:   TextToPrint$, screenrow, screencolumn, colorattribute

              TextToPrint$ is a normal ASIC text string; Screenrow is
              the row on the screen where you want the text to appear;
              Screencolumn is the column on the screen where you want
              the text, and Colorattribute is the color you want the
              text to be.  TPRINTCE works just like TPRINT except that
              the remainder of the row after the end of the string is
              cleared to the right edge of the screen.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

        See TPRINT.



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

TPUTCHR:      Print a single character on the screen.

Parameters:   row, column, character, color attribute.

              Prints ASCII character on the screen at (row, column) using
              specified color attribute.  Note that character is the
              ASCII character code, not a string.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

        row = 14
        column = 28
        colorattribute = 12
        character = ASC("!")
        call sub "tputchr", row, column, character, colorattribute



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

VSCROLL:      scroll a portion of the screen up or down.

Parameters:   row0, col0, row1, col1, color, rows

              (Row0, col0) are the coordinates of the upper left part of
              the screen you want to scroll; (row1, col1) is the lower
              right corner.  Color = color attribute for cleared columns.
              Rows is the number of rows scrolled up or down.  Scrolls up
              if rows > 0, scrolls down if columns < 0, clears area if
              columns = 0.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to scroll the entire screen area up 3 columns
REM  assume 80-column, 25-row screen

REM  use white-on-blue color attribute

        colorattribute = &hex0107
        call sub "vscroll", 1, 1, 25, 80, colorattribute, 3



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WCLEAR:       clear a rectangular portion of a text-mode screen

Parameters:   row0, col0, row1, col1, colorattribute

              (Row0, col0) are the coordinates of the upper left part of
              the screen you want to clear; (row1, col1) is the lower
              right corner.  Color = color attribute for the cleared area.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to clear from row 3, column 3 to row 20, column 62
REM  using white-on-blue color attribute

        colorattribute = &hex0107
        call sub "wclear", 3, 3, 20, 62, colorattribute


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WFILL:        fill a rectangular protion of a text-mode screen with
              specified character and attribute; variation of WClear

Parameters:   row0, col0, row1, col1, colorattribute, asciicode

              (Row0, col0) are the coordinates of the upper left part of
              the screen you want to clear; (row1, col1) is the lower
              right corner.  Color = color attribute for the cleared area.
              Asciicode is the ASCII character code for the character
              you want to fill the area with.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to fill from row 3, column 3 to row 20, column 62
REM  using white-on-blue color attribute and character "*"

        colorattribute = &hex0107
        i = ASC("*")
        call sub "wfill", 3, 3, 20, 62, colorattribute, i



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WFRAME:       draw a border around a part of a text-mode screen

Parameters:   row0, col0, row1, col1, colorattribute, asciicode

              (Row0, col0) are the coordinates of the upper left part of
              the screen you want to draw a border around; (row1, col1) is
              the lower right corner.  Color = color attribute for the
              border.  Colorattribute is the color you want the border
              to be.  Asciicode is the ASCII character code for the character
              you want to use for the border.  There are 2 special border
              types: if asciicode = 0, a single line is used, and if
              asciicode = -1, a double line is drawn.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to frame from row 4, column 4 to row 19, column 61
REM  using white-on-blue color attribute and a single-lined border.
REM  I need to draw the border OUTSIDE the area I want framed.

        colorattribute = &hex0107
        i = 0
        call sub "wframe", 3, 3, 20, 62, colorattribute, i



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WPAINT:       replace all color attributes in a window of the screen
              Any text or other information in the window will not be
              changed; only the color is changed.

Parameters:   row0, col0, row1, col1, colorattribute

              (row0, col0) are the coordinates of the upper left corner of
              the area you want to change, (row1, col1) are the coordinates
              of the lower right corner of the are you want to change.
              Colorattribute is the color you want the area changed to.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to change the color from row 3, column 5 to row 20, column 60
REM  to bright red on a blue background.

        colorattribute = &hex010C
        call sub "wpaint", 3, 5, 20, 60, colorattribute



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WRECOLOR:     change selected color attributes in a window of the screen

Parameters:   row0, col0, row1, col1, oldcolor, newcolor

              (row0, col0) are the coordinates of the upper left corner of
              the area you want to change, (row1, col1) are the coordinates
              of the lower right corner of the are you want to change.
              Oldcolor is the color you want to be changed; newcolor is the
              you want oldcolor in that window changed to.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I want to change yellow-on-black color attributes from row 3, column 5
REM  to row 20, column 60 to bright red on a blue background.

        oldcolor = &hex000E
        newcolor = &hex010C
        call sub "wrecolor", 3, 5, 20, 60, oldcolor, newcolor




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WRESTORE:     restore a portion of a text-mode screen from a buffer
WSAVE:        save a portion of a text-mode screen to a buffer
              (handy when using pop-up windows on the screen)

Parameters:   bufferseg, bufferoffset, row0, col0, row1, col1

              Bufferseg is the segment address of the buffer you want to
              use to save the screen portion.  Bufferoffset os the offset
              portion of the buffer's address.  (row0, col0) are the
              coordinates of the upper left corner of the screen window
              and ((row1, col1) are the coordinates of the lower right
              corner of the screen window.  WSave and WRestore use the
              same parameters; WSave copies from the screen to the buffer
              while WRestore copies from the buffer to the screen.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:

REM  I'm going to pop up a message window on the screen so I want
REM  to save the area of the screen where the message box is going
REM  to be 'cuz I want to make the message box disappear as quickly
REM  as it appeared.

        call sub "wsize", row0, col0, row1, col1, bytes
        longbytes& = bytes
        call sub "allocdos", longbytes&, bufferseg

REM  According to ASILIB documentation, memory blocks allocated with
REM  AllocDOS start at bufferseg:0
REM  thus bufferoffset = 0
        bufferoffset = 0
        call sub "wsave", bufferseg, bufferoffset, row0, col0, row1, col1

REM  now the program does its thing to the screen and waits for the humanoid
REM  staring at the screen to push either the "Y" or "N" key.

        call sub "yesno", keycode
REM  Having received an answer, the program may now clean up the screen.
        call sub "wrestore", bufferseg, bufferoffset, row0, col0, row1, col1




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

WSIZE:        calculate the memory required to save a screen window

Parameters:   row0, col0, row1, col1, bytes

              As with all other ASILIB text-mode Window subroutines, the
              row and column coordinates define the corners of the window.
              Bytes = the size of the buffer required to store this portion
              of the screen.

Restrictions: Text mode only; any screen dimensions supported by ASILIB.

Example:
        See example for WSave, WRestore.