Paul Wheaton of Banana Programming has done a thorough study of the
conflicts between the ANSI standard and ANSI music codes.  Bloomunit
wishes to strongly endorse the changes he suggests in the below
BANSI.DOC, and to encourage all software authors and developers to
make the suggested modifications to their ANSI music-supporting communi-
cations programs by January 1, 1997.

The most notable of these suggestions is replacing the [M sequence for
starting ANSI music with the [N sequence, which has no conflicts at all
with the existing standard, and furthermore is easy to remember since it
relates to the  character (Ctrl N) which closes a music string.

With cooperation and united effort, those of us who use and support BBS
ANSI music can bring about a permanent change for the better, and make
it more accessible for all to enjoy.

Linda Bloom
Bloomunit BBS
April 6, 1994

--------------------------------------------------------

BANSI.DOC
copyright (c) 1994 by Paul Wheaton, Banana Programming

The ANSI-BBS industry is riddled with conflicts.  Since the true ANSI
standard has not been strictly followed, a variety of variations have
evolved.  Some have become popular.

This document spells out what BananaCom uses for it's terminal emulation: A
mish-mash of ANSI, VT100, pseudo-ANSI and pseudo-VT100 that tries to follow
what most modem services expect and use. Perhaps this will help to make
BBS's and COM programs work together with a little less research and
programming effort.

Terminal sends:

  All ASCII characters from 1 to 127 are sent as is.  If somebody wants to
  feed a special character that comes through as a character 128 through
  255, send that through too.

  ANSI terminal emulation is supposed to be a superset of the escape
  sequences used by the DEC VT100 terminal.  These required that an escape
  (ASCII 27) be sent followed by some other characters.  The following
  keystrokes are well established:

        Keystroke             Sent

        left arrow key        ESC [ D
        right arrow key       ESC [ C
        up arrow key          ESC [ A
        down arrow key        ESC [ B
        home key              ESC [ H
        end key               ESC [ K
        ^home key             ESC [ L
        ^page up              ESC [ M

        F1 key                ESC O P
        F2 key                ESC O Q
        F3 key                ESC O w
        F4 key                ESC O x

                                  ^capital "oh", not a zero

  All other keys send a zero and then the BIOS scan code.  Note that most
  com programs will use Alt-A through Alt-Z and Alt-1 through Alt-9 and
  Alt-0.  If there happens to be keys left they will be passed through.

  Function keys are your best bet and are all passed through

              Alone     Shift      Ctrl      Alt

        F1              0  84     0  94     0 104
        F2              0  85     0  95     0 105
        F3              0  86     0  96     0 106
        F4              0  87     0  97     0 107
        F5    0  59     0  88     0  98     0 108
        F6    0  60     0  89     0  99     0 109
        F7    0  61     0  90     0 100     0 110
        F8    0  62     0  91     0 101     0 111
        F9    0  63     0  92     0 102     0 112
        F10   0  64     0  93     0 103     0 113

   Some com programs use the Page Up and Page Down keys to initiate a file
   transfer although this seems to be changing - these keys are of great
   use to BBS's.

        Page Up           0  73
        Page Down         0  81
        Insert            0  82

   Note that when you press control-page-down with some terminal programs,
   they send   ESC [ H ESC [ 2 J   and a lot of BBS's simply ignore that.

        ctrl-page-down    0 118
        ctrl-end          0 117
        ctrl-left-arrow   0 115
        ctrl-right-arrow  0 116
        shift-tab         0 15

Terminal receives:

  Most ANSI terminals use a screen 80x24 - with the last line reserved for
  reporting the current status of the terminal program.  BananaCom uses
  this standard.

  There are a few ASCII characters that have a special effect on on the
  terminal:

      Dec  Hex  char   function

       7    7    ^G    beep
       8    8    ^H    destructive backspace
       9    9    ^I    tab - move to next tab column (8,16,24,32,40...)
      10    A    ^J    line feed - move down one. Scroll up if needed
      12    C    ^L    clear screen (normal attribute) & home cursor (1,1)
      13    D    ^M    return - move cursor to column 1


  Escape sequences do not have spaces in them.  Spaces have been added
  here for readability.

  Anything appearing in angle brackets is a numeric variable.  The angle
  brackets are not sent.

  ESC D    scroll up

    All of the text on the screen (or the scrolling region, if one is
    defined) is scrolled up one line.  The bottom line is filled with
    spaces colored according to the current attribute.

    Note that there is no left bracket "[" between the ESC and the 'D'.

    Example:  ESC D              scroll all text up one line

  ESC M    scroll down

    All of the text on the screen (or the scrolling region, if one is
    defined) is scrolled down one line.  The top line is filled with spaces
    colored according to the current attribute.

    Note that there is no left bracket "[" between the ESC and the 'M'.

    Example:  ESC M              scroll all text down one line

  ESC [ @    insert char

    Insert a space into the current line at the current cursor position.
    The character at column 80 is thrown out.  The current attribute is
    used for the new space.

  ESC [ <NumLines> A    cursor up

    Move the cursor up specified number of lines (default is one).

    If "ESC [ ? 6 h" has been received since last "ESC [ <var> ; <var> r"
    then the cursor will not be allowed to move beyond the top of the
    scrolling region.

    Example:  ESC [ 1 0 A        move up ten lines

    Example:  ESC [ A            move up one line

  ESC [ <NumLines> B    cursor down

    Move the cursor down specified number of lines (default is one).

    If "ESC [ ? 6 h" has been received since last "ESC [ <var> ; <var> r"
    then the cursor will not be allowed to move beyond the bottom of the
    scrolling region.

    Example:  ESC [ 1 0 B        move down ten lines

    Example:  ESC [ B            move down one line

  ESC [ <NumCols> C    cursor right

    Move the cursor right specified number of lines (default is one).

    Example:  ESC [ 1 0 C        move right ten columns

    Example:  ESC [ C            move right one column

  ESC [ <NumCols> D    cursor left

    Move the cursor left specified number of lines (default is one).  Cannot
    move beyond left of screen.

    Example:  ESC [ 1 0 D        move left ten columns

    Example:  ESC [ D            move left one column

  ESC [ <Num> E    line feed

    Convert to specified number of line feeds.  If the cursor is at the
    bottom of the screen (or scrolling region if one is defined) text will
    be scrolled up and the bottom line will be cleared.

    Example:  ESC [ 1 0 E        convert and process as ten linefeeds

    Example:  ESC [ E            convert and process as onr linefeed
                                 (why not just send ^J ?)

  ESC [ F    undefined
  ESC [ G    undefined

  ESC [ <row> ; <col> H    move to

    Move cursor to this position.

    If "ESC [ ? 6 h" has been received since the last
    "ESC [ <var> ; <var> r" then the cursor will be positioned relative to
    the scrolling region.

    This will perform exactly the same as "ESC [ <row> ; <col> f".

    Example:  ESC [ 1 0 ; 5 H    The cursor will be positioned at row 10
                                 and column 5.

    Example:  ESC [ 10 H         The cursor will be positioned at row 10
                                 and column 1.

    Example:  ESC [ H            The cursor will be positioned at row 1
                                 and column 1.

  ESC [ I    undefined

  ESC [ <type> J    clear all or part of display

    Clear all or part of the screen (or scrolling region if one is
    defined).

    The cleared region will always be the "normal attribute" although
    future text will use the last set attribute.

    Cursor does not move.

    Example:  ESC [ 0 J          Clear from cursor to end of screen

    Example:  ESC [ 1 J          Clear from beginning of screen to cursor

    Example:  ESC [ 2 J          Clear whole screen
                                 (note that sending ^L does the same thing)

    Example:  ESC [ J            same as "ESC [ 0 J"

  ESC [ <type> K    clear all or part of current line

    The cleared region will always be the "normal attribute" although
    future text will use the last set attribute.

    Cursor does not move.

    Example:  ESC [ 0 K          Clear from cursor to end of line

    Example:  ESC [ 1 K          Clear from beginning of line to cursor

    Example:  ESC [ 2 K          Clear whole line

    Example:  ESC [ K            same as "ESC [ 0 K"

  ESC [ <num> L    insert line

    "<num>" blank lines will be inserted at the current cursor location.
    These lines will have the color of the current attribute.  The previous
    current line and all of the lines below will be moved down.  Lines that
    are scrolled beyone the bottom of the screen (or scrolling region, if
    one is defined) will be lost.

    Example:  ESC [ 1 0 K        insert ten lines

    Example:  ESC [ K            insert one line

  ESC [ M    ANSI Music / delete line

    This is the biggest conflict in ANSI emulation.  The actual ANSI
    standard clearly states that this sequence is to be used for "delete
    line".  The person that came up with "ANSI music" must not have known
    this.  There are still many modem services and mainframe computers that
    depend on this being "delete line" - however, far more people are
    served by systems that depend on this being "ANSI music".

    What this means is that as a programmer, you cannot depend on ESC [ M.
    Some modem service and com programs will lock up when they expect one
    thing and receive another.

    Here is a solution:

        a)  A modem service can send "ESC [ b" to the terminal.  If the
        emulation outlined in this document is supported, 000 will be sent
        back.  If it is not, the terminal will most likely not show the
        escape sequence and you can then know that ESC [ M should be
        avoided since its interpretation is unknown and could cause a
        lockup.

        b)  Use "ESC [ N" for music and "ESC [ Y" for delete line.

    What BananaCom supports for ESC [ M may change although at the time of
    this writing, it is used for ANSI music.  See "ESC [ N" and "ESC [ Y"
    for information on how to use ANSI music and delete line.

  ESC [ N <music codes> <^N>  ANSI music (formerly unused)

    This command is provided with BananaCom as a substitute to the
    traditional ANSI music sequence of "ESC [ M" since that sequence has
    conflicts.

    For complete information on how to use ANSI music, look for the file
    BBSAMT*.* (BBS ANSI Music Tutor) by Linda Bloom.  This file is
    available on the Montana Banana BBS (406)543-8234 and Bloomunit BBS
    (407)687-8712.

    Example:  ESC [ N E 8 G 8 G 8 G 8 F 4 E 8 G 2 ^N    this will belt out
    the first few notes of "Popeye the Sailor".  "ESC [ N" starts the music
    sequence and the control-N character finishes.  What's in between are
    all of the notes and how long each note lasts.  Further details of the
    music may be provided as specified in BBSAMT.

    Note that this is not an ANSI standard, but something that is in
    BananaCom.  Other COM program folks are welcome to do the same.

  ESC [ O    undefined

  ESC [ <num> P    delete char

    Delete the character at the current cursor position.  All characters to
    the right of the cursor will be shifted one to the left.  The right
    most character on the screen will be converted to a space and will have
    the same attribute as the character that used to be there.

    Example:  ESC [ 1 0 P        delete ten characters

    Example:  ESC [ P            delete one character

  ESC [ Q    undefined
  ESC [ R    undefined

  ESC [ S    scroll up

    see ESC D

  ESC [ T    scroll down

    see ESC M

  ESC [ U    clear

    Clear the screen with the "normal" attribute and home the cursor.
    New text will use the previously defined attribute.

  ESC [ V    undefined
  ESC [ W    undefined
  ESC [ X    undefined

  ESC [ <num> Y    delete line

    This command is provided with BananaCom as a substitute to the
    traditional delete line sequence of "ESC [ M" since that sequence has
    conflicts.

    "<num>" lines will be deleted at the current cursor location.
    Lines from below will be scrolled up.  The blank lines inserted at the
    bottom of the screen (or scrolling region, if one is defined) will be
    colored with the current attribute.

    Example:  ESC [ 1 0 Y        delete ten lines

    Example:  ESC [ Y            delete one line

    Note that this is not an ANSI standard, but something that is in
    BananaCom.  Other COM program folks are welcome to do the same.

  ESC [ Z    back tab

    Relocate the cursor to the previous tab.  Tabs are located at columns
    1, 8, 16, 24, 32, 40, 48, 56, 64, 72 and 80.  So, if your cursor is
    currently located at column 10 and a "ESC [ Z" is received, the cursor
    will be moved to column 8.

  ESC [ a    undefined

  ESC [ b    Banana ANSI?

    If a terminal uses everything listed in this document, it will send
    back

          000

    later versions may return  001  or  002  or  003   etc.

    Note that this is not an ANSI standard, but something that is in
    BananaCom.  Other COM program folks are welcome to do the same.

  ESC [ c    VT100 query response

    Some modem services use anal retentive computers that send this and are
    looking for some unique response or they will assume your terminal is
    brain dead.  BananaCom sends back "ESC [ ? 1 ; 2 c" and that seems to
    keep most machines happy.

  ESC [ d    undefined
  ESC [ e    undefined
  ESC [ f    undefined
  ESC [ g    undefined

  ESC [ h    set options

    There are only two options here, both include sending an actual
    question mark as part of the sequence:

       ESC [ ? 6 h     certain functions which normally ignore the
                       scrolling region, will now operate relative to the
                       scrolling region.  Note that those functions will
                       again ignore the scrolling region the next time the
                       scrolling region is changed.

       ESC [ ? 7 h     Auto word wrap is turned on (it is normally on -
                       this is provided in case you turn it off).

  ESC [ i    undefined
  ESC [ j    undefined
  ESC [ k    undefined

  ESC [ l    set options

    There are only two options here, both include sending an actual
    question mark as part of the sequence.  These compliment the "ESC [ h"
    sequences.  Note that these seqences end with a lowercase L:

       ESC [ ? 6 l     Negates "ESC [ ? 6 h".  This is the default.

       ESC [ ? 7 l     Auto word wrap is turned off.  Note that the next
                       time you change the scrolling region, word wrap will
                       be turned on again.

  ESC [ <num> ; <num> ; ... m    set video attributes

    Set the foreground color, background color and blink attributes for
    future text.  Note that each number may overwrite or enhance a previous
    number.  There are four basic attributes:

         Foreground color:  8 colors

                   Bright:  On or off

         Background color:  8 colors

                 Blinking:  On or off
                                                 Effects

    Possible numbers to pass:                  FC Br BC Bl

       0  "normal": gray on black, no blink     x  x  x  x
       1  bright foreground                        x
       2  regular (non-bright) foreground          x
       4  underscore if available               x
       5  Blink on                                       x
       6  Blink on (yup, same as 5)                      x
       7  reverse                               x     x
       8  invisible text (fore=back)            x  x     x
      30  black (+Br=dark gray)                 x
      31  red (+Br=bright red)                  x
      32  green (+Br=bright green)              x
      33  brown (+Br=yellow)                    x
      34  blue (+Br=bright blue)                x
      35  magenta (+Br=bright magenta)          x
      36  cyan (+Br=bright cyan)                x
      37  gray (+Br=white)                      x
      40  black                                       x
      41  red                                         x
      42  green                                       x
      43  brown                                       x
      44  blue                                        x
      45  magenta                                     x
      46  cyan                                        x
      47  gray                                        x

    Examples:

      ESC [ 0 ; 1 ; 3 3 m        yellow on black with no blink

      ESC [ 3 3 m                use same background as before.
                                 no change to blink attribute.
                                 foreground is either brown or yellow
                                 depending on the bright attribute.

      ESC [ m                    use "normal" attribute - gray on black,
                                 no blink.

  ESC [ 6 n    report current cursor location

    If the cursor is located in the lower-right corner of the screen,
    BananaCom will respond "ESC 2 4 ; 8 0 R".  Many modem services will
    send "ESC [ 6 n" before asking a user what their name is.  When the
    response is given, the modem service knows that the calling computer
    supports ANSI terminal emulation.

  ESC [ o    undefined
  ESC [ p    undefined
  ESC [ q    undefined

  ESC [ <top> ; <bottom> r    set scroll region

    Define a region of the screen for scrolling.  This is usually used for
    full screen text editors.  Some information can be stored on some parts
    of the screen that will remain for the entire editing session - such as
    what keys you push to indicate that you are done editing.  The scroll
    region will be where the user types the text of their message.  Some
    commands (escape sequences) always ignore the scrolling region; some
    default to ignoring the scrolling region, but can work relative to the
    scrolling region when the "ESC [ ? 6 h" sequence is sent; some always
    work relative to the scrolling region if one is defined.

    Example:  ESC [ 2 ; 2 3 r    leave the first and last lines out of
                                 the scrolling region.

    Example:  ESC [ 5 r          the first four lines are left out of the
                                 scrolling region.

    Example:  ESC [ r            turn off scrolling region

  ESC [ s    save current cursor position

    The current cursor position is stored and can be reset with
    "ESC [ u"

  ESC [ t    undefined

  ESC [ u    restore cursor position from last save

    Restores the cursor position that was stored with "ESC [ s"

  ESC [ v    undefined
  ESC [ w    undefined
  ESC [ x    undefined
  ESC [ y    undefined
  ESC [ z    undefined

The information in this document is for programmers writing all sorts of
communications software - whether BBS's, door programs, or terminal
emulation programs.  If you use this, I hope you mention "Banana ANSI" in
your documentation.