Terry Bohning
11851 NW 37 Place
Sunrise, FL 33323

Compuserve [71036,1066]
original: 11/4/88


Rev. 1: 11/8/88
Corrected an error in the DEBUG source
was:
or     byte ptr [0411],16      ;game port indicator is bit 4 of high byte
changed to
or     byte ptr [0411],10      ;game port indicator is bit 4 of high byte
since DEBUG uses hex, not decimal.

Note that JOYFORCE.COM was OK, just the doc was wrong.



        Force System Recognition of Joystick 

Recently I fired up my AT clone's game port for the first time since
I purchased it and discovered that Striker, one of my favorite
public domain games, would not work with a joystick.  

After  quite a few hours of work, I found that the DOS 
Equipment Check Call (INT 11H) was saying that there was 
no game port!  I examined my old XT BIOS source code and 
found that the equipment flag is a word stored at 00:0410.
Bit 12 of the word signifies whether there is a game port
or not.  

The BIOS sets this at power up based upon whether there is a 
stick attached to the port or not. So if you boot up without
your stick attached, you don't have a game port.

Well, in my case, it didn't seem to matter whether the stick
was there at power-up or not, it just didn't work.

I keyed the program shown below in under DEBUG (minus
the comments of course) , saved it as JOYFORCE.COM 
and now Striker works fine.  

C>DEBUG
-a100
xor    ax,ax                   ;equipment flag is in segment 0
mov    ds,ax                   ;set Data Segreg to 0
                               ;high byte of equipment flag is at 0x411
or     byte ptr [0411],10      ;game port indicator is bit 4 of high byte
int    20                      ;terminate program

-rcx
CX 0000
:0b
-njoyforce.com
-w
Writing 000B bytes
-q
C>
/********************* EOF *************************/