MKey


                                                            Version 1
                                                                Rev 0


        by Gary Chanson
        (C) 1991


            MKey and MCONFIG are Copyright 1991 by Gary Chanson and
            Starquest Systems.  No restrictions  are placed  on the
            use or copying of these programs,  except that they may
            not be used  for commercial purposes without a license.


    Description:

        MKey is an event handler for the PC mouse which translates mouse
        events  such as  movement  and  button presses  into  keystrokes
        usable by application software.  MKey installs a tiny (less than
        600 bytes)  resident program  attached to your mouse driver.  It
        is re-configurable and removeable.  It can be also be re-enabled
        if an application disables it.

        MKey  can  generate  any  scan code  a  keyboard  can  generate.
        Keystrokes  can  be generated  on any  movement, on pressing  or
        releasing either button, or on pressing both buttons  (the third
        button  on three  button mice  is not  supported).  The  scaling
        factor for movement is also customizable.

        MKey can read its configuration  from a data file and comes with
        a  configuration  program  (MCONFIG.COM)   which  produces  MKey
        configuration files.

        MKey saves  the state of the mouse driver event handler  when it
        is loaded  and  restores it  when removed.  This feature  can be
        used  to  shield  programs  which  use  the  mouse   from  being
        de-activated  by  other programs  which might  be executed  from
        within it.

        MKey  can  be  used  within  multitasking  environments  such as
        DESQview (tm)  from  within  several windows  simultaneously, as
        long as it is installed after the multitasker is running, and in
        each window which it will be used within.


    Usage:

        MKey must be loaded  before any application with which you would
        like to use the mouse.  If you have created a configuration file
        for your application, its name (and path)  should be included in
        the command tail.   For instance, if your application is  QEDIT,
        and you have  a configuration file called  QEDIT.MKC  located in
        C:\UTILS, the command would look like:

            MKEY C:\UTILS\QEDIT.MKC

        After using  QEDIT, run  MKey again, and replace  the  file name
        with  the `R' switch  (/r or -r)  to remove  the resident  event
        handler.

        If you use  several applications, you can run MKey  between them
        to re-configure  it for  each application.  You  do not  have to
        remove it until you are done.  Each time it is run, it will look
        for the resident event handler, and the re-configuration will be
        performed on it.  Note that MKey can not search upper memory for
        the resident event handler.

        You can force MKey to ignore any resident event handler already
        installed by using the `N' switch.  This allows for nesting one
        application within another without interference.

        Running MKey  with no options  or file names  will re-enable the
        current configuration without changing it.  This is useful if an
        application  which already uses the mouse is run, and leaves the
        mouse driver disabled.  The `D' switch is useful  when the mouse
        might interfere with the operation of an application.  MKey will
        remain disabled until run again.

        The `Q' switch suppresses display of error messages.

        Running MKey with the `?' switch  displays a help screen and the
        revision level.

        If  you  are running  MKey  from a  batch file (most likely, you
        are), you  can use  ERRORLEVEL  to  test for  MKey  errors.  See
        "Error levels" for a listing of codes returned.  Your batch file
        might look like this:

            MKEY c:\utils\qedit.mkc
            IF ERRORLEVEL 1  QUIT

            QEDIT %1 %2 %3 %4

            MKEY -r


    Configuration:

        MKey comes with a configuration program called MCONFIG.  MCONFIG
        generates  configuration files which MKey  can read to setup its
        configuration  for  each  application.  To  create  or  modify a
        configuration file,run MCONFIG with the file name as its command
        tail.  If the file name  does not have an extension, the default
        extension `.MKC' will be used.  Running MCONFIG without any tail
        displays  a brief  help screen.  To modify (or create)  the file
        QEDIT.MKC in C:\UTILS enter:

            MCONFIG c:\utils\qedit

        MCONFIG displays a menu of all of MKey's configurable parameters
        and displays  their current settings.  For each of the 9 events,
        the name of the key assigned is shown (disabled events are shown
        as `[disabled]').  The scale factors for vertical and horizontal
        movement  are also shown.  Movement scale factors  are displayed
        in "Mickeys per character".

        To change  a setting,  press  the  hot key  for the  appropriate
        function.  MCONFIG  will prompt you  for a key to assign to that
        function.   You  can enter  any key  or key combination  at this
        prompt.  To disable a function, enter `ctrl @' (this key can not
        be entered by MCONFIG, but can  be patched  into data files with
        DEBUG  or a hex editor).  To modify  the movement scale factors,
        select  the  `V' or `H'  choices  from  the  menu.  You  will be
        prompted  for a  new  setting.  Numbers  are  assumed  to be  in
        decimal unless prefaces with a `$'.

        When you have completed modifications to the configuration file,
        press  `X'  to  save  the  file  and  exit  MCONFIG.   To  abort
        modifications,  press `Q'  to quit MCONFIG  without saving file.


    Switches:

        -d      Disable event handler
        -n      Nest event handlers
        -r      Remove event handler
        -q      Quiet; suppresses display of error messages
        -?      display help screen


    Error levels:

        0       no error
        1       configuration file not found
        2       un-recognized option switch
        3       no resident handler found (not removed)
        4       no mouse driver found


    Patching:

        The format of MKey configuration files is the same as the format
        of MKey's parameter table.  The parameter table is located at an
        offset of 3 bytes  in the MKEY.COM file (address 103H in DEBUG).
        Each event has a 2 byte entry in the parameter table.  The first
        byte is the ASCII code  and the second byte is the scan code  of
        the keystroke  which  will  be feed  into the  keyboard  buffer.
        Vertical and horizontal  movement scale factors  are each one 16
        bit word.  The table has 11 entries totaling 22 bytes.

          offset    default   key     function
            00      4800H     up      movement up
            02      5000H     down    movement down
            04      4B00H     left    movement left
            06      4D00H     right   movement right
            08      0000H             left button press
            10      000DH     enter   left button release
            12      0000H             right button press
            14      001BH     esc     right button release
            16      3B00H     F1      both buttons pressed
            18        24              vert speed (mickeys/char)
            20        24              horz speed (mickeys/char)


    -----------------------------------------------------------------------

            Please forward all comments and bug reports to:

                Gary Chanson

                360 Waltham Street
                West Newton, MA  USA  02165-1732

                Voice:  617-527-7206

                Email:  BCS-IBM BBS - 617-332-5584



         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 4,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                             MC/Visa/AmEx/Discover

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.