Installing KYBD.BUF is automatic when you type INSTALL {drive}:
This is covered in README.1ST.  
 
KYBD.BUF has five switches that may be set at bootup time (if you don't like 
        the default values) by putting them on the line DEVICE=KYBD.BUF in 
        CONFIG.SYS.  BE SURE to leave a blank space after "... .BUF", then put 
        a "/", the first letter of the command, and the number to which you 
        wish to set the parameter.  For example, the line: 

                DEVICE=KYBD.BUF /b35/R3/V1/W1
                               ^ blank space
        
        will set the keystroke buffer size to 35 (/b35, default is /b48), place 
        the buffer window on line 3 of the display (/r3, default is /r1), opens 
        the window as soon as KYBD.BUF is loaded (/v1, this is the default), 
        and attaches the code and storage for a warm boot (the default is NO 
        warm boot). 
       
        * /V0 closes the view-port to the keystroke buffer on bootup.  The 
          view-port may be reopened by pressing KEYPAD 5, V after PKII.MOD has 
          been loaded (unless the /N1 switch has been set, see below).

NOTE: If you are a registered user, and the view-port causes "snow" to appear 
on your screen, ask for KYBD.SNO, a version of KYBD.BUF that suppresses "snow". 

        * /Bn, n = 16 to 255, sets the maximum number of keystrokes held in the 
          extended keystroke buffer

        * /Rn, n = 1 to 25, tells KYBD.BUF what line on the display you want 
          the WINDOW to appear. 

        * /N1 disables the view-port and warm boot, and replaces that code and 
          storage with the buffer contents.  This saves 112 bytes (382 bytes if 
          warm boot was attached). 

        * /W1 attaches the code and storage necessary for SCROLL LOCK, F1 to 
          perform a warm boot.  Normally, it is not attached.
 
IF you have chosen to use the view-port and attach the warm boot code and 
        storage, KYBD.BUF uses only 398 bytes, plus twice whatever length the 
        buffer is.  KYBD.BUF will operate just fine whether POWERKIT II is 
        loaded or not (but then, its fast warm boot routine would have to be 
        accessed by a far jump to offset 0Eh in KYBD.BUF's segment) 
       
NOTE: The luxury of POWERKIT II's extended keystroke buffer may have to be 
        foregone in some cases.  Unfortunately, some programmers think the only 
        buffer the BIOS (Basic Input Output System) supports is the small buf-
        fer at 40h:1Eh.  Their programs use this buffer exclusively, thus ig-
        noring the buffer whose dimensions the BIOS reads at 40h:80h.  You will 
        know when you encounter such a program and POWERKIT II's buffer is set 
        to more than 15 keystrokes, because your machine will hang and not even 
        KEYPAD 5-ESC (described in PKII.DOC, page 6) will save you, and POWER-
        KIT II's fast warm boot (SCROLL LOCK-F1) will just put you back in the 
        same fix.