HIGH MEMORY UTILITIES


                This disk contains several utilities, some of which are 
        general purpose utilities, and others are designed to work with 
        high memory.  High memory is defined as that memory between the 
        DOS 640K and the ROM BIOS at the top of the PC's address space.

                In the normal PC, this memory is simply non-existent.
        Memory may be added, or accessed, in a variety of ways:

                1.      Some clones make this memory available.  I guess
                        the reason is that it is easier to manufacture a
                        motherboard with three rows of 256K chips (768K)
                        than it is to make four rows, two with 256K's and
                        two with 64K's (to give 640K).

                        If they have done this, it is quite easy to jigger
                        the addressing so that the extra 128K (768 - 640)
                        shows up as available memory.  This is usually
                        addressed at the D000 and E000 portions of memory.

                2.      There were some commercial boards manufactured by
                        IBM and others which could have their DIP switches
                        set to make the memory available pretty much any
                        where you wanted.  Though these boards are obsolete,
                        several mail order houses sell them and they often
                        show up in flea markets, swap meets, etc.

                3.      With current memory technology, it is fairly easy
                        to make a board at home which will provide the
                        required memory, and provide other advantages as
                        well, such as the ability to back it up with a
                        battery.

                4.      Even if none of these avenues is open to you, you
                        may still have some 'free' memory available if you
                        are using a Hercules or clone video card, or a CGA
                        card.  See the file HERCUSER.DOC on this disk.

                The above options were discussed in more detail in the 
        author's article "Filling in the holes on the XT" in Micro 
        Cornucopia magazine for January 1990, Issue # 52.


                                  THE UTILITIES


                The utilities included on this disk are as follows:


        EDISK.BIN               A Ramdisk which uses the 128K in the
                                D and E blocks.  It will retain its
                                contents after a warm-boot. Depending
                                on your computer's BIOS, it may even
                                survive a reset.  Will not survive a
                                power off/on sequence, however.

        EDISK-S.BIN             Similar to the above program, but
                                must be used with the home-made memory
                                board.  This board uses static RAM and
                                it may be backed up with a battery.
                                This RAMdisk will survive a power off.

        HILOAD.COM              A utility to load memory-resident programs,
                                (TSR's) such as SideKick, in upper memory, 
                                thus freeing up your DOS memory for larger
                                application programs.

        ZERORAM.COM             Small utility to zero out a block of
                                memory.  Used to initialize non-DOS
                                memory to prevent parity check errors.

        DIAGS.EXE               A public-domain utility by Joan Riff.
                                Very nice for 'hackers' to nose around
                                in the PC to see what's going on.  I
                                used this extensively in developing
                                HILOAD to keep track of the interrupt
                                vectors.

        MAPMEM.COM              Another public domain utility.  Gives
                                a map of what's loaded in your computer
                                and other information.

        RMAP.COM                Similar to MAPMEM, but is memory resident
                                (and can be HILOADed). Very useful.

        VIDEOTSR.COM            A small utility that looks at the 
                                interrupt vector table to see if you
                                have loaded any TSR's there.  Meant to
                                be used by batch files to see if it's OK
                                to go into graphics mode.

        MEMPEEK.COM             A utility to examine the entire 1 MB of
                                the PC memory.  Handy for poking around
                                in memory.

        MEMPEEKC.COM            Same as MEMPEEK, but with de-glitching
                                code for use on some CGA monitors.  It
                                is slower, so don't use it unless you
                                have to.