SPEED.COM


         This program compares the microprocessor and memory
         operations in your computer with the "standard" IBM/PC.
         Peter Norton's Norton Utilities has a routine called SI
         (SYSINFO.COM) that attempts to measure the performance of a
         compatible against an IBM/PC.  This program expands upon that
         idea and gives a more complete showing of what the actual
         performance of a machine may be in "real world" applications.

         For a fair check, you should boot from the DOS disk so that
         no extra device drivers are installed (that use interrupts
         and slow things down).  With the standard IBM/PC, each of the
         operations indicated will show 100% (or nearly so).  Any
         slight difference is due to asynchronism between the programs
         operation and the system clock.

         The response from my "turbo-XT" looks like this:

         Checking memory block write   ticks: 129 compared to IBM/PC 391%
         Checking register to memory   ticks: 262 compared to IBM/PC 187%
         Checking memory to register   ticks: 279 compared to IBM/PC 175%
         Checking register to register ticks: 326 compared to IBM/PC 169%
         Checking divide by register   ticks: 102 compared to IBM/PC 501%
         Checking divide by memory     ticks: 169 compared to IBM/PC 357%
         Checking multiply by register ticks: 115 compared to IBM/PC 418%
         Checking multiply by memory   ticks: 143 compared to IBM/PC 389%
         Checking stack operations     ticks: 248 compared to IBM/PC 179%
         Checking far jumps, far calls ticks: 309 compared to IBM/PC 167%

      Total time is: 2082 clock ticks, (115 seconds) compared to IBM/PC 247%

         This means that my system is 247 percent faster than an
         IBM/PC.  Note that memory operations (stack, register to
         memory, etc.) are not quite as fast as register only
         operations.  This shows that the probable bottle-neck in my
         system is memory access.  This "turbo" system runs a V-20 at
         8MHz.

         If you take this program to computer swap-meets, you can
         compare the speed of various "clones" before you purchase or
         update your system.  It can even help you negotiate for a
         better price if the speed is not quite as fast as the saleman
         says!

           Cheers,

           Dick Johnson
           SYSTOP
           Program Exchange
           3603 Chestnut Street Apt. C
           Lafayette, CA. 94549
           (415) 283-3505  data
           (415) 283-2809  voice