---------------------
                  COMMCHK (TM) and COMMSET (TM)
                          Version 90-2
                      ---------------------

                Copyright 1990 by John W. Roberts
                       All Rights Reserved

                UTILITY PROGRAMS TO CHECK AND SET
                 COMMUNICATIONS ADAPTER SETTINGS



1. INTRODUCTION

1.1 The Problems that COMMCHK and COMMSET Solve:

A  friend or client has asked you to help solve a  communications 
problem.   You  remember having difficulty  installing  a  serial 
device on your own system but that was a long time ago.   As  you 
gather  the stuff you think you'll need for the help session,  be 
sure  to  put  COMMCHK and COMMSET in your  toolbox.   These  two 
utility  programs are designed to help you install a  new  serial 
device.   They were created to overcome the deficiencies in  most 
versions of DOS in use today.  

Option  3  of  the DOS MODE command lets  you  set  the  protocol 
parameters  of an Asynchronous Communications Adapter  or  serial 
port.   For example entering,

          A> mode com1:24,n,8,1

is sets the mode of operation of COM1 to 2400 baud, no parity,  8 
databits, and 1 stopbit.  This works for COM1 and COM2 but  there 
are some problems.  

First  of all the MODE command does not provide a way to  examine 
the  current settings.  After entering "mode  com1:24,n,8,1"  you 
can't tell if it took.  This can be frustrating when you  suspect 
that  one of the programs that is supposed to talk to the  device 
sets  up its own protocol without telling you.   COMMCHK  reduces 
this  frustration.   COMMCHK reads and displays  the  baud,  data 
bits,  stop  bits  and parity settings  for  four  communications 
ports.

The second problem involves the number of comm ports supported by 
the mode command -- and DOS.  Basically, PC hardware in use today 
is  capable of supporting the use of seven or more serial  ports.  
The  mode command in some versions of PC-DOS (3.10  for  example) 
can only set the communications parameters for COM1 and COM2. You 
can't  use  the MODE command to set the parameters  for  COM3  or 
COM4, although programs such as ProComm do it all the time.  When 
you  are helping a friend or client and get an  "illegal  device" 
response to this command,

          A> mode com3:24,n,8,1

the  problem may be with the installed operating system  and  not 
the  communications  adapter.  Use COMMSET to configure  COM3  or 
COM4.   After  doing  so,  use  COMMCHK  to  "double  check"  the 
settings.

The third problem can occur when you are trying to use a PC as  a 
terminal  for  a  larger  local  computer  and  want  to  use   a 
transmission  rate  of  19,200 bps.  The mode  command  does  not 
support 19,200.  COMMCHK and COMMSET do!


1.2.  How to Use COMMCHK

To use COMMCHK type

                 [d:][path]COMMCHK

where  [d:][path] before COMMCHK specify the drive and path  that 
contains  the COMMCHK.EXE file.  In a moment or two  the  display 
will look something like this:

     ------------------------------------------------------
     C> A:COMMCHK

     COMM PORT NUMBER 1:    mode com1:2400,N,8,1
       Transmission speed:   2400
       8 Data Bits     1 Stop Bit   Parity: NO

     COMM PORT NUMBER 2:    mode com2:1200,N,8,1
       Transmission speed:   1200
       8 Data Bits     1 Stop Bit   Parity: NO

     COMM PORT NUMBER 3
       This port does not exist or is not
       set up for communications
     
     COMM PORT NUMBER 4:    mode com4:2400,E,8,1
       Transmission speed:   2400
         8 Data Bits     1 Stop Bit   Parity: Even

     C>_
     ------------------------------------------------------

Simply read and record the parameters of the port (or ports)  you 
are  investigating.  Later, when you want to see if any  programs 
or  batch files have changed the settings, run COMMCHK again  and 
compare the results.

COMMCHK  always  tries to read the communications  parameters  of 
four  communications  ports  even though fewer  may  be  present.  
Notice  the two-line error message for COM3 in  example  display.  
This  is  how COMMCHK handles the situation where the  comm  port 
does not exist, or is not set up for communications.  If you  are 
trying to configure a comm port that displays such a message, you 
can  determine which situation applies by attempting to  set  the 
parameters  using COMMSET.  If you are successful,  COMMSET  will 
display  the new settings.  If the port does not  exist,  COMMSET 
will  report the same error message and advise you that the  port 
is  missing.   You may determine the situation by first  using  a 
MODE command such as

          A> mode com3:24,n,8,1

instead  of  COMMSET.  Next run COMMCHK to see  if  the  settings 
"took."   If  the settings "take" (as indicated by  COMMCHK)  the 
port  exists.  If the same two-line error message appears  again, 
the  port probably does not exist.  If DOS responds to  the  mode 
command  with an "illegal device" message, you must  use  COMMSET 
instead of the MODE command to set that port.

It  is  possible  for COMMCHK  to  display  bogus  communications 
parameters instead of the two-line message shown for COM3.  Treat 
the  bogus  data  as an error message and  proceed  as  described 
above.

By  setting  switches or moving jumpers you  can  configure  most 
communications  adapters  as COM1, COM2, COM3, or COM4.   If  the 
port  you  need  seems to be missing, you may have  to  open  the 
computer so you can examine the boards.

Suppose you suspect your program is changing communications  port 
settings when it starts but does not restore the original  values 
when  it finishes. Prove it by installing a unique  setup  before 
running the program.  After the program stops use COMMCHK to  see 
if the program changed any of your settings.


1.3.  How to Use COMMSET

To use COMMSET type

                 [d:][path]COMMSET

where  [d:][path] before COMMSET specify the drive and path  that 
contains  the COMMSET.EXE file.  COMMSET uses  interactive  input 
routines  that suggest an appropriate response to each  question.  
The first "screenfull" of questions looks something like this:

     ------------------------------------------------------
                *** Sets Comm Port Parameters ***

     Set parameters on port number= 4            <--- a

     COMM PORT NUMBER 4:  mode com1:2400,N,8,1   <--- b
       Transmission speed:   2400
       8 Data Bits  1 Stop Bit   Parity: NONE

     Is this the one you want to change? YES     <--- c
     ------------------------------------------------------

After  the screen clears and the title appears, line "a"  appears 
in  the form of a question: "Set parameters on port  number?  1."  
You  may  accept  the suggested answer, "1"  by  simply  pressing 
Enter.   The  example shows the result of selecting  a  different 
port.   After overrstriking 1 with 4 and pressing Enter,  COMMSET 
changes the question mark to an equal sign to indicate acceptance 
of  your choice. Next the settings for port 4 appear starting  on 
line  "b."  The question on line "c" is COMMSET's way  of  asking 
you to confirm or approve your choice of ports to change.  Accept 
the  "YES"  answer  by pressing ENTER and the  next  screen  will 
appear.   Overstrike  the YES with "n", "no",  "x",  or  anything 
other that "YES" you start over again with line "a."

     ------------------------------------------------------
                 *** Enter the New Settings ***

             1       110   Baud                <--- d
             2       150   Baud
             3       300   Baud
             4       600   Baud
             5       1200  Baud
             6       2400  Baud
             7       4800  Baud
             8       9600  Baud
             9       19200 Baud
        Your choice= 5                         <--- e
          Data bits (7 or 8)= 7                <--- f
          Stop bits (1 or 2)= 2                <--- g
          Parity codes: N = None, O = Odd, E = Even
          Set the parity code to? N_           <--- h

     COMM PORT NUMBER 4:  mode com1:2400,N,8,1 <--- i
       Transmission speed:   2400
       8 Data Bits  1 Stop Bit   Parity: NONE

         Shall we set another one? Ok          <--- j

     ------------------------------------------------------

An  indexed table of Baud choices appears beginning on line  "d."  
On  line "e" enter the index or number of the baud rate you  want 
to  use.  As a reminder or reference the old or  original  values 
appear in the COMMCHK-like table that starts on line "i."   Enter 
your  choices  for data bits, stop bits and  parity  settings  on 
lines  "f", "g", and "h" respectively.  Line "h" (and  the  table 
starting  on  line  "i")  represent  the  situation  just  before 
pressing  ENTER in response to the parity question.   Just  after 
pressing ENTER the color of the table changes and your new values 
appear.  The question on line "j" appears.

If you accept the "Ok" answer to the question on line "j" COMMSET 
takes  you back to the "Sets Comm Port Parameters" screen so  you 
can  select  a  different  port to change.   If  you  answer  the 
question by overstriking the "Ok" with anything other than  "Ok", 
the COMMSET stops.  (You may also stop the program pressing ^C or 
entering  the  word  "abort"  (or "ABORT")  in  response  to  any 
question.)

COMMSET  checks  the validity of every entry, tells you  when  an 
illegal  value  is  found  and waits for you  to  enter  a  valid 
setting.

Here's  how  the  display looks after you've  tried  to  set  the 
parameters of a comm port that does not exist:

     ------------------------------------------------------
                 *** Enter the New Settings ***

             1       110   Baud               <--- d
             2       150   Baud
             3       300   Baud
             4       600   Baud
             5       1200  Baud
             6       2400  Baud
             7       4800  Baud
             8       9600  Baud
             9       19200 Baud
        Your choice= 5                        <--- e
          Data bits (7 or 8)= 7               <--- f
          Stop bits (1 or 2)= 2               <--- g
          Parity codes: N = None, O = Odd, E = Even
          Set the parity code to= N           <--- h

     COMM PORT NUMBER 3                       <--- i
       This port does not exist or is not     <--- k
       set up for communications.
     Somebody bad took that communications adapter!!! <--- l
     (If it can't be set, it does not exist.)         <--- m
         Shall we set another one? Ok         <--- j

     ------------------------------------------------------

In  this  case, the two-line error message starting on  line  "k" 
would appear when the port is first selected.  The content of the 
COMMCHK  table does not change when you enter your parity  choice 
in line "h."  Instead lines "l" and "m" appear to explain why the 
settings did not change.

1.4.  Development

The  original version of COMMCHK was written in Turbo  Pascal  in 
1989.   It  was  based on information found in  a  public  domain 
program   named  DUMBTERM.PAS,  created  by  Jim   McCarthy   and 
distributed  by the Turbo User Group, P.O. Box 1510, Poulsbo,  WA 
98370.  The Turbo Pascal version was published in April/May issue 
of  Tug Lines, the magazine of the Turbo User Group.  In  January 
1990,  COMMCHK  was  rewritten using  Janus/Ada.   The  code  was 
modified   to   eliminate  the  occasional   display   of   bogus 
communications port settings.  The need for a COMMSET utility was 
recognized.   Communications  routines  that  could  be  used  in 
COMMCHK  and  COMMSET  were placed in  a  package  of  "reusable" 
routines called COMMSTUF.  In February 1990, COMMSET and  COMMCHK 
were modified to handle a baud rate of 19,200.  

COMMSTUF depends on off-the-shelf library units (System and  Bit) 
provided  by  R.R. Software, P.O. Box  1512,  Madison  Wisconsin, 
developers  of the Janus/Ada compiler.  All Ada compiler  vendors 
provide  a System package and most provide one or  more  packages 
that include the types of functions and procedures found in  R.R. 
Software's Bit package.

COMMCHK is a "plain vanilla" Ada program that depends on or needs 
only  the COMMSTUF package and the standard TEXT_IO package.   It 
is  small  and  does a simple job without  any  extra  frills  or 
features.

COMMSET  depends  on  COMMSTUF and  a  few  powerful  interactive 
Ada  IO  packages  designed for use with  color  terminals  (AG6, 
PORTNUMS,  and  NUMOPS).  These packages add a variety  of  extra 
frills and features.

Ada  source code is provided for COMMSTUF, COMMCHK  and  COMMSET.  
Those  who use Janus/Ada should be able to modify COMMCHK  and/or 
reuse  the routines found in COMMSTUF in other  programs  without 
difficulty.  The packages used to add the frills and features  to 
COMMSET  are not yet ready for release.  Without these  packages, 
modifying  COMMSET  will be more difficult  but  not  impossible.  
COMMSET  source  code  contains enough  information  for  you  to 
identify the routines taken from AG6, PORTNUMS and NUMOPS.   Once 
these are replaced with routines based on TEXT_IO you will have a 
"plane  vanilla"  version  of  COMMSET.   A  comparison  of   the 
Display_setup_of_port procedure found in both COMMCHK and COMMSET 
would be a good place to start.

2.  Warranty
This  software  and  manual  are provided  "as  is"  and  without 
warranties  as  to performance of merchantability  or  any  other 
warranties whether expressed or implied.  Because of the  various 
hardware and software environments into which these programs  may 
be  put,  no  warranty of fitness for  a  particular  purpose  is 
offered.

Good  data  processing procedures dictates that  any  program  be 
thoroughly  tested with non-critical data before relying  on  it.  
The user must assume the entire risk of using this program.   Any 
liability  of the seller will be limited exclusively  to  product 
replacement or refund of the purchase price.

3.  Shareware
These utility programs are distributed as shareware.  This  means 
you  may test these programs on your system free of charge.   The 
programs are not free.  They are copyrighted software provided to 
you  to  evaluate  before  paying.  If  you  find  these  utility 
programs useful, you are encouraged to fill out the  registration 
form  (found in COMMREGS.TXT) and mail it together with  a  check 
for $10.00 to

              John W. Roberts
              P.O. Box 68453
              Virginia Beach, VA 23455-9998


These  utility programs are not the kind of tools you are  likely 
to  use on a daily basis.  I really don't expect you to  register 
just because you were able to run the programs on your  system... 
or  when  you first use them to actually solve  a  communications 
interface  problem.   Wait until the second time  you  use  these 
programs to solve a problem and then register.

If  you  develop software, there is a place on  the  registration 
form  for you to request more information about Ada  software  in 
general  and the release of the interactive IO packages  used  in 
developing COMMSET in particular.

4.  Distribution
You  are free to make copies of these programs for  yourself  and 
your friends providing you do not charge a fee to do so.   Anyone 
wishing to charge people a fee for giving them a copy of  COMMCHK 
or COMMSET must have my written authorization to do so.   Without 
this  authorization,  the  distributor  is  guilty  of  copyright 
violation.   To  obtain authorization, write to me at  the  above 
address  and  request a COMMCHK  COMMSET  distribution  licensing 
agreement.

























         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                                 MC/Visa/AmEx

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.