›4 L
                                      ESC.COM

         PURPOSE: utility to configure DOS ANSI console.
           USAGE: ESC xxxxxx
           WHERE: xxxxxx is an ANSI escape sequence.


         Escape sequences are control codes that change cursor, screen,
         keyboard, or speaker attributes.  Control codes are useful for
         customizing your PC without having to deal directly with console
         hardware.

         ANSI consoles are devices that respond to "ANSI X3.64" escape
         sequences.  American Standard terminals are ANSI console devices.
         The IBM PC is not an ANSI device and does not respond to escape
         codes until you install an ANSI "console device driver."

         DOS provides a driver called "ANSI.SYS" that responds to a subset
         of the ANSI X3.64 control codes - enough to configure your display
         and keyboard.

         Install the DOS console driver by adding the statement:
                                 device = ANSI.SYS
         to your "CONFIG.SYS" file.  Make sure DOS can find the file
         ANSI.SYS by copying it from the DOS system disk to your "working"
         system disk.  If you have a fixed disk, copy ANSI.SYS to the root
         directory of C:\.

         If you have no CONFIG.SYS file, you can create one by typing at
         the DOS prompt:
                            copy con config.sys <cr>
                            device  = ANSI.SYS <cr>
                            buffers = 24 <cr>
                            <ctrl-Z><cr>

         This file tells DOS to use the ANSI console driver - and tells DOS to
         use 12Kb of RAM to buffer disk data.  Change the number of BUFFERS to
         fine tune disk I/O.  The default disk buffer is about 2Kb.

         DOS reads CONFIG.SYS when you fire up your PC or reboot.

         ESCAPE SEQUENCES for ANSI.SYS      source: DOS Technical Reference

               ESC [#A          cursor up # lines
                                where # = number of lines to move
                                default # = 1
                                ignored at top of screen

               ESC [#B          cursor down # lines
                                where # = number of lines to move
                                default # = 1
                                ignored at bottom of screen

               ESC [#C          cursor right # columns
                                where # = number of columns to move
                                default # = 1
                                ignored at end of screen

               ESC [#D          cursor left # columns
                                where # = number of cols to move
                                default # = 1
                                ignored at beginning of screen

               ESC [r;cH        position cursor at row r column c
                                where r = 1 to 24 and c = 1 to 80
                                default r = 1       default c = 1

               ESC [r;cf        position cursor at row r column c
                                where r = 1 to 24 and c = 1 to 80
                                default r = 1       default c = 1

               ESC [6n          cursor position request - console
                                sends back cursor position report:

                    ESC [r;cR      cursor position report...
                                   where r = row and c = col
                                ...in response to ESC [6n request.

               ESC [s           save current cursor position.
                                the cursor is not moved, but its
                                position is saved by DOS


                                     ESC  page 2


               ESC [u           restore current cursor position.
                                the cursor is moved to the saved
                                row and column

               ESC [2J          clear screen - sends cursor home.

               ESC [K           erase from cursor to end of line.

               ESC [#;...;#m    set graphics rendition to #
                                where # include the following:

                                     00  =  all attributes OFF
                                     01  =  bold ON
                                     04  =  underscore (mono only)
                                     05  =  blink ON
                                     07  =  reverse ON
                                     08  =  concealed ON

                                     30  =  black   foreground
                                     31  =  red     foreground
                                     32  =  green   foreground
                                     33  =  yellow  foreground
                                     34  =  blue    foreground
                                     35  =  magenta foreground
                                     36  =  cyan    foreground
                                     37  =  white   foreground

                                     40  =  black   background
                                     41  =  red     background
                                     42  =  green   background
                                     43  =  yellow  background
                                     44  =  blue    background
                                     45  =  magenta background
                                     46  =  cyan    background
                                     47  =  white   background

               EXAMPLE:    ESC [01m               ...sets BOLD ON

               EXAMPLE:    ESC [00;37;44m         ...sets WHITE on BLUE


               ESC [=#h         set screen mode to # where # =
           or  ESC [=h
           or  ESC [=0h               0  =  40x25 BLK & WHT
           or  ESC [?7h               1  =  40x25 COLOR
                                      2  =  80x25 BLK & WHT
                                      3  =  80x25 COLOR
                                      4  =  320x200 COLOR
                                      5  =  320x200 BLK & WHT
                                      6  =  640x200 BLK & WHT
                                      7  =  wrap at end of line

               ESC [=#l         reset screen mode to # where # =
           or  ESC [=l
           or  ESC [=0l               0  =  40x25 BLK & WHT
           or  ESC [?7l               1  =  40x25 COLOR
                                      2  =  80x25 BLK & WHT
                                      3  =  80x25 COLOR
                                      4  =  320x200 COLOR
                                      5  =  320x200 BLK & WHT
                                      6  =  640x200 BLK & WHT
                                      7  =  truncate at end of line

               ESC [#;#p                          redefine keyboard:
           or  ESC [#;"string"p
           or  ESC [#;"string";#;"string";#p      The first  #  ASCII code
                                                  specifies which key is to
           or  any other combination of           be redefined.  Following
               strings and decimal numbers         #  numbers or "strings"
                                                  redefine the key to ASCII
                                                  codes and/or strings.









                                     ESC  page 3

         where  #  is the decimal number of an ASCII character:

         dec   character      dec    key      dec    key      dec    key
          0    ^@    NUL       32  <space>     64     @        96     `
          1    ^A    SOH       33     !        65     A        97     a
          2    ^B    STX       34     "        66     B        98     b
          3    ^C    ETX       35     #        67     C        99     c
          4    ^D    EOT       36     $        68     D       100     d
          5    ^E    ENQ       37     %        69     E       101     e
          6    ^F    ACK       38     &        70     F       102     f
          7    ^G    BEL       39     '        71     G       103     g
          8    ^H    BS        40     (        72     H       104     h
          9    ^I    HT        41     )        73     I       105     i
         10    ^J    LF        42     *        74     J       106     j
         11    ^K    VT        43     +        75     K       107     k
         12    ^L    FF        44     ,        76     L       108     l
         13    ^M    CR        45     -        77     M       109     m
         14    ^N    SO        46     .        78     N       110     n
         15    ^O    SI        47     /        79     O       111     o
         16    ^P    DLE       48     0        80     P       112     p
         17    ^Q  DC1-XON     49     1        81     Q       113     q
         18    ^R    DC2       50     2        82     R       114     r
         19    ^S  DC3-XOFF    51     3        83     S       115     s
         20    ^T    DC4       52     4        84     T       116     t
         21    ^U    NAK       53     5        85     U       117     u
         22    ^V    SYN       54     6        86     V       118     v
         23    ^W    ETB       55     7        87     W       119     w
         24    ^X    CAN       56     8        88     X       120     x
         25    ^Y    EM        57     9        89     Y       121     y
         26    ^Z    SUB       58     :        90     Z       122     z
         27    ^[    ESC       59     ;        91     [       123     {
         28    ^\    FS        60     <        92     \       124     |
         29    ^]    GS        61     =        93     ]       125     }
         30    ^^    RS        62     >        94     ^       126     ~
         31    ^_    US        63     ?        95     _       127    DEL

         where # is the decimal number of a "special" character:

                [Library note: These characters are not printable.
                                See the ESC.DOC file on the disk.]


         IBM PC console keys are specified by an "extended ASCII" code:

                     for:     ESC [#;#;...p

              if first '#' =  0 <NUL>;
           then second '#' =  the extended ASCII coded key:

                 59 to 68  =  Function Keys  F1 to F10
                94 to 103  =     CTRL-       F1 to F10
                 84 to 93  =    SHIFT-       F1 to F10
               104 to 113  =      ALT-       F1 to F10
                       15  =  SHIFT-Tab
               120 to 131  =  ALT-  1  2  3  4  5  6  7  8  9  0  -  =
                 16 to 25  =  ALT-   Q  W  E  R  T  Y  U  I  O  P
                 30 to 38  =  ALT-    A  S  D  F  G  H  J  K  L
                 43 to 50  =  ALT-  \  Z  X  C  V  B  N  M
                       82  =  Insert
                       83  =  Delete
                       71  =  Home
                       79  =  End
                       75  =  Cursor Left
                       77  =  Cursor Right
                       72  =  Cursor Up
                       80  =  Cursor Down
                       73  =  Page Up
                       81  =  Page Down
                        3  =  NUL ( since 0 is index to this table )

               EXAMPLE:    ESC [36;156p          ...changes $ to   character
               EXAMPLE:    ESC [36;36p                 ...and then back to $

               EXAMPLE:    ESC [0;59;"DIR";13p         ...sets F1 to DIR<cr>
               EXAMPLE:    ESC [0;59;0;59p            ...and then back to F1

         You create console utilities by putting ESC commands in batch files.
         This example modifies display attributes whenever you enter BLUE...



                                     ESC  page 4


         ...at the DOS prompt> copy con blue.bat <cr>
                               esc [00;34;40m <cr>
                               <ctrl-Z><cr>

         Use ESC commands to enhance existing batch files.  This D.BAT
         displays a direcory listing using BLUE.BAT:
                                                     ___________________
                            echo off
                            blue                     ...run BLUE.BAT
                            esc [2J                  ...clear screen
                            dir                      ...display files
                            esc [00;32;40m           ...make prompt GRN

         The DOS PROMPT command can send ANSI escape sequences to your
         console.  Try the following PROMPT:

         ( mono  )     A> PROMPT $e[01m$p$g $e[00m$e[K

         ( color )     A> PROMPT $e[01;36;40m$p$g $e[00;32m$e[K

         This sequence upgrades your 'A>' DOS prompt to a bold cyan that
         shows the current directory; sets screen attributes to GRN on BLK;
         clearing the prompt line for your command.  Changes remain in effect
         until you issue another PROMPT command.  DOS PROMPT syntax includes:

                            $e   =  escape character
                            $n   =  current drive
                            $g   =  the > character
                            $p   =  current directory
                            $d   =  current date
                            $t   =  current time
                            $v   =  DOS version
                            $l   =  the < character
                            $q   =  the = character
                            $b   =  the | character
                            $$   =  the $ character
                            $h   =  backspace
                            $_   =  <cr><lf>
                            $.   =  NUL character

                          $n$g   =  default PROMPT


         Put the console configuration that suits you into the file EXEC.BAT.
         This example defines a key to run EXEC on your command:
                                                       ____________________
            echo off
            esc [=3h                                   ...80x25 color mode
            esc [=7h                                   ...autowrap ON
            esc [00;32;40m                             ...green on black
            esc [2J                                    ...clear screen
            esc [0;59;"CLS";13;"DIR";13p               F1  =  display files
            esc [0;60;"CHKDSK";13p                     F2  =  status report
            esc [0;61;"A:";13p                         F3  =  select A:
            esc [0;62;"EDIT";13p                       F4  =  run EDIT.BAT
            esc [0;63;"B:";13p                         F5  =  select B:
            esc [0;64;"CALC";13p                       F6  =  run CALC.BAT
            esc [0;65;"C:";13p                         F7  =  select C:
            esc [0;66;"COMM";13p                       F8  =  run COMM.BAT
            esc [0;67;"D:";13p                         F9  =  select D:
            esc [0;68;"EXEC";13p                       F10 =  run EXEC.BAT
            prompt $e[01;36;40m$p$g $e[00;32m$e[K      ...custom prompt

         Edit EXEC.BAT to fine tune your custom console.  Make EXEC the
         default console configuration by running it from AUTOEXEC.BAT.

         EXEC should provide a friendly environment for you to issue commands
         to the DOS prompt.  Application programs present different prompts
         to the console operator.

         Copy EXEC to create new batch files such as EDIT, CALC, and
         COMM.BAT.  These files should: configure the console for a specific
         application; run the program; and end with EXEC to reconfigure the
         console before returning to DOS.






                                     ESC  page 5

         Technical Notes:

         Because ESC.COM sends escape sequences to the "standard output"
         device, you can redirect control codes to other DOS devices, such as
         a printer.  Use DOS "console redirection" to send an escape sequence
         to LPT1:
                                  ESC xxxxxx >LPT1:

         This is useful for selecting print modes from your console;
         configuring your printer on power up; and custom printing of text
         files.  Codes are documented in your printer manual.

         You can redirect escape codes to a file.  Creative users will find
                               ESC xxxxxx >config.con
         makes a file named CONFIG.CON containing an ANSI control code.  Edit
         this file to change the escape sequence.  Send CONFIG.CON to CON:
                                   TYPE config.con
                              or   COPY config.con CON:
         ...and your ANSI console will respond to the control code in the
         file.  Copy CONFIG.CON to CONFIG.PRN and edit this file.  Send
         CONFIG.PRN to your printer with:
                                COPY config.prn LPT1:

         You could create a library of escape sequences, each a single file.
         Use your editor to insert control codes from the library into text.
         Such files display text in color at any location on the screen, or
         print text in different styles on dot-matrix printers.

         To append additional escape sequences to an existing file, use:
                               ESC xxxxxx >>config.con

         It is more efficient to copy an ANSI configuration file containing
         a string of escape sequences directly to CON: -- than it is to run
         ESC.COM many times from a batch file.

         Redirect configuration batch files to "compile" them into simpler
         files containing control code strings.  For example...
                                   EXEC >exec.con
         ....redirects everything EXEC.BAT displays > to the file EXEC.CON.
         Edit this file to delete characters that are not escape sequences.
         What EXEC.BAT used to do is now accomplished simply:

                            TYPE exec.con

         __________________________________________________________________

         ANSI.SYS is a subset of the full ANSI X3.64 standard - some console
         drivers have more features.  The most elegant ANSI is called FANSI.
         FANSI provides back-scrolling and a type-ahead buffer, and features
         high speed screen and keyboard drivers.

                            Hersey Micro Consulting, Inc.
                            P.O. Box 8276
                            Ann Arbor, MI 48107

                   voice:  (313) 994-3259   0900 to 1700 EST
                   modem:  (313) 994-3946   2300 to 0800 EST




         ------------------------------------------------------------

                   This disk copy provided as a service of

                        The Public (Software) Library

         For a copy of the latest monthly software library newsletter
          and a list of the 600+ disks in the library, call or write

                        The Public (Software) Library
                                P.O.Box 35705
                           Houston, TX 77235-5705
                               (713) 721-6104