mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
			SVGA256 GRAPHICS LIBRARY
 	     Copyright (C) 1993 by Orthware.   All rights reserved.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm


			ABOUT THE SVGA256 LIBRARY



mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
TABLE OF CONTENTS 
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

I.	Introduction to the SVGA256 library.
II.	About the VESA 256-color extended video modes
III.	Requirements for using the SVGA256 library.	
IV.	File description.
V.	Registration/Comments.
VI.	Disclaimer.
VII.	Distribution of SVGA256.
VIII.	Technical information.
		1) About text display.
		2) About windows.
		3) About saving and displaying images.
		4) About manipulating color.
	 	5) About using extended memory for data storage.
		




mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
I.	INTRODUCTION TO THE SVGA256 LIBRARY.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

	Welcome to the world of high resolution 256-color programming.  If you
are getting tired of low resolution or 16-color programming like I was then
this library should be helpful to you.   If you are new to Super VGA 256-color
programming you should find this library fairly straight forward to use without
having to know all about bank switching, segment overflow, register setting,
and some of the other quirks found when programming in the SVGA video modes.  
I tried to make it as easy to use as the standard graphics libraries that come 
with most C compilers.  If you are an experienced SVGA programmer than I hope 
some of the features in SVGA256 will be useful in expanding your abilities and 
program functionality.  In any case I hope SVGA256 is useful to you in 
developing your applications.  Good Luck in your endeavors.

	The SVGA256 library consists of routines for performing the following
functions in one of the high resolution, 256-color VESA (Video Electronics
Standard Association) video modes: 

	1. Video mode initialization and detection routines.
	2. Text display using pixel coordinates and/or col-row coordinates.
	3. Windowing (pop-up windows) routines.
	4. Screen block saving, hiding, restoring.
	5. Bitmap and "bytemap" image display and manipulation.
	6. Common drawing functions (pixels, lines, circles, polygons, ...)
	7. Color (palette) manipulation functions.
	8. Extended memory access for data storage.

	Most of the routines are fairly high level as far as programming the
video card.  The guts of SVGA video programming are hidden from the programmer
allowing the programmer to concentrate on the application at hand and not so 
much on the video bank switching, port I/O, segmentation overflow management, 
basic scan conversion algorithmics and other bit/byte twiddling that goes on 
with SVGA video programming.  

	The file s256ref.doc is a reference manual that has a description
and prototype for each of the routines in the SVGA256 library.  Printing 
s256ref.doc to hardcopy and keeping it by your side while programming can 
help you to use the library more efficiently and correctly. 


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
II.	ABOUT THE VESA 256-COLOR EXTENDED VIDEO MODES
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

	Up until the VESA (Video Electronic Standards Association) was formed 
the VGA standard was only defined for up to 640x480 resolution with 16 colors.
Video cards that came with high resolution (> 640x480) modes and more colors
were non-standardized in the way they were programmed.  Each manufacturer had
its own set of video mode numbers and methods of programming the modes, no 
doubt a true programmers nightmare.  VESA set a standard for the high
resolution modes and now most SVGA video cards today are VESA compatible or 
at least have a software driver that can be installed to make the video system 
VESA compatible.  Because of VESA we now have a standard way of programming 
these cards and the SVGA256 graphics library takes advantage of this. 

	SVGA256 should work with all VESA compatible cards or cards that have
a VESA driver.  I have tested the library using 3 different VESA video cards
from 3 different manufacturers so hopefully it is sound for all VESA compatible
video SVGA systems.  If it is not let me know about it so I can investigate and
make fixes for future versions.

	Included in this package is a utility program, VESA_CK.EXE, that will
give you information on all of the VESA video modes available for your
video card.  The program will tell you if your video card is not VESA
compatible (or it is but VESA driver isn't installed) by saying 

		"ERROR: Cannot locate VESA BIOS"  

	If your card is not VESA compatible without a driver then look at the 
drivers that came with your SVGA video card.  Look for an .EXE file with the 
name VESA in it and that is probably your VESA driver.  Run this program first 
to install the driver and then check to see if VESA_CK.EXE runs without 
complaining.  If your video card is not VESA compatible and does not have a 
driver but is capable of the SVGA resolutions/colors you may be out of luck 
with respect to using SVGA256.  The only exception is if you have a TSENG4000 
video processor on your card.  SVGA256 is designed to work with VESA 
compatible cards BUT also has routines geared to the TSENG4000 video processor 
chip when VESA compatibility is absent.   If you have a TSENG4000 chip then 
you can use the mode numbers specific to this chip listed below instead of the 
VESA mode numbers.  The following is a list of graphic mode numbers supported 
by the SVGA256 Graphics Library.


		256-color VGA mode number (supported on all Standard VGA cards)
		--------------------------------------------------------------	
		19 (13 hex) for the 320x200 pixel resolution


		256-color SVGA VESA graphic modes supported by SVGA256:
		--------------------------------------------------
		256 (100 hex) for the 640x400 pixel resolution
		257 (101 hex) for the 640x480 pixel resolution
		259 (103 hex) for the 800x600 pixel resolution
		261 (105 hex) for the 1024x768 pixel resolution
		263 (107 hex) for the 1280x1024 pixel resolution (untested)


		256-color SVGA TSENG-4000 video processor modes.
		--------------------------------------------------------
		46 (2E hex) for the 640x480 pixel resolution
		47 (2F hex) for the 640x400 pixel resolution
		48 (30 hex) for the 800x600 pixel resolution
		56 (38 hex) for the 1240x768 pixel resolution
		


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
III.	Requirements for using the SVGA256 library.	
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

1) 80386/80486 CPU - Assembly language routines use 80386 32-bit instructions.  
		     C routines were compiled with BC++ 3.1 with 80386 compile 
		     option turned ON.

2) VGA/SVGA        - The video card must be one of the following:
		     a). Super VGA card that is VESA compatible without driver.
		     b). Super VGA card that is VESA compatible with a driver. 
		     c). Super VGA card with a TSENG 4000 video processor chip.
		     d). Plain old VGA card if you only use standard VGA 
			 mode 19 (13 hex).

3) HIMEM.SYS       - Microsoft's HIMEM.SYS driver must be installed to use the 
		     extended memory access routines in the library.  The 
		     windowing routines also require HIMEM.SYS for opening and 
		     manipulating large windows on the screen.  You do not
		     need HIMEM.SYS if you do not use the extended memory
		     access routines or if you do not want to use extended
		     memory for windowing (see "About Windows" below).  

4) LARGE MEM MODEL - The SVGA256 Graphics Library was written and compiled for 
		     the LARGE memory model.


NOTE:  The SVGA256 Graphics Library has routines for checking all of these 
	 requirements except for detection of a TSENG-4000 video processor.


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
IV.	SVGA256 file description.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm


     ALL files listed under (1) and (2) below are considered to be part of
the SVGA256 library and are not to be seperated from the library during
distribution (see topic "Distribution of SVGA256").


(1) The library code (files to include with your application source code):


	SVGA256.LIB	- The library of routines making up the SVGA256 Graphics
			  Library.  Compiled using BC++ 3.1, Large Memory Model,
			  80386 Compiler Option turned on, no debugger info, 
			  other settings default. 

	SVGA256.H	- Header file for the routines in the 
			  SVGA256 Graphics Library.  



(2) Files not part of the SVGA256 code but still part of SVGA256 package.

	VESA_CK.EXE	- A utility program that reports information about
			  all of the available VESA video modes your video
			  card supports.  This program can be used to determine
			  if your card is VESA compatible.  It will also tell 
			  you if your card is not VESA compatible.  If your 
			  card is VESA compatible (either with or without VESA 
			  driver) the program will give a screen full of 
			  information on each video mode supported by your 
			  video system.  For more information on VESA video
			  programming the following 2 books are informative:

			  1) "Programmer's Guide to the EGA and VGA Cards" by
			     Richard F. Ferraro, 2nd Edition, Addison-Wesley.

			  2) "Advanced Programmer's Guide to SuperVGAs" by
                              George Sutty and Steve Blair, Brady.
			 

	S256READ.DOC	- The file you are now reading.

	S256REF.DOC	- Reference manual for the library routines.

	S256REGI.DOC	- Registration form for the SVGA256 Graphics Library.

	S256DEMO.EXE	- A program that demonstrates many of the key features 
			  of the SVGA256 library. This program is made by 
			  linking SVGA256.LIB, DEMOMSGS.C, and S256DEMO.C

	S256DEMO.C	- Source code of the demonstration program.  Look at 
			  this for examples on how SVGA256 can be used.

	DEMOMSGS.C	- Useful routines used to display messages in the 
			  s256demo program.  Also contains routines for 
			  controlled user input of strings, numbers (not part 
			  of the library but may be useful to you).  

	S256DEMO.H	- Header file for the demo program. 

	S256DEMO.IMG	- An image file containing a medical ultrasound image
			  that is displayed by the demo program.  This image
			  is 501x333 pixels in size and is displayed using
			  a 64-level gray scale. 
			  


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
V.	SVGA256 registration information.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm


	You are free to use this shareware library and the included files for 
a period of 30 days without payment. After this 30 day period you must register 
your copy of this software package with the author if you wish to continue using
this library. You may not distribute in any way, shape, or form, any files or 
programs created with the SVGA256 Graphics Library until you have registered 
with the author. 

	Use the order form included in the text file S256REGI.DOC to register 
your copy of this software package with the author.  Complete instructions on
how to register are found in this file.  This file also details what you
will receive by registering this package with the author. 
                
        Remember, only through user registrations are shareware authors
able to continue to provide high quality, low cost programs to the 
computing community. Your contributions are greatly appreciated by all.

     Questions, comments, and suggestions about SVGA256 are always welcome.  
I can be contacted by Prodigy or U.S. mail:

	      Prodigy:	   VNVH69A

	      US Mail:	   Jeff Orth 
			   1182 Greenmar Dr.
			   Fenton, MO  63026



mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
VI.	Disclaimer.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

All users of the SVGA256 Graphics Library must agree to the following:

	This software is provided "as is".  All warranties relating to 
this software are disclaimed, whether expressed or implied, including 
without limitation any implied warranties of merchantability or fitness 
for a particular purpose.  Neither the author nor an agent of the author 
will be liable for any special, incidental, consequential, indirect or 
similar damages due to loss of data or any other reason, even if the 
author or an agent of the author has been advised of the possibility of 
such damages.  In no event shall the author's or an agent of the 
author's liability for any damages ever exceed the price paid for the 
license to use software, regardless of the form of the claim.  The 
person using the software bears all risk as to the quality and 
performance of the software.


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
VII.	Distribution of SVGA256.
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

You are free to copy and distribute SVGA256 if, and only if:

1)      It is used strictly for non-commercial purposes.
2)      No fee is charged for use, copying or distribution.
3)      It is not modified in any way.
4)	None of the files are seperated from the package.  ALL files listed 
	under section IV "SVGA256 file description" are part of the SVGA256 
	Graphics Library package.

	Clubs and user groups may charge a nominal fee not to exceed $10 for
expenses and handling while distributing SVGA256.


mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm
VIII.	Technical Information	
mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

1) ABOUT TEXT DISPLAY.

	SVGA256 uses the fonts stored in your ROM BIOS to display characters on 
the screen.  This frees the programmer from having to store fonts in memory and
makes available the whole IBM character set (all 256 characters).  These fonts
are somewhat small on the screen when using hi-resolution modes so the character
display routines allow you to set a "zoom" size (using the SV_setcharsize() 
routine) to zoom the characters to a more readable size.  If the programmer 
wishes to make his own fonts then he can display his own fonts using the 
routine SV_putbitpattern() if the fonts are bit-map fonts (1 bit per pixel).  
This routine displays a bit-map image where data is in format such that 1 bit of
data equals 1 screen pixel.  Refer to S256ref.doc for these routines:

	SV_setfont(), SV_getfont(), SV_setcharsize(), SV_getcharsize(), 
	SV_charwidth(), SV_charht(), SV_putbitpattern() 

	SVGA256 has a set of routines that allow for easy placement of text on
the screen using either pixel coordinates (x,y) or character coordinates
(col,row).  A character origin is set by SV_setcharorigin() which is a screen 
pixel position used as the starting point in calculating the columns and rows of
the text display routines.  To display text in a window for example you would 
set the text origin to the upper-left corner of the window and then use
column,row positioning to display text.  The upper-left corner would be 
column 0, row 0 and the other columns and rows would be calculated based on the
currently chosen font and char size (zoom factor).  The main text display
routines: SV_putchar(), SV_putstring(), SV_putstringxy(), display graphics 
characters and graphics strings but accept pixel coordinates as arguments, not 
col & row coordinates.  This is no problem because the functions SV_charx() 
and SV_chary() convert text col,row positions to pixel (x,y) positions.  For 
example, if you know the col and row (say col=5, row = 6) and you wish to 
display a text string then you could make the following call:

	SV_putstringxy("Hello World", SV_charx(5), SV_chary(6), color); 

Refer to S256ref.doc for more details on these routines:
	
	SV_charmaxcol(), SV_charmaxrow(), SV_charmoveto(), SV_charx(), 
	SV_chary(), SV_putstring(), SV_putstringxy(), SV_putchar(), 
	SV_setcharorigin(), SV_savecharstate() SV_restorecharstate(), 
	SV_getcharorigin()



2) ABOUT WINDOWS 

	SVGA256 has a set of routines that provides strong windowing and
screen-saving features.  The library refers to saved screen areas as "blocks".
It also refers to "windows" which are blocks (saved screen areas) with framed,
filled rectangles drawn over them.  The blocks and windows save the
screen areas and allow the programmer to easily restore the saved screen data if
desired.  The blocks and windows must save the screen data to one of 3 places

	1)  Extended memory (memory above 1 MB)
	2)  Unused video memory (video memory not used for the current screen).
	3)  System RAM (free conventional memory below 640K) 

The programmer can fine tune and specify how and where this data is saved 
depending on how he/she sees fit.  If he/she wishes to keep all conventional 
memory free then he/she may only want to use extended memory and/or video 
memory.  If he/she doesn't have extended memory then the other two storage 
places can be used, etc.  All three places can be used together and an 
order of precedence can be set to fix the priority of the methods used by the 
block and window routines.  For example if the order is set 1) Extended memory,
2) Video memory, 3) System memory then when a block or window is created the 
routines SV_saveblock() or SV_openwind() will first attempt to use extended 
memory.  If that fails they check to see if enough free video memory is 
available.  If that fails they check for enough system memory.  If that fails 
then the error code -1 is returned and you are out of luck.  It is nice to be 
able to use all 3 methods and set their priorities, especially in the 
high-resolution modes where saving screen data takes up a lot of space.  Saving 
a full screen in the 1024x768 mode takes up a whopping 786,432 bytes 
(definitely an extended memory candidate).  For more details on these methods 
see S256ref.doc under the SV_initwindows() routine.  The following block and 
window routines are explained in more detail in S256ref.doc:

   blocks
   ------
	SV_blockexists(), SV_closeblock(), SV_freeallblocks(), SV_freeblock(), 
	SV_getblockcoords(), SV_restoreblock(), SV_saveblock() 

   windows
   -------
	SV_closewind(), SV_freeallwinds(), SV_freewind(), SV_getwindcoords(), 
	SV_hidewind(), SV_initwindows(), SV_openwind(), SV_unhidewind(), 
	SV_windexists()

 

3) ABOUT SAVING AND DISPLAYING IMAGES. 

	The following routines are used to save and display bit-map and
"byte-map" images from/to the screen and memory.  A bit-map image is an image
whose data is such that 1 bit represents 1 pixel on the screen.  "byte-map" here
refers to an image whose data is such that 1 byte represents 1 pixel on the 
screen.  Refer to S256ref.doc for more details on each routine.  All are written
in 80386 assembly language for maximum speed.

      SV_getimage() - This routine takes the coordinates of an image and stores
		   the image in the format 1 byte per pixel into a buffer in
		   memory.  This buffer must be set up before the call to this
		   routine.  The image can be greater than 64K as long as your
		   buffer is big enough to hold it (Borland users can use 
		   farmalloc() to allocate a contiguous buffer larger than 
		   64K in size).

      SV_putimage() - This routine takes an image in memory and copies it to the
		   screen at a specified (x,y) location.  The image must be in 
		   the format 1 byte per pixel.  The image can be greater than 
		   64K bytes in size.

      SV_invertimagebuffer() - This routine was added just because I had it from
		   an application I was working on using SVGA256.  It
		   turns upside-down an image stored in a buffer (not an image 
		   on the screen).  The buffer can be bigger than 64K bytes in
		   size.

      SV_moveimage() - This routine copies an image on the screen from its 
		    current location to another specified (x,y) location.  
		    This routine is used in the S256demo program when the 
		    example image starts jumping all over the screen.  The 
		    image can be greater than 64K bytes in size.

      SV_putbitpattern() - This routine displays an image that is in the format
 		   1 bit of data for each pixel.  This format is great if you
		   only need one color in the image (like fonts) because it
		   stores 8 pixels of data per byte instead of 1 pixel/byte.  
		   This routine also allows you to XOR the image which is
 		   useful for animation.  THE IMAGE DATA MUST BE LESS THAN 64K 
		   BYTES FOR THIS ROUTINE. 

     SV_putbytepattern() - This routine is the same as SV_putbitpattern() except
		  the data must be stored as 1 byte/pixel.  It is also 
		  identical to SV_putimage() except that for this routine the 
		  image can be XOR'd for animation and the IMAGE DATA MUST BE 
		  LESS THAN 64K BYTES IN SIZE.  Useful for small images and for
		  animation of small objects.



4) ABOUT MANIPULATING COLOR

	The 256-color modes allow the display of 256 colors on the screen at
one time.  This also means that 1 byte represents 1 pixel on the screen since
1 byte can take on a value from 0-255.  Each of the 256 colors is comprised of
a RED component, GREEN component, and a BLUE component.  Since we have 256
colors with 3 components each we have 768 RGB components with which to play with
to make all sorts of colors (but only display 256 at a time).  Each RGB 
component can take on a 6-bit value (0-64).  You can mix and match any of the
values of each of the RGB components to make one of the 256 colors.  The
routines SV_readDAC() and SV_writeDAC() read and write these 768 RGB components 
to allow you to save and write colors to/from the palette.  The routines are
flexible to allow you to read/write only a subset of the RGB components if 
you do not need to read/write all 768.  They let you read/write the 
components in triplets.  There are 256 triplets (1 for each available palette
color).  You specify the starting triplet (0-255) and the number of triplets
to read/write.

	SVGA256 also has fading routines that allow you to fade the screen 
in/out at different speeds.  It also allows you to change the palette colors
after the screen is faded so that when you fade back in the palette is
changed.

	Refer to s256ref.doc for more details on the following palette
manipulation routines.  When the routines refer to DAC they are refering
to Digital-to-Analog Converters which is the hardware term for changing
digital color information to the analog information seen on the screen:

	SV_fadein(), SV_fadeout(), SV_fadewriteDAC(), SV_getcolor(), 
	SV_initgrayscale64(), SV_readDAC(), SV_writeDAC(), SV_setbkcolor(), 
	SV_setcolor(), writeDAC()



5) ABOUT USING EXTENDING MEMORY FOR DATA STORAGE

	When programming in the high-resolution modes there is a need for a lot
of memory for storage of screen data and images.   SVGA256 has routines that
will allow you to allocate blocks of extended memory that you can use to store
data.   All of these routines use 32-bit size arguments to allow you to 
allocate, read and write to blocks of extended memory of any size, limited
only by the amount of free extended memory you have.  The windowing and block
saving routines automatically use these extended memory routines when they 
save and restore screen data.  You the programmer can also use them for storing
other data.  The routines are designed to be used with the Microsoft XMS driver
HIMEM.SYS that comes with MS-DOS or MS-WINDOWS.  See s256ref.doc for more 
details on these routines:

	SV_allochimem(), SV_availhimem(), SV_contighimem(), SV_freeallhimem(),
	SV_freehimem(), SV_himemexists(), SV_inithimem(), SV_readhimem(),
	SV_writehimem() 
 

mmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmmm

GOOD LUCK!