Cover

    Disk File Encryption/Decryption Using Virtual One-Time-Pad Files

                     Program Name VOTPCRYP
                  Version 1.1 15 August 1994

         * * * * * * * * * * WARNING * * * * * * * * * *
         Version 1.1 supercedes and replaces prior Versions
Files encrypt with Version 0.9 can NOT be decrypt with Version 1.0/1.1

                        Copyright 1994 by
                        James T. Demberger
                   9862 Lake Seminole Drive West
                        Seminole, FL  34643
                            813-397-2930
                       CompuServe 74425,1642

     Under current copyright regulations, a copyright was automatically
granted to the author for the VOTPCRYP program and for this information
file. The author of the VOTPCRYP program and this information file does
not intend to assert any of the rights granted by the copyright and
hereby releases the VOTPCRYP program and this information file to the
Public Domain.  The files may be freely copied, distributed or modified
for any lawful purpose.

                             Disclaimer

     The VOTPCRYP program and its associated documentation is provided
on an "as is" basis without warranty of any kind, expressed or implied.
Anyone using this software assumes all risks as to the quality and
performance of the software.  The author disclaims all liability for any
special, incidental, consequential, direct or indirect damages due to
either proper or improper use of the program.

                          Table of Contents

            Introduction  - - - - - - - - - - - - - - 1
            System Requirements - - - - - - - - - - - 1
            Vernam XOR Encryption and
               One-Time-Pad Keyfiles  - - - - - - - - 1
            Are VOTPCRYP Encrypt Files Unbreakable? - 2
            Creating Virtual One-Time Pads  - - - - - 2
            VOTP.HDR File and VOTP Header Block - - - 3
            Running VOTPCRYP  - - - - - - - - - - - - 4
            What is a Session Phrase? - - - - - - - - 4
            VOTPCRYP Menu - - - - - - - - - - - - - - 5
            File Encryption - - - - - - - - - - - - - 7
            File Decryption - - - - - - - - - - - - - 7
            Transmitting Encrypt Files  - - - - - - - 8
            Customizing VOTPCRYP  - - - - - - - - - - 8
            Basic Source Code for VOTPCRYP  - - - - - 8
            Generating Physical One-Time-Pads - - - - 9
            Export Exemption  - - - - - - - - - - - -10
            Version History - - - - - - - - - - - - -10

                                                                 Page 1
                            Introduction

     The VOTPCRYP software has three main functions:
     a:  Outline operation of the program and the algorithms used by the
         program.
     b:  Encryption and decryption of disk files using One-Time-Pad files
         and XOR encryption.
     c:  Provide Basic source code that can be run as is or that can be
         modified to meet specific user requirements.

     The VOTPCRYP program is not a finished product; it is a fully
functional prototype that can be used to create a secure encryption
system for anyone or for any activity.

                         System Requirements

     The program requires an IBM computer or compatible running DOS with
color or monochrome display and one or more disk drives.  File storage
space equal to twice the size of the largest file to be encrypt or
decrypt must be available.  Any work with the source code will require
PowerBASIC, QuickBASIC or QBASIC.

            Vernam XOR Encryption and One-Time-Pad Keyfiles

     In 1917, long before the age of electronic computers, Gilbert S.
Vernam developed an encryption process for messages punched in paper
tape using Baudot or five channel teletype code.  He used the electro-
mechanical equivalent of a logical exclusive OR operation (XOR) on each
character code in a message tape and a corresponding random character
code in a key tape to produce a third tape with the encrypt message.
Decryption used the same process except that a tape with the encrypt
message and a copy of the key tape were XORed to produce a decrypt
message tape.

     In 1918, Major Joseph O. Mauborgne of the Army Signal Corps invented
or conceived an encryption method that is considered to be unbreakable.
This encryption method has the following characteristics:
a. The characters in the encryption key are in naturally random order.
b. The encryption key must have as many (or more) random characters
       as the number of characters in the file being encrypt.
c. The encryption key is used to encrypt plain text while a copy
       of the same key is used to decrypt the cipher test.
d. The encryption key is used to encrypt and decrypt only one file or
       message and is never reused.
The keyfiles used by this method of encryption later became known as
One-Time-Pads (O-T-Ps).

     There have been many variations of O-T-P (one-time-pad) encryption
systems used over the seventy plus years since the Vernam O-T-P tape
system was first used.  In addition to XOR encryption, other reversible
arithmetic operations can be used with a O-T-P.  One such system first
encrypts letters as one or two numbers then uses MOD 10 arithmetic to
encrypt the message with a O-T-P of random digits 0 thru 9.

     The primary problem with the use of a O-T-P encryption occurs in
the creation and security of the pairs of keyfiles required for
encryption and decryption.  The original Vernam process required the
creation of miles of paper tape.  The ease with which computers can
create the random strings of characters or numbers required for O-T-Ps
is the converse of the difficulty of creating a secure distribution
system for the large number of magnetic tape or disk files required for
the O-T-Ps.

                                                                   Page 2

                  Are VOTPCRYP Encrypt Files Unbreakable?

     To answer this question you must first decide on a definition of
random numbers.  The primary requirement for an unbreakable O-T-P is a
naturally random series of numbers.  One definition of a naturally
random series of numbers is that there is no know method which will
permit the prediction of the next number in the series.  Much has been
written about the creation of truly random series of numbers since
there are many processes that require a random series of numbers.  Much
has also been written about psuedo random number generators that will
produce a series of numbers that appear to be random.  O-T-Ps created
by the VOTPCRYP do not meet the primary requirement for an unbreakable
O-T-P in that the O-T-Ps are not a naturally random series of numbers.

     Another definition of a random series of numbers is that the series
is random if it is random enough to meet the requirements of a
particular process.  If this definition of randomness is accepted in the
case of the VOTPCRYP O-T-Ps, the files are unbreakable in the same sense
that DES, RSA or IDEA encrypt files are unbreakable.  Any brute force
"try every possible key code" attempt to break VOTP encryption would
probably require more time and hardware than could be justified.  A
brute force attack would require the creation of a very large number of
O-T-Ps and a very large number of test decryptions of the cipher text
file in the hope that one of the clear text files created might be
recognized as the original plain text file.

     The primary feature of the VOTPCRYP program is the fact that it
uses a virtual O-T-P; the O-T-P keyfiles do not actually exist as
physical files.  Since no physical files are used there is no need for
a secure keyfile distribution system.  Encryption creates in memory one
character or code of a virtual O-T-P by XORing the values of one number
from each of three arrays or lists of 256 random numbers to create one
eight-bit code that is XORed with a corresponding character from a plain
text file.  The program creates the same virtual O-T-P keyfile when
needed for the decryption of a cipher text file as was used for the
original plain text encryption.

                   Creating Virtual One-Time-Pads

     The program uses the setting of three counters read from a header
record file (VOTP.HDR) to insure that a different O-T-P is used for each
file encrypt by the program.  The counters are updated in memory before
they are written back out to the header file for use when needed to
create a O-T-P for the next file to be encrypt.  Each of the three
counters can vary in value from 1 to 256.  In theory 16,777,216
different O-T-Ps are possible.  Some lesser number of O-T-Ps, however,
can actually be created since the program never uses the same value for
any two of the three counters when encrypting a file.  The values of the
three counters used for encrypting a file are encrypt and copied to the
header record block of the encrypt file.  When a file is decrypt, the
decrypt counter values are then used to recreate the same virtual O-T-P
for decryption as was used by the original encryption.

                                                                 Page 3

     The program starts the creation of an O-T-P by setting up an array
or list of the numbers 0 thru 255.  This array in then permutated or
shuffled into another array using pointers derived from a psuedo random
number generator that has been initialized or seeded with the value of
the first of the three counters. This same procedure is used to create
two more arrays using the random number generator initialized or seeded
with the values from the second and third counters.  The three arrays
each have 256 codes from 0 thru 255 in a different random order.

     When encrypting or decrypting a file the program cycles thru the
three 256 character arrays, picking up one code from each array and a
character code from the plain or encrypt text.  The four codes are XORed
to produce either an encrypt character code or a decrypt character code.
Cycling continues with the next code in each array and next character in
the plain or encrypt text.  Cycling can proceed either up or down thru
the arrays.  The cycling is reversed to cycle down when the 256th
character in each array is reached; cycling is reversed to count up thru
the arrays when the counters reach 1 for the first array, 2 for the
second array, and 3 three for the third array.  The period or cycle for
the first array is 510; the pointer is incremented from 1 to 256 (256
codes) then decremented from 255 to 2 (another 254 codes) with the next
cycle starting with 1.  The period for the second array is 508; the
period for the third array is 506.

     Subsequent looping thru the three arrays will pick up a different
set of code values from those picked on a prior cycle or loop thru the
arrays.  To further confound any attempt to predict the next XOR value
that might be generated, the three cycle or loop counters are
initialized to different values for each encryption cycle.  The initial
starting values for each encryption cycle use the values of the three
O-T-P counters.

     Assuming any set of initial values of the three pointers, the
pointer values will simultaneously return to these same values after the
first pointer value has recycled thru the first random number array
257,048 times, the second pointer value has recycled 258,060 times and
the third pointer has recycled 259,080 times. This will occur after
131,094,480 keyfile characters have been generated if you should have a
need to encrypt a file this long.

                VOTP.HDR File and VOTP Header Block

     VOTPCRYP reads a 512 byte disk file (VOTP.HDR) with three numeric
fields which will become the O-T-P counters for the next file that is
encrypt by the program.  The program writes the VOTP.HDR file back out
after updating the counters so that each plain text file will make use
of a unique O-T-P for encryption.  The VOTP.HDR file is used as a
pattern for a VOTP header block that is written out as the first 512
bytes of an encrypt or cipher text file.  To simplify running VOTPCRYP,
the prompt for entry of a filename for the header record file defaults
to VOTP.HDR when the enter key is pressed for entry of a header
filename.

     While the format of the header record file, eight 62 character
lines each followed by carriage return and line feed characters, must be
maintained, the 2nd thru the 8th lines can be changed or edited with an
ASCII text editor.  DO NOT make any changes to the first line.  A change
could result in the program not recognizing the file as VOTP.HDR file.

                                                                 Page 4
Even worse, a change in the values of the three counters could result in
unpredictable encryption or decryption errors.  Any data in the 2nd thru
8th lines is duplicated in the same relative position in the first block
of an encrypt file.  These lines are NOT encrypt and they may be used
for an address, for a digital signature or for any other use that will
fit within these seven lines.

     The header record block written as the first block of an encrypt or
cipher test file is a duplication of the information in the VOTP.HDR
file with the following exception - the counters used to the create the
O-T-P used for encrypting the file are encrypt with the Session Key
codes before they are moved into the first line of the block. In theory
the three counters can provide 16,777,216 (256 X 256 X 256) different
O-T-Ps.  The initial setting of the three counters is 051 for the first
counter, 101 for the second and 201 for the third. The VOTP.HLD file is
a backup of the initial VOTP.HDR file with the same initial settings.

     Updating the counters for the next encryption is performed as
follows: increment the first counter by 1, if first counter modulo 2 is
0 increment second counter by 1, if second counter modulo 2 is 0
increment third counter by 1.  If after incrementing the second or third
counters, any counter is equal to one of the other counters, the
incrementing procedure is repeated.  This method of incrementing the
counters makes more frequent changes in the value of the second and
third counters than would occur if the second and third counters were
increment after the preceding counter reached the maximum value of 256.

                           Running VOTPCRYP

     From the DOS ready prompt key [dr:][\path\]VOTPCRYP then press the
Enter key.

     The initial screen displays prompts relating to the entry of a
Session Phase.  The same Session Phrase must be used when decrypting a
file as was used for the encryption of the file.  In addition, both the
activity encrypting a file and the activity decrypting a file must have
matching versions of the VOTPCRYP program.  This will be no problem so
long as both activities are using copies of the compiled EXE file
provided with this documentation file or matching versions of any
recompilation of the source code.

                     What is a Session Phrase?

     The VOTPCRYP program does not use a password as such.  A Session
Phrase entered in response to the prompts for the following display
might be considered the equivalent of a password.  The Session Phrase is
just camouflage for the input of three pairs of hexadecimal values that
are used to encrypt the three O-T-P counters before they are written to
the VOTP header record block when encrypting a file and to decrypt the
counters when a file is being decrypt.  Three hexadecimal character
pairs might at first glance appear to be a very poor choice for a
"password".  A second glance, however, will reveal that the three
hexadecimal pairs can provide 16,777,216 potential "passwords" or sets
of counter values.

                                                                 Page 5

     The default session phrase used by the program is "This is the
default Session Phrase" results in encryption keys of the hexadecimal
pairs ed ef ae or decimal 237 239 174.  Session Phrase input will accept
a string of 50 characters however input of any six hexidecimal character
will also be accepted.  Use of wild and weird strings for passwords has
been recommended by some security experts; if the wild and weird string
you enter does not have at least six hexadecimal characters you will be
prompted to enter a different or longer string.  If prearranged with the
activity that will be decrypting a file, you could actually hide or
camouflage a session key in the plain text lines 2 thru 8 of the VOTP
header block.

Screen Display Top -----------------------------------------------------

                         Select Session Phrase

          Any combination of alphabetic characters (upper or lower case),
          numeric characters, and spaces or special characters may be
          used for a Session Phrase.  The program uses the first three
          pairs of hexadecimal characters (0123456789abcdefABCDEF) found
          in the Session Phrase as three numeric values for the actual
          session codes for both file encryption and decryption.

          THE SAME SESSION PHRASE MUST BE USED FOR DECRYPTING A FILE
                    AS WAS USED FOR ENCRYPTING THE FILE

          Press Enter for NO visible display of Session Phrase OR
          Press V for a visible display of Session Phrase only OR
          Press D for display of the Session Phrase and hex pairs D

Old Session Phrase           This is the default Session Phrase

Enter new Session Phrase OR
Press Enter for old default  changed to something weird & wild

                                   1st    2nd    3rd
           Session Codes Hex      &Hca   &Hed   &Hee
                         Dec       202    237    238

                         Press any key to continue _

Screen Display Bottom --------------------------------------------------

                          VOTPCRYP Menu

     Pressing any key after the "Press any key to continue" prompt for
the Session Phrase screen display will result in the appearance of the
VOTPCRYP MENU display shown on the next page.

                                                                 Page 6
Screen Display Top -----------------------------------------------------

                                 VOTPCRYP MENU

                          P  Enter Session Phrase
                          E  Encrypt plain text file
                          D  Decrypt cipher text file
                          T  Turn Timer Off/On
                          S  Shell to DOS
                          X  Exit/End Program

                              Enter Option Letter T

                                  Timer is OFF

              Press O for Timer on - Press F for Timer off - o/F O

                                  Timer is ON

                         Press any key to continue _

Screen Display Bottom --------------------------------------------------

     The screen display shown above is the menu for all VOTPCRYP
functions.  In this instance the Timer and ON options were selected.
Only the time for execution of encryption or decryption code is clocked;
the total time does not include time for reading and writing files.  The
program uses these totals to compute and display the thruput in
characters per second.  Timing is accurate to approximately 1/18th of a
second.  Timings are not displayed when too few character have been
encrypt or decrypt to permit calculation of a valid characters per
second rate.  Press P for the Session Phrase option if you wish to
change the Session Phrase originally entered during the initial display.

                          File Encryption

Screen Display Top -----------------------------------------------------

                          Encrypt a Plain Text Disk File

                          Enter dr:filename.ext OR
                          Press Enter for VOTP.HDR  VOTP.HDR

               Enter Input  dr:filename.ext VOTPCRYP.DOC

               Enter Output dr:filename.ext VCDOC.ENC

                    Processing         30,733 bytes

                                    30733

    Total time  0 hours  0 minutes  2.859 seconds
    Total characters         30,733        Characters per second    10,748

                         Press any key to continue _
 
Screen Display Bottom --------------------------------------------------

                                                                 Page 7
     The timing information is not displayed unless the Timer On option
was selected.

     An error message "filename.ext does not exist or has 0 length" will
be displayed if either the VOTP.HDR file or the input file is not found.
The message "filename.ext is NOT a VOTP.HDR file" will be displayed if
the file does not have the correct characteristic of a VOTP.HDR file.

                          File Decryption

Screen Display Top -----------------------------------------------------

                      Decrypt a Cipher Text Disk File

          THE SAME SESSION PHRASE MUST BE USED FOR DECRYPTING A FILE
                    AS WAS USED FOR ENCRYPTING THE FILE

               Enter Input  dr:filename.ext VCDOC.ENC

               Enter Output dr:filename.ext VCDOC.DEC

                    Processing         30,733 bytes

                                    30733

    Total time  0 hours  0 minutes  2.969 seconds
    Total characters         30,733        Characters per second    10,352

                         Press any key to continue _

Screen Display Bottom --------------------------------------------------

                                                                 Page 8

     The timing information is not displayed unless the Timer On option
was selected.

     An error message "filename.ext does not exist or has 0 length" will
be displayed if the input file to be decrypt is not found.  The message
"filename.ext does NOT have a VOTP.HDR block" will be displayed if the
file to be decrypt does not have a header block with the correct
characteristic of a VOTP.HDR block.

     Any existing file with the same name as that entered for the decrypt
output file will be overlaid by the new output file.

                       Transmitting Encrypt Files

     An encrypt data file may be sent to another user or activity using
a communications link or as a disk file.  Since encrypt data files may
contain character strings corresponding to transmission control codes,
encrypt files must be transmitted as eight bit binary files using XMODEM
or some equivalent transmission protocol for binary files.

     Encrypt files can be converted with a UU-encode/decode program to
files that can be transferred on Internet.  If there is enough need for
UU encoding, someone might patch the necessary source code into the
BASIC source code for VOTPCRYP.

                      Customizing VOTPCRYP

     Many users will prefer to use a customized variation of the program
and may want to limit the distribution of the customized program to only
"authorized" users.  The VOTPCRYP program uses a random number generator
to produce the random numbers used to permutate or shuffle the random
code arrays or lists.  The RNG can be seeded or initialized with values
from -32,768 to 32,768.  The program, however, uses only three values
from 1 to 256.  A change in one line in the source code from RNGRANGE% =
0 to RNGRANGE% = any value from 1 thru 127 result in a customized program
that will generate a different set of O-T-Ps.  Both the activity
encrypting a file and the activity decrypting a file must use copies of
the program that have the same value for RNGRANGE.

                     Basic Code for VOTPCRYP

     The Basic source code for VOTPCRYP is in the file VOTPCRYP.BAS.
This source code file has statement lines for PowerBASIC version 3.0
(PB) and for QuickBASIC version 4.5 and QBASIC (QB).  The only
differences between these two BASIC dialects in so far as the source
code is concerned are found in the statements for the binary file input
and output. The VOTPCRYP.EXE file furnished with this software package
was compiled with PowerBASIC version 3.0c.  While an EXE file compiled
with QuickBASIC version 4.5 may run 1 or 2 percent faster than the
PowerBASIC EXE file, the PB EXE file is much smaller (45,851 KB) than
the QB EXE file (59,818 KB).

                                                                Page 9

     WARNING - Encrypt files produced using the PowerBASIC program can
NOT be decrypt with the QuickBASIC program and vice versa.  The random
number generator used by PowerBASIC produces a different series of
numbers from that produced by QuickBASIC.

     All statement lines peculiar either to PB or to QB have a REM PB or
REM QB comment at character position 60 (+/-).  The source code file
will run as is using QBASIC or QuickBASIC since the REM PB statements
have another REM at the beginning of each of the REM PB statements.  If
you want to run or to compile the source code using Power Basic, make a
copy of VOTPCRYP.BAS and rename the copy to VOTPCRPB.BAS.  Edit the PB
copy to add a REM at the beginning of each statement that has a REM QB
and delete the REM found at the beginning of each REM PB statement
before you run or compile the PB version.

     Much of the BASIC source code has been re-written over the years
starting with interpreted BASIC for the Radio Shack TRS-80 and for the
original IBM PC.  For the most part, changes to the source code were
made only when and where required to run or to compile the code for
newer versions of the IBM, MicroSoft compilers and for PowerBASIC.

     The program was written using basic BASIC statement so that the
source statements would compile and run under both PowerBASIC and QBASIC
or QuickBASIC.  Some of the variable names and labels are rather
cryptic.  Just enough error checking is done to correct some of the more
likely errors.  A reasonably proficient programmer, using this text and
the Basic source code, should be able to write a program in Basic,
Pascal, C or some other high level language that would have the same
functionality as VOTPCRYP.

                 Generating Physical One-Time-Pads

      VOTPCRYP can be used to generate physical O-T-Ps if you have need
for a O-T-P disk file.  A "nothing" file consisting of a character
string of the hexadecimal value 00 when encrypt using any key phrase or
counter values will generate a file of random character code with
decimal values from 0 to 255.  The file NULL.ZIP that is included with
the other VOTPCRYP files can be unZIPped to the "nothing" file NULL.1MB
that is a string of 1,024,000 bytes each with a hexadecimal value of 00.
If you need a longer O-T-P, you can concatenate two or more of the 1
megabyte null files.  Encrypting a null file will create a physical
O-T-P that correponds to the virtual O-T-P which otherwise might have
been used to encrypt a plain text file of the same length.

     A physical O-T-P can be used to test the randomness of the
generated character codes or to look for character code strings that may
be duplicated two or more times within the O-T-P.  Finding duplicated
strings might indicate a potential point of attact to someone trying
to decrypt a file.  Since encrypting a file does a very good job of
concealing a virtual O-T-P under the XOR encryption of an unknown plain
text file, finding duplicate string of characters is much less likely to
occur in an encrypt file.

                                                                Page 10
                            Export Exemption

      Federal Government regulations require a license for the export of
technical data relative to munitions; cryptographic technology is
included in the government's definition of technical data.  The
regulations provide an exemption to the export license requirements for
information that is in the public domain.  The VOTPCRYP program and this
information file has been released to the public domain by the author.
Information regarding XOR encryption and the use of One-Time-Pads has
long since been in the public domain.  An extract of the pertinent
portions of the regulations follows:

                                FEDERAL REGISTER
                                VOL. 58, No. 139
                             Rules and Regulations
                              DEPARTMENT OF STATE
                       Bureau of Politico-Military Affairs
       22 CFR Parts 120, 121, 122, 123, 124, 125, 126, 127, 128, and 130
                              [Public Notice 1832]
          Amendments to the International Traffic in Arms Regulations
                                    Part II
                                  58 FR 39280
DATE: Thursday, July 22, 1993

  S 120.11 -- Public domain.
   Public domain means information which is published and which is
generally accessible or available to the public:
   (1) Through sales at newsstands and bookstores;
   (2) Through subscriptions which are available without restriction to
any individual who desires to obtain or purchase the published
information;
   (3) Through second class mailing privileges granted by the
U.S. Government;
   (4) At libraries open to the public or from which the public can
obtain documents;
   (5) Through patents available at any patent office;
       (additional definitions 6 thru 8 not applicable)

                          Version History

     Version 0.9  1 July 1994
                  Beta Release

     Version 1.0  1 July 1994
                  Major change to XOR en/decryption processing.

     Version 1.1  15 August 1994
                  Minor changes to program and documentation.