To create the executable file SOLID.COM, first prepare a file called
SOLID.SCR containing the following:

a       100
mov     ah,3
mov     bh,0
int     10
mov     ah,1
mov     ch,0
int     10
int     20

rcx
e
n solid.com
w
q

Then use the following command to make SOLID.COM:

C>A:
A>C:DEBUG <A:SOLID.SCR

This will create A:SOLID.COM which can be executed by typing

A>SOLID