ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC X10 Direct Control
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Version 1.50
December 1993

Copyright 1993 ù D.Huras ù All Rights Reserved

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄX10DC.DOC v1.50ÄÄÄÄÄÄ
CONTENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 1. DESCRIPTION                11. KEYBOARD USAGE
 2. WARRANTY                   12. MENU BAR
 3. FEATURE OVERVIEW           13. UNDOCUMENTED CP290 COMMANDS
 4. REQUIREMENTS               14. CP290 SELF TEST
 5. INSTALLATION INSTRUCTIONS  15. SIGNAL TEST GENERATOR
 6. COMMAND LINE ARGUMENTS     16. CLOCK SYNCHRONIZATION
 7. COMMUNICATION PORTS        17. BASE HOUSECODE
 8. OPERATING MODES            18. PROBLEM RESOLUTION
 9. DEBUG MODE                 19. REGISTRATION INFORMATION
10. PROGRAM OVERVIEW           20. OTHER HOME AUTOMATION SOFTWARE

1. DESCRIPTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is a program which sends immediate commands to the X10 CP290
(*1) Computer Interface.  The CP290 transmits these commands over the
power line to control X10 devices.  X10DC does not currently modify
the EVENT DATA stored in the CP290 Interface (*2).  X10DC is a DOS
program that uses a simple point & click user interface.  (A Mouse
though not required is highly recommended).  X10DC is designed to be
robust software that is processor speed independent.  This program is
shareware and you are invited to evaluate it for 30 days. If you
continue to use the program after the 30 day evaluation period you are
asked to register it.  The author retains all rights to the program.

(*1) The CP290 Computer Interface is a device manufactured by X-10
     that can be connected to a micro-computer serial port.  The CP290
     also plugs into an electrical outlet and it is through this
     connection that the CP290 imposes X-10 commands onto the powerline.
     X-10 commands use the power line as a carrier; other X-10 devices
     connected to the power line will respond to these commands (ie.
     switch ON/OFF lights, appliances).

2. WARRANTY
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is supplied as is.  The author disclaims all warranties,
expressed or implied, including, without limitation, the warranties
of merchantability and of fitness for any purpose.  The author
assumes no liability for damages, direct or consequential, which may
result from the use of X10DC.

3. FEATURE OVERVIEW
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù User-Friendly point & click DOS character-based Interface

ù All program functions can be controlled using a mouse; no keyboard
  intervention is required.

ù Supports Standard CommPorts 1 thru 4 and a User Defined CommPort
  which can support any IRQ between 1 & 15 (inclusive) and any
  Base I/O Address.

ù SUPPORTS * 5 * UNDOCUMENTED CP290 Commands

ù The Program supports 3 operating modes; each mode uses a different
  combination of on-screen controls.  Mode 1 is suggested for users
  not using a mouse.

ù When running in Mode 3, the program reads in an X10.DAT file
  [this file format is used by the X10 Program supplied with
  the CP290 Interface] and presents a list box of device
  descriptions/locations which can be targetted for commands.
  (The Unregistered version will only send commands to the 1st
   8 Devices found; SEE REGISTRATION BENEFITS)

ù Commands can be sent to all 256 X10 device addresses.

ù Commands can be targetted for any number of units within an X10
  House Code (effectively supporting for ALL ON and ALL OFF).

ù Supports 16 discrete dimming levels.

ù Acknowledgements sent from the CP290 (after receiving commands from
  the program) are monitored and checksums are verifed.

ù A scrollable Command History is available for browsing while the
  program is running.

ù A software-based Signal Test Generator is available to assist in
  identifying and isolating X10 transmission/reception problems.

ù A Debug Mode is available which reports all data sent from the
  CP290 as well as timing information.

ù A CP290 Self Test with event preservation is supported.
  (*2) NOTE, the self test overwrites the EVENT/ICON DATA.  X10DC
  will preserve the EVENT/ICON DATA by downloading it from the
  CP290, saving it in memory, running the Self Test, and
  finally uploading the saved EVENT/ICON DATA back to the CP290.

ù Clock Synchronization function for the CP290 and the PC

ù Change Base HouseCode stored in the CP290 function with
  or without Event & Icon Data Preservation.

ù Detects and exploits EGA/VGA 43/50 line mode

ù A comprehensive on-line Help sub-system that can be disabled
  at the user's option to decrease program load time.

ù The program WILL load without a CP290 Interface attached, however
  all attempts at serial communications will result in errors; the
  program will attempt to trap all such errors.

4. REQUIREMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ù An IBM-Compatible PC with at least 1 serial port.

ù An X10 CP290 Computer Interface attached to a serial port.

ù A Microsoft-Compatible Mouse is highly recommended

ù A Colour adapter/display is recommended although the program
  should run with a monochrome display/adapter.  If you
  experience problems with the default colors, then try the /BW
  command line argument which will set everything to Black &
  White.

The program requires approximately 415K available conventional memory
to run.  The Command History will consume up to an additional 32K
of memory however this translates to approximately 1000 commands; its
unlikely that this many commands will be sent during one invokation of
the program.  However, if Debug Mode is on, the Command History will
quickly fill up since all CP290 responses are reported in the
Command History list box.

6. INSTALLATION INSTRUCTIONS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
There are no special installation instructions; simply copy the
program to a sub-directory of your choice and run it.  The program
will look for 3 files in the directory it is run from.  However,
the program will run with or without the following 3 files:

  1) X10.DAT
     If you want to use Mode 3 then you may want to copy an
     X10.DAT file to the sub-directory where you have installed
     X10DC.EXE.  Alternatively, you can load an X10.DAT file from
     any sub-directory by using the 'Load X10 File' menu option.
     An X10.DAT file is a file format used by the X10 program
     supplied by X10 with the CP290 interface.  The unit
     addresses, locations and descriptions are read from this
     file and presented in a list box by X10DC.  X10DC DOES NOT
     MODIFY THE X10.DAT FILE.  A sample X10.DAT is provided
     with X10DC.

  2) X10DC.HLP
     X10DC retrieves the on-line help text from this file. If the
     file is not found then X10DC will display a message during
     startup and then continue.  The help feature will be
     unavailable in this case.  If you decide that you no longer
     need the help sub-system, then you should run the program
     with the /NH command line argument; this will suppress the
     'Help not found' message and decrease program load time.

  3) X10DC.INI
     The registered version of the program will look for a
     X10DC.INI file in the current directory.  The X10DC.INI file
     is a text file containing all program parameters; there is no
     need to create this file yourself since the program will
     generate one whenever you select the 'Save Options' menu item.
     A sample X10DC.INI file (generated by X10DC.EXE) is shown
     below:

;
;X10DC.INI File Created: 08-06-1993 01:40:00
;
;All Lines prefixed with ; are ignored
; Program Options
; ---------------
; CommPort=1,2,3 OR 4            DEFAULT=1
; Mode=1,2 OR 3                  DEFAULT=1
; Debug=ON/OFF                   DEFAULT=OFF
; X10File=[d:]\FILENAME.EXT      DEFAULT=X10.DAT
; LoadHelp=YES/NO                DEFAULT=YES
; Sounds=ON/OFF                  DEFAULT=ON
; PreserveICONData=YES/NO        DEFAULT=NO
;
Mode=1
X10File=X10.DAT
;
; User Defined CommPort
; ---------------------
; IRQ and Base_IO_Address apply to User Defined CommPort ONLY
;
; IRQ=1-15                 DEFAULT=4; IF Base_IO_Address is set
;                                     --
; Base_IO_Address=nnnn(n)  DEFAULT=1016; IF IRQ is set
;                                        --
IRQ=5
Base_IO_Address=1016
;
; Colour Values
; -------------
; 0=Black  4=Red       8=Gray          12=Bright Red
; 1=Blue   5=Magenta   9=Bright Blue   13=Pink
; 2=Green  6=Brown    10=Bright Green  14=Yellow
; 3=Cyan   7=White    11=Bright Cyan   15=Bright White
;
BackColor=7
ForeColor=0
HiLiteKey=14
DisabledItem=8
MenuBackColor=1
MenuForeColor=7
MenuSelectedBackColor=0
MenuSelectedForeColor=7
LabelBackColor=9
LabelForeColor=7
Hilite1ForeColor=4
Hilite2ForeColor=1
Hilite3ForeColor=14
HelpTitleBackColor=5
HelpTitleForeColor=15
StatusTitleBackColor=4
StatusTitleForeColor=15
WarningTitleBackColor=12
WarningTitleForeColor=15
;
; Other Screen Settings
; ----------------------
; ThreeD=ON/OFF*                 DEFAULT=ON
; Shadow=ON/OFF*                 DEFAULT=ON
; Graphics=ON/OFF                DEFAULT=ON
;  * OFF Recommended for Monochrome Displays
;
ThreeD=ON
Shadow=ON
Graphics=ON
;
; End of X10DC.INI (13:59:37)

This X10DC.FILE was created using the 'Save Options' menu item.

NOTE:the DEBUGFORECOLOR directive was replaced with HILITE1FORECOLOR
     effective with Version 1.50.  However, X10DC will still
     recognize DEBUGFORECOLOR and map it to HILITE1FORECOLOR.
     When the INI file is rewritten, the old directive will be
     replaced.


6. COMMAND LINE ARGUMENTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
DEFAULTS:  If the program is run without any command line arguments
           it will default to COMMPORT 1,OPERATING MODE 1,DEBUG OFF,
           F:X10.DAT.

The following command line arguments can be entered in any order:

/Annnn(n) ù Base I/O Address applicable to User Defined CommPort
            (Must be specified as a decimal number)
            If /I agrument is present, but /A is not; then Base
            I/O Address will default to 1016 (3F8 Hex).

/BW  ù Use Monochrome colours (Black & White)

/Cn  ù COMMPORT where n = 1,2,3 & 4
       ALWAYS overrides User Defined CommPort during Program Startup

/D   ù TURNS ON DEBUG MODE
       When DEBUG MODE is ON, the CP290 responses & checksums are
       displayed in the Command History List Box.

/F:[d]\filename ù X10.DAT FILE SPECIFICATION for MODE 3
      where [d] = drivespec eg. /F:C:\X10\X10.DAT

/In  ù IRQ applicable to User Defined CommPort where n = 1 - 15
       If /A argument is present, but /I is not; then IRQ
       will default to 4.

/Mn  ù MODE where n = 1,2 or 3
       MODE 1 Provides a List Box of Unit Codes; only 1 Unit Code
              can be selected.  However, this mode will be easier to
              use if you don't have a mouse since you'd have to TAB
              through all the unit code check boxes used in MODE 2.
       MODE 2 Provides a Check Box for each Unit Code plus ALL and
              NONE buttons to quickly Check/Uncheck all check boxes.
              In this mode, multiple Unit Codes can be targetted for
              the X10 Command.
       MODE 3 Provides a List Box of Devices which are read from
              an X10.DAT file; X10DC will look for "X10.DAT" in the
              current directory UNLESS the /F: command line argument
              is supplied.  If X10.DAT cannot be found, the program
              will switch to Mode 1.  Select 'Load X10 File' under
              the File menu to load an X10.DAT file from another
              sub-directory. (Once the file is loaded, its location
              can be saved [REGISTERED VERSION ONLY] by selecting
              'Save Options' under the Options menu.

/NH  ù Do Not Load HELP Sub-System

/NH- ù Load HELP Sub-System (Override INI directive)

/NS  ù No Sounds during Signal Test

/NS- ù Sounds during Signal Test (Override INI directive)

/P   ù Toggles ON 'Preserve ICON Data'
       Normally, X10DC will only preserve the Event Memory stored
       in the CP290.  This is because the DOS-based CP290 software
       only utilizes the Cp290 Event Memory and does not utilize the
       CP290 Icon memory area.  However, X10EC does store information
       in the Icon memory, and X10DC has been upgraded to preserve
       the Icon memory area for compatibility reasons.


             NOTE: ONLY THE 1st 8 DEVICES CAN BE TARGETTED FOR
                   COMMANDS WITH THE UNREGISTERED VERSION.

       1) Most Command Line directives (with the exception
          exception of /A,/I & /NH) can be modified once the
          program loads by selecting the appropriate menu items
          under the Options Menu.  Registered Users can save all
          these settings to the X10DC.INI file by using the 'Save
          Options' menu item.

       2) COMMAND LINE OPTIONS OVERRIDE ALL X10DC.INI SETTINGS

7. COMMUNICATION PORTS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC supports "pseudo standard" CommPorts 1 thru 4 using the
following settings:

            ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³          ³      ³ Base I/O Address ³
            ³ CommPort ³ IRQ  ÃÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ´
            ³          ³      ³ Decimal ³  HEX.  ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    1     ³   4  ³  1016   ³  3F8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    2     ³   3  ³   760   ³  2F8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    3     ³   4  ³  1000   ³  3E8   ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    4     ³   3  ³   744   ³  2E8   ³
            ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ

If one of these CommPort settings matches your hardware configuration
simply use the /C command line argument with the appropriate
CommPort.  The CommPort= X10DC.INI directive can also be used.  Note
that if X10DC is run without the  /I (IRQ) or /A (Base I/O Address)
Command Line arguments then the 'User Defined CommPort' is
"undefined" and not selectable from the menu bar.

If your hardware configuration differs from the table above, then
you can define your own CommPort by using the /I and /A command
line arguments (or IRQ= & Base_IO_Address= X10DC.INI file directives).
IRQ can be set to any value between 1 and 15 (inclusive).  Base I/O
Address can be set to any value greater than zero.  CAUTION: your
hardware may "lock up" if incorrect settings are used.  You should
supply both arguments (/A & /I), however, if you only supply one of
the arguments then the defaults applicable to CommPort 1 will apply
to the other argument.  (eg. if only the /I5 argument is supplied,
then the /A argument defaults to 1016).  If either the /I or /A
argument is supplied, then the 'User Defined Commport' under the
'Options' menu becomes enabled.

NOTES: 1) The /C command line argument AND the CommPort= X10DC.INI
          directive ALWAYS override the the User Defined CommPort
          when the program first loads.  However, the 'User Defined
          CommPort' will remain enabled under the 'Options' menu.
          To start the program with the User Defined CommPort active,
          ensure that there is no /C command line argument AND no
          CommPort= X10DC.INI directive.

          THE BASE I/O ADDRESS MUST BE SPECIFIED IN DECIMAL NOTATION.

          IBM PS/2 CommPort Parameters are shown below:
            ÚÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
            ³   PS/2   ³      ³ Base I/O Address ³
            ³ CommPort ³ IRQ  ÃÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄ´
            ³          ³      ³ Decimal ³  HEX.  ³
            ÃÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄ´
            ³    1     ³   4  ³  1016   ³  3F8   ³
            ³    2     ³   3  ³   760   ³  2F8   ³
            ³    3     ³   3  ³ 12832   ³ 3220   ³
            ³    4     ³   3  ³ 12840   ³ 3228   ³
            ³    5     ³   3  ³ 16928   ³ 4220   ³
            ³    6     ³   3  ³ 16936   ³ 4228   ³
            ³    7     ³   3  ³ 21024   ³ 5220   ³
            ³    8     ³   3  ³ 21032   ³ 5228   ³
            ÀÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÙ
          A User Defined CommPort must be used for
          PS/2 CommPorts 3-8.

8. OPERATING MODES
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Operating Mode can be set using the 'Options' menu, the MODE command
button (cycles through the modes), or the /M command line argument.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 1                    Unit
                          Code            NOTE: Mode can be toggled
In this mode only        ÚÄÄÄÄÄ¿                at runtime by clicking
one Unit Code can be     ³   1                 the MODE button.
selected from the        ³   2 Û                (Keyboard users press
Unit Code List Box.      ³   3 °                 ALT-m).
                         ³   4 °
                         ³   5 °                Can also be set from
                         ³   6                 the Options Menu.
                         ÀÄÄÄÄÄÙ
RECOMMENDED IF YOU DON'T HAVE A MOUSE.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 2                             Unit Code(s)
                         ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
In this mode multiple    ³[X] 1  [ ] 5  [ ] 9   [ ] 13³
Unit Codes can be        ³[ ] 2  [ ] 6  [ ] 10  [ ] 14³
checked; in addition     ³[ ] 3  [ ] 7  [ ] 11  [ ] 15³
the ALL button can be    ³[ ] 4  [ ] 8  [ ] 12  [ ] 16³
clicked to check all     ³ÚÄÄÄÄÄÄÄÄÄÄÄ¿  ÚÄÄÄÄÄÄÄÄÄÄÄ¿³
the Unit Codes. The      ³³    ALL    ³  ³    NONE   ³³
NONE button unchecks     ³ÀÄÄÄÄÄÄÄÄÄÄÄÙ  ÀÄÄÄÄÄÄÄÄÄÄÄÙ³
all the unit codes.      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ


ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
MODE 3          ** Example 1 **
                  Unit Location               Description
An X10.DAT      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
is read and     ³ A  1³DINING ROOM           ³TABLE LAMP             
a List Box      ³ A  2³FAMILY ROOM           ³TV                     Û
replaces the    ³ A  3³GARAGE                ³CEILING LIGHT          °
House/Unit      ³ A  4³GUEST ROOM            ³DE-HUMIDIFIER          °
Controls used   ³ G  7³HALL                  ³CEILING LIGHT          
in Modes 1 & 2. ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
Also note that   {11 Device(s) Found} Brightness ®Û°°°°°°°¯ 1÷00.0%
the Brightness
List Box has been replaced by a Horizontal Slider Control. (above)
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
9. DEBUG MODE

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³ Using COMMPORT: 2   X10 ù X-10 Direct Control   CP290 Day: Tuesday ³
³Base House Code: P         Version 1.50         CP290 Time: 11:51 AM³
³Mode: 1   Debug ON      (c)1993 ù D.Huras          PC Time: 11:52 AM³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
               ÀÄÄÄÄ¿
                  ÄÄÁÄÄÄÄÄ
When enabled, the DEBUG ON message appears in the screen Header and all
responses from the CP290 are displayed in the Command History List Box,
as well as Checksums and Timing Information.

Debug Mode can be toggled ON/OFF from the Options Menu.

NOTE: Debug Mode increases program overhead; memory requirements will
be greater and program performance will be somewhat degraded.  It is
recommended that you only toggle Debug Mode ON when necessary.

10. PROGRAM OVERVIEW
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
When X10DC initially loads, it requests the base house code and time
stored in the CP290 via serial I/O using the selected COMMPORT.
This information will be reported in the Screen Header if found.
Note:  the CP290 Time and PC Time reported in the Screen are static
and are only updated when the Base House Code is changed, a
Self-Test is run or the Time is set.  You can use the 'Refresh' menu
item under the 'Clock' menu to force an update to the on-screen Time
displays.  The House Code List Box defaults to the Base House Code
if the CP290 is found.  Once the program is loaded the SEND command
button is disabled until you have selected all required
information.  In some cases you need only to select a House Code and
an Action (eg. All Units Off).  If the selected action is DIM, then
a Brightness Level must be be selected before the SEND button
becomes enabled.

The program supports 3 operating modes; use whatever mode suits
your requirements.  Mode 3, which reads in Device Descriptions
from an X10.DAT file, is likely the most user-friendly since you
do not have to remember specific House/Unit code addresses.  X10EC
a companion program to X10DC can read, write, and create X10.DAT
files.

The Command History list box is scrollable and will store up to 1000
commands after which it becomes a circular FIFO buffer.  If you
suspect problems with your CP290, then you may want to toggle
Debug Mode ON; in this case the Command History list box will
contain additional information including responses from the CP290.
You may also want to perform a CP290 Self-Test to ensure that
the CP290 Memory is not being corrupted.

Finally, if you are experiencing X-10 transmission problems in your
application; you may want to take advantage of the Signal Test
Generator features provided by X10DC.  This subject is covered in
detail in a later section of this document.

11. KEYBOARD USAGE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Use the TAB/Shift-TAB keys to move among the various controls.(*3)
The Up/Down arrows can be used to move up and down List Boxes, and
the Spacebar and Enter key can be used to select the current List
Box item, check/uncheck a check box, or invoke a command button.
The ESCAPE key will exit the current function or the program if no
other windows are visible.  All of the Command Buttons and controls
have quick access keys:

     House Code ù Alt-o [Mode 1 & 2]
   Unit Code(s) ù Alt-u [Mode 1 & 2]
    Device List ù Alt-u [Mode 3]
            ALL ù Alt-l [Mode 2]
           NONE ù Alt-n [Mode 2]
         Action ù Alt-a
     Brightness ù Alt-b [when enabled]

           MODE ù Alt-m (*3)
           SEND ù Alt-s
           EXIT ù Alt-x
           HELP ù Alt-h

Command History ù Alt-c

(*3) The MODE Command Button is NOT in the TAB STOP sequence;
     Keyboard users must use ALT+character to access this
     button. (This eliminates extraneous TAB keystrokes)

12. MENU BAR
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Press & release the ALT key to activate the Menu Bar.  Menu items
can be selected by pressing the highlighted key (when applicable),
or by positioning the highlight bar using the up/down arrow keys and
pressing ENTER.  Some screen button functions are replicated within
the menus (eg. Exit, Help).  However, there are some functions which
are only available from within menus.  CommPort, Operating Mode,
Debug, & Sounds can all be set from the Options Menu; the current
state of each of these parameters is indicated on the menu itself
with a 'ù' character to the left of the menu item.

The following short-cut keys can also be used at any time to
select menu items:

*FILE* Menu
        Load X10 File ù Ctrl-L
            Exit      ù Ctrl-X (Same as Exit Button, Alt-X)

*CLOCK* Menu
         Set PC Clock ù Ctrl-T (Enter Time)
      Set CP290 Clock ù Ctrl-K (Synchronize w/PC) - Registered Version
       Refresh Clocks ù Ctrl-R
   Set Base HouseCode ù Ctrl-B (Preserve Events) - Registered Version

*TEST* Menu
      CP290 Self Test ù Ctrl-E
Signal Test Generator ù Ctrl-G

*OPTIONS* Menu
           CommPort 1 ù Ctrl-F1
           CommPort 2 ù Ctrl-F2
           CommPort 3 ù Ctrl-F2
           CommPort 4 ù Ctrl-F2
User Defined CommPort ù Ctrl-F5 (when applicable)

               Mode 1 ù Shift-F1
               Mode 2 ù Shift-F2
               Mode 3 ù Shift-F3

        Sounds Toggle ù Ctrl-N
    Debug Mode Toggle ù Ctrl-D
   Preserve ICON Data ù Ctrl-I

       Screen Colours ù Ctrl-C

         Save Options ù Ctrl-S  [Not Available in Unregistered Version]

*HELP* Menu
                 Help ù F1 (Same as Help Button, Alt-H)
                About ù Ctrl-A

13. UNDOCUMENTED CP290 COMMANDS
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10EC supports the following undocumented CP290 commands:

   Fade OFF   þ DIMS Light(s) to 0 then turns Unit(s) OFF
                (Can target multiple units for this command)
   X-Light ON þ Exclusive Light ON - Issues an ALL LIGHTS OFF
                then Brightens selected Unit(s)
                (Can target multiple units for this command)
   All Lights ON  þ All Lights on selected House Code set ON
   All Lights OFF þ All Lights on selected House Code set OFF
   All Units OFF  þ All Units on selected House Code set OFF

14. CP290 SELF TEST
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The CP290 can perform a Self-Test to determine if there are any
detectable problems within the device.  The Self-Test will return
either a pass or fail status when it is run.  X10DC will report the
results of the test in the CP290 Status window.  Whenever a
Self-Test is run the memory contents of the CP290 are overwritten.
X10DC can preserve the CP290 Event and Icon Data by downloading it
from the CP290 prior to the Self-Test and uploading it back to the
CP290 after the Test.  (X10DC also allows a Self-Test to be invoked
without event preservation, but this leaves the device in a state
which may cause problems with other programs that communicate with
the CP290. It is recommended that the Self-Test always be invoked
with Event Preservation regardless of whether or not there is any
stored Event Data.)

15. SIGNAL TEST GENERATOR
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The Signal Test Generator is a powerful feature that enables the
user to track down and isolate X-10 transmission/reception problems
and faulty modules.  This feature will send X-10 ON/OFF commands
repeatedly until the test is ended by the user.  (Similar to the
Leviton 6385 device).  The address to be targetted for commands can
be a fixed House Code and Unit Code; alternatively, either the House
Code or Unit Code (or both) can be varied. This allows you to send
commands repeatedly to:

ù A 'Fixed' House Code & 'Fixed' Unit Code (eg. A1)
ù A 'Fixed' House Code & 'Variable' Unit Code (eg. A1 - A16)
ù A 'Variable' House Code & 'Variable' Unit Code (ie. A1 - P16;
  All 256 addresses would be tested in this case)
ù A 'Variable' House Code & 'Fixed' Unit Code (eg. A1 - P1)

When the Signal Test Generator is selected, a window is
displayed that allows you to set the House Code & Unit Code to
either 'Fixed' or 'Variable' mode; if 'Fixed' is selected then
a List Box is enabled so that the fixed code can be selected.
The Delay between commands can be set from 0 to 60 seconds;
this delay applies to the pause between each pair of ON/OFF
commands.  Once all required settings have been made the OK
button becomes enabled.  When the OK button is clicked the
test will begin; the test can be terminated by pressing [Esc].
Note, if the Delay is set to 0, then the [Esc] key may have to
be hit several times to stop the Signal Test.  X10DC will emit
a brief beep before each ON command is sent, and another lower
pitched beep before each OFF command is sent.  These beeps can
be disabled by toggling the Sounds item on the 'Options'
Menu.

'Fixed' Mode Testing
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Generally speaking, you would want to use the 'Fixed' option
to test the range of X-10 signal reception by starting the
Signal Test using address P1 for example (the "only" address
that the Leviton 6385 will test) and then walking around to a
variety of outlet locations within your home and plugging in a
module set to P1 to see if the ON & OFF commands are being
received at all locations.  The program attempts to let you
know when the commands are sent by beeping although you may
not be able to hear the beep from all outlet locations.

'Variable' Mode Testing
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The 'Variable'(*4) option can be used when you suspect that an
X-10 module has trouble receiving commands targetted for
specific House and/or Unit Codes.  In this case, instead of
walking around to locations, you would adjust the House and/or
Unit Code dials on the module as the Signal Test cycles
through each combination.  You may want to toggle the Sounds
off in this case.

ÄÄÄÄ
(*4) Not available in UNREGISTERED Version

16. CLOCK SYNCHRONIZATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Clocks tend to run either fast or slow and therefore should be
synchronized periodically.  X10DC allows you to set the time in both
the PC and CP290 manually by specifying hh:mm and also allows you to
synchronize the PC and CP290 by using one of the clocks to set the
other.  When the PC clock is used to synchronize the CP290 clock,
X10DC will wait until the seconds are at zero since the resolution
of the CP290 clock is limited to minutes.  (This wait can be
cancelled by pressing the [Esc] key).  When the CP290 is used to
synchronize the PC, the hours and minutes from the CP290 are used
immediately to set the PC Clock; since the CP290 cannot provide
'seconds', it is recommended that a CP290->PC Clock Sync be followed
by a PC->CP290 Clock Sync.  This will ensure that both Clocks are
synchronized.

17. BASE HOUSECODE
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
The Base HouseCode stored in the CP290 is only applicable to the
rocker keys on the top of the CP290.  These keys are labelled 1 to 8
and correspond to whatever House Code is stored as the Base
HouseCode in the CP290.  The CP290 re-initializes itself whenever
the Base HouseCode is changed; as a result, all of the CP290 Event
Data is erased.  X10DC gives you the option of either Preserving or
Erasing the Event and Icon Data whenever the Base HouseCode is
changed.  If the user elects to preserve the Event Data, it is
downloaded from the CP290 before the Base HouseCode is changed and
then uploaded back to the CP290 after the Base HouseCode has been
changed.

18. PROBLEM RESOLUTION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Generally, if your CP290 works with the X-10 supplied software then
you should have no problems running X10DC.  The program will load if
you run it without any arguments (thereby defaulting to COMMPORT 1)
and your CP290 is actually attached to COMMPORT 2.  If this is the
case X10DC will report an error when it attempts to retrieve the
Time and Base HouseCode.  You can toggle to the correct COMMPORT
once the program is running by using the Options menu.  In future
you should include the Command Line argument /C2 if your CP290 is
connected to COMMPORT 2.  The Save Options menu option will save all
settings to the X10DC.INI which obviates the need for command line
arguments.

If you run X10DC with a modem attached to the COMMPORT, you may get
unpredictable results since the modem will echo everything back to
X10DC.

If you are sure that the X10DC is using the correct COMMPORT and
problems persist, try using Debug mode and then scroll through the
Command History List Box; see if the calculated checksums match;
look at the TIMER and MaxTimer Values. If the MaxTimer Value exceeds
the TIMER value then the program is timing out while waiting for
X-10 responses. PLEASE REPORT ANY TIMING PROBLEMS TO ME; adjustments
can be made to the program to improve its compatibility if this
turns out to be a problem.  As a last resort, run the CP290 Self
Test, but only do so if you have backed up your EVENT DATA using a
program you are sure works within your operating environment.
(X10DC will preserve the CP290 Event Data but if you are
experiencing problems with X10DC then this function may fail).

In some cases X10DC may report that a command failed, or a checksum
did not match, but in fact the command was accepted by the CP290 and
transmitted on the powerline.  This could happen if spurious
responses are received from the CP290, ie.  if you were to press the
rocker buttons on the CP290 just after sending a command.  If this
happens, exit the program and re-invoke it to resynchronize,
alternatively, if you have 2 serial ports you could try toggling the
CommPort. (ie. if your CP290 is on CommPort 1 then switch to
CommPort 2, then switch back to CommPort 1).

The open architecture of the PC compatible operating environment and
the near infinite combinations of hardware and software complicate
the compatibility of applications software.  While every effort has
been made to ensure that X10DC is compatible with all
hardware/software combinations, there may be operating environments
in which X10DC will not run properly.

Problems can be reported to:

   David Huras
   37 Ruddell Crescent
   Georgetown, Ont. L7G 5N4
   CANADA

   FAX: 905-873-6429
   CIS: 72767,472
   Internet: david.huras@canrem.com

19. REGISTRATION INFORMATION
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
X10DC is currently supplied as fully functioning software without
built-in delays or obtrusive "nag" screens prompting you to
register.  The ABOUT screen contains registration information in
case this documentation file gets misplaced.  A significant amount
of time and effort went into this program; please register the
program if you intend to use it beyond the 30 day evaluation period.
Registered Users will be shipped a printed manual and a 3«" diskette
(if you would prefer a 5¬" diskette please advise) containing the
Registered Version of the program which includes the following
features:

ù Full support for the Signal Test Generator which allows you to
  cycle through all House & Unit Codes and send an ON/OFF command
  to each address.

ù Full support for operating mode 3 which reads in an X10.DAT file
  and builds a "list box" of device names which can be targetted
  for X10 commands.  (Unregistered Version will only send commands
  to the first 8 Devices).

ù Support for an INI file which provides complete program
  customization capabilities including Screen Colours.

ù BONUS PROGRAM: Registered Users will also receive a bonus
  program; X10DAT reads an X10.DAT file and prepares a report
  listing all installed devices and scheduled events including
  "frozen" events and multiple unit events. See X10DAT.RPT for
  a report sample.

Charge the registration fee to your Visa, Master Card, American
Express by ordering X10DC (Item #10924) from Public (software)
Library, call 800-242-4PsL (713-524-6394 overseas) or FAX your
order to 713-524-6398.  These numbers are for ordering only.
ALL OTHER INQUIRIES (eg. technical support, volume discounts
site licensing) should be directed to the author: see PROBLEM
RESOLUTION section.

   -=OR=-

Register by sending $20 (cheque/money order) to:

   David Huras
   37 Ruddell Crescent
   Georgetown, Ont. L7G 5N4
   CANADA

Alternatively, you may wish to register using CompuServe Shareware
Registration; you can register X10DC, X10EC or BOTH using CompuServe
Shareware Registration.  The Registration Fee will be charged to
your CompuServe billing account and the latest version of the
software will be shipped within one business day. GO SWREG while on
CompuServe to use Shareware Registration.

Program Title         Program Name    Program ID#   Charge
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   ÍÍÍÍÍÍÍÍÍÍÍÍ    ÍÍÍÍÍÍÍÍÍÍÍ   ÍÍÍÍÍÍÍ
X-10 Direct Control      X10DC             620       $20.00
X-10 Event Control       X10EC            1774       $25.00

X-10 Control Bundle      X10CB            1775       $40.00
(X10DC + X10EC)

Shareware Registration (SWREG) will prompt you through the
registration process; you can register programs by referring to them
by program name or ID #.  SWREG will display a description of the
program and prompt you to confirm the registration order; you have
the opportunity to abandon the registration process at any time.

ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
ºREGISTERED USERS of prior versions of X10DC can upgrade to theº
ºcurrent version at ANY TIME by simply sending a diskette      º
ºcontaining their registered version of the software and $2    º
ºfor postage to the address above.                             º
ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

20. OTHER HOME AUTOMATION SOFTWARE by David Huras
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Program   Description                                     Status
-------   ------------------------------------------   --------------
X10DC     X10 Direct Control - CP290 Point & Click     Version 1.50
          Initial Release: February '93                December '93

X10EC     X10 Event Control - CP290 Point & Click      Version 1.00
          Interface Program to manage Event Data.      December '93
          Includes Sunrise/Sunset Time Offsets.
          Initial Release: December '93

IRDC/     INFRA-RED Direct Control/Command Line Ctrl   Version 1.01
IRDQ      A program which sends instructions to a      October '93
          ONE FOR ALL (6 or 12) remote control. The
          remote then emits I/R signals.

IRDCW     INFRA-RED Direct Control for WINDOWS         Version 1.00
                                                       Development

ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
Please register this software if you use it regularly; by registering
you reinforce my commitment to ongoing development.
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

21. RELEASE HISTORY ù X10DC Shareware/Registered Version
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
 Date      Version     Changes
------   ----------   ----------------------------------------------
DEC'93    1.50        þAdded support for 5 UNDOCUMENTED CP290 Cmds
                      þAdded support for ICON Data Preservation
                      þOptimized screen layout for all 3 Modes
                      þAdded support for EGA/VGA 43/50 Line Mode
                      þAdded graphic 'percentage complete' gauges
                      þCountdown Timer added to Status Window while
                       waiting for CP290 responses.
NOV'93    1.42        þCorrected problem reporting Base House Code
                       when CP290 returns bad data.
AUG'93    1.41        þPublic (software) Library registration method
                       added to documentation.
                      þX10DAT Bonus Program added as registration
                       benefit.
                      þX10DC.INI File Comment re: X10File argument
                       corrected in documentation.
AUG'93    1.40        þCorrected 'Load X10 File' problem when X10.DAT
                       located in Root Directory.
                      þCorrected problem whereby X10DC.INI was not
                       processed when X10DC was started from a Root
                       Directory (impacted Registered Version only).
AUG'93    1.40 á      þCOMMPORT 3 & 4 Support Added.
                      þUser Defined CommPort support Added.
                      þMinor changes to default colours (LABELS).
JUL'93    1.32        þCorrected problem with DEBUG MODE colour setting
                       not 'sticking'; setting from INI is workaround.
                       (Not released).
JUL'93    1.31        þFixed mouse cursor reset problem if Signal Test
                       is run without a CP290 device. (Not released).
JUL'93    1.30        þENABLED SEND Command under MODE 3 in Unregistered
                       version for 1st 8 Devices in X10.DAT File
                      þENABLED ALL Clock Sychronization options in
                       Unregistered version
                      þENABLED Change Base HouseCode with Event
                       Preservation in Unregistered version
                      þENABLED Screen Colours dialogue in Unregistered
                       version
                      þTest menu item added to Menu Bar;
                       ù CP290 Self Test disassociated with Debug Mode
                         and Self Test button removed from Screen
                         Header; Self-Test feature now a sub-menu
                         item under Test.
                       ù Signal Test Generator feature added; send
                         ON/OFF commands repeatedly to a fixed/variable
                         House Code/Unit Code address.  Unregistered
                         version supports the fixed option only.
                      þHelp Sub-system added; contains additional
                       X10 background information as well as extracts
                       from the documentation file.
                      þ/NH command line argument added to optionally
                       not load the help system for faster program
                       load times.
                      þ/NS command line argument added to disable
                       sounds generated during the Signal Test.
                      þSounds Toggle added as a sub-menu item under
                       Options.
                      þINI Overwrite warning now uses the WARNING
                       screen title colour(*5)
                      þ'Save Options' displays a message box whenever
                       INI options are saved(*5)
                      þThe access key for the 'Exit' option under the
                       'File' menu changed from 'E' to 'x'.
                      þ[Esc] key will now back out any screen
                       colour changes while in the Screen Colours
                       dialogue
                      þ[Esc] key will now skip the wait while
                       SYNC'ing the CP290 clock based on the PC
                       Clock
MAR'93    1.20        þMerged Shareware & Registered Versions;
                       Registered Version features are disabled in
                       the Unregistered version, specifically:
                         ù Complete Mode 3 Support (X10.DAT File)
                         ù Complete Screen Color Customization
                           Dialogue
                         ù INI File Support to save/modify
                           Program settings/colors
                         ù Preserve/Restore Event Data when
                           Base House Code changed
                         ù PC ¯ CP290 Clock Synchronization
                         ù CP290 ¯ PC Clock Synchronization
                      þENABLED Self Test EVENT Preservation
                       in Unregistered version
                      þENABLED MODE 3 Switch & X10.DAT File Load
                       in Unregistered version (SEND-Disabled)
                      þENABLED some Clock Functions, & Base House
                       Code Setting in Unregistered Version
                      þCP290 Self Test changed to reset interface
                       upon completion (The self test overwrites
                       the Event Data and this data may cause
                       problems with some programs)
                      þAdded /BW command line argument to startup
                       with monochrome color settings
                      þAdded 'Refresh' menu item to refresh on-screen
                       Clock Displays
                      þError handling improved
                      þRetry logic added for all CP290 communications
                       with automatic wait time adjustment (if program
                       times out waiting for a response, it will
                       increase the wait time if the command is retryed)
                      þCommand History caption now indicates which
                       entry is highlighted (ie. entry x of n)

MAR'93    1.10        þMENU BAR Added - CommPort,Mode, & Debug can
                       now be changed using the Options Menu
                      þMode Indicator added to Screen Header
                      þMinor Screen Colour modifications

FEB'93    1.00        þMode Switch Command Button Added (Alt-M)
                      þDebug Command Button TAB Stop disabled-keyboard
                       users must use ALT-T
                      þCIS Software Registration # added to ABOUT

FEB'93    1.00 á.02   þOperating Mode 2 Added (FIRST PUBLIC RELEASE)
                      þOperating Mode 3 Added to Registered Version
                      þClock/Base House Code manipulation added to
                       Registered Version

JAN'93    1.00 á.01   þDebug Mode Added

JAN'93    1.00 á.00   þInitial Beta (not publicly released)

ÄÄÄÄÄÄ
 (*5) Applicable to REGISTERED VERSION Only.