************************************************************************
*                                                                      *
*   ASMGEN.COM - by J. Gersbach   and  J. Damke    (Ver. 2.01)         *
*                                                                      *
*   A program to generate cross-referenced assembly language code      *
*   from any executable file.                                          *
*                                                                      *
*                                                                      *
*   Uploaded to PCanada by Mark Magner   November 23, 1983             *
*                                                                      *
************************************************************************


*  PREFACE  *

              This program will generate 8086/87/88 assembly code text
         that is compatible with the Macro Assembler from any
         executable diskette file up to 65,535 bytes.  The output can
         be routed to the console or a diskette file.  A cross
         reference may be generated separately or embedded at the
         appropiate instruction counter address in the assembly code.

              Some manual touch up will be required before reassembly,
         but nearly all the typing is done for you by ASMGEN and
         anything questionable is marked with "??".

              A file of sequential instructions may be resident on the
         same diskette to indicate to ASMGEN which addresses contain
         code, byted, words, or strings.  This file may also include
         instructions to assume segment register values or toggle the
         output of assembly code text, generation of the cross
         reference table, 8087 mnemonics, or of the inclusion of
         embedded reference information in the assembly file.

              DEBUG may be used to browse through the executable file
         to determine the starting locations of code and data to
         develop the sequential instruction file.  It is important to
         accurately specify these locations for an accurate reference
         table and minimum touching up of the ASM output text.

              The number of references within the file determines the
         amount of memory required since a reference table is built in
         memory during the first pass.  Disassembly is done from disk
         and only one file sector is in memory at any given time.
         Therefore memory size does not limit the size of the file to
         be disassembled.  48K bytes of memory will be enough for most
         programs but a few will need 64K or 128K.  One diskette drive
         is sufficient but two is more convenient.


*  STARTING ASMGEN  *

              There are two ways to work with ASMGEN:  either by using
         the command menu or by calling ASMGEN with parameters.
         Following are the descriptions of both options.

*  USING THE ASMGEN MENU  *

              The program is invoked by typing:  ASMGEN

              You are then prompted for a file specification.  Respond
         with the name of the executable file from which you wish to
         generate the assembly code.  The executable file will
         normally have an extension of .EXE or .COM.  ASMGEN will
         check this file spec for validity and then respond with a
         prompt that includes a summary of the command letters
         indicating that you may give it a command.  The executable
         file contents are not checked for valid code and ASMGEN will
         try to disassemble text or compressed BASIC files and produce
         unintelligible assembly code.

The commands are:

X filespec      This file spec replaces any previous executable
                file spec.  The usual file extension is .COM
                or .EXE

                EXAMPLE:  X DATE.COM


A <filespec>    The executable file is disassembled and the assem-
                bly code is routed to the specified file.  The
                usual file extension is .ASM.  If the filespec is
                omitted, the output will default to the console.

                EXAMPLE:  A DATE.ASM

R <filespec>    The reference table is sent to the file specified.
                The usual file extension is .TBL.  If the filespec
                is omitted, the output will default to the console.

                EXAMPLE:  R DATE.TBL

Q               The program is terminated and control returned to
                DOS.


              Each time a command has been executed, ASMGEN waits with
         a one line prompt for the next command.

              X <filespec>, A <CON>, R <CON> or Q ?

              The default filespec for each command is shown in
         brackets.  Enter the next command as described above.


* USING ASMGEN WITH PARAMETER CALLS *

              Up to three file specifications may be included when
         ASMGEN is first called from DOS.  The executable file's name
         is given first, followed by specifications for the assembly
         and reference table files.

EXAMPLE:  ASMGEN DATE.COM, DATE.ASM, DATE.TBL

              If a semicolon follows the last filespec, ASMGEN will
         exit to DOS when the command has been executed.  If no
         semicolon is entered, ASMGEN will display the menu options
         described above and wait for further input after executing
         the command.

EXAMPLE:  ASMGEN DATE.COM, DATE.ASM;

              If the filespec for the .ASM file and/or .TBL file is
         omitted, ASMGEN will generate first the .ASM file, then a
         .TBL file using the filename of the first filespec.

EXAMPLE:  ASMGEN DATE.COM,,; creates DATE.ASM and DATE.TBL and exits
                             to DOS.

              If only the reference table is desired, the dummy name
         NUL should be entered in place of an .ASM filespec

EXAMPLE:  ASMGEN DATE.COM, NUL, DATE.TBL

              If only one filespec is given when the program is
         called, the reference table is built in memory and then the
         menu options are displayed for further commands.

EXAMPLE:  ASMGEN DATE.COM


*  PROGRAM EXECUTION  *

              The disassembly is done in two passes through the
         scource file.  On pass #1, the reference table is built in
         memory and the actual output is generated during pass #2.
         Once the reference table is established, it remains in memory
         until an X or Q command is issued, and subsequent A and R
         command executions skip pass #1.  This saves a lot of time
         when the executable file is large.

              Three contiguous data areas are built dynamically in
         memory during pass #1.  First is the compressed sequential
         instruction list.  Second is a list of pointers for .EXE
         files that point to the locations of all relocatable
         variables in the program, also arranged in numerical order.
         These are established before reading any code.  Third, the
         reference table is then built in a higher area of memory as
         pass #1 progresses.

              If all available memory in the program segment is filled
         before the first two data areas are completed, ASMGEN will
         abort to the command prompt.  After the reference table is
         started, a shortage of memory will produce the message
         "Reference Table Incomplete Due to Insufficient Memory" and
         continue.

              Ctrl-Break may be used at any time to interrupt a
         command in progress.


*  READING THE ASSEMBLY CODE FILE (.ASM)  *

              This file begins with a title taken from the executable
         file's name and date followed by the current date (in
         brackets).

              If not inhibited by the M switch in a SEQ file
         (explained later), the macro library will appear next in the
         file.

              Next will be a .RADIX 16 pseudo-op which tells the macro
         assembler that all numbers are in hexadecimal form.

              Then comes a header that indicates a starting value for
         the code segment, stack segment, instruction pointer and the
         stack pointer.  The stack pointer is usually set to FFFF for
         .COM files but may be somewhat less depending on available
         memory.  These values are passed by the linker for .EXE
         files.

              The first ASSUME statement might come next.  There is
         one generated for each segment that begins with code.  All
         segment registers are designated according to the current set
         of ASSUMEs.  They will sometimes be incorrect, so all ASSUME
         statements should be checked prior to re-assembly.

              The disassembled output follows, terminated by an END
         statement and the execution address.  An ORG psuedo-op is
         included if required.

              The text is compatible with the IBM Macro Assembler and
         the format is the same except for RETurns.  To avoid the need
         for PROCedure titles, special mnemonics are provided for all
         RET instructions.  These are defined in the macro library at
         the beginning of the file.  Only macros that are needed for
         the current file are produced.  The optional embedded
         commands that make up the reference table enhance the
         readability of the file.  For very large files, this is
         sometimes undesirable and a separate reference table is best.

              When invalid instructions are encountered in code areas,
         they are reproduced as byte values followed by "??".  If a
         near jump is defined previously in the code, and it is within
         range of a short jump, a NOP instruction is inserted after
         the jump.  The executable file created with this .ASM file
         and the Macro Assembler and Linker will then be the same
         length as the original file.  This makes it less important to
         differentiate between labels and numeric constants since the
         label values and their offsets within the file will be the
         same.  The fundamental problem of disassembly is in knowing
         if the original assembly code defined a number as a label
         which changes as a function of it's position or as a number
         that always remains the same.  If you make changes in the
         assembly code however, you must properly specify all values.
         You might as well remove all NOPs at the same time.

              Labels are five characters long and begin with "L".
         Segment labels begin with "S".  The remaining characters are
         the current instruction counter in hex form, thus making each
         label unique and showing it's location in the original file.
         The instruction counter is continuous throughout the assembly
         code without resetting at segment boundaries.  The segment
         labels are then in byte as opposed to paragraph form.  In
         those cases where a label value is modified by an ASSUME
         statement, the original value is included as a comment in the
         referencing instruction so that it may be easily changed back
         if it was not intended as a location.

              The word "Relocatable" is printed at the end of any line
         that contains an ablolute paragraph value.  These are values
         that DOS modifies after loading but before executing a
         program.  They are used for loading segment registers that
         are sensitive to the program location in menory.  Relocatable
         values are not modified by ASSUMEs.  ASMGEN converts these
         numbers from paragraph to byte values by multiplying them by
         sixteen so that they will fit within the 16-bit instruction
         counter field.  When the paragraph value is negative or
         exceeds 0FFFH, it is left unchanged and a warning (??) is
         issued on that line.  When a program larger than 64K bytes is
         being disassembled, it should be divided into smaller files.

              All words are produced as labels, except when the "L"
         switch has been enacted in the .SEQ file (explained later).
         The label name indicates it's numeric value and, if it does
         not occur on an instruction boundary, the name indicates it's
         position relative to the current instruction pointer is given
         by an EQU statement.  Therefore the Macro Assember will
         assume that it is a location, but it is easily changed to a
         constant since the value is given in the label name.  The
         word OFFSET precedes a label whenever it is questionable
         whether it is a label or an immediate value.  You must decide
         which of the labels should be constants and which of the
         constants should be labels, and change them accordingly.
         When changing labels to numbers, be sure to append an "H" if
         the number ends with a "D" or a "B" since the Macro Assembler
         will otherwise assume that it is decimal or binary.

              Bytes are always treated as constants.  An optional
         switch may be included in the .SEQ file (explained later)
         which enables numbers instead of labels if all references to
         the value are data segment and immediate operation types.

              An effective procedure to follow in attempting to
         understand the assembly code file is to look first for the
         message text area, the input commands, and the simpler
         subroutines.  Then add label names to addresses in the .SEQ
         file (explained later) that remind the you of their purpose.
         Add comments to the labels.  If these names are well chosen,
         the larger routines eventually will become clear.  The
         embedded references are produced as labels so they will
         retain their meanings as they are changed.

              It is also helpful to spend some time studying the
         structure of data areas.  Vector tables, which are frequently
         used to control the program's flow, reveal the program's
         structure very quickly.  If some routines do not have labels
         at the beginning, it is usually because the code or tables
         that reference them (or the segment register assumptions) are
         not properly defined in the .SEQ file.


*  READING THE REFERENCE TABLE (.TBL)  *

              A referencee is defined as a number that is referenced
         somewhere in the program.  It may be a program loaction or a
         numeric constant.

              A referencor is is defined as the address in the program
         from which a refer- ence is made to the referencee.

              Each entry is composed of a referencEE followed by a
         list of referencors.  If more than one line is needed,
         additional lines are indented to the first referencor
         position.  The referencEE is followed by an "S" if it
         includes references to the beginning of segment.  The
         referencor is followed by two letters, the first of which
         represents the segment register that is implied or prefixed
         in the referencing instruction.  The second letter indicates
         the type of operation on the referencEE.  When the reference
         entries are embedded in the assembly code, all values are
         preceded with the letter "L".

----------------------------------------------------------------------------
1st letter      |  2nd letter
SEG REGISTER    |  TYPE OF OPERATION
----------------------------------------------------------------------------
C  code         |  J  jump         M  modify - INC, ADD, etc.
S  stack        |  C  call         I  immediate - value or offset
D  data         |  R  read         T  test or compare
E  extra        |  W  write        ?  unknown or ESC instruction
                |  P  port
----------------|-----------------------------------------------------------



*  WRITING/READING THE SEQUENTIAL INSTRUCTION FILE (.SEQ)  *

              The sequential instruction file is a list of special
         instructions to ASMGEN which the user creates.  The file
         takes the form of a list of hexadecimal addresses and
         single-letter instructions or generation switches.  If used,
         the .SEQ file must be on the same diskette as the source file
         and have the same name as the source file with an extension
         of .SEQ.  Each instruction in the file must be in one of the
         following formats:

addr    command
or
addr    command         ;comment
or
addr    command         label   comment
or
addr    command         label   comment ;comment

              "addr" represents the instruction pointer value.  All
         addr values must be in numerical sequence in the file.

              "command" may be either a toggle switch or a generation
         instruction.

              "label" is optional and replaces the label generated for
         this address with this non-blank string.

              "comment" is optional and must be preceded by "label"
         unless the dummy label "." is used.  Everything following
         "label" is treated as an address comment and will be printed
         in the ASM file behind the generated instruction.  The
         address comment may be up to 255 characters in length and
         should not contain a semi-colon.

              ";comment" is optional.  Anything following a semi-colon
         in the .SEQ file instructions is considered as a comment in
         the .SEQ file only and is not added to the generated .ASM
         file.

              "label" and "comment" are not allowed when a generation
         switch is coded, but a ";comment" may be used to help clarify
         the .SEQ file.

              The .SEQ file is read into memory before the first pass
         starts.  The addresses and commands will be compressed, but
         "label" and "comment" will be held in memory one to one.  An
         effect of this is that memory space required for dis-
         assembly increases with each "label" and "comment" added to
         the .SEQ file.


*  DESCRIPTION OF GENERATION SWITCHES  *

              THE VARIOUS TOGGLE SWITCHES ARE SET TO ON BY DEFAULT.
         Switches may be toggled on and off at any point in the .SEQ
         file/disassembly.

              All options switches except /M and /H can be either
         toggled or directly set by the user.  A suffix of "+" turns
         the switch ON, and a suffix of "-" turns the switch OFF.
         Switches encountered in the file that have neither of these
         suffixes are toggled to the opposite of their state at the
         time; ON switches are turned OFF and OFF switches are turned
         ON.

/B - generate byte references

              When ON, byte and word references are included in the
         reference table.  When OFF, only word references are
         generated.

/E - embedded references in ASM file

              When ON, reference table entries are inserted in the
         text just before the referencee's definition statement.  When
         OFF, these entries are not included with the disassembled
         text.  The entire reference table can be printed with the "R"
         command.

/F - 8087 mnemonics

              When ON, ESC instructions are produced.  When OFF, ESC
         instructions are assumed to be 8087 instructions and 8087
         mnemonics are produced.

/H - append hex "H"

              When this switch appears at any point in the .SEQ file,
         an "H" is appended to all hex numbers.  This does not, of
         course, apply to the labels which are hex values preceded by
         the letter "L".  The .RADIX 16 pseudo-op is omitted which
         allows the assembler's radix to default to decimal.  This
         switch defaults to NO H APPEND.  Note that it will be set
         only once.  It retains it's value until the next .SEQ file is
         read.

/L - generate label or number

              When ON, all word references are treated as labels.
         When OFF, a word reference is treated as a constant if all
         referencors are data immediate types.

/M - suppress macro library

              When this switch appears at any point in the .SEQ file,
         no macro library is included in the text output.  The DEFAULT
         IS THAT THE MACRO LIBRARY WILL BE INCLUDED.  Note that this
         switch will be set only once.  It retains it's value until
         the next .SEQ file is read.

/O - control ASM output

              When ON, ASMGEN will output the generated text.  When
         OFF, output will be suppressed.

/R - control TBL output

              When ON, ASMGEN will output the generated reference
         data.  When OFF, the reference table is not printed.

/T - control trace output

              When ON, up to 16 bytes of object code are included as
         comments in each line of the assembly code file.  When OFF,
         object code is not included.


*  DESCRIPTION OF .SEQ FILE COMMANDS  *

A - assume

              The following lines contain ASSUMptions for segment
         register values.  They become effective at the address
         specified by this instruction and may be modified anywhere in
         the disassembly.  The required format for assumptions is:

& 0400  DS

              The ampersand indicates a continuation of the A
         instruction.

              In this example, a data segment beginning at a
         instruction pointer value of 400 will be assumed until
         another A instruction changes it.  CS, ES, and SS are also
         supported.  The segment assumptions are used for effective
         address calculations only.  The code segment assumption does
         not affect the instruction pointer value.

B - bytes

              The bytes encountered in the source file are assumed to
         have meaning as single byte values.

C - code

              The bytes encountered in the source file are assumed to
         be valid 8088 machine language instructions.

D - generate data operand

              The operand of the instructions is changed to immediate
         data.  Subsequent bytes are interpreted as "C" (code
         follows).

I - initial value for IP

              The hexadecimal value on this line overrides the
         instruction pointer value at the beginning of the file - not
         to be confused with the address at which execution begins.
         The default values are 0000 for EXE files and 0100H for COM
         and other files.  The execution address following the END
         statement is omitted if this option is invoked.

S - strings

              The bytes encountered in the source file are assumed to
         form text.  Quoted text is produced for valid ASCII
         characters and byte values for others.

# - defined length strings

              The first byte encountered in the source file contains
         the length of the character string which begins with the next
         encountered character.  This length value may be overridden
         by a subsequent SEQ file instruction.

$ - defined length strings

              The first byte encountered in the source file contains
         the length of the character string which begins with the next
         encountered character plus the length byte itself.  This
         length value may be overridden by a subsequent SEQ file
         instruction.

W - words

              Pairs of bytes encountered in the source file are
         assumed to have meaning as word values.

X - repeating data structure

              A cyclic data structure is assumed to begin at the
         specified instruction pointer value.  The structure
         definition may follow and is prefixed by an ampersand (&) to
         indicate the continuation of this instruction.  If the
         definition does not follow, then the most recent definition
         is used.  If no structure is yet defined, then an error
         message is displayed.

              The following elements may be used to define the
         structure:

& NNNN S  -  The next NNNN bytes are defined as string characters
& NNNN B  -  The next NNNN bytes are defined as byte values
& NNNN W  -  The next NNNN bytes are defined as word values
& XXNN $  -  The next sequence of bytes is defined as NN fields.  Each field
             consists of a length byte and a string of characters.  The length
             of each field is contained in the first encountered byte.  The
             high nibble (XX), if non-zero, is a bit mask of the length field
             within the byte.  The length field is right-justified within the
             byte after the byte value is sent to the output file.



*  EXAMPLES OF .SEQ COMMANDS  *

              This example .SEQ file shows all the possible
         instructions in the appropriate format.

;All switches are on at the beginning.
0       /T      ;no object code as comments in output
0       /M      ;no macro library in output
0       /H      ;append "H" to all numbers
00H     /A      ;assume the following segment values
;Note that the ampersand (&) indicates the extended ASSUME
& 380   DS      ;the data segment starts at 380 hex
& 380   ES      ;the extra segment starts at 380 hex
0200     I      ;initialize the instruction pointer to 200
0200    /F      ;introduce 8087 mnemonics (not ESC)
0200    /E      ;no embedded references
0200     C      ;code begins at 200
0203H    W      ;words are at 203
0207     C      ;more code starting here
220      X      ;complex data structure begins here
& 3      W      ;words
& 1      B      ;byte
& 0E02   $      ;2 strings starting with the 2nd byte follow
                ;bits 3,2,1 of the first byte contain the length of the
                ;string including the length byte.
                ;the high nibble (0E) is the mask.
                ;see also # in summary below
& 1      B      ;byte
                ;the structure repeats until 351
351      B      ;bytes
358      C      ;more code
380      S      ;strings - list of messages
421      W      ;words
4FD     /B      ;no further byte references
502     /R      ;garbage here - turn off reference generation
502     /O      ;and output
600H    /O+     ;valid code - turn output back on
600     /R
600      C
1A60    /O-     ;output file about to fill diskette - turn output off but keep
                ;scanning for references.
                ;another run will be needed to get the remaining code.
1B00    /D      ;treat operand as immediate data
1DFD    /B+     ;continue with byte references
1F45     W      user_prt        ;user provided labels will translate
2256     S      $MSG            ;to upper case


              Comments may be included if preceded by a semicolon.

              Alphabetic characters may be either upper or lower case.

              An "H" may follow the hex address.



*  SAMPLE SESSION  *

              The external command CHKDSK.COM will serve as an example
         for this sample session because it is short.  The .SEQ file
         is also short and easy to generate.  Only these few
         instructions are needed.


0100  /T  ;include object code as comments in .ASM file
0100  /E  ;simpler output without references
04F7H  S  ;messages
04F7H /H  ;append "H" to numeric values

              Using DEBUG, browse through CHKDSK.COM to see how this
         was arrived at.  Usually, but not always, the best procedure
         is to assume code.  If the code appears unintelligible,
         display it in hex/ASCII.  If it is not text, assume bytes.
         Label positions in the first disassembly may indicate that
         some locations should be words.  Next, generate the .ASM file
         by typing

ASMGEN CHKDSK.COM <enter>
A                 <enter>

The assembly code can be viewed on the screen.  Then type:

A CHKDSK.ASM      <enter>

to save the assembly source code to a file.  Then,

R CHKDSK.TBL      <enter>

to save the cross-reference table to disk.

              The Macro Assembler, Link.exe and Exe2bin could now be
         used to assemble CHKDSK.ASM, link it to .EXE and convert it
         to a .COM file.  No modification should be necessary in this
         case.

              If working with code that is to be modified, the symbol
         types must be correctly specified as locations or as
         constants.  If they are constants, place them outside of any
         segment.  The label names may then be changed to make the
         code more readable.