TABLE OF CONTENTS

                         Description ..................2

                         Syntax .......................2

                           Labels .....................3

                           Opcodes ....................3

                           Operands ...................4

                           Pseudo ops .................5

                        Error Messages ................6

                        Source code ...................6

                        Disclamer .....................7

                        Op code table .................8


















                                        1











                                   DESCRIPTION
              ASSEMBLE.COM is a two pass assembler written in Turbo
        Pascal. It was written because I was a new owner of an IBM PCjr
        with little software and I was not aware of any public domain
        assemblers that had reasonable performance. Additionaly I had
        reciently purchased Turbo Pascal from Borland International and
        wanted a project to help me learn Pascal.

             ASSEMBLE.COM  is  a  simple assembler  for  Intel  8088/8086
        instruction set. It closely follows the syntax of the instruction
        set described in THE 8806 BOOK by Russel Rector and George Alexy.
        It is also patterened after CHASM.BAS version 1.9 written in
        basic by David Whitman of Whitman Software (there have been
        numerious changes to avoid copywrite violations). It is not a
        macro assembler and therefore recognizes only a few pseudo op
        codes. Listed later in this documemtation is a complete list of
        op codes and pseudo ops recognized by ASSEMBLE.COM.

             The input requirememts to ASSEMBLE.COM are ordinary DOS
        files which can be created with most text editors. The output
        will be a listing sent to the screen, printer or a disk file and
        a .COM file. This assembler was designed to creat executeable
        code or subroutines used in BASIC or Turbo Pascal programs. It
        will not generate code that can be linked to other other
        programs. See your BASIC or TURBO instruction manuals for
        includeing executable code in your programs. Since this assembler
        is intended for small projects you will probably find bypassing
        the Link and conversion from .EXE to .COM files is a convience.
        If you intend to write large software projects, I recomend you
        get a macro assembler such as IBM's or CHASM version 4.0 (also
        written in Turbo Pascal). Speaking of size, since both the input
        file and output file(s) are on the disc the only limitations to
        the size of your program is the disk space, number of labels you
        use and your endurance. Labels and their memory address are
        stored on the first pass in ASSEMBLE.COM's area for dynamic
        variables. This area uses all avaliable memory above the program
        area therefore even on a 64K byte system you should have plenty
        room for several hundred labels. My goal is to keep this program
        under 35K bytes so it can be run on small systems.

                                     SYNTAX
             Each line of source code begins with a label or blank space
        followed by the op code (8088 instruction or pseudo op) and then
        the operand(s) (if required by the opcode). The source code may be
        followed with a semi colon (;) and any commemts for that line.
        Optionaly a line may be only comments if it starts with a semi
        colon. A blank space must preceed and follow the op code field.
        For readability I recomemd one or more spaces between the label
        and the op code and between the op code and the operand. A comma
        must be used to seperate operands.




                                        2








        EXAMPLE:

        1stLabel mov  ax,90H    ;format example

        Labels:
             Although labels may be longer only the first 7 letters of
        the label are stored for future reference therefore any labels
        with the first seven characters the same will cause a duplicate
        label error. Also since the line parsing routine converts all
        source code not in single quotes to upper case prior to decodeing
        the line, you can not use upper and lower case to distinguish
        labels. For example LongLabel1 and longlabel2 are both stored as
        LONGLAB therefore would cause an duplicate label error. If you
        are going to use numbers to distinguish labels I suggest you use
        them at the beginning of a label such as 2LongLabel.

        Op Codes:
             All of the op codes specified in THE 8086 BOOK are supported
        however in order to resolve some ambiguous op codes the syntax
        was modified. The first ambiguous opcode is JMP which can be
        either a 8 or 16 bit displacement jump. Eight bit displacement
        jumps are resolved by specifying JMPS for short jump. Jumps
        useing mem/reg (indirect) addressing for their destination must
        specify Near or Far to indicate a jump within the current CS or
        an intersegment jump. These jumps are coded as JMPN or JMPF. This
        same logic is used for CALLN and CALLF when useing the mem/reg
        addressing mode. The other major area of ambiguity comes from
        useing op codes that do not specify a register as either the
        destination or source. This assembler requires you to append the
        op code with a B or W to distinguish between bytes and words ie.
        MOVSB for move a string of bytes or MOVW [bx],8 to load 8 into
        the word address pointed to by BX.

             Normally all data moves are assumed to be relative to the DS
        (data segment) register. This default can be over ridden one
        instruction at a time by useing the SEG op code in the line prior
        to the desired over ride.
        EXAMPLE:
                   SEG   ES
                   MOV   AX,[BX]
        This moves a word into the accumulator from the address in the
        extra segment offset by the bx register. This is a little used
        function since ASSEMBL assumes all of the segment registers are
        set to the same location as is required for the start of a .COM
        program. Access of system resources should be done with BIO or
        DOS calls when possible rather than going directly to a hardware
        memory location outside your program.

             The opcode table lists the avaliable opcodes and pseudo ops
        and the various addressing modes associated with each. Please
        note that the mem/reg addressing mode includes several sub modes
        such as base relative (useing BX as an offset), stack relative
        (useing BP as an offset), and indexed (useing the SI or DI). See
        the 8086 BOOK for an explination of each mode.



                                        3









        Operands:
             The operands describe to the assembler the destination and
        source of the data to be operated on. The 8088 uses a number of
        addressing modes to determine where that data is and should go.
        You will discover by looking at the op code table, not all modes
        can be used with an individual op code. Addressing modes are :

          Accumulator - data is transfered to/from the accumulator.
          Displacement - the displacement value is added to the present IP.
          Immediate - data is assembled into the instruction.
          Memory/Reg - data is transfered to/from address pointed to
                       by [mem] or [reg].
          Register - data is transfered to/from the register.

        Accumulator: The accumulator(s) are AX or AL and AH where AX is a
        16 bit accumulator, AL is the lower 8 bits of AX and AH is the
        higher 8 bits.

        Displacement: A displacement value to be added to the instruction
        pointer (IP) is included as immediate data in the opcode. The
        assembler calculates the amount of displacement based on the
        location of the opcode and then location of the address in the
        operand. The address in the operand can be expressed as a number
        (binary,hex or decimal) but is most commonly expressed as a
        label. EXAMPLE:

        LABEL MOV AX,[BX]
              CMP AX,10H
              JLE LABEL

        With this example the assembler calculates a negative
        displacement to jump back to LABEL when then value in AX is less
        than or equal 10H.

        Immediate: All immediate data is assembled into the instruction
        code. This data can be represented in two ways. First immediate
        data can be presented in binary, decimal or hexidecimal format in
        a signed range of -32768 to 32767 (8000H to 7FFFH) or if the sign
        bit is not used, 0 to 65535 (0000H to FFFFH). As in these
        examples a 'H' is appended to the number to indicate hexidecimal.
        Binary numbers are expressed as a series of up to 16 ones and
        zeros followed by a B, ie 11010B represents 26. The other method
        of representing immediate data is with labels. The value of the
        label is the address at which the label was used or the value
        assigned to the label in an EQU pseudo op. When useing labels in
        the operand for data access the assembler assumes you are
        reffering to the data in the refferenced address. If you want to
        load the value of the address itself then the modifier OFFSET(..)
        must be used.
        EXAMPLE:

             MOV BX,LABEL         ;Load BX with the value at address Label
             MOV BX,OFFSET(LABEL) ;Load BX with the address of Label



                                        4








        Some math is supported when useing immediate data however the
        number parser is very simple therefore the format is restricted.
        Only one math operator is  permited between numbers (-3*4 is ok
        but 4*-3 gives an error). Parseing is done from left to right
        with no presience set for the math operator (+ or * are
        interpeted when recieved in the input string verses the usual of
        interperting multiplication and division before addition and
        subtraction).

        Memory/register: This addressing mode is also called indirect
        addressing. The operand is used to point to a memory location
        that contains the data rather than the instruction containing the
        data as in the immediate addressing mode. The operand can be a
        memory location expressed as a label, decimal number or a
        hexidecimal number or it can be a memory location pointed to by a
        register. The following indirect modes are allowed:
              MOV Reg,[BP]
              MOV [BX],Reg
              MOV [BX+SI],Reg  ;BX plus SI displacement equal location
              MOV Reg,[BX+DI]  ;BX plus DI       "        "      "
              MOV Reg,[BP+SI]  ;BP plus SI       "        "      "
              MOV [BP+DI],Reg  ;BP plus SI       "        "      "
              MOV [DI],Reg
              MOV Reg,[SI]
              MOV LABEL,Reg
        Any of the general purpose registers can be used in place of Reg
        in these examples. Immediate data may also be substituted for a
        register however then the opcode most be appended with W or B so
        the assembler knows if you are pointing to a word or byte
        address. In addition to the above when an indirect address useing
        a register is chosen a displacement may also be used.
        EXAMPLE:

              MOV Reg,10H[BP]     ;Source address equal BP+10H
              MOV Reg,-5[BP+SI]   ;Source address equal BP+SI-5
        DEMO  EQU FFH
              MOV DEMO[BX+DI],Reg ;Destination address equal BX+DI+255

        Register: In this addressing mode the data is contained in or is
        to be stored in one of the 8088 registers. The  registers are AX
        (AL+AH), BX (BL+BH), CX (CL+CH), DX (DL+DH), BP, DI, SI  and the
        four segment registers CS, DS, ES, SS. All math operations use
        the accumulator (AX, AL or AH) plus the MUL and DIV use the DX
        register when 32 bit numbers are involved. The BX and BP
        registers can be used as base pointers in the Data or Stack
        segments respectively. The CX register can be used for a
        automatic counter for some instructions. As demonstrated in
        earlier examples the SI and DI registers can be used as indexing
        registers. Any of the numerious assembly language books for the
        IBM PC or PCjr will give you an explination of each of the
        processor registers and their uses.

                                 PSEUDO OPCODES
             Pseudo opcodes are assembler directives that control the
        generation of the object code. The avaliable pseudo ops are DB,


                                        5








        DS, DW, ENDP, EQU, ORG and PROC.
          DB = define byte and has operands of one or more bytes and/or
               a string ( DB 20H,'Demo' ). Strings are set off by single
               quotes. Numbers are less than 256 and expressed in binary,
               decimal or hexidecimal.
          DS = define segment and initializes a string of memory
               locations. The first operand defines the number of bytes to
               be initialized. If included the second operand defines the
               value the memory is to be initialized to. The default value
               is zero. ( DS 20,FFH ;initialize 20 bytes to 255).
          DW = define word and its operand(s) must be numeric or a
               label. With DW the low order byte is stored first in memory
               as this is the format used by the 8088 for integer storage
               (ie: dw 1020H = db 20H,10H).
          EQU= define the value of a label. All label definitions must
               occur at the beginning of your program or errors may occur
               in the assembly process. The most common error message
               recieved from defining a label late in the program is 'PHASE
               ERROR'. A phase error indicates the assembler generated a
               address for a label on the second pass different from that
               of the  first pass.
          ORG= reset the location counter to new orgin. Since all .COM
               programs start at 100H the default setting for ASSEMBLE.COM
               is 100H however you may have a need to start at 00H for a
               driver routine or a machine language routine for BASIC.
          PROC and ENDP are used together to define a program or procedure
               as Near or Far. This information is used to determine the
               type of return to be generated when a RET is encountered.
               If no procedure is defined a Near procedure is assumed. The
               syntax is:
               PROC NEAR ;Proc must be followed by Near or Far
               ....
               ....
               ENDP
               If PROC is used an ENDP must be used.


                                 ERROR MESSAGES
             All error messages and diagnostics are printed immediately
        before the line in which the error occurs. The total number of
        error and diagnostic messages will be displayed at the end of the
        source code print out immediately prior to the symbol table dump.
             I have made an attempt to make error messages as user
        friendly as possible. The most criptic of the error messages is
        the series you recieve when there is a syntax error. This message
        will be the opcode and ASSEMBLE.COM's interpetation of the type
        of data included in the operands.
        EXAMPLE:
        *** Syntax Error: MOV (16 bit immediate or 8 bit immediate), (none)

        This message would appear immediate before a line of code
        containing the instruction MOV 45H. By reviewing the type of data
        and the allowable operands for each instruction you should be
        able to locate the error.
             'Phase Error' is most commonly caused by referenceing an


                                        6








        equate before defineing it. I strongly recomend you only use the
        EQU pseudo op at the beginning of your source code. This pratice
        should prevent this error and will make your source code more
        easier to read.
             'Error: EQU without symbol' is recieved when you use the equate
        pseudo-op without a label.
             'Error: EQU with forward refference' is recieved if you
        attempt to use a forward refference when equating a label.
             'Error: ENDP without PROC'. You must specify where the
        procedure begins.
             'Error: Missing ENDP'. You must specify where the procedure
        ends if PROC is used.
             'Error: Procedures nested too deeply'. Only 10 levels of
        nesting are allowed.
             'Error: Duplicate label'. See section on labels.
             'Error: Data too long' indicates use of a byte operand where
        the data is out of the range of 0 to 255.
             'Error: Too far for short jump' indicates an attempt to jump
        further than +or- 127 bytes.
             'Error: Undefined Symbol' plus the operand being interpeted
        is displayed when no match is found in the symbol table.
        Frequently caused by bad syntax in the operand.
             'Error: Illegal or undefined argument for OFFSET' is simular
        to 'Undefined Symbol'

             Two diagnostic messages may be given. The first follows a
        syntax error and is 'Specify word or byte operand' if the
        assembler could not determine which to use. The opcode must be
        corrected by appending a B or W to it. The other message is just
        a notice that you used a long jump where you could have used a
        short jump and saved a byte of object code.

                                   SOURCE CODE
             Turbo Pascal source code for this assembler is avaliable for
        those who wish to customize it for their own needs (or those who
        would like to see what makes it tick). If you would like a copy
        of the source code send a formated disk and $10 to
                                 George Fulford
                                 RR 1 Box 163c
                                 Shellsburg Ia 52332
        Although I have no intentions of entering the software market at
        this time I do plan to make corrections to this program as the
        bugs are found. If you obtain a copy of the source code from me
        it will be the most up to date version.

                               WARRENTY/GUARANTEE
             There is NONE.
             This assembler runs on my PCjr and since I used all standard
        Turbo Pascal it should run on any PC DOS machine. If it does not
        I probably won't be able to help you.

        I have spent quite a bit of time debuging but I am sure there are
        still a few bugs lurking in the code. I will attempt to stamp out
        any reported.



                                        7









                                  OP CODE TABLE
             addressing modes supported  (b/w = must specify byte or word)
             A = acumulator reg(ax, ah, al)
             b/w = must add B or W to opcode for this addressing mode
             D = displacememt (8 or 16 bit as required by the instruction)
             I = immediate (byte for 8 bit registers, word for 16 bit reg)
             M/R = memory or register (indirect addressing)
             N = none
             R = register(bx, cx, dx, bp, si, di)
             S = segment register (cs, ds, es, ss)
         Op                   Operand
        types
          dest.  N | A |  A  | R | R | M/R |  R  | M/R | I | I | D | M/R
          source N | I | M/R | I | N |  R  | M/R |  I  | I | N | N |  N
        AAA      x |   |     |   |   |     |     |     |   |   |   |
        AAD      x |   |     |   |   |     |     |     |   |   |   |
        AAM      x |   |     |   |   |     |     |     |   |   |   |
        AAS      x |   |     |   |   |     |     |     |   |   |   |
        ADC        | x |     | x |   |  x  |  x  | b/w |   |   |   |

        AND        | x |     | x |   |  x  |  x  | b/w |   |   |   |
        CALL       |   |     |   |   |     |     |     | x |   | x |
        CALLF      |   |     |   |   |     |     |     |   |   |   |  x
        CALLN      |   |     |   |   |     |     |     |   |   |   |  x
        CBW      x |   |     |   |   |     |     |     |   |   |   |

        CLC      x |   |     |   |   |     |     |     |   |   |   |
        CLD      x |   |     |   |   |     |     |     |   |   |   |
        CLI      x |   |     |   |   |     |     |     |   |   |   |
        CMC      x |   |     |   |   |     |     |     |   |   |   |
        CMP        | x |     | x |   |  x  |  x  | b/w |   |   |   |

        CMPS   b/w |   |     |   |   |     |     |     |   |   |   |
        CWD      x |   |     |   |   |     |     |     |   |   |   |
        DAA      x |   |     |   |   |     |     |     |   |   |   |
        DAS      x |   |     |   |   |     |     |     |   |   |   |
        DB         |   |     |   |   |     |     |     | x | x |   |

        DEC        |   |     |   | x |     |     |     |   |   |   | b/w
        DIV        |   |  x  |   |   |     |     |     |   |   |   |
        DS         |   |     |   |   |     |     |     | x | x |   |
        DW         |   |     |   |   |     |     |     | x | x |   |
        ENDP     x |   |     |   |   |     |     |     |   |   |   |

        EQU        |   |     |   |   |     |     |     |   | x |   | memory
        HLT      x |   |     |   |   |     |     |     |   |   |   |
        IDIV       |   |  x  |   |   |     |     |     |   |   |   |
        IMUL       |   |  x  |   |   |     |     |     |   |   |   |
        IN         | x |note1|   |   |     |     |     |   |   |   |







                                        8








         Op                   Operand
        types
          dest.  N | A |  A  | R | R | M/R |  R  | M/R | I | I | D | M/R
          source N | I | M/R | I | N |  R  | M/R |  I  | I | N | N |  N
        INC        |   |     |   | x |     |     |     |   |   |   | b/w
        INT      x |   |     |   |   |     |     |     |   | x |   |
        INTO     x |   |     |   |   |     |     |     |   |   |   |
        IRET     x |   |     |   |   |     |     |     |   |   |   |
        JA         |   |     |   |   |     |     |     |   |   | x |

        JAE        |   |     |   |   |     |     |     |   |   | x |
        JB         |   |     |   |   |     |     |     |   |   | x |
        JBE        |   |     |   |   |     |     |     |   |   | x |
        JCXZ       |   |     |   |   |     |     |     |   |   | x |
        JE         |   |     |   |   |     |     |     |   |   | x |

        JG         |   |     |   |   |     |     |     |   |   | x |
        JGE        |   |     |   |   |     |     |     |   |   | x |
        JL         |   |     |   |   |     |     |     |   |   | x |
        JLE        |   |     |   |   |     |     |     |   |   | x |
        JMP        |   |     |   |   |     |     |     |   |   | x |

        JMPF       |   |     |   |   |     |     |     |   |   | x |
        JMPN       |   |     |   |   |     |     |     |   |   | x |
        JMPS       |   |     |   |   |     |     |     |   |   | x |
        JNE        |   |     |   |   |     |     |     |   |   | x |
        JNO        |   |     |   |   |     |     |     |   |   | x |

        JNP        |   |     |   |   |     |     |     |   |   | x |
        JNS        |   |     |   |   |     |     |     |   |   | x |
        JNZ        |   |     |   |   |     |     |     |   |   | x |
        JO         |   |     |   |   |     |     |     |   |   | x |
        JP         |   |     |   |   |     |     |     |   |   | x |

        JPE        |   |     |   |   |     |     |     |   |   | x |
        JPO        |   |     |   |   |     |     |     |   |   | x |
        JS         |   |     |   |   |     |     |     |   |   | x |
        JZ         |   |     |   |   |     |     |     |   |   | x |
        LAHF     x |   |     |   |   |     |     |     |   |   |   |

        LDS        |   |     |   |   |     |note2|     |   |   |   |
        LEA        |   |     |   |   |     |note2|     |   |   |   |
        LES        |   |     |   |   |     |note2|     |   |   |   |
        LOCK     x |   |     |   |   |     |     |     |   |   |   |
        LODS   b/w |   |     |   |   |     |     |     |   |   |   |

        LOOP       |   |     |   |   |     |     |     |   |   | x |
        LOOPE      |   |     |   |   |     |     |     |   |   | x |
        LOOPNE     |   |     |   |   |     |     |     |   |   | x |
        LOOPNZ     |   |     |   |   |     |     |     |   |   | x |
        LOOPZ      |   |     |   |   |     |     |     |   |   | x |






                                        9








         Op                   Operand
        types
          dest.  N | A |  A  | R | R | M/R |  R  | M/R | I | I | D | M/R
          source N | I | M/R | I | N |  R  | M/R |  I  | I | N | N |  N
        MOV   note3|   |  x  |   |   |  x  |  x  | b/w |   |   |   |
        MOVS   b/w |   |     |   |   |     |     |     |   |   |   |
        MUL        |   |  x  |   |   |     |     |     |   |   |   |
        NEG        |   |     |   | x |     |     |     |   |   |   |
        NOP      x |   |     |   |   |     |     |     |   |   |   |

        NOT        |   |     |   | x |     |     |     |   |   |   | b/w
        OR         | x |     | x |   |  x  |  x  | b/w |   |   |   |
        ORG        |   |     |   |   |     |     |     |   | x |   |
        OUT        |   |note1|   |   |     |     |     |   |   |   |
        POP        |   |     |   | x |     |     |     |   |   |   |x or seg

        POPF     x |   |     |   |   |     |     |     |   |   |   |
        PROC  note4|   |     |   |   |     |     |     |   |   |   |
        PUSH       |   |     |   | x |     |     |     |   |   |   |x or seg
        PUSHF    x |   |     |   |   |     |     |     |   |   |   |
        RCL        |   |     |   | x |     |     |     |   |   |   | b/w

        RCR        |   |     |   | x |     |     |     |   |   |   | b/w
        REP      x |   |     |   |   |     |     |     |   |   |   |
        REPE     x |   |     |   |   |     |     |     |   |   |   |
        REPNE    x |   |     |   |   |     |     |     |   |   |   |
        REPNZ    x |   |     |   |   |     |     |     |   |   |   |

        REPZ     x |   |     |   |   |     |     |     |   |   |   |
        RET      x |   |     |   |   |     |     |     |   |   | x |
        ROL        |   |     |   | x |     |     |     |   |   |   | b/w
        ROR        |   |     |   | x |     |     |     |   |   |   | b/w
        SAHF     x |   |     |   |   |     |     |     |   |   |   |

        SAR        |   |     |   | x |     |     |     |   |   |   | b/w
        SBB        | x |     | x |   |  x  |  x  | b/w |   |   |   |
        SCAS   b/w |   |     |   |   |     |     |     |   |   |   |
        SEG        |   |     |   |   |     |     |     |   | x |   |
        SHL        |   |     |   | x |     |     | b/w |   |   |   |

        SHR        |   |     |   | x |     |     | b/w |   |   |   |
        STC      x |   |     |   |   |     |     |     |   |   |   |
        STD      x |   |     |   |   |     |     |     |   |   |   |
        STI      x |   |     |   |   |     |     |     |   |   |   |
        STOS   b/w |   |     |   |   |     |     |     |   |   |   |

        SUB        | x |     | x |   |  x  |  x  | b/w |   |   |   |
        TEST       | x |     | x |   |  x  |  x  | b/w |   |   |   |
        WAIT     x |   |     |   |   |     |     |     |   |   |   |
        XCHG       |   |note5|   |   |  x  |  x  |     |   |   |   |
        XLAT     x |   |     |   |   |     |     |     |   |   |   |

        XOR        | x |     | x |   |  x  |  x  | b/w |   |   |   |

        note 1 IN/OUT supports  DX<-acum(8 or 16) and  port<-acum(8 or 16).


                                       10








        note 2 These instructions can use only memory refference
               in the source operand.
        note 3 MOV also supports mem<-acum  seg<-M/R  and  M/R<-seg(or CS).
        note 4 Must specify near or far PROCedure.
        note 5 The accumulator can be exchanged with any of the registers
               using the form XCHG AX,BX or XCHG BX





         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

                  Disks in the library are updated monthly.
         For a copy of the latest monthly software library newsletter
          and a list of the 800+ disks in the library, call or write

                        The Public (Software) Library
                               P.O.Box 35705 K
                           Houston, TX 77235-5705
                               (713) 721-6104

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.