ESCREEN DESIGN AIDF


                                 Copyright 1983

                                       by

                                   DD Systems


















             Dan Daetwyler
             Route 5, Box 518A
             Springdale, AR 72764
             501-756-0212







           





        Screen Design Aid - Version 3.0


        EPREFACEF

             This is a T.P.I.R product!  (The Price Is... Reasonable?)  I 
        object  to  paying  half the price of my hardware  for  a  single 
        software  package,  so  I'm trying to do something about  it.   I 
        believe  that there are enough "micros" around to make a  reason-
        able  return on your labor investment through  volume...  if  you 
        don't  have  to pay substantive advertising and marketing  costs.  
        If  you're reading this document,  you have the package.   It  is 
        copyrighted, so what are your rights?  They are given here:

        --  You are free to copy, and encouraged to distribute to any/all 
             of your friends,  the materials included in the distribution 
             diskettte.  Please include this document.

        --  You  may use these materials in any way you see fit,  but you 
             may  not "sell" the package.   You may use screens  designed 
             using the package in commercial products,  and the  $SDA.OBJ 
             module and the $FIELD.MAC macros are hereby declared "Public
             Domain",  so  you  are free to use those in your  commercial 
             endevors.

        Where's the "catch"?   Simple.   Its up to you.   If you use this 
        package, and like it, send me a check for $25.  Otherwise, thanks 
        for experimenting!   What do you get for the $25, besides a clear 
        conscience?   Not much.  I'll put you on my mailing list and when 
        (not  if) bugs are encountered,  I'll notify you and  offer   our 
        handy, dandy copy service, which incidentally is available to all 
        your friends for their initial copy,  if you don't want to bother 
        copying   the  diskette.    I'll  also  notify  you  when  future 
        developments  are available:   within a few weeks,  we'll have  a 
        programmers  full  screen  editor,  a  catalog  facility,  and  a 
        reasonable "batch" listing capability that makes use of all those 
        "goodies" hiding in the EPSON printer.  

             The copy service mentioned,  is also simple:  Send diskette, 
        mailer, and enough postage to the writer and we'll make a copy of 
        the distribution diskette for you.  If you don't want to send the 
        diskette,  mailer,  et al., send a check for $7.50 and we'll send 
        you a new Verbatim with the materials.

        DISCLAIMER (Or I really don't want to be sued!)

        Although  reasonable  testing  has  been  conducted,   under   no 
        circumstances will the author be liable to you or any third party 
        for  any damages,  including lost profits or other incidental  or 
        consequential damages arising out of the use of, or the inability 
        to use,  this software.  Further the offers made in this document 
        are  subject to withdrawal at any time and without  notification, 
        and prices quoted are subject to change without notice.      







        Preface                         2





        Screen Design Aid - Version 3.0


                                TABLE OF CONTENTS

        Preface .........................................  2

        Introduction ....................................  4

        Organization of Document ........................  6

        Basic Operation .................................  7

        Saving a Screen ................................. 12

        Loading an Existing Screen ...................... 14

        Field Definition/Maintenance .................... 15

        Printing Screens ................................ 19

        Printing Field Tables ........................... 20

        Changing Display Device ......................... 21

        Color ........................................... 22

        Line Lengths .................................... 23

        Application Interface ........................... 24

        High Level Languages ............................ 27

        Technical Reference ............................. 30

        Error Messages .................................. 32
         























        Table of Contents               3





        Screen Design Aid - Version 3.0


        EINTRODUCTIONF

             The  Screen  Design  Aid  (SDA,  henceforth)  is  a  utility 
        designed   to  permit  effective  exploitation  of  the   graphic 
        capabilities  of  the IBM Personal Computer,  when  operating  in 
        "text"  mode.   It  requires a relatively minimal  configuration, 
        operating  on something less than a 64K machine euipped  with  at 
        least  one  diskette  drive,  and utilizing at least one  of  the 
        display interfaces (Monochrome or color/graphic) provided by IBM. 
        It  can be used with monitors of either 40 or 80  character  line 
        resolution, and will operate in either "black and white" or color 
        mode.  IBM DOS (or equivalent) is required.

             Basically, it does no more than provide a relatively simple, 
        fast  method  for  laying out display screens for  use  in  other 
        processes.  This "trivial" task happens to be a relatively labor-
        ious job and is usually more than painful.   The display hardware 
        provided is excellent, and includes a fairly comprehensive set of 
        "graphic" characters than may be displayed in "text"  mode.   Un-
        fortunately,  no effective means for utilization of this facility 
        was  provided.   The user is forced to perform detailed  clerical 
        "coding" at the individual character level if he or she wishes to 
        exploit the excellent character set.  This utility elminates that 
        "coding",  and  provides a few other fringe benefits that  should 
        find a lot of friends.

             Before  going  to  more detail,  fair  warning!   If  you're 
        looking  for  a  true  "graphic"  capability  for  use  with  the 
        color/graphic  board,  this ain't it!   This utility operates  in 
        "text" mode exclusively,  and is limited to the graphics that can 
        be  formed  using  the read only memory  (ROM)  based  characters 
        provided by the hardware.  

             Having  said at least one thing its not,  what is  SDA?   It 
        provides the following functions:

             -- Permits  the  definition  of  a  "screen"  utilizing  any 
                  combination of the 254 displayable characters.

             -- Captures this definition in a compressed form, usually a 
                  few  hundred  bytes versus the 4000  required  for  the 
                  actual screen.

             -- Permits 4full5 exploitation of the attribute byte (eg:
                  high intensity, blink, underscore, reverse, et al).

             -- Provides  simple  "maintenance"  of the  image,  so  that 
                  required modifications are "painless".









        Introduction                    4  





        Screen Design Aid - Version 3.0


             -- Allows for definition of up to 100 fields on each screen, 
                  where the "field" is limited only by line length. 
                  Fields,  incidentally,  may have their own  (different) 
                  attributes.  The application using the screen may then
                  easily:

                  *  Output to a field

                  *  Position (cursor) to a field

                  *  Clear a field

                  *  Input from a field (destructively/non-destructively)

                  *  Out/In from a field (output followed by input)

             -- Provides a convenient interface that may be "bridged"
                  to most "high level" compiled languages.  A minimum
                  bridge to BASIC is provided, and sufficient data for
                  development of other bridges is included in this 
                  document.

             -- Provides full color support for those users equipped with
                  the color/graphics interface.

             -- Provides both 80 and 40 character line support for users
                  with the color/graphics interface.

             -- "Memory cost" for the application is limited to slightly
                  over   500  bytes  PLUS  the  size  of  the  compressed 
                  screen(s) used.

             -- Utilizes  "memory mapped" I/O,  so performance is  easily 
                  within human response thresholds.

             -- Liberally provided with "help" menus and prompt aids, to 
                  assist in "learning" the system.

             -- Provides documentation support by permitting print of the
                  resulting screens (and their field tables), on EPSON
                  MX80 with GRAFTRAX plus.

        In short,  provides all the facilities needed for the "bread  and 
        butter" application utilizing interactive display screens.













        Introduction                    5  





        Screen Design Aid - Version 3.0


        EORGANIZATION OF DOCUMENTF

             Because of the variety of interfaces,  display devices, line 
        lengths,  etc., it would be easy to become so involved in details 
        as to make use of the utility appear complicated.  It is not!  To 
        avoid this pitfall,  this document begins by ignoring some of the 
        more  sophisticated uses of the utility.   The next sections will 
        "walk  through" development of a screen,  and will  not  consider 
        which  display  adapter  or line length your machine  happens  to 
        have.   The  following  sections  then  explore  different  "Line 
        lengths"  and "Color".  

             A  section  on use of screens in applications  is  then  in-
        cluded,  together  with  a "cook book" for interfacing with  high 
        level  languages.   A "technical reference" section is  included, 
        which provides insight into the compressed screen,  field tables, 
        etc., for the user that wishes to know more than you need to know 
        to  use the utility.   Finally,  a very brief "error" section  is 
        included,  to  cover the few primitive error conditions that  may 
        occur during use of the utility.  

             It  is  suggested  that all users follow  through  the  next 
        section.   Beyond that section, you can "pick and choose" to suit 
        your  operating environment and needs.   The next section assumes 
        you  will bring the utility up on your machine,  and  follow  the 
        text with use of the utility.  To prepare for that process, it is 
        suggested that you copy the file, SDA.COM to a work diskette, and 
        maintain  your distrubution diskette as a "master  backup".   The 
        file  is  NOT protected,  and you are free to copy it  using  the 
        standard DOS utilities (see Preface for your "rights").  The file 
        is  approximately 24,000 bytes,  so be sure you have a relatively 
        empty diskette.  

























        Organization of Document        6





        Screen Design Aid - Version 3.0


        EBASIC OPERATIONF

             Assuming  that DOS is loaded and running,  simply enter  the 
        "command":

                       SDA

        As  soon as the load process is complete,  you will see, on  what 
        ever  display  you happen to be using,  the main "menu" for  SDA.  
        This menu lists the major functions available under SDA,  and you 
        may   select   any  function  by  entering   the   single   digit 
        corresponding  to the function,  and depressing the "enter"  key.  
        If  you happen to hit a wrong digit,  the error prompt giving the 
        acceptable  range of values,  and a request to "depress any  key" 
        will appear.  

             Since we're starting "cold", enter "1" -- a request to enter 
        "edit/create".   Your  screen will immediately "clear"  with  the 
        exception  of a few cryptic characters on the lowest line of  the 
        display.   A  flashing cursor will be in the upper left corner of 
        the screen.  

             Before explaining the "prompt line" (lowest line), let's try 
        something else.   Depress function key 9 (hereafter given as F9).  
        Again,   the  screen  immediately  changes,  but  this  time  its 
        relatively  full  of "text".   Don't bother to read it  all  now.  
        We'll come back to it many times in the next few paragraphs.  For 
        now,  notice the last line "depress any key to exit", and hit the 
        space bar (or any other key).   Whap!  Back to the "edit screen".  
        As you'll discover,  anything that was displayed on this  screen, 
        before entering "help" mode, will be restored after "help" mode.

             Now  lets look at the prompt line.   The first two fields on 
        the  left  are relatively obvious:   the row and  column  of  the 
        current  cursor  position (zero,  zero).   Let's move the  cursor 
        around a bit.   Use any of the arrow keys on the numeric key  pad 
        or the "backspace" key.   If you happen to display numeric digits 
        rather  than  see the cursor move,  you have the "Num  Lock"  key 
        depressed.  Depress it once, and try again.  OK now?

             Two things to note, as you move the cursor.  The prompt line 
        display "tracks" the cursor,  by showing the current row/col each 
        time  a key is depressed (yes,  the "typematic" function works  - 
        hold a key down,  and watch the cursor fly).   Second, the cursor 
        "wraps" the screen.   If you go off the right side,  you enter on 
        the  same line on the left side.   Similarily,  exit/entry on the 
        top  and  bottom of the screen also "wraps".   Depending  on  the 
        device you're using,  you'll find that the last column is  either 
        39  or  79.   The "bottom" row is 23,  since we're using line  24 
        (25th line) for the prompt (but you can use it too...  we'll talk 
        about that later).  

             OK,  that should be enough watching the blinking light  move 
        around.   Position  the  cursor  to any convenient point  on  the 
        screen,  and key in "data".   "Data", by the way is about all the 


        Basic Operation                 7





        Screen Design Aid - Version 3.0


        other  keys on the keyboard,  with the exception of the  function 
        keys,  the numeric keypad keys, and use of the "control" or "Alt" 
        key  combinations.   For example,  hit the "enter"  key.   That's 
        strange...  a music note appeared, and the cursor advanced!  Well 
        that's  just  what it should do.   Other than the  normal  cursor 
        advance after a character entry, all cursor movement must be made 
        by using the numeric keypad "arrow" keys.   Carriage  return/line 
        feed  just  happens to be two valid  graphic  characters.   Since 
        we've  got 254 of them and only about 90 keys,  we're frugal with 
        keys.   It'll   feel  a little strange for a  short  period,  but 
        you'll get used to it quickly.  One trick is to "wrap" the screen 
        and then move down one line.  

             Experiment  with  the keys a bit.   Don't  use  the  numeric 
        keypad  keys  or function keys,  yet,  but anything else is  fair 
        game.   Screen getting messy?   OK, hit F9, and we're back to the 
        "help"  screen.   Scan  down the list to F8 -- Erase  screen  and 
        field table.   Hit any key,  and we're back to the mess you left.  
        Now try F8.   Whoops!   What happened?   Screen went  blank,  and 
        there's  this "Are you sure?" message on the prompt line.   First 
        let's say "N" for no.   Back to the mess!   Ok,  now lets try  F8 
        again, and this time respond "Y" to the protection against fumble 
        fingers.   That's  better.   Blank screen,  prompt line restored, 
        cursor back to the upper left corner... in fact just like when we 
        started.  

             You  may  use  F8 any time you  desire.   Just  remember  -- 
        anything you haven't saved to disk is LOST, LOST, LOST.  

             One more little "housekeeping" exercise.   Type any  message 
        you  like on the screen.   F9 to see the "help" screen,  and this 
        time  scan down to F10 -- Exit to Main Menu.   Hit any  key,  and 
        confirm that your message is still there.   OK, now hit F10.  And 
        we're back to the main menu we started with.   Ho hum,  so  what?  
        Well  enter a "1" again,  and when you return to the edit  screen 
        you'll  see your message is still displayed.   SDA will save  the 
        current screen through all of its manipulations.   In fact, there 
        are  only  two  ways to getting rid of it.   One  you've  already 
        learned,  F8,  to  clear the screen.   The other is to  "load"  a 
        "saved" screen over the top of the current screen.  

             So far, about all you've got is a very limited single screen 
        editor...right?   OK,  lets start to play a bit.  F9, and look at 
        F3 - Toggle Normal/Reverse video.  While you're here, look at F4, 
        F5 and F6 also.  F3 through F6 all control the "attribute" of the 
        character  you're keying to the screen.   Hit any key,  and we'll 
        see how they work.   First hit F3.   The prompt line changed.  In 
        the field following "At:",  the "N" (for normal) became "R"  (for 
        reversed).   Now  key in some data (yes,  the space bar is data), 
        and watch the characters appear black on white, rather than white 
        on  black.   I'll  mention that the "FG:" and "BG:"  fields  also 
        changed,  but  we'll worry about them in the section on  "Color".  
        You can ignore them throughout this section.  

             One  of  the  exercises  you can  perform  is  to  note  the 


        Basic Operation                 8





        Screen Design Aid - Version 3.0


        difference  between the space bar and the right arrow key.   When 
        you're in reverse video,  the difference is noticable.  The space 
        bar is "data",  but the right arrow is not.   Useful when  you're 
        either trying to move over something without eraseing it, or when 
        you do want to erase.  

             I  won't bother telling you to hit F8 when your screen  gets 
        messy.   Hit F3,  and return to normal video.   Now hit F4.  This 
        time  the  prompt line displays a "B" for "blink".   Key in  some 
        data and watch it flash!.   Hit F4 to turn blink off, and hit F5.  
        An "H" for "high intensity" appears, and the data you key will be 
        displayed  at the "high intensity" level of your display  device. 
        F5 to turn it off,  and F6 to see "U" (for underscore) and  watch 
        your data appear with the "underscore".  

             Now that you've seen it work, try various combinations.  All 
        but one is permissable, although one is of doubtful utility.  You 
        may  not have "reverse" video and "underscore" active at the same 
        time.   You've  probably already noticed that you can't get  this 
        combination  on  the  prompt line.   The reason  is  a  "hardware 
        limitation",  so  SDA  won't  allow  it.   "High  intensity"  and 
        "reverse video" is the "doubtful" combination.   SDA will  permit 
        it, but it sure won't be used for any normal case.  

             Now  do  the F9 and look at the last several lines  -- those 
        labeled "Home",  "PgUp",  "PgDn", "Ins", and "Del".  Hit any key, 
        and we'll try "Ins" and "Del" first.   Position your cursor to  a 
        mid  point  of a string,  and hit the "Del" key.   As  you  would 
        expect,  a single character was deleted,  while the right side of 
        the  line  was shifted left -- blank inserted at the  right  end.  
        Now tap the "Ins" key.   The "In" flag appears on the prompt line 
        to  warn you that you're in "insert mode",  and data entered will 
        be "inserted" into the line at the cursor.  The right side of the 
        line if shifted right to make room.   Characters shifted off  the 
        end of the line went into the "bit bucket", and are lost.  Delete 
        works  each  time you depress the key.   Insert "toggles" a  mode 
        switch,  and you remain in insert mode until the next  depression 
        of the "Ins" key.

             That  was about what you would have expected,  but the  next 
        gets a bit more "tricky".   Move your cursor to the bottom screen 
        line (line above the prompt line),  and enter a data string.   Do 
        the  same thing with the top line.   Now depress the "PgUp"  key.  
        Three  things happened.   First,  an "up arrow" appeared  on  the 
        prompt  line,  indicating  that you're "shifted".   The top  line 
        disappeared from the display,  and all lower lines were moved  up 
        one.   Finally,  the  bottom line showed up blank.   Move back to 
        that bottom line (blank), and key in another string.  Now hit the 
        "PgDn" key.   Your original top line reappears,  the new  "bottom 
        line" disappeared, and the old bottom line shifted down to become 
        the  current  bottom  line.   What's all this?   Not  that  much.  
        Remember,  I  told  you that you could use all 25  lines  of  the 
        display, even though SDA used one for the prompt line?  Well this 
        is  the  mechanism that lets you do  that.   Normally,  the  edit 
        screen  is displaying the first 24 lines of the completed screen.  


        Basic Operation                 9





        Screen Design Aid - Version 3.0


        When "shifted",  it displays lines 2 through 25 (1 through 24  if 
        you start with zero).   All 25 lines are "remembered" and will be 
        in your completed screen,  however.  This shift function lets you 
        use  that  bottom  line just as you would any other line  on  the 
        display.  

             Of the last group of keys we noted, we've still got one left 
        -- "Home".   This  one is not appropriately  labeled,  so  you're 
        memory will have to serve.  To see it most effectively, do the F8 
        bit, and then key a single word at the left margin of the screen.  
        With  the cursor still on the line containing the word,  hit  the 
        "Home" key.   Centered!   That's all it does.   Specifically,  it 
        will  center the string defined by the left most non-blank to the 
        right   most  non-blank  characters.    I'm  tired  of   counting 
        characters  and  computing the leading  blanks,  and  this  works 
        nicely.

             The  F7 key will be discussed in the section on "Color",  so 
        just ignore it now.
         
             OK,  that's  all...  but two of the keys defined on the help 
        screen.   Where  are  the "graphics"?   That's  those  keys,  but 
        they're  at least two topics themselves.   If you glance  at  the 
        help  screen,  you'll see that F1 is defined to "toggle" graphics 
        mode, while F2 is defined to "assign graphic characters".  Before 
        we can use graphics,  we'll have to "assign" some,  so let's talk 
        about F2 first.  

             This  is  the  function  that  gets  around  the  apparently 
        unsolvable  problem of having less than half as many keys  as  we 
        have  characters  to play with.   Poke F2 and let's see  what  we 
        have...    Ugh,  what a mess.  That's every displayable character 
        available  on  the machine,  with the exception of the  "standard 
        data" characters we've been using.   To keep from getting  bogged 
        down in mechanics,  let's do this quickly.   The cursor is in the 
        upper left corner, and the "happy face" graphic character at that 
        position  is "high lighted".   Depress any "data" key (preferably 
        one you can remember for a few minutes,  like "A" or  "a").   The 
        character you depressed will appear in the list on the right side 
        of  the screen,  together with an equals symbol,  and the  "happy 
        face".   You've  just  "assigned" the "happy face" to  that  key.  
        Using  the numeric pad arrow keys,  move the cursor  around,  and 
        note how the graphic characters are high lighted showing which is 
        active  (you  have the cursor too,  just as a  double  visibility 
        aid).   You may "assign" up to 19 graphic characters.   You  need 
        more?   You'll never remember which is which...  but OK.  You may 
        "reassign" as you desire.   If you select the same data character 
        as you have selected previously, you'll see a "prompt" which says 
        "Reassign?".  An "N" will cancel the assignment, while a "Y" will 
        cause  the  prior assignment to be replaced by your  current  re-
        quest.  I'd suggest you only assign a few keys this time, and try 
        to  remember which is which.   When you've assigned all that  you 
        wish to, hit the "Esc" key and you're back to your edit screen.




        Basic Operation                 10





        Screen Design Aid - Version 3.0


             Two  points to remember.   If you use up the 19  slots,  you 
        "must" reassign, if you wish other graphics.  There is no "clear" 
        function for graphic assignments, other than bringing the utility 
        down and starting all over.   On the other hand,  the assignments 
        you've  made are "remembered" from screen to  screen,  throughout 
        the session.  Second, above all, remember the "Esc" to get out of 
        the assignment phase.   Nothing else will take you out,  short of 
        Ctrl-Break,  which takes you completely out of the utility,  with 
        the loss of what ever you were working on.  

             So  now  we've  assigned some keys.   I hope you  used  "a".  
        Let's enter that character a few times.   Gee,  it still displays 
        as "a".   Hit F1,  and enter some more "a's".   Now you're seeing 
        your  "happy face".   You also noted a change in the prompt  line 
        which now displays "Gr" for graphics mode.  Hit F1 again, and the 
        prompt  will disappear,  and your "a" key is now again  producing 
        "a's".  

             And that really is it.   You've covered all of the functions 
        of  the edit phase!   We're not done,  of course,  but you've got 
        enough  now to define a "pretty" screen.   I'd suggest  you  play 
        with  the  edit  phase for a little while,  and then  clear  your 
        screen  and try to define a screen that might have  applicability 
        to some application or another.  Leave room for some "fields" for 
        input and/or output.   Put on headings, etc., and if you want the 
        field  to  have an "initial display" fill in the  initial  value.  
        When you've completed that exercise, proceed to the next section.






























        Basic Operation                 11





        Screen Design Aid - Version 3.0


        ESAVING A SCREENF

             We'll assume you're still in "edit" phase,  and the  current 
        screen is displayed.  Depress the F10 key, and return to the main 
        menu.   Function  3  permits saving the screen you just  created.  
        Depressing  that key will reward you with a prompt screen  and  a 
        request for a file name.   

             I'll  assume  you're familiar with DOS file names,  and  DOS 
        file  name  conventions.    Your  response  to  the  prompt   may 
        (optional) include a drive specifier (ie:  B:),  and must include 
        the  "name"  portion of a file name.   It should NOT include  the 
        "type".   If it does, the type will be ignored.  Entering a name, 
        and depressing the "enter" key will result in some disk  activity 
        and then,  normally,  a return to the main menu.  If you happened 
        to  pick  a  name that already exists on the drive  you  selected 
        (default or specification), you'll get another prompt which warns 
        you that this case exists,  and asks permission to proceed.   You 
        can respond "Y",  in which case the old file is deleted,  or "N", 
        which  will  put back to the original prompt,  and  you  can  try 
        another  name.   "Esc" takes you totally out of the "save"  mode, 
        and back to the main menu.  

             Having made it back to the main menu,  try choice 8!  Yes, I 
        know that takes you out of SDA, but there's madness in my method, 
        or  some  such stuff.   Note that you'll get the usual  "Are  you 
        sure?"  prompt,  to keep from accidentally exiting and  losing  a 
        file you've worked awhile on.   This time, tell it "Y", and we'll 
        go back to DOS.  Enter the DOS command for the drive you've saved 
        to:

                  DIR [drive:] savename.*

        You  should see two files listed,  one with the type .IMG and the 
        other with the type .INC.   Note the size of the .IMG file.  This 
        is the amount of memory your screen will take when included in an 
        application.   If you didn't "fill" the screen with garbage,  I'm 
        sure  you'll  find the size is substantially less than  the  4000 
        bytes  required to store a screen image.   This file is a  binary 
        file,  and is not directly "viewable".   It is, incidentally, the 
        file the SDA will work with if we do any additional work on  this 
        screen.  

             The  .INC  file,  on  the other hand,  may be  displayed  by 
        entering the TYPE command:

                  TYPE  [drive:]savename.INC

        What  you're seeing going whipping by is a set of data  constants 
        in a source format acceptable to the Assembler.   We'll talk more 
        about  this form in the section discussing interface to  applica-
        tions.   Another  section discusses the content of these files in 
        some detail, but we'll wait for that section.




        Saving a Screen                 12





        Screen Design Aid - Version 3.0


             This exercise was simply to demonstrate that when you "save" 
        a screen,  you're creating two files, both of which have use, and 
        to demonstrate that a significant compression occurs.   One point 
        to  remember.   With the .IMG file,  we can always re-create  the 
        ???.INC file,  but the reverse is NOT true.  The .IMG file is the 
        one SDA works with, while the .INC file is a "spin off" for other 
        purposes.  

             Now,  fire  up SDA again,  and we'll continue with the  next 
        section.















































        Saving a Screen                 13





        Screen Design Aid - Version 3.0


        ELOADING AN EXISTING SCREENF

             Assuming we're at the main menu,  glance at option 2.   That 
        seems to be the one we're ready for,  so enter a 2.  Up comes the 
        usual  prompt  menu,  this time asking for the name of  the  file 
        containing  the  screen to edit.   Enter the name you saved  your 
        screen under.   Just as in saving the screen, the drive specifier 
        is optional,  and the type is ignored.   The utility will load  a 
        file  of the name you provided,  with a type of  .IMG.   Assuming 
        nothing "glitched",  there will be some brief disk activity,  and 
        then  you'll flash back to the main menu.   In the event you made 
        an  error on the name,  a "not found" prompt will appear and  you 
        can try again.   As in save,  the "Esc" will take you back to the 
        main menu without executing the load function.  

             Now,  enter a "1",  and confirm that your screen is back  on 
        display.   You  could  make "corrections" or extensions  at  this 
        point,  if  needed,  and then save the screen again.   This time, 
        we're just demonstrating that what you had,  you still have.  Hit 
        F10,  and we'll go back to the main menu.   We're about ready for 
        option "4" -- field definition or maintenance,  so let's  proceed 
        to the next section.



































        Loading An Existing Screen      14 





        Screen Design Aid - Version 3.0


        EFIELD DEFINITION/MAINTENANCEF

             From the main menu, enter "4", and you'll be rewarded by yet 
        another screen.  This one has a blank column on the left and some 
        text  on  the right.   The text will be repeated and expanded  in 
        this section,  so you don't have to read it now.  Note that there 
        are  a  "list" of active function keys shown in the body  of  the 
        text.

             Before getting into the "mechanics" of definition of fields, 
        let's talk first about what is a field, and what use are they?

             First,  a  field  is  any  contiguous  string  of  character 
        positions,  all  of which must be within the same  display  line.  
        The content of the positions does not effect this definition.

             Second,  under  SDA,  a field may have its own "attributes", 
        which may differ from that assigned in the original definition of 
        the screen itself.   For example, lets assume that row 2, columns 
        10  to  20  on the screen contain the first  20  letters  of  the 
        alphabet,  normal attribute.   We could define a field containing 
        any  or  all  of  those  characters,   or  extending  beyond  the 
        characters,  and  the  field could be given the "high  intensity" 
        attribute.  Gee isn't that nice... so what?        

             Well,  when the screen is displayed the 20 letters would  be 
        displayed  at normal intensity,  however the first I/O  operation 
        against  that  field  would cause the result of that  I/O  to  be 
        displayed  at high intensity!   Works nice when you want to  high 
        light a user's response against the "static" screen body.  

             This  is  probably  a great place to talk about  this  vague 
        thing called I/O.   As you read in the introduction,  we  provide 
        support for:  output to a field,  input from a field,  a combined 
        output followed by input,  the clear of a field,  and the ability 
        to  position  the cursor to a field.   Let's take them one  at  a 
        time,  and in a bit more detail.  Don't worry about how we invoke 
        the function,  yet.   This is what the function does, when you do 
        invoke it.  

        EOutput to a fieldF -

             This  function permits output of a character string  to  the 
        specified field.  The attributes of the displayed literal will be 
        the attbributes of the field.   The string may be terminated by a 
        null.  Output of the string will continue until one of two condi-
        tions  is met.   Either the "end of string" (nul) is  encountered 
        before  the  end  of field,  or the end of field  is  encountered 
        first.   In the former case, the balance of the field will be set 
        to blank,  with the attributes of the field.   In either case the 
        cursor  will be positioned to the "end of  field"  position,  and 
        remains there on return to the caller.





        Field Definition/Maintenance    15





        Screen Design Aid - Version 3.0


        EInput from a fieldF -

             Similar to output,  this service will position the cursor to 
        the  start of a defined field,  and wait for input.   As input is 
        keyed  to the field,  it will be displayed,  with  the  attribute 
        assigned  to  the field.   Since this function returns the  input 
        string to a user defined  buffer, it is the user's responsibility 
        to  assure  that the buffer is at least as long  as  the  defined 
        field.   The  input operation is terminated by any of the follow-
        ing:  "enter" key, "Esc" key, "Tab right", "Tab left".  Feed back 
        information is provided in the return to indicate which  termina-
        tor occured,  and to provide the length of the valid string (zero 
        is valid).  The input operation will NOT be terminated by exceed-
        ing  the field length.   Rather if such an attempt is  made,  the 
        "beep"  signal from the console will be invoked,  and the current 
        data character not accepted.  Only a terminator or a backspace is 
        acceptable at end of field.  The backspace may be used to correct 
        keying errors.

             This  function includes one additional  option.   The  input 
        operation   may  be  "destructive"  or   "non-destructive".    In 
        "destruct" mode, initiation of the input operation will clear the 
        defined  field  to blanks with the  appropriate  attribute.   The 
        "non" mode leaves the existing display unchanged, except for data 
        keyed  in  by the user.   This permits display of  the  "default" 
        value for a field.   Note that this "default" must be established 
        by  software,  since  if the user makes an  immediate  terminator 
        response (no data entry),  the feed back will provide a length of 
        zero, and an indication of the terminator used.  

        EOut/In functionF -

             This  is  simply  a  single  call  combining  the  functions 
        described in the previous paragraphs.  It is useful when you wish 
        to  display  "existing"  data and  allow  overwrite.   The  Input 
        portion  of  this  operation is always in  the  "non-destructive" 
        mode.

        EField clearF -

             Clears  the  defined  field to  blanks  with  the  attribute 
        defined for the field.  Cursor is left at START of field.

        EPosition CursorF - 

             Positions  cursor  to  START of a  defined  field.   Current 
        display is not changed, nor is field content.  

        Having learned what you can do with fields, now we're in a better 
        position  to define some.   Refer back to the screen.   The  keys 
        displayed  as  "active"  are  also covered on  a  "help"  screen.  
        Depressing F9 will display that screen,  and as before, returning 
        to the field maintenance screen from "help" is simply the  matter 
        of depressing any key.



        Field Definition/Maintenance    16





        Screen Design Aid - Version 3.0


             Key  assignments  are  as  consistent  as  possible  between 
        functions.  You'll note that F9 is still "help", F8 is clear (the 
        field table ONLY, this time), and F10 returns to the main menu.
        Keys F5 through F7 are not used at this point in this phase.   To 
        better  demonstrate the remaining keys,  press F3 (Add to end  of 
        field list) and watch your current screen appear.

             This  is  not the "edit" screen,  although it has  the  same 
        appearance.   We'll come back to the various options available on 
        this  screen,  but for right now,  simply move the cursor to  the 
        start of a likely field and depress F1.  Note that an "*" appears 
        on  the prompt line.   This is a flag to indicate you're half way 
        through the process of defining a field.   Now move the cursor to 
        the other end of the field, and again depress F1. 

             Flash!  Back to the original field maintenance  screen,  but 
        now  you'll  see one entry in the previously blank column on  the 
        left.   As the column headings indicate, the data displayed (from 
        left to right), is the field number, row (0-24), column (0-screen 
        width), length, and attributes of the field.  

             To  give  us something to work with,  press  F3  and  define 
        another field, repeating the above process.  Do this two or three 
        times,  until you have defined three or four fields,  ending with 
        the  field table display.   As you go through this process you'll 
        note  that  the list of fields continues to  extend  towards  the 
        bottom  of the display.   You'll also note that the last entry in 
        the  list is high lighted.   You've also noticed some changes  on 
        the field definition screen,  but we'll delay discussion of those 
        for a few moments.  

             Two of the numeric keypad arrow keys are active.  The up and 
        down  arrows  (only).   Try pressing the "up"  arrow.   The  high 
        lighted entry moved "up" the list.  The down arrow moves the high 
        lighted  entry  down,  of course.   The indicated  entry  is  the 
        currently "active" entry.  Note the content of the list, position 
        the  active  entry somewhere in the list (not at  the  end),  and 
        depress  F1 (insert field before active entry).   You'll get back 
        to  the definition screen,  so use F1 twice (this time to  define 
        another  field),  and  when you return to the active  field  list 
        you'll find that the field you just defined has been inserted  in 
        the list immediately before the field you selected.

             Depressing F2 will delete the currently active field,  while 
        F4  allows you to redefine it.   As we mentioned  previously,  F8 
        will  clear  the  entire field table (complete with an  "are  you 
        sure" prompt), while F10 will return you to the main menu, and is 
        used  after you have completed field  definition.   Incidentally, 
        you may enter field definition,  define a few fields,  return  to 
        the  edit  phase,  modify the screen,  and then return  to  field 
        defintion  to  find your original definitions as you  left  them.  
        Note  that  if the change in the edited screen throws your fields 
        out of alinement,  its your problem to fix them.   There's no tie 
        back   between  the  edit  screen  phase  and  the  field   table 
        maintenance phase.  


        Field Definition/Maintenance    17





        Screen Design Aid - Version 3.0



             Two points,  before we discuss the field definition  screen.  
        The  number of fields that may be defined for a screen may be any 
        number between zero (valid),  and 100.   As you exceed the number 
        of fields that can be displayed (20),  the list simply grows  off 
        the  top or bottom of the screen.   If you're positioned at field 
        30  and  want to see field 3,  simply move the  currently  active 
        field to the top of the displayed list (using the up arrow),  and 
        continue  to depress the up arrow.   You'll see the  list  scroll 
        down until field 1 is displayed.  Similarily, if the field is off 
        the display "at the bottom", use the down arrow until you see the 
        field you've selected.  

             Now on to the field definition screen.   Again, there's a F9 
        "help"  screen.   If you use one of the field definition keys (F1 
        F3 or F4) to get back to the definition screen,  you can bring up 
        the "help" screen, and follow it through this brief discussion.  

             At first glance, this "help" menu appears almost the same as 
        the  edit  "help" screen,  but closer examination  will  indicate 
        differences.   F1  is  now the "define field"  key  (rather  than 
        toggle  graphics mode,  which isn't applicable now).   F2 is  not 
        active.   F3  through F7 have the same functions as they did  for 
        edit,  but F8 is not active.   F9 is still the "help" key,  while 
        F10   simply  returns  you  to  the  maintenance  screen  without 
        definition of a field.   "Home" is not active,  nor are "Del"  or 
        "Ins".   "PgUp" and "PgDn" are,  and allow shifting the screen as 
        in  edit,  when you wish to define a field on the bottom line  of 
        the  screen.   The cursor positioning keys work the same as edit, 
        of course.   Not much "new" here,  so hit any key to get back  to 
        the definition screen.

             Since you've defined several fields, you'll notice the "half 
        tone"  areas demarking the location of the fields.   These  areas 
        have  "clobbered" any data you might have included in the  screen 
        at that point.   Not to worry...  the data is still there, but we 
        need to show two things in the same space and the display devices 
        won't  cooperate  to that extent.   A "standard" practice  is  to 
        enter the "default" value on the original screen, and then define 
        a field over the top of it.   By using the input function in non-
        destructive  mode,  you can display the default,  but permit  the 
        user to key over the top when he wants to change the default.  

             As  we've said several times,  the field has an attribute of 
        its  own.   You'll see it show up in the field table,  and  there 
        will  be  some  change in the "half tone" display  when  you  use 
        different attributes.  Try defining a field with "high intensity" 
        for an example.  

             That's   all  for  field  definition.    I've   deliberately 
        "skipped" any discussion of F7 in field definition  phase,  since 
        that's  only  used  under  "Color" mode and  is  discussed  in  a 
        separate section.   When you've experimented as much as you like, 
        return to the main menu (F10).



        Field Definition/Maintenance    18





        Screen Design Aid - Version 3.0


        EPRINTING SCREENSF

             This  time,  don't  start poking keys till you've read  this 
        paragraph.   If  you  do not have the EPSON MX80  4with  GRAFTRAX 
        plus5,  or a "bit level" equivalent device,  the only reason  for 
        reading  this  section  is to learn what  you're  missing!   This 
        function will only work using such a device.   You're welcome  to 
        try  it on your printer,  but I'll tell you now that the  results 
        will not be usable.

             For  those  with the "goodies" options,  this  section  will 
        continue.   Assuming  you've left the screen you created  in  the 
        utility (if not,  you can reload it using the 2 option),  depress 
        the  5  key and hit "enter".   You'll be rewarded by yet  another 
        menu,  which asks for a "caption".   Key in any string (up to  40 
        characters)  you  might like to use as a caption for the  screen.  
        If  you  don't want a caption,  try keying one  blank,  and  then 
        "enter".   No data at all will behave similar to the "Esc", which 
        will "take you out" with out printing the screen.

             So  the  printer  "fires  up" and  you  start  printing  the 
        screen...  very  slowly!   If you become fascinated with  printer 
        head  motion,  and watch it,  you'll notice that it behaves in  a 
        very  unusual manner.   Sweeps part  way,  hesitates,  backs  up, 
        resweeps,  etc.,  etc.  Don't worry about it, since that's normal 
        behavior  when printing a mix of "dot graphics" and  text.   This 
        whole behavior pattern (together with the low speed) is caused by 
        the  requirement  to  print characters the printer  doesn't  have 
        "built in".   Under this utility,  however,  the printer can  and 
        will  print any character you've included on your display  screen 
        (or at least a reasonable facsimile, thereof).      

             When  the  screen finally completes,  your caption  will  be 
        added,  centered  in  the  second line below  the  screen.   That 
        completes  the  "functioning" of this  option,  however  for  the 
        "mechanics" of this operation, we'll include a few other words.

             Paper  alignment  (prior to starting the utility) should  be 
        with  the  perfs positioned at the top of  the  bail.   Sorry  if 
        you've  adopted a different "standard" position.   Seems to be at 
        least  two  used in practice.   Printing is  done  in  compressed 
        print,  eight lines/inch.  This gives something that approximates 
        screen  representation.   Don't worry about your printer  control 
        load, however.  The utility restores the printer to normal print, 
        six lines/inch when it ends.  Similarily, it keeps track of forms 
        position,  and will restore to top of form when the utility ends, 
        so DON'T REPOSITION THE PAPER after printing a screen.  

             The  format  is such that two screens will be printed  on  a 
        single  11"  sheet,  or if you use the next option  (print  field 
        table), a screen and its field table will usually be printed on a 
        single sheet (if you have less than 75 fields, that is).  





        Printing Screns                 19





        Screen Design Aid - Version 3.0


        EPRINT FIELD TABLEF

             Option  6  permits  printing the field  table.   This  one's 
        requirements are not as stringent,  and will work on any  printer 
        capable  of handling 132 column print.   Again,  its designed for 
        the EPSON,  and you could find some "funny" characters showing up 
        at the start of print on other printers.   Again, the first thing 
        you  see is a menu requesting a "caption".   "Esc" will take  you 
        out without printing,  while a "caption" of any string (at  least 
        one character, which may be blank) of up to 40 characters will be 
        accepted.  

             A print out of the current field table results.   The format 
        is a three column layout, with headers.  The only thing "cryptic" 
        is  the last columns of the attributes,  which contain "F:xxxxxx" 
        and "B:xxxxxx".   These are "colors" and become meaningful in the 
        section  discussing  "Color".   When print  is  complete,  you're 
        returned to the main menu.   If you're using this option but  not 
        the screen print, better read the screen print option for details 
        of paper handling, alignment, etc.  





































        Print Field Table               20





        Screen Design Aid - Version 3.0


        ECHANGING DISPLAY DEVICEF

             Two groups of users will be interested in this section.  For 
        those afluent types that have both the Monochrome Display and the 
        Color/Graphics  board,   read  on.    For  those  with  only  the 
        color/graphics board, and a monitor that will operate effectively 
        in either 80 or 40 character line width,  read on.   For the user 
        who  has  only  the Monochrome display,  or who does not  have  a 
        monitor  that will work in 80 character mode,  you might as  well 
        skip  this section.   But since you won't,  you can read and  see 
        what you're missing.  

             WARNING:   ANY "CURRENT" SCREEN AND FIELD TABLE WILL BE LOST 
        WHEN THIS FUNCTION IS INVOKED.   IF YOU HAVE A SCREEN AND WANT TO 
        KEEP IT, DO A "SAVE" BEFORE USING THIS FACILITY.

             Before poking keys,  be sure your hardware configuration  is 
        "ready".   For example,  if you're running on the monochrome, but 
        have the color graphics adapter and a monitor driven by it,  turn 
        the  monitor on.   Now,  enter "7",  and on your current  display 
        device  you'll see yet another menu.   This one says what  device 
        you're  currently on (Monochrome or Color/graphics),  and asks if 
        you want to switch.   A "y" response is called for,  so enter it, 
        and  then  look at the next response.   This one says  what  your 
        current  line  width is,  and asks if you want to change  to  the 
        other supported length (80-40).   Make the appropriate  response, 
        and  the  display  will be refreshed with the  configuration  you 
        requested, but you'll still be asked to confirm by responding "Y" 
        to the last prompt.   When you give this last "Y", you'll see the 
        display  switch to the other display monitor (if you  have  two), 
        and/or the line width change to the requested width.   And you'll 
        be back to the main menu.

             I won't include it here, but you'll be interested in reading 
        the  section on "40 Character screens on 80  character  terminals 
        and Visa Versa" included later in this document.





















        Changing Display Device         21





        Screen Design Aid - Version 3.0


        ECOLORF

             If  you have the Color/graphics display board,  and a  color 
        display,  this section will interest you.   Before getting in  to 
        the  discussion,  a couple of "disclaimers".   First,  the  color 
        names used are those in the "book".   I've already found that the 
        actual  color  displayed varies widely with the type  of  display 
        device.  The only "solution" is "try it and see", and then do the 
        mental  conversion  necessary to match the color names  with  the 
        color shown on the display.   Second,  unless you have a true RGB 
        monitor,  using 80 character line width is likely to be a joke -- 
        but  not too funny.   Readability is likely to be totally lost on 
        most composite monitors.  

             Its probably a good place to mention that assigning  "color" 
        to  the  attribute  typically has "no effect" on  the  Monochrome 
        display.   The  one  exception is  that  requesting  "underscore" 
        attribute or the color "blue" has the same effect.  

             With that introduction, get to the "edit" screen (option "1" 
        on  the main menu),  and depress F7.   This will produce  another 
        menu which simply asks for the "foreground" color you wish to use 
        at this point in time.   Entering the initial letter of the color 
        (X  for  black)  and depressing the "enter" key  will  cause  the 
        display  to change to a request for the "background"  color.   In 
        either  case,  an  "enter" without data simply leaves  the  color 
        currently assigned,  still in effect.  After your response to the 
        "background" prompt, you'll be returned to the "edit" screen.  

             Assuming you're on a color display, you can play around with 
        various  combinations.   The color can be changed for  each  data 
        character  entry,  if  you like rainbows,  or it can be  left  in 
        effect  for  the entire screen.   The attribute  assignment  keys 
        still  work as they did,  with two exceptions.   Underscore  will 
        force  a  foreground  color of "Blue",  and will not  produce  an 
        underscore.  Normal/Reverse Video now has the effect of "swaping" 
        the foreground and background colors.  

             This  key  has  a similar use  in  field  definition  phase, 
        permiting  assignment  of "color" to field attributes  associated 
        with  the  defined  fields of the display.   Its  use  should  be 
        obvious, so we'll wave at a detailed review of the screen.  















        Color                           22 





        Screen Design Aid - Version 3.0


        E40 CHARACTER SCREENS TO 80 CHARACTER DISPLAYS
        E(AND VISA VERSA)F

             This topic gets a bit complicated.   If you normally operate 
        using a single display width, you can safely ignore this section.  
        On the other hand,  if you want your application to be capable of 
        running on most configurations, you'll probably need this data.

             First, screens are "saved" in either 40 or 80 character line 
        width.   The mode of the "save" is determined totally by the mode 
        you're running in at the time of the "save".  If you're operating 
        on  an 80 character display,  you can't save in 40 width and visa 
        versa.   So  to  control the width of "saved"  screen,  you  must 
        control the width of the mode you're operating under.  

             Second, the display generation code (used in the utility and 
        included for your use with applications) will attempt to  display 
        a  screen  irregardless of the mode of the display its  outputing 
        to.   It  does this by either expanding or truncating the  screen 
        when  the  screen  mode doesn't  match  the  display  mode.   For 
        example,  if you're trying to display a 40 character screen on an 
        80 character terminal,  it simply "centers" the image,  providing 
        20 blanks of padding on either side of the image.  

             Displaying  an 80 character screen on a 40 character display 
        is  not  as satisfactory.   The only thing the display  code  can 
        rationally do is to truncate the image,  and that's what it does.  
        It  displays  the first 40 columns of  each  line,  dropping  the 
        remainder.

             What's the effect of all this?  Assuming you wish to use the 
        screens  on any device,  your preferred mode of operation will be 
        in 40 character line mode.   Do the edit, field assignment, etc., 
        and  then  "save".   The resultant screen can be used  on  either 
        Monochrome  or  color/graphics adapters,  and will be  usable  in 
        either  40  or  80  character  line  mode.    It  also,   not too 
        incidentally,  will make a smaller compressed image,  so it saves 
        both disk and memory space.

             If you have to work on an 80 character device,  then its all 
        up to you.   If you build your screen in the first 40 columns  of 
        the  edit  screen (and stay totally within those  columns),  then 
        when  that screen is saved,  it can be displayed on a  40  column 
        device, since the 40 unused columns will simply be discarded.  It 
        includes the penalty of a slightly larger "compressed" image than 
        that described for the same screen in 40 column mode.

             This  utility is a good example of the 40 column mode.   All 
        of the screens used were formed under that option,  and therefore 
        may  be displayed on either 40 or 80 column  devices,  in  either 
        color  or black and white.   I won't claim the "art work" is good 
        nor will I boast about the choice of colors...  I'm a hacker, not 
        a painter... but it does demonstrate the flexibility of SDA. 




        Line Lengths                    23





        Screen Design Aid - Version 3.0


        EAPPLICATION INTERFACEF  

             Use  of  screens  produced by SDA may be  made  by  Assembly 
        Language  programs.   The  next section discusses "bridges"  that 
        permit  use  of the screens by "high  level"  languages.   It  is 
        suggested  that even if your interest is "high level",  that  you 
        read this section.   It contains information you will need if you 
        attempt to "bridge" to a language other than BASIC.

             Assembly  usage is very easy.   Just use the macros provided 
        in the file $FIELD.MAC.  The macros are well commented, but we'll 
        cover  them,  and  the  code  sequences  generated  here,  as  an 
        introduction to the "bridges" of the next section.

             In all cases,  a "command code" which indicates the function 
        desired,  is provided in the AH register.   In all cases but one, 
        the  field number is given in the AL  register.   Other  register 
        usage is specified where appropriate.   In all cases the register 
        status,  with the exception of the AX register,  is preserved and 
        restored  before  return to the calling program.   In the  single 
        case that "feed back" is provided,  that data is contained in the 
        AX register.

             To display a screen:

                  $FDISP          screen-image        

                    or

                  XOR       AH,AH
                  MOV       DX,OFFSET screen-image
                  CALL      $SDA

             To output to a field:

                  $FDOUT    field-number,character string
                  
                    or

                  MOV       AH,1
                  MOV       AL,field-number
                  MOV       DX,OFFSET character-string
                  CALL      $SDA

        where  character-string  is any string terminated by a zero  byte 
        (nul).   Output  will  cause the string to be  displayed  in  the 
        output field, and the cursor left at end of field.  If the string 
        is  shorter  than  the field,  the balance of the field  will  be 
        cleared to blank.   If the string is longer than the  field,  the 
        string  will  be  truncated  to  field  length.   Note  that  the 
        attribute of the displayed data is that defined for the field.  






        Application Interface           24





        Screen Design Aid - Version 3.0


             To input from a field:

                  $FDINP    field number,buffer,[flag]

                     or

                  MOV       AH,2
                  MOV       AL,field number  or  field number+80H
                  MOV       SI,OFFSET buffer
                  CALL      $SDA

        where "buffer" is any work buffer for return of the input string.  
        It  is YOUR responsibility that the buffer is at least as long as 
        the  defined  field.   The "flag" in the macro is  any  non-blank 
        string,  which will cause the expansion to "add 80H" to the value 
        in  AL.   This  "+80H" indicates that a  "non-destructive"  input 
        operation is desired.  Input may be either "destructive" or "non-
        destructive".  Destructive clears the field to be blanks with the 
        field's attributes,  while "non-destructive" simply positions the 
        cursor to the start of the field.   In either case,  input  waits 
        for  keyed  data.   If  data is entered and  the  last  character 
        position  of the field is filled,  a "beep" signal is given  when 
        any  additional character entry is attempted.   A terminator or a 
        "backspace" are the only acceptable characters when positioned at 
        end of field.  When "entry termination" is sensed, return is made 
        to the caller, with the following "feed back" information.

             The  input  string will be in the  "buffer"  provided.   The 
        length of the returned data will be contained in the AL  register 
        (zero length is valid), while the AH will contain data indicating 
        the type of termination that occured.  The AH contents may be:

                  AH = 0    Normal return ("enter" key)
                  AH = 1    Right tab
                  AH = 2    Left tab
                  AH = 4    "Esc" key
                  AH = 8    Scan code terminator

        In  all but the first case above,  the carry flag will be set  on 
        return.   The  scan  code  terminator is  a  special  case.   The 
        hardware  produces  two characters for special  keys.   First,  a 
        "nul"  character,  and then typically the scan code of  the  key.  
        When  this condition is sensed,  the "nul" is discarded,  and the 
        second  character  is moved to the buffer,  and the  80H  bit  is 
        turned  on in that character.   Finally the carry and the AH code 
        are set, and return is made.  

             You'll note that this is set up for rapid "field advance" by 
        using, and sensing, the use of the tab keys.








        Application Interface           25





        Screen Design Aid - Version 3.0


             To perform output followed by input in a single call, use:

                  $FDOIN    field-number,output-string,buffer

                    or

                  MOV       AH,3
                  MOV       AL,field-number+80H
                  MOV       DX,OFFSET output-string
                  MOV       SI,OFFSET buffer
                  CALL      $SDA

        which  is  simply  a  combination  of  the  previously  discussed 
        functions.   Feed  back  is  the same as  that  in  the  previous 
        function.   Note that "non-destructive" mode is automatic in this 
        option, when using the macro.

             To  clear a field,  or to position the cursor to a field are 
        almost identical:

                  $FDCLR    field-number  or  $FDPOS   field-number

                    or

                  MOV       AH,4 (clear)  or  MOV    AH,5  (position)
                  MOV       AL,field-number
                  CALL      $SDA

        These simple primitives are all that have been defined,  current-
        ly,  for  use of the screens.   They seem to be all that are  re-
        quired,  and provide the basic building blocks for management  of 
        complex screens.

























        Application Interface           26





        Screen Design Aid - Version 3.0


        EHIGH LEVEL LANGUAGEF          

             Since essentially all high level languages support some form 
        of a "call" interface,  building a "bridge" to permit utilization 
        of  screens from high level code appears straight  forward.   The 
        program BASSCR is included with this distribution,  and is such a 
        bridge for compiled BASIC.  It performs correctly with either the 
        "run time execution library" or the "stand alone" products of the 
        compiler.   A listing of the source form of this program would be 
        helpful in following the discussion given.

             Interface and parameter passing is usually performed through 
        the "stack".   BASIC,  at least,  only insists that the SS and SP 
        registers  be reset to the entry value,  before returning to  the 
        calling BASIC modules.  Those two registers are saved immediately 
        on  entry.   Note  that the MOV instruction uses the  CS  segment 
        register,  rather  than the normal DS.   Both DS and ES registers 
        point to the BASIC data area on entry.   The BP register is  then 
        set to the value of the entry SP, and used to access the stack.  

             The  "call" interface defined for this bridge expects  three 
        parameters: the first two are integers while the last is a string 
        variable.   The  convention  is  that the first  integer  is  the 
        command  type,  while  the  second  is the  field  number  (where 
        applicable).   The arguments are passed as pointers to  arguments 
        in the stack,  with the first argument at the "top".  You'll note 
        that  the  stack  offset for the first argument is 8  (number  of 
        arguments  plus 1 times 2).   Getting this pointer into an  index 
        register  and then using the index to get the integer  is  direct 
        code.  Since  we  are  only  interested in the low  byte  of  the 
        integers,  the  required byte is saved temporarily,  and the  2nd 
        argument  loaded using the same technique (offset  6).   The  two 
        arguments are then returned to the AH and AL register, since they 
        are the command type and field number, respectively.

             The  third argument is an optional string pointer,  so after 
        establishing the address to the pointer,  that address is  simply 
        "saved" (SAVSI).  Unfortunately, establishing the requirement for 
        the string pointer requires "decode" of the command type, so that 
        function  is next performed.   As an aside,  note that the use of 
        the segment registers is such that the BASIC data segment is used 
        for  access to the pointers,  while the segment register set  for 
        this code is used for "saves".  

             Decode  of  the type then permits  establishing  the  proper 
        string relationships for the various call types.   The "combined" 
        output/input operation is not supported in this code, although it 
        could readily be supported by a single simple change.  Because of 
        the  segment  addressability  problem,  and the need to  place  a 
        terminating  "nul" on output strings,  all string operations  are 
        mapped through an internal buffer in this code.   The code  which 
        handles  this mapping and segment register manipulation is direct 
        and straight forward, so no further explanation is given here.




        High Level Language             27





        Screen Design Aid - Version 3.0


             One point is important.  BASIC provides a very limited stack 
        when calling a user application.  This stack must handle not only 
        the  bridge code,  but must also handle $SDA.   $SDA is a  "stack 
        hog", and requires at least 106 bytes of stack area.  This forces 
        reassignment of the SS and SP registers before calling $SDA,  and 
        the inclusion of a stack area in the bridge.  

             You'll  note that even though considerable  manipulation  of 
        registers  has  been made,  the only requirement for  "clean  up" 
        before  return is the restoration of the SS and SP registers.   A 
        FAR return is required with an argument of 2 times the number  of 
        passed parameters.  

             For  the "sharp eyed",  yes there is a call to BIOS  turning 
        "on"  the  cursor.    In  writing  this  bridge,   I  found  some 
        interesting behavior patterns coming out of BASIC.  It apparently 
        does  not  follow the DOS/BIOS interfaces for screen  management.  
        Not  only did I "lose" the cursor on return from this  code,  but 
        BASIC ignored the cursor position established by SDA,  when doing 
        I/O on its own.  Originally, I had hoped that simply using SDA to 
        display  the screen,  and to position the cursor,  would be  ade-
        quate.  This would eliminate the cumbersome LOCATE code sequences 
        of  BASIC,  but would permit use of the I/O statements  directly.  
        Unfortunately,  that won't work!!   So, use the I/O facilities of 
        SDA when working with screens.  

             How do you put the whole mess together?   Well,  first embed 
        the  .INC  file  into  an  assembler  program  that  should  look 
        something like this:

             CODE     SEGMENT PARA PUBLIC 'CODE'
                      ASSUME    CS:CODE,DS:CODE
             ;
                      PUBLIC    BASMEN
             ;
             BASMEN   EQU       $
                  (Include the .INC file here)
             ;
             CODE     ENDS
             ;
                      END

        Now assemble this thing.  You have on the distribution diskette a 
        module  named BASSCR.OBJ.   Write your BASIC program (or look  at 
        the  program named DEMO on the distribution diskette),  and  then 
        run Link.   When Link requests "object" module names, give it the 
        string:  your-module+BASSCR+BASMEN+$SDA.  Obviously, these object 
        modules  must all be on the "signed on" drive,  and the remainder 
        of  the link parameters are standard responses as for  any  other 
        BASIC  compilation.   The  result is a program that will use  SDA 
        generated screens.  

             I'm  sure this is enough information to guide you in writing 
        your own "bridges" what ever language you prefer.   I started  to 
        build  primitive  bridges  for  additional  languages,   but  its 


        High Level Language             28





        Screen Design Aid - Version 3.0


        difficult  to anticipate the potential use,  and that use  should 
        effect the form of the "call" interface.   Frankly,  I also  felt 
        that  I  really  didn't want to have to dig through  all  of  the 
        "nits"  in other languages...   I'm an Assembler bigot,  so happy 
        bridge building...




















































        High Level Language             29





        Screen Design Aid - Version 3.0


        ETECHNICAL REFERENCEF

             For  those  of you who have a burning desire  for  a  deeper 
        understanding  of  this  whole mess,  I've  included  this  brief 
        section  on  the compressed screen and include files produced  by 
        this process.   You really don't need this information for use of 
        the  utility,  so  if your curiosity bump is not  itching  badly, 
        don't bother reading this section.

             First,   the   .IMG   and  .INC  files   contain   identical 
        information, in an obviously different format.  All the .INC file 
        is,  is  an "external" representation of the  binary  information 
        contained in the .IMG file.   Its converted to "external" so that 
        it  can  be handed to the assembler,  who then converts  it  back 
        again into its binary form,  but now it has the nice attribute of 
        being an .OBJ file which can be linked with your code.

             So  what does the .IMG file contain?   It divides  into  two 
        sections:   The field table, and the compressed image.  Beginning 
        with the first word, its content is:

             First  word  contains a count of the defined fields in  this 
        screen.   Immediately  following  the first word is a  series  of 
        repeating entries, each four bytes in length, one for each field.  
        An  entry contains in the first byte the row of the start of  the 
        field,  in the second byte, the column of the start of the field.  
        The third byte contains the length of the field, while the fourth 
        contains  the  attribute  of  the  field  (as  defined  in  IBM's 
        technical reference manual).  

             Immediately  following  the field table  is  the  compressed 
        image.   The  first word of the image is a "length" of the image, 
        including  the  length word.   Following this length  word  is  a 
        string  of  slightly  more complex  structure.   This  string  is 
        composed  of  three  types  of  "sub-strings".   Sub-strings  are 
        identified by their first byte.   If the byte is 0FFH,  then this 
        is  an attribute sub-string,  and the next byte is the  attribute 
        that  is  to  be used until next encountering an  attribute  sub-
        string.  Screens typically start with an attribute sub-string.

             If the byte is 00H,  then this is a repeating character sub-
        string.  The next byte is the number of times the character is to 
        be repeated (max of 255), and the following byte is the character 
        to be repeated.  

             Any other byte configuration (other than FFH or 00H),  is  a 
        data sub-string which is a single byte.   Its simply data that is 
        to be placed on the screen.  

             I'm sure with this,  the basic loop is  apparent.   Starting 
        with  the upper left corner of the screen,  and the start of  the 
        string,  simply  decode  the sub-strings and store the  resultant 
        data  characters and the current attribute.   When the string  is 
        exhausted,  you're  at the end of the regen buffer,  since  every 
        byte  in the original screen is represented.   One  minor  point.  


        Technical Reference             30





        Screen Design Aid - Version 3.0


        Since  a  "compressed"  string requires  three  bytes,  repeating 
        characters  must  repeat more than three times  before  they  are 
        "compressed"  into  a repeating character  substring.   Three  or 
        less, they simply are placed in the string without compression.

             I  won't  dwell  on making 40 character screens work  on  80 
        character displays,  (and visa versa) but that is simply a matter 
        of  "reformatting"  the regen buffers  after  expansion.   You've 
        probably noticed an almost subliminal flash of a poorly displayed 
        screen prior to seeing the "steady" image.  This is caused by the 
        "reformatting"  required.   If the "flash"  bothers  you,  simply 
        avoid  using 40 character screens on 80 character  displays.   It 
        won't occur if you match the screen to the display.












































        Technical Reference             31





        Screen Design Aid - Version 3.0


        EERROR MESSAGESF

             The  only "true" error messages issued by this utility  come 
        from diskette I/O error conditions.  All are identified as to the 
        cause  of error and the file involved.   They appear  at  various 
        locations  on the screens,  so I won't attempt to delineate  each 
        message.   If  you  encounter  a "read" error,  I hope  you  were 
        "backed up".   A write error will invariably be because of a lack 
        of space,  either directory or data,  so try again with a "clean" 
        diskette.   You  may "swap" diskettes at any time the utility  is 
        not actually engaged in reading or writing disk, so if you have a 
        problem  writing  one  diskette,  wait till  you  get  the  error 
        message, and then swap diskettes, and try the command again.  

             Because  of the difficulty in testing "error code",  this is 
        probably the "softest" area in the utility.   I've tried to force 
        all error conditions,  but I'm sure I missed a  few.   Typically, 
        these  conditions  will only occur when something is "not  right" 
        with the hardware, so try again after correcting your problem.






































        Error Messages                  32






         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

                  Disks in the library are updated monthly.
         For a copy of the latest monthly software library newsletter
          and a list of the 800+ disks in the library, call or write

                        The Public (Software) Library
                               P.O.Box 35705 K
                           Houston, TX 77235-5705
                               (713) 721-6104

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.