CTask

                           A Multitasking Kernel for C



                          Version 2.2  Released 90-10-12




                        Public Domain Software written by

                                  Thomas Wagner

                             Ferrari electronic GmbH




                                     Contents


        About this Manual                                               1

        Introduction                                                    2
          An Example                                                    2
            Switching the Context                                       2
            You have Mail                                               3
            Reentrancy and Resources                                    3
            DOS Access                                                  4
            Handling the Keyboard                                       4
            Serial I/O and Timeouts                                     5
            Priorities                                                  5
          Change to your liking                                         5

        General Notes                                                   7
          What can CTask NOT be used for?                               7
          What is required to use CTask?                                7
          Do I have to pay for using CTask?                             8
          What support can I expect?                                    9
          About this Release                                           10

        Multitasking Basics                                            11
          Tasks                                                        11
          Events                                                       11
          Reentrancy                                                   12
          Deadlocks                                                    13

        Using CTask                                                    15
          Configuration Options                                        15
          Memory Allocation                                            21
          Snapshot                                                     21
          Task Stacks                                                  22
          Drivers                                                      22
          Things to remember                                           23
          Priority Handling                                            23

        Multitasking and DOS                                           25
          Spawning and CTask TSR's                                     26
          Task Groups                                                  27

        How does CTask work                                            29
          Queues                                                       29
          The Scheduler                                                30
          Events                                                       30
            Resources                                                  30
            Flags                                                      31
            Counters                                                   31
            Mailboxes and Pipes                                        31
          Serial and Printer Drivers                                   32


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -          Contents 1



        CTask Data Types                                               34
          Other definitions                                            35
          Typedefs used for simplified type specifications             36
          Error return values for event wait functions                 37
          Queues                                                       37
          The timer/watch/hotkey control block                         38
          The name link structure                                      43
          The task control block structure                             43
          Task states                                                  46
          Task flags                                                   47
          The Group Control Block                                      48
          The event control blocks                                     49
            The Ticker structure                                       49
            The flag event structure                                   50
            The counter event structure                                50
            The resource event structure                               51
            The mailbox event structure                                51
            The pipe and word pipe event structure                     51
            The buffer event structure                                 52
            The call chain structure                                   53

        CTask Routines                                                 54
          Global Variables                                             54
          Installation and Removal                                     54
          Searching for names                                          57
          Adding names                                                 58
          Remove Functions                                             58
          Preemption and Scheduling                                    59
          Miscellaneous                                                60
          Task Operations                                              62
          Timer Operations                                             64
          Event wait Timeouts                                          65
          "Tickers"                                                    65
          Delays                                                       66
          Timed Events, Watch Events, and Hotkeys                      66
          Event Operations                                             75
            Resources                                                  75
            Flags                                                      77
            Counters                                                   79
            Mailboxes                                                  81
            Pipes                                                      83
            Buffers                                                    86
          The Keyboard Handler                                         88
          The Serial I/O handler                                       88
          The Printer Output Driver                                    94
          Support Modules                                              96
            Memory Allocation Interface                                96
            Printf replacements                                        97
            Snapshot Dump                                             100




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -          Contents 2



        Advanced Topics                                               101
          Primary and Secondary Kernels                               101
          TSR, Spawning, and EMS                                      104
          Functions called by Kernel Routines                         105

        Some notes on potential trouble spots                         107
          Turbo C console output                                      107
          The timer tick EOI                                          107
          Debugging                                                   108

        Changes from Previous Versions                                109
          Changes for CTask 2.1 to 2.2                                109
            Version 2.2 Interface Changes                             111
          Changes for CTask 2.0 to 2.1                                112
            Version 2.1 Interface Changes                             115
          Changes for CTask 1.2 to 2.0                                116
            Version 2.0 Interface Changes                             116
          Changes for CTask 1.1b to 1.2                               118
          Changes for CTask 1.1 to 1.1b                               120
          Changes for CTask 0.1 to 1.1                                120

































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -          Contents 3



                                About this Manual

        If you are new to CTask, I would suggest reading all chapters
        before attempting to build your first application. One chapter
        you can skip is the CTask Data Types section, since you are not
        required to know about the innards of CTask's structures. You can
        also ignore the List of Changes.

        If you are updating from version 2.0, read the List of Changes,
        and the new Advanced Topics section. The chapters on Data Types
        and Routines, and the Using CTask section, also contain new
        information. All other chapters are basically unchanged.

        Version 2.1 users will find little new information here. The
        changes in the data structures, and the new routines, are
        reflected here, but if you're short on paper, it should be
        sufficient to print just the list of changes.

        If you are updating from an older release, the List of Changes at
        the end is for you. You can safely skip the Introduction, and the
        section on Multitasking Basics. In the General Notes, you should
        read the section on support and the info about this release. In
        the Using CTask section, check the new configuration options, and
        the chapter on Memory Allocation. Check the Routine descriptions,
        and, if you are using internal data structures directly, the Data
        Type descriptions, for changes. The Advanced Topics section is
        new.


        Finally, a note to German speaking readers:

        Dieses Handbuch, wie auch die Kommentare im Quellcode, ist in
        Englisch abgefaát, da dies die universelle Sprache f�r Computer-
        benutzer weltweit ist. Es gibt keine deutsche Version, und es
        wird voraussichtlich auch keine geben (sofern nicht jemand bereit
        ist einen angemessenen Betrag f�r eine šbersetzung auf den Tisch
        des Hauses zu legen). Selbstverst„ndlich bleibt es Ihnen
        unbenommen, das Handbuch selbst zu �bersetzen und diese Version
        auch zu vertreiben, oder mir zum Vertrieb anzubieten. Wie die
        Software ist auch dieses Handbuch Public Domain.













        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 1



                                   Introduction

        CTask is a set of routines that allow your C program to execute
        functions in parallel, without you having to build in sophisti-
        cated polling and switching schemes. CTask handles the switching
        of processor time with a priority based, preemptive scheduler,
        and provides a fairly complete set of routines for inter-task
        communication, event signalling, and task interlocking. CTask
        also includes a number of drivers for MS-DOS that build on the
        basic functions to allow you to include serial I/O, printer
        buffering, and concurrent access to DOS functions into your
        programs with little programming effort.


                                    An Example

        To illustrate one possible use of CTask, let me elaborate on the
        following example. Say you just finished your nifty telecommuni-
        cations program, complete with download protocols, scripts, and
        everything.  But wouldn't it be nice to be able to print the file
        you just downloaded while receiving the next, and edit a comment
        to some previous message without interrupting the transmission?
        So you take those editor routines from a previous project, plug
        them in, and - oops, how do you switch back and forth between
        editing, communication and printing? The answer to this is CTask.
        CTask allows your C program to do many different things at the
        same time by switching the processor between the tasks you de-
        fine. And since most of the time your program is waiting for some
        slow device (like the human hand) to provide feedback, this
        switching is completely transparent, and will not noticeably slow
        your program down.


                              Switching the Context

        So what is needed to allow the user to edit a file while at the
        same time downloading another and printing a third? First, you
        have to have some form of "context switching". This means that
        you have to be able to interrupt the processing of the download
        when the user presses a key, process the key, and return to the
        download "task" at the exact same point it was interrupted. One
        solution to this would be to include a poll for the keyboard at
        several points in the download routine, and call the editor task
        when a key is available.  But apart from cluttering your code
        with lots of unrelated calls, there is another problem. What if
        the operation the user requested is more involved than just
        putting the character on the screen, like writing the file to
        disk? This might take so long that your download times out. There
        must be a way to pass control back and forth between the two
        tasks, such that no task is delayed for an extended period of
        time, and also to activate the print spooler task at some defined
        interval to output the data to the printer. This context
        switching is called "scheduling" in CTask. The "scheduler" is
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 2



        invoked on every system timer tick, and will save the context of
        the current task. The scheduler then takes the first element from
        the queue of tasks that are eligible to be run, and restores the
        context of this task, returning to the point where the task was
        interrupted. This switching is completely automatic, and requires
        no special programming in the tasks itself. All you have to do is
        to tell CTask that there are three tasks, the download task, the
        spooler task, and the editor task.


                                  You have Mail

        All you have to do for context switching, that is. There's a bit
        more to multitasking than meets the eye. How do you tell the
        spooler task what files to spool, and the download task what
        files to download? You can't call a task like an ordinary func-
        tion, so what you need for this is "inter-task communication".
        There must be a way to pass a message containing the filename to
        be printed to the spooler task, and there are several in CTask,
        one of them the "mailbox". The spooler can use a CTask call,
        wait_mail, to wait for a message to arrive at its mailbox. As
        long as nothing arrives, the spooler task will no longer be
        scheduled, so if there is nothing to print, it will not use any
        processor time. When you send a message with send_mail to the
        mailbox, the spooler will wake up, and process the file. You can
        also send more file name messages to the spooler while it still
        prints a file, leaving the messages in the mailbox until the
        spooler is ready to process the next file.


                             Reentrancy and Resources

        This last example seems innocent enough, but there's a big stumb-
        ling block hidden in it. You allocate the file name messages in
        the controlling task with malloc, and you free them in the
        spooler with free, no problem, right? Wrong, there is a big
        problem, "reentrancy". Reentrancy means that you can re-enter a
        routine while another task is already using it, and that this
        will not disturb the operation of the interrupted task. But
        malloc and free share and modify global data, the chain of free
        memory blocks. Imagine the following: You just called malloc from
        the controlling task. Malloc has loaded the address of a free
        element into a local variable, and is about to write back the
        pointer to the next free element into the last. At exactly this
        moment, the timer ticks, and the spooler is activated. It has
        just finished printing, so it calls free. Free steps through the
        chain of free blocks to find the right place to insert the block.
        According to Murphy's law, it will find just the place where
        malloc is about to write back the pointer. Free coerces the
        elements, points the next pointer to the element malloc just
        wants to take off the chain, and returns. Malloc writes its next
        pointer into the middle of the newly coerced block, and now re-
        turns an element which is still in the free list. Compared to the
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 3



        job of finding this kind of bug, stepping in for Tantalus may
        feel like a vacation. This kind of problem code is called a
        "critical region". There must be a way to make sure that no two
        tasks simultaneously enter such a region, and, you guessed it,
        CTask provides one, the "resource". When you request a resource
        in one task, all other tasks trying to request the same resource
        after that are put to sleep until you call release_resource. Only
        then will the highest priority task that waits for the resource
        wake up, and get access to the protected region. So you would
        have to substitute malloc and free calls in your routines with
        calls to functions that first request a resource, execute the
        function, and then release the resource.


                                    DOS Access

        But, you might ask, isn't there another reentrancy problem in
        this example, since both the spooler and the download task might
        simultaneously call DOS to do their file-I/O, and DOS is not
        reentrant? Do I have to substitute all my calls to fread and
        fwrite, too? The answer to this, luckily, is no. CTask traps all
        your DOS calls, and automatically encloses them in the necessary
        resource request and release calls, so you don't have to worry
        about trashing your disk by simultaneous DOS requests. The
        limited multitasking capabilities of DOS are exploited to allow
        some parallel processing in DOS, and CTask will also detect and
        handle DOS calls by resident background programs like the DOS
        PRINT utility.


                              Handling the Keyboard

        CTask also allows you to circumvent DOS for keyboard input, so
        that waiting for the keyboard will not block other tasks from
        access to DOS functions. Previous versions of CTask used a "pipe"
        to store all keyboard input. Starting with version 1.2, CTask
        uses a "flag" to signal that keyboard input might be available. A
        "flag" is another form of inter-task communication that just sig-
        nals that some event occurred, without passing any specific data.
        The reason for using flags in the keyboard handler is compati-
        bility to TSR's. If a keyboard interrupt occurs, the interrupt
        handler just sets a flag, and passes on the interrupt. The key-
        board routines wait for this flag to be set, and then check the
        keyboard buffer if a character has arrived. If the keyboard buf-
        fer is empty, the flag is again cleared, and the keyboard rou-
        tines put the waiting task to sleep again, so the processor is
        free to do more interesting things than to loop waiting for the
        user to press a key.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 4



                             Serial I/O and Timeouts

        The "pipe" is similar to the mailbox in that you can wait for
        items to be sent to a pipe. But unlike mailboxes, pipes use their
        own buffer to store the items (which are limited to bytes and
        words), so you don't have to allocate mail blocks for each item.
        When waiting on the pipe, your task is put to sleep, freeing the
        processor. Pipes are used for the serial I/O handler included
        with CTask that makes some of the work you've put into your
        communications package obsolete. When outputting data to the
        serial port via the CTask routines, the data is buffered in a
        pipe, and incoming data is also placed in a pipe. All interrupt
        handling, and the processing of modem status and XON/XOFF proto-
        cols, is done by CTask, so you can concentrate on implementing
        the higher level protocols. Since CTask allows all calls that
        wait for pipes, mail, and other events, to specify a timeout that
        is based on the system tick, you do not have to resort to timed
        waiting loops to detect communication line faults. You simply
        give a time limit on the wait call, and if that limit expires,
        the wait routine will return with an error indication.


                                    Priorities

        If the protocol you implement requires fast responses to incoming
        blocks, you can influence the response of CTask to your comm
        task's needs by giving this task a higher priority. CTask allows
        65535 different priority levels, and tasks having higher priority
        are scheduled before tasks with lower priority. Also, high prio-
        rity tasks will get access to mail, pipes, and resources, before
        other tasks. It might even be sensible to split the comm task
        into two separate tasks, one of high priority that assembles the
        incoming bytes into blocks and handles the protocol, and a lower
        priority task that reads the received blocks from a mailbox and
        stores them on the disk. In extremely time critical applications,
        you can even turn off task preemption, so the timer tick will no
        longer cause a task switch.


                              Change to your liking

        CTask provides all basic building blocks for implementing
        concurrent programs in an easy and comprehensible way. Since
        CTask is mainly implemented in C, it may not be the fastest
        possible system, but due to the straightforward design which uses
        few shortcuts, modifying the sources to suit your needs and taste
        can be done without weeks of studying assembler code that
        squeezes every microsecond from the processor. CTask is public
        domain code, and there are no restrictions on its use. It is
        distributed in source form, so you are free to change all aspects
        of the package. Multitasking programs, especially in embedded
        applications, tend to be very diverse in their needs for specific
        constructs. So although CTask is ready to run under DOS, and is
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 5



        easily adaptable for embedded applications, you should see CTask
        more as a starting point for your own thoughts, and as a toolbox
        from which you can pick the instruments you need, than as a
        finished and fixed block of code you simply plug into your
        application.
















































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 6



                                  General Notes


                         What can CTask NOT be used for?

        CTask is not intended to provide for multitasking on the command
        level of MS-DOS. Although version 1.2 of CTask added the ability
        to TSR and spawn other programs, and to communicate between
        multiple copies of CTask, a full DOS-process management (which
        would have to include keeping track of memory allocation and DOS
        process control blocks) is not included. Adding this functio-
        nality would not be trivial (although certainly worthwhile).

        CTask also is not a true "Real-Time" multitasking system. Due to
        the completely dynamic structure of tasks and events, and the
        minimal restrictions on what interrupt handlers may do, it is
        nearly impossible to calculate a maximum interrupt or task switch
        latency. If you have critical timing requirements, you should
        consider getting a professional package like AMX. CTask has been
        used successfully in embedded control applications, and if your
        timing requirements are not that critical, or you're ready to
        take up the task of measuring and calculating latencies with your
        specific task setup, CTask may be useful even for Real-Time
        applications. However, you're more or less on your own in this
        field.

        And, there is no warranty that CTask does perform without errors,
        or does exactly what you or I intended. So CTask should not be
        used in applications in which malfunction of routines of this
        package would result in damage to property or health of any
        person without *very* extensive testing under all kinds of loads.
        In using CTask, you do so at your own risk. I have tested CTask
        extensively, but with a complex system like CTask, where timing
        might make a big difference, you can't be completely sure that
        all will work as intended.


                          What is required to use CTask?

        To compile CTask, Microsoft C 5.1 or later, or Turbo C 2.0 or
        later are required. Microsoft MASM 5.1 or later, or TASM 1.01 or
        later is required for the assembler parts. Conversion to other
        compilers is possible if they conform to the new ANSI standard.
        Conversion of the assembler parts to other Assembler versions
        will likely be more complicated, since it requires substitution
        of the simplified model directives by explicit segment
        definitions, and adding the DGROUP to offsets referencing data.

        Note that you can not use TASM 1.0 to assemble CTask routines.
        The first version of TASM was not fully compatible with MASM, and
        creates different code in some places, which will lead to fatal
        crashes. TASM version 1.01 does not have this problem, and can
        safely be used.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 7



        The CTask modules have been compiled and tested with Microsoft C
        6.0 without any apparent problems (Optimization level tested was
        /Ox). Since the stability of the MSC 6.0 code generator is
        doubtful, the distributed library was compiled with MSC 5.1.

        CTask will add 14k-25k of code to your program, depending on
        options and installed drivers. The minimum static data used by
        CTask is approximately 4k. Non-DOS versions use less memory.

        Converting CTask for stand-alone operation requires few changes.
        Mainly, the timer interrupt handler (in "tsktim.asm") has to be
        rewritten, and the initialization code (in "tskmain.c") may have
        to be changed. Changes to other modules (naturally except the
        optional hardware drivers) should not be necessary. The "DOS" and
        "IBM" configuration flags in tskconf.h can be disabled to elimi-
        nate most system-dependent features of CTask.

        Another requirement is a good debugger. If you never before wrote
        multitasking applications, you're in for some surprises. The nor-
        mal debugging tools (Symdeb, Codeview) are of only limited use,
        since they use DOS calls for their I/O, and thus may conflict
        with your background tasks. One safety measure is to first thor-
        oughly test your program with preemption disabled, possibly
        inserting some schedule() calls, and only allow task preemption
        if you found most major bugs. I personally recommend Periscope
        for debugging, since it can be made resident and so is always
        available, and because it does not use DOS. Periscope IV is the
        most expensive solution, and the best tool you can imagine, but
        the less costly versions will also help a lot.


                        Do I have to pay for using CTask?

        No. One reason for writing CTask was to provide a free, no
        strings attached, utility, instead of the usual "for personal use
        only" restriction. Writing a multitasking application for
        personal use only doesn't seem too interesting to me. CTask is
        completely free, and there is no restriction on its use. You may
        incorporate all or parts of CTask in your programs, and redistri-
        bute it in source or binary form by any means. I also do not
        restrict the use of CTask in commercial applications. Since
        trying to distribute the unmodified CTask for money will only
        give you a bad name, you may even do that if you find someone
        dumb enough to buy it. Naturally, if you make a bundle from it,
        or simply like CTask, I would not reject a donation. However,
        this is not required, and it will not give you any special
        support.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 8



                           What support can I expect?

        I will try my best to eliminate any bugs reported to me, and to
        incorporate suggested enhancements and changes. However, my spare
        time is limited, so I can not guarantee continued or individual
        support. (But since I'm one of the owners of a consulting firm,
        you can always hire me to do it...). Please address all reports
        or questions to my business address:

                Ferrari electronic GmbH
                attn: Thomas Wagner
                Ruhlsdorfer Strasse 138
                D-14513 Teltow, Germany

                Phone: (+49 3328) 474 626
                Fax:   (+49 3328) 438 04-0
                BBS:   (+49 3328) 438 04-8 (from 8/15/93)

                Internet:    twagner@bix.com
                BIX:         twagner
                Compuserve:  100023,2042

        But, please, if at all possible, do it in writing. Please do not
        phone unless it is absolutely vital (or you have a business
        proposal). I like to hear about any applications for CTask, and
        if you are visiting Berlin, I also invite you to drop by for a
        talk. But I am usually not that happy when I am interrupted in my
        paid work by a phone call requesting support for a free product.

        I will try to answer all letters and Faxes I receive. However, I
        am usually not the fastest in this respect, so please be patient.
        If you don't hear for me for a while, send me a short reminder.
        The preferred, and the fastest, method to reach me is through
        BIX, which is connected to the Internet, or through our own
        BBS, which is scheduled to be operational August 15th, 1993.

        BIX (tm) is an Information Exchange, an electronic confe-
        rencing system owned by GVC. BIX can be (and is) accessed from all
        parts of the world. Although accessing BIX from outside the US
        isn't exactly cheap (don't ask me what I have to pay each month),
        the wealth of information available there, and the fast and
        extensive help the other members can give you on all kinds of
        hard- and software problems, makes it worth every Mark, Peseta,
        Franc, or Ruble you have to spend. New versions and updates of
        CTask will first appear on BIX.

        At the time of this writing, I am one of the moderators of the
        IBM exchange on BIX, moderating the "ibm.other" conference. I
        have created a support topic for CTask, where all suggested
        enhancements and changes, plus bug reports, can be posted. Just
        join "ibm.other", topic "ctask". You can also report problems of
        limited general interest via BIXmail to "twagner". Unless I am
        not able to reach the keyboard for some reason, I log on at least
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -              Page 9



        once per day, so you can expect relatively fast responses to your
        queries.

        To get more info on joining BIX, call the BIX Customer Service at
        800-227-2983 (U.S. and Canada), or 603-924-7681 (New Hampshire
        and outside the U.S.) from 8:30 to 23:00 Eastern Time (-5 GMT).
        BIX access currently is $39 for three months (flat fee, no extra
        charges for connect time), plus the applicable telecomm charges
        (Tymnet in the U.S. and Canada, your local PTT's Packet Net
        charges from outside the U.S.). 
        International users living near a BT Tymnet node can access BIX 
        through international Tymnet at special low rates. Call the BIX 
        helpline for Tymnet access points and charges. Other international 
        users will need an account (NUI) with their local packet net. 
        Please enquire at your post/telecomm office for details.


                                About this Release

        Since the Beta release of CTask in March 1988, CTask has found
        widespread distribution through several channels. I have heard
        from some users, and their suggestions have been implemented in
        this version as far as possible.

        Special thanks go to Kent J. Quirk, Peter Heinrich, Stephen
        Worthington, Burt Bicksler, Tron Hvaring, Joe Urso, Dave Goodwin,
        Chris Blum, and Dan Heine, for their bug reports, suggestions,
        and enhancements. Bug reports and suggestions also came in from
        others, thanks to all who wrote or called. The serial code in
        TSKSIO.C was enhanced for version 2.0 by S. Worthington, and his
        ideas on debugging have been incorporated in the version 2.1
        debugging mode. Dan Heine provided valuable info on 80x87 numeric
        coprocessor support. Chris Blum wrote the integer-based
        millisecond to clock-tick conversion routine.

        Again, please notify me of your CTask application, report bugs,
        or suggest changes and enhancements. If I know you're using
        CTask, I can notify you of possible new releases and of possible
        severe bugs.









        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 10



                               Multitasking Basics

                                      Tasks

        In CTask, a "task" is defined as a (far) C function. The number
        of tasks is not limited, and one function may be used for several
        tasks. There is little difference between a task function and a
        normal function. The usual form of a task function is

             void Taskfunc my_task (farptr arg)
             {
                  one-time initialization code
                  while (TRUE)
                    {
                    processing code
                    }
             }

        A task function is (usually) never called directly. Rather, it is
        specified in the call to the create_task routine, and started by
        start_task. It will then continue to run, sharing the processor
        time with all other tasks, until it is "killed" by kill_task.
        Returning from the routine will have the same effect as a kill.
        The sharing of processor time is accomplished by "preempting" the
        tasks. Preemption means that the task is interrupted in the
        middle of some statement by a hardware interrupt (usually the
        timer), and is *not* immediately restarted when the interrupt
        handler returns. Instead, the next task that is able to run is
        activated by the "scheduler", with the interrupted task
        continuing its duty at some (normally unpredictable) later time.
        You can also have multi-tasking without preemption, and CTask
        supports this, too, but this requires full cooperation of all
        tasks in the system, such that no task continues to run for an
        extended period of time without passing control to other tasks by
        an explicit scheduling request, or by waiting for an event.

        The optional argument to the task function may be used if one
        function is to be used for more than one task, for example to
        pass a pointer to a static data area for use by this specific
        instance of the function.


                                      Events

        Tasks alone would be of limited use. If you have several routines
        which just do number crunching or sorting or such, making them
        into parallel tasks would be sensible only on a multiprocessor
        system. Normally, at least some of your tasks will wait for some
        outside "event" to happen, be it the user pressing a key, or a
        character arriving from the modem. Then there may be tasks which
        have to wait until another task finishes processing on some piece
        of data before they can continue. For this synchronization, there
        are a number of constructs in CTask, which I summarize under the
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 11



        name "event". Common to all events are the operations of waiting
        for an event to happen, and signalling that the event has
        happened. Using a CTask event is much more efficient than looping
        while waiting on some shared data location to change state, and
        also eliminates concurrency problems inherent in such a simple
        approach. Tasks waiting for an event are taken off the scheduler
        queue, so they no longer use processor time.


                                    Reentrancy

        One of the biggest problem with multitasking in general, and C on
        the PC in particular, is reentrancy. Reentrancy means that you
        can use a routine, be it you own, or one of the C run-time
        library, from different tasks at the same time. When writing your
        own code, you can easily avoid problems, but when using the run-
        time library routines, you often can only guess if the routines
        are reentrant or not.

        A routine is NOT reentrant if it modifies static data. This can
        be illustrated by the following nonsense example:

             int non_reentrant (int val)
             {    static int temp;
                  temp = val;
                  return temp * 2;
             }

        Now take two tasks, which call this routine. Task1 calls it with
        val=3, Task2 with val=7. What will be the return value for both
        tasks? You never know. There are three possible outcomes:

          1) The tasks execute sequentially. Task1 will get 6, and Task2
             14 as a result. This is what one normally expects.

          2) Task1 runs up to "temp = val", then is interrupted by the
             timer. Task2 executes, and gets 14 as result. Then Task1
             continues. Return for Task1 is 14.

          3) Task2 runs up to "temp = val", then is interrupted by the
             timer. Task1 executes, and gets 6 as result. Then Task2
             continues. Return for Task2 is 6.

        add to this the effects of optimization, and a loop, and the
        outcome is completely random.

        Most routines in the C library will not explicitly do something
        like this, but all functions that

             - do file I/O (read, write, printf, scanf, etc.) or
             - change memory allocation (malloc, free, etc.)


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 12



        have to use some static data to do buffering, or to store the
        chain of memory blocks in. Interrupting such an operation may
        have disastrous effects. The most devilish aspect of non-
        reentrancy is that the effects are unpredictable. Your program
        may run 1000 times without any error, and then on the 1001th time
        crash the system so completely that only the big red switch will
        help.

        So what can you do about it? A lot. There are several ways to
        protect "critical regions" from being entered in parallel. The
        most simple method is to disable interrupts. This, however,
        should be used only for *very* short periods of time, and not for
        rou-tines that might themselves re-enable them (like file-I/O). A
        better method is to temporarily disable task preemption. The
        routines tsk_dis_preempt and tsk_ena_preempt allow this form of
        short-term task switch disable. Interrupts may still be
        processed, but tasks will not be preempted. The best way is to
        use a "resource". A resource is a special kind of event, which
        only one task can possess at a time. Requesting the resource
        before entering the routine, and releasing it afterwards, will
        protect you from any other task simultaneously entering the
        critical region (assuming that this task also requests the
        resource).

        It is also reasonably safe to use file-I/O without protection if
        it goes to different files. The C file control blocks for
        different files are distinct, so there will be no conflict
        between tasks. Since DOS access is automatically protected by
        CTask, concurrent file I/O is possible.

        What you may NEVER do is to use a non-reentrant routine that is
        not protected by an interrupt disable from an interrupt handler.
        An interrupt handler is not a task, and so can not safely request
        a resource or disable task preemption. This is the reason why the
        CTask routines generally disable interrupts before manipulating
        the internal queues rather than only disabling task preemption.


                                    Deadlocks

        One thing to watch out for when using resources or similar event
        mechanisms is not to get into a situation where Task 1 waits for
        a resource that Task 2 has requested, while at the same time Task
        2 waits for a resource that Task 1 already has. This situation is
        called a deadlock (or, more picturesque, deadly embrace), and it
        can only be resolved with outside help (e.g. waking up one of the
        tasks forcibly). To illustrate, consider the following example:






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 13



             void far task_1 ()
             {
               ...
               request_resource (&rsc1, 0L);
               request_resource (&rsc2, 0L);
               ...
             }

             void far task_2 ()
             {
               ...
               request_resource (&rsc2, 0L);
               request_resource (&rsc1, 0L);
               ...
             }

        Since interrupts are always enabled on return from a task switch,
        even if the statements are enclosed in a critical region, there
        is no guarantee that the request_resource calls will be executed
        without interruption. In this example, the problem is obvious,
        but in a more complex application, where resource requests or
        other waits might be buried in some nested routine, you should
        watch out for similar situations. One way to avoid problems would
        be in this example to change task_2 to

             void far task_2 ()
             {
                  int again;
                  ...
                  do {
                       request_resource (&rsc2, 0L);
                       if (again = c_request_resource (&rsc1))
                          {
                          release_resource (&rsc2);
                          delay (2L);
                          }
                     } while (again);
                  ...
             }

        Note that this is only one of many possible approaches, and that
        this approach favors task_1 over task_2.

        You should also take care not to kill tasks that currently own a
        resource. CTask will not detect this, and the resource will never
        be freed.







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 14



                                   Using CTask

        CTask comes archived with both source and binaries. The binary
        version is compiled in the large model, but since the precompiled
        kernel routines don't use any functions from the C library, you
        can use all functions in small or other model programs (except
        Turbo C's Tiny and Huge models). The include files provided
        specify all model dependencies, so you don't have to use the
        large model for your application, but always remember to include
        "tsk.h" for the type definitions and function prototypes.

        The C source files will work without changes for both Microsoft
        and Turbo C. The library files are not compatible, so use
        "ctaskms.lib" for Microsoft, and "ctasktc.lib" for Turbo C.

        In the distributed configuration (i.e. dynamic allocation of
        control blocks enabled), the file TSKALLOC.C must be added to the
        library or separately linked after compiling it *in the same
        model as the main program*. This file uses C-library routines,
        and thus must match the main program's memory model. The same
        goes for TSKSNAP.C, an optional snapshot-dump utility, and
        CONOUT.C, the sample console output handler. The provided
        "ctsupms.lib" and "ctsuptc.lib" files have been compiled in the
        large model, and may only be used with large model programs.

        Turbo C's huge model uses a different segment setup for data
        segments. This requires using a special data segment for all
        CTask data, and compilation of the CTask kernel in huge model.
        For the assembler files, the symbol TC_HUGE must be defined
        during assembly, the C files must be compiled with the Data-
        Segment and BSS-Segment naming options. Make-files for Turbo C
        Huge model are included.


                              Configuration Options

        The file TSKCONF.H contains a number of #define's that allow you
        to configure some CTask features. In general, you should
        recompile all of CTask when changing one of the flags. Version
        2.1 collects all configuration options for both Assembler and C
        in this file.

        The entries are

        CODE_SHARING
             If TRUE, the generated kernel supports code sharing. This
             requires the entry points to load DS on entry, and compi-
             lation with Large model (MSC) or Huge model (TC).

             This option is normally disabled (FALSE).



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 15



        NEAR_CODE
             If TRUE, all CTask routines are 'near'. Use only with small
             or compact model. You will have to change the make-files so
             the compiler model is no longer Large, and the code segment
             is not named, when turning on this flag. The default is
             FALSE. Setting this option TRUE will save code, and make
             calls faster, but the library will no longer be model
             independent.

             This option is normally disabled (FALSE).

        LOCALS_FAR
             If TRUE, internal CTask routines ar 'far'. This might be
             necessary if your compiler/linker does not allow placing all
             CTask kernel code in a common segment. Do not set this flag
             if NEAR_CODE is set.

             This option is normally disabled (FALSE).

        CALL_PASCAL
             Use Pascal calling sequence for CTask routines.  This may
             save some code, but may cause naming conflicts if your
             compiler limits external Pascal names to 8 characters.

             This option is normally disabled (FALSE).

        TC_HUGE
             (Assembler only) Define TC_HUGE for use with the Turbo C
             Huge model, and if it is desired to separate CTask's data
             from the normal data segment. This flag causes the
             CTASK_DATA segment to be defined, (class is DATA) and DS to
             be loaded with this segment on function entry. The C
             functions in the CTask kernel must be compiled to use the
             same data segment.

             This option is normally disabled (undefined).

        LOAD_DS
             (Assembler only) Define LOAD_DS to reload the data segment
             on entry to global functions. This flag must be defined for
             TC_HUGE. It can also be defined if the data segment can not
             safely be assumed to be loaded in DS on function entry, for
             example if the code sharing feature of version 2.1 is used.
             The C routines must be compiled with the necessary compiler
             switches or the _loadds keyword in this case.

             This option is normally disabled (undefined).






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 16



        ROM_CODE
             (Assembler only) Define ROM_CODE TRUE for embedded systems
             using ROM-based code. This option disables storing variables
             in the code segment in some modules. Note that most DOS-
             related modules are not ROMable.

             This option is normally disabled (FALSE).

        FAR_STACK
             (Assembler only) Define FAR_STACK TRUE to save some space in
             the default DGROUP. With this define TRUE, the local stacks
             for the scheduler, the timer, and the interrupt handlers,
             are allocated in a separate segment. With Turbo C, you may
             have to edit the "c0.asm" startup module to accomodate the
             new segment.

             This option is normally disabled (FALSE).

        TSK_DYNAMIC
             If TRUE, you can let CTask dynamically create task and event
             control blocks, task stacks, and pipe buffers, by passing
             NULL as the block address. Since this requires the C runtime
             allocation calls, it is not suitable for non-DOS appli-
             cations (except if you provide your own memory allocation
             routines).

             This option is normally enabled (TRUE).

        TSK_DYNLOAD
             If FALSE, this instance of the kernel does not include
             dynamic allocation routines. Setting this flag to FALSE when
             TSK_DYNAMIC is TRUE only makes sense with multiple linked
             kernels. A resident kernel might not employ dynamic
             allocation, whereas a secondary kernel needs it. In this
             situation, TSK_DYNAMIC must be set in the primary so that
             the task kill code is included and the kernel configurations
             match, but TSK_DYNLOAD may be false to prevent inclusion of
             the malloc/free run-time routines. This option has no effect
             if TSK_DYNAMIC is FALSE. The default is TRUE.

             This option is normally enabled (TRUE).

        TSK_NAMEPAR
             If TRUE, all create_xxx calls accept an additional
             parameter, the name of the created control block. This name
             should contain only printeable characters, and should not be
             longer than 8 characters plus the zero terminator. This
             option is used together with TSK_NAMED (see below).

             This option is normally enabled (TRUE).
             It must be enabled for DOS.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 17



        TSK_NAMED
             If TRUE, all control blocks (except timer control blocks)
             are named and linked on creation. This allows the snapshot
             dump routine to display the system state, and also allows
             linking to control blocks from secondary kernels.
             TSK_NAMEPAR must be defined for this option to work. Since
             it may be desirable to switch off the handling of the names
             after the debugging phase, without having to change all
             create_xxx calls to omit the name parameter, the name
             parameter is ignored if TSK_NAMED is undefined, but
             TSK_NAMEPAR is defined.

             This option is normally enabled (TRUE).
             It must be enabled for DOS.

        GROUPS
             If enabled, task groups, i.e. multiple invocations of CTask,
             are supported.

             This option is normally enabled (TRUE).
             It must be enabled for DOS.

        CLOCK_MSEC
             If TRUE, all timeouts are specified in milliseconds instead
             of timer ticks. This allows programming of delays and
             timeouts independent of the speedup-parameter or the system
             tick rate.

             This option is normally disabled (FALSE).

        PRI_TIMER
             Specifies the priority of the timer task. Normally the timer
             task should have a higher priority than any other task in
             the system.

             The value is normally 0xf000.

        PRI_STD
             This value may be used in your programs as the standard
             priority of user tasks. Its value is arbitrary. It is not
             used in the kernel except for the definition of PRI_INT9
             (see below).

             The value is normally 100 (decimal).









        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 18



        PRI_INT8
             Determines the priority of the "int8"-task. This task chains
             to the previous interrupt vector for the sytem timer tick,
             and thus may activate resident TSR's. Since TSR's normally
             use polling when accessing the keyboard and other devices,
             the priority of the int8-task should be equal to or lower
             than normal user-defined tasks to allow your program to con-
             tinue to run while the TSR is active. You can tune this
             value so that some tasks are blocked by the TSR to avoid
             trashing the screen.

             The value is normally  PRI_STD.

        AT_BIOS
             If enabled, the AT BIOS wait/post handler is installed. May
             be disabled when compatibility problems arise. You can also
             disable installation of this handler with an install flag in
             the install_tasker call, but using the configuration flag
             will save some code. Embedded systems likely will use FALSE.

             This option is normally enabled (TRUE).

        INT8_EARLY
             If TRUE, the timer interrupt always uses early INT8 proces-
             sing, regardless of the IFL_INT8_EARLY installation flag.
             Setting this flag saves some code and data, but eliminates
             some flexibility. Under DOS, timer ticks can be missed under
             certain circumstances when set, so DOS based configurations
             always should use FALSE. The installation flag has a
             slightly different effect, and may be used under DOS with no
             adverse effects. Embedded systems likely will always use
             TRUE.

             This option is normally disabled (FALSE).

        INT8_LATE
             If TRUE, the timer interrupt always uses late INT8 proces-
             sing, regardless of the IFL_INT8_EARLY installation flag.
             Setting this flag saves some code, but eliminates some
             flexibility. Embedded systems likely will always use FALSE.

             This option is normally disabled (FALSE).

        IBM
        DOS
             Both IBM and DOS are more or less of informative value only,
             to point out those areas in the kernel that need attention
             when converting to non-IBM or non-DOS environments.
             Disabling one or both of this options requires the
             substitution of your own routines for installation, timer,
             and keyboard handling.

             Both options must normally be enabled (TRUE).
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 19



        SINGLE_DATA
             If enabled, only a single global data block is used. This
             speeds up processing, but prohibits linkage of multiple
             groups. Useful for dedicated systems, and also if your
             program is known to never interact with another copy of
             CTask. Should be left FALSE if you're not so sure, must be
             FALSE if GROUPS is enabled. The current version of the DOS
             handler requires GROUPS to be used, so it should only be
             TRUE for embedded systems.

             This option is normally disabled (FALSE).

        EMS
             If TRUE, EMS support is included. For DOS applications using
             spawn or going TSR, this should always be TRUE, unless it is
             known that the program will never be executed in an EMS
             environment. It must also be TRUE for programs using EMS.

             This option is normally enabled (TRUE).

        EMS_SAVE_SIZE
             Size of the EMS page info save area. For LIM 4.0 drivers,
             only four pages are saved, so 16 bytes should be sufficient.
             If the partial page map function is not available in the
             driver, more space may be required for holding the full page
             map.

             The value is normally 16.

        NDP
             If TRUE, 80x87 support is included. If this option is
             enabled, and no coprocessor is present, the machine can hang
             if the BIOS equipment configuration is set incorrectly.
             NOTE: Coprocessor support is not yet tested. Please report
             your experiences with this option.

             This option is normally disabled (FALSE).

        HOTKEYS
             If TRUE, keyboard hotkey support is included. Embedded
             systems likely will not use hotkeys, and may set this to
             FALSE.

             This option is normally enabled (TRUE).


        CHECKING
             Enables pointer and stack checks when TRUE. Checking
             pointers and task stacks slows down the system, but it is
             highly recommended to enable this option during development.
             Only turn off checking after debugging is complete.

             This option is normally disabled (FALSE).
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 20



                                Memory Allocation

        TSKALLOC.C is needed if TSK_DYNAMIC is enabled in tskconf.h to
        handle the allocation and free calls. If you want to use dynamic
        allocation in your own tasks, you should also use the functions
        tsk_alloc and tsk_free to avoid the reentrancy problems mentioned
        in the introduction. If you should need other forms of alloc
        (like calloc) the recommended way is to add those functions to
        TSKALLOC.C, requesting the resource alloc_resource before calling
        the C memory-allocation function.

        Joe Urso provided the following tip on how to force all memory
        allocation to pass through the resource handling functions:

        "I have found that some MS Library functions call the allocate
        and free library functions, namely the first call to fread(),
        fopen(), and fclose().

        To fix this situation I have

           - extracted FMALLOC from the llibce library,

           - renamed the functions within that object (via the Norton
             Utilities) to the upper case spelling of the functions
             (FREE, MALLOC, _FFREE and _FMALLOC) and replaced the file in
             the lib. I also did the same for object EXPAND because of
             the function REALLOC.

           - then modified TSKALLOC.C to contain the lower case spelling
             of malloc, free, and expand. These functions aquire the
             alloc resource, then call the upper case spelling of the
             name.

        At link time I now link with /NOIGNORECASE and /NODEFAULTLIB."

        An option is provided in tskalloc.c to compile the module with
        the modifications suggested by Joe Urso.


                                     Snapshot

        TSKSNAP.C is only needed if you want to include the snapshot dump
        into your program. Note that you can *not* use snapshot if you
        disable TSK_NAMED in tskconf.h.









        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 21



                                   Task Stacks

        When compiling your application, turn stack checking off. The
        standard stack check is of little use with task stacks, and may
        interfere with CTask's operation. The stack area for tasks should
        be allocated on the main program's stack, not in the static or
        heap data space. The reason for this is that some of the C
        library routines check for stack overflow regardless of your
        compile-time switches, and will crash your application if you use
        stacks outside the normal stack. The stack allocation parameter
        with LINK (MS-C), or the _stacksize variable (Turbo C) have to be
        increased to reflect the additional stack space. When calculating
        task stack sizes, keep in mind that library routines (esp.
        printf) allocate a lot of space on the stack for temporary
        variables. A minimum of 1k for tasks using library routines is
        recommended, 2k puts you on the safe side. Tasks not using C
        library routines may use a smaller stack, about 256 bytes at a
        minimum, plus space for any local variables and nested routines.
        Then add up all task stacks, and add space for the main task (the
        function calling install_tasker), with this size also dependent
        on what you will do in the main task while CTask is active.
        Stacks for tasks that do not use C library routines may be
        allocated anywhere.

        If you have the CHECKING option enabled, the snapshot dump will
        output the number of unused bytes of stack for each task. This
        can help you determine the optimum stack size for your
        application.


                                     Drivers

        The keyboard and DOS handlers are always installed with CTask.
        Using the serial I/O and printer drivers is optional, so you have
        to install them separately, but only *after* installing CTask.
        When using the serial driver, include "sio.h" in your modules,
        when using the printer driver, include "prt.h".

        Another driver that is automatically installed is the BIOS
        wait/post handler for the IBM AT. The AT BIOS contains some
        multitasking hooks to avoid busy waiting in the BIOS. If you
        experience problems with disk accesses or printer output through
        BIOS (not through the CTask printer driver), you should disable
        installation of this driver by setting AT_BIOS to zero in
        tskconf.h, or not specifying the IFL_INT15 flag in
        install_tasker. Normally, no problems should arise with this
        driver even in XT type machines.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 22



                                Things to remember

        Remember that tasks are not automatically started after creation.
        Use start_task to allow a created task to run.

        Always use create_xxx on resources, pipes, etc. Using the event
        routines without doing so will have unpredictable results. This
        is especially true with the new queue structure introduced in
        2.0/2.2, where uninitialised control structures will invariably
        lead to a system crash. Enable the CHECKING option to trap such
        cases.

        Before exiting the program, all installed drivers and CTask
        should be explicitly removed. Although the DOS handler traps the
        terminate call and automatically calls remove_tasker, you should
        make sure that all tasks are completed properly, and call
        remove_tasker yourself.

        Deleting events before exiting the program is not mandatory, but
        recommended to kill all tasks waiting for the event. You should
        be careful not to kill tasks while they are active in DOS. The
        kill_task routine should be reserved for fatal error handling.
        The best way is to let the tasks kill themselves depending on
        some global variable or event. If a task is killed while waiting
        for input in DOS, DOS operation may be severely impaired. If you
        use the C console input routines, make sure that the task returns
        from DOS before it is killed, if necessary by requesting the user
        to press a key.



                                Priority Handling

        CTask provides for prioritized task execution and event
        processing. This means that a task that has a higher priority
        will be run before any other tasks having lower priority. Also, a
        higher priority task will gain access to resources, counters,
        pipes, and mail, before lower priority tasks. With fixed
        priorities, this means that a high priority task can monopolize
        CPU time, even if it calls schedule() explicitly. Variable
        priority increases each eligible task's priority by one on each
        scheduler call, so that lower priority tasks will slowly rise to
        the head of the queue until they get executed. The priority will
        be reset to the initial priority when a task is run.

        Since variable priority increases processing time in the critical
        region of the scheduler, it is not recommended for systems in
        which a larger number of tasks is expected to be eligible
        simultaneously.

        Usually, all tasks in a system should have the same priority,
        with only very few exceptions for non-critical background
        processing (low priority) or very time-critical tasks (high
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 23



        priority). High priority tasks should be written in such a way
        that they either reduce their priority when processing is
        completed, or that they wait for an event. Busy waiting in a high
        priority task will severely impair system operation with variable
        priority enabled, and will stop the system until the task is
        placed in a waiting state with fixed priority.

        The (automatically created) main task is started with the highest
        possible priority below the timer task, so that it can process
        all initialisations before other tasks start running. To allow
        the system to operate, the priority of the main task must be
        reduced, or the main task must wait for an event or a timeout.









































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 24



                               Multitasking and DOS


        CTask includes (and automatically installs) a routine which traps
        all DOS calls, and makes sure that no two tasks simultaneously
        enter DOS. This is accomplished using the resource mechanism,
        with special provisions for the limited multitasking capabilities
        provided by DOS. There are a few calls, namely those with
        function codes <= 0x0c, which allow functions with codes > 0x0c
        to be executed while DOS is waiting for an external device
        (generally the keyboard) to get ready.

        This, however, limits the use of some C library functions, namely
        scanf and fread, for console input. Both these functions use
        handle input, and thus can not be interrupted. When writing
        routines for handling user input, keyboard read functions should
        either use the low-level calls getch and gets, or, better yet,
        the direct entries into the keyboard handler, t_read_key and
        t_keyhit, and then process the string with sscanf if desired.

        The keyboard handler (contained in tskkbd.asm) traps all keyboard
        interrupts, setting a flag when a key is hit. If a task reads
        from the keyboard, it is automatically made waiting if there is
        no key to read. Using getch and gets is less desirable since they
        use polling instead of event waiting, and thus degrade system
        performance. Also, the t_read_key and t_keyhit functions do not
        use DOS, so DOS functions <= 0C can be executed concurrently.

        The BIOS interrupts 10 (Video), 13 (Disk), and 16 (Keyboard) are
        protected by CTask. Using other BIOS interrupts directly should
        generally be avoided, unless you are absolutely sure they will
        not be used by other routines via DOS, or you provide your own
        critical region handling. Protection of INT 10 is optional, and
        should only be used if you expect to use BIOS level video output
        in parallel to other tasks. Since INT 10 calls occur extremely
        frequent in most programs, the overhead for reserving and
        releasing the resource can slow down the system noticeably.

        Starting with version 1.2, the DOS handling has been extended to
        automatically save and restore the DOS variable context on a task
        switch. This is done by directly saving the critical variables of
        the DOS data area in the task control block. An undocumented DOS
        call is used to determine location and length of this area. NOTE
        that this call is not available in DOS versions prior to 3.1, and
        may not be available in MS-DOS clones or emulators. This context
        save allows multiple DOS applications to run concurrently.

        The DOS access module has been tested to work with PC-DOS and MS-
        DOS versions 3.20, 3.30, 4.00, and 4.01. There were also no
        problems with the DOS PRINT program, and with Network drivers
        (Invisible Net) running in the background. Special provisions are
        built into the DOS module to detect background DOS calls. Using
        Sidekick also hasn't lead to any problems, although you may trash
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 25



        Sidekick's screen display by writing to the screen while Sidekick
        is active (note that your application *continues* to run while
        Sidekick or other pop-ups are active). I can not guarantee
        complete compatibility with all background and pop-up programs
        under all versions of DOS. Specifically, DOS versions prior to
        3.1 have significant problems with multitasking, and do not
        support the variable save call necessary for full DOS
        multitasking. Upgrading to a newer DOS version is recommended if
        you are still using DOS < 3.2 (DOS 3.1 has some bugs in other
        areas).

        Also starting with version 1.2, CTask is now compatible with MS-
        Windows in non-enhanced mode. It has been tested to work with
        Windows 286 1.2 and 2.1, and with Windows 3.0 in real mode, but
        the mechanism used should work with other non-preemptive
        versions, too.  CTask can be installed as a background TSR before
        starting Windows, or you may spawn Windows from CTask.
        Windows/386 is a special virtual-mode operating system and can
        generally not be combined with other multitaskers.

        CTask 2.2 will not work with Windows 3.0 in 386 enhanced mode
        when installed as a TSR before starting Windows. I now know why,
        but I did not have the time to do anything about it. The next
        version probably will support full Windows 3.0 compatibility. If
        you start CTask within Windows, everything will work smoothly,
        but CTask instances in different DOS-windows will not be able to
        communicate with each other.

        Other preemptive multitaskers like DesqView will most likely not
        coexist peacefully with CTask.

        Critical errors and Control C occurring while concurrent DOS
        access takes place may be fatal. Using the ctrlbrk() and
        harderr() functions of Turbo C, or their equivalents in MS C, to
        trap critical errors and Control C is highly recommended. Error
        handlers should be installed before CTask is installed.


                             Spawning and CTask TSR's

        Starting with Version 1.2, CTask programs can now spawn other
        programs, and Terminate and Stay Resident (TSR). The DOS context
        switch, plus the saving and restoring of interrupts 21-24, on
        every task switch, makes it possible to have multiple, nearly
        completely independent, programs running under DOS. But please
        note that CTask is not intended as a replacement for true DOS-
        multitaskers like DesqView. Implementation of such a system would
        surely be possible, using CTask as a base, but would require
        keeping track of all DOS control blocks. This is left as an
        exercise to the reader. The new features are intended to allow
        you to easily write background data aquisition or communication
        modules that run in parallel to other DOS applications.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 26



        Since the spawned program might itself be a CTask program,
        Version 1.2 automatically checks for the presence of a background
        copy of CTask. If one is found, the secondary invocation will
        link to the global data of the first CTask copy, making it
        possible to easily communicate between independent instances of
        CTask programs. The naming mechanism has been slightly changed to
        make it easier to find a task or data structure by name.

        For example, you could write a communications program in two
        separate parts. One part, the resident part, contains interrupt
        handlers and the protocol routines. The other part, the transient
        portion, contains the driving program, with editor, menus, script
        language and so on.  If the resident part is started, it first
        spawns the transient part, which handles setup, and starts
        communications. Both parts can communicate using all CTask
        mechanisms, i.e. pipes, buffers, mailboxes etc., with the
        transient part obtaining the pointers to the CTask structures
        defined in the resident part via the structure name. Now if an
        up- or download is started, the transient part can exit to DOS,
        and the resident part can spawn a copy of command.com. Voila -
        background up/download with minimum hassle.


                                   Task Groups

        Each invocation of the CTask kernel (i.e. each call of the
        install_tasker routine) creates a new "Task Group". This group
        chains all tasks and other control structures created by this
        program together, so they can be killed if the group terminates
        (through a DOS call or the remove_tasker routine). Although it is
        recommended to kill all structures before terminating, there are
        a number of situations where this is hard to control under DOS.
        So CTask tries to take a few safety measures to make sure the
        system does not crash due to pointers chaining into nowhere.

        But please note that care should be taken not to "pull the rug
        under a group's feet". CTask will attempt to clean up memory when
        a group terminates. However, if that group has spawned another
        non-CTask program, CTask doesn't know about it, so an orphan will
        be left in memory, and you might even manage to get the system
        into an unstable state.

        And, there are a few restrictions. Although it is possible to
        create multiple groups running, and terminating, independently in
        parallel, those groups must be created by separate tasks from one
        "home group". If one task creates a group, and the same task, or
        another task from this group, creates a second, then it is not
        possible to terminate the first group without also killing the
        second. You can view this like a tree, where you can cut off
        branches, but all sub-branches of that branch will come down with
        it.  The root of that tree, the primary invocation of CTask, can
        not be killed without killing the whole tree.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 27



        Also, it is mandatory that you at least try to call remove_tasker
        on termination. CTask can trap a program's termination, but this
        happens at a time when all the program's memory has already been
        released by DOS. This can lead to extremely dangerous situations
        if other tasks, or TSR's, allocate and modify this memory before
        CTask finishes it's cleanup. CTask will stop preemption while it
        is removing the group, but it still is definitely not recommended
        to rely on this mechanism.


        A sample for a task group structure follows:

                               -Root-
                                home
                                level
                                branch -----+
                                 ^ ^        |
                                 | |        |
                                 | |        v
                   -Group1-      | |     -Group2-
                    home   ------+ +----- home
                    level  <------------- level
                    branch -----+         branch
                     ^ ^        |
                     | |        |
                     | |        v
        -GroupA-     | |     -GroupB-
         home   -----+ +----- home
         level  <------------ level
         branch               branch


        In this sample, Groups 1 and 2 were created by different tasks in
        the Root group, Groups A and B by different tasks in Group 1.

        Three pointers are used in chaining groups. The 'branch' points
        to the first element in an unordered list of task groups on the
        same "branch level" one level "up" the tree. Those groups are
        chained by the 'level' pointer. To allow finding the home group
        when going "down" the tree (towards the root), all groups on the
        same level point there through the 'home' pointer. In this
        sample, you could kill Group2 without affecting Group1 or it's
        subgroups. Killing Group1 will terminate GroupA and GroupB.










        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 28



                               How does CTask work

                                      Queues

        CTask uses priority queues for most of its functions. A priority
        queue differs from the usual FIFO (first in, first out) queues in
        the insertion of elements into the queue. Rather than just
        placing new elements after the last queue member, the priority of
        the task determines its place in the queue. A task is enqueued
        after all queue members with higher or equal priority, but before
        any member with lower priority. Removal from the queue takes
        place at the first element. These queues are used with all
        operations in which a task is made waiting, be it waiting to get
        run, or waiting for an event. The advantage of this is the
        simplicity of implementing priorities. Other schemes might rely
        on arrays of queues, or searching through lists, to determine the
        highest priority waiting task. With priority queues, the most
        time critical function, scheduling, is very fast, since it can
        simply take the first task from the queue of eligible functions.
        The disadvantage is the time required to step through all greater
        or equal priority members of a queue to find the right place to
        insert the task. But since the number of tasks simultaneously
        enqueued in the same queue is normally relatively small with most
        multitasking systems, this disadvantage is more than offset by
        the simple, and thus easy to implement efficiently, scheme.

        Version 2.0 generalizes the queueing scheme, and uses doubly
        linked lists for all internal chains (except the ticker chain).
        The introduction of the "yield" function, which inserts a task at
        the end of the eligible queue, but resets the priority, mandated
        searching through the queue from the back end. The previous
        scheme, which walked the queue from the front end, could lead to
        task starvation in a system with polling tasks when yielding.
        Also, the timer algorithm was changed such that the timer task
        didn't have to step through all timeout elements, but rather to
        only decrement the first queue element ticker. This is
        implemented by storing the timeout as a tick difference to the
        next queue element rather than as an absolute value. Doubly
        linked lists make insertion and removal of elements at arbitrary
        points very simple, and eliminate the time needed to find an
        element in a queue.

        To alleviate the additional overhead associated with managing
        dual pointers, the main queueing routines were coded in
        assembler. Especially when operating with multiple far pointers,
        the code generated by the C compilers even with maximum
        optimization is not that impressive. The corresponding C code is
        included as a reference, and to aid porting to non-8086
        environments.




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 29



                                  The Scheduler

        In a CTask system, there is at least one essential queue: the
        eligible queue, which contains all tasks waiting to run. Each
        time the scheduler is invoked, it will first save all processor
        registers in the current task control block, and then enqueue the
        current task into the appropriate queue.  Normally, this will be
        the eligible queue. Then the first element in the eligible queue
        is removed from the queue, the stack is switched to the stack of
        this task, and processor registers are restored from the new TCB,
        returning to the point where the new task was interrupted. If the
        eligible queue is empty the scheduler will loop with interrupts
        enabled. The queue head pointer of the task control block of the
        current running task determines what will happen to the task when
        the scheduler is invoked. If it points to an event control block,
        the task will be enqueued as waiting for this event. If it is
        NULL, the task will not be enqueued in any queue, effectively
        stopping it. If it points to the eligible queue, the task will be
        enqueued there. In any case, the scheduler does not care what
        queue the task is to be enqueued in, since all queues use the
        same priority based ordering. If a task is no longer in the
        eligible queue, it can only be returned to this queue by an
        external event.


                                     Events

        External events can take several forms, which are relatively
        similar on the inside. All CTask events use a control block, with
        at least one queue for tasks waiting for the event. Although it
        would have been possible to summarize all events under a global
        structure, this approach was not used in CTask, the main reasons
        being execution speed and ease of use. So if you scan through the
        source files for CTask events, you will see many very similar
        routines, which only differ in the types of data and the names of
        queues they process. In a class based language like C++, one
        would certainly define all events as instances or derivations of
        one class. In plain C, the necessary type casting, and the
        different handling of certain cases, would clobber the code to
        the point of illegibility.


                                    Resources

        The event types "resource", "flag", and "counter" differ only in
        the kind of wait operations and the handling of the state
        variable. The resource is mainly for use in interlocking critical
        regions of code, to protect access to non-reentrant resources.
        Only one task can "own" a resource, all other tasks requesting
        the resource are delayed until the owning task releases it. For
        added protection, CTask stores the task control block address of
        the current owner of the resource in the resource control block,
        so no other task can erroneously release it.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 30



                                      Flags

        Flags, on the other hand, can be set and cleared by any task, and
        also by interrupt handlers. Tasks can wait on either state of the
        flag, and all tasks waiting for a state are simultaneously
        activated when the flag is changed to this state. This makes
        flags suitable for use as a global signalling mechanism.


                                     Counters

        Counters are a variation on the flag concept. A counter can be
        incremented and cleared by any task, and by interrupt handlers.
        Tasks can wait for a counter to be zero or nonzero. Like flags,
        all tasks waiting for the zero state are activated
        simultaneously. But unlike flags, only the first task waiting for
        the nonzero state of a counter will be activated on incrementing
        the counter, and the counter will be automatically decremented by
        one. The counter is used inside CTask to handle timer interrupts.
        The timer counter will be incremented on each timer tick,
        activating the timer task. If for any reason the timer task is
        unable to complete its run until the next tick, this tick will
        not be lost, since the counter is incremented, and the timer task
        will continue to run the next time it calls the counter wait
        request.


                               Mailboxes and Pipes

        The "mailbox" and "pipe" events can be used for inter-task
        communication, and for the communication between interrupt
        handlers and tasks.

        Mailboxes can hold an unlimited number of mail blocks. Mail
        blocks have no fixed structure, but the first doubleword in each
        block passed to a mailbox routine is used as a chain pointer.
        Mail blocks are chained into a mailbox in FIFO order. Tasks can
        wait for mail to arrive, or can conditionally read mail if a
        block is available. Tasks and interrupt handlers can write blocks
        to a mailbox. Since mailboxes don't need any copying of data,
        they are suited for high speed exchange of larger amounts of data
        between tasks. The disadvantage of sending mail this way is that
        you have to make sure that a mail block is not re-used before it
        has been read out of the box and processed by the receiving task.
        When exchanging fixed length messages, you can build a free mail
        block chain by using a mailbox to hold the available blocks.

        Buffered message exchange is possible using pipes. When creating
        a pipe, you specify a buffer area and its length, and the pipe
        routines will buffer all data written to the pipe in this area.
        This implies that writing to a pipe may cause a task to be
        delayed until there is space available in the pipe. To allow
        interrupt handlers to write to pipes, there is a conditional
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 31



        write request, which will simply return if the pipe is full.
        Tasks can wait for data to arrive in a pipe, and for the pipe to
        be emptied. A conditional read request is also provided. The
        disadvantage of pipes is that they are slightly slower than
        mailboxes due to the necessary copying, and that you can only
        place word or byte sized items in a pipe. When there is more than
        one reader or writer task, you can not rely on the bytes in a
        pipe being in any specific order. A "buffer" construct is
        provided in CTask that expands pipes to allow arbitrary length
        messages to be written and read. This is implemented using a
        resource for reading and writing to the pipe associated with the
        buffer, so the message is always guaranteed to be written and
        read in one piece. But since resources can not be used in
        interrupt handlers, using such buffers is not allowed from
        interrupts.


                            Serial and Printer Drivers

        There are a number of routines included in the CTask package for
        PC-specific tasks. Although they will be of limited use for
        embed-ded applications, studying the serial I/O and printer
        interface routines will give you some hints on how to use the
        CTask kernel for implementing your own device drivers. For PC
        based appli-cations, the routines should be usable with no or
        little changes for implementing complete communications packages.

        The serial I/O handler uses interrupts for both input and output
        of data, and supports both XON/XOFF and RTS/CTS handshake
        methods. The modem inputs can selectively be enabled to control
        data transmission. Pipes are used for transmit and receive data,
        with the buffer and its size specified on initialization. Both
        COM1 and COM2 can be active simultaneously, and other ports can
        be supported by editing a table in the source code or defining
        ports on-line. Since CTask allows the access to all events in
        interrupt handlers, writing interrupt based I/O drivers is
        relatively simple.  On receiving a character, the character and
        any associated errors are placed in the receive pipe, and the
        transmit pipe is read on transmit ready interrupt. Note that
        conditional reads and writes have to be used in the interrupt
        handler, since you can't safely delay an interrupt handler.

        The printer output driver supports both polling and interrupt
        output. Again, a pipe is used for the output characters.
        However, since polling is supported, and because of the somewhat
        unreliable interrupt structure of the printer ports, a driver
        task is required. This task is automatically created on
        installing the driver. The task first waits on the pipe for a
        character to be written to the printer.  When polling is enabled,
        it tries to output the character directly, using a short busy-
        waiting loop. So as not to load the system too heavily by the
        polling, the task will yield if it can't output the character
        after a small number of loops. When interrupts are enabled, the
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 32



        process is essentially the same at the start, but after the
        character is written to the port, the task will wait on a flag to
        be set. The interrupt handler will set the flag on interrupt,
        enabling the task to get the next character from the pipe. Since
        interrupts are unreliable with most printers due to the usually
        very short pulses on the acknowledge line, the task uses a
        timeout on the flag wait, so it does not hang if an interrupt is
        missed. Studying the printer driver will also give you an idea
        what the optional parameter on task creation can be used for. In
        the printer driver, this parameter is used to pass the address of
        the printer control block, which contains the pipe, the flag, and
        the hardware info, to the task. This allows the printer driver to
        be simultaneously installed for any number of printers without
        having to write separate printer tasks.







































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 33



                                 CTask Data Types


        Note that you do not have to know the innards of the structures.
        All structure fields are filled by the "create_xxx" routines and
        modified by the CTask functions. You should NEVER modify a field
        in one of the structures directly. The structures are explained
        here shortly only for those wanting to modify the routines.

        NOTE: When modifying CTask structures, take care to modify the
        equivalent definitions in the assembler include file "tsk.mac".
        Some of the assembler routines have to use field offsets into
        pointers, so having different offsets in C and assembler will
        crash the system.


        If you only want to use the routines, you should simply include
        the file "tsk.h" in your source, and define variables of the
        types

             tcb         - for task control blocks
             tcbptr      - for far pointers to tcbs

             flag        - for flag events
             flagptr     - for far pointers to flags

             resource    - for resource events
             resourceptr - for far pointers to resources

             counter     - for counter events
             counterptr  - for far pointers to counters

             mailbox     - for mailbox events
             mailboxptr  - for far pointers to mailboxes

             pipe        - for pipe events
             pipeptr     - for far pointers to pipes

             wpipe       - for word pipe events
             wpipeptr    - for far pointers to word pipes

             buffer      - for buffer events
             bufferptr   - for far pointers to buffers

             tlink       - for timeout and watch control blocks
             tlinkptr    - for far pointers to timeout control blocks

             namerec     - for control block names
             nameptr     - for name pointers

        without caring what's behind them.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 34



        Additionally, you may use the types

             byte         - for unsigned characters
             word         - for unsigned short integers
             dword        - for unsigned long integers

             funcptr      - for far pointers to void functions
             funcptr_void - for far pointers to void functions taking no
                            parameters
             funcptr_int  - for far pointers to void functions taking a
                            single int parameter
             funcptr_fp   - for far pointers to void functions taking a
                            single far pointer parameter
             funcptr_dword - for far pointers to void functions taking a
                            single doubleword parameter

             farptr       - for far pointers to anything
             byteptr      - for far pointers to byte arrays
             wordptr      - for far pointers to word arrays

        in defining or typecasting items to be passed as parameters to
        CTask functions.


                                Other definitions

        The following definitions are used inside CTask to avoid problems
        with Microsoft C in some memory models. The standard FP_SEG and
        FP_OFF macros will not work correctly in near data models, and
        the NULL pointer may not actually be 0 when assigned to a far
        pointer. The offsetof operator is not defined for MSC 5.1.

             TFP_SEG(ptr)       Is a macro to isolate the segment part of
                                a far pointer.

             TFP_OFF(ptr)       Is a macro to isolate the offset part of
                                a far pointer.

             TMK_FP(seg,off)    Is a macro to make a far pointer out of a
                                segment and an offset.

             LNULL              Is a far pointer to nothing.

             TSK_OFFSETOFF(struc,field)
                                Is a macro that returns the byte offset
                                of "field" within the structure type
                                "struc".

             TSK_STRUCTOP(struc,ptr,field)
                                Is a macro that returns a pointer to the
                                start of the structure of type "struc",
                                given a pointer "ptr" which points to
                                "field" within the structure.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 35



        The definition TN is used in CTask starting at version 2.1 to
        avoid using extensive #if directives for routines accepting name
        parameters. The previous way of enclosing the parameter in #if /
        #endif made the sources hard to read. The TN macro will expand to
        nothing if TSK_NAMEPAR is FALSE, and to a comma followed by the
        parameter if TSK_NAMEPAR is TRUE.

             TN(name)           Define name parameter if TSK_NAMEPAR is
                                TRUE.


        In addition, a number of definitions are provided to statically
        initialise event structures (flags, resources, etc.). Those
        definitions (DEF_xxx) are listed in the "routines" section under
        the corresponding create_xxx routine entry. You use them in place
        of a normal variable definition, i.e. to create an initialised
        flag, you would write

             static DEF_FLAG (myflag, "MyFlag");
             ...
             add_event_name (&myflag);

        instead of

             static flag myflag;
             ...
             create_flag (&myflag, "MyFlag");


                 Typedefs used for simplified type specifications

             typedef unsigned char byte;
             typedef unsigned short word;
             typedef unsigned long dword;
             typedef void (Taskfunc *funcptr)();
             typedef void (Taskfunc *funcptr_void)(void);
             typedef void (Taskfunc *funcptr_int)(int);
             typedef void (Taskfunc *funcptr_dword)(dword);
             typedef void (interrupt far *intprocptr)(void);
             typedef void far *farptr;
             typedef byte far *byteptr;
             typedef word far *wordptr;











        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 36



                   Error return values for event wait functions


             #define TTIMEOUT ((farptr) -1L)
             #define TIMEOUT  (-1)

                  -1 is returned if a timeout occurred while waiting for
                  an event.

             #define TWAKE    ((farptr) -2L)
             #define WAKE     (-2)

                  -2 is returned if the task was waked up while waiting
                  for an event.

             #define TWATCH    ((farptr) -3L)
             #define WATCH     (-3)

                  -3 is returned if the task was waked up during a wait
                  by a watchpoint or hotkey action.


                                      Queues

        The 'queue' structure is a dual link for linking task control
        blocks and timer blocks. The first three fields are used both for
        the queue head, and for elements to be inserted in a queue.

        CAUTION: Do not change the order of the first three fields in
        either queue or queue_head! Those two structures are used
        interchangeably in various places in the CTask kernel. Changing
        one of them would have catastrophic results.

        The queue element ("queue") contains the forward and backward
        pointer, a structure kind field, plus the priority (when used in
        a TCB) or the timeout value (when used in a tlink structure). The
        kind field is used to identify the type of structure the queue
        element is a part of, and also to identify the "end" of the
        queue. To simplify insertion and removal, all queues are circular
        in nature, i.e. there is no NULL-pointer at the head or tail. The
        queue head, and thus the end of a queue, is identified by a bit 7
        (Q_HEAD) being set in the kind field.

        #define Q_HEAD 0x80 /* Queue head flag */

             typedef struct {
                             word     prior;
                             word     ini_prior;
                            } qelem_pri;

             typedef struct queue_rec far *queptr;


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 37



             typedef struct queue_rec {
                                       queptr   volatile next;
                                       queptr   volatile prev;
                                       byte     kind;
                                       union  {
                                              qelem_pri   pri;
                                              dword       ticks;
                                              } el;
                                       } queue;

        The queue head ("queue_head") also contains the forward and
        backward pointer, and the structure kind field. The same
        structure is also used to chain name and timeout/watch/hotkey
        blocks, since those do not need the priority/tick field present
        in normal queue elements.

             typedef struct {
                             queptr   volatile first;
                             queptr   volatile last;
                             byte     kind;
                            } queue_head;

             typedef queue_head far *queheadptr;



                       The timer/watch/hotkey control block

        The timer control block is included in every task control block.
        It may also be created as a separate entity to specify special
        actions to be executed after or every n timer ticks, to specify
        memory or port locations to be watched for a change or a certain
        value on every timer tick, or for keyboard hotkeys.

        The "link" field links the active structures into the timer,
        watch, or hotkey queue. The kind of the element (which is
        specified by the "kind" field of "link") determines the
        appropriate queue.

        The "chain" field (present only if task groups are enabled) links
        all timer structures of a group. This allows automatic removal of
        elements on termination.

        The "next" field is exclusively used by the timer task to chain
        elements that have to be activated.








        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 38



        "strucp" points to the structure to be acted upon, "struckind"
        specifies the kind of structure:

             #define  TKIND_TASK        1

                  Strucp points to the task control block of which the
                  element is a member. The task will be awakened when the
                  timeout expires.

             #define  TKIND_WAKE        2

                  Strucp points to a task control block. Otherwise same
                  as TKIND_TASK.

             #define  TKIND_PROC        3

                  Strucp contains the address of a function to be called
                  on timeout.

             #define  TKIND_FLAG        4

                  Strucp points to a flag that should be set on timeout.

             #define  TKIND_COUNTER     5

                  Strucp points to a counter that should be increased on
                  timeout.

             #define  TKIND_COUNTDEC    6

                  Strucp points to a counter that should be decreased on
                  timeout.

        The timeout structure is used for timeouts, memory/port
        watchpoints, and hotkeys. The union "elem" contains either the
        tick reload value, the specs for the memory or port location to
        watch, or the hotkey scancode and flag values. "elkind" specifies
        the kind of structure used in the upper nibble:

             #define  TELEM_TIMER       0x10

                  This is a timeout element.

             #define  TELEM_MEM         0x20

                  This is a memory watch element.

             #define  TELEM_PORT        0x30

                  This is a port watch element.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 39



             #define  TELEM_HOTKEY      0x40

                  This is a keyboard hotkey element.


        The lower nibble of "elkind" is used for watchpoints, it
        specifies the comparison operation:

             #define  TCMP_EQ           1

                  Activate watch if value read is equal to "compare".

             #define  TCMP_NE           2

                  Activate watch if value read is not equal to "compare".

             #define  TCMP_GE           3

                  Activate watch if value read is >= "compare"
                  (unsigned).

             #define  TCMP_LE           4

                  Activate watch if value read is <= "compare"
                  (unsigned).

             #define  TCMP_GES          5

                  Activate watch if value read is >= "compare" (signed).

             #define  TCMP_LES          6

                  Activate watch if value read is <= "compare" (signed).

             #define  TCMP_CHG          7

                  Activate watch if value read is not equal to "compare".
                  Additionally, store the value read into the "compare"
                  field. Only useful for continuous watchpoints.


        For timeouts, "elem.time" contains the "reload" value used for
        repetitive timeout actions to reload the original timeout value.
        The actual timeout value is part of the link structure.

        For port watches, "elem.port" contains the values "port", "mask",
        "compare" and "in_word". "port" holds the port number to read
        from.  The value read is masked with "mask", and compared with
        "compare". A word access is used if "in_word" is nonzero.

        Memory watches are similar to port watches, with "elem.mem"
        containing "address", the memory address to watch, and "mask" and
        "compare" as above.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 40



        Keyboard hotkeys hold the three BIOS keyboard flag comparison
        values, and the keyboard scancode, in "elem.key".

        The "flags" field holds both permanent and temporary processing
        flags:

             #define  TFLAG_BUSY        0x01

                  If this bit is set, the timer task is busy processing
                  this element. It may not be deleted or de/enqueued.
                  Routines processing timer elements must not modify the
                  control block except the flag field.

             #define  TFLAG_ENQUEUE     0x02

                  The element is to be (re-)enqueued in the appropriate
                  queue after processing. This is a temporary flag, used
                  only while TFLAG_BUSY is set.

             #define  TFLAG_UNQUEUE     0x04

                  The element is to be removed from its queue after
                  processing. This is a temporary flag, used only while
                  TFLAG_BUSY is set.

             #define  TFLAG_REMOVE      0x08

                  The element is to be deallocated after processing. This
                  is a temporary flag, used only while TFLAG_BUSY is set,
                  for elements with TFLAG_TEMP set.

             #define  TFLAG_REPEAT      0x40

                  The element is a repeat element. For timeout elements,
                  the timeout count is reloaded on activation. Other
                  elements are re-enqueued without change when activated.

             #define  TFLAG_TEMP        0x80

                  If this bit is set, this is a temporary element, which
                  will be deallocated on activation or delete.


        The "user_parm" field may be used to pass pointers or other
        values to timeout functions. It is not modified by the CTask
        kernel routines.







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 41



             typedef struct tlink_rec far *tlinkptr;

             struct telem_memwatch {
                                   wordptr address;
                                   word    mask;
                                   word    compare;
                                   };

             struct telem_portwatch {
                                     word  port;
                                     word  mask;
                                     word  compare;
                                     byte  in_word;
                                    };

             struct telem_timeout {
                                   dword    reload;
                                  };

             typedef struct {
                              byte  mask;
                              byte  compare;
                            } kbflag;

             struct telem_hotkey {
                                  kbflag   flag1;
                                  kbflag   flag2;
                                  kbflag   flag3;
                                  byte     scancode;
                                 };

             struct tlink_rec {
                               queue    link;
                               tlinkptr next;
                               farptr   strucp;
                               dword    user_parm;
                               queue_head chain; (if GROUPS)
                               union {
                                     struct telem_memwatch   mem;
                                     struct telem_portwatch  port;
                                     struct telem_timeout    time;
                                     struct telem_hotkey     key;
                                     }  elem;
                               byte     elkind;
                               byte     struckind;
                               byte     flags;
                              };

             typedef struct tlink_rec tlink;




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 42



                             The name link structure

        If TSK_NAMED is enabled, all structures except the timer control
        block contain a name link. All control blocks are linked and
        named via this element.

        "strucp" points to the head of the structure the name link is an
        element of, with "kind" in the list field specifying the type of
        structure:

             #define  TYP_GROUP      0     Group control block
             #define  TYP_TCB        1     task control block
             #define  TYP_FLAG       2     flag event
             #define  TYP_RESOURCE   3     resource event
             #define  TYP_COUNTER    4     counter event
             #define  TYP_MAILBOX    5     mailbox event
             #define  TYP_PIPE       6     byte pipe
             #define  TYP_WPIPE      7     word pipe
             #define  TYP_BUFFER     8     buffer
             #define  TYP_TIMER      9     timeout element
             #define  TYP_WATCH     10     memory/port watch element
             #define  TYP_HOTKEY    11     hotkey element

        The head element of the name list (normally the group control
        block) has the Q_HEAD bit in its kind field set.

        The "name" field contains an up to 8-character name plus a zero
        terminator.

             #define  NAMELENGTH     9

             typedef struct name_rec far *nameptr;

             struct name_rec {
                             queue_head list;
                             farptr     strucp;
                             char       name [NAMELENGTH];
                             };

             typedef struct name_rec namerec;


                         The task control block structure


        The "cqueue" field links the TCB into one of the queues. The
        "qhead" pointer points to the head of the queue the task is
        enqueued in, or will be enqueued in on the next schedule request
        in the case of the current running task.

        The "prior" field in the cqueue structure contains the tasks
        current priority, with 0xffff the highest possible priority, and
        0 the lowest. The "ini_prior" field initially contains the same
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 43



        value. If variable priority is enabled, "prior" is incremented on
        each scheduler call, and reset to "ini_prior" when the task is
        activated.

        "stack" contains the saved task stack pointer (offset and
        segment) if the task is not running. The field "stkbot" contains
        the bottom address of the task stack. It is set by create_task,
        and is used by the scheduler and the snapshot dump module if
        checking is enabled to check for stack overflow and stack usage.

        The "t_ax", "t_cx", ..., "t_ds" fields hold the register contents
        while a task is inactive.

        "state" and "flags" contain the tasks state and flags.

        "timerq" is a tlink structure used to chain the tcb into the
        timer queue if the task is waiting for a timeout, into the watch
        queue if the task is waiting for a watch event, or into one of
        the hotkey queues if the task is waiting for a hotkey. See above
        for a description of the tlink structure.

        The fields "retptr" and "retsize" are used in event handling.
        They are used when a task is waiting for an event by the task
        activating the event, and also by timeout and wake to indicate
        error returns. The use of these pointers eliminates the need to
        loop for an event, which requires slightly more code in the event
        handling routines, but reduces the need for task switching.

        The "save_func" and "rest_func" pointers can optionally point to
        task-switch save and restore functions. In special applications,
        it may be necessary to save and restore global variables or other
        items when a task is deactivated. The save function is called
        when a task is deactivated, the restore function when a task is
        activated. Both functions should be defined as

           void Taskfunc funcname (tcbptr tcb);

        The functions are called with a pointer to the current TCB, DS is
        set up to point to the TCB data segment. Interrupts are enabled.
        The stack is the scheduler's local stack, so the routine must not
        use excessive local stack space. Calling CTask-routines that
        might cause the scheduler to be activated must be avoided. See
        the "Advanced Topics" chapter for more information.

        The "user_ptr" field can hold any pointer or other value to be
        used by the save/restore functions or to point to task-related
        items. This field is not modified by the CTask routines.

        The "group" and "homegroup" pointers link a task with it's
        current task group, and with the base group that created the task
        if the task spawned a secondary invocation of CTask.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 44



        The DOS-related fields "indos", "new", "base_psp", "psp_sssp",
        and "swap_area" are used to save critical information on the
        state of DOS. They should never be tampered with. The same goes
        for "sched_ent_func" which holds a function pointer to an
        internal function of the DOS module when a task is active in DOS.

        The "name" namerec structure is present only if TSK_NAMED is
        enabled. It may be used in debugging (see tsksnap.c for an
        example), and in applications where the address of the structure
        can not be passed directly.

        The "ems_map" and "ndpsave" fields hold the EMS and numeric
        coprocessor state, and are only present if the respective options
        are enabled.

             typedef struct tcb_rec far *tcbptr;

             struct tcb_rec {
                         queue          cqueue;
                         queheadptr     qhead;
                         byteptr        stkbot;
                         volatile byte  state;
                         byte           flags;

                         byteptr        stack;
                         word           t_ax;
                         word           t_cx;
                         word           t_dx;
                         word           t_si;
                         word           t_di;
                         word           t_bp;
                         word           t_es;
                         word           t_ds;

                         tlink          timerq;
                         volatile farptr retptr;
                         volatile int    retsize;

                         funcptr        save_func;
                         funcptr        rest_func;
                         farptr         user_ptr;
                         gcbptr         group; (if GROUPS)
                         gcbptr         homegroup; (if GROUPS)
                         funcptr        sched_ent_func; (if DOS)
                         volatile byte  indos; (if DOS)
                         volatile byte  new; (if DOS)
                         word           base_psp; (if DOS)
                         dword          psp_sssp; (if DOS)
                         byte           swap_area [DOSSWAPSIZE]; (if DOS)
                         namerec        name; (if TSK_NAMED)
                         byte           ems_map [EMS_SAVE_SIZE]; (if EMS)
                         ndpsave_t      ndpsave; (if NDP)
                         };
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 45



             typedef struct tcb_rec tcb;



                                   Task states


             #define  ST_KILLED   0

                  The task has been killed. Restarting the task is not
                  possible. Queue pointers are invalid.

             #define  ST_STOPPED  1

                  The task is not enqueued in any queue. To be included
                  in scheduling, it has to be explicitly started. The
                  queue head pointer is NULL.

             #define  ST_DELAYED  2

                  The task is enqueued in the timer queue only. When the
                  timer expires, it is placed in the eligible queue.  The
                  queue head pointer is NULL.

             #define  ST_WAITING  3

                  The task is waiting for an event to happen.  It can
                  also be chained into the timer queue if a timeout was
                  specified in the call.  The queue head pointer points
                  to the queue head in the event control block for the
                  event the process is waiting on.

             #define  ST_ELIGIBLE 4

                  The task is enqueued in the queue of processes eligible
                  for running. It can not be chained in the timer queue.
                  The queue head pointer points to the eligible queue.

             #define  ST_RUNNING  5

                  The task is the current running process. Although it is
                  not enqueued in any queue, the queue head pointer in
                  its control block is valid and points to the queue the
                  process will be enqueued in on the next schedule
                  request.








        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 46



        Possible state transitions and their reasons:

           stopped  -> eligible    by start_task ()

           delayed  -> killed      by kill_task ()
                    -> eligible    by timer task, or wake_task ()

           eligible -> killed      by kill_task ()
                    -> running     by scheduler

           running  -> killed      by kill_task (), or return
                    -> stopped     by delay (0)
                    -> delayed     by delay (n != 0)
                    -> eligible    by scheduler
                    -> waiting     by wait_xxx ()

           waiting  -> killed      by kill_task (), or event deletion
                    -> eligible    by event happening, timeout,
                                   or wake_task()



                                    Task flags

        System flags:

             #define  F_TEMP   0x80

                  This tcb was allocated automatically, and must be
                  free'd on task kill.

             #define  F_STTEMP 0x40

                  The tasks stack was allocated automatically, and must
                  be free'd on task kill.

             #define  F_PERM   0x20

                  This is a "permanent" system task, it may not be killed.














        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 47



        User changeable flags:

             #define  F_CRIT   0x01

                  This task may not be preempted. It will run until it
                  clears this flag, delays itself, calls the scheduler
                  explicitly, or waits for an event.

             #define  F_USES_NDP  0x02

                  This task uses the numeric coprocessor. The NDP state
                  must be saved/restored on a task switch. Do not set
                  this flag if no coprocessor is installed.


                             The Group Control Block

        Each invocation of CTask owns a group control block, gcb. This
        structure holds all information relevant to this invocation only,
        and chains all data structures created in this group.

        The "home", "level", and "branch" fields interconnect the groups
        (see the chapter on groups for more information).

        The "creator" field identifies the creating task.

        The "exit_addr", "create_psp", "save_psp", and "save_sssp" fields
        hold the information necessary to allow spawning CTask
        applications.

        The "namelist" field contains the name of the group itself, and
        links all structures created within this group.

        "main_ptr" points to the "main" task of this group, i.e. the task
        designated by a NULL tcb pointer.

        "remove" holds the last element in a chain of remove functions.
        This function is called whenever the group is uninstalled.

        The "telem_list" and "ticker_list" are the heads for the timer
        element and ticker lists. Timers and tickers are chained into
        this list to allow automatic removal on group termination.

        The "palloc" and "pfree" functions hold pointers to the
        allocation functions tsk_alloc and tsk_free. The functions are
        accessed through group-relative pointers to allow code sharing
        between invocations.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 48



             struct group_rec {
                            gcbptr         home;
                            gcbptr         level;
                            gcbptr         branch;
                            tcbptr         creator;
                            dword          exit_addr;
                            word           create_psp;
                            word           save_psp;
                            dword          save_sssp;
                            namerec        namelist;
                            tcbptr         main_ptr;
                            callchainptr   remove;
                            queue_head     telem_list;
                            queue_head     ticker_list;
             #if (TSK_DYNAMIC)
                            farptr (Globalfunc *palloc)(word);
                            farptr (Globalfunc *pfree)(farptr);
             #endif
                            };



                             The event control blocks

        All event control blocks have two optional fields:

        "name" is only present if TSK_NAMED is enabled. It is a namerec
        structure as explained above.

        "flags" is only present if TSK_DYNAMIC is enabled. It contains

             F_TEMP     If this control block was allocated
                        automatically, and must be free'd on delete.

             F_STTEMP   If the buffer for this event was allocated auto-
                        matically, and must be free'd on delete (pipes
                        and buffers only).



                               The Ticker structure

        The ticker is not an event structure in the true sense, since
        there are no operations that wait on a ticker. It is the only
        control structure linked by a single forward pointer. It contains
        this "next" pointer, a doubleword "ticks" count that is counted
        down towards zero on every hardware clock tick, and the optional
        "flags" field. It is permissible to access and modify the "ticks"
        field directly. If task groups are enabled, an additional "chain"
        field links all ticker structures of a group to allow automatic
        removal on group termination.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 49



             typedef struct ticker_rec far *tick_ptr;

             typedef struct ticker_rec {
                                        tick_ptr next;
                                        dword    ticks;
                                        queue_head chain; (if GROUPS)
                                        byte     flags; (if TSK_DYNAMIC)
                                        } ticker;



                             The Flag event structure

        Contains two queues for processes waiting on a flag state (clear
        or set), plus the flag state (0 = clear, 1 = set).

             typedef struct {
                             queue_head  wait_set;
                             queue_head  wait_clear;
                             int         state;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                             } flag;

             typedef flag far *flagptr;


                           The counter event structure

        Similar to a flag, but contains a doubleword state counter.

             typedef struct {
                             queue_head  wait_set;
                             queue_head  wait_clear;
                             dword       state;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                            } counter;

             typedef counter far *counterptr;













        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 50



                           The resource event structure

        Contains a queue for the tasks waiting for access to the
        resource, a pointer to the current owner of the resource (to
        check for illegal "release_resource" and nested request calls),
        and the resource request counter (0 = free, <> 0 = in use).

             typedef struct {
                             queue_head   waiting;
                             queue_head   owner;
                             word         count;
                             byte         flags;   (if TSK_DYNAMIC)
                             namerec      name;    (if TSK_NAMED)
                            } resource;

             typedef resource far *resourceptr;



                           The mailbox event structure

        The msgptr type is only used internally to chain mail blocks into
        the mailbox. The mailbox type contains a queue of the tasks
        waiting for mail, and a first and last pointer for the chain of
        mail blocks.

             struct msg_header {
                                struct msg_header far *next;
                               };

             typedef struct msg_header far *msgptr;
             typedef mailbox far *mailboxptr;

             typedef struct {
                             queue_head  waiting;
                             msgptr      mail_first;
                             msgptr      mail_last;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                            } mailbox;



                      The pipe and word pipe event structure

        Contains queues of the tasks waiting to read or write to the
        pipe, indices for reading (outptr) and writing (inptr) into the
        buffer, the buffer size, the number of bytes or words currently
        in the pipe ("filled"), and the pointer to the buffer. A word
        pipe is handled exactly the same as a byte pipe, the only
        difference being the element size placed in the buffer. With
        normal pipes, characters are buffered, with word pipes, words.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 51



             typedef struct {
                             queue_head  wait_read;
                             queue_head  wait_write;
                             queue_head  wait_clear;
                             word        bufsize;
                             word        filled;
                             word        inptr;
                             word        outptr;
                             byteptr     contents;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                            } pipe;

             typedef pipe far *pipeptr;

             typedef struct {
                             queue_head  wait_read;
                             queue_head  wait_write;
                             queue_head  wait_clear;
                             word        bufsize;
                             word        filled;
                             word        inptr;
                             word        outptr;
                             wordptr     wcontents;
                             byte        flags;   (if TSK_DYNAMIC)
                             namerec     name;    (if TSK_NAMED)
                            } wpipe;

             typedef wpipe far *wpipeptr;


                            The buffer event structure

        Contains resources for read and write access, the word pipe used
        for buffering, and a message counter.

             typedef struct {
                              resource   buf_write;
                              resource   buf_read;
                              wpipe      pip;
                              word       msgcnt;
                              byte       flags;   (if TSK_DYNAMIC)
                              namerec    name;    (if TSK_NAMED)
                             } buffer;

             typedef buffer far *bufferptr;







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 52



                      The call chain structure

        The call chain structure is used to link "remove" functions into
        a chain. This chain is processed when a task group, or the CTask
        kernel, is removed. It contains a single forward link, and a
        pointer to the remove function. It also contains a user defined
        value that can be used by the called remove function.

             typedef struct callchain_rec far *challchainptr;

             typedef void (Taskfunc *funcptr_ccp)(callchainptr);

             typedef struct callchain_rec
                                    {
                                    callchainptr next;
                                    funcptr_ccp  func;
                                    farptr       user_ptr;
                                    byte         flags; (if TSK_DYNAMIC)
                                    } callchain;


































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 53



                                  CTask Routines

                                 Global Variables


        int ctask_active

             Contains 1 if CTask was installed, 0 before the call to
             install_tasker and after the call to remove_tasker.


        int tsk_use_ndp

             Is set to 1 by install_tasker if the NDP configuration
             option is TRUE and a numeric coprocessor is installed. This
             variable is used by create_task to determine whether to set
             the F_USES_NDP task flag. If tsk_use_ndp is nonzero during
             the call to create_task, the flag is set, causing the NDP
             state to be saved and restored for this task. You can change
             this variable to 0 before calling create_task to avoid this.
             You can also turn on or off the flag individually with
             tsk_set_flag, but it is usually safer to use the
             tsk_uses_ndp variable. Setting the F_USES_NDP flag through
             tsk_set_flag when no coprocessor is present may hang the
             system.


                             Installation and Removal

        int install_tasker (int varpri, int speedup,
                            word flags, byteptr name);


             Installs the multitasker. Must be called prior to any other
             routine except for secondary kernels. The calling routine is
             defined as the main task, and assigned the highest priority.
             To allow other tasks to execute, the main task must have its
             priority reduced, be delayed, or wait on an event.

             Returns 1 if CTask was already present in the system, i.e.
             this is a secondary invocation. Returns 0 if this is the
             first installation of CTask.

             "varpri"  Enables variable priority if nonzero.









        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 54



             "speedup" is defined for the IBM PC/XT/AT as the clock tick
                       speedup factor. The timer tick frequency will be
                       set to 

                       speedup  ticks/sec   msecs/tick
                          0        18.2        54.9   (normal clock)
                          1        36.4        27.5
                          2        72.8        13.7
                          3       145.6         6.9
                          4       291.3         3.4

                       Note that all timeouts are specified in tick
                       units, so changing the speedup parameter will
                       influence timeouts and delays. You can enable
                       CLOCK_MSEC in tskconf.h to allow timeouts to be
                       specified in milliseconds. The system clock will
                       not be disturbed by changing the speed. Using
                       values above 2 can lead to interrupt overruns on
                       slower machines and is not recommended.

             "flags"   controls various installation flags through the
                       bitwise OR of the following flags defined in
                       TSK.H:

               IFL_VIDEO      Install INT 10 access resource if set. No
                           protection of Video interrupt if clear.
                           Installation of the Video resource is safer,
                           but may slow down the system noticeably. It is
                           not necessary if you don't do screen-I/O
                           through the BIOS from your CTask program.

               IFL_DISK        Install INT 13 access resource if set. No
                           protection of Disk interrupt if clear.
                           Installation of INT 13 is recommended for
                           better system safety. The resource will allow
                           parallel access to floppy and harddisk, but
                           might be incompatible with some special
                           programs (though none have yet been reported).

               IFL_INT8_DIR Call original INT 8 directly if set.
                           This changes the timing for the timer inter-
                           rupt. If this flag is clear, the original
                           timer interrupt is chained to through a task,
                           so it can be preempted. If it is set, the
                           original interrupt is chained to directly, at
                           the start of timer interrupt processing. This
                           avoids compatibility problems with certain
                           TSR's and Networks, but may impair CTask
                           operations while those TSR's are active.




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 55



               IFL_PRINTER  Install INT 17 handler if set.
                           Installation of the printer interrupt handler
                           avoids lengthy busy waiting on printer output,
                           but might be incompatible with certain printer
                           redirectors.

               IFL_INT15      Install IBM-AT INT 15 handler if set.
                           The IBM INT 15 handler allows avoiding some
                           busy waiting loops. It may, however, be
                           incompatible with some non-100% clones, and
                           with debuggers like Periscope IV. If you're
                           not sure, don't set this flag.

               IFL_NODOSVARS
                           Do not copy the internal DOS variable area if
                           set. This flag may be used for incompatible
                           versions of DOS or it's clones, but background
                           DOS access will not work if this flag is set.
                           Use only for known incompatible versions, and
                           only if you do not intend to TSR or Spawn.

               IFL_NOEXITCHECK
                           Don't check for premature exit if set. This
                           flag may be set to disable the standard check
                           for program exit without proper CTask
                           termination. It may be useful in conjunction
                           with MS Windows programs using CTask, since
                           the Windows logic may fool the normal exit
                           check.

             "name"     is the name of the created task group.


        void  remove_tasker (void);

             Uninstalls the multitasker. Must only be called from the
             main task, and should be called before exiting the program.


        int ctask_resident (void);

             This routine allows checking if another copy of CTask is
             already resident. It must be called before install_tasker is
             invoked.

             Returns 1 if CTask is resident, 0 otherwise. It always
             returns 1 after install_tasker has been called.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 56



        int link_ctask (void);

             This routine checks if another copy of CTask is resident,
             and verifies that the resident copy has a routine stub table
             to allow code sharing. It must be called before
             install_tasker is invoked.

             Returns 1 if a code-sharing copy of CTask is resident, 0
             otherwise. It always returns 1 after install_tasker has been
             called.


                               Searching for names


        farptr find_name (byteptr name, int kind);

             This routine searches for a task, group, or event structure
             from the current task's group downward to the base group.

             Returns a pointer to the structure, or a pointer to the name
             record within the structure (depending on kind) if the name
             was found, LNULL otherwise.

             This routine may be called before "install_tasker" has been
             invoked to search names in resident copies.

             "name"     pointer to a zero-terminated, up to eight
                        character, name. Case is significant in names.

             "kind"     is the kind of structure to search for:

                        If -1, all structures are searched, and the first
                        structure with the given name is returned. In
                        this case, the returned pointer points to the
                        name record within the structure, to allow
                        identification of the structure. The "strucp"
                        pointer within that record points to the start of
                        the structure, the "kind" field in the link
                        structure identifies the type of the structure.

                        If kind is >= 0, the returned pointer is a
                        pointer to the start of the structure:

                          TYP_GROUP      - Search for Groups only
                          TYP_FLAG       - Search for Flags only
                          TYP_RESOURCE   - Search for Resources only
                          TYP_COUNTER    - Search for Counters only
                          TYP_MAILBOX    - Search for Mailboxes only
                          TYP_PIPE       - Search for Pipes only
                          TYP_WPIPE      - Search for Word Pipes only
                          TYP_BUFFER     - Search for Buffers only

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 57



        farptr find_group_name (gcbptr group, byteptr name, int kind);

             Looks for a name in the specified group only.

             Return value and parameters match those of find_group_name,
             except

             "group"    pointer to a group control block.



                                   Adding names


        void  add_event_name (nameptr elem);

             Task and event names are normally linked into the name chain
             automatically on creation. Statically initialised event
             blocks (events defined with DEF_xxx macros) do not need the
             create_xxx call, but you have to call add_event_name to link
             the structure into the name chain.

             "elem"     is a pointer to the "name" field in the event
                        control block.

             Example:

                  void init_my_flag (void)
                  {
                       static DEF_FLAG(my_flag, "MyFlag");

                       add_event_name (&my_flag.name);
                  }



                                  Remove Functions


        callchainptr chain_removefunc (funcptr_ccp func,
                                       callchainptr chain,
                                       farptr user_ptr);

             Chain a "remove" routine. The remove routine chain is called
             whenever the group or CTask is removed. It may be used for
             clean-up work, for example to un-install interrupt handlers.
             The function enters the routine address passed as parameter
             into the call chain control block, and chains the block into
             the remove chain. If dynamic allocation is enabled, the
             chain pointer may be LNULL.

             The routine returns the chain pointer, or LNULL if the block
             could not be allocated.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 58



             Installation example:

                  callchain remchain;

                  chain_removefunc (my_remove_func, &remchain, NULL);

             The remove routine should have the following form:

                  void Taskfunc my_remove_func (callchainptr chain)
                  {
                       ... /* cleanup */
                  }

             For more information, refer to the "Advanced Topics" chapter.


        void  unchain_removefunc (callchainptr chain);

             Unchain a remove routine from the remove chain.



                            Preemption and Scheduling


        void  preempt_off (void);

             Disables task preemption. This is the default after instal-
             lation. With preemption turned off, only delays, event
             waits, and explicit scheduler calls will cause a task
             switch.


        void  preempt_on (void);

             Enables task preemption. Task switches will occur on timer
             ticks.


        void  tsk_dis_preempt (void)

             Temporarily disable task preemption. Preemption will be re-
             enabled by tsk_ena_preempt or an unconditional scheduler
             call.


        void  tsk_ena_preempt (void)

             Re-enable task preemption. Note that tsk_dis_preempt and
             tsk_ena_preempt do not change the global preemption state
             set by preempt_off and preempt_on.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 59



        void  schedule (void);

             Explicit scheduling request. The highest priority eligible
             task will be made running.


        void  c_schedule (void);

             Conditional scheduling request. Scheduling will take place
             only if preemption is allowed.


        void  yield (void);

             Explicit scheduling request, with task priority temporarily
             set to zero. If a task has to wait for some external event
             in a polling loop, this call may be used to allow tasks of
             lower priority to execute.


        The following entry points may be used from assembler routines:

        extrn _tsk_scheduler: far

             Direct entry into the scheduler. The stack must be set up as
             for an interrupt handler, e.g.

                  pushf
                  cli
                  call  _tsk_scheduler


        extrn _sched_int: far

             Conditional scheduling call. The stack must be set up as for
             an interrupt handler. This entry should be used by interrupt
             handlers to cause a reschedule. Interrupt handlers should
             not use _tsk_schedule.



                                  Miscellaneous


        int tsk_dis_int (void)

             Disable interrupts. Returns the state of the interrupt flag
             prior to this call (1 if interrupts were enabled).





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 60



        void  tsk_ena_int (int state)

             Enables interrupts if "state" is nonzero. Normally used in
             conjunction with tsk_dis_int.


        The routines tsk_dis_int and tsk_ena_int may be used in a simpli-
        fied  scheme with the defines

             CRITICAL;      Declares "int crit_intsav;".
             C_ENTER;       Expands to "crit_intsav = tsk_dis_int ();"
             C_LEAVE;       Expands to "tsk_ena_int (crit_intsav);".


        void  tsk_cli (void)

             Disables interrupts (intrinsic function).


        void  tsk_sti (void)

             Unconditionally enables interrupts (intrinsic function).


        void  tsk_outp (int port, byte b)

             Outputs the value "b" to hardware-port "port" (intrinsic
             function).


        byte  tsk_inp (int port)

             Returns the value read from port "port" (intrinsic
             function).



















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 61



                                 Task Operations


        tcbptr create_task (tcbptr task, funcptr func, byteptr stack,
                            word stksz, word prior, farptr arg
                            [, byteptr name]);

             Initialises a task. Must be called prior to any other opera-
             tions on this task. The task is in the stopped state after
             creation. It must be started to be able to run. If the NDP
             option is enabled, the F_USES_NDP flag is set in the tcb
             when the NDP is installed and the global variable
             tsk_use_ndp is nonzero.

             Returns a pointer to the created tcb, or LNULL on error.

             "task"     is a pointer to a tcb (LNULL for automatic allo-
                        cation).

             "func"     is a pointer to a void far function, with a
                        single dword sized parameter.

             "stack"    is a pointer to a stack area for the task (LNULL
                        for automatic allocation).

             "stksz"    is the size of the stack area in bytes.

             "prior"    is the tasks priority (0 lowest, 0xffff highest).

             "arg"      is an argument to the created task. It may be
                        used to differentiate between tasks when using
                        the same function in different tasks.

             "name"     is the name of the task, up to eight characters,
                        plus zero-terminator. This parameter is defined
                        only if TSK_NAMEPAR is enabled in tskconf.h.


        void  kill_task (tcbptr task);

             Kills a task. The task can no longer be used.


        int start_task (tcbptr task);

             Starts a task, i.e. makes it eligible for running.

             Returns 0 if task was started, -1 if the task was not
             stopped. A value of LNULL for "task" will start the "main
             task".



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 62



        int stop_task (tcbptr task);

             Stops a task, i.e. removes it from all queues. A value of
             LNULL for "task" will stop the "main task".

             Returns 0 on success.


        int wake_task (tcbptr task);

             Prematurely wakes a delayed or waiting task. If the task was
             waiting for an event, it will be removed from the waiting
             queue, with the operation terminating with an error return
             value.

             Returns 0 if task was waked, -1 if the task was not delayed
             or waiting. A value of LNULL for "task" will wake the "main
             task".


        void  set_priority (tcbptr task, word prior)

             Sets the priority of the specified task to "prior". Note
             that you should NOT modify the priority field in the tcb
             structure directly. A value of LNULL for "task" will set the
             priority of the "main task".


        word  get_priority (tcbptr task)

             Returns the initial priority of the specified task. A value
             of LNULL for "task" will get the priority of the "main
             task".


        void  set_task_flags (tcbptr task, byte flags)

             Sets the flags of the task to "flags". The only flags that
             can be changed are

                  F_CRIT         the task can not be preempted if set
                  F_USES_NDP     the task uses the numeric coprocessor

             Note that you may NOT modify the flag field in the tcb
             structure directly. A value of LNULL for "task" will set the
             flags of the "main task".







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 63



        void  set_funcs (tcbptr task, funcptr save, funcptr rest);

             Sets the save and restore functions for the specified task.
             The save function is called whenever the task is deacti-
             vated, the restore function is called whenever the task is
             scheduled. This allows saving of critical system states upon
             a task switch. Both functions are called with a far call,
             the pointer to the task control block is passed as
             parameter. A value of LNULL for "task" will set the
             functions of the "main task". To deactivate one or both
             functions, pass LNULL as function parameter.
             See the "Advanced Topics" chapter for more information.


        farptr set_user_ptr (tcbptr task, farptr uptr);

             Sets the user pointer in the specified TCB, and returns it's
             previous value. The user pointer may be used to point to
             memory blocks local to a task, or to hold other task-
             specific values. It is never accessed or modified by the
             CTask kernel. A value of LNULL for "task" will set the user
             pointer of the "main task".


        farptr get_user_ptr (tcbptr task);

             Returns the user pointer of the specified TCB. A value of
             LNULL for "task" will get the user pointer of the "main
             task".


        tcbptr curr_task (void);

             Returns the pointer to the TCB of the currently running
             task.



                                 Timer Operations


        Timeouts are normally specified in timer ticks. If CLOCK_MSEC is
        enabled, timeouts will be converted to the nearest number of
        timer ticks automatically.


        word  ticks_per_sec (void);

             Returns a rough estimate of the number of ticks per second
             even if CLOCK_MSEC is not enabled.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 64



                               Event wait Timeouts

        When  waiting for an event, a timeout may be specified. The ope-
        ration will terminate with an error return value if the timeout
        is reached before the event occurs. NOTE that the timeout para-
        meter is not optional. To specify no timeout, use the value 0L.


                                    "Tickers"

        It sometimes is desirable to measure timing intervals or global
        timeouts without creating special tasks, or while waiting for
        external events in polling loops. A low overhead way of doing
        this  is the "ticker" structure. When this structure is linked
        into  the ticker chain, the doubleword "ticks" field is decre-
        mented on every timer tick (in the timer interrupt itself), until
        it reaches zero.


        tick_ptr create_ticker (tick_ptr elem, dword val);

             Links a ticker element into the ticker chain. The ticks
             field is initialized to "val", and will be decremented to
             zero. If the elem pointer is LNULL, a new ticker element
             will be created.

             Returns the ticker element pointer, LNULL on error.


        void  delete_ticker (tick_ptr elem);

             Unlinks a ticker element from the ticker chain. Countdown
             will stop. If the element was allocated dynamically, it will
             be deleted.


        void  set_ticker (tick_ptr elem, dword val);

             Sets the ticks field to the given value. If the ticks field
             is modified directly instead of through this routine,
             interrupts should be disabled when writing a doubleword
             value.


        dword get_ticker (tick_ptr elem)

             Returns the current ticker value. If the ticks field is read
             directly instead of through this routine, interrupts should
             be disabled when reading the doubleword value.




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 65



                                      Delays


        int t_delay (dword ticks);

             Delay the current task for "ticks" clock ticks/milliseconds.
             If ticks is 0, the task is stopped.

             Returns TIMEOUT if the delay expired, WAKE if the task was
             activated by wake_task.



                     Timed Events, Watch Events, and Hotkeys

        You can create timer control blocks, memory/port watch blocks,
        and keyboard hotkey blocks, to

             - set a flag
             - increment or decrement a counter
             - wake up a task
             - call a function

        after a specified timeout interval, or when a certain condition
        is met. The operation may optionally be repeated.

        Watch control blocks are checked on every timer tick. They allow
        memory locations and I/O ports to be checked for a certain value,
        or for a change in value. When the specified condition is met,
        the given action is executed.

        Keyboard hotkeys are checked in the keyboard hardware interrupt.
        They  allow checking for key scan codes and/or keyboard state flag
        combinations.

        See the "Advanced Topics" chapter on restrictions placed on
        functions called by timer/watch/hotkey conditions.
















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 66



        tlinkptr create_timer_elem (tlinkptr elem, dword tout,
                                    farptr strucp, byte kind,
                                    byte rept [,dword userpar]);

             Creates a timer control block, but does not activate it.

             Returns the address of the control block, LNULL on error.

             "elem"     is the control block to initialise (LNULL for
                        automatic allocation).

             "tout"     specifies the timeout interval.

             "strucp"   points to the structure to be used. This is a
                        flagptr for setting a flag, a counterptr for
                        in/decreasing counters, a tcbptr for waking a
                        task, or a funcptr for calling a function.

             "kind"     gives the kind of structure "strucp" points to.
                        It must be one of

                           TKIND_WAKE     for task-wakeup
                           TKIND_PROC     for function call
                           TKIND_FLAG     for flag set
                           TKIND_COUNTER  for counter increment.
                           TKIND_COUNTDEC for counter decrement.

             "rept"     if nonzero, the action will be repeated on every
                        "tout" timeout interval.

             "userpar"  is a doubleword value that can be used by the
                        timeout function if kind is TKIND_PROC. This
                        parameter is optional.

             NOTE: Timer control blocks can not be named.


        tlinkptr create_timer (tlinkptr elem, dword tout, farptr strucp,
                               byte kind, byte rept [,dword userpar]);

             Creates a timer control block and activates it.

             Returns the address of the control block, LNULL on error.

             See create_timer_elem above for parameters. If the timeout
             is zero, the control block is initialized, but is not
             entered into the timer chain. The timeout must be changed
             with change_timer for the timer control block to be
             activated.




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 67



        void  enable_timer (tlinkptr elem);

             Activates a timeout element. This call is ignored if the
             timeout value in the control block is zero.


        void  disable_timer (tlinkptr elem);

             Disables a timeout element. The element is not deleted.


        void  change_timer (tlinkptr elem, dword tout, byte rept);

             Changes the timeout value and/or the repeat flag for an
             existing timer control block. If "tout" is zero, the call
             has the same effect as disable_timer.


        void  delete_timer (tlinkptr elem);

             Deletes a timer control block, and removes it from the
             timeout queue.


        tlinkptr create_memory_watch_elem (tlinkptr elem, farptr address,
                                           word mask, word compare,
                                           byte cmpkind, farptr strucp,
                                           byte kind, byte rept
                                           [, dword userpar]);

             Creates a memory watch control block. Memory watches compare
             a byte or word value at the specified address against a
             comparison value. The value loaded is always a word, the
             "mask" parameter may be used to restrict comparison to a
             byte. The watch is not activated.

             Returns the watch control block pointer, or LNULL on error.

             "elem"     is the control block to initialise (LNULL for
                        automatic allocation).

             "address"  is a pointer to the memory location to watch.

             "mask"     is a bitmask to mask out irrelevant bits before
                        comparison.

             "compare"  is the value the memory contents are to be
                        compared with.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 68



             "cmpkind"  is the kind of comparison to be used:

                        TCMP_EQ   (*address & mask) == compare
                        TCMP_NE   (*address & mask) != compare
                        TCMP_GE   (*address & mask) >= compare (unsigned)
                        TCMP_LE   (*address & mask) <= compare (unsigned)
                        TCMP_GES  (*address & mask) >= compare (signed)
                        TCMP_LES  (*address & mask) <= compare (signed)

                        TCMP_CHG  Change in value:
                                  (*address & mask) != compare
                                  compare = *address & mask

             "strucp"   points to the structure to be used. This is a
                        flagptr for setting a flag, a counterptr for
                        in/decreasing counters, a tcbptr for waking a
                        task, or a funcptr for calling a function.

             "kind"     gives the kind of structure "strucp" points to.
                        It must be one of

                            TKIND_WAKE     for task-wakeup
                            TKIND_PROC     for function call
                            TKIND_FLAG     for flag set
                            TKIND_COUNTER  for counter increment.
                            TKIND_COUNTDEC for counter decrement.

             "rept"     if nonzero, the action will be repeated whenever
                        the condition is met.

             "userpar"  is a doubleword value that is passed to the watch
                        function if kind is TKIND_PROC. This parameter is
                        optional.

             NOTE: Watch control blocks can not be named.


        tlinkptr create_memory_watch (tlinkptr elem, farptr address,
                                      word mask, word compare,
                                      byte cmpkind, farptr strucp,
                                      byte kind, byte rept
                                      [, dword userpar]);

             Creates a memory watch control block and activates it.

             Returns the watch control block pointer, or LNULL on error.

             See create_memory_watch_elem for parameters.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 69



        int wait_memory (farptr address,
                         word mask, word compare, byte cmpkind)

             Delays the current task until the specified condition is
             met. Parameters are the same as in create_memory_watch. No
             timeout can be specified.

             Returns WATCH if the watch condition was met, WAKE if the
             task was activated by wake_task.


        tlinkptr create_port_watch_elem (tlinkptr elem,
                                         word port, byte in_word,
                                         word mask, word compare,
                                         byte cmpkind, farptr strucp,
                                         byte kind, byte rept
                                         [, dword userpar]);

             Creates a port watch control block. Port watches compare a
             byte or word value read from the specified port address
             against a comparison value. The value read is either a word
             or a byte, depending on the "in_word" parameter. The watch
             is not activated.

             Returns the watch control block pointer, or LNULL on error.

             "elem"     is the control block to initialise (LNULL for
                        automatic allocation).

             "port"     is the port address to read.

             "in_word"  Specifies whether a word or byte input
                        instruction is to be used. If zero, a byte is
                        input, if nonzero, a word is read from the port.

             "mask"     is a bitmask to mask out irrelevant bits before
                        comparison.

             "compare"  is the value the port contents are to be compared
                        with.













        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 70



             "cmpkind"  is the kind of comparison to be used:

                        TCMP_EQ   (in(port) & mask) == compare
                        TCMP_NE   (in(port) & mask) != compare
                        TCMP_GE   (in(port) & mask) >= compare (unsigned)
                        TCMP_LE   (in(port) & mask) <= compare (unsigned)
                        TCMP_GES  (in(port) & mask) >= compare (signed)
                        TCMP_LES  (in(port) & mask) <= compare (signed)

                        TCMP_CHG  Change in value:
                                  (in(port) & mask) != compare
                                  compare = in(port) & mask
                                  (NOTE: The port is read only once.)

             "strucp"   points to the structure to be used. This is a
                        flagptr for setting a flag, a counterptr for
                        in/decreasing counters, a tcbptr for waking a
                        task, or a funcptr for calling a function.

             "kind"     gives the kind of structure "strucp" points to.
                        It must be one of

                            TKIND_WAKE     for task-wakeup
                            TKIND_PROC     for function call
                            TKIND_FLAG     for flag set
                            TKIND_COUNTER  for counter increment.
                            TKIND_COUNTDEC for counter decrement.

             "rept"     if nonzero, the action will be repeated whenever
                        the condition is met.

             "userpar"  is a doubleword value that is passed to the watch
                        function if kind is TKIND_PROC. This parameter is
                        optional.

             NOTE: Watch control blocks can not be named.


        tlinkptr create_port_watch (tlinkptr elem,
                                    word port, byte in_word,
                                    word mask, word compare,
                                    byte cmpkind, farptr strucp,
                                    byte kind, byte rept
                                    [, dword userpar]);

             Creates a port watch control block and activates it.

             Returns the watch control block pointer, or LNULL on error.

             See create_port_watch_elem for parameters.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 71



        int wait_port (word port, byte in_word,
                       word mask, word compare, byte cmpkind)

             Delays the current task until the specified condition is
             met. Parameters are the same as in create_port_watch. No
             timeout can be specified.

             Returns WATCH if the watch condition was met, WAKE if the
             task was activated by wake_task.


        void  enable_watch (tlinkptr elem);

             The specified watch element is activated.


        void  disable_watch (tlinkptr elem);

             The specified watch element is deactivated. The element is
             not deleted.


        void  delete_watch (tlinkptr elem);

             The specified watch element is removed.


        NOTE: delete_timer, delete_watch, and change_timer should not be
        used  on automatically allocated timer/watch control blocks. Since
        such  blocks are deallocated once the timeout expires or the
        condition is met (except for repeat operations), the validity of
        the pointer is not guaranteed.


        tlinkptr create_hotkey_elem (tlinkptr elem,
                                     byte scancode,
                                     byte mask1, byte flag1,
                                     byte mask2, byte flag2,
                                     byte mask3, byte flag3,
                                     farptr strucp, byte kind,
                                     byte rept
                                     [, dword userpar]);

             Creates a keyboard hotkey control block. Keyboard hotkeys
             compare the scancode and/or the BIOS keyboard flags against
             the given values. The flag fields are masked before
             comparing. The hotkey is not activated.

             The file "kbd.h" contains definitions for scan codes and
             flag byte values.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 72



             Returns the hotkey control block pointer, or LNULL on error.

             CAUTION: In contrast to the timer/watch creation functions,
                      this function does not accept a LNULL parameter for
                      the element to create. Dynamic allocation can not
                      be used in an interrupt handler, and a temporary
                      element would have to be released in the keyboard
                      interrupt. Therefore, the hotkey control block must
                      always be static.

             "elem"     is the control block to initialise. This pointer
                        must NOT be LNULL.

             "scancode" is the keyboard scancode to look for. If scancode
                        is 0, only the flag values are compared.

             "flag1..3" are the values the BIOS keyboard flags are to be
                        compared with.

             "mask1..3" are bitmasks to mask out irrelevant bits before
                        comparing the flag values. Set both mask and flag
                        to 0 to disable comparison.

             "strucp"   points to the structure to be used. This is a
                        flagptr for setting a flag, a counterptr for
                        in/decreasing counters, a tcbptr for waking a
                        task, or a funcptr for calling a function.

             "kind"     gives the kind of structure "strucp" points to.
                        It must be one of

                            TKIND_WAKE     for task-wakeup
                            TKIND_PROC     for function call
                            TKIND_FLAG     for flag set
                            TKIND_COUNTER  for counter increment.
                            TKIND_COUNTDEC for counter decrement.

             "rept"     if nonzero, the action will be repeated whenever
                        the hotkey is activated.

             "userpar"  is a doubleword value that is passed to the
                        hotkey function if kind is TKIND_PROC. This
                        parameter is optional.

             NOTE: Hotkey control blocks can not be named.








        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 73



        tlinkptr create_hotkey_entry (tlinkptr elem,
                                      byte scancode,
                                      byte mask1, byte flag1,
                                      byte mask2, byte flag2,
                                      byte mask3, byte flag3,
                                      farptr strucp, byte kind,
                                      byte rept
                                      [, dword userpar]);

             Creates a keyboard hotkey control block and enables it.

             Returns the hotkey control block pointer, or LNULL on error.

             See create_hotkey_elem for parameters.


        int wait_hotkey (byte scancode,
                         byte mask1, byte flag1,
                         byte mask2, byte flag2,
                         byte mask3, byte flag3)

             Delays the current task until the specified hotkey is hit.
             Parameters are the same as in create_hotkey_entry. No
             timeout can be specified.

             Returns WATCH if the hotkey was hit, WAKE if the task was
             activated by wake_task.


        void  enable_hotkey (tlinkptr elem);

             The specified hotkey element is activated.


        void  disable_hotkey (tlinkptr elem);

             The specified hotkey element is deactivated. The element is
             not deleted.


        void  delete_hotkey (tlinkptr elem);

             The specified hotkey entry is removed.










        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 74



                                 Event Operations

                                    Resources

        A Resource is either in use or free, the default state is free.
        If a  task has requested a resource, its state is in use, and the
        requesting task is said to "own" the resource.  Tasks requesting
        a resource while it is in use will be made waiting. If the
        resource is released, the highest priority waiting task is made
        eligible, and is assigned the resource. Interrupt handlers may
        not use resource functions other than "check_resource".

        To facilitate use of resources in nested routines, CTask allows a
        resource to be requested by a Task already owning it. Different
        calls may be used to request resources, depending on how such
        nested calls should be handled. The standard request_resource and
        c_request_resource calls just mark the resource as in use by
        setting the owner count to 1, and the first nested routine that
        releases the resource will cause the resource to be freed. The
        request_cresource and c_request_cresource calls increment the
        owner count, so the resource will only be freed upon a matching
        count of requests and releases.


        resourceptr create_resource (resourceptr rsc [, byteptr name]);

             This initialises a resource. Must be used prior to any other
             operations on a resource.

             Returns the address of the control block, LNULL on error.

             "rsc"      is the resource control block (LNULL for
                        automatic allocation).

             "name"     is the name of the resource, up to eight
                        characters, plus zero-terminator. This parameter
                        is defined only if TSK_NAMEPAR is enabled in
                        tskconf.h.















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 75



        DEF_RESOURCE(var,name)

             This macro defines and initialises a resource control block
             at compile time. It can replace the run-time call to
             create_resource. However, the created block is not linked
             into the name chain. To make the block visible, you must use
             add_event_name. Most compilers will not allow aggregate
             initialisers of automatic variables, so you must use this
             definition with the static attribute inside routines.

             "var"      is the variable name to define.

             "name"     is the name of the resource. It can be a zero
                        length string, but it must not be LNULL. Since
                        this is a macro, you must give the parameter even
                        when TSK_NAMEPAR is disabled.


        void  delete_resource (resourceptr rsc);

             Calling this routine is optional. It will kill all tasks
             waiting for the resource.


        void  release_resource (resourceptr rsc);

             Decrement the owner count, and release the resource if it is
             zero. If the task does not own the resource, the call is
             ignored. If the resource is released, and tasks are waiting
             for access, the highest priority task will gain access to
             the resource.


        int request_resource (resourceptr rsc, dword timeout);

             Requests the resource. If it is not available, the task is
             suspended. A timeout may be specified.

             Returns 0 if resource was allocated, TIMEOUT if a timeout
             occurred, WAKE on wake.

             This call is ignored (returns a 0) if the calling task
             already owns the resource.










        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 76



        int request_cresource (resourceptr rsc, dword timeout);

             Requests the resource. If it is not available, the task is
             suspended. A timeout may be specified.

             Returns 0 if resource was allocated, TIMEOUT if a timeout
             occurred, WAKE on wake.

             This call increments the owner count, and returns 0, if the
             calling task already owns the resource.


        int c_request_resource (resourceptr rsc);

             Requests the resource only if it is available.

             Returns 0 if resource was allocated, -1 if unavailable.


        int check_resource (resourceptr rsc);

             Returns 0 if resource is allocated, 1 if free.



                                      Flags


        A Flag can be either on or off, the default state is off (0).
        Tasks can wait on either state of the flag. If the state is
        changed, all tasks waiting for the state are made eligible.
        Interrupt handlers may use the "set_flag", "clear_flag", and
        "check_flag" functions.


        flagptr create_flag (flagptr flg [, byteptr name]);

             This initialises a flag. Must be used prior to any other
             operations on a flag. The state is set to 0.

             Returns the address of the control block, LNULL on error.

             "flg"      is the flag control block (LNULL for automatic
                        allocation).

             "name"     is the name of the flag, up to eight characters,
                        plus zero-terminator. This parameter is defined
                        only if TSK_NAMEPAR is enabled in tskconf.h.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 77



        DEF_FLAG(var,name)

             This macro defines and initialises a flag control block at
             compile time. It can replace the run-time call to
             create_flag. However, the created block is not linked into
             the name chain. To make the block visible, you must use
             add_event_name. Most compilers will not allow aggregate
             initialisers of automatic variables, so you must use this
             definition with the static attribute inside routines.

             "var"      is the variable name to define.

             "name"     is the name of the flag. It can be a zero length
                        string, but it must not be LNULL. Since this is a
                        macro, you must give the parameter even when
                        TSK_NAMEPAR is disabled.


        void  delete_flag (flagptr flg);

             Calling this routine is optional. It will kill all tasks
             waiting for the flag.


        void  set_flag (flagptr flg);

             This sets the flag. All tasks waiting for the set state will
             be made eligible for running.


        void  clear_flag (flagptr flg);

             This clears the flag. All tasks waiting for the clear state
             will be made eligible for running.


        int wait_flag_set (flagptr flg, dword timeout);

             Waits for the set state of the flag. If the flag is not set,
             the task is suspended. A timeout may be specified.

             Returns 0 if the flag was set, TIMEOUT on timeout, WAKE on
             wake.


        int wait_flag_clear (flagptr flg, dword timeout);

             Waits for the clear state of the flag. If the flag is not
             clear, the task is suspended. A timeout may be specified.

             Returns 0 if the flag was cleared, TIMEOUT on timeout, WAKE
             on wake.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 78



        int clear_flag_wait_set (flagptr flg, dword timeout)

             Combines the operations clear_flag and wait_flag_set.

             Returns 0 if the flag was set, TIMEOUT on timeout, WAKE on
             wake.


        int check_flag (flagptr flg);

             Returns 0 if flag clear, 1 if set.



                                     Counters

        A Counter can have any value from 0L to 0xffffffffL, the default
        value is 0. Tasks can wait for a counter being zero or non-zero.
        If the counter is cleared or decremented to zero, all tasks wai-
        ting  for the zero condition are made eligible. If the counter is
        incremented, the highest priority task waiting for non-zero is
        made  eligible, and the counter is decremented by one. Interrupt
        handlers may use the "clear_counter", "inc_counter",
        "dec_counter", "set_counter", and "check_counter" functions.


        counterptr create_counter (counterptr cnt [, byteptr name]);

             This initialises a counter. Must be used prior to any other
             operations on a flag. The value is set to 0.

             Returns the address of the control block, LNULL on error.

             "cnt"      is the counter control block (LNULL for automatic
                        allocation).

             "name"     is the name of the counter, up to eight
                        characters, plus zero-terminator. This parameter
                        is defined only if TSK_NAMEPAR is enabled in
                        tskconf.h.













        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 79



        DEF_COUNTER(var,name)

             This macro defines and initialises a counter control block
             at compile time. It can replace the run-time call to
             create_counter. However, the created block is not linked
             into the name chain. To make the block visible, you must use
             add_event_name. Most compilers will not allow aggregate
             initialisers of automatic variables, so you must use this
             definition with the static attribute inside routines.

             "var"      is the variable name to define.

             "name"     is the name of the counter. It can be a zero
                        length string, but it must not be LNULL. Since
                        this is a macro, you must give the parameter even
                        when TSK_NAMEPAR is disabled.


        void  delete_counter (counterptr cnt);

             Calling this routine is optional. It will kill all tasks
             waiting for the counter.


        void  clear_counter (counterptr cnt);

             Clears the counter to zero. All tasks waiting for the zero
             state will be made eligible for running.


        int wait_counter_set (counterptr cnt, dword timeout);

             Waits for the counter having a nonzero value. If the value
             is zero, the task is suspended. The value is decremented
             when the task gets access to the counter.  A timeout may be
             specified.

             Returns 0 if the counter was nonzero, TIMEOUT on timeout,
             WAKE on wake.


        int wait_counter_clear (counterptr cnt, dword timeout);

             Waits for the counter having a zero value. If the value is
             nonzero, the task is suspended. A timeout may be specified.

             Returns 0 if the counter was zero, TIMEOUT on timeout, WAKE
             on wake.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 80



        dword inc_counter (counterptr cnt);

             Increments the counter. If tasks are waiting for the nonzero
             state, the highest priority task is given access to the
             counter.

             Returns the new value of the counter.


        dword dec_counter (counterptr cnt);

             Decrements the counter unless it is already zero. If the
             counter is decremented to zero, all tasks waiting for the
             zero state are made eligible.

             Returns the new value of the counter.


        void  set_counter (counterptr cnt, dword val);

             Sets the counter to the given value. If "val" is nonzero,
             and tasks are waiting for the set state, the highest
             priority tasks are made eligible, and "val" is decremented,
             until either "val" reaches zero, or there are no more tasks
             waiting. If val is, or is counted down to, zero, all tasks
             waiting for the zero state are made eligible.


        dword check_counter (counterptr cnt);

             Returns the current value of the counter.



                                    Mailboxes

        A Mailbox can hold any number of mail blocks. Tasks can send mail
        to a  mailbox and wait for mail to arrive. A mail block is
        assigned to the highest priority waiting task. Care must be
        exercised not to re-use a mail block until it has been processed
        by the receiving task. The mail block format is user defineable,
        with  the first doubleword in a block reserved for the tasking
        system. Interrupt handlers may use the "send_mail",
        "c_wait_mail", and "check_mailbox" functions.

        Note  that mailboxes are well suited to provide the mechanism for
        managing a chain of (equally sized) free mail blocks. On
        initialization, all free blocks would be "sent" to the manager
        box.  Requesting a free block would use "wait_mail", and freeing a
        used  block would again "send" it to the manager mailbox.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 81



        mailboxptr create_mailbox (mailboxptr box [, byteptr name]);

             This initialises a mailbox. Must be used prior to any other
             operations on a mailbox.

             Returns the address of the control block, LNULL on error.

             "box"      is the mailbox control block (LNULL for automatic
                        allocation).

             "name"     is the name of the mailbox, up to eight
                        characters, plus zero-terminator. This parameter
                        is defined only if TSK_NAMEPAR is enabled in
                        tskconf.h.


        DEF_MAILBOX(var,name)

             This macro defines and initialises a mailbox control block
             at compile time. It can replace the run-time call to
             create_mailbox. However, the created block is not linked
             into the name chain. To make the block visible, you must use
             add_event_name. Most compilers will not allow aggregate
             initialisers of automatic variables, so you must use this
             definition with the static attribute inside routines.

             "var"      is the variable name to define.

             "name"     is the name of the mailbox. It can be a zero
                        length string, but it must not be LNULL. Since
                        this is a macro, you must give the parameter even
                        when TSK_NAMEPAR is disabled.


        void  delete_mailbox (mailboxptr box);

             Calling this routine is optional. It will kill all tasks
             waiting for mail.


        void  send_mail (mailboxptr box, farptr msg);

             Sends a message to the specified mailbox. If tasks are
             waiting for mail, the highest priority task will get it.


        farptr wait_mail (mailboxptr box, dword timeout);

             Waits for mail. If no mail is available, the task is
             suspended. A timeout may be specified.

             Returns the pointer to the received mail block, TTIMEOUT on
             timeout, TWAKE on wake.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 82



        farptr c_wait_mail (mailboxptr box);

             Reads mail only if mail is available.

             Returns LNULL if there is no mail, else a pointer to the
             received message.


        int check_mailbox (mailboxptr box);

             Returns 0 if mailbox is empty, 1 otherwise.



                                      Pipes

        A Pipe has a buffer to hold character or word sized items. An
        item  may be written to a pipe if there is space in the buffer.
        Otherwise, the writing task will be made waiting. A reading task
        will  be made waiting if the buffer is empty. If an item has been
        read, the highest priority task waiting to write to the pipe will
        be allowed to write. Interrupt handlers may only use pipe
        functions "check_pipe", "c_write_pipe", and "c_read_pipe".

        Note  that the values -1 and -2 (0xffff and 0xfffe) should be
        avoided when writing to word pipes. These values are used to mark
        timeout and wake when reading, or pipe empty when checking a word
        pipe, and thus may lead to erroneous operation of your routines.


        pipeptr create_pipe (pipeptr pip, farptr buf, word bufsize
                             [, byteptr name]);
        wpipeptr create_wpipe (wpipeptr pip, farptr buf, word bufsize
                               [, byteptr name]);

             This initialises a pipe. Must be used prior to any other
             operations on a pipe. "bufsize" specifies the buffer size in
             bytes. With word pipes, the buffer size should be divisible
             by two.

             Returns the address of the control block, LNULL on error.

             "pip"      is the pipe/wpipe control block (LNULL for
                        automatic allocation).

             "buf"      is a pointer to the pipe buffer.

             "bufsize"  is the size of the buffer in bytes.

             "name"     is the name of the pipe, up to eight characters,
                        plus zero-terminator. This parameter is defined
                        only if TSK_NAMEPAR is enabled in tskconf.h.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 83



        DEF_PIPE(var,name,buf,bufsize)
        DEF_WPIPE(var,name,buf,bufsize)

             This macro defines and initialises a pipe/word pipe control
             block at compile time. It can replace the run-time call to
             create_pipe/create_wpipe. However, the created block is not
             linked into the name chain. To make the block visible, you
             must use add_event_name. Most compilers will not allow
             aggregate initialisers of automatic variables, so you must
             use this definition with the static attribute inside
             routines.

             "var"      is the variable name to define.

             "name"     is the name of the pipe. It can be a zero length
                        string, but it must not be LNULL. Since this is a
                        macro, you must give the parameter even when
                        TSK_NAMEPAR is disabled.

             "buf"      is a pointer to the pipe buffer.

             "bufsize"  is the size of the buffer in bytes.


        void  delete_pipe (pipeptr pip);
        void  delete_wpipe (wpipeptr pip);

             Calling this routine is optional. It will kill all tasks
             waiting to read or write messages.


        int read_pipe (pipeptr pip, dword timeout);
        word  read_wpipe (wpipeptr pip, dword timeout);

             Read an item from a pipe. If no item is available, the task
             is suspended. A timeout may be specified.

             Returns the item, or TIMEOUT on timeout, WAKE on wake.


        int c_read_pipe (pipeptr pip);
        word  c_read_wpipe (wpipeptr pip);

             Reads an item from a pipe only if one is available.

             Returns the received item, or -1 if none is available.







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 84



        int write_pipe (pipeptr pip, byte ch, dword timeout);
        int write_wpipe (wpipeptr pip, word ch, dword timeout);

             Writes an item to a pipe. If the buffer is full, the task is
             suspended. A timeout may be specified. If tasks are waiting
             to read, the item will be assigned to the highest priority
             waiting task.

             Returns 0 on success, or TIMEOUT on timeout, WAKE on wake.


        int c_write_pipe (pipeptr pip, byte ch);
        int c_write_wpipe (wpipeptr pip, word ch);

             Writes an item to a pipe only if enough space is available.

             Returns 0 on success, or -1 if no space available.


        int wait_pipe_empty (pipeptr pip, dword timeout);
        int wait_wpipe_empty (wpipeptr pip, dword timeout);

             Waits for the pipe to be emptied. If the pipe is already
             empty on entry, the task continues to run.

             Returns 0 on empty, TIMEOUT on timeout, WAKE on wake.


        int check_pipe (pipeptr pip);
        word  check_wpipe (pipeptr pip);

             Returns -1 if the pipe is empty, else the first item in the
             pipe. The item is not removed from the pipe.


        word  pipe_free (pipeptr pip);
        word  wpipe_free (wpipeptr pip);

             Returns the number of free items available in the pipe.


        void  flush_pipe (pipeptr pip)
        void  flush_wpipe (wpipeptr pip)

             Clears the pipe. Tasks waiting for the empty state are made
             eligible.







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 85



                                     Buffers


        A Buffer has a buffer to hold message strings. A message may be
        written to a buffer if it fits into the buffer. Otherwise, the
        writing task will be made waiting. A reading task will be made
        waiting if the buffer is empty. If a message has been read, the
        highest priority task waiting to write to the buffer will be
        allowed to write if its message fits into the available space.
        Interrupt handlers may not use buffer functions other than
        "check_buffer".

        The buffer routines are implemented using resources and pipes,
        and thus are not part of the true "kernel" routines. There is no
        static creation macro for buffers.


        bufferptr create_buffer (bufferptr buf, farptr pbuf, word bufsize
                                 [, byteptr name]);

             This initialises a buffer. Must be used prior to any other
             operations on a buffer.

             The minimum buffer size is the length of the longest
             expected message plus two.

             Returns the address of the control block, LNULL on error.

             "buf"      is the buffer control block (LNULL for automatic
                        allocation).

             "pbuf"     is a pointer to the buffer.

             "bufsize"  is the size of the buffer in bytes.

             "name"     is the name of the buffer, up to eight
                        characters, plus zero-terminator. This parameter
                        is defined only if TSK_NAMEPAR is enabled in
                        tskconf.h.


        void  delete_buffer (bufferptr buf);

             Calling this routine is optional. It will kill all tasks
             waiting to read or write messages.








        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 86



        int read_buffer (bufferptr buf, farptr msg, int size,
                         dword timeout);

             Read a message from a buffer. If no message is available,
             the task is suspended. A timeout may be specified.

             The message will be copied to the buffer "buf", with a
             maximum length of "size" bytes.

             Returns the length of the received message, TIMEOUT on
             timeout, WAKE on wake.


        int c_read_buffer (bufferptr buf, farptr msg, int size);

             Reads a message from a buffer only if one is available.

             Returns the length of the received message, or -1 if none is
             available.


        int write_buffer (bufferptr buf, farptr msg, int size,
                          dword timeout);

             Writes a message from "msg" with length "size" to a buffer.
             If not enough space for the message is available, the task
             is suspended. A timeout may be specified. If tasks are
             waiting for messages, the highest priority task will get it.

             Returns the length of the message, TIMEOUT on timeout, WAKE
             on wake, -3 on error (length < 0 or length > buffer size).


        int c_write_buffer (bufferptr buf, farptr msg, int size);

             Writes a message to a buffer only if enough space is
             available.

             Returns the length of the message, -1 if no space available,
             or -3 on error (length < 0 or length > buffer size).


        word  check_buffer (bufferptr buf);

             Returns the current number of bytes (not messages) in the
             buffer, including the length words.







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 87



                               The Keyboard Handler


        word  t_read_key (void)

             Waits for a key to be entered. Returns the ASCII-code in the
             lower byte, and the scan-code in the upper byte, or WAKE
             (0xfffe) on wake.


        word  t_wait_key (dword timeout)

             Waits for a key to be entered. Returns the ASCII-code in the
             lower byte, and the scan-code in the upper byte, or TIMEOUT
             (0xffff) on timeout, WAKE (0xfffe) on wake.


        word  t_keyhit (void)

             Returns -1 (0xffff) if no key was entered, else the value of
             the key. The key is not removed.



                              The Serial I/O handler

        The serial I/O handler provides full duplex interrupt driven I/O
        on the serial ports. Support for COM1 and COM2 is included,
        adding other ports is possible by changing the source and/or
        defining ports on-line.


        int v24_define_port (int base, byte irq, byte vector)

             Defines a new COM-port. This routine can only be used if
             TSK_DYNAMIC is enabled.

             "base"     is the port base I/O address.

             "irq"      is the IRQ-line number (0-7 for XT, 0-15 for AT)
                        the port uses for interrupts.

             "vector"   is the interrupt vector number (0-0xff).

             The return value is the internal port number for use with
             v24_install. -1 is returned on error (memory full).







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 88



        sioptr v24_install (int port, int init,
                            farptr rcvbuf, word rcvsize,
                            farptr xmitbuf, word xmitsize);

             Installs the handler for the specified port. Currently,
             ports 0 (COM1) and 1 (COM2) are supported by default. Both
             ports may be used simultaneously, the buffer areas for the
             ports must not be shared.

             "rcvbuf"   is a word pipe buffer area for received
                        characters. May be LNULL for automatic allocation.

             "rcvsize"  specifies the receive buffer size in bytes. Note
                        that the buffer will hold rcvsize / 2 received
                        characters.

             "xmitbuf"  is a byte pipe buffer for characters waiting for
                        transmission. May be LNULL for automatic
                        allocation.

             "xmitsize" gives the transmit buffer size in bytes.

             "port"     Port number to install (0: COM1, 1: COM2).

                        If the port number is ORed with 0x80, the port is
                        *relative*. This means that the entry in the BIOS
                        table for COM-Ports is used to search the tables
                        internal to the driver for the port information,
                        instead of using the table entry directly. If the
                        port address cannot be found, the driver returns
                        with an error code. Note that ports are numbered
                        from 0, so to specify relative COM1, pass 0x80 as
                        parameter.

             "init"     if non-zero, the port is initialised with the
                        default values specified in the source. If the
                        parameter is zero, the control registers and baud
                        rates on entry are not modified.

             The return value is a pointer to the sio control block for
             use with the other driver routines. LNULL is returned on
             error (invalid port number, bad buffer sizes, nonexistent
             hardware, out of memory).










        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 89



        void  v24_remove (sioptr sio, int restore);

             Removes the driver for the specified control block. Should
             be called for all ports installed before exiting the
             program.

             If the "restore" parameter is nonzero, the control registers
             and the baud rate that were set before installation of the
             driver are restored. If the parameter is zero, the values
             are not changed.


        void  v24_remove_all (void)

             Removes all installed serial i/o drivers. This routine is
             automatically called on remove_tasker if drivers were
             installed. Note that you can not specify a restore
             parameter, the default restore parameter is used (constant
             in tsksio.c).


        void  v24_change_rts (sioptr sio, int on);

             Changes the state of the RTS output line. A nonzero value
             for "on" will turn the output on.


        void  v24_change_dtr (sioptr sio, int on);

             Changes the state of the DTR output line. A nonzero value
             for "on" will turn the output on.


        void  v24_change_baud (sioptr sio, long rate);

             Changes the baud rate. The following baud rates are suppor-
             ted:

                50,    75,   110,   134,   150,   300,   600,
              1200,  1800,  2000,  2400,  3600,  4800,  7200,  9600,
             19200, 38400.

             Note that baud rates above 9600 may cause problems on slow
             machines.









        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 90



        void  v24_change_parity (sioptr sio, int par);

             Changes parity. The parameter must be one of the following
             values defined in "sio.h":

                  PAR_NONE  no parity checks
                  PAR_EVEN  even parity
                  PAR_ODD   odd parity
                  PAR_MARK  mark parity
                  PAR_SPACE space parity


        void  v24_change_wordlength (sioptr sio, int len);

             Changes word length. Values 5, 6, 7, 8 may be given.


        void  v24_change_stopbits (sioptr sio, int n);

             Changes Stopbits. Values 1 and 2 are allowed.


        void  v24_watch_modem (sioptr sio, byte flags);

             Watches the modem status lines to control transmission.

             "flags"    Specifies the input lines that must be active to
                        allow transmission. Transmission will stop if one
                        of the lines goes inactive. The parameter may be
                        combined from the following values defined in
                        "sio.h":

                        CTS  to watch clear to send
                        DSR  to watch data set ready
                        RI   to watch ring indicator
                        CD   to watch carrier detect

             A value of zero (the default) will allow transmission
             regardless of modem status.














        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 91



        void  v24_protocol (sioptr sio, int prot,
                           word offthresh, word onthresh);

             Sets the handshake protocol to use.

             "prot"     specifies the protocol. This parameter may be
                        combined from the following values:

                        XONXOFF   to enable XON/XOFF (DC1/DC3) handshake
                        RTSCTS    to enable RTS/CTS handshake

             "offthresh" specifies the minimum number of free items in
                        the receive buffer. If this threshold is reached,
                        an XOFF is transmitted and/or the RTS line is
                        inactivated.

             "onthresh" specifies the minimum number of items that must
                        be free before XON is transmitted and/or the RTS
                        line is re-activated.

             Enabling XONXOFF will remove all XON and XOFF characters
             from the input stream. Transmission will be disabled when
             XOFF is received, and re-enabled when XON is received.

             Enabling RTSCTS will stop transmission when the CTS modem
             input line is inactive.


        int v24_send (sioptr sio, byte ch, dword timeout);

             Transmits the character "ch". A timeout may be specified.

             Returns TIMEOUT on timeout, WAKE on wake, else 0.


        int v24_receive (sioptr sio, dword timeout);

             Waits for a received character. A timeout may be specified.

             Returns TIMEOUT on timeout, WAKE on wake, else the character
             in the lower byte, plus an error code in the upper byte. The
             error code is the combination of

                  0x02      overrun error
                  0x04      parity error
                  0x08      framing error
                  0x10      break interrupt.


        int v24_check (sioptr sio);

             Returns -1 if no receive character is available, else the
             next character from the pipe. The character is not removed.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 92



        int v24_overrun (sioptr sio);

             Checks for receive pipe overrun. Returns 1 if an overrun
             occurred, 0 otherwise. Clears the overrun flag.


        int v24_modem_status (sioptr sio);

             Returns the current modem status word. The CTS, DSR, RI, and
             CD defines may be used to extract the modem input line
             status.


        int v24_complete (sioptr sio);

             Returns 1 if all characters in the transmit pipe have been
             sent, else 0.


        int v24_wait_complete (sioptr sio, dword timeout);

             Waits for the transmit pipe to be empty. Returns TIMEOUT on
             timeout, WAKE on wake, else 0.


        void  v24_flush_receive (sioptr sio);

             Flushes the receive pipe.


        void  v24_flush_transmit (sioptr sio)

             Flushes the transmit pipe. Tasks waiting for transmit
             completion are made eligible.



















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 93



                            The Printer Output Driver


        The printer output driver provides for buffered output to up to
        three printer ports (more can be added by editing the source).
        Interrupt or polling may be selected. Due to the usual hardware
        implementation of printers and the printer interface, using
        polling is recommended. When using interrupts, you should not
        simultaneously install both port 0 and port 1 with interrupt
        enabled, since both ports share the same interrupt line.


        int prt_install (int port, byte polling, word prior,
                         farptr xmitbuf, word xmitsize);

             Installs the printer driver for the specified port. Ports 0
             (LPT1), 1 (LPT2), and 2 (LPT3) are supported.

             "port"     The output port to use.

                        If the port number is ORed with 0x80, the port is
                        relative. This means that the entry in the BIOS
                        table for LPT-Ports is used to search the tables
                        internal to the driver for the port information,
                        instead of using the table entry directly. If the
                        port address cannot be found, the driver returns
                        with an error code. Note that ports are numbered
                        from 0, so to specify LPT1, pass 0x80 as
                        parameter.

             "polling"  specifies polling output when nonzero, interrupt
                        output when zero.

             "prior"    sets the priority of the printer output task.

             "xmitbuf"  is a buffer area for the printer output buffer.
                        May be LNULL for automatic allocation.

             "xmitsize" specifies the output buffer size in bytes.

             The return value is the internal port number for use with
             the other driver routines. -1 is returned on error (invalid
             port number, bad buffer sizes, nonexistent hardware).


        void  prt_remove (int port);

             Removes the printer driver for the specified port.





        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 94



        void  prt_remove_all (void)

             Removes all installed printer ports. This routine is
             automatically called on remove_tasker if ports were
             installed.


        void  prt_change_control (int port, byte control);

             Changes the printer control output lines of the port. The
             value for "control" may be combined from the following
             values defined in "prt.h":

                  AUTOFEED  will enable printer auto feed if set
                  INIT      will initialise (prime) the printer if clear
                  SELECT    will select the printer if set


        int prt_write (int port, byte ch, dword timeout);

             Write a byte to the printer. A timeout may be given.

             Returns 0 on success, TIMEOUT on timeout, WAKE on wake.


        int prt_status (int port);

             Returns the current printer status lines, combined from the
             values

                  BUSY      Printer is busy when 0
                  ACK       Acknowledge (pulsed 0)
                  PEND      Paper End detected when 0
                  SELIN     Printer is selected (on line) when 1
                  ERROR     Printer error when 0


        int prt_complete (int port);

             Returns 1 if the printer buffer has been completely
             transmitted, 0 otherwise.


        int prt_wait_complete (int port, dword timeout);

             Waits for printer output to complete.

             Returns 0 on success, else TIMEOUT on timeout, WAKE on wake.

        void  prt_flush (int port)

             Flushes the output pipe of the printer. Tasks waiting for
             print completion are made eligible.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 95



                            Support Modules

                            Memory Allocation Interface


        The file tskalloc.c contains routines that interface CTask to the
        standard C memory allocation routines. Since the CTask kernel is
        model independent, it can not use the runtime routines directly.
        Also, to avoid crashes, CTask routines allocating memory must use
        a resource to channel access to the memory allocator, since the
        standard routines are not reentrant. All memory allocation in
        tasks should use the CTask allocation functions instead of the
        standard ones. See the chapter on memory allocation for more
        information.

        farptr tsk_alloc (word size);

             Replacement function for the standard malloc.


        farptr tsk_calloc (word item, word size);

             Replacement function for the standard calloc.


        farptr tsk_free (farptr item);

             Replacement function for the standard free. This routine
             always returns LNULL.


        farptr tsk_realloc (farptr item, word size);

             Replacement function for the standard realloc.


        Global variables:

             resource alloc_resource;

                  Is the memory allocation routine access resource. If
                  you use other allocator routines, or want to allocate
                  several items in a row, you may enclose the calls to
                  the standard C functions in calls to request_resource
                  (&alloc_resource) and free_resource (&alloc_resource).








        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 96



                            Printf Replacements


        Version 2.1 adds several functions that can (at least in most
        cases) replace the standard C printf family functions. Apart from
        being a lot faster and smaller, the routines do not assume
        DS==SS, are reentrant and completely self-contained, and thus can
        be used independent of the memory model in use. They use no CTask
        kernel functions, and could also be used in non-CTask
        applications, for example in Assembler modules, or device
        drivers/DLLs for DOS and Windows. The routines support direct
        access to the secondary screen in a dual monitor system.


        int tsk_sprintf (farptr str, farptr fmt, ...);
        int tsk_vsprintf (farptr str, farptr fmt, farptr arg);

             Print to string. Replacement for sprintf and vsprintf.
             Returns number of character written, not counting the
             terminating zero character.


        void  tsk_rprintf (farptr fmt, ...);
        void  tsk_vrprintf (farptr fmt, farptr arg);

             Output directly to screen regen hardware buffer. Allows
             printing to the secondary monitor in dual-screen systems,
             and is extremely fast.


        void  tsk_printf (farptr fmt, ...);
        void  tsk_vprintf (farptr fmt, farptr arg);

             Print to console. Uses INT 10 calls, so it's faster than
             standard printf, but can't be redirected.


        void  tsk_fprintf (int handle, farptr fmt, ...);
        void  tsk_vfprintf (int handle, farptr fmt, farptr arg);

             Print to file. Note that this is no direct replacement for
             fprintf/vfprintf, since the parameter is a DOS file handle,
             not a FILE *. Use with files opened through the low-level
             open functions, or use the standard fileno() function to get
             the handle of a stream file. Stream files should be flushed
             before use if other C functions were used to write to the
             file.


        void  tsk_putc (char c);

             Put character to screen using INT 10.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 97



        void  tsk_puts (farptr str);

             Put string to screen using INT 10. A new line is started
             after output.


        void  tsk_rputc (char c);

             Put character directly to screen hardware regen buffer.


        void  tsk_rputs (farptr str);

             Put string directly to screen hardware regen buffer. A new
             line is started after output.


        word  tsk_set_dualdis (void);

             Initialize the hardware regen output to go to the secondary
             monitor. Returns the regen buffer address, or 0 if no
             secondary adapter was found.


        word  tsk_set_currdis (void);

             Initialize the hardware regen output to go to the primary
             monitor. Returns the regen buffer address, or 0 on error.


        void  tsk_set_colour (int rows, int cols);

             Initialize the hardware regen output to go to the colour
             monitor with the given number of screen rows and columns.


        void  tsk_set_mono (int rows, int cols);

             Initialize the hardware regen output to go to the monochrome
             monitor with the given number of screen rows and columns.













        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 98



        void  tsk_set_regen (int regenseg, int port, int rows, int cols);

             Initialize the hardware regen output to go to the specified
             monitor address. You have to specify

                  regenseg  The segment address of the regen buffer.

                  port      The 6845 display controller port. If zero,
                            you can still write to the screen, but the
                            cursor will not be moved.

                  rows      The number of rows on screen.

                  cols      The number of columns on screen.

             Note that you can use this function to restrict output to
             a smaller part of the screen by increasing the segment
             address and decreasing the number of rows.


        void  tsk_setpos (int row, int col);

             Set the cursor position for hardware output. Row and column are
             numbered starting at 0.


        void  tsk_set_attr (int attr);

             Set the screen display attribute byte for subsequent hardware
             output to "attr".


        Global variables:

             dword tsk_regen;
             word tsk_regen_o;
             word tsk_regen_s;

                  Contain the current hardware screen pointer.
                  tsk_regen_o contains the current offset, tsk_regen_s
                  the regen buffer segment. tsk_regen is a synonym for
                  doubleword access to both variables.

             word tsk_disport;

                  The hardware 6845 controller port address. If set to 0,
                  the display cursor will not be updated.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -             Page 99



                            Snapshot Dump


        The snapshot dump module TSKSNAP.C provides a display of the
        current state of tasks and control structures. This display is
        rather extensive, and can easily exceed screen capacity. It may
        be useful to change the routines to suit your needs by omitting
        some  of the information, or displaying other than the standard
        info.

        Since display of the snapshot runs at high priority, the system
        will  slow down noticeably if snapshots are output with high
        frequency.

        The standard routines provided are

        void  screensnap (int rows);

             Output to hardware screen regen buffer. The hardware screen
             must have been initialised with a call to the
             tsk_set_dualdis or similar functions (see description of
             printf replacements). If the "rows" parameter is nonzero,
             the display will be truncated at the given number of rows.

        void  csnapshot (void);

             Output to console using INT 10.

        void  snapshot (FILE *f);

             Output to the given stream file.






















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 100



                                 Advanced Topics

                          Primary and Secondary Kernels

        Version 2.0 officially introduced support for CTask programs
        going TSR and spawning. Version 2.1 adds some features to make
        this  safer (especially in EMS systems), and to save code in
        secondary applications.

        The manual often refers to the terms "primary" and "secondary"
        kernel. The primary kernel is the first installation of CTask.
        This  kernel installs all basic interrupt handlers, the DOS and
        keyboard support, and the system tasks (timer, killer). It basi-
        cally is nothing else than a normal, stand-alone CTask
        installation.

        A secondary kernel is installed by a CTask program run "on top"
        of the primary. This, naturally, is only possible if the primary
        program has gone resident (TSR), or has spawned another program
        (for  example COMMAND.COM). A secondary kernel automatically de-
        tects that a primary copy of CTask is already installed, and does
        not attempt to re-install the interrupt handlers and system
        tasks. Instead, it uses a pointer to the global variable block in
        the primary to access all global CTask data. This results in both
        CTask copies cooperating such that all events, tasks, and other
        structures, are common to both invocations, and share all global
        resources. The names of control structures are visible accross
        the copies, so that a secondary can access control blocks of the
        primary, and vice versa.

        There is a separate control structure, the "group control block",
        for every invocation (or "task group"). This block links all con-
        trol  structures created by tasks inside the group together, so
        that  the system can remove those tasks and events from the system
        that  belong to the secondary, should the secondary terminate
        without cleaning up properly. The group control block additio-
        nally contains pointers to data structures and routines that can
        not be shared (like the memory allocation routines). The group
        control block is a static structure that is initialised when you
        call  install_tasker.

        This  primary/secondary structure can be completely invisible if
        you run CTask programs that could also run as standalone CTask
        applications. But the automatic data sharing also makes it
        possible to create multi-level programs, which use a resident
        part  to handle hardware interrupts (for example a com port) in
        the background, and an independently loadable program (which
        might even be a MS Windows program or driver) to control the
        resident part. If the controlling (secondary) program does not
        itself use multitasking features (i.e. create tasks), there is no
        need  for it to include a full-fledged CTask kernel with all the
        features, and no need to create a task group. But even if it
        creates tasks, but will never use the full CTask features if
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 101



        there is no background kernel, it will not need to include the
        code  for the basic (primary) interrupt handlers and tasks.

        CTask 2.1 includes several options for cooperating CTask appli-
        cations to save code in a secondary program. With all these
        options, the generated program will not be able to use CTask if
        there is no primary kernel installed.

        The first option is to use the "stskmain" object created by
        compiling tskmain.c with SECONDARY defined. With this define, the
        install_tasker and remove_tasker routines will only reference the
        second-level group creation routines. All references to the
        primary task installation routines, which in turn reference the
        interrupt handlers and system tasks, are eliminated.
        Install_tasker returns an error code if there is no primary
        kernel installed, but all other aspects of CTask will work as
        usual. A task group is created.

        The second option is to not call install_tasker at all in the
        secondary. You need not link either tskmain or stskmain. Calling
        "ctask_resident" will establish the data link. This link enables
        CTask to work without a task group, such that everything you do
        in the secondary appears as if it were executed in the primary
        kernel. This, however, means that you should not create any CTask
        control structures in the secondary (or at least you should not
        allow them to be linked into the name chain). If the secondary
        terminates without removing all control structures and tasks it
        created, the pointers chained into the primary links will point
        to some other program loaded later, which may be destroyed if any
        action causes those pointers to be referenced. You also may not
        use dynamic allocation in the secondary, since this would try to
        allocate memory in the primary applications data space.

        The third option is to use code sharing with the "stskmain"
        object. Code sharing requires the primary kernel to be compiled
        with  the CODE_SHARING and LOAD_DS configuration options set to
        TRUE. With Microsoft C, setting those options in tskconf.h is
        sufficient. With Turbo C, which does not have the "_loadds"
        keyword, the primary must be compiled in Huge memory model, and
        the TC_HUGE option must be TRUE. The reason for this is that the
        routines can now be called from an application with completely
        different segment setup. If a routine in the primary kernel is
        called from a secondary, the data segment register will point to
        the secondary's data segment. The offsets to CTask structures in
        the primary code will point to some other data in the secondary.
        So all routines that could be accessed from the outside must set
        up the data segment register to point to the primary data.

        Code  sharing uses a "stub table" and an "entry table" for a
        primitive form of run-time linking. The entry table simply
        contains the addresses of all global routines present in the
        primary in fixed order. The stub table contains short "stub"
        routines that access the entry table through the global variable
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 102



        pointer, and jump to the address corresponding to the called stub
        routine. Both tables are generated from one source,
        "tskstub.asm". You must first decide which routines should be
        included in the primary, and edit the stub definitions in this
        file  accordingly. The file is then assembled twice. The copy to
        be included with the primary is assembled with GEN_JTAB defined
        (this is automatically done by the standard makefile). The stub
        table copy for the secondary is assembled without this define.
        Install_tasker returns an error code if there is no primary
        kernel installed, but all other aspects of CTask will work as
        usual. The link_ctask routine can be used before calling
        install_tasker to verify that the primary kernel is installed and
        has code sharing enabled. A task group is created. The primary
        kernel will be slightly larger due to the additional code
        required to load the data segment on function entry, but the
        secondary will need to link only those CTask routines that are
        not defined as entry stubs.

        The fourth option is to use code sharing with no call to
        install_tasker. This requires nearly zero code in the secondary,
        but the same restrictions mentioned with the second option apply.


        There is one restriction on cooperating applications, whether
        they  use code sharing or not: The control structures for both
        primary and secondary must be identical. This requires that the
        following configuration options are identical on compilation of
        both  kernels:

           TSK_DYNAMIC
           TSK_NAMED
           EMS
           NDP
           HOTKEYS

           IBM, DOS, GROUPS (must be TRUE for groups to work at all)

        If you change those options, the sizes of the global structures,
        and the location of some fields within them, change, making it
        impossible to share structures. Linking two kernels with
        different configurations will not work.

        You may, however, change all other configurations. It is
        perfectly legal to compile the primary in large model, and the
        secondary in small (NEAR_CODE set to TRUE), even if you are using
        code  sharing. The secondary does not have to set the CODE_SHARING
        option, this option is only required in the primary.






        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 103



        Secondary application link examples (Microsoft C Large model):

          Option 1: link myprog+stskmain,,,ctaskms+ctsupmsl/NOE
          Option 2: link myprog,,,ctaskms+ctsupmsl
          Option 3: link myprog+stskmain+tskstub,,,ctaskms+ctsupmsl/NOE
          Option 4: link myprog+tskstub,,,ctaskms+ctsupmsl/NOE

        Note  that the "tskstub" object linked with options 3 and 4 is the
        one assembled without the GEN_JTAB define. It is not the
        tskstub.obj created by the standard makefile.

        The /NOE switch is required for the Microsoft linker, since the
        entry points in stskmain and tskstub duplicate entries in the
        standard CTask library.


                              TSR, Spawning, and EMS

        If you are writing a CTask application that should stay resident
        or spawn DOS, you will be hard pressed to reduce the space
        required to a minimum. One option to consider is replacing the
        standard startup code. This code calls a number of routines to
        setup parameters and the environment copy, and requests a lot of
        memory, that most likely will never be used by your program. The
        source for the startup code is included with MS and Turbo C.

        Another space saver is the included printf replacement. If you
        don't need the floating point output, tsk_printf and its cousins
        give  you all the capabilities you'll normally need at greatly
        reduced space (if you need printf at all in your TSR).

        In general, memory allocation is not needed in a TSR or spawning
        program, since you can't allocate once you are resident.
        Ommitting the memory allocation routines saves another chunk of
        code. The TSK_DYNLOAD define may be set to FALSE to prevent
        reference to the memory allocator routines from the CTask kernel
        even  when TSK_DYNAMIC is TRUE to support secondary kernels.
        Again, you may have to change the C startup code to prevent it
        from  calling routines that allocate memory.

        The final option is putting some of your code and/or data in EMS
        memory. CTask 2.1 switches EMS on a task basis, and saves the EMS
        configuration when a task is created. It would thus be possible
        to move tasks and their local data into an EMS bank (in the 64k
        LIM 3.2 page frame), and call create_task with the required page
        configuration activated. Whenever the task is scheduled in, the
        EMS page will have been switched correctly.  The only restriction
        is that the task control block itself, and all CTask data
        structures (event control blocks etc.) must be in common memory.
        All other data, and even the task's stack, may be in EMS
        (although having stacks in EMS is generally not recommended).
        This  may be hard to do with C programs, but could possibly be
        achieved with the use of overlay techniques.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 104



                       Functions called by Kernel Routines

        User-defined functions called from the kernel are the task
        save/restore functions, the functions activated with timers,
        watches and hotkeys, and the "remove" functions. Some
        restrictions apply to those functions.

        For calling functions on a timeout, hotkey, or watch, the
        following must be noted:

           -  Timeout/watch functions should be as short as possible,
             since they run at the highest priority.

           -  The stack area is the area of the timer task, which is
             relatively small. Do not use large automatic variables.

           -  Timeout/watch functions may not use any functions that could
             cause the timer task to be made waiting.

        Since version 2.0, timeout/watch functions are called with
        interrupts enabled. The definition of the timeout/watch/hotkey
        function is

             void Taskfunc funcname (tlinkptr elem)

        The function is called with a pointer to the timer control block.
        The user parameter passed to the create_xxx routines is
        accessible through this pointer (elem->user_parm). The data
        segment is set to the segment address of the timer control block.

        Hotkey functions are equal to timeout/watch functions, but they
        are called from inside the keyboard hardware interrupt. The stack
        is a  local interrupt stack, and the function must not use any
        CTask routines that could cause a task to be made waiting or to
        be killed.

        Remove functions may be called at a time when the state of the
        system is unstable, i.e. during the "emergency exit". To avoid
        problems, you should not call any DOS functions, and also refrain
        from  using CTask functions. Remove functions should only be used
        to uninstall interrupt handlers and do similar cleanups. The
        functions are called with a pointer to the call chain block, and
        the data segment is set to the segment address of this block. The
        definition is

             void Taskfunc funcname (callchainptr chain)


        Two functions may be set in the TCB that are called whenever the
        task  defining them is scheduled out (the "save" function) or
        scheduled in (the "restore" function). The main use for those
        functions is to save and restore static state variables that are
        shared among tasks. A windowing package, for example, may have
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 105



        global variables describing the current window. If you want to
        output to different windows from different tasks, you may have to
        save  the current state whenever the task changes. A better way
        than  to copy a number of variables would be to make the windowing
        package "CTask aware", for example by letting it reference those
        variables through the user pointer in the TCB. This solution,
        however, may not be feasible with third-party libraries. That's
        where the save/restore functions come into play. Both functions
        are defined as

                void Taskfunc funcname (tcbptr tcb)

        i.e.  they do not return a value, and receive a pointer to the
        current TCB (the task control block defining the function). The
        data  segment register is set to the segment address of the TCB.


        The data segment that all those functions are entered with is not
        necessarily the same segment as the normal data segment of your
        program. Especially with far data memory models in Microsoft C,
        the huge model in Turbo C, or dynamically allocated blocks, you
        can not rely on the data segment having the correct value, unless
        you make sure that the control block is located in the same
        segment. To allow you to access global variables from your code,
        you should either use the _loadds keyword with Microsoft C, or
        compile the routine in a separate module with all data references
        defined extern with Turbo C huge model. The safest way is to
        collect all data the routine should modify in a single structure,
        and pass the address of this structure as the user pointer/user
        parameter. If all data you reference is located in the same file
        as the control block, it is reasonably safe to assume that this
        data  is in the same segment, and thus accessible without special
        precautions. You may have to take care not to set the "data
        threshold" with Microsoft C too low, however, since this may
        cause data items in the same file to be placed in different
        segments. The same_seg pragma can be used to avoid this.

















        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 106



                      Some notes on potential trouble spots

                              Turbo C console output

        As mentioned in the manual, console output should generally be
        done  only from one task, or be protected with resources. This is
        especially true for Turbo C (Version 1.5 and later), because the
        putch function is NOT REENTRANT. Since other console output also
        uses  putch in the end, you have to be extremely careful not to
        crash your system by entering the putch routine concurrently. You
        should use the "conout" module provided with CTask to channel
        console output through a buffer. If you own the Turbo C library
        source code, you could replace the "_VideoInt" routine in file
        "crtinit.cas" with an (inline) assembler equivalent that pushes
        BP on the stack instead of storing it into a static variable.


                                The timer tick EOI

        To allow CTask to run concurrently with other background programs
        that  might steal the timer tick interrupt, and to enable high
        priority tasks to override timer ticks, the tick interrupt
        handler issues an EOI before calling the scheduler. Later, the
        tick  task will (possibly indirectly) call the original BIOS tick
        handler, which again issues an EOI for an interrupt that is no
        longer pending. Although this should practically not pose any
        problems, since no other interrupts could normally be pending at
        this  time, and the EOI is not stored, some experts believe it is
        theoretically possible for interrupts to be falsely acknowledged.

        However, according to the INTEL documentation of the 8259
        interrupt controller, the additional EOI can not cause any harm.
        What  the EOI does is to reset the highest priority ISR (Interrupt
        under Service Register) bit in the PIC. According to Intel's
        specs, it will never dismiss an interrupt that is not being
        serviced, since only the INTAK sequence will cause the ISR to be
        set in the first place. If there is an interrupt under service,
        the scheduler is not invoked, so the timer chain can't issue an
        EOI whilst in the middle of another interrupt.  So I think it's
        safe  to issue multiple EOIs, and I haven't had any adverse
        effects with INT8_LATE enabled, even while running serial comms
        with  19200 bps on a networked machine (which should generate a
        lot of INTs).

        If you experience problems in special applications anyway
        (especially if interrupt priorities have been reprogrammed), you
        may use the IFL_INT8_DIR installation flag. This flag changes the
        logic in the timer interrupt handler such that the original
        interrupt is called first, and no additional EOI is issued. You
        could also replace the timer-chaining logic with a routine that
        substitutes the BIOS timekeeping (use the BIOS listing as a
        reference). This, however, would preclude chaining to TSR's that
        have  hooked the timer tick.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 107



                                    Debugging

        Debugging CTask programs can be surprising. The debugger can't
        know  about the task structure of your program, and you can easily
        sit and wonder for hours why the debugger is behaving so
        strangely until it finally sinks down: the debugger itself can be
        preempted.

        The keyboard and timer interrupts are the main culprits. Both can
        hit during execution of debugger routines, so that data may be
        different from what you expect it to be. For example, if you are
        tracing through code that reads or writes a global variable that
        is also modified by another task, you may find that this variable
        has a completely different value when you dump it from the value
        that  was just loaded into a register on the last instruction
        trace. If you are using Periscope, be sure to let Periscope
        restore the INT 8 and INT 9 entries. This is not exactly pleasant
        when  you're using a foreign keyboard, but it can avoid a lot of
        trouble. If you're debugging at the application level, those
        precautions may not be necessary, but if you want to trace into
        the kernel routines, you must be extremely careful not to trash
        the debugger.































        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 108



                          Changes from Previous Versions

        When  upgrading from previous versions, you have to recompile all
        modules that use any CTask functions or data structures. Due to
        the changes in the control blocks, just re-linking is not
        sufficient.

                           Changes for CTask 2.1 to 2.2

        Version 2.2 mainly is a maintenance release. Several bugs, some
        of them severe, were introduced into 2.1 by a number of last-
        minute changes. Most bugs were reported by S. Worthington.

        Bugs  fixed include

           -  The Microsoft C 5.1 and 6.0 compilers generated incorrect
             code for the va_arg macro used to access the optional user
             parameter in the create_timer/watch/hotkey routines. The
             definition of the last parameter before the "..." as "byte"
             caused MSC to access an incorrect (odd) offset for the
             parameter. The "rept" parameter for the create_xxx calls has
             been redefined as "int" to circumvent this.

           -  Enabling the interrupts early in the scheduler could lead to
             race conditions if a task was made waiting, but then made
             runable before the scheduler had enqueued it. This could
             lead to unpredictable behaviour. The fix eliminates the race
             condition by enqueueing the task into the appropriate queue
             immediately, instead of waiting for the scheduler to do it.

           -  The keyboard handler installation caused problems with some
             older BIOSes, since it assumed too easily that an extended
             keyboard was present. This caused keyboard input to hang on
             some machines with non-extended keyboard BIOS. The check has
             now been made more robust.

           -  The hotkey detection logic would cause an immediate schedule
             if a hotkey match occurred, without checking for other
             active interrupts. This could lead to problems if the
             keyboard interrupt had interrupted another, timing critical,
             interrupt. The interrupt active check has been added.

           -  The "CALL_PASCAL" configuration option did not work. Half of
             the implementation was missing in the Assembler parts. This
             has been corrected, with Assembler routines using a slightly
             different procedure header, and different public/external
             pseudo-ops. Assembler routines now can be defined with
             Pascal calling sequence, and the test file "minres.asm" has
             been updated to use the new definitions.




        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 109



           -  The TC_HUGE option would not work when given in the
             assembler command line only, without changing the LOAD_DS
             option. Also, the ctaskh.tc make-file had an incorrect
             dependency, causing the tskint17 module to be omitted from
             the assembly. Both errors have been corrected, you can again
             specify TC_HUGE without editing tskconf.h. The change also
             eliminates pass dependency warnings with Tasm 2.0.

           -  Some key definitions in "kbd.h" were incorrect, and some
             were missing. This has been corrected.

           -  The tsk_switch_stack routine used an incorrect DS in several
             places if the ROM_CODE option was defined TRUE. This has
             been fixed, the ROM_CODE option now works as expected.

           -  If a task waiting for a memory/port watch or hotkey was made
             runable by tsk_wake or a similar action, some locations in
             the next queue element or the queue header could be
             destroyed. The logic to identify timer elements has been
             changed to avoid this problem.

           -  Hotkeys, watches, timeout elements, and tickers created by a
             secondary invocation were not automatically removed on
             termination. This would lead to crashes is there was no
             explicit delete_xxx call. The elements are now chained,
             removal is automatic.

           -  Some routine prototypes were missing in tsk.h, and the
             add_event_name function was actually defined as add_name.

           -  The interface between the t_read_key and t_wait_key
             functions and the INT 16 handler in tskkbd.h was using the
             wrong DS, which would lead to crashes in secondary
             invocations. (Fixed in 2.1a)

           -  The "ticker" structure was defined differently in tsk.h and
             tsk.mac. This would cause problems for programs defining
             tickers in Assembler modules. (Fixed in 2.1b)

        Other changes:

        An optional "checking" mode has been implemented. If CHECKING is
        defined TRUE in tskconf.h, all task and event pointers are
        checked for validity on entry to task functions and other
        strategic points. Although some errors can still go undetected,
        most  memory overwrites or uninitialised pointers that would cause
        a catastrophic crash will now be caught, and the system will stop
        with  an error message before anything vital is destroyed. The
        checking also includes a task stack check, which is performed on
        every scheduler entry. The stack of a task is initialized to a
        defined pattern (0..FF repeated) on a create_task, and the
        scheduler checks for the pattern to be present in the bottom
        eight bytes of the current tasks stack. If this pattern was
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 110



        overwritten, the system is stopped. This feature can also be used
        to determine the maximum amount of stack actually used by a task.
        The tsksnap module will display the number of unused bytes of
        stack for all tasks if checking is enabled.

        The CLOCK_MSEC option, which allows all timeouts to be specified
        in milliseconds rather than timer ticks, has been changed to no
        longer require floating point support. The routine to convert
        milliseconds into ticks was provided by Chris Blum, who also
        supplied some fixes to other modules required to correctly handle
        the CLOCK_MSEC option.

        Timeout elements, watches, and hotkeys can now be created without
        being activated. Separate enable/disable routines are provided to
        avoid the overhead involved in creating and deleting elements
        when  switching hotkey-sets or watches.

        If multiple hotkey entries for the same key/flag combination were
        created, version 2.1 always activated the first entry entered.
        Version 2.2 will activate hotkeys in a round-robin fashion.

        The hotkey checking code now uses the keyboard intercept entry in
        INT 15 if the BIOS supports it. This should increase portability,
        since the routine no longer needs to access the keyboard hardware
        ports directly.


                          Version 2.2 Interface Changes

        New functions:

           create_timer_elem
           create_hotkey_elem
           create_memory_watch_elem
           create_port_watch_elem

              These routines are similar to the old-style create_xxx
              routines, but they do not activate the created element.

           enable_timer
           enable_watch
           enable_hotkey

              Enable timer/watch/hotkey elements

           disable timer
           disable_watch
           disable_hotkey

              Disable, i.e. temporarily suspend, timer/watch/hotkey
              elements. This is different from the delete_xxx calls,
              which will release dynamically allocated elements.

        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 111



        Internal changes:

        The queue handling logic has been slightly changed to allow run-
        time  structure type checking. The queue head is no longer marked
        by a  zero "kind" field, bit 7 (define Q_HEAD) of this field is
        now set in a queue head instead. This should not interfere with
        your  programs unless you are traversing internal CTask queues
        yourself (for example in a modified tsksnap module).

        The structure and handling of timer/watch/hotkey elements has
        changed. The link kind now identifies the kind of the element
        itself, a new struckind field specifies the type of the structure
        "strucp" points to. The element state is no longer needed, the
        field was eliminated. To allow automatic removal on termination
        of a  secondary invocation, the elements are now chained.


                           Changes for CTask 2.0 to 2.1

        Several bugs were fixed. The fixes include

           -  Killing the current task could crash the system if the task
             had a dynamically allocated TCB and/or stack. A new "killer"
             task was introduced to free those blocks after scheduling is
             complete.

           -  Killing a task with a dynamically allocated stack would try
             to free an invalid pointer.

           -  Timers and watches with the TKIND_WAKE attribute ignored the
             repeat specification.

           -  Debugging CTask routines in single-step mode would sometimes
             unexpectedly step into interrupt handlers, because the Trap
             flag in the flag word on the interrupt stack would be
             restored inside the stack switch routine, long before
             exiting the handler.

           -  Timer/watch function calls were supposed to receive the user
             parameter when called. Actually, the address of the
             timer/watch control block is, and always was, passed. The
             documentation has been corrected.

           -  The INT 15 wait/post handler could be overrun by fast disk
             controllers, resulting in disk timeouts.

           -  When compiling for embedded systems, i.e. with GROUPS, DOS,
             and IBM disabled, some statements would not compile, since
             they referenced undefined field names.

           -  The prototype for c_schedule was missing.


        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 112



           -  The resource for INT 10 could be released prematurely if the
             video routines used recursive calls. The request_cresource
             is now used to catch this.

        The routine get_priority now returns the initial, not the current
        priority. With variable priority enabled, saving and restoring
        the priority could lead to a tasks priority gradually increasing.

        The keyboard handler now supports the extended INT 16 functions.
        The t_read_key, t_wait_key, and t_keyhit routines use the
        extended functions if available. The timer interrupt now checks
        the BIOS keyboard buffer, and sets the key_avail flag to wake up
        tasks waiting for the keyboard. This supports keyboard stuffers
        putting characters directly into the buffer.

        The TURBOC and MSC defines caused conflicts with other libraries.
        They  were renamed to TSK_TURBOC and TSK_MSC.

        Resources, flags, counters, mailboxes, and pipes can now be
        initialized statically, i.e. at compile time. This eliminates the
        need  to call the create_xxx routine. The only restriction is that
        such  events are not automatically linked into the name chain. A
        new function, add_event_name, was created for this purpose.

        Version 2.1 introduces keyboard hotkeys, which are similar to the
        timer control blocks and the memory/port watches. Keyboard
        hotkeys are trapped in the keyboard interrupt handler, and can
        activate tasks or functions, or set flags, whenever a particular
        key/shift-key combination is hit.

        Timer control blocks, watchpoints, and keyboard hotkeys can now
        specify counter decrementing in addition to counter incrementing.
        A dec_counter function was added to explicitly decrement a
        counter.

        Support for EMS and 80x87 numeric coprocessors was added. The EMS
        support saves and restores the EMS page map state on every task
        switch to avoid problems with resident utilities, especially EMS-
        based disk cachers. The 80x87 support saves and restores the
        state of the coprocessor on a task switch.

        The scheduler module was revisited, and interrupts are now
        enabled most of the time. This should help to reduce interrupt
        latency. In this context, checks for operations which are illegal
        in interrupt handlers (task wait, kill current task) were added
        to help diagnosing problems. Previous versions would usually
        crash silently in those situations. The task switch save/restore
        functions are now entered with interrupts enabled, and with DS
        set to the data segment of the active task control block.

        A replacement printf module was added. This assembler printf
        replacement is faster than the standard C printf, and is not
        model dependent. It can also output to the secondary screen in a
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 113



        dual-monitor system. This printf is used in the tsksnap module,
        which is now model independent except for the snapshot() routine,
        which uses two C runtime routines (flush and fileno). tsksnap
        also  was fixed to work with small model (some pointers had to be
        explicitly forced to FAR). Some calls to the snapshot dump
        routines now need different parameters.

        A debugging mode provides real-time active task display, and on-
        screen counters for the scheduler, plus counters for timer and
        keyboard interrupts and internal interrupt stack usage. The
        precompiled libraries do not provide debugging, you will have to
        recompile with the DEBUG option in tskdeb.h changed.

        The attributes for internal and external functions are now
        #defined, and can thus easily be changed. This should ease
        porting to other compilers that require different keywords. Also,
        the attributes can now be defined for near code, allowing all
        CTask functions to be compiled in small model if desired. Data
        pointers still have to be far. All calls from Assembler routines
        have  been converted to macro calls, to allow customizing the
        calling sequence. Several customization options have been added
        to better support code-sharing and mixed model compilation and
        assembly.

        Secondary kernels now can share the CTask code with the primary
        invocation. A jump-table linking external modules to installed
        CTask code can be created, so that foreground programs
        communicating with background CTask TSRs do not have to link in
        the full CTask kernel code. A new function, "link_ctask", has
        been  added to check for code sharing installed in a primary
        kernel. Several changes were necessary to allow access to
        functions and variables local to a group from shared code. The
        change also allows applications to call CTask functions from a
        primary kernel without installing their own secondary kernel.

        The mechanism for removing interrupt handlers upon group/kernel
        termination was generalized. Previously, only two "remove"
        routines (for the SIO and printer handlers) could be set. Version
        2.1 introduces the "chain_removefunc" and "unchain_removefunc"
        functions to allow multiple clean-up routines.

        Some  modules were split up, and IFDEF's added to TSKMAIN to allow
        "secondary-only" programs. This change is intended for programs
        that  communicate with a background copy of CTask, and don't
        intend to install the Kernel if that background copy does not
        exist. The make-files create a "secondary" tskmain,
        "stskmain.obj", which is not included in the library. Linking
        with  this stripped-down TSKMAIN saves 6-7k of program code.

        A few other modules also were split up, and routines were
        shuffled around, to avoid linking unreferenced routines. The
        tsk.h and tsklocal.h files were amended to include the module
        name  defining the routine to make it easier to locate routines.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 114



        Name  pointers for tasks and structures may now be NULL.
        Structures with NULL name pointers are not linked into the name
        chain. This is useful for applications linking into CTask without
        creating their own task group.

        Name  parameters are now specified using the #defined macro "TN".
        This  eliminates the need for explicit #if statements on each and
        every name parameter. This change makes the code a lot more
        readable.

        Minor changes, mostly type-casts, were done in several modules to
        eliminate compiler warnings.

        The make-files for the support routines were changed to add the
        model-letter to the filename for both object and library files.
        This  avoids confusion when you use more than one model. The
        Turbo-Make files for the support routines and the sample
        applications were updated to allow model modification from the
        command line. The special ctsuph.tc make-file is no longer
        needed.

                          Version 2.1 Interface Changes

        The interface to the global kernel functions has not changed in
        version 2.1. Note, however, that the v24_remove_func and
        prt_remove_func entries have been replaced by the new remove
        chaining, so this will require changes if you used one of those
        entries to enter your own remove processing.

        The global variable "ticks_per_sec" was moved to the global
        variable block. Since this variable is no longer directly
        accessible, the "ticks_per_sec" function was added.

        If you were using task save/restore routines, or timer/watch
        functions, please note the different handling of DS. DS is now
        set to the data segment of the associated control block, which
        normally, but not always, is equal to the segment created by the
        file  the block was defined in. See the "Advanced topics" chapter
        in the manual for more information.

        For timer/watch/hotkey functions, the parameter passed is a
        pointer to the timer element, not the user parameter, as
        erroneously specified in previous versions of the manual.
        Interrupts are enabled on entry to all functions, including task
        save/restore functions.

        The "screensnap" function in the support module "tsksnap.c" was
        changed. Previously, you had to specify the screen buffer address
        and dimensions with the call to screensnap.  The new version
        requires initialising the screen driver with a call to
        tsk_set_regen or tsk_set_dualdis before calling screensnap, which
        now only accepts a screen length parameter. The function
        "csnapshot" has been added to output to the screen using standard
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 115



        INT 10 calls. The "snapshot" function still takes a FILE *
        parameter, but should preferably no longer be used to output the
        snapshot dump to the screen, since it is significantly slower,
        and requires DOS access. It should only be used to write the dump
        to a  file or a different device.


                           Changes for CTask 1.2 to 2.0

        CTask 2.0 unifies the queue concept, and uses doubly-linked lists
        for all queues, including the task and timer queues. Although the
        overhead is slightly higher when inserting elements, the overall
        logic is greatly simplified, and removing elements from arbitrary
        points in a queue is a snap. To avoid a timing penalty for the
        new functionality, all low-level queue handling code was
        implemented in assembler.

        The new concept allows better support for the yield() operation,
        and it also allows an improved handling of timeout elements. With
        the 1.1/1.2 algorithm, it was not completely safe to process the
        timeout queue with interrupts enabled, and changes to the queue
        required great care. The new handling of the timeout queue, which
        is now sorted, and stores the tick difference to the previous
        element instead of an absolute count, decreases the amount of
        time  spent in the timeout loop. Watch elements, which still
        require stepping through all queue elements, have been separated
        from  timeouts. While the processing of the queue still has to be
        done  with interrupts disabled, the timeout/watch action now is
        completely uncritical.

        The changes to the queue structures required changes in nearly
        all modules. The main changes were in the tsksub, tsktimer, and
        tskasm modules, the tskque module was added.

        Minor corrections were added 89-12-29 to fix a bug in
        tsk_remove_int17 (file TSKINT17.ASM), and minor typos in the
        documentation. The documentation was again fixed 90-01-02, and a
        warning about TASM 1.0 incompatibilities was added to READ.ME.


                          Version 2.0 Interface Changes

        Version 2.0 introduces some changes in the interface. Since the
        changes only affect installation and previously unavailable
        functions, the impact on your programs should be minimal. If
        you're using a 1.2 pre-release, watch out for the changes in the
        name  search and ticker functions. The affected routines are

                install_tasker
                        Two new parameters added. Late 1.2 pre-releases
                        implemented but ignored the "flags" parameter,
                        and recommended setting it to zero. This is no
                        longer true.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 116



                ctask_resident
                        New routine to check if CTask is already
                        resident.

                find_name
                        Name changed from tsk_find_name, values for
                        "kind" parameter changed.

                find_group_name
                        New routine for 1.1, in 1.2 this was called
                        tsk_find_group_name. Searches names within a
                        group. The "kind" parameter values changed.

                yield
                        New routine, schedules with minimal priority.
                        Version 1.2 also had this, but using it could
                        lead to task starvation under certain conditions.

                get_priority
                set_funcs
                set_user_ptr
                get_user_ptr
                        New routines to access fields in the TCB.

                create_ticker
                delete_ticker
                set_ticker
                get_ticker
                        New routines for a simplistic time counter. Late
                        versions of 1.2 had similar functions with
                        different names, and different parameters.

                create_timer
                        New optional parameter.

                create_memory_watch
                create_port_watch
                        New routines to create memory/port watch entries.
                        Some pre-release versions of 1.2 don't support
                        the last, optional, user pointer parameter.

                wait_memory
                wait_port
                        New routines to wait for memory/port changes.

                delete_watch
                        New routine to delete watch element. Pre-release
                        versions of 1.2 equated this to delete_timer,
                        version 2.0 requires delete_watch to be
                        different.

                set_counter
                        New routine to set counter to given value.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 117



                v24_flush_transmit
                        New routine in serial handler to flush transmit
                        pipe.

                prt_flush
                        New routine in printer handler to flush output
                        pipe.


                timout functions
                        The timeout function now is passed a parameter,
                        and is called with interrupts enabled.

                assembler interface
                        All entry points now start with the usual
                        underline, since the extended language-specific
                        procedure definitions are used. The "scheduler"
                        entry was renamed to _tsk_scheduler to avoid
                        catastrophic results of typos.

                internal functions
                        Previous versions defined most internal CTask
                        functions as far. This allowed calling them from
                        outside the CTask kernel (although that was never
                        recommended). The new version no longer allows
                        this, since internal functions are near relative
                        to the common CTask code segment.


                          Changes for CTask 1.1b to 1.2

        The never released version 1.2 added the concept of task groups,
        and the save/restore of internal DOS variables, to support
        spawning and TSR'ing CTask programs. The TSKDOS module went
        through several changes in the pre-release copies.

        All relevant global variables of CTask were grouped into a single
        structure, and are indirectly accessed through a pointer. This
        allows linkage between multiple copies of CTask, with automatic
        detection of other copies.

        This  change required adding new structures, and changing the task
        control block to accommodate the new group linkage and the space
        for the DOS variable swap.

        Also  new in 1.2 was the addition of a stack switch on entry to
        all interrupt handlers. This change was required to eliminate
        problems with TSR's, especially networks, and to support spawned
        programs that supply only a minimal amount of stack. CTask now
        allocates local stacks from a stack pool to hardware and software
        interrupt handlers. On entry to the scheduler, the task registers
        are no longer pushed on the stack, but instead are stored in the
        task  control block. This again mandated a change to the TCB.
        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 118



        Support for memory and port watches that check the state of a
        memory location or an I/O port on every tick was added.

        A "ticker" structure that allows simple timeouts in polling tasks
        was introduced.

        Task  switch save/restore functions were added.

        The printer output driver was reworked, an an INT 17 interface
        driver has been added. The INT 15 printer output support was
        dropped.

        Resources to protect concurrent access to INT 10 and INT 13 were
        added in the TSKDOS module.

        The timer tick interrupt now supports both early and late INT 8
        chaining (and the INT9 stuff has finally been renamed to INT8).
        This  change was required to support network software that would
        time  out without really having waited long enough if the INT 8
        task  was postponed, and ticked a number of ticks at once. It can
        also  avoid incompatibilities with other software that does
        strange things in the timer interrupt. Installation of the new
        INT 8 handling is optional.

        Installation flags now allow on-line customization of some
        functions, especially the installation of some of the BIOS
        interrupts, and the INT 8 algorithm.

        The name-searching functions were augmented to better support
        searching local to groups, and searching groups.

        The make-files were cleaned up, and the Turbo C make-files
        changed to work with Borland's make.

        Support for the Turbo C Huge model was added, assembler files now
        load  the DS register when necessary.

        The placement of external definitions in the assembler files was
        changed to avoid the fixup errors that appeared when assembling
        with  TASM instead of MASM (thanks for H.J. Haug for pointing this
        out).

        All CTask routines are now allocated in a common code segment.
        This  allows calling local functions with a near call.

        All files were polished a bit, with a version number and change
        date  at the top. Comments have again been added. No warnings
        remain for Turbo and Microsoft with all warnings enabled.

        All files were affected, and some new files were added.



        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 119



                          Changes for CTask 1.1 to 1.1b

        Release 1.1b fixed a minor bug in tskmain.c which prevented the
        main  task from being delayed. Thanks to Kent J. Quirk for
        reporting the bug.

        Release 1.1a was necessary to fix three severe and some minor
        bugs  in release 1.1. The bugs corrected in 1.1a were

           -  tskasm.asm:  Interrupts enabled too early in the scheduler
           -  tskdos.asm:  Registers swapped in DOS version test
           -  tsksio.c:    Incorrect loop variable in v24_sio_initialise
           -  tskmain.c:   Function tsk_dis_preempt missing
           -  tsksnap.c:   Incorrect format specification for continuation
                          line
           -  tskasm.asm:  Task state incorrect for eligible tasks

        Also  some minor changes to eliminate warnings, and changes to the
        test  files so they no longer use concurrent console output.

        A console output task was added ("conout.c" and "conout.h") as a
        sample for channeling console output through a single task.

        Some  changes suggested by Stephen Worthington were incorporated
        (pipe flush functions, better SIO transmit interrupt handling).

        Thanks to Peter Heinrich, Stephen Worthington, and Burt Bicksler
        for reporting the bugs.


                           Changes for CTask 0.1 to 1.1

        Thanks to Peter Heinrich, Tron Hvaring, and Dave Goodwin for
        their suggestions and the bug reports.

        The main changes, apart from bug fixes, were

           -  Support for named control blocks
           -  Support for dynamic allocation of control blocks and
             buffers
           -  Task state display support (snapshot dump)
           -  More flexible timer handling, interrupt disable times
             reduced
           -  SIO support extended for shared IRQ's and on-line
             definition of ports; save and restore of control
             registers







        
        
        Ctask Manual       - Version 2.2 - 90-10-12 -            Page 120



                                      Index


           add_event_name                     58
           alloc_resource                     96
           AT_BIOS                            19
           BIOS                               25
           buffer                             52
           bufferptr                          52
           byte                               36
           byteptr                            36
           CALL_PASCAL                        16
           chain_removefunc                   58
           change_timer                       68
           CHECKING                           20
           check_buffer                       87
           check_counter                      81
           check_flag                         79
           check_mailbox                      83
           check_pipe                         85
           check_resource                     77
           check_wpipe                        85
           clear_counter                      80
           clear_flag                         78
           clear_flag_wait_set                79
           CLOCK_MSEC                         18
           CLOCK_MSEC                         64
           code sharing                      102
           code sharing                      103
           CODE_SHARING                       15
           CODE_SHARING                      102
           console                            25
           counter                            50
           counterptr                         50
           create_buffer                      86
           create_counter                     79
           create_flag                        77
           create_hotkey_elem                 72
           create_hotkey_entry                74
           create_mailbox                     82
           create_memory_watch                69
           create_memory_watch_elem           68
           create_pipe                        83
           create_port_watch                  71
           create_port_watch_elem             70
           create_resource                    75
           create_task                        62
           create_ticker                      65
           create_timer                       67
           create_timer_elem                  67
           create_wpipe                       83
           CRITICAL                           61
           ctask_active                       54
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 1



           ctask_resident                     56
           ctask_resident                    102
           curr_task                          64
           C_ENTER                            61
           C_LEAVE                            61
           c_read_buffer                      87
           c_read_pipe                        84
           c_read_wpipe                       84
           c_request_resource                 77
           c_schedule                         60
           c_wait_mail                        83
           c_write_buffer                     87
           c_write_pipe                       85
           c_write_wpipe                      85
           dec_counter                        81
           DEF_COUNTER                        80
           DEF_FLAG                           78
           DEF_MAILBOX                        82
           DEF_PIPE                           84
           DEF_RESOURCE                       76
           DEF_WPIPE                          84
           DEF_xxx                            36
           delete_buffer                      86
           delete_counter                     80
           delete_flag                        78
           delete_hotkey                      74
           delete_mailbox                     82
           delete_pipe                        84
           delete_resource                    76
           delete_ticker                      65
           delete_timer                       68
           delete_watch                       72
           delete_wpipe                       84
           disable_hotkey                     74
           disable_timer                      68
           disable_watch                      72
           DOS                                19
           DOS                                25
           DOS                               103
           dword                              36
           EMS                                20
           EMS                               103
           EMS_SAVE_SIZE                      20
           enable_hotkey                      74
           enable_timer                       68
           enable_watch                       72
           entry table                       102
           farptr                             36
           FAR_STACK                          17
           find_group_name                    58
           find_name                          57
           flag                               50
           flagptr                            50
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 2



           flush_pipe                         85
           flush_wpipe                        85
           funcptr                            36
           funcptr_dword                      36
           funcptr_int                        36
           funcptr_void                       36
           F_CRIT                             48
           F_STTEMP                           47
           F_TEMP                             47
           F_USES_NDP                         48
           GEN_JTAB                          102
           get_priority                       63
           get_ticker                         65
           get_user_ptr                       64
           group control block               101
           GROUPS                             18
           GROUPS                            103
           group_rec                          49
           Hotkey functions                  105
           HOTKEYS                            20
           HOTKEYS                           103
           IBM                                19
           IBM                               103
           IFL_DISK                           55
           IFL_INT15                          56
           IFL_INT8_DIR                       55
           IFL_NODOSVARS                      56
           IFL_NOEXITCHECK                    56
           IFL_PRINTER                        56
           IFL_VIDEO                          55
           inc_counter                        81
           installation flags                 55
           install_tasker                     54
           INT8_EARLY                         19
           INT8_LATE                          19
           intprocptr                         36
           kbflag                             42
           keyboard                           25
           kill_task                          62
           link_ctask                         57
           link_ctask                        103
           LNULL                              35
           LOAD_DS                            16
           LOAD_DS                           102
           LOCALS_FAR                         16
           mailbox                            51
           mailboxptr                         51
           msgptr                             51
           msg_header                         51
           NAMELENGTH                         43
           nameptr                            43
           namerec                            43
           NDP                                20
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 3



           NDP                               103
           NEAR_CODE                          16
           NEAR_CODE                         103
           pipe                               52
           pipeptr                            52
           pipe_free                          85
           preempt_off                        59
           preempt_on                         59
           primary                           101
           primary kernel                    101
           PRI_INT8                           19
           PRI_STD                            18
           PRI_TIMER                          18
           prt_change_control                 95
           prt_complete                       95
           prt_flush                          95
           prt_install                        94
           prt_remove                         94
           prt_remove_all                     95
           prt_status                         95
           prt_wait_complete                  95
           prt_write                          95
           qelem_pri                          37
           queheadptr                         38
           queptr                             37
           queue                              38
           queue_head                         38
           read_buffer                        87
           read_pipe                          84
           read_wpipe                         84
           release_resource                   76
           remove function                   105
           remove routine                     59
           remove_tasker                      56
           request_cresource                  77
           request_resource                   76
           resource                           51
           resourceptr                        51
           restore function                   44
           restore function                  105
           ROM_CODE                           17
           save function                      44
           save function                     105
           schedule                           60
           sched_int                          60
           secondary                         101
           SECONDARY                         102
           secondary kernel                  101
           send_mail                          82
           set_counter                        81
           set_flag                           78
           set_funcs                          64
           set_priority                       63
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 4



           set_task_flags                     63
           set_ticker                         65
           set_user_ptr                       64
           SINGLE_DATA                        20
           spawn                              26
           start_task                         62
           stop_task                          63
           stub table                        102
           ST_DELAYED                         46
           ST_ELIGIBLE                        46
           ST_KILLED                          46
           ST_RUNNING                         46
           ST_STOPPED                         46
           ST_WAITING                         46
           tcb                                46
           tcbptr                             45
           tcb_rec                            45
           TCMP_CHG                           40
           TCMP_EQ                            40
           TCMP_GE                            40
           TCMP_GES                           40
           TCMP_LE                            40
           TCMP_LES                           40
           TCMP_NE                            40
           TC_HUGE                            16
           TC_HUGE                           102
           TELEM_HOTKEY                       40
           telem_hotkey                       42
           TELEM_MEM                          39
           telem_memwatch                     42
           TELEM_PORT                         39
           telem_portwatch                    42
           telem_timeout                      42
           TELEM_TIMER                        39
           TFLAG_BUSY                         41
           TFLAG_ENQUEUE                      41
           TFLAG_REMOVE                       41
           TFLAG_REPEAT                       41
           TFLAG_TEMP                         41
           TFLAG_UNQUEUE                      41
           TFP_OFF                            35
           TFP_SEG                            35
           ticker                             50
           ticker                             65
           ticks_per_sec                      64
           tick_ptr                           50
           TIMEOUT                            37
           Timeout/watch functions           105
           Timeouts                           64
           TKIND_COUNTDEC                     39
           TKIND_COUNTER                      39
           TKIND_FLAG                         39
           TKIND_PROC                         39
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 5



           TKIND_TASK                         39
           TKIND_WAKE                         39
           tlink                              42
           tlinkptr                           42
           TMK_FP                             35
           TN                                 36
           tsk_alloc                          96
           tsk_calloc                         96
           tsk_cli                            61
           tsk_disport                        99
           tsk_dis_int                        60
           tsk_dis_preempt                    59
           TSK_DYNAMIC                        17
           TSK_DYNAMIC                       103
           TSK_DYNLOAD                        17
           tsk_ena_int                        61
           tsk_ena_preempt                    59
           tsk_fprintf                        97
           tsk_free                           96
           tsk_inp                            61
           TSK_NAMED                          18
           TSK_NAMED                         103
           TSK_NAMEPAR                        17
           TSK_OFFSETOF                       35
           tsk_outp                           61
           tsk_printf                         97
           tsk_putc                           97
           tsk_puts                           98
           tsk_realloc                        96
           tsk_regen                          99
           tsk_regen_o                        99
           tsk_regen_s                        99
           tsk_rprintf                        97
           tsk_rputc                          98
           tsk_rputs                          98
           tsk_scheduler                      60
           tsk_setpos                         99
           tsk_set_attr                       99
           tsk_set_colour                     98
           tsk_set_currdis                    98
           tsk_set_dualdis                    98
           tsk_set_mono                       98
           tsk_set_regen                      99
           tsk_sprintf                        97
           tsk_sti                            61
           TSK_STRUCTOP                       35
           tsk_use_ndp                        54
           tsk_vfprintf                       97
           tsk_vprintf                        97
           tsk_vrprintf                       97
           tsk_vsprintf                       97
           TSR                                26
           TTIMEOUT                           37
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 6



           TWAKE                              37
           TWATCH                             37
           TYP_BUFFER                         43
           TYP_COUNTER                        43
           TYP_FLAG                           43
           TYP_GROUP                          43
           TYP_HOTKEY                         43
           TYP_MAILBOX                        43
           TYP_PIPE                           43
           TYP_RESOURCE                       43
           TYP_TCB                            43
           TYP_TIMER                          43
           TYP_WATCH                          43
           TYP_WPIPE                          43
           t_delay                            66
           t_keyhit                           88
           t_read_key                         88
           t_wait_key                         88
           unchain_removefunc                 59
           user pointer                       44
           v24_change_baud                    90
           v24_change_dtr                     90
           v24_change_parity                  91
           v24_change_rts                     90
           v24_change_stopbits                91
           v24_change_wordlength              91
           v24_check                          92
           v24_complete                       93
           v24_define_port                    88
           v24_flush_receive                  93
           v24_flush_transmit                 93
           v24_install                        89
           v24_modem_status                   93
           v24_overrun                        93
           v24_protocol                       92
           v24_receive                        92
           v24_remove                         90
           v24_remove_all                     90
           v24_send                           92
           v24_wait_complete                  93
           v24_watch_modem                    91
           wait_counter_clear                 80
           wait_counter_set                   80
           wait_flag_clear                    78
           wait_flag_set                      78
           wait_hotkey                        74
           wait_mail                          82
           wait_memory                        70
           wait_pipe_empty                    85
           wait_port                          72
           wait_wpipe_empty                   85
           WAKE                               37
           wake_task                          63
             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 7



           WATCH                              37
           word                               36
           wordptr                            36
           wpipe                              52
           wpipeptr                           52
           wpipe_free                         85
           write_buffer                       87
           write_pipe                         85
           write_wpipe                        85
           yield                              60











































             
             
             Ctask Manual     - Version 2.2 - 90-10-12 -          Index 8