The ______.ENG files included with this release of NX3 are
     samples of engines we have simulated.  These files are simply the
     report output for these engines.  You can review them using
     whatever method you use to read this, or you can print them.
     
     The following engine simulations are included:
     
           353 cid Ford SVO SuperModified drag engine          SM_FORD .ENG
           338 cid Chev SuperModified drag engine              SM_CHEV .ENG
           "Grumpy" Jenkins 330 cid Pro Stock of the '70s      GRMPYTOY.ENG
           SCCA Formula 5000, 302 Chev, road racer             F5000CHV.ENG
           305 cid Ford Cobra wedge head for vintage racing    COBRA302.ENG
           Typical NASCAR single 4 bbl before restrictors      NASCAR  .ENG
           500 cid Pro-Stock Chevrolet, Low block deck         PRSTKCHV.ENG
           A tunnel port, stroked Ford FE built for
              "street" currently happily in a '74 Pantera      TPFORDFE.ENG
           1275cc Mini-Minor British sedan road racer          BMC_MINI.ENG
           Ford 351c Oval Track race engine                    BOSS351C.ENG
           Ruggles-style Buick V-6, 4.5 liter NASCAR           V6_BUICK.ENG
           Speculation about Lamborghini-Chrysler
                  Formula 1, 3.5 liter V-12                    F1_LAMBO.ENG
           350 Chev engine you get if you accept all defaults  ES3SMPL .ENG
     
     The Lambo is known to be an 80 degree bank, naturally aspirated,
     V-12 of 3.5 liter displacement.  Both 4 and 5 valve cylinder heads 
     are being developed, and over 600 horsepower will probably be 
     required to be competitive.  Interestingly, this class of engine is
     not limited by the strength of parts required to cope with nearly
     turbine level engine speeds with short rod ratios, but rather by 
     piston ring flutter.  Enormous piston acceleration across TDC com-
     pression/ignition will throw all but the lightest rings off the bottom 
     ring land, losing gas pressure loading off the top of the ring, and 
     allowing blow-by at the most critical part of the combustion cycle.
     Knife thin motorcycle style rings are required, high compression for 
     greater pressure on top of the ring, and Grumpy Jenkins style gas ports 
     should help.

     The BOSS351C was an iron head, flat tappet cam, Edelbrock Torker, and
     850 Holley 351c we built and dyno-ed in 1977. The car was competitive
     with aluminum head Rat Chevrolet engines, but as you may see had a narrow 
     power band.  If we had this program in '77, we would have redesigned the 
     cam and headers, run up to 7500 RPM and done much better.
     
     Among the SuperModified and NASCAR engines it is interesting to
     note the tremendous performances being attained with restrictive
     carburetors.  The SM engines are limited to 750 cfm Holleys with
     choke horn intact, but no choke blade.  Holley says the latest
     models actually flow 800 cfm, which in Denver amounts to 890 (a
     carburetor is a mass flow device, not a volume flow device).  The
     SM Ford uses a large plenum, fabricated tunnel ram manifold; and
     the SM Chev uses the latest Bow-Tie single plane manifold with a
     1-1/2+ inch tall open spacer.  In any case, these engines must
     fight carb size limits to be competitive.
     
     The other engines have no such intake limits.  The F5000 engines
     used timed port injection and achieved excellent wide range
     driveability.  The pro-stocks use 2 x 660 cfm for Grumpy's Toy
     and 2 x 1150 on tunnel ram manifolds for the 500 cid Pro Stocks.