This program is copyrighted in Canada and other countries by:
        
        Bob Seaborn  PO Box 1741 Saskatoon Saskatchewan Canada S7K-3S.
        
        All rights are reserved.  This program is released as shareware 
        for the IBM series of computers, and will operate on the 8086, 
        8088, 80286, and 80386 processors.  A math co-processor is NOT 
        required. A $10.00 donation is requested if you find that this 
        program is useful and of some help in setting up and maintaining 
        a satellite TVRO system. 
        
        If you wish a version that does not contain the closing "request 
        for donation" screen, please send $15.00 to the author at the 
        above address. Comments, suggestions, and bug reports are always 
        welcome, and can be sent via mail to the above address, or by E-
        mail to the author at Fido-net 1:140/51.  This program is 
        updated as new satellites are placed in orbit, and old ones are 
        retired.  The latest version can always be made available at 
        Fido-net 1:140/1 (HST) for file-request.  Please send E-mail 
        requesting the file, and you will be advised via E-mail what the 
        file name is and when it can be accessed.  It can also be made 
        available at Northern Nights (1:140/48) HST (1-306-384-0572) for 
        downloading. 
        
        To use this program, you need to know the geographical 
        coordinates for the location of the satellite dish.  The better 
        the accuracy, the more accurate the output data.  If you don't 
        know the coordinates, they can be found on any topographical 
        map.  The coordinates of the nearest airport can also be used if 
        it's within a few miles.  This program has been tested 
        throughout the Nort-Western hemisphere, and found to be quite 
        accurate. Although it can calculate dish aiming for the other 
        hemispheres, no guarantee can be made of it's accuracy.  Also 
        the Canada-US satellites are aimed at the Northern hemisphere, 
        and might not be viewable elsewhere. 
        
        When you start the program, you are asked if you want hardcopy.  
        If you answer "Yes", and no printer is attached, or the printer 
        output is not redirected, the program will hang until the 
        printer is attached or the computer is rebooted. 
        
        The program will display the aiming coordinates for all the 
        geostationary satellites currently in the North American section 
        of the Clark belt.  If hardcopy is requested, the printout will 
        also contain areas so that technical values of each system may 
        be recorded.