CAMDESGN.EXE
          
          
     This program calculates the displacement, velocity and acceleration of a
     cam follower.  Two standard cam profiles are included for comparison.
     The results may be either sent to the screen or to a printer.  
          
     INPUT DATA:
          
     1.  Select Motion Profile:  Two cam profiles are available.
           Cycloidal 
           Modified Sine
         For a discussion of the advantages of each profile, see a mechanical     
         engineering text or reference book.  By running the program with the   
         same data for both profiles and looking at the displacement results,      
         one can see the physical difference between the two profiles.
          
     2.  Select Motion Parameters:  
         a) Enter Cam Zone (1-4) -- The total 360 degree cam profile can be
          divided into as many as four zones.  Use as many of the four
          zones as required.  It is not necessary to use all four.  The data
          described in items b) through f) below must be entered for each
          zone.
         b) Enter Motion (1=Dwell  2=Rise or Fall) -- Within the cam zone
          selected, tell the program if it will be a dwell (a period of no rise
          or fall) or if the cam follower will be rising or falling in this zone
          of the cam profile.
         c) Enter Initial Displacement (inches)  -- This is the radius of the cam
          at the beginning angle of the zone for which the data is being
          entered.  Data MUST be entered in inches.
         d) Enter Final Displacement (inches) -- This is the radius of the cam
          at the final angle of the zone being entered.  Data MUST be
          entered in inches.
         e) Enter Initial Angle (degrees) -- Enter the starting angle of the cam
          profile for the selected zone.
         f) Enter Final Angle (degrees) -- Enter the angle that defines the end
          of the zone. 
          
     An example:  Assume that a cam has one dwell section that is 180
     degrees in length with a radius of 1.5 inches (the first zone). It has a rise
     section that is 90 degrees long with an initial radius of 1.5 inches and a
     final radius of 2.2 inches (the second zone.)  The fall section is 90
     degrees in length, with the radius then falling from 2.2 to 1.5 inches (the 
     third zone.)  The data entry would be as follows:
     


           
          Cam Zone              1              2            3
          Motion Type           1 (dwell)      2 (rise)     2 (fall)
          Initial Displ         1.5            1.5          2.2
          Final Displacement    1.5            2.2          1.5
          Initial Angle         0              180          270
          Final Angle           179            269          359

     RESULTS:
          
     Two parameters may be varied before or after you have entered the cam
     physical profile data -- the speed of rotation and the motion profile
     (cycloidal and modified sine).  Therefore, you can examine various
     combinations of rotation speed and motion profile with a given physical
     cam profile without re-entering the cam profile data. 
          
     The cam follower displacement, velocity and acceleration versus cam
     angle may be viewed on screen graphs (item 3 on the menu).  If you
     wish to capture this information, use the "print screen" function.
     Additionally, you may print the displacement vs. cam angle, in one
     degree increments, on your printer by selecting menu item 4.
          
     The companion program, CAMFORCE.EXE, will calculate the forces
     on the cam surface that result from the acceleration of the driven load.
     
     ACKNOWLEDGEMENTS:
     
     The basis for this program was derived from an article in Machine
     Design magazine on November 21, 1985.  The author of the article was
     Chris S. Pedicini of the Eveready Battery Company of Brunswick, Ohio.
          
     DISCLAIMER:
          
     Results derived from the use of this program are believed to be accurate. 
     However, the author will not be responsible for any actual or
     consequential damages that may result from the use of this program.
     Your sole remedy is to recover any payment that you may have made
     directly to the author for this program.  If you find an error, please
     notify the author via Compuserve and a revision will be posted promptly.





     SHAREWARE NOTICE:
          
     If you find this program of value, you are requested to register the 
     program using the file, REGISTER.TXT, included with this distribution.
               


     Bill R. Wittner PE                     Compuserve:  72167,3172
     1705 Skyline Drive
     Russellville, AR  72801         
     USA