CAMFORCE.EXE
          
          
     This program calculates the loading on a cam follower.  Two standard cam          
     profiles are included for comparison.  The program neglects the effects of            
     friction and pressure angle.  However, for pressure angles less than 30 degrees     
     and for a coefficient of friction of less than 0.1, minimal error should be             
     introduced.
          
     INPUT DATA:
          
     SELECT CAM PROFILE:  Two cam profiles are available.
          Cycloidal 
          Modified Sine
     For a discussion of the advantages of each profile, see a mechanical     
     engineering text or reference book.  By running the program with the   
     same data for both profiles and observing the results, one can see the
     effects of the two profiles.
     
     After selecting the cam profile, the following data is entered:

     CAM SPEED:       Enter the speed in revolutions per minute
     PERIOD OF RISE:  Enter the number of degrees of cam rotation in which the      
                      rise occurs.
     CAM RISE:        Enter the rise of the cam lobe in inches.
     INERTIA WEIGHT:  Enter the weight, in pounds, of the cam follower, valve and 
                      any additional mechanism that will be moved by the cam.
     SPRING PRELOAD:  Enter the initial spring loading that exists just prior to        
                      starting the rise.  Load must be entered in pounds.
     SPRING RATE:     Enter the spring rate, expressed in pounds per inch.  It is       
                      assumed that the spring follows Hookes law, i.e. it remains in the     
                      elastic range.
     GRAVITY EFFECT:  If the inertia weight is significant or if the acceleration is    
                      low, the effect of gravity may not be insignificant on the loading.  If 
                      the centerline of the inertia weight is in-line with gravity, enter Y.    
                      If the centerline of the inertia weight is perpendicular to gravity,      
                      enter N.  If it is at an angle, a best-guess approximation must be      
                      made after running the program with and without gravity affects.
     



     RESULTS:
          
     If the loading becomes negative during any part of the cycle, this is an indication   
     that the follower is "floating" away from the cam lobe.  Damage may result if      
     operated under this condition.  To eliminate float, increase the pre-load and/or the 
     spring rate.

     The companion program, CAMDESGN.EXE, will calculate the acceleration of the 
     follower and attachments.  Cam loading is directly proportional to mass and         
     acceleration.
         
     ACKNOWLEDGEMENTS:
     
     The basis for this program was derived from an article in Machine
     Design magazine on November 26, 1987.  The author of the article was
     Chris S. Pedicini of the Eveready Battery Company of Brunswick, Ohio.
          
     DISCLAIMER:
          
     Results derived from the use of this program are believed to be accurate. 
     However, the author will not be responsible for any actual or
     consequential damages that may result from the use of this program.
     Your sole remedy is to recover any payment that you may have made
     directly to the author for this program.  If you find an error, please
     notify the author via Compuserve and a revision will be posted promptly.

     SHAREWARE NOTICE:
          
     If you find this program of value, you are requested to register the
     program using the file, REGISTER.TXT, included with this distribution.
          
          
     Bill R. Wittner PE                     Compuserve:  72167,3172
     1705 Skyline Drive
     Russellville, AR  72801         
     USA