EZSSTV.DOC  --  November 1994
		-----------------------------

Amateur SSTV has been around for decades but most people were scared
away because it was so expensive and complicated.  It isn't anymore.
Many hams are now discovering this interesting mode and many old-timers
from the early days are returning.

In the 1980's it was necessary to spend well over a kilobuck to
buy special equipment dedicated to SSTV.  In the last couple years
several PC-based systems have appeared.  These all use fairly simple
interfaces to get audio in and out of the computer and do most of
the work in software.

This EZ SSTV software will allow you to receive the two currently most 
popular SSTV modes.  The nets often use Robot 36 color because it is
reasonably quick and universally available. During more leisurely times, 
Scottie S1 seems to be the favorite for its much better image quality.


What you need to watch SSTV
---------------------------

	* This software.
	* An IBM PC or compatible with at least:
		- '386 or better CPU. (Might be able to sneak by with '286.)
		- 640K memory.
		- Color VGA display.
		- Spare serial port (COM1 or COM2) for the interface.
		- A mouse is handy but not necessary.
	* A cheap and simple interface described below.  If you
	  already have a receive interface for one of these it
	  should work fine:
		- HAMCOM.
		- VESTER (see note below).
		- JVFAX (single op-amp version).
		- FAXCAP.
		- SSC PC SSTV.
		- SSC PC HF Fascimile.
		- AEA FAX.
	  This software will also work with the AEA PK-900.  See notes
	  toward end of file for details.


The Interface
-------------

A well stocked junk box probably has all of these.  Otherwise, you can
get everything at your local Radio Shack store. The resistor and capacitor
values are not at all critical.  Use either a 25 or 9 pin connector
depending on the type of serial port available.

						part #          $
						------        -----
	U1      741 or similar op amp           276-007         0.79
	R1      47K resistor                    271-1342        0.39
	C1      0.01 uF capacitor               272-131         0.49
	J1      DB25S                           276-1548        1.99
	    or  DB9S connector                  276-1538        1.29
	-       Shielded cable for audio         ?               ?

There are many variations on this basic circuit.  Others use diodes
for reverse voltage protection, capacitors for power filtering, and/or
transformers for breaking up ground loops.  This is trimmed to the
bare essentials but still seems to work well.


				U1 - top view
			(pins pointing away from you)                25    9
			    notch on this end           J1    name   pin  pin
			    and/or dot near pin 1             ----   ---  ---

				  +----U----+         +-----+
				  | 1     8 |    +----|--O  |  RTS    4    7
audio from         | |            |         |    |    |     |
receiver    -------| |---+--------| 2     7 |----+    |     |
		   | |   |        |         |         |     |
		C1       |   +----| 3     6 |---------|--O  |  DSR    6    6
			<    |    |         |         |     |
			 >   | +--| 4     5 |         |     |
		    R1  <    | |  +---------+         |     |
			 >   | |                      |     |
			<    | +----------------------|--O  |  DTR   20    4
			 >   |                        |     |
			 |   |                        |     |
audio ground ------------+---+------------------------|--O  |  GND    7    5
						      +-----+


Let's see some pictures
-----------------------

Attach the interface to a serial port and to the audio output of your
receiver or transceiver.  Tune into one of the SSTV frequencies:

	80 meters:      3.845   3.857   MHz
	40 meters:      7.171
	20 meters:      14.230  14.233
	15 meters:      21.340
	10 meters:      28.680
	2 meters:       144.5

20 and 80 meters are generally your best bet.  There are nets every
Saturday at 15:00 and 18:00 UTC on 14.230 MHz.

Type "EZSSTV" to run the program.  You can use either the mouse or keyboard.


Mouse Operation
---------------

Click on the "Recv" button.  You will be asked which serial port the
interface is attached to.  Click on either the "COM1" or "COM2" button. 
If you click on the serial port used for the mouse, the mouse will
stop working.  In this case, exit the program using the keyboard and
start over again.

Sit back and enjoy the pictures.  The receive mode will automatically
switch between Robot 36 and Scottie S1 if a valid VIS code is received.
The software also has automatic fine tuning which will track signals
up to 100 Hz off frequency.

Just try the buttons and menus to see what they do.  This is a lot 
quicker and more interesting than reading detailed descriptions.
You will notice that some features are "grayed out" and disabled.  All
these features are in the full version of Pasokon TV.


Keyboard Operation
------------------

Notice that the "Recv" button has a red label.  Whenever there is a
button with a red label, the 'Enter' key can be used to select this
default button.

Press 'Enter' to start receiving.  Press "1" or "2" depending on where 
the interface is located.  

Keyboard equivalents:

	F1      - Robot 36 second color mode.
	F4      - Scottie S1 mode.
	Alt-D   - Desk menu, contains only "About" item in this version.
	Alt-F   - File menu, read files, quit, etc.
	Alt-E   - Edit menu, modify existing images.
	Alt-M   - Make menu, make test patterns.
	Alt-C   - Config menu, display information and set options.
	left & right arrows     - Select images along bottom of screen.
	up arrow                - Full screen image display.

It is not necessary to pull down a menu to access one of its functions.
For example, you can simply press "Q" for quit instead of Alt-F then "Q".


VESTER SSTV Interface
---------------------

A minor change is required to use the VESTER SSTV interface with the 
EZ SSTV software.  This modification should not affect operation of
the interface with the VESTER software.

Simply add a 1N914 or similar diode:

    * Cathode end (bar) to U1, pin 7.
    * Anode end to RTS pin of J1.    
		(This is pin 4 of a 25 pin connector.)
		(This is pin 7 of a 9 pin connector.)


AEA PK-900
----------

This multimode TNC is capable of receiving WEFAX and SSTV.  You can use
use it for SSTV reception by following these steps:

    1. Connect transceiver to radio port 1, which is where you'd
	normally connect an HF transceiver.  Even if using a VHF radio
	still connect it to radio port 1.
    2. Connect the PK-200 to a serial port on your computer in the 
	usual way.
    3. Run a terminal program.  Send these commands to the PK-900:
    
		radio 1/0
		analog
		
	It should now be in the proper mode to demodulate the SSTV 
	signals.
    4. Exit out of the terminal program and run EZSSTV.  Follow usual
	instructions above.

When finished with SSTV operation, perform a hardware reset on the PK-900 
to remove all remnants of the "analog" mode.  It has been reported 
that some PK-900 control programs don't work properly after the TNC
has been in "analog" mode.  The solution is a hardware reset on the 
PK-900; a software reset doesn't seem to be adequate.


For more information on SSTV
----------------------------

See the January 1993 issue of QST or the SSTV section of the 1995 ARRL
Handbook for Radio Amateurs or contact:

	John Langner WB2OSZ
	115 Stedman St. # E
	Chelmsford, MA 01824-1823
	U.S.A.

	telephone: (508) 256 6907
	Internet e-mail: johnl@world.std.com