***************************** DISK & FILE *******************************

ASM32 disk & file subroutines Copyright (C) 1993 Douglas Herr
All rights reserved

The DOS file attribute byte tells you whether a file is read-only,
system, a subdirectory, or may provide other information.  File attribute
bits may be combined.  Each bit of the file attribute means:

        0 = normal files
        1 = read-only
        2 = hidden files
        4 = system files
        8 = volume label (only one per disk)
       16 = subdirectories
       32 = archive bit set

   Thus a file with an attribute of 18 is a hidden subdirectory (16 OR 2)



                      ASM32 buffered file I/O system

    Several ASM32 subroutines are available for buffered file Input or
    Output.  Files to be managed by the buffered I/O system must be opened
    by FOPEN or FCREATE, and must be closed by FCLOSE.  Buffered file I/O
    will be much faster than unbuffered.  ASM32's default buffer size is
    4096 bytes; this can be changed by altering FBUFFER_SIZE in FOPEN.ASM
    and re-assembling.  Up to 20 files can be managed by FOPEN; this can
    be changed by altering NUMBER_OF_FILES in $handle.asm and reassembling.

    Subroutines: FOPEN        open file & initialize buffer
                 FCREATE      create file & initialize buffer
                 FCLOSE       flush & close output buffer; close file
                 FSEEK        move file pointer & update buffer
                 FGETSTR      read a string from buffer
                 FGETCHR      read a character from buffer
                 FGET         read specified number of bytes from buffer
                 FPUTSTR      write string to buffer
                 FPUTCRLF     write CR+LF to buffer
                 FPUTCHR      write character to buffer
                 FPUT         write specified number of bytes to buffer



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DISKSIZE:    determines total and free disk space
Source:      disksize.asm

Call with:   DL = drive number (drive A: = 0, default drive = -1)
Returns:     if CF = 0, EAX = total disk space
                        EDX = free disk space
             if CF = 1, AX = DOS error code
              DiskSize does not trap "drive not ready" errors
Uses:        EAX, EDX, flags
Supports:    all DOS drives
Example:

public  example_code
extrn	disksize:near

include codeseg.inc

; code
example_code    proc near
        mov	dl,0
        call    disksize
        jc      disk_error


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

diskwp:      determines if a floppy disk is write-protected
Source:      diskwp.asm

Call with:   DL = floppy disk number (drive A: = 0)
Returns:     AL = BIOS error code
                0 = no error
                1 = invalid disk number
                3 = disk is write-protected or wrong media
              128 = drive not ready
Uses:        EAX, flags
Supports:    physical drives A: and B:
Example:

public  check_disk
extrn   diskwp:near

include codeseg.inc

; code
check_disk      proc near
        .
        .
        .
        mov     dl,1              ; drive B:
        call    diskwp            ; can I write to this disk?
        jnc     short no_problem



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DOTBAK:      changes the file extension of an existing file to .BAK
Source:      dotbak.asm (strrchr.asm)

Call with:   ESI = address of a valid ASCIIZ filename
             dotbak deletes a previous .BAK file of this name and
             renames the input filename.ext to filename.bak.
Returns:     if CF = 0, no error
             if CF = 1, AL = DOS error code.  If AL = 5, the previous
             .BAK filename is probably read-only.  All other errors refer
             to the name change operation.
Uses:        AX, flags
Example:

extrn   dotbak:near

include dataseg.inc

; data

disk_doc  db 'DISK.DOC',0

@curseg	ends

include codeseg.inc

; code
             .
             .
             .
             mov   esi,offset disk_doc
             call  dotbak


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCLOSE:      close a file managed by ASM32's buffered file I/O system
Source:      fopen.asm ($handle.asm)

Call with:   BX = file handle
             The file must have been opened by FOPEN or FCREATE;  If the
             file is not read-only, the output buffer will be written to
             the disk file before closing the file.
Returns:     if CF = 0, no error
             if CF = 1, AX = error code
Uses:        AX, flags
Example:     see FOPEN





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCOPY:       copy a file
Source:      fcopy.asm

Call with:   ESI = address of source filename
             EDI = address of destination filename
             Both filenames must be ASCIIZ strings.  Drive and path need
             not be fully specified; filenames may not include * or ?
             wildcards.
Returns:     if CF = 0, no problem
             if CF = 1, AX = DOS error code
Uses:        EAX, CF
Example:

extrn   fcopy:near

include dataseg.inc

; data
        db 'b:'
source  db 'asm32cw.lib',0         ; copy the library to b:

@curseg	ends

include codeseg.inc

; code
        .
        .
        lea     esi,source
        mov     edi,esi               ; EDI also points to source
        sub     edi,2                 ; back the pointer to the 'B:'
        call    fcopy
        jc      oops




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCOUNT:      counts the number of files matching an ASCIIZ filespec string.
             The filespec string may include the '*' and '?' wildcards.
Source:      fcount.asm

Call with:   EDX pointing to filespec string
             CX = file attributes
Returns:     EAX = number of files matching the filespec string
Uses:        EAX
Example:

extrn   fcount:near

include dataseg.inc

; data
filespec  db '*.asm',0

@curseg	ends

include codeseg.inc

; code
        .
        .
        .
        lea    edx,filespec     ; address of filespec string
        xor    cx,cx            ; normal files only
        call   fcount



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCREATE:     create new file and initialize output buffer
Source:      fcreate.asm ($handle.asm)

Call with:   EDX pointing to ASCIIZ filename
             The file is created with write-only access.  If a file with
             the same name already exists, it is truncated to zero
             length by FCREATE.
Returns:     if CF = 0, AX = file handle
             if CF = 1, AX = error code
Uses:        AX, flags
Example:

public   myprog
extrn    fcreate:near

include  dataseg.inc

; data
file_name   db 'ANYNEW.FIL',0
file_handle dw 0

@curseg	ends

include codeseg.inc

; code
myprog   proc  near
         .
         .
         .
         lea   edx,file_name
         call  fcreate
         jc    something_went_wrong      ; go to error control code
         mov   file_handle,ax            ; save the handle
         .
         .
         .



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FEXIST:      determines if a file exists and can be opened with read access
Source:      fexist.asm

Call with:   EDX pointing to ASCIIZ filename
Returns:     if CF = 0, file exists
             if CF = 1, AX = DOS error code
Uses:        AX, CF; all other flags and registers are saved
Example:

extrn    fexist:near

include  dataseg.inc

; data
filename db 'asm32.doc',0

@curseg	ends

include  codeseg.inc

; code
         .
         .
         .
         lea   edx,filename
         call  fexist
         jnc   got_the_file      ; if CF = 0, go on
         jmp   doserror          ; else go to error handling code




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FFLUSH:      flushes the ASM32 and DOS output buffers for specified handle
Source:      fflush.asm (fseek.asm)

Call with:   BX = file handle
             flushing the buffers guards against data loss in case of system
             failure, such as power loss
Returns:     if CF = 0, no error; function successful
             if CF = 1, AX = DOS error code
Uses:        AX, flags
Example:

include codeseg.inc

extrn   fflush:near

; code
; program opens file & writes to file
      .
      .
      .
; flush the buffers to disk
      mov    bx,handle
      call   fflush




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FGET:        read specified number of bytes from file buffer
Source:      fget.asm ($handle.asm, $fget.asm)

Call with:   BX = file handle
             ECX = number of bytes requested (up to 4096 bytes)
Returns:     if CF = 0, EAX = number of bytes read
                        EBX points to data in buffer
             if CF = 1, AX = DOS error code
Uses:        EAX, EBX, flags
Example:

extrn   fopen:near, fget:near

include dataseg.inc

; data
file_name   db 'asm32.doc',0
file_handle dw 0

@curseg	ends

include codeseg.inc

; code
          .
          .
          .
          lea   edx,file_name
          call  fopen
          jc    fopen_problem
          mov   file_handle,ax  ; save for later

          mov   bx,ax           ; file handle
          mov   ecx,8           ; I want 8 bytes
          call  fget            ;  returned at [EBX]
          jc    read_problem    ; uh oh, trouble ...
          cmp   eax,ecx         ; did I get what I wanted?
          jne   not_enough
          .
          .





°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FGETCHR:     read a character from a file buffer
Source:      fgetchr.asm ($handle.asm)

Call with:   BX = file handle
Returns:     if CF = 0, AL = next character from file buffer
             if CF = 1, AX = DOS error code
                        AX = 0 if at end of file
Uses:        AX, flags
Example:

extrn   fopen:near, fgetchr:near

include dataseg.inc

; data
file_name   db 'asm32.doc',0
file_handle dw 0

@curseg	ends

include codeseg.inc

; code
          .
          .
          .
          lea   edx,file_name
          call  fopen
          jc    fopen_problem
          mov   file_handle,ax  ; save for later

          mov   bx,ax           ; file handle
          call  fgetchr         ; character in AL
          jc    read_problem

          .
          .




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FGETSTR:     read an ASCII string from a file buffer
Source:      fgetstr.asm ($handle.asm, $fget.asm)

Call with:   BX = file handle
             ASCII strings may be terminated with either 0Dh or 0Dh+0Ah.
             After reading each string, FGetStr positions the buffer pointer
             to read the next string.  String length should be less than
             the buffer size.  See FOPEN.
             NOTE THAT THE STRING IN THE BUFFER IS NOT ZERO-TERMINATED.
Returns:     if CF = 0, EBX points to string in buffer
                        ECX = length of ASCII string
                     if ECX = byte length of buffer, string >= size of buffer
             if CF = 1, AX = DOS error code
                        AX = 0 if end of file
Uses:        EBX, EAX, ECX, flags
Example:

extrn   fopen:near, fgetstr:near

include dataseg.inc

; data
file_name   db 'asm32.doc',0
file_handle dw 0

@curseg	ends

include codeseg.inc

; code
        .
        .
        .
        lea   edx,file_name
        call  fopen
        mov   al,0            ; read-only access
        jc    fopen_problem
        mov   file_handle,ax  ; save for later

        mov   bx,ax           ; file handle
        call  fgetstr
        jc    read_problem

        call  strndup         ; make a copy for later
        .
        .
        .




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

filelist:    creates a list of file names matching a filespec mask
Source:      filelist.asm (fcount.asm)

Call with:   ESI pointing to filespec mask
             CX = file attribute mask
Returns:     if CF = 0:
               EDI = address of list buffer
               EAX = number of filenames in list
               ECX = list field width
             if CF = 1, AX = DOS error code
             You should use ASM32's HFREE to release the file list
             buffer when you're done with it.
Uses:        EAX, ECX, EDI, flags
Example:

public  myproc
extrn   filelist:near

include dataseg.inc

; data
filespec db '*.*',0

@curseg	ends

include codeseg.inc

; code
        .
        .
        .
        lea    esi,filespec
        mov    cx,16            ; normal files and subdirectories
        call   filelist
        jc     cant_do_it       ; oops




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FOPEN:       opens existing file and initializes ASM32 buffered I/O
Source:      fopen.asm ($handle.asm)

Call with:   EDX pointing to name of file to be opened
             AL = access mode
              0 = read-only access
              1 = write-only access
              2 = read-write access NOT SUPPORTED YET
Returns:     if CF = 0, AX = file handle
             if CF = 1, AX = ASM32 or DOS error code; file not opened
                if AX = 0, insufficient memory available
                if AX = 0FFFFh, no handles available in ASM32 I/O array;
                   change NUMBER_OF_HANDLES in $handle.asm and re-assemble
                   (default = 20 handles)
Uses:        AX, flags
Example:

public   myprog
extrn    fopen:near, fclose:near

include  dataseg.inc

; data
file_name   db 'ASM32.DOC',0
file_handle dw 0

@curseg	ends

include  codeseg.inc

; code
myprog   proc  near
         .
         .
         .
         lea   edx,file_name
         xor   al,al          ; read-only access
         call  fopen
         jc    something_went_wrong
         mov   file_handle,ax ; save the handle
         .
         .
         .

; all done with this file
         mov   bx,file_handle
         call  fclose




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FPUT:        write specified number of bytes to output file buffer
Source:      fput.asm ($handle.asm)

Call with:   BX = file handle
             EDI pointing to data to write
             ECX = number of bytes to write
Returns:     if CF = 0, no error
             if CF = 1, AX = error code
Uses:        EAX, flags
Example:

public  myproc
extrn   fput:near
extrn   fputchr:near
extrn   fputcrlf:near

include dataseg.inc

; data
data1    db 'several bytes may be written at once'
data_len equ $-data1

@curseg	ends

include codeseg.inc

; code
         .
         .
         .
         mov   bx,output_handle
         lea   edi,data1              ; EDI -> data1
         mov   ecx,data_len           ; bytes to write
         call  fput
         call  fputcrlf               ; write CR+LF for new line
                                      ; in ASCII text file
         mov   al,26                  ; End-of-File byte (optional)
         call  fputchr


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FPUTCHR:     write one character to output file buffer
Source:      fputchr.asm (fput.asm)

Call with:   BX = output file handle
             AL = character to write
Returns:     if CF = 1, AX = DOS error code
             if CF = 0, no error
Uses:        AX, flags
Example:     see FPUT


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FPUTCRLF:    write CR+LF pair to output file buffer
Source:      fputcrlf.asm (fput.asm)

Call with:   BX = output file handle; file must have been opened by
             FOPEN or FCREATE
Returns:     if CF = 0, no error
             if CF = 1, AX = DOS error code
Uses:        AX, flags
Example:     see FPUT



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FPUTSTR:     write an ASCIIZ string to output buffer
Source:      fputstr.asm (strlen.asm, fput.asm)

Call with:   BX = file handle
             EDI pointing to ASCIIZ string
Returns:     if CF = 0, EAX = bytes written
             if CF = 1, AX = DOS error code
Uses:        EAX, flags
Example:

public  myproc
extrn   fputstr:near
extrn   fputcrlf:near

include dataseg.inc

; data
strptr   dd 0                         ; pointer to string, assigned by program

@curseg	ends

include codeseg.inc

; code
         .
         .
         .
         mov   bx,output_handle
         mov   edi,strptr             ; EDI -> string
         call  fputstr
         call  fputcrlf               ; write CR+LF for new line
                                      ; in ASCII text file




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSEEK:       move file pointer for a file opened by FOPEN
Source:      fseek.asm ($handle.asm)

Call with:   BX = file handle
             AL = method code: 0 = absolute offset from start of file
                               1 = signed offset from current file pointer
                               2 = signed offset from end of file
             EDX = dword offset
Returns:     if CF = 1, AX = DOS error code
             if CF = 0, EAX = new location of file pointer
Uses:        EAX, flags

Example:

public  whoknows
extrn fopen:near, fseek:near

include dataseg.inc

; data
file0   db 'file0.dat',0

@curseg	ends

include codeseg.inc

; code
whoknows  proc near
        .
        .
        .
        mov     edx,offset file0
        mov     al,1              ; write only
        call    fopen
        jc      error
        xor     edx,edx           ; zero offset
        mov     al,2              ; relative to end of file
        call    fseek             ; move pointer to end of file






°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSIZE:       determines a file's size
Source:      fsize.asm

Call with:   BX = valid file handle
Returns:     if CF = 0, EAX = file size
             if CF = 1, AX = DOS error code
Uses:        EAX, CF
Example:


extrn   fsize:near

include dataseg.inc

; data

filenam db 'ASM32.DOC',0      ; ASCIIZ filename

@curseg	ends

include codeseg.inc

; code
        .
        .
        .
        lea     edx,filenam    ; point to filename
        mov     al,0           ;  read-only access (not required by FSIZE)
        call    fopen          ;  open the file
        jc      oops           ; jump to error control
                               ;  else no problem - continue
        mov     bx,ax          ; file handle in BX
        call    fsize          ; returns file size in EAX



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MLOAD:       read a file into far memory, allocating new selector
Source:      mload.asm (fsize.asm)

Call with:   [EDX] pointing to ASCIIZ filename
Returns:     if CF = 0, BX = selector of memory block
                        EAX = bytes loaded from disk
             if CF = 1, AX = DOS error code
Uses:        EAX, BX, CF
Example:

include model.inc

public  test_mload

extrn   mload:near

include dataseg.inc
filesel         dw 0
fname           db 'filename.txt',0
file_size       dd 0

include codeseg.inc

test_mload      proc near
        .
        .

        lea     edx,fname
        call    mload           ; read file into DOS memory
        jc      short no_good   ;  jump if there was a problem

        mov     filesel,bx      ; save new selector of memory block
        mov     file_size,eax   ; save file size

no_good:                        ; return with CF = 1 if error
        ret                     ; CF = 0 if no error
test_mload      endp
        end




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

MSAVE:       write memory block to file
Source:      msave.asm

Call with:   [EDX] pointing to ASCIIZ filename
             ES:[EBX] -> first byte to write
             EAX = number of bytes to write
Returns:     if CF = 0, no error
             if CF = 1, AX = DOS error code
Uses:        EAX, flags
Example:

include model.inc

public  test_msave

extrn   msave:near

include dataseg.inc
filesel         dw 0
fname           db 'filename.txt',0
file_size       dd 0

include codeseg.inc

test_msave      proc near
        .
        .

        lea     edx,fname
        mov     eax,file_size
        mov     es,filesel      ; selector of memory block
        xor     ebx,ebx         ; start at beginning of memory block
        call    mload           ; read file into DOS memory
                                ; return with CF = 1 if error
        ret                     ; CF = 0 if no error
test_msave      endp
        end




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

QFNAME:      qualifies a filename
Source:      qfname.asm

Call with:   EBX pointing to a filename; the filename may contain
             drive specification and/or complete or partial path name.
             Drive specification and path name not required.
Returns:     ESI pointing to the full DRIVESPEC:\PATH\FILENAME
             ECX = length of full filename
             Note that ESI points to QFName's buffer space; the next
             call to QFName will return a new filename at the same address.
Uses:        ESI, ECX, flags
Example:

include dataseg.inc

; data
docs    db '*.doc',0         ; search for .DOC files in current directory

@curseg	ends

include codeseg.inc

; code
        .
        .
        .
        lea    ebx,docs
        call   qfname        ; returns 'drive:\path\*.doc'