CHECK

         Purpose: For use with batch files, CHECK tests for various conditions
                  and reports by setting DOS ErrorLevel.

         Format: CHECK parameter [parameter...]

         Parameters must be separated with spaces.  Some of them require
         parameters of their own.  Here is the list:

         DAY
                 Returns day of the month (1-31)

         DISKSPACE [d:]
                 returns the number of whole 16K blocks of free disk space
                 from the indicated or default drive.  It returns 0 if an
                 error is encountered.  A return of 255 means that there are
                 at least that many blocks free.

         FILEFOUND filename
                 returns 0 if the indicated file is found, 1 if it's not.

         FILESIZE filename
                 returns the length in kilobytes of the specified file.  255
                 means the file is 255K or larger.  0 means the file can't be
                 found.

         FILETEXT filename 'text'
                 returns 0 if the specified text is found within the indicated
                 file.  1 is returned if the file doesn't contain the text, if
                 the file can't be found or if there's syntax error.

         KEYBOARD
                 returns 1 if a key has been pressed, 0 if one has not.

         KEYPRESS
                 waits for a keypress (if one hasn't already been pressed) and
                 returns its ASCII code.

         MEMORY
                 returns the number of 16K RAM modules present in the system.

         MODEL
                 returns the machine ID byte of the computer being used.  For
                 IBM machines, 255 means a plain PC, 254 a PC/XT or a port-
                 able, 253 a PCjr, 252 a PC/AT, and 249 a PC Convertible.

         MONTH
                 returns the current month (1-12)

         TIME
                 returns the current hour of the day (0-23)

         VIDEOCARD
                 returns the current video mode (0-16).

         VIDEOMODE
                 returns a value indicating what kind of video adapter is
                 being used.  (0=MDA, 1=CGA, 2=EGA)

         VERSION
                 returns the major number of the version of DOS in use.

         8087 or 80287
                 return 0 if either an 8087 nor an 80287 is present, 1 if not.


         Remarks: To use CHECK, you run it from a batch file and sort out the
                  returned value with IF ERRORLEVEL statements.  Remember that
                  IF ERRORLEVEL n is true if the error level is n or higher.

         This program is copyright 1986 by Ziff-Davis Publishing Co.  It was
         written by Jeff Prosise and published in "PC Lab Notes," PC Magazine,
         6/3, Feb. 10, 1987, pp. 299-321.  See that article for detailed
         discussion of how CHECK works.