Documentation for FIXFAT                Copyright 1991, P. R. Fletcher          _________________________              _______________________________
          
          
                                       INTRODUCTION                                       ____________

          FIXFAT is part of the HDTEST package, and is distributed with the
          Shareware and Registered versions of that software. The program and
          documentation may only be used or copied under the conditions laid
          down in the DOC files distributed with the package. The program allows
          DOS's two on-disk copies of the FAT to be made to correspond, when
          they have got "out of sync". This is required for HDCHEK and HDTEST to
          run. FIXFAT is only intended to be used when something has happened to
          corrupt or alter one copy of the FAT (usually because the second copy                           ___                                                 
          was only partially updated when a disk write was immediately followed
          by a reboot or use of the "big red switch"). The program cannot repair
          the FAT if both copies have become corrupted, nor is it intended to be
          a replacement for CHKDSK or the more complex disk repair utilities
          that are supplied with (e.g.) the Norton and Mace Utilities (TM).
          Users who have, and are comfortable with, the latter utilities will
          probably find FIXFAT superfluous. It is intended to provide a simple,
          limited, but fairly safe way for less experienced users to correct
          minor FAT problems prior to running HDTEST.

          FIXFAT is Copyright by Peter R. Fletcher, 1991. All rights are
          reserved. It was largely written in C, compiled with the Microsoft C
          compiler (V6.0A). A few low-level functions were written in assembly
          language and assembled with the Microsoft MASM assembler (V6.0). The
          program was linked with code from the Microsoft C function libraries
          by means of the Microsoft LINK linker (V5.13). It consequently
          contains material that is Copyright by Microsoft Corp, 1985-1990. This
          material is used under the terms of a license from Microsoft Corp.


                                     USING THE PROGRAM                                     _________________

          You should generally run CHKDSK before running FIXFAT, unless you have                                          ______                                
          some good reason to believe that the primary copy (and only the                                                            _____________
          primary copy of the FAT on your disk (FAT 1) has been corrupted. If          ____________                                                       
          CHKDSK reports any problems other than "orphan clusters", you should,
          if possible, also back up any irreplaceable files on the disk before
          either using CHKDSK with its /F option or running FIXFAT. If both your
          FATs have been damaged (e.g. by a defective program writing junk to
          the FAT area), neither CHKDSK nor FIXFAT will be able to help you, and
          your only hope is to use a disk repair utility such as those provided
          with the Mace or Norton Utilities (TM).

          The command line syntax for FIXFAT is:

                        FIXFAT dev[:]

          "dev" is the single letter DOS device identifier for the device whose
          FAT is to be fixed - the colon is optional. FIXFAT will first read and
          compare the two copies of the FAT on the target disk. If they are
          identical, this fact will be reported and the program will terminate.
          If there are any discrepancies between the two copies of the FAT, the
          program will examine them individually for evidence of corruption. If
          FAT 1 appears valid, you will be prompted for permission to overwrite
          FAT 2 with a copy of FAT 1. If FAT 1 appears invalid but FAT 2 appears                                                       __                       

           
          Documentation for FIXFAT                Copyright 1991, P. R. Fletcher          _________________________              _______________________________
          
          
          valid, you will similarly be prompted for permission to overwrite FAT
          1 with a copy of FAT 2. If neither FAT appears valid, this will be
          reported and the program will terminate. In determining whether a copy
          of the FAT is valid, FIXFAT makes similar checks to those performed by
          CHKDSK, except that "orphan clusters" (chains of clusters with no
          corresponding directory entries) are not flagged as problems. The
          occasional appearance of orphan clusters was rather common under
          versions of DOS prior to 3.0, usually following a program abort, and
          these are still not (usually) evidence of major trouble.


                               LIMITATIONS AND RESTRICTIONS                               ____________________________

          FIXFAT uses the DOS disk interrupts (INT 25 and 26) to access the disk
          - the program will not run on hardware/software combinations that do
          not support the use of these interrupts (this is almost never a
          problem). The program will, however, not run in the DOS compatibility                                               ___                             
          box under OS/2. FIXFAT requires an amount of free memory (over and
          above that which it uses for its own code) that is equal to at least
          four times the size of the FAT on the target device. For most devices,
          512 kB should be more than enough, but a device whose size pushes DOS
          4.0's limits may be more than the program can handle. For this version
          of the program, a previous (undocumented) restriction on sector size
          to the normal DOS value of 512 bytes has been lifted.


                                  ADDITIONAL INFORMATION                                  ______________________

          Like all well-behaved programs (!), FIXFAT signals successful
          completion by returning to DOS with the ERRORLEVEL variable set to
          zero. Different small positive values are returned for various errors.

          Comments, suggestions, etc. may be addressed to the author at:

                   1515 West Montgomery Avenue
                   Rosemont
                   PA 19010
                   U.S.A.

          Please enclose a s.a.e. if you would like to receive a reply to a
          question or a response to a comment.
















          
          
                                          Page 2