Nifty James' Disk Parking Utility
Version 1.00 of 11 June, 1988
(C) Copyright 1988 by Mike Blaszczak
All Rights Reserved by Author



THIS PROGRAM MAY NOT BE REDISTRIBUTED WITHOUT THE PRIOR WRITTEN
CONSENT OF THE AUTHOR.  RESELLING THIS PROGRAM FOR PROFIT OR OFFERING
THIS PROGRAM AS INSENTIVE TO PURCHASE IS UNLAWFUL.



This simple utility quickly parks the read-write heads of all hard
disk drives attached to the system.  The program has been tested on
Seagate ST-238, ST-238R, and ST-251 drives.  The program should work
with all Seagate hard disk drives, and will probably work with any
hard disk drive that has a landing area after the last data cylinder.

To run NJPARK, simply type

	NJPARK

at the DOS command prompt.  The NJPARK.EXE file will be loaded and
run.  The program will report an error if the BIOS thinks that no
disk drives are installed.  For this reason, the program may not work
on older systems with special nonstandard hardware.

NJPARK will then find the last data sector for each disk drive, and
try to seek eight cylinders past that data sector.  This is the
method specified by Seagate:

	"The read/write heads may be parked in the shipping zone by
	 issuing a seek to any cylinder between 615-670.  The drive
	 may then be powered down."

(This is from the Seagate ST-238 Product Manual, section 1.8.3.)

Since this seek-to-landing cylinder range is just past the last
normal data cylinder, NJPARK will seek to it by adding eight
cylinders to the last cylinder number.

NJPARK prints a message for each hard disk drive parked.  The message
should reflect a number that is within your hard disk drive's parking
zone.  For most drives, you can tell that the heads are parked by a
louder click when the heads are latched, or a very long seek time as
the drive pulls the head assembly out of the way.

If you have any doubt that NJPARK will not work for your hard disk
drive, you should consult the disk drive manufactuer.

I can assume no responsibility, direct or indirect, for the use of
NJPARK.  I use it on my own drives, and that should be enough proof
that I have confidence in my own work.  If another parking program
was supplied with your drives, you should use that program if
possible.

If you find this program useful, please send a registration fee of
$5.  To mail your check, or to adress me with any comments,
suggestions, or questions about this or any of my other Shareware
products, please use this address:

	Mike Blaszczak
	35 Ginger Lane #229
	East Hartford, CT  06118

Thank you very much!







         ----------------end-of-author's-documentation---------------

                        Software Library Information:

                   This disk copy provided as a service of

                        The Public (Software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  The P(s)L cannot de-
         bug programs over the telephone.

         Disks in the P(s)L are updated monthly, so if you did not get
         this disk  directly from the P(s)L,  you should be aware that
         the files in this set may no  longer be the current versions.

         For a copy of the latest monthly software library newsletter
         and a list of the 1,000+ disks in the library, call or write

                        The Public (Software) Library
                              P.O.Box 35705 - F
                           Houston, TX 77235-5705
                               (713) 665-7017