A     N     S     I     K     E     Y

                 How to reprogram your keyboard with  ANSI.SYS

               copr. 1988, 1989,  Dave Williams, Jacksonville AR

                             version 2.1 11/20/89


 PCDOS/MSDOS has had the ANSI.SYS driver ever since DOS 2.0. This program is a 
device driver for the "console", or keyboard and screen of your computer. It 
interprets a subset of the American National Standards Institute terminal 
control codes. You can use ANSI.SYS in a variety of ways, but you mostly see 
it used for color graphics on communications programs and used to do strange
things with the system PROMPT command.
 
 The DOS manuals stopped covering ANSI.SYS with version 2.0. Beginning with 
DOS 2.1, ANSI.SYS was relegated to the $150 DOS Technical Reference Manual. A 
lot of people never found out about ANSI.SYS' interesting uses.
 
 One of the uses, quite thoroughly explained in the DOS 2.0 manual, was the 
ability to reprogram the keyboard. You could conceivably turn the Enter key 
into a number 2, but of somewhat better use was the ability to reprogram the 
function keys to do things.
 
 There are a number of programs on the BBSs to help you reprogram the 
keyboard. Some of them are intepreted BASIC, some are massive 75k .EXE files. 
You don't need all this stuff, though. All you need to do is "TYPE" the
appropriate file to the screen, and it will reprogram your keys easily!
 
 The ANSIKEY.PRG file included in this arc will reprogram your keys for you. 
In your autoexec.bat file, include this line:

             type ansikey.prg

 The DOS ANSI.SYS program is rather limited. It will only accept about 200 
bytes of key redefinition, and it will slow the system down somewhat. The 
ZANSI.SYS file included with this archive has a much larger redefinition 
buffer, and contains very fast direct-screen-writing code to actually speed 
the screen up. You will be impressed with the improvement in screen update and 
scrolling - unless you have a CGA card. ZANSI causes massive "snow" on a CGA, 
so you'll have to use DOS' ANSI and stay inside the 200 byte limit. The doc 
file and SYS driver for ZANSI have been extracted from a file called 
ZANSI.ARC. They are in the public domain.

 Typing the file will set your keyboard. You can have several files, each 
programming them in a different way. ANSIKEY.PRG includes definitions for F11 
and F12 keys, these are ignored if you don't have a keyboard with them. It 
will also wipe out the DOS F1-F6 "editing" keys and replace them with its own 
definitions. You can delete the first six "normal" function key entries to 
preserve the DOS editing keys. The best solution is to reprogram them anyway, 
and use Chris Dunford's killer CED 1.0D or PC Magazine's DOSEDIT.

 Place the keystrokes you wish to enter within the quote marks. For example, 
to make the F1 key automatically bring up your terminal program, you can do 
the following:

      (escape character)[0;59"qmodem",13p

and that will set the keyboard up so that all you have to do is tap the F1 key 
to bring up your term program.

 The ',13p' at the end of each line is an ASCII carriage return, the same as 
hitting the "enter" key after typing the keystrokes enclosed in the quote 
marks. If you don't want the carriage return, just delete the 13, leaving the 
'p'.

 The required escape character (the left pointing arrow) is included in the 
ANSIKEY.PRG file.

 You can reprogram more than just function keys. Here are some useful keyboard 
scan codes:
           
        Normal          Shift          Control         Alt

ESC     1
1       2                                               0;120
2       3                                               0;121
3       4                                               0;122
4       5                                               0;123
5       6                                               0;124
6       7                                               0;125
7       8                                               0;126
8       9                                               0;127
9       10                                              0;128
0       11                                              0;129
-       12                                              0;130
=       13                                              0;131
TAB     15
backtab none                                             0;15
RETURN  28


         Normal      Shift     Control      Alt


a   =     30                               0;30
b   =     48                               0;48
c   =     46                               0;46
d   =     32                               0;32
e   =     18                               0;18
f   =     33                               0;33
g   =     34                               0;34
h   =     35                               0;35
i   =     23                               0;23
j   =     36                               0;36
k   =     37                               0;37
l   =     38                               0;38
m   =     50                               0;50
n   =     49                               0;49
o   =     24                               0;24
p   =     25                               0;25
q   =     16                               0;16
r   =     19                               0;19
s   =     31                               0;31
t   =     20                               0;20
u   =     22                               0;22
v   =     47                               0;47
w   =     17                               0;17
x   =     45                               0;45
y   =     21                               0;21
z   =     44                               0;44

         Normal      Shift     Control      Alt

F1  =     0;59       0;84       0;94       0;104
F2  =     0;60       0;85       0;95       0;105
F3  =     0;61       0;86       0;96       0;106
F4  =     0;62       0;87       0;97       0;107
F5  =     0;63       0;88       0;98       0;108
F6  =     0;64       0;89       0;99       0;109
F7  =     0;65       0;90       0;100      0;110
F8  =     0;66       0;91       0;101      0;111
F9  =     0;67       0;92       0;102      0;112
F10 =     0;68       0;93       0;103      0;113
F11 =     0;152      0;162      0;172      0;182
F12 =     0;153      0;163      0;173      0;183

ÚÄÄÂÄÄÂÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄÂÄÄÄÄÄ¿
³59³60³³ 1 ³ 2 ³ 3 ³ 4 ³ 5 ³ 6 ³ 7 ³ 8 ³ 9 ³10 ³11 ³12 ³13 ³ 14  ³ 69  ³ 70  ³
ÃÄÄÅÄÄ´ÃÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄ´
³F1³F2³³Esc³ 1 ³ 2 ³ 3 ³ 4 ³ 5 ³ 6 ³ 7 ³ 8 ³ 9 ³ 0 ³ - ³ = ³ <ÄÄ ³ Num ³Scrol³
ÃÄÄÅÄÄÅÅÄÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÄÂÄÄÄÅÄÄÂÄÄÅÄÄÂÄÄ´
³61³62³³ 15 ³16 ³17 ³18 ³19 ³20 ³21 ³22 ³23 ³24 ³25 ³26 ³27  ³28 ³71³72³73³74³
ÃÄÄÅÄÄ´ÃÄÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÄÅÄÄÄÅÄÄÅÄÄÅÄÄÅÄÄ´
³F3³F4³³ Tab³ Q ³ W ³ E ³ R ³ T ³ Y ³ U ³ I ³ O ³ P ³ [ ³ ]  ³ ³ ³7 ³8 ³9 ³- ³
ÃÄÄÅÄÄÅÅÄÄÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÁÂÄÄÄ´ ³ ÃÄÄÅÄÄÅÄÄÅÄÄ´
³63³64³³  29 ³30 ³31 ³32 ³33 ³34 ³35 ³36 ³37 ³38 ³39 ³40 ³41 ³<Ù ³75³76³77³78³
ÃÄÄÅÄÄ´ÃÄÄÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄ´   ÃÄÄÅÄÄÅÄÄÅÄÄ´
³F5³F6³³  Ctr³ A ³ S ³ D ³ F ³ G ³ H ³ J ³ K ³ L ³ ; ³ ' ³ ` ³   ³4 ³5 ³6 ³+ ³
ÃÄÄÅÄÄÅÅÄÄÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÂÄÁÄÄÄÅÄÄÄÅÄÄÅÄÄÅÄÄ´  ³
³65³66³³42 ³43 ³44 ³45 ³46 ³47 ³48 ³49 ³50 ³51 ³52 ³53 ³54   ³55 ³79³80³81³  ³
ÃÄÄÅÄÄ´ÃÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÅÄÄÄÄÄÅÄÄÄÅÄÄÅÄÄÅÄÄ´  ³
³F7³F8³³Shf³ \ ³ Z ³ X ³ C ³ V ³ B ³ N ³ M ³ , ³ . ³ / ³Shf  ³ * ³1 ³2 ³3 ³  ³
ÃÄÄÅÄÄÅÅÄÄÄÁÄÂÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÄÁÄÄÂÁÄÄÄÄÄÅÄÄÄÁÄÄÅÄÄÁÄÄÅÄÄÙ
³67³68³³ 56  ³                 57                     ³  58  ³  82  ³ 83  ³ 
ÃÄÄÅÄÄ´ÃÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄÄÅÄÄÄÄÄ´ 
³F9³F0³³ Alt ³             Space Bar                  ³ Caps ³  Ins ³ Del ³ 
ÀÄÄÁÄÄÁÁÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÄÁÄÄÄÄÄÙ 


 You will occasionally run across a program that will read the keys through
DOS instead of doing it the normal way through the BIOS. Fortunately, these
programs are fairly rare - in two years I've seen only two or three. 

 If you need to occasionally run such a program, you can use the ANSIKEY.NUL 
file to eliminate the keyboard redefinitions. Simple TYPE ANSIKEY.NUL to
zero-out the keyboard redefinitions, and you can reload them later. If you 
encounter a program you commonly run that requires this you can use a CED 
macro to zero the keys, run the program, and then reset it when you are 
finished.

 My system has the following keys defined with this little utility:

normal keys

F1      nsd     (sorted directory)      F2      ED        (PC-write)
F3      dir/p A:                        F4      dir/p B:
F5      pctools (PC-Tools 4.22)         F6      diskcopy A: B:
F7      exit                            F8      *.*       (with no CR)
F9      cls                             F10     list function.84    (help)


control keys

^F1     masm    (Macro Assembler)       ^F2     msc      (Microsoft C)
^F3     aobj    (assemble to OBJ)       ^F4     cobj     (compile to OBJ)
^F5     tp      (Turbo Pascal)          ^F6     diskpark (park hard disk)


alt keys

alt-D   qmodem  (Qmodem SST 3.1)



 I haven't found much use for any of the other ones, since I use CED macros 
heavily.

 When you edit the ANSIKEY.PRG file, you will need to use a straight-ASCII 
word processor, such as PC-Write or (gag) EDLIN. The (escape) character is 
ASCII #27. You can enter this character in PC-Write and most other word 
processors by holding down the alt key and typing "27" on the numeric 
keypad. If you have one of the bloated commercial wordprocessors, you'll have 
to figure out how to get it to write an ASCII file.

 ZANSI and ANSIKEY will correctly interpret the keyboard codes for a Tandy 
1000 TX 101-key (12 function key) keyboard and on the IBM PS/2.

 Two additional text files are included with version 2.0 - FUNCTION.84 and 
FUNCTION.101. They are help files to remind you of your function key 
redefinitions. Set up one of the keys (I recommend F10 or F12) to a string 
something like "LIST FUNCTION.84" to use Vern Buerg's LIST.COM to view your 
key settings. The help screens are very useful when you are just beginning and 
have trouble remembering what you've programmed the keys to do. If you use 
more than one ANSIKEY.PRG file, you can call a separate help screen for each 
loaded file.


                                                       Enjoy!

                                                    Dave Williams

reachable at:

Twit's End BBS - The Gigabyte Board - (501)771-0114

| version 1.0          original release
| version 2.0 12/28/88 improved docs, added helpkey templates
| version 2.1 11/20/89 minor corrections and update



         ----------------end-of-author's-documentation---------------

                         Software Library Information:

                    This disk copy provided as a service of

                           Public (software) Library

         We are not the authors of this program, nor are we associated
         with the author in any way other than as a distributor of the
         program in accordance with the author's terms of distribution.

         Please direct shareware payments and specific questions about
         this program to the author of the program, whose name appears
         elsewhere in  this documentation. If you have trouble getting
         in touch with the author,  we will do whatever we can to help
         you with your questions. All programs have been tested and do
         run.  To report problems,  please use the form that is in the
         file PROBLEM.DOC on many of our disks or in other written for-
         mat with screen printouts, if possible.  PsL cannot debug pro-
         programs over the telephone, though we can answer questions.

         Disks in the PsL are updated  monthly,  so if you did not get
         this disk directly from the PsL, you should be aware that the
         files in this set may no longer be the current versions. Also,
         if you got this disk from another vendor and are having prob-
         lems,  be aware that  some files may have become corrupted or
         lost by that vendor. Get a current, working disk from PsL.

         For a copy of the latest monthly software library newsletter
         and a list of the 2,000+ disks in the library, call or write

                           Public (software) Library
                               P.O.Box 35705 - F
                            Houston, TX 77235-5705

                                1-800-2424-PSL
                                 MC/Visa/AmEx

                          Outside of U.S. or in Texas
                          or for general information,
                              Call 1-713-524-6394

                          PsL also has an outstanding
                          catalog for the Macintosh.